Electrical Systems & Instrumentation

Several good presentations were made related to this topic. Exhaustive considerations were made to many issues affecting beam stability.

Followings recommendations are made on some topics -

Power Supplies –

- Corrector power supply – stability to 1 ppm level (from 4 ppm level) should be considered (20 bits resolution)

- Re-visit main magnet and multipole magnet 60 Hz ripple specification – include chamber filtering effects

- Re-visit multi-pole stability specification – consider 400ppm-->100ppm

- Multipole resolution 16 bits ( 18 bits; provides added resolution flexibility for fine measurement such as beam base alignment.

- Employ a common PS controller for all PS; embed into the PS to minimize any interface related issue

- Mitigate EMI sources, routing of high current buses, kicker pulses

BPMs

- Develop a comprehensive BPM specification table to include

- dc beam stability

- ac beam stability – with a frequency band

- turn by turn measurement specification

- Specify requirements separately for

  - user RF bpms -UBPM

  - accelerator RF bpms

  - Xpms

- Continue R&D to achieve sub micron level performance without looking into what is available now

- Develop a budget table for mechanical stability, dc stability, ac stability, fill pattern effects

- Measure UBPM mechanical motion to provide a reference – added cost should be minimum

XBPMs –

- Use of Xbpms may be crucial to get to submicron level stability for some beamlines

- Plan for 2 xbpms each for ID and BM beamlines to get both position and angle stability

- Integrate xbpms data acquisition into rfbpms data acquisition

- Plan to reduce background radiation – decker distortion.

- Investigate other type of xbpms

- Perform calculations of background radiation level vs ID radiation level at larger gaps

- Recommend a mini workshop on discussing special issues with xbpms

- Investigate rogue microwave effect in a prototype curved chamber