#### Appendix C: CONTAM Flow Element Libraries

This appendix presents four flow element libraries: ASHRAELA.lb3, RESMISC.lb3, C&ISUM.lb3 and C&IMISC.lb3. The first two contain flow elements relevant to residential buildings, and the other two apply to commercial, institutional and high-rise residential buildings. Within the libraries, each element name consists of four parts: component, descriptors (most names will have more than one descriptor), generic building type, and tightness value. The component and descriptor parts of the name will be separated from building type and value by an underscore “_”. The following are the abbreviations used to create the flow elements names:

Components:

CE	Ceiling

CH	Chimney

DR	Door

DW	Doorway

FL	Floor

FP	Fireplace

FR	Frame

IT	Interface

JT	Joint

PE	Penetrations

RF	Roof

VE	Vent

WH	Water heater

WL	Wall

WN  	Window

Descriptors:

2W	Two Way Air Flow

AL	Aluminum

AP	Apartment

AR	Per unit area

AS	Assembly

AT	Attic

BA	Bathroom

BL	Block

BR	Brick

CA	Caulked, sealed or 	gasketed

CASE	Casement

CC	Cast-in-place concrete

CK	Crack

CL	Closed

CO	Concrete

CP	Concrete panel

CR	Corner

CS	Crawl Space

CT	Closet

CW	Curtain wall

DA	Damper

DB	Double or double hung

DE	Difference

DW	Ductwork

DY	Dryer

EC	Electrical outlet or 	switch

EL	Elevator

EX	Exterior

FD	Fold Down

FR	Frame

GA	Garage

GL	Glass

GS	Gas

HA	Hall

HC	Healthcare

ID	Industrial

IN	Interior

IO	Inoperable

IS	Insulation

JA	Jalousie

KI	Kitchen

MA	Masonry

ME	Metal

MN	Manufactured

NO	No

NW 	Not weatherstripped

OO	Operable

OP	Open

PA	Partition

PC	Precast Concrete

PL	Plumbing

PT	Patio

RE	Shopping mall/Retail 	store

RL	Recessed light

RS	Restaurant

SC	School

SH	Single hung

SI	Single

SL	Slider or sliding

SM	Storm

SN	Stone

SP	Sports

SR	Stair/Stairwell

ST	Steel

TI	Tile

UC	Uncaulked

UN	Per unit item

WD	Wood

WE	Weatherstripped

WF	Whole house fan

YE	Yes

Generic Building Types:

C	Commercial

I	Institutional

M	Manufactured House

N	Industrial

R	Residential

Values:

AV	Average or best estimate

MN	Minimum

MX	Maximum

+S	Mean plus one standard deviation

-S	Mean minus one standard deviation

For example, a flow element designated as DRINCTCL_RAV would refer to a closed interior closet door in a residential building with an average tightness value.

#### Appendix C1: ASHRAELA.lb3

Selected items from 1997 ASHRAE Fundamentals, Chapter 25, Table 3

| Element Name | Building Type | Description | Model | Value | Reference |
| --- | --- | --- | --- | --- | --- |
| CE_RAV | Residential | Ceiling, general – best estimate | ELA4 | 1.8 cm2/m2 | C1 |
| CE_RMN | Residential | Ceiling, general – minimum | ELA4 | 0.79 cm2/m2 | C1 |
| CE_RMX | Residential | Ceiling, general – maximum | ELA4 | 2.8 cm2/m2 | C1 |
| CERL_RAV | Residential | Ceiling penetrations, recessed lights– best estimate | ELA4 | 10 cm2/item | C1 |
| CERL_RMN | Residential | Ceiling penetrations, recessed lights – minimum | ELA4 | 1.5 cm2/item | C1 |
| CERL_RMX | Residential | Ceiling penetrations, recessed lights – maximum | ELA4 | 21 cm2/item | C1 |
| CEWF_RAV | Residential | Ceiling penetrations, whole house fans – best estimate | ELA4 | 20 cm2/item | C1 |
| CEWF_RMN | Residential | Ceiling penetrations, whole house fans – minimum | ELA4 | 1.6 cm2/item | C1 |
| CEWF_RMX | Residential | Ceiling penetrations, whole house fans – maximum | ELA4 | 21 cm2/item | C1 |
| CH_RAV | Residential | Chimney– best estimate | ELA4 | 29 cm2/item | C1 |
| CH_RMN | Residential | Chimney – minimum | ELA4 | 21 cm2/item | C1 |
| CH_RMX | Residential | Chimney – maximum | ELA4 | 36 cm2/item | C1 |
| DR_RAV | Residential | Door, general, average– best estimate | ELA4 | 0.31 cm2/m | C1 |
| DR_RMN | Residential | Door, general, average – minimum | ELA4 | 0.23 cm2/m | C1 |
| DR_RMX | Residential | Door, general, average – maximum | ELA4 | 0.45 cm2/m | C1 |
| DRATCSNW_RAV | Residential | Doors, attic/crawl space, not weatherstripped – best estimate | ELA4 | 30 cm2/item | C1 |
| DRATCSNW_RMN | Residential | Doors, attic/crawl space, not weatherstripped – minimum | ELA4 | 10 cm2/item | C1 |
| DRATCSNW_RMX | Residential | Doors, attic/crawl space, not weatherstripped – maximum | ELA4 | 37 cm2/item | C1 |
| DRATCSWE_RAV | Residential | Doors, attic/crawl space, weatherstripped – best estimate | ELA4 | 18 cm2/ item | C1 |
| DRATCSWE_RMN | Residential | Doors, attic/crawl space, weatherstripped – minimum | ELA4 | 8 cm2/ item | C1 |
| DRATCSWE_RMX | Residential | Doors, attic/crawl space, weatherstripped – maximum | ELA4 | 18.5 cm2/ item | C1 |
| DRATFDNW_RAV | Residential | Doors, attic fold down, not weatherstripped – best estimate | ELA4 | 44 cm2/ item | C1 |
| DRATFDNW_RMN | Residential | Doors, attic fold down, not weatherstripped – minimum | ELA4 | 23 cm2/ item | C1 |
| DRATFDNW_RMX | Residential | Doors, attic fold down, not weatherstripped – maximum | ELA4 | 86 cm2/ item | C1 |
| DRATFDWE_RAV | Residential | Doors, attic fold down, weatherstripped – best estimate | ELA4 | 22 cm2/ item | C1 |
| DRATFDWE_RMN | Residential | Doors, attic fold down, weatherstripped – minimum | ELA4 | 14 cm2/ item | C1 |
| DRATFDWE_RMX | Residential | Doors, attic fold down, weatherstripped – maximum | ELA4 | 43 cm2/ item | C1 |
| DRDBNW_RAV | Residential | Door, double, not weatherstripped– best estimate | ELA4 | 11 cm2/m2 | C1 |
| DRDBNW_RMN | Residential | Door, double, not weatherstripped – minimum | ELA4 | 7 cm2/m2 | C1 |
| DRDBNW_RMX | Residential | Door, double, not weatherstripped – maximum | ELA4 | 22 cm2/m2 | C1 |
| DRDBWE_RAV | Residential | Door, double, weatherstripped– best estimate | ELA4 | 8 cm2/m2 | C1 |
| DRDBWE_RMN | Residential | Door, double, weatherstripped – minimum | ELA4 | 3 cm2/m2 | C1 |
| DRDBWE_RMX | Residential | Door, double, weatherstripped – maximum | ELA4 | 23 cm2/m2 | C1 |
| DREL_CAV | Commercial | Doors, elevator (passenger) – best estimate | ELA4 | 0.26 cm2/ item | C1 |
| DREL_CMN | Commercial | Doors, elevator (passenger) – minimum | ELA4 | 0.14 cm2/ item | C1 |
| DREL_CMX | Commercial | Doors, elevator (passenger) – maximum | ELA4 | 0.35 cm2/ item | C1 |
| DRMS_RAV | Residential | Door, mail slot – best estimate | ELA4 | 4 cm2/m | C1 |
| DRPTSLAR_RAV | Residential | Door, sliding exterior glass patio – best estimate | ELA4 | 5.5 cm2/m2 | C1 |
| DRPTSLAR_RMN | Residential | Door, sliding exterior glass patio – minimum | ELA4 | 0.6 cm2/m2 | C1 |
| DRPTSLAR_RMX | Residential | Door, sliding exterior glass patio – maximum | ELA4 | 15 cm2/m2 | C1 |
| DRPTSLUN_RAV | Residential | Door, sliding exterior glass patio – best estimate | ELA4 | 22 cm2/item | C1 |
| DRPTSLUN_RMN | Residential | Door, sliding exterior glass patio – minimum | ELA4 | 3 cm2/item | C1 |
| DRPTSLUN_RMX | Residential | Door, sliding exterior glass patio – maximum | ELA4 | 60 cm2/item | C1 |
| DRSINW_RAV | Residential | Door, single, not weatherstripped – best estimate | ELA4 | 21 cm2/item | C1 |
| DRSINW_RMN | Residential | Door, single, not weatherstripped – minimum | ELA4 | 12 cm2/item | C1 |
| DRSINW_RMX | Residential | Door, single, not weatherstripped – maximum | ELA4 | 53 cm2/item | C1 |
| DRSIWE_RAV | Residential | Door, single, weatherstripped – best estimate | ELA4 | 12 cm2/item | C1 |
| DRSIWE_RMN | Residential | Door, single, weatherstripped – minimum | ELA4 | 4 cm2/item | C1 |
| DRSIWE_RMX | Residential | Door, single, weatherstripped – maximum | ELA4 | 27 cm2/item | C1 |
| DRSMDE_RAV | Residential | Door, storm (difference between with and without) – best estimate | ELA4 | 6 cm2/item | C1 |
| DRSMDE_RMN | Residential | Door, storm (difference between with and without) – minimum | ELA4 | 3 cm2/item | C1 |
| DRSMDE_RMX | Residential | Door, storm (difference between with and without) – maximum | ELA4 | 6.2 cm2/item | C1 |
| FLCS_RAV | Residential | Floors over crawl spaces, general – best estimate | ELA4 | 2.2 cm2/m2 | C1 |
| FLCS_RMN | Residential | Floors over crawl spaces, general – minimum | ELA4 | 0.4 cm2/m2 | C1 |
| FLCS_RMX | Residential | Floors over crawl spaces, general – maximum | ELA4 | 4.9 cm2/m2 | C1 |
| FLCSNODW_RAV | Residential | Floors over crawl spaces, without ductwork in crawl space – best estimate | ELA4 | 1.98 cm2/m2 | C1 |
| FLCSYEDW_RAV | Residential | Floors over crawl spaces, with ductwork in crawl space – best estimate | ELA4 | 2.25 cm2/m2 | C1 |
| FPDACL_RAV | Residential | Fireplace, with damper closed – best estimate | ELA4 | 43 cm2/m2 | C1 |
| FPDACL_RMN | Residential | Fireplace, with damper closed – minimum | ELA4 | 10 cm2/m2 | C1 |
| FPDACL_RMX | Residential | Fireplace, with damper closed – maximum | ELA4 | 92 cm2/m2 | C1 |
| FPDAOP_RAV | Residential | Fireplace, with damper open – best estimate | ELA4 | 350 cm2/m2 | C1 |
| FPDAOP_RMN | Residential | Fireplace, with damper open – minimum | ELA4 | 145 cm2/m2 | C1 |
| FPDAOP_RMX | Residential | Fireplace, with damper open – maximum | ELA4 | 380 cm2/m2 | C1 |
| FPGLDR_RAV | Residential | Fireplace, with glass doors – best estimate | ELA4 | 40 cm2/m2 | C1 |
| FPGLDR_RMN | Residential | Fireplace, with glass doors – minimum | ELA4 | 4 cm2/m2 | C1 |
| FPGLDR_RMX | Residential | Fireplace, with glass doors – maximum | ELA4 | 40 cm2/m2 | C1 |
| FRDR_RAV | Residential | Door frame, general – best estimate | ELA4 | 12 cm2/ item | C1 |
| FRDR_RMN | Residential | Door frame, general – minimum | ELA4 | 2.4 cm2/ item | C1 |
| FRDR_RMX | Residential | Door frame, general – maximum | ELA4 | 25 cm2/ item | C1 |
| FRDRMACA_RAV | Residential | Door frame, masonry, caulked – best estimate | ELA4 | 1 cm2/m2 | C1 |
| FRDRMACA_RMN | Residential | Door frame, masonry, caulked – minimum | ELA4 | 0.3 cm2/m2 | C1 |
| FRDRMACA_RMX | Residential | Door frame, masonry, caulked – maximum | ELA4 | 1 cm2/m2 | C1 |
| FRDRMAUC_RAV | Residential | Door frame, masonry, uncaulked – best estimate | ELA4 | 5 cm2/m2 | C1 |
| FRDRMAUC_RMN | Residential | Door frame, masonry, uncaulked – minimum | ELA4 | 1.7 cm2/m2 | C1 |
| FRDRMAUC_RMX | Residential | Door frame, masonry, uncaulked – maximum | ELA4 | 5 cm2/m2 | C1 |
| FRDRWDCA_RAV | Residential | Door frame, wood, caulked – best estimate | ELA4 | 0.3 cm2/m2 | C1 |
| FRDRWDCA_RMN | Residential | Door frame, wood, caulked – minimum | ELA4 | 0.1 cm2/m2 | C1 |
| FRDRWDCA_RMX | Residential | Door frame, wood, caulked – maximum | ELA4 | 0.3 cm2/m2 | C1 |
| FRDRWDUC_RAV | Residential | Door frame, wood, uncaulked – best estimate | ELA4 | 1.7 cm2/m2 | C1 |
| FRDRWDUC_RMN | Residential | Door frame, wood, uncaulked – minimum | ELA4 | 0.6 cm2/m2 | C1 |
| FRDRWDUC_RMX | Residential | Door frame, wood, uncaulked – maximum | ELA4 | 1.7 cm2/m2 | C1 |
| FRWNMACA_RAV | Residential | Window framing, masonry, caulked – best estimate | ELA4 | 1.3 cm2/m2 | C1 |
| FRWNMACA_RMN | Residential | Window framing, masonry, caulked – minimum | ELA4 | 1.1 cm2/m2 | C1 |
| FRWNMACA_RMX | Residential | Window framing, masonry, caulked – maximum | ELA4 | 2.1 cm2/m2 | C1 |
| FRWNMAUC_RAV | Residential | Window framing, masonry, uncaulked – best estimate | ELA4 | 6.5 cm2/m2 | C1 |
| FRWNMAUC_RMN | Residential | Window framing, masonry, uncaulked – minimum | ELA4 | 5.7 cm2/m2 | C1 |
| FRWNMAUC_RMX | Residential | Window framing, masonry, uncaulked – maximum | ELA4 | 10.3 cm2/m2 | C1 |
| FRWNWDCA_RAV | Residential | Window framing, wood, caulked – best estimate | ELA4 | 0.3 cm2/m2 | C1 |
| FRWNWDCA_RMN | Residential | Window framing, wood, caulked – minimum | ELA4 | 0.3 cm2/m2 | C1 |
| FRWNWDCA_RMX | Residential | Window framing, wood, caulked – maximum | ELA4 | 0.5 cm2/m2 | C1 |
| FRWNWDUC_RAV | Residential | Window framing, wood, uncaulked – best estimate | ELA4 | 1.7 cm2/m2 | C1 |
| FRWNWDUC_RMN | Residential | Window framing, wood, uncaulked – minimum | ELA4 | 1.5 cm2/m2 | C1 |
| FRWNWDUC_RMX | Residential | Window framing, wood, uncaulked – maximum | ELA4 | 2.7 cm2/m2 | C1 |
| JTCEWL_RAV | Residential | Joints, ceiling wall – best estimate | ELA4 | 1.5 cm2/m | C1 |
| JTCEWL_RMN | Residential | Joints, ceiling wall – minimum | ELA4 | 0.16 cm2/m | C1 |
| JTCEWL_RMX | Residential | Joints, ceiling wall – maximum | ELA4 | 2.5 cm2/m | C1 |
| JTFLWLCA_RAV | Residential | Joints, sole plate, floor/wall, caulked– best estimate | ELA4 | 0.8 cm2/m | C1 |
| JTFLWLCA_RMN | Residential | Joints, sole plate, floor/wall, caulked – minimum | ELA4 | 0.075 cm2/m | C1 |
| JTFLWLCA_RMX | Residential | Joints, sole plate, floor/wall, caulked – maximum | ELA4 | 1.2 cm2/m | C1 |
| JTFLWLUC _RMN | Residential | Joints, sole plate, floor/wall, uncaulked – minimum | ELA4 | 0.38 cm2/m | C1 |
| JTFLWLUC _RMX | Residential | Joints, sole plate, floor/wall, uncaulked – maximum | ELA4 | 5.6 cm2/m | C1 |
| JTFLWLUC_RAV | Residential | Joints, sole plate, floor/wall, uncaulked – best estimate | ELA4 | 4.0 cm2/m | C1 |
| PECA_RAV | Residential | Piping/Plumbing/Wiring penetrations, caulked – best estimate | ELA4 | 2.0 cm2/ item | C1 |
| PECA_RMN | Residential | Piping/Plumbing/Wiring penetrations, caulked – minimum | ELA4 | 1.0 cm2/ item | C1 |
| PECA_RMX | Residential | Piping/Plumbing/Wiring penetrations, caulked – maximum | ELA4 | 2.0 cm2/ item | C1 |
| PEECCA_RAV | Residential | Electrical outlets/switches, gaskets – best estimate | ELA4 | 0.15 cm2/item | C1 |
| PEECCA_RMN | Residential | Electrical outlets/switches, gaskets – minimum | ELA4 | 0.08 cm2/item | C1 |
| PEECCA_RMX | Residential | Electrical outlets/switches, gaskets – maximum | ELA4 | 3.5 cm2/item | C1 |
| PEECUC_RAV | Residential | Electrical outlets/switches, no gaskets – best estimate | ELA4 | 2.5 cm2/item | C1 |
| PEECUC_RMN | Residential | Electrical outlets/switches, no gaskets – minimum | ELA4 | 0.5 cm2/item | C1 |
| PEECUC_RMX | Residential | Electrical outlets/switches, no gaskets – maximum | ELA4 | 6.2 cm2/item | C1 |
| PEUC_RAV | Residential | Piping/Plumbing/Wiring penetrations, uncaulked – best estimate | ELA4 | 6.0 cm2/ item | C1 |
| PEUC_RMN | Residential | Piping/Plumbing/Wiring penetrations, uncaulked – minimum | ELA4 | 2.0 cm2/ item | C1 |
| PEUC_RMX | Residential | Piping/Plumbing/Wiring penetrations, uncaulked – maximum | ELA4 | 24.0 cm2/ item | C1 |
| VEBADACL_RAV | Residential | Vents, bathroom with damper closed– best estimate | ELA4 | 10 cm2/item | C1 |
| VEBADACL_RMN | Residential | Vents, bathroom with damper closed – minimum | ELA4 | 2.5 cm2/item | C1 |
| VEBADACL_RMX | Residential | Vents, bathroom with damper closed – maximum | ELA4 | 20 cm2/item | C1 |
| VEBADAOP_RAV | Residential | Vents, bathroom with damper open– best estimate | ELA4 | 20 cm2/item | C1 |
| VEBADAOP_RMN | Residential | Vents, bathroom with damper open – minimum | ELA4 | 6.1 cm2/item | C1 |
| VEBADAOP_RMX | Residential | Vents, bathroom with damper open – maximum | ELA4 | 22 cm2/item | C1 |
| VECS_RAV | Residential | Crawl space, 200 mm by 400 mm vent – best estimate | ELA4 | 129 cm2/item | C1 |
| VEDYDANO_RAV | Residential | Vents, dryer without damper– best estimate | ELA4 | 15 cm2/item | C1 |
| VEDYDANO_RMN | Residential | Vents, dryer without damper – minimum | ELA4 | 12 cm2/item | C1 |
| VEDYDANO_RMX | Residential | Vents, dryer without damper – maximum | ELA4 | 34 cm2/item | C1 |
| VEDYDAYE_RAV | Residential | Vents, dryer with damper– best estimate | ELA4 | 3 cm2/item | C1 |
| VEDYDAYE_RMN | Residential | Vents, dryer with damper – minimum | ELA4 | 2.9 cm2/item | C1 |
| VEDYDAYE_RMX | Residential | Vents, dryer with damper – maximum | ELA4 | 7 cm2/item | C1 |
| VEKIDACA_RAV | Residential | Vents, kitchen tight gasket – best estimate | ELA4 | 1 cm2/item | C1 |
| VEKIDACL_RAV | Residential | Vents, kitchen with damper open – best estimate | ELA4 | 5 cm2/item | C1 |
| VEKIDACL_RMN | Residential | Vents, kitchen with damper open – minimum | ELA4 | 1 cm2/item | C1 |
| VEKIDACL_RMX | Residential | Vents, kitchen with damper open – maximum | ELA4 | 7 cm2/item | C1 |
| VEKIDAOP_RAV | Residential | Vents, kitchen with damper open – best estimate | ELA4 | 40 cm2/item | C1 |
| VEKIDAOP_RMN | Residential | Vents, kitchen with damper open – minimum | ELA4 | 14 cm2/item | C1 |
| VEKIDAOP_RMX | Residential | Vents, kitchen with damper open – maximum | ELA4 | 72 cm2/item | C1 |
| WCCASEWE _RMN | Residential | Windows, casement with weatherstripping –minimum | ELA4 | 0.1 cm2/m | C1 |
| WCCASEWE _RMX | Residential | Windows, casement with weatherstripping –maximum | ELA4 | 3.0 cm2/m | C1 |
| WCCASEWE_RAV | Residential | Windows, casement with weatherstripping – best estimate | ELA4 | 0.24 cm2/m | C1 |
| WHGS_RAV | Residential | Gas water heater – best estimate | ELA4 | 20 cm2/item | C1 |
| WHGS_RMN | Residential | Gas water heater – minimum | ELA4 | 15 cm2/item | C1 |
| WHGS_RMX | Residential | Gas water heater – maximum | ELA4 | 25 cm2/item | C1 |
| WLCS_RAV | Residential | Crawl space, general (area for exposed wall) – best estimate | ELA4 | 10 cm2/m2 | C1 |
| WLCS_RMN | Residential | Crawl space, general (area for exposed wall) – minimum | ELA4 | 8 cm2/m2 | C1 |
| WLCS_RMX | Residential | Crawl space, general (area for exposed wall) – maximum | ELA4 | 17 cm2/m2 | C1 |
| WLEXCC_RAV | Residential | Walls (exterior), cast-in-place concrete – best estimate | ELA4 | 0.5 cm2/m2 | C1 |
| WLEXCC_RMN | Residential | Walls (exterior), cast-in-place concrete – minimum | ELA4 | 0.049 cm2/m2 | C1 |
| WLEXCC_RMX | Residential | Walls (exterior), cast-in-place concrete – maximum | ELA4 | 1.8 cm2/m2 | C1 |
| WLEXPC_RAV | Residential | Walls (exterior), precast concrete panel – best estimate | ELA4 | 1.2 cm2/m2 | C1 |
| WLEXPC_RMN | Residential | Walls (exterior), precast concrete panel – minimum | ELA4 | 0.28 cm2/m2 | C1 |
| WLEXPC_RMX | Residential | Walls (exterior), precast concrete panel – maximum | ELA4 | 1.65 cm2/m2 | C1 |
| WNCASENW_RAV | Residential | Windows, casement, not weatherstripped – best estimate | ELA4 | 0.28 cm2/m | C1 |
| WNDBNW_RAV | Residential | Windows, double hung, not weatherstripped – best estimate | ELA4 | 2.5 cm2/m | C1 |
| WNDBNW_RMN | Residential | Windows, double hung, not weatherstripped –minimum | ELA4 | 0.86 cm2/m | C1 |
| WNDBNW_RMX | Residential | Windows, double hung, not weatherstripped –maximum | ELA4 | 6.1 cm2/m | C1 |
| WNDBNWSM_RAV | Residential | Windows, double hung with storm, not weatherstripped – best estimate | ELA4 | 0.97 cm2/m | C1 |
| WNDBNWSM_RMN | Residential | Windows, double hung with storm, not weatherstripped –minimum | ELA4 | 0.48 cm2/m | C1 |
| WNDBNWSM_RMX | Residential | Windows, double hung with storm, not weatherstripped –maximum | ELA4 | 1.7 cm2/m | C1 |
| WNDBWE_RAV | Residential | Windows, double hung, weatherstripped – best estimate | ELA4 | 0.65 cm2/m | C1 |
| WNDBWE_RMN | Residential | Windows, double hung, weatherstripped –minimum | ELA4 | 0.2 cm2/m | C1 |
| WNDBWE_RMX | Residential | Windows, double hung, weatherstripped – maximum | ELA4 | 1.9 cm2/m | C1 |
| WNDBWESM_RAV | Residential | Windows, double hung with storm, weatherstripped – best estimate | ELA4 | 0.79 cm2/m | C1 |
| WNDBWESM_RMN | Residential | ndows, double hung with storm, weatherstripped – minimum | ELA4 | 0.44 cm2/m | C1 |
| WNDBWESM_RMX | Residential | ndows, double hung with storm, weatherstripped – maximum | ELA4 | 1.0 cm2/m | C1 |
| WNJA_RAV | Residential | Windows, jalousise – best estimate | ELA4 | 3.38 cm2/m | C1 |
| WNSISHWE_RAV | Residential | Windows, single hung, weatherstripped – best estimate | ELA4 | 0.87 cm2/m | C1 |
| WNSISHWE_RMN | Residential | Windows, single hung, weatherstripped – minimum | ELA4 | 0.62 cm2/m | C1 |
| WNSISHWE_RMX | Residential | Windows, single hung, weatherstripped – maximum | ELA4 | 1.24 cm2/m | C1 |
| WNSISLAL_RAV | Residential | Windows, single horizontal slider, aluminum – best estimate | ELA4 | 0.8 cm2/m | C1 |
| WNSISLAL_RMN | Residential | Windows, single horizontal slider, aluminum – minimum | ELA4 | 0.27 cm2/m | C1 |
| WNSISLAL_RMX | Residential | Windows, single horizontal slider, aluminum – maximum | ELA4 | 2.06 cm2/m | C1 |
| WNSISLWD_RAV | Residential | Windows, single horizontal slider, wood – best estimate | ELA4 | 0.44 cm2/m | C1 |
| WNSISLWD_RMN | Residential | Windows, single horizontal slider, wood – minimum | ELA4 | 0.27 cm2/m | C1 |
| WNSISLWD_RMX | Residential | Windows, single horizontal slider, wood – maximum | ELA4 | 0.99 cm2/m | C1 |
| WNSISLWE_RAV | Residential | Windows, single horizontal slider, weatherstripped – best estimate | ELA4 | 0.67 cm2/m | C1 |
| WNSISLWE_RMN | Residential | Windows, single horizontal slider, weatherstripped – minimum | ELA4 | 0.2 cm2/m | C1 |
| WNSISLWE_RMX | Residential | Windows, single horizontal slider, weatherstripped – maximum | ELA4 | 2.06 cm2/m | C1 |
| WNSLALWE_RAV | Residential | Windows, double horizontal slider, aluminum, weatherstripped - best estimate | ELA4 | 0.72 cm2/m | C1 |
| WNSLALWE_RMN | Residential | Windows, double horizontal slider, aluminum, weatherstripped – minimum | ELA4 | 0.58 cm2/m | C1 |
| WNSLALWE_RMX | Residential | Windows, double horizontal slider, aluminum, weatherstripped –maximum | ELA4 | 0.8 cm2/m | C1 |
| WNSLNW_RAV | Residential | Windows, double horizontal slider, not weatherstripped – best estimate | ELA4 | 1.1 cm2/m | C1 |
| WNSLNW_RMN | Residential | Windows, double horizontal slider, not weatherstripped – minimum | ELA4 | 0.019 cm2/m | C1 |
| WNSLNW_RMX | Residential | Windows, double horizontal slider, not weatherstripped – maximum | ELA4 | 3.4 cm2/m | C1 |
| WNSLWDWE_RAV | Residential | Windows, double horizontal slider, wood, weatherstripped – best estimate | ELA4 | 0.55 cm2/m | C1 |
| WNSLWDWE_RMN | Residential | Windows, double horizontal slider, wood, weatherstripped – minimum | ELA4 | 0.15 cm2/m | C1 |
| WNSLWDWE_RMX | Residential | Windows, double horizontal slider, wood, weatherstripped – maximum | ELA4 | 1.72 cm2/m | C1 |

#### Appendix C2: RESMISC.lb3

Assorted residential airtightness values used in previous airflow modeling studies at NIST.

| Element Name | Building Type | Description | Model | Value | Reference |
| --- | --- | --- | --- | --- | --- |
| DRAT_RAV | Residential | Attic door, typical value | ELA4 | 30 cm2/item | C2 |
| DRAT_RMN | Residential | Attic door, tight value | ELA4 | 18 cm2/item | C2 |
| CE_RAV | Residential | General ceiling, typical value | ELA4 | 1.8 cm2/m2 | C2 |
| CE_RMN | Residential | General ceiling, tight value | ELA4 | 0.79 cm2/m2 | C2 |
| DRCTCL_RAV | Residential | Closet door, closed, typical value | ELA4 | 0.9 cm2/m | C2 |
| DRCTCL_RMN | Residential | Closet door, closed, tight value | ELA4 | 0.25 cm2/m | C2 |
| DRCTFR_RAV | Residential | Closet door frame, typical value | ELA4 | 25 cm2/item | C2 |
| DRCTFR_RMN | Residential | Closet door frame, tight value | ELA4 | 12 cm2/item | C2 |
| CPEN_RAV | Residential | HVAC ceiling penetration, typical value | ELA4 | 5 cm2/item | C2 |
| CPEN_RMN | Residential | HVAC ceiling penetration, tight value | ELA4 | 1 cm2/item | C2 |
| DREXSI_RAV | Residential | Door, exterior, single, typical value | ELA4 | 21 cm2/item | C2 |
| DREXSI_RMN | Residential | Door, exterior, single, tight value | ELA4 | 12 cm2/item | C2 |
| DREXFRWD_RAV | Residential | Door, exterior, wood, frame, typical value | ELA4 | 1.7 cm2/m2 | C2 |
| DREXFRWD_RMN | Residential | Door, exterior, wood, frame, tight value | ELA4 | 0.3 cm2/m2 | C2 |
| VEBA_RAV | Residential | Bathroom exhaust vent, typical value | ELA4 | 20 cm2/item | C2 |
| VEBA_RMN | Residential | Bathroom exhaust vent, tight value | ELA4 | 10 cm2/item | C2 |
| VEKI_RAV | Residential | Kitchen exhaust vent, typical value | ELA4 | 40 cm2/item | C2 |
| VEKI_RMN | Residential | Kitchen exhaust vent, tight value | ELA4 | 5 cm2/item | C2 |
| JTCEWL_RAV | Residential | Ceiling-wall joint, typical value | ELA4 | 1.5 cm2/m | C2 |
| JTCEWL_RMN | Residential | Ceiling-wall joint, tight value | ELA4 | 0.5 cm2/m | C2 |
| JTFLWL_RAV | Residential | Floor-wall joint, typical value | ELA4 | 4 cm2/m | C2 |
| JTFLWL_RMN | Residential | Floor -wall joint, tight value | ELA4 | 0.8 cm2/m | C2 |
| JTWLWL_RAV | Residential | Wall-wall joint, typical value | ELA4 | 1.5 cm2/m | C2 |
| JTWLWL_RMN | Residential | Wall-wall joint, tight value | ELA4 | 0.5 cm2/m | C2 |
| DRGA_RAV | Residential | Garage door, typical value | ELA4 | 0.45 cm2/m | C2 |
| DRGA_RMN | Residential | Garage door, tight value | ELA4 | 0.31 cm2/m | C2 |
| DRGAFRWD_RAV | Residential | Garage door frame, wood, typical value | ELA4 | 1.7 cm2/m2 | C2 |
| DRGAFRWD_RMN | Residential | Garage door frame, wood, tight value | ELA4 | 0.3 cm2/m2 | C2 |
| RFGA_RAV | Residential | Garage roof, typical value | ELA4 | 1.8 cm2/m2 | C2 |
| RFGA_RMN | Residential | Garage roof, tight value | ELA4 | 0.79 cm2/m2 | C2 |
| DWHA_RAV | Residential | Hall doorway, typical value | ELA4 | 2.4 m2/item | C2 |
| DRINCL_RAV | Residential | Door, interior, closed, typical value | ELA4 | 140 cm2/item | C2 |
| DRINCL_RMN | Residential | Door, interior, closed, tight value | ELA4 | 75 cm2/item | C2 |
| DRINOP_RAV | Residential | Door, interior, open, typical value | ELA4 | 2.1 cm2/item | C2 |
| WLIN_RAV | Residential | Wall, interior, typical value | ELA4 | 2.0 cm2/m2 | C2 |
| PEEC_RAV | Residential | Electrical outlet, typical value | ELA4 | 2.5 cm2/item | C2 |
| PEEC_RMN | Residential | Electrical outlet, tight value | ELA4 | 0.5 cm2/item | C2 |
| PEPL_RAV | Residential | Plumbing penetration, interior, typical value | ELA4 | 6 cm2/item | C2 |
| PEPL_RMN | Residential | Plumbing penetration, interior, tight value | ELA4 | 2 cm2/item | C2 |
| DREXSLGL_RAV | Residential | Door, exterior, sliding glass, typical value | ELA4 | 22 cm2/item | C2 |
| DREXSLGL_RMN | Residential | Door, exterior, sliding glass, tight value | ELA4 | 3 cm2/item | C2 |
| VEAT_RAV | Residential | Attic vent, based on attic floor area, typical value | ELA4 | 1 cm2/300 cm2 | C2 |
| WNDB_RAV | Residential | Window, double hung, typical value | ELA4 | 2.5 cm2/m | C2 |
| WNDB_RMN | Residential | Window, double hung, tight value | ELA4 | 0.65 cm2/m | C2 |
| WNFRWD_RAV | Residential | Window door frame, wood, typical value | ELA4 | 1.7 cm2/m2 | C2 |
| WNFRWD_RMN | Residential | Window door frame, wood, tight value | ELA4 | 0.3 cm2/m2 | C2 |
| WLEX_R | Residential | Wall, exterior | ELA4 | 0.1 cm2/m2 | C3 |
| JTFLWL_R | Residential | Floor -wall joint | ELA4 | 0.8 cm2/m | C3 |
| JTCEWL_R | Residential | Ceiling-wall joint | ELA4 | 0.5 cm2/m | C3 |
| JTCR_R | Residential | Wall-wall corner joint | ELA4 | 0.5 cm2/m | C3 |
| WN_R | Residential | Window | ELA4 | 2 cm2/m | C3 |
| DRFREX_R | Residential | Exterior door frame | ELA4 | 0.3 cm2/m2 | C3 |
| DREXSLGL_R | Residential | Door, exterior, sliding glass | ELA4 | 3 cm2/item | C3 |
| DREX_R | Residential | Door, exterior | ELA4 | 6 cm2/item | C3 |
| WLGAEX_R | Residential | Exterior garage wall, exterior | ELA4 | 0.4 cm2/m2 | C3 |
| ITGAEX_R | Residential | Wall-floor and wall-ceiling interface, exterior garage wall | ELA4 | 2 cm2/m | C3 |
| CECS_R | Residential | Crawl space ceiling | ELA4 | 0.5 cm2/m2 | C3 |
| FLAT_R | Residential | Attic floor | ELA4 | 0.5 cm2/m2 | C3 |
| PEDW_R | Residential | Duct penetration in crawl space ceiling or attic floor | ELA4 | 1 cm2/item | C3 |
| VECS_R | Residential | Crawl space vent, based on floor area | ELA4 | 1 cm2/150 cm2 | C3 |
| WLIN_R | Residential | Wall, interior | ELA4 | 2.0 cm2/m2 | C3 |
| CEIN_R | Residential | Ceiling, interior | ELA4 | 0.79 cm2/m2 | C3 |
| DRINCL_R | Residential | Door, interior, closed, including frame and undercut | ELA4 | 250 cm2/item | C3 |
| WLEX_RM | Residential | Wall, exterior, manufactured home | ELA4 | 0.067 cm2/m2 | C4 |
| JTFLWL_RM | Residential | Floor-wall joint, manufactured home | ELA4 | 0.53 cm2/m | C4 |
| JTCEWL_RM | Residential | Ceiling-wall joint, manufactured home | ELA4 | 0.33 cm2/m | C4 |
| JTCR_RM | Residential | Wall-wall corner joint, manufactured home | ELA4 | 0.33 cm2/m | C4 |
| WN1_RM | Residential | Window, manufactured home | ELA4 | 2.3 cm2/m | C4 |
| WN2_RM | Residential | Window, manufactured home | ELA4 | 2.1 cm2/m | C4 |
| WN3_RM | Residential | Window, manufactured home | ELA4 | 2.7 cm2/m | C4 |
| WN4_RM | Residential | Window, manufactured home | ELA4 | 0.9 cm2/m | C4 |
| DREX_RM | Residential | Door, exterior, manufactured home | ELA4 | 4 cm2/item | C4 |
| CECS_RM | Residential | Crawl space ceiling, manufactured home | ELA4 | 1.33 cm2/m2 | C4 |
| FLAT_RM | Residential | Attic floor, manufactured home | ELA4 | 0.67 cm2/m2 | C4 |
| WLIN_RM | Residential | Wall, interior, manufactured home | ELA4 | 2.0 cm2/m2 | C4 |
| DRBACL_RM | Residential | Bathroom door, closed, including frame and undercut, manufactured home | ELA4 | 330 cm2/item | C4 |
| DRINCL_RM | Residential | Interior (bedroom) door, closed, including frame and undercut, manufactured home | ELA4 | 410 cm2/item | C4 |
| DRBAOP_RM | Residential | Bathroom door, open, including frame and undercut, manufactured home | ELA4 | 1.3 m2/item | C4 |
| DRINOP_RM | Residential | Interior (bedroom) door, open, including frame and undercut, manufactured home | ELA4 | 1.6 m2/item | C4 |

#### Appendix C3: C&ISUM.lb3

Summary values from database of commercial and institutional building airtightness values.

| Element Name | Building Type | Description | Model | Value | Reference |
| --- | --- | --- | --- | --- | --- |
| WLEXMA_CAV | Commercial | Exterior wall, masonry, mean | ELA4 | 4.2 cm2/m2 | C5 |
| WLEXMA_C+S | Commercial | Exterior wall, masonry, mean plus one standard deviation | ELA4 | 6.9 cm2/m2 | C5 |
| WLEXMA_C-S | Commercial | Exterior wall, masonry, mean minus one standard deviation | ELA4 | 1.5 cm2/m2 | C5 |
| WLEXMA_CMN | Commercial | Exterior wall, masonry, minimum | ELA4 | 0.6 cm2/m2 | C5 |
| WLEXMA_CMX | Commercial | Exterior wall, masonry, maximum | ELA4 | 11.4 cm2/m2 | C5 |
| WLEXCP_CAV | Commercial | Exterior wall, concrete panel, mean | ELA4 | 4.0 cm2/m2 | C5 |
| WLEXCP_C+S | Commercial | Exterior wall, concrete panel, mean plus one standard deviation | ELA4 | 6.9 cm2/m2 | C5 |
| WLEXCP_C-S | Commercial | Exterior wall, concrete panel, mean minus one standard deviation | ELA4 | 1.2 cm2/m2 | C5 |
| WLEXCP_CMN | Commercial | Exterior wall, concrete panel, minimum | ELA4 | 1.1 cm2/m2 | C5 |
| WLEXCP_CMX | Commercial | Exterior wall, concrete panel, maximum | ELA4 | 10.0 cm2/m2 | C5 |
| WLEXFRMA_CAV | Commercial | Exterior wall, frame/masonry, mean | ELA4 | 9.1 cm2/m2 | C5 |
| WLEXFRMA_C+S | Commercial | Exterior wall, frame/masonry, mean plus one standard deviation | ELA4 | 13.2 cm2/m2 | C5 |
| WLEXFRMA_C-S | Commercial | Exterior wall, frame/masonry, mean minus one standard deviation | ELA4 | 4.9 cm2/m2 | C5 |
| WLEXFRMA_CMN | Commercial | Exterior wall, frame/masonry, minimum | ELA4 | 4.5 cm2/m2 | C5 |
| WLEXFRMA_CMX | Commercial | Exterior wall, frame, maximum | ELA4 | 19.9 cm2/m2 | C5 |
| WLEXFR_CAV | Commercial | Exterior wall, frame, mean | ELA4 | 8.6 cm2/m2 | C5 |
| WLEXFR_C+S | Commercial | Exterior wall, frame, mean plus one standard deviation | ELA4 | 13.0 cm2/m2 | C5 |
| WLEXFR_C-S | Commercial | Exterior wall, frame, mean minus one standard deviation | ELA4 | 4.3 cm2/m2 | C5 |
| WLEXFR_CMN | Commercial | Exterior wall, frame, minimum | ELA4 | 3.1 cm2/m2 | C5 |
| WLEXFR_CMX | Commercial | Exterior wall, frame, maximum | ELA4 | 15.6 cm2/m2 | C5 |
| WLEXMN_CAV | Commercial | Exterior wall, manufactured, mean | ELA4 | 4.3 cm2/m2 | C5 |
| WLEXMN_C+S | Commercial | Exterior wall, manufactured, mean plus one standard deviation | ELA4 | 7.0 cm2/m2 | C5 |
| WLEXMN_C-S | Commercial | Exterior wall, manufactured, mean minus one standard deviation | ELA4 | 1.5 cm2/m2 | C5 |
| WLEXMN_CMN | Commercial | Exterior wall, manufactured, minimum | ELA4 | 2.4 cm2/m2 | C5 |
| WLEXMN_CMX | Commercial | Exterior wall, manufactured, maximum | ELA4 | 8.7 cm2/m2 | C5 |
| WLEXME_CAV | Commercial | Exterior wall, metal, mean | ELA4 | 4.6 cm2/m2 | C5 |
| WLEXME_C+S | Commercial | Exterior wall, metal, mean plus one standard deviation | ELA4 | 7.2 cm2/m2 | C5 |
| WLEXME_C-S | Commercial | Exterior wall, metal, mean minus one standard deviation | ELA4 | 1.9 cm2/m2 | C5 |
| WLEXME_CMN | Commercial | Exterior wall, metal, minimum | ELA4 | 2.0 cm2/m2 | C5 |
| WLEXME_CMX | Commercial | Exterior wall, metal, maximum | ELA4 | 8.0 cm2/m2 | C5 |
| WLEXCW_CAV | Commercial | Exterior wall, curtain wall, mean | ELA4 | 2.7 cm2/m2 | C5 |
| WLEXCW_C+S | Commercial | Exterior wall, curtain wall, mean plus one standard deviation | ELA4 | 5.6 cm2/m2 | C5 |
| WLEXCW_CMN | Commercial | Exterior wall, curtain wall, minimum | ELA4 | 0.8 cm2/m2 | C5 |
| WLEXCW_CMX | Commercial | Exterior wall, curtain wall, maximum | ELA4 | 6.9 cm2/m2 | C5 |
| WLEXOF_CAV | Commercial | Exterior wall, office building, mean | ELA4 | 4.1 cm2/m2 | C5 |
| WLEXOF_C+S | Commercial | Exterior wall, office building, mean plus one standard deviation | ELA4 | 7.8 cm2/m2 | C5 |
| WLEXOF_C-S | Commercial | Exterior wall, office building, mean minus one standard deviation | ELA4 | 0.4 cm2/m2 | C5 |
| WLEXOF_CMN | Commercial | Exterior wall, office building, minimum | ELA4 | 0.6 cm2/m2 | C5 |
| WLEXOF_CMX | Commercial | Exterior wall, office building, maximum | ELA4 | 19.9 cm2/m2 | C5 |
| WLEXSC_IAV | Institutional | Exterior wall, school, mean | ELA4 | 3.1 cm2/m2 | C5 |
| WLEXSC_I+S | Institutional | Exterior wall, school, mean plus one standard deviation | ELA4 | 5.1 cm2/m2 | C5 |
| WLEXSC_I-S | Institutional | Exterior wall, school, mean minus one standard deviation | ELA4 | 1.0 cm2/m2 | C5 |
| WLEXSC_IMN | Institutional | Exterior wall, school, minimum | ELA4 | 0.4 cm2/m2 | C5 |
| WLEXSC_IMX | Institutional | Exterior wall, school, maximum | ELA4 | 8.6 cm2/m2 | C5 |
| WLEXID_NAV | Industrial | Exterior wall, industrial building, mean | ELA4 | 3.8 cm2/m2 | C5 |
| WLEXID_N+S | Industrial | Exterior wall, industrial building, mean plus one standard deviation | ELA4 | 7.9 cm2/m2 | C5 |
| WLEXID_NMN | Industrial | Exterior wall, industrial building, minimum | ELA4 | 0.4 cm2/m2 | C5 |
| WLEXID_NMX | Industrial | Exterior wall, industrial building, maximum | ELA4 | 15.6 cm2/m2 | C5 |
| WLEXRE_CAV | Commercial | Exterior wall, retail, mean | ELA4 | 6.9 cm2/m2 | C5 |
| WLEXRE_C+S | Commercial | Exterior wall, retail, mean plus one standard deviation | ELA4 | 10.5 cm2/m2 | C5 |
| WLEXRE_C-S | Commercial | Exterior wall, retail, mean minus one standard deviation | ELA4 | 3.3 cm2/m2 | C5 |
| WLEXRE_CMN | Commercial | Exterior wall, retail, minimum | ELA4 | 0.7 cm2/m2 | C5 |
| WLEXRE_CMX | Commercial | Exterior wall, retail, maximum | ELA4 | 12.0 cm2/m2 | C5 |
| WLEXRS_CAV | Commercial | Exterior wall, restaurant, mean | ELA4 | 3.8 cm2/m2 | C5 |
| WLEXRS_C+S | Commercial | Exterior wall, restaurant, mean plus one standard deviation | ELA4 | 5.2 cm2/m2 | C5 |
| WLEXRS_C-S | Commercial | Exterior wall, restaurant, mean minus one standard deviation | ELA4 | 2.3 cm2/m2 | C5 |
| WLEXRS_CMN | Commercial | Exterior wall, restaurant, minimum | ELA4 | 1.4 cm2/m2 | C5 |
| WLEXRS_CMX | Commercial | Exterior wall, restaurant, maximum | ELA4 | 5.5 cm2/m2 | C5 |
| WLEXAS_NAV | Institutional | Exterior wall, assembly, mean | ELA4 | 3.7 cm2/m2 | C5 |
| WLEXAS_N+S | Institutional | Exterior wall, assembly, mean plus one standard deviation | ELA4 | 5.8 cm2/m2 | C5 |
| WLEXAS_N-S | Institutional | Exterior wall, assembly, mean minus one standard deviation | ELA4 | 1.5 cm2/m2 | C5 |
| WLEXAS_NMN | Institutional | Exterior wall, assembly, minimum | ELA4 | 1.8 cm2/m2 | C5 |
| WLEXAS_NMX | Institutional | Exterior wall, assembly, maximum | ELA4 | 6.3 cm2/m2 | C5 |
| WLEXHC_IAV | Institutional | Exterior wall, healthcare, mean | ELA4 | 5.6 cm2/m2 | C5 |
| WLEXHC_I+S | Institutional | Exterior wall, healthcare, mean plus one standard deviation | ELA4 | 7.5 cm2/m2 | C5 |
| WLEXHC_I-S | Institutional | Exterior wall, healthcare, mean minus one standard deviation | ELA4 | 3.7 cm2/m2 | C5 |
| WLEXHC_IMN | Institutional | Exterior wall, healthcare, minimum | ELA4 | 3.7 cm2/m2 | C5 |
| WLEXHC_IMX | Institutional | Exterior wall, healthcare, maximum | ELA4 | 7.6 cm2/m2 | C5 |
| WLEXSP_CAV | Commercial | Exterior wall, sports facility, mean | ELA4 | 7.4 cm2/m2 | C5 |
| WLEXSP_C+S | Commercial | Exterior wall, sports facility, mean plus one standard deviation | ELA4 | 10.1 cm2/m2 | C5 |
| WLEXSP_C-S | Commercial | Exterior wall, sports facility, mean minus one standard deviation | ELA4 | 4.8 cm2/m2 | C5 |
| WLEXSP_CMN | Commercial | Exterior wall, sports facility, minimum | ELA4 | 3.7 cm2/m2 | C5 |
| WLEXSP_CMX | Commercial | Exterior wall, sports facility, maximum | ELA4 | 9.8 cm2/m2 | C5 |

#### Appendix C4: C&IMISC4.lb3

Assorted commercial, institutional and high-rise residential airtightness values

| Element Name | Building Type | Description | Model | Value | Reference |
| --- | --- | --- | --- | --- | --- |
| WLEXPC6A_C | Commercial | Exterior Wall: Precast concrete panel, Building A | ELA4 | 2.19 cm2/m2 | C6 |
| WNIO6A_CMN | Commercial | Inoperable window, Building A, minimum | ELA4 | 0.58 cm2/m2 | C6 |
| WNIO6A_CMX | Commercial | Inoperable window, Building A, maximum | ELA4 | 1.73 cm2/m2 | C6 |
| WLEXTV6AA_C | Commercial | Exterior Wall: Tile veneer, Building AA | ELA4 | 1.34 cm2/m2 | C6 |
| WNIO6AA_CAV | Commercial | Inoperable window, Building AA, typical | ELA4 | 0.58 cm2/m2 | C6 |
| WLEXPC6C_C | Commercial | Exterior Wall: Precast concrete panel, Building C | ELA4 | 1.96 cm2/m2 | C6 |
| WNOO6C_CMN | Commercial | Operable window, Building C, minimum | ELA4 | 1.73 cm2/m2 | C6 |
| WNOO6C_CMX | Commercial | Operable window, Building C, maximum | ELA4 | 3.46 cm2/m2 | C6 |
| WLEXBR6H_C | Commercial | Exterior Wall: Brick veneer, Building H | ELA4 | 0.62 cm2/m2 | C6 |
| WLEXBR6N_C | Commercial | Exterior Wall: Brick veneer, Building N | ELA4 | 2.35 cm2/m2 | C6 |
| WNIO6N_CAV | Commercial | Inoperable window, Building N, typical | ELA4 | 0.86cm2/m2 | C6 |
| WLEXBR6P_C | Commercial | Exterior Wall: Brick veneer, Building P | ELA4 | 1.14 cm2/m2 | C6 |
| WLEXPC6S_C | Commercial | Exterior Wall: Precast concrete panel, Building S | ELA4 | 3.01 cm2/m2 | C6 |
| WLEXPC7O_C | Commercial | Exterior Wall: Precast concrete panel, Building O | ELA4 | 6.88 cm2/m2 | C7 |
| WLEXCW8A_C | Commercial | Exterior Wall: Glass and metal curtain wall, Building A | ELA4 | 5.07 cm2/m2 | C8 |
| WLEXPC8B_C | Commercial | Exterior Wall: Precast concrete panel, Building B | ELA4 | 2.51 cm2/m2 | C8 |
| WLEXPC9A_C | Commercial | Exterior Wall: Precast concrete panel, Building A | ELA4 | 3.59 cm2/m2 | C9 |
| WLEXPC9B_C | Commercial | Exterior Wall: Precast concrete panel, Building B | ELA4 | 1.79 cm2/m2 | C9 |
| WLEXPC9C_C | Commercial | Exterior Wall: Precast concrete panel, Building C | ELA4 | 1.79 cm2/m2 | C9 |
| WLEXCW9D_C | Commercial | Exterior Wall: Curtain wall, Building D | ELA4 | 2.03 cm2/m2 | C9 |
| WLEXCW9E_C | Commercial | Exterior Wall: Curtain wall, Building E | ELA4 | 1.14 cm2/m2 | C9 |
| WLEXPC9F_C | Commercial | Exterior Wall: Precast concrete panel, Building F | ELA4 | 1.14 cm2/m2 | C9 |
| WLEXPC9G_C | Commercial | Exterior Wall: Precast concrete panel, Building G | ELA4 | 1.67 cm2/m2 | C9 |
| WLEXCW9H_C | Commercial | Exterior Wall: Curtain wall, Building H | ELA4 | 0.78 cm2/m2 | C9 |
| WLEX10_NAV | Industrial | Exterior Wall: Average | ELA4 | 0.96 cm2/m2 | C10 |
| WLEX10_NMN | Industrial | Exterior Wall: Minimum | ELA4 | 0.48 cm2/m2 | C10 |
| WLEX10_NMX | Industrial | Exterior Wall: Maximum | ELA4 | 2.40 cm2/m2 | C10 |
| WLEXSC11_NAV | Institutional | Exterior Wall: School, average | ELA4 | 1.44 cm2/m2 | C11 |
| WLEXSC11_NMN | Institutional | Exterior Wall: School, minimum | ELA4 | 0.48 cm2/m2 | C11 |
| WLEXSC11_NMX | Institutional | Exterior Wall: School, maximum | ELA4 | 1.60 cm2/m2 | C11 |
| WLEXSC12_NAV | Institutional | Exterior Wall: School, average | ELA4 | 4.48 cm2/m2 | C12 |
| WLEXSC12_NMN | Institutional | Exterior Wall: School, minimum | ELA4 | 3.20 cm2/m2 | C12 |
| WLEXSC12_NMX | Institutional | Exterior Wall: School, maximum | ELA4 | 4.80 cm2/m2 | C12 |
| WLEXSC13_CAV | Commercial | Exterior Wall: Retail stores/shopping malls, average | ELA4 | 7.84 cm2/m2 | C13 |
| WLEXSC13_CMN | Commercial | Exterior Wall: Retail stores/shopping malls, minimum | ELA4 | 4.00 cm2/m2 | C13 |
| WLEXSC13_CMX | Commercial | Exterior Wall: Retail stores/shopping malls, maximum | ELA4 | 11.20cm2/m2 | C13 |
| WLELCC14A_C | Commercial | Elevator shaft wall, cast-in-place concrete, 17 story office building | ELA4 | 5.55 cm2/m2 | C14 |
| WLELCC14B_C | Commercial | Elevator shaft wall, cast-in-place concrete, 14 story office building | ELA4 | 2.25 cm2/m2 | C14 |
| WLELCC14C_C | Commercial | Elevator shaft wall, cast-in-place concrete, 12 story office building | ELA4 | 1.72 cm2/m2 | C14 |
| WLELCOBL14D_C | Commercial | Elevator shaft wall, concrete block, 6 story office building | ELA4 | 5.55 cm2/m2 | C14 |
| WLELCC14E_C | Commercial | Elevator shaft wall, cast-in-place concrete, 16 story office building | ELA4 | 0.75 cm2/m2 | C14 |
| WLELTIBL14F_C | Commercial | Elevator shaft wall, clay tile block, 10 story office building | ELA4 | 6.15 cm2/m2 | C14 |
| WLELCC14G_C | Commercial | Elevator shaft wall, cast-in-place concrete, 14 story office building | ELA4 | 2.25 cm2/m2 | C14 |
| WLSRCC14A_C | Commercial | Stair shaft wall, cast-in-place concrete, 19 story office building | ELA4 | 0.45 cm2/m2 | C14 |
| WLSRCC14B_C | Commercial | Stair shaft wall, cast-in-place concrete, 23 story office building | ELA4 | 0.07 cm2/m2 | C14 |
| WLSRCC14C_C | Commercial | Stair shaft wall, cast-in-place concrete, 28 story office building | ELA4 | 0.15 cm2/m2 | C14 |
| WLSRCC14D_C | Commercial | Stair shaft wall, cast-in-place concrete, 23 story office building | ELA4 | 0.41 cm2/m2 | C14 |
| WLSRCC14E_C | Commercial | Stair shaft wall, cast-in-place concrete, 15 story office building | ELA4 | 0.30 cm2/m2 | C14 |
| WLSRCC14F_C | Commercial | Stair shaft wall, cast-in-place concrete, 17 story office building | ELA4 | 1.42 cm2/m2 | C14 |
| WLSRTIBL14G_C | Commercial | Stair shaft wall, clay tile block, 11 story office building | ELA4 | 0.67 cm2/m2 | C14 |
| WLSRCC14H_C | Commercial | Stair shaft wall, cast-in-place concrete, 12 story office building | ELA4 | 0.37 cm2/m2 | C14 |
| DREL14_CMN | Commercial | Elevator doors, 7 office buildings, minimum | ELA4 | 187.5 cm2/door | C14 |
| DREL14_CMX | Commercial | Elevator doors, 7 office buildings, maximum | ELA4 | 262.5 cm2/door | C14 |
| DRSR14_CMN | Commercial | Stair shaft doors, 8 office buildings, minimum | ELA4 | 75.0 cm2/door | C14 |
| DRSR14_CMX | Commercial | Stair shaft doors, 8 office buildings, maximum | ELA4 | 187.5 cm2/door | C14 |
| FLCO15_CMN | Commercial | Floor: Office building, reinforced concrete, minimum | ELA4 | 0.18 cm2/m2 | C15 |
| FLCO15_CMX | Commercial | Floor: Office building, reinforced concrete, maximum | ELA4 | 0.35 cm2/m2 | C15 |
| WLEX16A_R | Residential | Exterior Wall: Individual apartment (#405) in high-rise building | ELA4 | 1.87 cm2/m2 | C16 |
| WLEX16B_R | Residential | Exterior Wall: Individual apartment (#509) in high-rise building | ELA4 | 2.36 cm2/m2 | C16 |
| WLEX16C_R | Residential | Exterior Wall: Individual apartment (#609) in high-rise building | ELA4 | 2.33 cm2/m2 | C16 |
| WLEX16D_R | Residential | Exterior Wall: Individual apartment (#1009) in high-rise building | ELA4 | 1.57cm2/m2 | C16 |
| WLEXBRBL17_R | Residential | Exterior Wall: 5-story apartment building, brick and block backup | ELA4 | 2.55 cm2/m2 | C17 |
| FLCEAP17_RMN | Residential | Floor/ceiling interface: 5-story apartment building, minimum | ELA4 | 0.11 cm2/m2 | C17 |
| FLCEAP17_RMX | Residential | Floor/ceiling interface: 5-story apartment building, maximum | ELA4 | 0.43 cm2/m2 | C17 |
| FLCEAP17_RAV | Residential | Floor/ceiling interface: 5-story apartment building, average | ELA4 | 0.32 cm2/m2 | C17 |
| WLINAP17_RMN | Residential | Interior partition: 5-story apartment building, minimum | ELA4 | 0.37 cm2/m2 | C17 |
| WLINAP17_RMX | Residential | Interior partition: 5-story apartment building, maximum | ELA4 | 2.25 cm2/m2 | C17 |
| WLINAP17_RAV | Residential | Interior partition: 5-story apartment building, average | ELA4 | 1.12 cm2/m2 | C17 |
| WLEXAP18_R | Residential | Exterior Wall: Multi-story apartment building | ELA4 | 1.46 cm2/m2 | C18 |
| WLEXAP19D_R | Residential | Exterior Wall: High-story apartment building D | ELA4 | 1.65 cm2/m2 | C19 |
| WLEXAP19V_R | Residential | Exterior Wall: High-story apartment building V | ELA4 | 2.62 cm2/m2 | C19 |

#### Appendix C5: REFERENCES

Sources of data in flow element libraries.

C1.	ASHRAE Handbook 1997. American Society of Heating, Refrigerating and Air-Conditioning Engineers, Inc., Atlanta, GA.  Chapter 25 Table 3.

C2.	Emmerich, S.J and Persily, A.K.. 1996. “Multizone Modeling of Three Residential Indoor Air Quality Control Options,” NISTIR 5801, National Institute of Standards and Technology, Gaithersburg, MD.

C3.	Persily, A.K. 1998. “A Modeling Study of Ventilation, IAQ  and Energy Impacts of Residential Mechanical Ventilation,” NISTIR 6162, National Institute of Standards and Technology, Gaithersburg, MD.

C4.	Persily, A.K. 2000. “A Modeling Study of Ventilation in Manufactured Houses.” NISTIR 6455, National Institute of Standards and Technology, Gaithersburg, MD.

C5.	Persily, A.K. 1998. “Airtightness of Commercial and Institutional Buildings: Blowing Holes in the Myth of Tight Buildings.” DOE/ASHRAE/ORNL/BETEC/NRCC/CIBSE Conference Thermal Performance of the Exterior Envelopes of Buildings VII, 829-837.

C6.	Persily, A. K. and R. A. Grot. 1986. “Pressurization Testing of Federal Buildings.” Measured Air Leakage of Buildings, ASTM STP 904. H. R. Trechsel and P. L. Lagus, Eds. American Society for Testing and Materials, 184-200.

C7.	Persily, A.K., W.S. Dols, S.J. Nabinger and S. Kirchner. 1991. “Preliminary Results of the Environmental Evaluation of the Federal Records Center in Overland Missouri,” NISTIR 4643, National Institute of Standards and Technology, Gaithersburg, MD.

C8.	Perera, M.D.A.E.S., R.K. Stephen and R.G. Tull. 1990. “Airtightness Measurements in Two UK Office Buildings,” Air Change Rate and Airtightness in Buildings, ASTM STP 1067, M.H. Sherman, Ed., American Society for Testing and Materials, 211-221.

C9.	Tamura, G.T. and C.Y. Shaw. 1976. “Studies on Exterior Wall Air Tightness and Air Infiltration of Tall Buildings,” ASHRAE Transactions, Vol. 82, Part 1, 122-134.

C10.	Lundin, L.I. 1986. “Air Leakage in Industrial Buildings – Description of Equipment,” Measured Air Leakage of Buildings, H.R. Trechsel and P.L. Lagus Eds., ASTM STP 904, American Society for Testing and Materials, Philadelphia, 101-105.

C11.	Brennan, T. W. Turner, G. Fisher, B. Thompson and B. Ligman. 1992. “Fan Pressurization of School Buildings,” Thermal Performance of the Exterior Envelopes of Buildings V, 643-645.

C12.	Shaw, C.Y., and L. Jones. 1979. “Air Tightness and Air Infiltration of School Buildings,” ASHRAE Transactions, Vol. 85, Part 1, 85-95.

C13.	Shaw, C.Y. 1981. “Air Tightness: Supermarkets and Shopping Malls,” ASHRAE Journal, Vol. 23, 44-46.

C14.	Tamura, G.T. and C.Y. Shaw. 1976 “Air Leakage Data for the Design of Elevator and Stair Shaft Pressurization Systems,” ASHRAE Transactions, Vol. 82, Part 2, 179-190.

C15.	Tamura, G.T. and C.Y. Shaw. 1978. “Experimental Studies of Mechanical Venting for Smoke Control in Tall Office Buildings,” ASHRAE Transactions, Vol. 84, Part 1, 54-71.

C16.	Gulay, B.W. and C.D. Stewart. 1991. Field Investigation of Airtightness, Air Movement and Indoor Air Quality in High Rise Apartment Buildings Prairie Region. Canada Mortgage and Housing Corporation.

C17.	Shaw, S.Y., R.J. Magee and J. Rousseau. 1991. “Overall and Component Airtightness Values of a Five-Story Apartment Building,” ASHRAE Transactions, Vol. 97, Part 2, 347-353.

C18.	Shaw, C.Y. 1980. “Methods for Conducting Small-Scale Pressurization Tests and Air Leakage Data of MultiStorey Apartment Buildings.” ASHRAE Transactions 86(1): 241-250.

C19.	Shaw, C.Y., S. Gasparetto and J.T. Reardon. 1990. “Methods for Measuring Air Leakage in High-Rise Apartments,” Air Change Rate and Airtightness in Buildings, M.H. Sherman Ed., ASTM STP 1067, American Society for Testing and Materials, Philadelphia, 222-230.