MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A17243 | In-Flight Anomaly Number -- | Contractor Report Number P-083 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title PROPULSION |
| EICN# -- | ELEMENT ET | Contractor LMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LH2 RECIRCULATION LI | PART# 11009-509 | SER/LOT# ET-97 | MANUFACTURER LMMSS |
| Test/Operation A - ATP | Prevailing Condtion P - PRESSURE | F / U -- | Fail Mode MV - EXT LEAK | Cause MA - MFG-ASY |
| System PROPULSION | Defect -- | Material -- | Work Contact B. MATTHEESS | Fail Date 02/19/1998 |
| Received at MSFC 02/20/1998 | Date Isolated 02/19/1998 | FMEA Reference 2.6.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom MV - EXT LEAK | Time Cycle -- |
| Effectivity Text ET97 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 06/08/1998 | Contractor Req Defer Until Date 02/11/1998 | LVL 3 Close -- | Remark / Action 03/11/1998 |
| Investigation / Resolution Summary |
| Last MSFC Update 03/31/1998 | CN RSLV SBMT 03/17/1998 | Defer Date 03/03/1998 | Add Date 02/20/1998 | R/C Codes -- -- -- |
| Assignee |
| Design J. SANFORD | Chief Engineer M. G. HARSH | S & MA M. SMILES | Project -- | Project MGR P. COUNTS |
| Approval |
| Design J. SANFORD | Chief Engineer M. G. HARSH | S & MA J. GREEN | Project -- | Project MGR P. COUNTS |
| PAC Assignee R. TUCKER | PAC Review Complete -- | MSFC Closure Date 03/30/1998 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID N031678 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE LH2 RECIRCULATION LINE TO UMBILICAL JOINT WAS LEAKING AT A RATE OF 52.0 SCCM DURING THE PERFORMANCE OF THE LEAKAGE TEST TP-8C101-FA. THIS EXCEEDS THE ALLOWABLE LEAKAGE RATE OF 10 SCCM CRITICALITY: THIS IS A CRITICALITY 1 FAILURE AS DESIGNATED BY PARAGRAPH 2.6.1.1 IN THE FMEA DOCUMENT (MMC-ET-RAO4a-K) * REV. A (DATED 3/11/98) REVISES TASKS I, II AND IV, DETERMINED CAUSE AND CORRECTIVE ACTIONS AND CLOSED CAPS |
| Contractor Investigation/Resolution GENERAL: DURING THE SEAL CAVITY LEAK TEST PROCEDURE TP-8C101-FA ON THE JOINT BETWEEN THE LH2 RECIRCULATION LINE AND THE UMBILICAL, A 52.0 SCCM HELIUM LEAK WAS DETECTED (6.0 +/- .5 PSIG APPLIED PRESSURE). THIS EXCEEDS THE ALLOWABLE LEAKAGE RATE OF 10 SCCM THE FOLLOWING STEPS WERE IMPLEMENTED IN ORDER TO DETERMINE THE CAUSE OF THE LEAK AT THE JOINT OF THE LH2 RECIRCULATION LINE TO UMBILICAL INSTALLATION: A. THE HARDWARE AT THE LH2 RECIRCULATION LINE TO ET JOINT WAS LOOSENED IN ORDER TO RELIEVE TENSION AND VERIFY THAT THE TORQUE ON THE HARDWARE THAT SECURES THE LH2 RECIRCULATION LINE TO THE UMBILICAL MEETS ENGINEERING DRAWING REQUIREMENT OF 90 TO 100 IN-LB. THE TORQUE VERIFICATION TEST MET THE ENGINEERING DRAWING REQUIREMENTS, AND A 52.0 SCCM LEAK WAS STILL DETECTED B. THE LH2 RECIRCULATION LINE TO UMBILICAL JOINT WAS DISMANTLED IN ORDER TO PERFORM A VISUAL INSPECTION OF THE FLANGE AND SEAL TASK I. FAILURE/PROBLEM INVESTIGATION A. GENERATE FAILURE ANALYSIS PLAN AND EVALUATE SEAL AND SEALING SURFACES FOR CONFORMANCE TO ENGINEERING REQUIREMENTS, AND CAUSE OF FAILURE RESPONSIBILITY: W. MATTHEESSEN - 3741/D. WESTPHAL - 3740 R. MEYER - 4640/E. HORAK - 4600 ECD: 3/8/98 * CLOSURE STATEMENT: UPON REMOVAL OF THE LH2 RECIRCULATION LINE TO UMBILICAL JOINT, THE JOINT WAS EXAMINED FOR IMPERFECTIONS OR DAMAGE. ON THE UMBILICAL SIDE OF THE JOINT NO DEFECTS WERE FOUND. ON THE LINE SIDE, A PIECE OF WHITE MATERIAL WAS VISIBLE OVER BOTH THE PRIMARY AND SECONDARY SEALING SURFACES. THIS MATERIAL WAS REMOVED FOR EVALUATION. IT WAS DETERMINED THAT THE MATERIAL IS PART OF A QUALITY CONTROL INSPECTION/NON-TAMPER SEAL ("EGG SHELL") REFERENCE LAB REPORT 98O011 THE ME261-0045-0006 (NAFLEX SEAL) WAS VISUALLY INSPECTED, AND TWO AREAS OF IMPERFECTIONS WERE NOTED. A 5X INSPECTION SHOWED THREE AREAS OF CONCERN ON THE PRIMARY SEALING SURFACE. AT HIGHER MAGNIFICATION (16X TO 60X) TWO AREAS WERE DEFINITELY IDENTIFIED AS MANUFACTURING DEFECTS. THE THIRD AREA IS A POSSIBLE MANUFACTURING DEFECT, BUT THIS CANNOT BE CONCLUSIVELY DETERMINED. THE PRIMARY SEAL NONCONFORMANCES WERE REPORTED TO BOEING NORTH AMERICAN (BNA) BY THE PROJECT PLANNING ET GFP COORDINATOR. BNA REQUESTED NO FURTHER EVALUATION BE PERFORMED AND THAT THE SEAL BE RETURNED TO BNA CONSIDERING THE ABOVE INFORMATION, IT CANNOT BE DETERMINED IF EITHER ONE OF THE DEFECTS NOTED ABOVE COULD HAVE, BY ITSELF, CAUSED AN UNACCEPTABLE LEAK RATE. TOGETHER BOTH DEFECTS DID CAUSE AN UNACCEPTABLE CONDITION AFTER CLEANING, THE LINE WAS INSTALLED WITH A NEW SEAL AND PASSED ACCEPTANCE TESTING * B. REVIEW THE INSTALLATION PROCESS TO DETERMINE THE TRANSFER MECHANISM OF THE NON-TAMPER SEALS TO THE SEALING SURFACE RESPONSIBILITY: W. MATTHEESSEN - 3741/D. WESTPAHL - 3740 ECD: 3/8/1998 COMPLETE: 2/23/1998 CLOSURE STATEMENT THE INVESTIGATION DEMONSTRATED THAT DURING REMOVAL OF THE NON-TAMPER SEAL FROM A CLEAN PART, IT CAN BECOME ATTACHED TO THE CLEAN WHITE NYLON GLOVES USED IN THIS OPERATION. THE WHITE SEAL ON THE WHITE GLOVE CAN BE DIFFICULT TO DETECT. THIS HYPOTHESIS WAS CONFIRMED THROUGH DISCUSSIONS WITH THE PRACTITIONERS INVOLVED IN THE OPERATION. ADDITIONAL EVALUATION SHOWED THE NON-TAMPER SEAL WOULD NOT COME OFF A GLOVE EXCEPT FOR TRANSFERRING TO ANOTHER SURFACE. THE ONLY AVAILABLE SURFACES ARE THE FLANGE EXTERIOR, FLANGE SEALING SURFACES, AND THE SEAL. THE FIRST CASE IS EXTERIOR TO SERVICE MEDIA, AND OF NO CONCERN. THE SECOND AND THIRD CASES WOULD EITHER BE EXTERIOR TO THE SERVICE MEDIA OR CAUSE A LEAK WHICH WOULD BE DETECTED * C. EVALUATE AND PURCHASE NEW HIGHER CONTRAST, AGAINST WHITE CLEAN ROOM GLOVES, QUALITY CONTROL SEALS RESPONSIBILITY: D. OWENS - 3760 ECD: 4/8/1998 COMPLETE: 3/5/1998 CLOSURE STATEMENT: NEW INSPECTION SEALS HAVE BEEN ORDERED IN COLORS THAT ARE IN SHARP CONTRAST WITH THE WHITE GLOVES (REF.: RDS#: 78987) * D. INFORM ALL RESPONSIBLE PRACTITIONERS OF THE IMPORTANCE THAT ALL HARDWARE, TOOLS, AND PROTECTIVE GARMENTS ARE FREE OF CONTAMINATION RESPONSIBILITY: J. STANLEY - 3630 ECD: 4/8/1998 COMPLETE: 3/5/1998 CLOSURE STATEMENT: PRACTITIONERS HAVE BEEN INSTRUCTED VIA CREW MEETINGS TO ASSURE THAT HARDWARE, TOOLS, AND PROTECTIVE GARMENTS ARE FREE OF CONTAMINATION. (REF.: ccMAIL FROM M. HOLCOMB DATED 3/5/98) CAUSE: * 1. MANUFACTURING DEFECT ON GFP NAFLEX SEAL * 2. CONTAMINATED SEALING SURFACE ON LH2 RECIRCULATION LINE TASK II. CORRECTIVE ACTION * A. GFP NAFLEX SEAL NONE, GFP HARDWARE. GFP SEAL RETURNED TO BOEING NORTH AMERICAN FOR INVESTIGATION PER CONTRACTS DIRECTION. THIS WILL BE TRACKED BY STANDARD MSFC TRACKING SYSTEM FOR GFP PROBLEMS * B. CONTAMINATION ON LH2 RECIRCULATION LINE FLANGE 1. NEW INSPECTION SEALS HAVE BEEN ORDERED IN COLORS THAT ARE IN SHARP CONTRAST WITH THE WHITE GLOVES 2. PRACTITIONERS HAVE BEEN INSTRUCTED VIA CREW MEETINGS TO ASSURE THAT HARDWARE, TOOLS, AND PROTECTIVE GARMENTS ARE FREE OF CONTAMINATION TASK III. CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. THE PURPOSE OF LEAK TESTING IS TO FILTER OUT SUCH DISCREPANCIES. ALL INSTALLED JOINTS PASSED TM04 REQUIRED LEAK TEST TASK IV. CAPS CLOSURE SUMMARY * DURING THE STANDARD SEAL CAVITY LEAK TEST PROCEDURE TP-8C101-FA ON THE JOINT BETWEEN THE LH2 RECIRCULATION LINE AND THE UMBILICAL, A 52.0 SCCM HELIUM LEAK WAS DETECTED (6.0 +/- .5 PSIG APPLIED PRESSURE). THIS EXCEEDS THE ALLOWABLE LEAKAGE RATE OF 10 SCCM AFTER INVESTIGATION IT WAS DETERMINED THAT THERE WERE TWO POSSIBLE CAUSES THAT COULD HAVE BOTH CONTRIBUTED TO THE LEAKAGE: 1. Q.C. INSPECTION SEAL FOUND ON THE PRIMARY AND SECONDARY SEALING SURFACES OF THE LH2 RECIRCULATION LINE FLANGE 2. SEVERAL MANUFACTURING DEFECTS WERE FOUND ON THE GFP SEAL PRIMARY SEALING SURFACE THE GFP SEAL HAS BEEN RETURNED TO BOEING NORTH AMERICAN FOR INVESTIGATION PER CONTRACTS DIRECTION. THE PRACTITIONERS HAVE BEEN INFORMED VIA CREW MEETINGS OF THE NEED TO ASSURE THAT HARDWARE, TOOLS, AND PROTECTIVE GARMENTS ARE FREE OF CONTAMINATION. IN ADDITION, NEW INSPECTION SEALS HAVE BEEN ORDERED IN COLORS THAT ARE IN SHARP CONTRAST TO THE WHITE CLEAN GLOVES THIS CAPS IS CLOSED. NO FURTHER ACTION REQUIRED |
| MSFC Response/Concurrence 03/03/98 - MSFC APPROVES CLOSED WITH ACTION STATUS. THIS STATUS IS EFFECTIVE THROUGH 06/08/98 |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A17243 | IFA# -- | Contractor RPT# P-083 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80921011009-509 | Asmnt Part Name LH2 RECIRCULATION LN | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MA - MFG-ASY | FAIL MODE MV - EXT LEAK |
| Asmnt FMEA 2.6.1.1 | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |