NWCG FIRELINE HANDBOOK

APPENDIX B

FIRE BEHAVIOR

OCTOBER, 1993

NFES 2165

Additional copies of this publication may be ordered from:

National Interagency Fire Center

ATTN:  Supply

3833 S. Development Avenue

Boise, Idaho 83705

Order NFES #2165

CONTENTS

PURPOSE	4

FIRE BEHAVIOR WORKSHEETS	5

INPUT 0–Projection Point	10

INPUT 1–Selecting a Fuel Model	10

Fire Behavior Fuel Model Key	12

Fire Behavior Fuel Model Descriptions	16

Grass Group	16

Shrub Group	17

Timber Litter Group	18

Logging Slash Group	19

TABLE 1–Description of Fuel Models	21

INPUT 2–Fine Dead Fuel Moisture (1-H FDFM)	22

TABLE 2–Reference Fuel Moisture, Day (0800-1959)	25

TABLE 3–Dead Fuel Moisture Content Corrections,

Day (0800-1959) May, June, July	26

TABLE 4–Dead Fuel Moisture Content Corrections,

Day (0800-1759) February, March, April, August,

September, October	27

TABLE 5–Fine Dead Fuel Moisture Content Corrections,

Day (0800-1759) November, December, January	28

INPUT 3–Live Fuel Moisture (LFM) Fuel Models

2, 4, 5, 7 and 10	29

TABLE 6–Live Fuel (Foliage) Moisture Content %	29

INPUT 4–Midflame Windspeed (MFWS)	30

DIAGRAM 1 – 20-Foot Windspeed Adjusted to

Midflame Windspeed Based on Overstory	32

TABLE 7–Wind Adjustment Table	33

TABLE 8–Modified Beaufort Scale for Estimating

20-Foot Windspeed	34

INPUT 5–Slope (SLP)	35

Slope Determination Process	35

TABLE 9–Map Scale Conversion Factors	36

INPUT 6–Effective Windspeed (EWS)	37

CONTENTS (Continued)

FIRE BEHAVIOR OUTPUTS

OUTPUT 1–Rate of Spread	38

OUTPUT 2–Heat Per Unit Area	38

OUTPUT 3–Fireline Intensity	38

OUTPUT 4–Flame Length	38

OUTPUT 5–Spread Distance	38

OUTPUT 6/7–Projected Fire Perimeter and Area	40

TABLE 10–Perimeter Estimations for Point Source Fires	41

TABLE 11–Area Estimations for Point Source Fires	44

DIAGRAM 2–Approximate Fire Shapes for Various

Effective Windspeeds	47

OUTPUT 8–Maximum Spotting Distance	48

NOMOGRAM 1–Flame Height	50

NOMOGRAM 2–Flame Duration	51

NOMOGRAM 3–Ratio of Lofted Firebrand Height to

Flame Height	52

NOMOGRAM 4–Maximum Spotting Distance	53

OUTPUT 9–Probability of Ignition	54

TABLE 12–Probability of Ignition Table	55

INTERPRETATION OF FIRE BEHAVIOR INFORMATION

TABLE 13–Fire Severity Related to Fuel Moisture Chart	56

DIAGRAM 3–Fire Behavior Characteristics Chart

(Light Fuel)	57

DIAGRAM 4–Fire Behavior Characteristics Chart

(Heavy Fuel)	58

TABLE 14–Fire Suppression Interpretations	59

SAFETY AND FIRE BEHAVIOR	61

Look Up/Look Down/Look Around	62

TABLES 15 through 78–Rate of Spread and Flame

Length Tables by Fuel Type and Percent Slope	64

PURPOSE

The purpose of this appendix is to provide some basic fire behavior information that will enable a person with a moderate level of fire behavior training (S-390) to predict and calculate some basic elements of fire behavior and fire size.

Information in this appendix will provide the qualified user with the means to:

•	Predict rate of spread (ROS) and flame length (FL) for each Fire Behavior Fuel Model based on the 1-hour timelag dead fuel moisture, live fuel moisture for Fuel Models 2, 4, 5, 7 and 10, midflame windspeed and percent slope.

•	Estimate the area and perimeter of a fire, given inputs of spread distance (rate of spread x time) and midflame windspeed.

•	Predict maximum spotting distance and probability of ignition.

•	Provide worksheets for fire behavior prediction.

The Fire Behavior Worksheet is on page B-5.  Other worksheets that help track fire behavior input and output date (Fine Dead Fuel Moisture/Probability of Ignition, Wind Adjustment, Slope, Map-Spread, Size, Spotting, and Map-Spot) are provided on pages B-6 through B-9.  Pages B-10 through B-37 go over the six required input items on the Fire Behavior Worksheet and B-38 through B-55 cover the output items.

FIRE BEHAVIOR WORKSHEET

NAME OF FIRE ___________FIRE PRED SPEC_____________

DATE____________________ TIME_______________________

PROJ PERIOD DATE_______PROJ TIME FROM _____TO____

INPUT

0	PP	PROJECTION POINT	___	___	___

1	MODEL#	FUEL MODEL NUMB (1-13)	___	___	___

2	1H-FDFM	FINE DEAD FUEL MOIST, %	___	___	___

3	LFM	LIVE FUEL MOISTURE, %	___	___	___

4	MFWS	MIDFLAME WINDSPD, mi/h	___	___	___

5	SLP	SLOPE, %	___	___	___

6	EWS	EFFECTIVE WNDSPD, mi/h	___	___	___

OUTPUT

1	ROS	RATE OF SPREAD, ch/h	___	___	___

2	HA	HEAT PER UNIT AREA,	___	___	___		Btu/sq ft

3	FLI	FIRELINE INTENSITY,	___	___	___		Btu/ft/s

4	FL	FLAME LENGTH, ft	___	___	___

5	SD	SPREAD DISTANCE, ch	___	___	___		MAP SPREAD DIST, in

6	PER	PERIMETER, ch	___	___	___

7	AC	AREA, ac	___	___	___

8	SPOT	MAX SPOTTING DIST, mi	___	___	___		MAP DIST SPOT, in	___	___	___

9	PIG	PROB OF IGNITION, %	___	___	___

FINE DEAD FUEL MOISTURE/PROBABILITY OF IGNITION WORKSHEET

INPUT

0	PP	PROJECTION POINT	____	____	____

1	D	DAY TIME CALCULATION	   D  	   D  	   D

2	DB	DRY BULB TEMP. °F	____	____	____

3	WB	WET BULB TEMP. °F	____	____	____

4	DP	DEW POINT, °F	____	____	____

5	RH	RELATIVE HUMIDITY, %	____	____	____

6	RFM	REFERENCE FUEL	____	____	____		MOIST, % (TABLE 2)

7	MO	MONTH	____	____	____

8	SH	UNSHADED (U)	U/S	U/S	U/S		SHADED (S)

9	T	TIME	____	____	____

10	CH	ELEVATION CHANGE	B/L/A	B/L/A	B/L/A

B=1000′ to 2000′ below site

L=+1000′ of site location

A=1000′ to 2000′ above site

11	ASP	ASPECT, (N, E, S, W)	____	____	____

12	SLP	SLOPE, %	____	____	____

13	FMC	FUEL MOIST CORRECT, %	____	____	____		(TABLE 3, 4, OR 5)

OUTPUT

1    1H-	FINE DEAD FUEL MOIST, %	____	____	____	  FDFM	(line 6 + line 13)

2    PIG	PROB OF IGNITION, %	____	____	____		(TABLE 12)

WIND ADJUSTMENT WORKSHEET

INPUT

0	PP	PROJECTION POINT	____	____	____

1	20′ W	20-FT WINDSPEED, mi/h	____	____	____

2	MODEL #	FUEL MODEL # (1-13)	____	____	____

3	SHLTR	WIND SHELTERING	____	____	____

1=Unsheltered

2=Partially Sheltered

3=Fully Sheltered, Open

4=Fully Sheltered, Closed

4	WAF	WIND ADJUST FACTOR	____	____	____		(TABLE 7)

OUTPUT

1	MFWS	MIDFLAME WNDSPD, mi/h	____	____	____		(line 1 x line 4)

SLOPE WORKSHEET

INPUT

0	PP	PROJECTION POINT	____	____	____

1	CON INT	CONTOUR INTERVAL	____	____	____

2	SLC	MAP SCALE	____	____	____

3	CF	CONVERSION FACTOR,	____	____	____		ft/in

4	# INTVLS	# CONTOUR INTERVALS	____	____	____

5	RISE	RISE IN ELEVATION	____	____	____

6	MD	MAP DISTANCE, in	____	____	____		(Between Points)

7	HZGD	HORIZ GROUND DIST, ft	____	____	____

OUTPUT

1	SLP %	SLOPE, %	____	____	____

MAP-SPREAD WORKSHEET

INPUT

0	PP	PROJECTION POINT	____	____	____

1	ROS	RATE OF SPREAD, ch/h	____	____	____

2	PT	PROJECTION TIME, hr	____	____	____

3	SDCH	SPREAD DISTANCE, ch	____	____	____		(line 1 x line 2)

4	SDFT	SPREAD DISTANCE, ft	____	____	____		(line 3 x 66 ft/ch)

5	SCL	MAP SCALE	____	____	____

6	CF	CONVERSION FACTOR,	____	____	____		ft/in (See Map Scale Conversion)

OUTPUT

1	MD	MAP SPREAD DIST, in	____	____	____		(line 4 divided by line 6)

SIZE WORKSHEET

INPUT

0	PP	PROJECTION POINT	____	____	____

1	ROS	RATE OF SPREAD, ch/h	____	____	____

2	EWS	EFFECTIVE WINDSPD, mi/h	____	____	____

3	PT	PROJECTION TIME, hr	____	____	____

4	SD	SPREAD DISTANCE, ch	____	____	____		(line 1 x line 3 = line 4)

OUTPUT

1	PER	PERIMETER, ch	____	____	____

2	AC	AREA, ac	____	____	____

SPOTTING WORKSHEET

MAP-SPOT WORKSHEET

INPUT

0	PP	PROJECTION POINT	____	____	____

1	SPOTMI	SPOTTING DISTANCE, mi	____	____	____

2	SPOTFT	SPOTTING DISTANCE, ft	____	____	____		(line 1 x 5,280 ft)

3	SCL	MAP SCALE	____	____	____

4	CF	CONVERSION FACTOR,	____	____	____		ft/in

OUTPUT

1	SPOT	MAP DISTANCE SPOT, in	____	____	____		(line 2 divided by line 4)

COMPLETING THE FIRE BEHAVIOR WORKSHEET

INPUT 0:	Projection Point (PP)

Assign a number or letter to designate the projection point location and enter as Input 0 on the Fire Behavior Worksheet on page B-5.

INPUT 1:	Fuel Model (Model #)

•	Using the guidelines below, proceed through the fuel model key and descriptions which follow and select a fuel model and enter as Input 1 on the Fire Behavior Worksheet on page B-5.

•	Determine the primary carrier of fire.

•	Determine which stratum of the surface fuels is most likely to carry the spreading fire (grass, needle litter, leaves, logging slash, etc.).

•	Determine the appropriate fuel group/general vegetation type; i.e., Grass (Models 1-3), Shrub (Models 4-7), Timber Litter (Models 8-10), or Logging Slash (Models 11-13).

•	Using the fuel model key, determine the appropriate fuel model.

•	Go to the fuel model description and determine if it fits.

•	If yes, use it and enter into Input 1 on the Fire Behavior Worksheet.

•	If no, find another that more closely fits your situation.

•	The fuel models used here are those used by Albini (1976)¹ to develop the nomograms published in his paper Estimating Wildfire Behavior and Effects.  There are 13 models which are called the Fire Behavior Fuel Models.

¹Albini Frank A.; Estimating Wildfire Behavior and Effects.  Gen. Tech. Report INT-30; 1976.

They are tuned to the fine fuels that carry the fire and thus describe the conditions at the head of the fire or the flaming front.  These models are designed to give predictions for fire spread at a steady rate.  It is important to recognize that rate of spread (ROS) and flame length (FL) predictions are estimates and the actual ROS and FL may vary considerably from the predicted.

•	Assessment of fire behavior is simpler if a single fuel model is used to describe the fuels in the area.  In fact, as experience is gained by observation of fires and estimating their behavior, it is possible to pick the fuel model not only by its description of physical vegetation, but also by its known fire behavior characteristics.

Examples:  The fire may be in timbered area, but the timber is relatively open and dead grass, not needle litter, is the stratum carrying the fire.  In this case, Fuel Model 2, which is not listed as a timber model, should be considered, or

In the same area if the grass is sparse and there is no wind or slope, the needle litter would be the stratum carrying the fire and Fuel Model 9 would be the better choice.

•	Determine the general depth and compactness of the fuel.  This information will be needed when using the fuel model key.  There are very important considerations when matching fuels, particularly in the grass and timber types.

•	Determine which fuel models are present and what their influence on fire behavior is expected to be.

Example:  Green fuel may be present, but will it play a significant role in fire behavior?  Large fuels may be present, but are they sound, or decaying and breaking up?  Do they have limbs and twigs attached or are they bare cylinders?  Look for the fine fuels and choose a model that represents their depth, compactness, and to some extent, the amount of live fuel and its contribution to fire.  Do not be restricted by the model name or the original intended application.

FIRE BEHAVIOR FUEL MODEL KEY¹

I.	PRIMARY CARRIER OF THE FIRE IS GRASS.  Expected rate of spread is moderate to high, with low to moderate fireline intensity (flame length).

A.	Grass is fine structured, generally below knee level, and cured or primarily dead.  Grass is essentially continuous.  SEE THE DESCRIPTION OF MODEL 1.

B.	Grass is coarse structured, above knee level (averaging about 3 ft.) and is difficult to walk through.  SEE THE DESCRIPTION OF MODEL 3.

C.	Grass is usually under an open timber or brush overstory.  Litter from the overstory is involved, but grass carries the fire.  Expected spread rate is slower than Fuel Model 1 and intensity is less than Fuel Model 3.  SEE THE DESCRIPTION OF MODEL 2.

¹ Richard C. Rothermel; How to Predict the Spread and Intensity of Forest and Range Fires.  Gen. Tech Report INT-143; June 1983 (NFES 1574).

II.	PRIMARY CARRIER OF THE FIRE IS SHRUB or LITTER BENEATH SHRUB.   Expected rates of spread and fireline intensities (flame length) are moderate to high.

A.	Vegetative type is southern rough or low pocosin.  Shrub is generally 2 to 4 ft. high.  SEE THE DESCRIPTION OF MODEL 7.

B.	Live fuels are absent or sparse.  Brush averages 2 to 4 ft. in height.  Brush requires moderate winds to carry fire.  SEE THE DESCRIPTION OF MODEL 6.

C.	Live fuel moisture can have a significant effect on fire behavior.

1.	Shrub is about 2 ft. high, with light loading of brush litter underneath.  Litter may carry the fire, especially at low windspeeds.  SEE THE DESCRIPTION OF MODEL 5.

2.	Shrub is head-high (6 ft.), with heavy loadings of dead (woody) fuel.  Very intense fire with high spread rates expected.  SEE THE DESCRIPTION OF MODEL 4.

3.	Vegetative type is high pocosin.  SEE THE DESCRIPTION OF MODEL 4.

III.	PRIMARY CARRIER OF THE FIRE IS LITTER BENEATH A TIMBER STAND.  Spread rates are low to moderate, fireline intensity (flame length) may be low to high.

A.	Surface fuels are mostly foliage litter.  Large fuels are scattered and lie on the foliage litter, that is, large fuels are not supported above the litter by their branches.  Green fuels are scattered enough to be insignificant to fire behavior.

1. 	Dead foliage is tightly compacted, short needle (2 inches or less) conifer litter or hardwood litter.  SEE THE DESCRIPTION OF MODEL 8.

2.	Dead foliage litter is loosely compacted long needle pine or hardwoods.  SEE THE DESCRIPTION OF MODEL 9.

B.	There is a significant amount of larger fuels with attached branches and twigs, or it has rotted enough that it is splintered and broken.  The larger fuels are fairly well distributed over the area.  Some green fuel may be present.  Overall depth of the fuel is primarily below the knees, but some fuel may be higher.  SEE THE DESCRIPTION OF MODEL 10.

IV.	PRIMARY CARRIER OF THE FIRE IS LOGGING SLASH.  Spread rates are low to high, fireline intensities (flame lengths) are low to very high.

A.	Slash is aged and overgrown.

1.	Slash is from hardwood trees.  Leaves have fallen and cured.  Considerable vegetation (tall weeds) has grown in amid the slash and has cured or dried out.  SEE THE DESCRIPTION OF MODEL 6.

2.	Slash is from conifers.  Needles have fallen and considerable vegetation (tall weeds and some shrubs) has overgrown the slash.  SEE THE DESCRIPTIONOF MODEL 10.

B.	Slash is fresh (0-3 years) and not overly compacted.

1.	Slash is not continuous.  Needle litter or small amounts of grass or shrubs must be present to help carry the fire, but primary carrier is still slash.  Live fuels are absent or do not play a significant role in fire behavior.  The slash depth is about 1 ft.  SEE THE DESCRIPTION OF MODEL 11.

2.	Slash generally covers the ground (heavier loadings than Model 11), though there may be some bare spots or areas of light coverage.  Average slash depth is about 2 ft.  Slash is not excessively compacted.  Approximately one-half of the needles may still be on the branches but are not red.  Live fuels are absent, or are not expected to affect fire behavior.  SEE THE DESCRIPTION OF MODEL 12.

3.	Slash is continuous or nearly so (heavier loadings than Model 12).  Slash is not compacted and has an average depth of 3 ft.  Approximately one-half of the needles are still on the branches and are red, OR all the needles are on the branches but they are green.  Live fuels are not expected to influence fire behavior.  SEE THE DESCRIPTION OF MODEL 13.

4.	Same as 3, EXCEPT all the needles are attached and are red.  SEE THE DESCRIPTION OF MODEL 4.

FIRE BEHAVIOR FUEL MODEL DESCRIPTIONS²

•	Grass Group

Fuel Model 1 (1 foot deep) Fire spread is governed by the fine herbaceous fuels that have cured or are nearly cured.  Fires are surface fires that move rapidly through cured grass and associated material.  Very little shrub or timber is present, generally less than one-third of the area.

Grasslands and savanna are represented along with stubble, grass-tundra, and grass-shrub combinations that meet the above area constraint.   Annual and perennial grasses are included in this fuel model.

Fuel Model 2 (1 foot deep) Fire spread is primarily through the fine herbaceous fuels, either curing or dead.  These are surface fires where the herbaceous material, besides litter and dead-down stemwood from the open shrub or timer overstory, contribute to the fire intensity.  Open shrub lands and pine stands or scrub oak stands that cover 1/3 to 2/3 of the area may generally fit this model but may include clumps of fuels that generate higher intensities and may produce firebrands.  Some pinyon-juniper may be in this model.

Fuel Model 3 (2.5 feet deep) Fires in this fuel are the most intense of the grass group and display high rates of spread under the influence of wind.  The fire may be driven into the upper heights of the grass stand by the wind and cross over standing water.  Stands are tall, averaging about 3 feet, but considerable variation may occur.  Approximately one-third or more of the stand is considered dead or cured and maintains the fire.

² Anderson, Hal E.; Aids to Determining Fuel Models for Estimating Fire Behavior.  Gen. Tech Report INT-122, 1982.

•	Shrub Group

Fuel Model 4 (6 feet deep) Fire intensity and fast spreading fires involve the foliage and live and dead fine woody materials in the crowns of a nearly continuous secondary overstory.  Examples are stands of mature shrub, 6 or more feet tall, such as California mixed chaparral, the high pocosins along the east coast, the pine barrens of New Jersey or the closed jack pine stands of the north-central states.  Besides flammable foliage, there is dead woody material in the stand that significantly contributes to the fire intensity.  Height of stands qualifying for this model vary with local conditions.  There may be also a deep litter layer that confounds suppression efforts.

Fuel Model 5 (2 feet deep) Fire is generally carried in the surface fuels made up of litter cast by the shrubs and the grasses or forbs in the understory.  Fires are generally not very intense as surface fuel loads are light, the shrubs are young with little dead material, and the foliage contains little volatile material.  Shrubs are generally not tall, but nearly cover the entire area.  Young, green stands with little or no deadwood such as laurel, vine maple, alder, or even chaparral, manzanita, or chamise are examples.  As the shrub fuel moisture drops, consider using a Fuel Model 6.

Fuel Model 6 (2.5 feet deep) Fires carry through the shrub layer where the foliage is more flammable than Fuel Model 5, but require moderate winds (>8 mi/h) at midflame height.  Fire will drop to the ground at low windspeeds or openings in the stand.  Shrubs are older, but not as tall as shrub types of Model 4, nor do they contain as much fuel as Model 4.  A broad range of shrub conditions is covered by this model.  Typical examples include intermediate stands of chamise, chaparral, oak brush, low pocosins, Alaskan spruce taiga, and shrub tundra.  Cured hardwood slash can be considered. Pinyon-juniper shrublands may fit, but may overpredict rate of spread except at high winds (20 mi/h at the 20-foot level).

Fuel Model 7 (2.5 feet deep) Fire burns through the surface and shrub strata equally.  Fire can occur at higher dead fuel moisture contents due to the flammable nature of live foliage.  Shrubs are generally 2 to 6 feet high.  Examples are Palmetto-gallberry understory-pine overstory sites, low pocosins, and Alaska Black Spruce-shrub combinations.

•	Timber Litter Group

Fuel Model 8 (0.2 foot deep) Slow burning ground fires with low flame heights are generally the case, although an occasional “jackpot” or heavy fuel concentration may cause a flare up.  Only under severe weather conditions do these fuels pose fire problems.  Closed-canopy stands of short needle conifers or hardwoods that have leafed out support fire in the compact litter layer.  This layer is mainly needles, leaves, and some twigs since little undergrowth is present in the stand.  Representative conifer types are white pine, lodgepole pine, spruce, true fires, and larches.

Fuel Model 9 (0.2 foot deep) Fires run through the surface litter faster than model 8 and have higher flame height.  Both long-needle conifer and hardwood stands, especially the oak-hickory types, are typical.  Fall fires in hardwoods are representative, but high winds will actually cause higher rates of spread than predicted because of spotting caused by rolling blowing leaves.  Closed stands of long-needled pine like ponderosa, Jeffrey, and red pines or southern pine plantations are grouped in this model.  Concentrations of dead-down woody material will contribute to possible torching out of trees, spotting, and crowning activity.

Fuel Model 10 (1 foot deep) The fires burn in the surface and ground fuels with greater fire intensity than other timber litter models.  Dead-down fuels include greater quantities of 3-inch or larger limb wood resulting from over-maturity or natural events that create a large load of dead material on the forest floor.  Crowing out, spotting, and torching of individual trees are more frequent in this fuel situation leading to potential fire control difficulties.  Any forest type may be considered when heavy down materials are present; examples are insect or diseased stands, wind-thrown stands, over-mature situations with deadfall, and cured light thinning or partial-cut slash.

•	Logging Slash Group

Fuel Model 11¹ (1 foot deep) Fires are fairly active in the slash and herbaceous material intermixed with the slash.  The spacing of the rather light fuel load, shading from overstory, or the aging of the fine fuels can contribute to limiting the fire potential.  Light partial cuts or thinning operations in mixed conifer stands, hardwood stands, and southern pine harvests are considered.  Clear-cut operations generally produce more slash than represented here.  The <3 inch material load is less than 12 tons per acre.  The >3 inch material is represented by not more than 10 pieces, 4 inches in diameter along a 50-foot transect.

Fuel Model 12¹ (2.3 feet deep) Rapidly spreading fires with high intensities capable of generating firebrands can occur.  When fire starts, it is generally sustained until a fuel break or change in fuels is encountered.  The visual impression is dominated by slash and much of it is <3 inches in diameter.  These fuels total less than 35 tons per acre and seem well distributed.  Heavily thinned conifer stands, clear-cuts and medium or heavy partial cuts are represented.  The >3 inch material is represented by encountering 11 pieces, 6 inches in diameter, along a 50-foot transect.

¹ When working in Fuel Model 11 or 12 with significant “red” needles attached to limbs, consider using the next heavier model.  For example:  Fuel Model 11 with “red” needles, use Fuel Model 12.

Fuel Model 13² (3 feet deep) Fire is generally carried by a continuous layer of slash.  Large quantities of >3 inch material are present.  Fires spread quickly through the fine fuels and intensity builds up as the large fuels start burning.  Active flaming is sustained for long periods and a wide variety of firebrands can be generated.  These contribute to spotting problems as the weather conditions become more severe.  Clear-cut and heavy partial-cuts in mature and over-mature stands are depicted where the slash load is dominated by the >3 inch material.  The total load may exceed 300 tons per acre, but the <3 inch fuel is generally only 10 percent of the total load.  Situations where the slash still has “red” needles attached, but the total load is lighter like a Model 12, can be represented because of the earlier high intensity and faster rate of spread.

² If “red” needles are attached consider using a Fuel Model 4.

| Fuel Model | Typical Fuel Complex | Fuel Loading (T/A) 1-H 10-H 100-H Live | Fuel Bed Depth (ft) | Moist. of Extinction Dead Fuels (%) | ROS* ch/h | FL* (ft) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Short Grass | 0.74 | 0.00 | 0.00 | 0.00 | 1.0 | 12 | 78 | 4 |
| 2 | Timber | 2.00 | 1.00 | .50 | .50 | 1.0 | 15 | 35 | 6 |
| 3 | Tall Grass | 3.01 | .00 | .00 | .00 | 2.5 | 25 | 104 | 12 |
| 4 | Chaparral | 5.01 | 4.01 | 2.00 | 5.01 | 6.0 | 20 | 75 | 19 |
| 5 | Brush | 1.00 | .50 | .00 | 2.00 | 2.0 | 20 | 18 | 4 |
| 6 | Dormant brush | 1.50 | 2.50 | 2.00 | .00 | 2.5 | 25 | 32 | 6 |
| 7 | Southern rough | 1.13 | 1.87 | 1.50 | .37 | 2.5 | 40 | 20 | 5 |
| 8 | Closed timber litter | 1.50 | 1.00 | 2.50 | 0.00 | 0.2 | 30 | 2 | 1 |
| 9 | Hardwood litter | 2.92 | .41 | .15 | .00 | 0.2 | 25 | 8 | 3 |
| 10 | Timber | 3.01 | 2.00 | 5.01 | 2.00 | 1.0 | 25 | 8 | 5 |
| 11 | Light logging slash | 1.50 | 4.51 | 5.51 | 0.00 | 1.0 | 15 | 6 | 4 |
| 12 | Medium logging slash | 4.01 | 14.03 | 16.53 | .00 | 2.3 | 20 | 13 | 8 |
| 13 | Heavy logging slash | 7.01 | 23.04 | 28.05 | .00 | 3.0 | 25 | 14 | 11 |
| *ROS and FL are represented under a fine dead fuel moisture of 8%, a midflame windspeed of 5 mi/h, and live fuel moisture, if present, of 100% (Anderson, 1982). |

INPUT 2:	Fine Dead Fuel Moisture (1-H FDFM), %

Fine Dead Fuel Moisture Content is an important input to fire behavior predictions.  Fuel moisture measurements are difficult to make in the field; however, estimates can be made from measured or predicted values of dry bulb temperature and relative humidity.

Due to solar radiation differences that exist between aspect, time of year, shading, and the adiabatic difference between position on the slope, it is necessary to calculate an estimate of fuel moisture.  This is necessary as the National Fire Danger Rating System (NFDRS) tables used here were developed for “worst case” conditions (summer, 1400, SW aspect, open conditions).  These predications are for fine, dead forest fuels.  Heavier fuels can be estimated by other means as needed.

Temperature and humidity are predicted for a specific site (projection point) in relation to a site (site location) where dry bulb temperatures and relative humidity are measured.  Since temperature and relative humidity change with elevation, it is necessary to estimate these changes between the projection point and the site location.  There are tables to correct for elevation changes of 0 to 2000 feet above or below the site location, but a new site location is needed if the elevation difference between the site location and the projection point exceeds 2000 feet.

Time corrections cannot be made.  Temperature and relative humidity must be obtained for the time in question.

The tables may be used to adjust the moisture of fuels in valley bottoms from conditions measured on the slopes above, but do not use weather data taken beneath a valley inversion and attempt to interpolate fuel moistures at drier sites upslope.  The corrections are too large and uncertain, and you may get meaningless results.

To use the Fine Dead Fuel Moisture/Probability of Ignition Worksheet on page B-6 complete the following input/output items.  Enter the fine dead fuel moisture as Output 1 on the Fine Dead Fuel Moisture/Probability of Ignition Worksheet and as Input 2 on the Fire Behavior Worksheet on page B-5.

INPUT

0	(Projection Point)―Record the number of the projection point for which a fire behavior prediction is to be made.

1	(Day Time Calculation)―Only day time calculations will be considered.

2	(Dry Bulb Temperature)―Dry bulb temperature is determined for the time period in question, either by measurement or forecast.  The site location may or may not be at the projection point.  Record temperature in degrees Fahrenheit.

3	(Wet Bulb Temperature)―Wet bulb temperature is determined for the time period in question, either by measurement or forecast.  The site location may or may not be at the projection point.  Record temperature in degrees Fahrenheit.

4	(Dew Point)―Record dew point for the time period in question.

5	(Relative Humidity)―Record relative humidity for the time period in question.

6	(Reference Fuel Moisture)―Go to Table 2 and determine the reference fuel moisture percent from the intersection of temperature and relative humidity (Inputs 2 and 5).  Record as a percent.

7	(Month)―Record the appropriate month.

8	(Unshaded or Shaded)―Circle “U” if fine dead fuels ahead of the projection point are unshaded (<50% shading) from solar radiation due to cloud cover and/or canopy cover.  Circle “S” if fine dead fuels ahead of the projection point are shaded (>50% shading) from solar radiation due to cloud and/or canopy cover.

9	(Time)―Record the expected time when the projection point will be used to estimate fire behavior.  The temperature/RH forecast or measurement must be the same time period as the projection time period.

10	(Elevation Change)―Record the elevation difference between the location of the projection point and the temperature/RH site location and circle:

“B” if the projection point is 1000 to 2000 feet below the site location.

“L” if the projection point is 0 to 1000 feet above or below the site location.

“A” if the projection point is 1000 to 2000 feet above the site location.

If the projection point is more than 2000 feet above or below the site location, get a new forecast or reading.

11 	(Aspect)―Record the aspect of the projection point location (north, south, east, or west).

12	(Slope)―Record the slope in percent (%) at the project point.  (See pages B-35 and B-36 for determining percent slope.)

13	(Fuel Moisture Correction)―From Input Values 7 through 12 and the appropriate Daytime Correction Tables (Tables 3, 4, or 5) determine fuel moisture correction.  Record in percent.

OUTPUT

1	(Fine Dead Fuel Moisture)―Determine the fine dead fuel moisture by adding Input Item 6 and Input Item 13.  Record as a percent.

| Dry Bulb Temp (°F) | Relative Humidity (Percent) |
| --- | --- |
|  | 0 ↓ 4 | 5 ↓ 9 | 10 ↓ 14 | 15 ↓ 19 | 20 ↓ 24 | 25 ↓ 29 | 30 ↓ 34 | 35 ↓ 39 | 40 ↓ 44 | 45 ↓ 49 | 50 ↓ 54 | 55 ↓ 59 | 60 ↓ 64 | 65 ↓ 69 | 70 ↓ 74 | 75 ↓ 79 | 80 ↓ 84 | 85 ↓ 89 | 90 ↓ 94 | 95 ↓ 99 | 100 |
| 10-29 | 1 | 2 | 2 | 3 | 4 | 5 | 5 | 6 | 7 | 8 | 8 | 8 | 9 | 9 | 10 | 11 | 12 | 12 | 13 | 13 | 14 |
| 30-49 | 1 | 2 | 2 | 3 | 4 | 5 | 5 | 6 | 7 | 7 | 7 | 8 | 9 | 9 | 10 | 10 | 11 | 12 | 13 | 13 | 13 |
| 50-69 | 1 | 2 | 2 | 3 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 11 | 12 | 12 | 12 | 13 |
| 70-89 | 1 | 1 | 2 | 2 | 3 | 4 | 5 | 5 | 6 | 7 | 7 | 8 | 8 | 8 | 9 | 10 | 10 | 11 | 12 | 12 | 13 |
| 90-109 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 5 | 6 | 7 | 7 | 8 | 8 | 8 | 9 | 10 | 10 | 11 | 12 | 12 | 13 |
| 109+ | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 5 | 6 | 7 | 7 | 8 | 8 | 8 | 9 | 10 | 10 | 11 | 12 | 12 | 12 |

GO TO TABLE 3, 4, OR 5 FOR FUEL MOISTURE CONTENT CORRECTIONS.

NOTE:  When using Tables 3, 4, and 5:

B = 1000-2000 feet below the site location.

L = 0-1000 feet above or below the site location.

A = 1000-2000 feet above the site location.

| UNSHADED – LESS THAN 50% SHADING OF SURFACE FUELS |
| --- |
| Aspect | %Slope | 0800> | 1000> | 1200> | 1400> | 1600> | 1800> |
|  |  | B | L | A | B | L | A | B | L | A | B | L | A | B | L | A | B | L | A |
| N | 0-30 | 2 | 3 | 4 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 3 | 4 |
|  | 31+ | 3 | 4 | 4 | 1 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 2 | 2 | 3 | 4 | 4 |
| E | 0-30 | 2 | 2 | 3 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 2 | 3 | 4 | 4 |
|  | 31+ | 1 | 2 | 2 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 5 | 6 |
| S | 0-30 | 2 | 3 | 3 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 3 | 3 |
|  | 31+ | 2 | 3 | 3 | 1 | 1 | 2 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 3 |
| W | 0-30 | 2 | 3 | 4 | 1 | 1 | 2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 2 | 3 | 3 |
|  | 31+ | 4 | 5 | 6 | 2 | 3 | 4 | 1 | 1 | 2 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 2 | 2 |
| SHADED – 50% OR MORE SHADING OF SURFACE FUELS |
| N | all | 4 | 5 | 5 | 3 | 4 | 5 | 3 | 3 | 4 | 3 | 3 | 4 | 3 | 4 | 5 | 4 | 5 | 5 |
| E | all | 4 | 4 | 5 | 3 | 4 | 5 | 3 | 3 | 4 | 3 | 4 | 4 | 3 | 4 | 5 | 4 | 5 | 6 |
| S | all | 4 | 4 | 5 | 3 | 4 | 5 | 3 | 3 | 4 | 3 | 3 | 4 | 3 | 4 | 5 | 4 | 5 | 5 |
| W | all | 4 | 5 | 6 | 3 | 4 | 5 | 3 | 3 | 4 | 3 | 3 | 4 | 3 | 4 | 5 | 4 | 4 | 5 |

| UNSHADED – LESS THAN 50% SHADING OF SURFACE FUELS |
| --- |
| Aspect | %Slope | 0800> | 1000> | 1200> | 1400> | 1600> | 1800> |
|  |  | B | L | A | B | L | A | B | L | A | B | L | A | B | L | A | B | L | A |
| N | 0-30 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 2 | 3 | 3 | 4 | 5 |
|  | 31+ | 3 | 4 | 5 | 3 | 3 | 4 | 2 | 3 | 4 | 2 | 3 | 4 | 3 | 3 | 4 | 3 | 4 | 5 |
| E | 0-30 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 4 | 3 | 4 | 5 |
|  | 31+ | 3 | 4 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 3 | 4 | 5 | 4 | 5 | 6 |
| S | 0-30 | 3 | 4 | 5 | 1 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 3 | 4 | 5 |
|  | 31+ | 3 | 4 | 5 | 1 | 2 | 2 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 2 | 2 | 3 | 4 | 5 |
| W | 0-30 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 3 | 4 | 5 |
|  | 31+ | 4 | 5 | 6 | 3 | 4 | 4 | 1 | 3 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 4 |
| SHADED – 50% OR MORE SHADING OF SURFACE FUELS |
| N | all | 4 | 5 | 6 | 4 | 5 | 5 | 3 | 4 | 5 | 3 | 4 | 5 | 4 | 5 | 5 | 4 | 5 | 6 |
| E | all | 4 | 5 | 6 | 3 | 4 | 5 | 3 | 4 | 5 | 3 | 4 | 5 | 4 | 5 | 6 | 4 | 5 | 6 |
| S | all | 4 | 5 | 6 | 3 | 4 | 5 | 3 | 4 | 5 | 3 | 4 | 5 | 3 | 4 | 5 | 4 | 5 | 6 |
| W | all | 4 | 5 | 6 | 4 | 5 | 5 | 3 | 4 | 5 | 3 | 4 | 5 | 3 | 4 | 5 | 4 | 5 | 6 |

| UNSHADED – LESS THAN 50% SHADING OF SURFACE FUELS |
| --- |
| Aspect | %Slope | 0800> | 1000> | 1200> | 1400> | 1600> | 1800> |
|  |  | B | L | A | B | L | A | B | L | A | B | L | A | B | L | A | B | L | A |
| N | 0-30 | 4 | 5 | 6 | 3 | 4 | 5 | 2 | 3 | 4 | 2 | 3 | 4 | 3 | 4 | 5 | 4 | 5 | 6 |
|  | 31+ | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 |
| E | 0-30 | 4 | 5 | 6 | 3 | 4 | 4 | 2 | 3 | 3 | 2 | 3 | 3 | 3 | 4 | 5 | 4 | 5 | 6 |
|  | 31+ | 4 | 5 | 6 | 2 | 3 | 4 | 2 | 2 | 3 | 3 | 4 | 4 | 4 | 5 | 6 | 4 | 5 | 6 |
| S | 0-30 | 4 | 5 | 6 | 3 | 4 | 5 | 2 | 3 | 3 | 2 | 2 | 3 | 3 | 4 | 4 | 4 | 5 | 6 |
|  | 31+ | 4 | 5 | 6 | 2 | 3 | 3 | 1 | 1 | 2 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 5 | 6 |
| W | 0-30 | 4 | 5 | 6 | 3 | 4 | 5 | 2 | 3 | 3 | 2 | 3 | 3 | 3 | 4 | 4 | 4 | 5 | 6 |
|  | 31+ | 4 | 5 | 6 | 4 | 5 | 6 | 3 | 4 | 4 | 2 | 2 | 3 | 2 | 3 | 4 | 4 | 5 | 6 |
| SHADED – 50% OR MORE SHADING OF SURFACE FUELS |
| N | all | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 |
| E | all | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 |
| S | all | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 |
| W | all | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 | 4 | 5 | 6 |

INPUT 3:  Live Fuel Moisture (LFM), %

Live fuel moisture (foliage moisture) is required for Fire Behavior Models 2, 4, 5, 7 and 10.  If data are unavailable for estimating live fuel moisture, the following rough estimates (Table 6) can be used.  Enter the live fuel moisture for Fire Models 2, 4, 5, 7 and 10 as Input 3 on the Fire behavior Worksheet on page B-5.

TABLE 6:  Live Fuel (Foliage) Moisture Content (Percent)

| Moisture Content (%) | Stage of Vegetative Development |
| --- | --- |
| 300 | Fresh foliage, annuals developing early in the growing cycle. |
| 200 | Maturing foliage, still developing, with full turgor. |
| 100 | Mature foliage, new growth complete and comparable to older perennial foliage. |
| 50 | Entering dormancy, coloration starting, some leaves may have dropped from stem. Also indicative of drought conditions. |
| >30 | Completely cured. |

INPUT 4:  Midflame Windspeed (MFWS), mi/h

Midflame wind is the wind which acts directly on the flaming fire front at the level of one half the flame height.  Fire generated convective winds must be ignored.

You may take wind readings directly with a handheld anemometer or other measuring device; however, the readings must be taken far enough upwind of the fire to ensure that the wind is not influenced by convective indrafts.

If you choose to use a weather forecast to estimate windspeeds, you must determine whether the forecast is for 20-foot windspeeds or midflame windspeeds.

When midflame winds are forecast, enter them directly in Input 4 of the Fire Behavior Worksheet.

If the 20-foot winds are forecast (which they usually are), the midflame windspeed must be calculated.  Use the Wind Adjustment Worksheet on page B-7 and complete the following Input and Output Values.  Enter midflame windspeed as Output 1 on the Wind Adjustment Worksheet and as Input 4 on the Fire Behavior Worksheet on page B-5.

INPUT

0	(Projection Pint)―Record the number of the projection point for which a fire behavior prediction is to be made.

1	(20-foot Windspeed)―Enter the 20-foot windspeed provided in the Special Weather Forecast.

2	(Fuel Model Number)―Enter one of the 13 FBPS fuel models.

3	(Wind Sheltering)―Using Diagram 1 on page B-32, determine whether fuels are:  1) unsheltered, 2) partially sheltered, 3) fully sheltered (open) or 4) fully sheltered (closed).

4	(Wind Adjustment Factor)―Using Table 7 on page B-33, select the appropriate adjustment factor for the specific fuel and sheltering condition.

OUTPUT

1	(Midflame Windspeed)―Multiply Input 1 x Input 4 on the Wind Adjustment Worksheet for the midflame windspeed.

Remember, for basic point source predictions the wind should be blowing within + 30 degrees of upslope.

DIAGRAM 1 ―20 Foot Windspeed Adjusted to Midflame Windspeed Based on Overstory

TABLE 7:  Wind Adjustment Table

| Fuel Exposure | Fuel Model | Adjustment Factor |
| --- | --- | --- |
| UNSHELTERED FUELS: Fuel exposed directly to the wind. No or sparse overstory. Fuel beneath timber that has lost its foliage; fuel beneath timber near clearings or clearcuts; fuel on high ridges where trees offer little shelter form the wind. | 4 13 1, 3, 5, 6, 11, 12 (2, 7)¹ (8, 9, 10)² | 0.6 0.5 0.4 0.4 0.4 0.4 |
| PARTIALLY SHELTERED FUELS: Fuel beneath patchy timber where it is not well sheltered; fuel beneath standing timber at midslope or higher on a mountain with wind blowing directly at the slope. | All Fuel Models | 0.3 |
| FULLY SHELTERED FUELS: Fuel sheltered beneath standing timber on flat or gentle slope or near base of mountain with steep slopes. | All Fuel Models | Open Stands 0.2 Dense Stands 0.1 |
| ¹Fuels usually partially sheltered. ²Fuels usually fully sheltered. |  |  |

TABLE 8:  Modified Beaufort Scale for Est. 20-Foot Windspeed

| Range of Speeds mi/h | Nomenclature |
| --- | --- |
| <3 | Very Light―Smoke rises nearly vertically. Leaves of quaking aspen in constant motion; small branches of bushes sway; slender branchlets and twigs of trees move gently; tall grasses and weeds sway and bend with wind; wind vane barely moves. |
| 4-7 | Light―Trees of pole size in the open sway gently; wind felt distinctly on face; loose scraps of paper move; wind flutters small flag. |
| 8-12 | Gentle Breeze―Trees of pole size in the open sway very noticeably; large branches of pole-size trees in the open toss; tops of trees in dense stands sway; wind extends small flag; a few crested waves form on lakes. |
| 13-18 | Moderate Breeze―Trees of pole size in the open sway violently; whole trees in dense stands sway noticeable; dust is raised in the road. |
| 19-24 | Fresh―Branchlets are broken from trees; inconvenience is felt in walking against wind. |
| 25-31 | Strong―Tree damage increases with occasional breaking of exposed tops and branches; progress impeded when walking against wind; light structural damage to buildings. |
| 32-38 | Moderate Gale―Severe damage to tree tops; very difficult to walk into wind; significant structural damage occurs. |
| >39 | Fresh Gale―Surfaced strong Santa Ana; intense stress on all exposed objects, vegetation, buildings; canopy offers virtually no protection; wind flow is systematic in disturbing everything in its path. |

INPUT 5:  Slope (SL), %

Slope Determination Process

To use the Slope Worksheet on page B-7 complete the following Input and Output Items.  Enter slope as Output 1 on the Slope Worksheet and as Input 5 on the Fire Behavior Worksheet on page B-5.

INPUT

0	(Projection Point)―Record the number of the projection point for which a fire behavior prediction is to be made.

1	(Contour Interval)―Determine the contour interval from the map; i.e., 40 ft.  This is the elevation change between contour lines.

2	(Map Scale)―Determine the map scale; i.e., 1:24,000.  This is the number of units on the map to ground distance in the same units; i.e., one inch on the map equals 24,000 inches on the ground.

3	(Conversion Factor)―Determine how many feet are in one inch of map distance; i.e., 1 inch = 2,000 ft. To determine this, measure the distance between section lines (east to west) in inches and tenths of an inch.  Divide the number of feet in a mile (5,280) by the measured map distance for the mile in inches.

Choose an area with uniform contour line separation.  From the lowest point on the slope, Point A, draw a line up the slope with the contour lines intersecting at right angels, to Point B.

4	(# of Contour Intervals)―Count the number of contour interspaces crossed between Points A and B.

5	(Rise in Elevation)―Determine vertical change in elevation by counting the contour interspaces between Points A and B. Multiply by the contour interval (Input 1); i.e., 40 ft x 11 contours = 440 ft.

6	(Map Distance)―Measure horizontal distance with a ruler in inches to the tenth of an inch.

7	(Horizontal Ground Distance)―Multiply the Map Distance (Input 6) by the conversion factor (Input 3); i.e., 0.5 in x 2,000 ft/in = 1,000 ft.

OUTPUT

1	(Slope)―Calculate slope by dividing rise (Input 5) by run (Input 7) on the Slope Worksheet and multiplying by 100; i.e., rise (Input 5) divided by run (Input 7) x 100 or 440 ft divided by 1,000 ft x 100 = 44%.

RISE     Vertical Distance

RUN     Horizontal Distance

TABLE 9:  Map Scale Conversion Factors

| Scale | Representative Fraction | Map in/mi | Map in/ch | Ft/Map in |
| --- | --- | --- | --- | --- |
| 1:253,440 | 253.44 | .25 | 0.0031 | 21,120 |
| 1:126,720 | 126.72 | .50 | 0.0063 | 10,560 |
| 1:63,360 | 63.36 | 1 | 0.0125 | 5,280 |
| 1:62,500 | 62.50 | 1.01 | 0.0127 | 5,208 |
| 1:31,680 | 31.68 | 2 | 0.025 | 2,640 |
| 1:24,000 | 24.00 | 2.64 | 0.033 | 2,000 |
| 1:21,120 | 21.12 | 3 | 0.038 | 1,760 |
| 1:15,840 | 15.84 | 4 | 0.05 | 1,320 |
| 1:7,920 | 7.92 | 8 | 0.1 | 660 |

This table allows the selection of conversion factors for different map scales.

INPUT 6:  Effective Windspeed (EWS), mi/h

Effective windspeed is determined using the lower left quadrant of the nomogram of the fuel model being used. Enter slope (Input 5) on the horizontal axis, and the midflame windspeed (Input 4) from the Fire Behavior Worksheet on the right axis.  Interpolation between the midflame windspeed line may be necessary.  Read the effective windspeed on the left side of the graph.  Enter effective windspeed as Input 6 on the Fire Behavior Worksheet on page B-5.

FIRE BEHAVIOR OUTPUTS

Determine the Fire Behavior Output Items (1-9) listed below and enter them on the Fire Behavior Worksheet on page B-5.

OUTPUT 1:  	Rate of Spread (ROS), ch/h

Using the upper right quadrant (left vertical axis) of the nomogram and input items recorded on the Fire Behavior Worksheet, determine rate of spread.   Tables 15 to 78 can also be used to approximate rate of spread.

OUTPUT 2:	Heat per Unit Area (HA), Btu/sq ft

Using the upper right quadrant of the nomogram, determine heat per unit area from the lower axis.

OUTPUT 3:	Fireline Intensity (FLI), Btu/ft/s

Using the upper right quadrant of the nomogram, determine fireline intensity along the curved lines.

OUTPUT 4:	Flame Length (FL), ft

Using the upper right quadrant of the nomogram, determine the flame length along the curved lines.  Flame length can also be approximated using Tables 15 to 78.

OUTPUT 5:  	Spread Distance (SD), ch

Rate of spread (Output 1) on the Fire Behavior Worksheet multiplied by the hours in which a fire spreads at that rate equals spread distance.  Convert to map distance using the Map-Spread Worksheet as outlined on page 39.

Map-Spread Worksheet

Use the Map-Spread Worksheet on page B-8 and complete the following Input and Output Items to determine map-spread distance.  Enter the map-spread distance as Output 1 on the Map-Spread Worksheet and as Output 5 on the Fire Behavior Worksheet on page B -5.

INPUT

0	(Projection Point)―Record the number of the projection point for which a fire behavior prediction is to be made.

1	(Rate of Spread)―Fire Behavior Worksheet, Output 1.

2	(Projection Time)―Hours or part of an hour in which a fire has spread.

3	(Spread Distance, ch)―Input 1 multiplied by Input 2.

4	(Spread Distance, ft)―Input 3 multiplied by 66 ft/ch.

5	(Map Scale)―Table 9 on page B-36.

6	(Conversion Factor)―Table 9.

OUTPUT

1	(Map Spread Distance)―Input 4 divided by Input 6.

OUTPUT 6 and 7:	Projected Fire Perimeter (PER), ch and Fire Area (AC), ac

Use the Size Worksheet on page B-8 and complete the following Input and Output Items to determine fire perimeter and area.  Enter perimeter as Output 1 on the Size Worksheet and as Output 6 on the Fire Behavior Worksheet on page B-5.  Enter area as Output 2 on the Size Worksheet and as Output 7 on the Fire Behavior Worksheet on page B-5.

INPUT

0	(Projection Point)―Record the number of the projection point for which a fire behavior predication has been made.

1	(Rate of Spread)―Output 1 form the Fire Behavior Worksheet.

2	(Effective Windspeed)―Input 6 from the Fire Behavior Worksheet.

3	(Projection Time)―The time in which a fire has spread.

4	(Spread Distance)―Input 1 multiplied by Input 3.

OUTPUT

1	(Perimeter)―From Table 10 using the spread distance (Input 4) and effective windspeed (Input 2) determine perimeter.

2	(Area)―From Table 11 using the spread distance (Input 4) and effective windspeed (Input 2) determine area (acres).

TABLE 10:  Perimeter Estimations for Point Source Fires

| Spread Distance Chains | Effective Windspeed mi/h |
| --- | --- |
|  | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 |
|  | Chains |
| 1 | 4 | 3 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| 2 | 7 | 6 | 5 | 5 | 5 | 4 | 4 | 4 | 4 | 4 |
| 3 | 11 | 8 | 7 | 7 | 7 | 7 | 6 | 6 | 6 | 6 |
| 4 | 14 | 11 | 10 | 9 | 9 | 9 | 9 | 9 | 8 | 8 |
| 5 | 18 | 14 | 12 | 12 | 11 | 11 | 11 | 11 | 11 | 10 |
| 6 | 21 | 17 | 15 | 14 | 14 | 13 | 13 | 13 | 13 | 13 |
| 7 | 25 | 19 | 17 | 16 | 16 | 15 | 15 | 15 | 15 | 15 |
| 8 | 28 | 22 | 20 | 19 | 18 | 18 | 17 | 17 | 17 | 17 |
| 9 | 32 | 25 | 22 | 21 | 20 | 20 | 19 | 19 | 19 | 19 |
| 10 | 35 | 28 | 25 | 23 | 23 | 22 | 22 | 21 | 21 | 21 |
| 11 | 39 | 30 | 27 | 26 | 25 | 24 | 24 | 23 | 23 | 23 |
| 12 | 43 | 33 | 30 | 28 | 27 | 26 | 26 | 26 | 25 | 25 |
| 13 | 46 | 36 | 32 | 30 | 29 | 29 | 28 | 28 | 27 | 27 |
| 14 | 50 | 39 | 35 | 33 | 32 | 31 | 30 | 30 | 30 | 29 |
| 15 | 53 | 41 | 37 | 35 | 34 | 33 | 32 | 32 | 32 | 31 |
| 16 | 57 | 44 | 40 | 37 | 36 | 35 | 35 | 34 | 34 | 34 |
| 17 | 60 | 47 | 42 | 40 | 38 | 37 | 37 | 36 | 36 | 36 |
| 18 | 64 | 50 | 45 | 42 | 41 | 40 | 39 | 38 | 38 | 38 |
| 19 | 67 | 52 | 47 | 44 | 43 | 42 | 41 | 41 | 40 | 40 |
| 20 | 71 | 55 | 50 | 47 | 45 | 44 | 43 | 43 | 42 | 42 |
| 21 | 74 | 58 | 52 | 49 | 47 | 46 | 45 | 45 | 44 | 44 |
| 22 | 78 | 61 | 55 | 51 | 50 | 48 | 48 | 47 | 46 | 46 |
| 23 | 82 | 64 | 57 | 54 | 52 | 51 | 50 | 49 | 49 | 48 |
| 24 | 85 | 66 | 60 | 56 | 54 | 53 | 52 | 51 | 51 | 50 |
| 25 | 89 | 69 | 62 | 59 | 56 | 55 | 54 | 53 | 53 | 52 |
| 26 | 92 | 72 | 65 | 61 | 59 | 57 | 56 | 55 | 55 | 54 |
| 28 | 99 | 77 | 70 | 66 | 63 | 62 | 61 | 60 | 59 | 59 |
| 30 | 106 | 83 | 74 | 70 | 68 | 66 | 65 | 64 | 63 | 63 |
| 32 | 113 | 88 | 79 | 75 | 72 | 70 | 69 | 68 | 68 | 67 |
| 34 | 121 | 94 | 84 | 80 | 77 | 75 | 73 | 73 | 72 | 71 |
| 36 | 128 | 99 | 89 | 84 | 81 | 79 | 78 | 77 | 76 | 75 |
| 38 | 135 | 105 | 94 | 89 | 86 | 84 | 82 | 81 | 80 | 80 |
| 40 | 142 | 110 | 99 | 94 | 90 | 88 | 86 | 85 | 84 | 84 |

TABLE 10:  Perimeter Estimations for Point Source Fires (continued)

| Spread Distance Chains | Effective Windspeed mi/h |
| --- | --- |
|  | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 |
|  | Chains |
| 42 | 149 | 116 | 104 | 98 | 95 | 92 | 91 | 90 | 89 | 88 |
| 44 | 156 | 122 | 109 | 103 | 99 | 97 | 95 | 94 | 93 | 92 |
| 46 | 163 | 127 | 114 | 108 | 104 | 101 | 99 | 98 | 97 | 96 |
| 48 | 170 | 133 | 119 | 112 | 108 | 106 | 104 | 102 | 101 | 101 |
| 50 | 177 | 138 | 124 | 117 | 113 | 110 | 108 | 107 | 106 | 195 |
| 52 | 184 | 144 | 129 | 122 | 117 | 114 | 112 | 111 | 110 | 109 |
| 54 | 191 | 149 | 134 | 126 | 122 | 119 | 117 | 115 | 114 | 113 |
| 56 | 199 | 155 | 139 | 131 | 126 | 123 | 121 | 119 | 118 | 117 |
| 58 | 206 | 160 | 144 | 136 | 131 | 128 | 125 | 124 | 122 | 122 |
| 60 | 213 | 166 | 149 | 140 | 135 | 132 | 130 | 128 | 127 | 126 |
| 62 | 220 | 171 | 154 | 145 | 140 | 136 | 134 | 132 | 131 | 130 |
| 64 | 227 | 177 | 159 | 150 | 144 | 141 | 138 | 137 | 135 | 134 |
| 66 | 234 | 182 | 164 | 154 | 149 | 145 | 143 | 141 | 139 | 138 |
| 68 | 241 | 188 | 169 | 159 | 153 | 150 | 147 | 145 | 144 | 142 |
| 70 | 248 | 193 | 174 | 164 | 158 | 154 | 151 | 149 | 148 | 147 |
| 72 | 255 | 199 | 179 | 169 | 162 | 158 | 156 | 154 | 152 | 151 |
| 74 | 262 | 204 | 184 | 173 | 167 | 163 | 160 | 158 | 156 | 155 |
| 76 | 269 | 210 | 189 | 178 | 171 | 167 | 164 | 162 | 160 | 159 |
| 78 | 277 | 215 | 194 | 183 | 176 | 172 | 169 | 166 | 165 | 163 |
| 80 | 284 | 221 | 199 | 187 | 180 | 176 | 173 | 171 | 169 | 168 |
| 82 | 291 | 227 | 204 | 192 | 185 | 180 | 177 | 175 | 173 | 172 |
| 84 | 298 | 232 | 209 | 197 | 189 | 185 | 182 | 179 | 177 | 176 |
| 86 | 305 | 238 | 214 | 201 | 194 | 189 | 186 | 183 | 182 | 180 |
| 88 | 312 | 243 | 219 | 204 | 198 | 194 | 190 | 188 | 186 | 184 |
| 90 | 319 | 249 | 223 | 211 | 203 | 198 | 194 | 192 | 190 | 189 |
| 92 | 326 | 254 | 228 | 215 | 207 | 202 | 199 | 196 | 194 | 193 |
| 94 | 333 | 260 | 233 | 220 | 212 | 207 | 203 | 200 | 199 | 197 |
| 96 | 340 | 263 | 238 | 225 | 217 | 211 | 207 | 205 | 203 | 201 |
| 98 | 347 | 271 | 243 | 229 | 221 | 216 | 212 | 209 | 207 | 205 |
| 100 | 355 | 276 | 248 | 234 | 226 | 220 | 216 | 213 | 211 | 210 |
| 105 | 372 | 290 | 261 | 246 | 237 | 231 | 227 | 224 | 222 | 220 |
| 110 | 390 | 304 | 273 | 257 | 248 | 242 | 238 | 235 | 232 | 230 |
| 115 | 408 | 318 | 286 | 269 | 259 | 253 | 249 | 245 | 243 | 241 |
| 120 | 425 | 331 | 298 | 281 | 271 | 264 | 259 | 256 | 253 | 251 |

TABLE 10:  Perimeter Estimations for Point Source Fires (continued)

| Spread Distance Chains | Effective Windspeed mi/h |
| --- | --- |
|  | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 |
|  | Chains |
| 125 | 443 | 345 | 310 | 293 | 282 | 275 | 270 | 267 | 264 | 262 |
| 130 | 461 | 359 | 323 | 304 | 293 | 286 | 281 | 277 | 275 | 272 |
| 135 | 479 | 373 | 335 | 316 | 304 | 297 | 292 | 288 | 285 | 283 |
| 145 | 498 | 387 | 348 | 328 | 316 | 308 | 303 | 299 | 296 | 293 |
| 145 | 514 | 401 | 360 | 339 | 327 | 319 | 313 | 309 | 306 | 304 |
| 150 | 532 | 414 | 372 | 351 | 338 | 330 | 324 | 320 | 317 | 314 |
| 155 | 550 | 428 | 385 | 363 | 350 | 341 | 335 | 331 | 327 | 325 |
| 160 | 567 | 442 | 397 | 374 | 361 | 352 | 346 | 341 | 338 | 335 |
| 165 | 585 | 456 | 410 | 386 | 372 | 363 | 357 | 352 | 348 | 346 |
| 170 | 603 | 470 | 422 | 398 | 383 | 374 | 367 | 363 | 359 | 356 |
| 175 | 620 | 485 | 435 | 410 | 395 | 385 | 378 | 373 | 370 | 367 |
| 180 | 638 | 497 | 447 | 421 | 406 | 396 | 389 | 384 | 380 | 377 |
| 185 | 656 | 511 | 459 | 433 | 417 | 497 | 400 | 395 | 391 | 388 |
| 190 | 674 | 525 | 472 | 445 | 429 | 418 | 411 | 405 | 401 | 398 |
| 195 | 691 | 539 | 486 | 456 | 440 | 429 | 421 | 416 | 412 | 409 |
| 200 | 709 | 552 | 497 | 468 | 451 | 440 | 432 | 427 | 422 | 419 |
| 210 | 744 | 580 | 571 | 491 | 474 | 462 | 454 | 448 | 443 | 440 |
| 220 | 780 | 608 | 546 | 515 | 496 | 484 | 475 | 469 | 465 | 461 |
| 230 | 815 | 635 | 571 | 538 | 519 | 506 | 497 | 491 | 486 | 482 |
| 240 | 851 | 663 | 596 | 562 | 541 | 528 | 519 | 512 | 507 | 503 |
| 250 | 886 | 691 | 621 | 585 | 564 | 550 | 540 | 533 | 528 | 524 |
| 260 | 922 | 718 | 646 | 608 | 586 | 572 | 562 | 555 | 549 | 545 |
| 270 | 957 | 746 | 670 | 632 | 609 | 594 | 583 | 576 | 570 | 566 |
| 280 | 993 | 773 | 695 | 655 | 631 | 616 | 605 | 597 | 591 | 587 |
| 290 | 1028 | 801 | 720 | 679 | 654 | 638 | 627 | 619 | 612 | 608 |
| 300 | 1064 | 829 | 745 | 702 | 677 | 660 | 648 | 640 | 634 | 629 |

This table can be used to estimate the perimeter of a fire in chains from estimates of total spread distance (rate of spread x time) and effective windspeed.  When the effective windspeed is an even number or when spread distance is not broken out, estimations can be made or interpolation may be necessary.

TABLE 11:  Area Estimations for Point Source Fires

| Spread Distance Chains | Effective Windspeed mi/h |
| --- | --- |
|  | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 |
|  | Acres |
| 1 | .1 | .1 | <.1 | <.1 | <.1 | <.1 | <.1 | <.1 | <.1 | <.1 |
| 2 | .4 | .2 | .2 | .1 | .1 | .1 | .1 | .1 | .1 | .1 |
| 3 | .9 | .5 | .3 | .3 | .2 | .2 | .2 | .2 | .1 | .1 |
| 4 | 1.6 | .9 | .6 | .5 | .4 | .3 | .3 | .3 | .2 | .2 |
| 5 | 2.5 | 1.4 | 1.0 | .8 | .6 | .5 | .5 | .4 | .4 | .3 |
| 6 | 3.5 | 1.9 | 1.4 | 1.1 | .9 | .8 | .7 | .6 | .5 | .5 |
| 7 | 4.8 | 2.7 | 1.9 | 1.5 | 1.2 | 1.1 | .9 | .8 | .7 | .7 |
| 8 | 6.3 | 3.5 | 2.5 | 2.0 | 1.6 | 1.4 | 1.2 | 1.1 | 1.0 | .9 |
| 9 | 8.0 | 4.4 | 3.1 | 2.5 | 2.1 | 1.8 | 1.5 | 1.4 | 1.2 | 1.1 |
| 10 | 9.8 | 5.4 | 3.9 | 3.1 | 2.5 | 2.2 | 1.9 | 1.7 | 1.5 | 1.4 |
| 11 | 11.9 | 6.6 | 4.7 | 3.7 | 3.1 | 2.6 | 2.3 | 2.0 | 1.8 | 1.7 |
| 12 | 14.1 | 7.8 | 5.6 | 4.4 | 3.7 | 3.1 | 2.7 | 2.4 | 2.2 | 2.0 |
| 13 | 16.6 | 9.2 | 6.6 | 5.2 | 4.3 | 3.7 | 3.2 | 2.9 | 2.6 | 2.3 |
| 14 | 19.2 | 10.6 | 7.6 | 6.0 | 5.0 | 4.3 | 3.7 | 3.3 | 3.0 | 2.7 |
| 15 | 22.1 | 12.2 | 8.7 | 6.9 | 5.7 | 4.9 | 4.3 | 3.8 | 3.4 | 3.1 |
| 16 | 25.1 | 13.9 | 9.9 | 7.8 | 6.5 | 5.6 | 4.9 | 4.3 | 3.9 | 3.6 |
| 17 | 28.4 | 15.7 | 11.2 | 8.8 | 7.3 | 6.3 | 5.5 | 4.9 | 4.4 | 4.0 |
| 18 | 31.8 | 17.5 | 12.6 | 9.9 | 8.2 | 7.0 | 6.2 | 5.5 | 4.9 | 4.5 |
| 19 | 35.4 | 19.6 | 14.0 | 11.1 | 9.2 | 7.8 | 6.9 | 6.1 | 5.5 | 5.0 |
| 20 | 39.3 | 21.7 | 15.5 | 12.2 | 10.2 | 8.7 | 7.6 | 6.8 | 6.1 | 5.5 |
| 21 | 43.3 | 23.9 | 17.1 | 13.5 | 11.2 | 9.6 | 8.4 | 7.5 | 6.7 | 6.1 |
| 22 | 47.5 | 26.2 | 18.8 | 14.8 | 12.3 | 10.5 | 9.2 | 8.2 | 7.4 | 6.7 |
| 23 | 52 | 29 | 21 | 16 | 13 | 11 | 10 | 8.9 | 8.1 | 7.3 |
| 24 | 57 | 31 | 22 | 18 | 15 | 13 | 11 | 9.7 | 8.8 | 8.0 |
| 25 | 61 | 34 | 24 | 19 | 16 | 14 | 12 | 10.6 | 9.5 | 8.7 |
| 26 | 66 | 37 | 26 | 21 | 17 | 15 | 13 | 11.4 | 10.3 | 9.4 |
| 28 | 77 | 42 | 30 | 24 | 20 | 17 | 15 | 13 | 12 | 11 |
| 30 | 88 | 49 | 35 | 28 | 23 | 20 | 17 | 15 | 12 | 12 |
| 32 | 101 | 55 | 40 | 31 | 26 | 22 | 19 | 17 | 16 | 14 |
| 34 | 113 | 63 | 45 | 35 | 29 | 25 | 22 | 20 | 18 | 16 |
| 36 | 127 | 70 | 50 | 40 | 33 | 28 | 25 | 22 | 20 | 18 |
| 38 | 142 | 78 | 56 | 44 | 37 | 31 | 27 | 24 | 22 | 20 |
| 40 | 157 | 87 | 62 | 49 | 41 | 35 | 30 | 27 | 24 | 22 |

TABLE 11:  Area Estimations for Point Source Fires

(continued)

| Spread Distance Chains | Effective Windspeed mi/h |
| --- | --- |
|  | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 |
|  | Acres |
| 42 | 173 | 96 | 69 | 54 | 45 | 38 | 34 | 30 | 27 | 24 |
| 44 | 190 | 105 | 75 | 59 | 49 | 42 | 37 | 33 | 30 | 27 |
| 46 | 208 | 115 | 82 | 65 | 54 | 46 | 40 | 36 | 32 | 29 |
| 48 | 226 | 125 | 90 | 71 | 58 | 50 | 44 | 39 | 35 | 32 |
| 50 | 245 | 135 | 97 | 77 | 63 | 54 | 48 | 42 | 38 | 35 |
| 52 | 265 | 146 | 105 | 83 | 69 | 59 | 51 | 46 | 41 | 38 |
| 54 | 286 | 158 | 113 | 89 | 74 | 63 | 55 | 49 | 44 | 40 |
| 56 | 308 | 170 | 122 | 96 | 80 | 68 | 60 | 53 | 48 | 43 |
| 58 | 330 | 182 | 131 | 103 | 85 | 73 | 64 | 57 | 51 | 47 |
| 60 | 353 | 195 | 140 | 110 | 91 | 78 | 68 | 61 | 55 | 50 |
| 62 | 377 | 208 | 149 | 118 | 98 | 84 | 73 | 65 | 59 | 53 |
| 64 | 402 | 222 | 159 | 125 | 104 | 89 | 78 | 69 | 62 | 57 |
| 66 | 428 | 236 | 169 | 133 | 111 | 95 | 83 | 74 | 66 | 60 |
| 68 | 454 | 250 | 180 | 142 | 117 | 100 | 88 | 78 | 70 | 64 |
| 70 | 481 | 265 | 190 | 150 | 124 | 106 | 93 | 83 | 75 | 68 |
| 72 | 509 | 281 | 201 | 159 | 132 | 113 | 99 | 88 | 79 | 72 |
| 74 | 538 | 297 | 213 | 168 | 139 | 119 | 104 | 93 | 83 | 76 |
| 76 | 567 | 313 | 224 | 177 | 147 | 125 | 110 | 98 | 88 | 80 |
| 78 | 597 | 329 | 236 | 186 | 154 | 132 | 116 | 103 | 93 | 84 |
| 80 | 628 | 347 | 249 | 196 | 162 | 139 | 122 | 108 | 98 | 89 |
| 82 | 660 | 364 | 261 | 206 | 171 | 146 | 128 | 114 | 102 | 93 |
| 84 | 693 | 382 | 274 | 216 | 179 | 153 | 134 | 119 | 108 | 98 |
| 86 | 726 | 401 | 287 | 226 | 188 | 161 | 141 | 125 | 113 | 103 |
| 88 | 760 | 419 | 301 | 237 | 197 | 168 | 147 | 131 | 118 | 107 |
| 90 | 795 | 439 | 315 | 248 | 206 | 176 | 154 | 137 | 123 | 112 |
| 92 | 831 | 458 | 329 | 259 | 215 | 184 | 161 | 143 | 129 | 117 |
| 94 | 867 | 479 | 343 | 271 | 224 | 192 | 168 | 149 | 135 | 123 |
| 96 | 905 | 499 | 358 | 282 | 234 | 200 | 175 | 156 | 140 | 128 |
| 98 | 943 | 520 | 373 | 294 | 244 | 209 | 183 | 162 | 146 | 133 |
| 100 | 982 | 542 | 388 | 306 | 254 | 217 | 190 | 169 | 152 | 139 |
| 105 | 1082 | 597 | 428 | 338 | 280 | 420 | 210 | 186 | 168 | 153 |
| 110 | 1188 | 655 | 470 | 371 | 307 | 263 | 230 | 205 | 184 | 168 |
| 115 | 1298 | 716 | 514 | 405 | 336 | 287 | 251 | 224 | 202 | 183 |
| 120 | 1414 | 780 | 559 | 441 | 366 | 313 | 274 | 244 | 219 | 200 |

TABLE 11:  Area Estimations for Point Source Fires

(continued)

| Spread Distance Chains | Effective Windspeed mi/h |
| --- | --- |
|  | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 |
|  | Acres |
| 125 | 1534 | 846 | 607 | 478 | 397 | 339 | 297 | 264 | 238 | 217 |
| 130 | 1659 | 915 | 657 | 517 | 429 | 367 | 321 | 286 | 258 | 234 |
| 135 | 1789 | 987 | 708 | 558 | 463 | 396 | 346 | 308 | 278 | 253 |
| 140 | 1924 | 1061 | 761 | 600 | 497 | 426 | 373 | 331 | 299 | 272 |
| 145 | 2064 | 1139 | 817 | 644 | 534 | 457 | 400 | 356 | 320 | 292 |
| 150 | 2209 | 1219 | 874 | 689 | 571 | 489 | 428 | 381 | 343 | 312 |
| 155 | 2359 | 1301 | 933 | 736 | 610 | 522 | 457 | 406 | 366 | 333 |
| 160 | 2513 | 1386 | 995 | 784 | 650 | 554 | 487 | 433 | 390 | 355 |
| 165 | 2673 | 1474 | 1058 | 834 | 691 | 591 | 518 | 460 | 415 | 378 |
| 170 | 2837 | 1565 | 1123 | 885 | 734 | 628 | 549 | 489 | 440 | 401 |
| 175 | 3007 | 1659 | 1190 | 938 | 777 | 665 | 582 | 518 | 467 | 425 |
| 180 | 3181 | 1755 | 1259 | 992 | 822 | 704 | 616 | 548 | 494 | 449 |
| 185 | 3360 | 1854 | 1330 | 1048 | 869 | 743 | 651 | 579 | 572 | 475 |
| 190 | 3544 | 1955 | 1402 | 1105 | 916 | 784 | 686 | 611 | 550 | 501 |
| 195 | 3733 | 2059 | 1477 | 1164 | 965 | 826 | 723 | 643 | 579 | 527 |
| 200 | 3927 | 2166 | 1554 | 1225 | 1015 | 869 | 760 | 676 | 610 | 555 |
| 210 | 4330 | 2388 | 1713 | 1350 | 1119 | 958 | 838 | 746 | 672 | 612 |
| 220 | 4752 | 2621 | 1880 | 1482 | 1229 | 1051 | 920 | 819 | 738 | 671 |
| 230 | 5193 | 2865 | 2055 | 1620 | 1343 | 1149 | 1006 | 895 | 806 | 734 |
| 240 | 5655 | 3119 | 2238 | 1764 | 1462 | 1251 | 1095 | 974 | 878 | 799 |
| 250 | 6136 | 3385 | 2428 | 1914 | 1586 | 1358 | 1188 | 1057 | 952 | 867 |
| 260 | 6437 | 3661 | 2626 | 2070 | 1716 | 1469 | 1285 | 1143 | 1030 | 938 |
| 270 | 7157 | 3946 | 2832 | 2232 | 1850 | 1584 | 1386 | 1233 | 1111 | 1011 |
| 280 | 7697 | 4246 | 3046 | 2401 | 1990 | 1703 | 1490 | 1326 | 1195 | 1087 |
| 290 | 8256 | 4555 | 3267 | 2575 | 2135 | 1827 | 1599 | 1422 | 1281 | 1166 |
| 300 | 8836 | 4874 | 3496 | 2756 | 2284 | 1955 | 1711 | 1522 | 1371 | 1248 |

This table can be used to estimate the area (acres) from estimates of total spread distance (rate of spread x time) and effective windspeed.  When the effective windspeed is an even number or when spread distance is not broken out, estimations can be made or interpolation may be necessary.

DIAGRAM 2―Approximate Fire Shapes for Various Effective Windspeeds

OUTPUT 8:	Maximum Spotting Distance (SPOT), mi

The Spotting Worksheet is used to predict the distance a firebrand will travel from the originating torching tree.  It does not apply to firebrands resulting from a running crown fire, but may be considered as a first approximation in such situations.  Use the Spotting Worksheet and nomograms 1 through 4 to determine Maximum Spotting Distance.  Enter Maximum Spotting Distance on the Spotting Worksheet and as a Output 8 on the Fire Behavior Worksheet on page B-5.

INPUT

1	(Torching Tree Height)―Actual height of torching tree.

2	(Torching Tree Species)―When species is not provided, select species based on crown shape and knowledge of firebrand production.

3	(Torching Tree DBH)―Diameter at breast height.

4	(Average Tree Cover Height)―Estimate average tree cover height downwind from the torching tree.

5	(Windspeed at 20-foot Height)―Use the forecasted 20-foot windspeed.  When gusts are indicated, using the maximum gust would provide the worst case distance.

OUTPUT

(Maximum Spotting distance)―Enter maximum spotting distance on the Spotting Worksheet.

Convert spotting distance to map distance using the Map-Spot Worksheet as outlined on page B-49.

Map-Spot Worksheet

Use the Map-Spot Worksheet on page B-9 and complete the following Input and Output Items to determine map-spot distance.  Enter the map-spot distance as Output 1 on the Map-Spot Worksheet and under Output 8 on the Fire Behavior Worksheet on page B-5.

INPUT

0	(Projection Point)―Record the number of the projection point for which a fire behavior prediction is to be made.

1	(Spotting Distance, mi)―Record the Output from the Spotting Worksheet.

2	(Spotting Distance, ft)―Multiply mile distance in Input 1 by 5,280 to obtain feet.

3	(Map Scale)―Record the map scale taken from the map being used; e.g., 1:24,000.

4	(Conversion Factor)―See Table 9 on page B-36 for correct conversion factor; e.g., 2000.

OUTPUT

1	(Map Distance Spot)―Input 2 divided by Input 4.

NOMOGRAM 1―Flame Height

From Nomogram 1 determine flame height by using DBH and torching tree species.  Enter flame height in Box B on the Spotting Worksheet.

NOMOGRAM 2―Flame Duration

From Nomogram 2 determine flame duration by using DBH and tree species.  Enter flame duration on the Spotting Worksheet.

NOMOGRAM 3―Ration of Lofted Firebrand Height to Flame Height

From Nomogram 3 determine ratio of lofted firebrand height to flame height.  Use flame duration and ratio of tree height to flame height as inputs.  Enter ratio of lofted firebrand height to flame height in Box C on the Spotting Worksheet.

NOMOGRAM 4―Maximum Spotting Distance

On the lower right-hand edge of nomogram 4 locate the firebrand height. Proceed vertically to the effective tree cover height.  Move left horizontally until you reach the treetop windspeed, move vertically down to the bottom axis and read the maximum spotting distance.  Enter the maximum spotting distance on the Spotting Worksheet.

OUTPUT 9:	Probability of Ignition (PIG), %

Use Table 12 on page B-55 and the dry bulb temperature (Input 2), shading (Input 8) and the fine dead fuel moisture (Output 1) from the Fine Dead Fuel Moisture/Probability of Ignition Worksheet to determine probability of ignition.  Enter probability of ignition as Output 2 on the worksheet.  Also record it a Output 9 on the Fire Behavior Worksheet on page B-5.

TABLE 13―Fire Severity Related to Fuel Moisture Chart

| Relative Humidity | Fuel Moisture | Fuel Moisture | Relative ease of chance ignition and spotting, general burning conditions. |
| --- | --- | --- | --- |
| >60 | >20 | >15 | Very little ignition; some spotting may occur with winds above 9 mi/h. |
| 45-60 | 15-19 | 12-15 | Low ignition hazard – campfires become dangerous; glowing brands cause ignition when relative humidity is <50 percent. |
| 30-45 | 11-14 | 10-12 | Medium ignition hazard – matches become dangerous; “easy” burning conditions. |
| 26-40 | 8-10 | 8-9 | High ignition hazard – matches are dangerous; occasional crowning, spotting caused by gusty winds: “moderate” burning conditions. |
| 15-30 | 5-7 | 5-7 | Quick ignition, rapid buildup, extensive crowning; any increase in wind causes increased spotting, crowning, loss of control; fire moves up bark of trees igniting aerial fuels; long distance spotting in pine stands; dangerous burning conditions. |
| <15 | <5 | <5 | All sources of ignition dangerous; aggressive burning, spot fires occur often and spread rapidly, extreme fire behavior probable; critical burning conditions. |

DIAGRAM 3―Fire Behavior Characteristics Chart (Light Fuel)

DIAGRAM 4―Fire Behavior Characteristics Chart (Heavy Fuel)

TABLE 14―Fire Suppression Interpretations¹

CAUTION:  These are not guides to personal safety.  Fires can be dangerous at any level of intensity.  Wilson (1977) has shown that most fatalities occur in light fuels on small fires or isolated sections of large fires.

| Flame Length (ft) | Fireline Intensity (Btu/ft/s) | Interpretations |
| --- | --- | --- |
| 0-4 | 0-100 | Fires can generally be attacked at the head or flanks by persons using hand tools. Handline should hold the fire. |
| 4-8 | 100-500 | Fires are too intense for direct attack on the head by persons using hand tools. Handline cannot be relied on to hold fire. Equipment such as dozers, engines, and retardant aircraft can be effective. |
| 8-11 | 500-1,000 | Fires may present serious control problems – torching out, crowning, and spotting Control efforts at the head of the fire will probably be ineffective. |
| 11+ | 1,000+ | Crowning, spotting, and major runs are common. Control efforts at the head of the fire are ineffective. |

¹ Help in Making Fuel Management Decisions, 1975; Research Paper NC-112, USDA: Forest Service

SAFETY AND FIRE BEHAVIOR

•	Probably the most important aspect of predicting fire behavior is to identify potentially dangerous fireline conditions.

•	Be alert to all potentially dangerous situations and communicate the danger to all affected personnel.

•	Know, remember, and use:

•	THE STANDARD ORDERS (Inside Cover)

•	THE 18 WATCHOUT SITUATIONS (Inside Cover)

•	THE FOUR COMMON DENOMINATORS OF FIRE BEHAVIOR ON TRAGEDY AND NEAR-MISS FIRES (Inside Cover)

•	DOWNHILL/INDIRECT LINE CONSTRUCTION GUIDELINES (Chapter 4)

•	THE 9 URBANWILDLAND “WATCHOUTS”

•	LCES (LOOK OUTS, COMMUNICATIONS, ESCAPE ROUTES, AND SAFETY ZONES)

•	LOOK UP, LOOK DOWN, LOOK AROUND

Safety and Fire Behavior

FIRE ENVIRONMENT

FACTORS			INDICATORS

Fuel Characteristics	Continuous fine fuels CARRIER!	Assess		Heavy loading of dead and down

Ladder Fuels

Tight crown spacing (<20 ft.)

Special Conditions:

Firebrand sources

Numerous snags

Preheated canopy

Frost and bug kill

Unusual fine fuels

High dead-to-live ratio

Urban/Wildland

Fuel Moisture		How RH (Dangerous <25%)

Feel & Measure	Low 10 hr FMC (Dangerous <6%)

Drought conditions

Seasonal drying

Fuel Temperature		High temps (above 85 ˚F)

Feel & Measure	High % of fuels with direct sun

Aspect with increasing fuel temps.

Terrain			Steep slopes (>50%)

Scout		Chutes

Saddles

Narrow canyons

FIRE ENVIRONMENT

FACTORS			INDICATORS

Wind			Surface winds above 10 mi/h

Observe		Lenticular clouds

High, fast moving clouds

Approaching cold front

Cumulonimbus development

Sudden calm

Battling winds

Stability	Clear visibility

Observe	Gusty winds and dust devils

Cumulus clouds

Castellatus clouds in the a.m.

Smoke rises straight up

Inversion beginning to lift

Thermal belt

Fire Behavior	Learning column

Watch	Sheared column

Well developed column

Trees torching

Smouldering fires picking up

Small firewhirls beginning

Frequent spot fires

Remember to Expect Diurnal Changes!

•RH•		•Winds•

•Temperature•	•Stability•

•	Indicators may vary in different regions and fuel types.

•	Ask questions in unfamiliar situations.

Tables 15 through 78―Rate of Spread and Flame Length Tables by

Fuel Type and Percent Slope

NOTE:  Tables 15 to 78 for ROS and FL (Output Items 1 and 4) on the Fire Behavior Worksheet reflect slope classes 0, 30, 45, 60 and 90 percent.  You may use the slope class closest to the actual slope recorded (for Input Item 5) or interpolate between the slope class.

TABLE 15:  FUEL MODEL 1―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 5 | 22 | 77 | 172 | 307 | •446 | •446 |
| 6.0 | 4 | 18 | 61 | 135 | 242 | •270 | •270 |
| 9.0 | 3 | 13 | 45 | 101 | •136 | •136 | •136 |
| 12.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 1.3 | 2.5 | 4.5 | 6.4 | 8.4 | •10.0 | •10.0 |
| 6.0 | 1.1 | 2.1 | 3.8 | 5.4 | 7.1 | •7.5 | •7.5 |
| 9.0 | 0.9 | 1.7 | 3.0 | 4.3 | •5.0 | •5.0 | •5.0 |
| 12.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 16:  FUEL MODEL 1―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 25 | 42 | 97 | 191 | 327 | 446• | 446• |
| 6.0 | 20 | 33 | 76 | 151 | 257 | 270• | 270• |
| 9.0 | 15 | 25 | 57 | 112 | 136• | 136• | 136• |
| 12.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 2.7 | 3.4 | 4.9 | 6.8 | 8.6 | 10.0• | 10.0• |
| 6.0 | 2.2 | 2.8 | 4.2 | 5.7 | 7.3 | 7.5• | 7.5• |
| 9.0 | 1.8 | 2.3 | 3.3 | 4.6 | 5.0• | 5.0• | 5.0• |
| 12.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 17:  FUEL MODEL 1―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 50 | 67 | 122 | 216 | 352 | 446• | 446• |
| 6.0 | 39 | 53 | 96 | 170 | 270• | 270• | 270• |
| 9.0 | 29 | 39 | 71 | 127 | 136• | 136• | 136• |
| 12.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 3.6 | 4.2 | 5.5 | 7.1 | 8.9 | 10.0• | 10.0• |
| 6.0 | 3.1 | 3.5 | 4.6 | 6.0 | 7.5• | 7.5• | 7.5• |
| 9.0 | 2.5 | 2.8 | 3.7 | 4.8 | 5.0• | 5.0• | 5.0• |
| 12.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 18:  FUEL MODEL 1―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 84 | 101 | 156 | 251 | 386 | 446• | 446• |
| 6.0 | 66 | 80 | 123 | 197 | 270• | 270• | 270• |
| 9.0 | 49 | 59 | 91 | 136• | 136• | 136• | 136• |
| 12.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 4.6 | 5.0 | 6.2 | 7.7 | 9.3 | 10.0• | 10.0• |
| 6.0 | 3.9 | 4.3 | 5.2 | 6.5 | 7.5• | 7.5• | 7.5• |
| 9.0 | 3.1 | 3.4 | 4.1 | 5.9• | 5.0• | 5.0• | 5.0• |
| 12.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 19: FUEL MODEL 1―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 183 | 200 | 255 | 251 | 349 | 446• | 446• |
| 6.0 | 144 | 157 | 200 | 197 | 270• | 270• | 270• |
| 9.0 | 107 | 117 | 136• | 136• | 136• | 136• | 136• |
| 12.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 6.6 | 6.9 | 7.7 | 8.9 | 10.0• | 10.0• | 10.0• |
| 6.0 | 5.6 | 5.8 | 6.5 | 7.5• | 7.5• | 7.5• | 7.5• |
| 9.0 | 4.5 | 4.7 | 5.0• | 5.0• | 5.0• | 5.0• | 5.0• |
| 12.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 20:  FUEL MODEL 2―0% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 3 | 11 | 28-31 | 56062 | 92-102 | 138-152 | 191-211 |
| 6.0 | 120-90 | 2 | 9 | 23-25 | 45-50 | 75-83 | 112-124 | 156-172 |
| 9.0 | 120-90 | 2 | 8 | 20-22 | 40-44 | 66-73 | 99-109 | 137-151 |
| 12.0 | 120-90 | 2 | 6 | 16 | 30-33 | 49-54 | 73-81 | 102-112 |
| 15.0 | 120-90 | •0 | •0 | •3 | •3 | •3 | •3 | •3 |
| 18.0+ | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 2.1 | 3.8 | 6.2 | 8.4 | 10.7 | 12.8 | 14.9 |
| 6.0 | 120-90 | 1.8 | 3.2 | 5.3 | 7.2 | 9.1 | 11.0 | 12.8 |
| 9.0 | 120-90 | 1.7 | 3.0 | 4.8 | 6.6 | 8.4 | 10.0 | 11.6 |
| 12.0 | 120-90 | 1.3 | 2.3 | 3.7 | 5.2 | 6.5 | 7.8 | 9.1 |
| 15.0 | 120-90 | •0.2 | •0.3 | •0.4 | •0.5 | •0.5 | •0.5 | •0.5 |
| 18.0+ | 120-90 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  |  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 21:  FUEL MODEL 2―30% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 9 | 15-17 | 34-37 | 61-68 | 98-109 | 144-159 | 197-218 |
| 6.0 | 120-90 | 8 | 14 | 27-30 | 50-55 | 80-88 | 117-129 | 161-177 |
| 9.0 | 120-90 | 7 | 12 | 24-27 | 44-49 | 70-78 | 103-113 | 141-156 |
| 12.0 | 120-90 | 5 | 9 | 18-20 | 33-36 | 52-57 | 76-84 | 105-115 |
| 15.0 | 120-90 | •1 | •1 | •2 | •2 | •2 | •2 | •2 |
| 18.0+ | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 3.5 | 4.7 | 6.7 | 8.8 | 10.9 | 13.0 | 15.1 |
| 6.0 | 120-90 | 3.0 | 4.0 | 5.8 | 7.5 | 9.4 | 11.2 | 12.9 |
| 9.0 | 120-90 | 2.8 | 3.7 | 5.3 | 6.9 | 8.6 | 10.2 | 11.8 |
| 12.0 | 120-90 | 2.2 | 2.9 | 4.1 | 5.4 | 6.7 | 8.0 | 9.3 |
| 15.0 | 120-90 | •0.3 | •0.3 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 |
| 18.0+ | 120-90 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  |  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 22:  FUEL MODEL 2―45% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 17 | 23-25 | 41-45 | 69-76 | 105-117 | 151-167 | 204-226 |
| 6.0 | 120-90 | 14 | 20 | 33-37 | 56-62 | 86-95 | 123-136 | 167-184 |
| 9.0 | 120-90 | 12 | 16-18 | 29-32 | 49-54 | 76-83 | 108-119 | 147-161 |
| 12.0 | 120-90 | 9 | 13 | 22-24 | 37-40 | 56-62 | 80-88 | 109-129 |
| 15.0 | 120-90 | •1 | •1 | •2 | •2 | •2 | •2 | •2 |
| 18.0+ | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 4.7 | 5.6 | 7.3 | 9.3 | 11.3 | 13.4 | 15.3 |
| 6.0 | 120-90 | 4.0 | 4.8 | 6.3 | 7.9 | 9.7 | 11.4 | 13.2 |
| 9.0 | 120-90 | 3.7 | 4.4 | 5.8 | 7.3 | 8.9 | 10.5 | 12.0 |
| 12.0 | 120-90 | 2.9 | 3.4 | 4.5 | 5.7 | 6.9 | 8.2 | 9.4 |
| 15.0 | 120-90 | •0.3 | •0.4 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 |
| 18.0+ | 120-90 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  |  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 23:  FULE MODEL 2―60% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 26-28 | 33-36 | 51-56 | 79-87 | 116-128 | 161-178 | 214-237 |
| 6.0 | 120-90 | 21-23 | 27-30 | 42-46 | 64-71 | 94-104 | 131-145 | 175-193 |
| 9.0 | 120-90 | 18-20 | 24-26 | 37-40 | 57-62 | 83-91 | 115-127 | 154-169 |
| 12.0 | 120-90 | 15 | 17-19 | 27-30 | 42-46 | 62-68 | 86-94 | 114-126 |
| 15.0 | 120-90 | •1 | •2 | •2 | •2 | •2 | •0 | •0 |
| 18.0+ | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 5.9 | 6.6 | 8.1 | 9.9 | 11.8 | 13.8 | 15.7 |
| 6.0 | 120-90 | 5.1 | 5.7 | 6.9 | 8.5 | 10.1 | 11.8 | 13.5 |
| 9.0 | 120-90 | 4.6 | 5.2 | 6.4 | 7.7 | 9.3 | 10.8 | 12.3 |
| 12.0 | 120-90 | 3.6 | 4.1 | 5.0 | 6.1 | 7.2 | 8.4 | 9.6 |
| 15.0 | 120-90 | •0.4 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 |
| 18.0+ | 120-90 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  |  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 24:  FUEL MODEL 2―90% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 55-60 | 63-68 | 80-88 | 108-119 | 144-160 | 190-210 | 243-269 |
| 6.0 | 120-90 | 45-49 | 50-56 | 65-72 | 88-97 | 118-130 | 155-171 | 199-219 |
| 9.0 | 120-90 | 39-43 | 44-49 | 57-63 | 77-85 | 104-114 | 136-150 | 175-192 |
| 12.0 | 120-90 | 29-32 | 33-36 | 43-47 | 57-63 | 77-85 | 101-111 | 130-142 |
| 15.0 | 120-90 | •2 | •2 | •2 | •2 | •2 | •2 | •2 |
| 18.0+ | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 8.4 | 8.9 | 10.0 | 11.4 | 13.1 | 14.8 | 16.6 |
| 6.0 | 120-90 | 7.2 | 7.6 | 8.5 | 9.8 | 11.3 | 12.7 | 14.2 |
| 9.0 | 120-90 | 6.6 | 6.9 | 7.8 | 9.0 | 10.3 | 11.6 | 13.0 |
| 12.0 | 120-90 | 5.1 | 5.5 | 6.1 | 7.0 | 8.0 | 9.1 | 10.2 |
| 15.0 | 120-90 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 | •0.5 |
| 18.0+ | 120-90 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  |  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 25:  FUEL MODEL 3―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 6 | 52 | 121 | 201 | 290 | 387 | 490 |
| 6.0 | 5 | 39 | 89 | 148 | 214 | 286 | 361 |
| 9.0 | 4 | 32 | 73 | 122 | 176 | 234 | 296 |
| 12.0 | 3 | 28 | 64 | 107 | 154 | 206 | 260 |
| 15.0 | 3 | 25 | 57 | 95 | 137 | 182 | 213 |
| 18.0 | 2 | 20 | 47 | 79 | 114 | 151 | 191 |
| 21.0 | 2 | 14 | 32 | 53 | 77 | 103 | 130 |
|  | Flame Length/Feet |
| 3.0 | 3.8 | 10.1 | 14.8 | 18.7 | 22.2 | 25.3 | 28.2 |
| 6.0 | 3.0 | 8.0 | 11.8 | 14.9 | 17.7 | 20.2 | 22.5 |
| 9.0 | 2.6 | 7.0 | 10.3 | 13.0 | 15.4 | 17.6 | 19.6 |
| 12.0 | 2.4 | 6.5 | 9.5 | 12.1 | 14.3 | 16.3 | 18.2 |
| 15.0 | 2.2 | 6.0 | 8.9 | 11.2 | 13.3 | 15.2 | 16.9 |
| 18.0 | 2.0 | 5.3 | 7.7 | 9.8 | 11.6 | 13.2 | 14.7 |
| 21.0 | 1.4 | 3.8 | 5.6 | 7.1 | 8.4 | 9.6 | 10.7 |

TABLE 26: FUEL MODEL 3―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 26 | 72 | 140 | 221 | 310 | 407 | 510 |
| 6.0 | 19 | 53 | 103 | 163 | 229 | 300 | 376 |
| 9.0 | 16 | 43 | 85 | 133 | 187 | 246 | 308 |
| 12.0 | 14 | 38 | 75 | 117 | 165 | 216 | 271 |
| 15.0 | 12 | 34 | 66 | 104 | 146 | 192 | 240 |
| 18.0 | 10 | 28 | 55 | 86 | 121 | 159 | 199 |
| 21.0 | 7 | 19 | 37 | 59 | 82 | 108 | 135 |
|  | Flame Length/Feet |
| 3.0 | 7.3 | 11.7 | 15.9 | 19.6 | 22.9 | 25.9 | 28.7 |
| 6.0 | 5.8 | 9.3 | 12.6 | 15.6 | 18.2 | 20.6 | 22.9 |
| 9.0 | 5.0 | 8.1 | 11.0 | 13.6 | 15.9 | 18.0 | 19.9 |
| 12.0 | 4.7 | 7.5 | 10.2 | 12.6 | 14.7 | 16.7 | 18.5 |
| 15.0 | 4.4 | 7.0 | 9.5 | 11.7 | 13.7 | 15.5 | 17.2 |
| 18.0 | 3.8 | 6.1 | 8.3 | 10.2 | 11.9 | 13.5 | 15.0 |
| 21.0 | 2.7 | 4.4 | 6.0 | 7.4 | 8.6 | 9.8 | 10.9 |

TABLE 27:  FUEL MOEL 3―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 50 | 96 | 165 | 245 | 334 | 431 | 534 |
| 6.0 | 37 | 71 | 122 | 181 | 247 | 318 | 394 |
| 9.0 | 30 | 58 | 100 | 148 | 202 | 261 | 323 |
| 12.0 | 27 | 51 | 88 | 130 | 178 | 229 | 284 |
| 15.0 | 24 | 45 | 78 | 116 | 158 | 203 | 252 |
| 18.0 | 20 | 38 | 64 | 96 | 131 | 168 | 209 |
| 21.0 | 13 | 26 | 44 | 65 | 89 | 115 | 142 |
|  | Flame Length/Feet |
| 3.0 | 9.9 | 13.4 | 17.1 | 20.5 | 23.7 | 26.6 | 29.4 |
| 6.0 | 7.9 | 10.6 | 13.6 | 16.3 | 18.8 | 21.2 | 23.4 |
| 9.0 | 6.9 | 9.3 | 11.9 | 14.2 | 16.4 | 18.5 | 20.4 |
| 12.0 | 6.4 | 8.6 | 11.0 | 13.2 | 15.2 | 17.1 | 18.9 |
| 15.0 | 5.9 | 8.0 | 10.2 | 12.3 | 14.2 | 15.9 | 17.6 |
| 18.0 | 5.2 | 7.0 | 8.9 | 10.7 | 12.4 | 13.9 | 15.3 |
| 21.0 | 3.7 | 5.1 | 6.5 | 7.8 | 9.0 | 10.1 | 11.1 |

TABLE 28:  FUEL MODEL3―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 84 | 131 | 199 | 279 | 369 | 465 | 568 |
| 6.0 | 62 | 96 | 147 | 206 | 272 | 343 | 419 |
| 9.0 | 51 | 79 | 120 | 169 | 223 | 281 | 344 |
| 12.0 | 45 | 69 | 106 | 149 | 196 | 247 | 302 |
| 15.0 | 40 | 62 | 94 | 132 | 174 | 219 | 268 |
| 18.0 | 33 | 51 | 78 | 109 | 144 | 182 | 222 |
| 21.0 | 22 | 35 | 53 | 74 | 98 | 124 | 151 |
|  | Flame Length/Feet |
| 3.0 | 12.6 | 15.4 | 18.7 | 21.8 | 24.8 | 27.6 | 30.2 |
| 6.0 | 10.0 | 12.2 | 14.8 | 17.3 | 19.7 | 21.9 | 24.0 |
| 9.0 | 8.7 | 10.7 | 12.9 | 15.1 | 17.2 | 19.1 | 21.0 |
| 12.0 | 8.1 | 9.9 | 12.0 | 14.0 | 15.9 | 17.7 | 19.4 |
| 15.0 | 7.5 | 9.2 | 11.2 | 13.0 | 14.8 | 16.5 | 18.1 |
| 18.0 | 6.6 | 8.0 | 0.76 | 11.4 | 12.9 | 14.4 | 15.8 |
| 21.0 | 4.8 | 5.8 | 7.1 | 8.2 | 9.4 | 10.4 | 11.4 |

TABLE 29:  FUEL MODEL 3―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 182 | 228 | 297 | 377 | 467 | 563 | 666 |
| 6.0 | 134 | 168 | 219 | 278 | 344 | 415 | 491 |
| 9.0 | 110 | 138 | 179 | 228 | 282 | 341 | 403 |
| 12.0 | 97 | 121 | 158 | 201 | 248 | 299 | 354 |
| 15.0 | 86 | 108 | 140 | 178 | 220 | 266 | 314 |
| 18.0 | 71 | 89 | 116 | 147 | 182 | 220 | 260 |
| 21.0 | 48 | 61 | 79 | 100 | 124 | 150 | 177 |
|  | Flame Length/Feet |
| 3.0 | 17.9 | 19.9 | 22.4 | 25.0 | 27.6 | 30.1 | 32.5 |
| 6.0 | 14.3 | 15.8 | 17.8 | 19.9 | 22.0 | 23.9 | 25.9 |
| 9.0 | 12.4 | 13.8 | 15.6 | 17.4 | 19.2 | 20.9 | 22.6 |
| 12.0 | 11.5 | 12.8 | 14.4 | 16.1 | 17.7 | 19.4 | 20.9 |
| 15.0 | 10.7 | 11.9 | 13.4 | 15.0 | 16.5 | 18.0 | 19.5 |
| 18.0 | 9.3 | 10.4 | 11.7 | 13.1 | 14.4 | 15.7 | 17.0 |
| 21.0 | 6.8 | 7.5 | 8.5 | 9.5 | 10.4 | 11.4 | 12.3 |

TABLE 30:  FUEL MODEL 4―0% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 5 | 24-29 | 56-70 | 97-120 | 143-178 | 195-243 | 252-313 |
| 6.0 | 120-90 | 4 | 21-25 | 49-61 | 85-104 | 126-155 | 171-211 | 221-272 |
| 9.0 | 120-90 | 4 | 19-23 | 46-56 | 79-96 | 117-143 | 160-194 | 206-250 |
| 12.0 | 120-90 | 4 | 18-22 | 43-53 | 74-90 | 110-134 | 149-183 | 192-235 |
| 15.0 | 120-90 | 3 | 12-19 | 28-46 | 47-78 | 70-116 | 96-158 | 124-204 |
| 18.0+ | 120-90 | 1 | 6 | 11-13 | 19-23 | 29-34 | 39-46 | 51-60 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 5.7 | 12-13 | 18-20 | 23-25 | 27-31 | 32-35 | 35-40 |
| 6.0 | 120-90 | 5.1 | 11-12 | 16-18 | 20-23 | 25-27 | 28-32 | 32-35 |
| 9.0 | 120-90 | 4.8 | 10-11 | 15-17 | 19-21 | 23-26 | 27-30 | 30-33 |
| 12.0 | 120-90 | 4.6 | 10-11 | 14-16 | 18-20 | 22-24 | 25-28 | 28-32 |
| 15.0 | 120-90 | 3-4 | 6-10 | 10-14 | 12-18 | 15-22 | 17-25 | 19-28 |
| 18.0+ | 120-90 | 1 | 3 | 4-5 | 6 | 7 | 8 | 9 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

TABLE 31:  FUEL MODEL 4―30% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 15-18 | 34-42 | 67-83 | 107-133 | 154-191 | 206-256 | 262-326 |
| 6.0 | 120-90 | 13-16 | 30-37 | 58-72 | 94-116 | 135-166 | 180-222 | 230-283 |
| 9.0 | 120-90 | 12-14 | 28-34 | 55-66 | 88-107 | 126-153 | 168-205 | 215-261 |
| 12.0 | 120-90 | 11-14 | 26-32 | 51-62 | 82-100 | 118-144 | 157-192 | 200-245 |
| 15.0 | 120-90 | 7-12 | 17-28 | 33-54 | 53-87 | 76-125 | 101-167 | 129-213 |
| 18.0+ | 120-90 | 3 | 8 | 13-16 | 22-25 | 31-37 | 41-49 | 53-62 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 10-11 | 14-16 | 19-22 | 24-27 | 28-32 | 32-36 | 36-40 |
| 6.0 | 120-90 | 9 | 13-14 | 17-19 | 21-24 | 25-28 | 29-32 | 32-36 |
| 9.0 | 120-90 | 8-9 | 12-13 | 16-18 | 20-22 | 24-26 | 28-30 | 31-34 |
| 12.0 | 120-90 | 8 | 11-13 | 16-17 | 19-21 | 23-25 | 26-29 | 29-32 |
| 15.0 | 120-90 | 5-8 | 8-11 | 10-15 | 13-19 | 15-22 | 18-26 | 20-29 |
| 18.0+ | 120-90 | 2 | 4 | 5 | 6 | 7 | 8 | 9 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

TABLE 32:  FUEL MODEL 4―45% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 27-34 | 47-58 | 80-99 | 120-149 | 167-207 | 219-272 | 275-342 |
| 6.0 | 120-90 | 24-30 | 41-51 | 70-86 | 105-130 | 146-180 | 192-236 | 241-297 |
| 9.0 | 120-90 | 23-27 | 38-47 | 65-79 | 98-119 | 137-166 | 179-218 | 225-274 |
| 12.0 | 120-90 | 21-26 | 36-44 | 61-74 | 92-112 | 127-156 | 167-204 | 210-257 |
| 15.0 | 120-90 | 14-22 | 23-38 | 39-65 | 59-97 | 82-135 | 107-177 | 135-223 |
| 18.0+ | 120-90 | 7 | 9-11 | 16-19 | 24-29 | 34-40 | 44-52 | 55-65 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 13-14 | 16-18 | 21-23 | 25-28 | 29-33 | 33-37 | 37-41 |
| 6.0 | 120-90 | 12-13 | 15-16 | 19-21 | 23-25 | 26-29 | 30-33 | 33-37 |
| 9.0 | 120-90 | 11-12 | 14-15 | 18-20 | 21-24 | 25-28 | 28-31 | 31-35 |
| 12.0 | 120-90 | 10-11 | 13-15 | 17-19 | 20-13 | 24-26 | 27-30 | 30-33 |
| 15.0 | 120-90 | 7-10 | 9-13 | 11-17 | 14-20 | 16-23 | 18-26 | 20-28 |
| 18.0+ | 120-90 | 3 | 4 | 5 | 6 | 7 | 8 | 8-9 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

TABLE 33: FUEL MODEL 4―60% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 26-57 | 65-81 | 98-121 | 138-172 | 185-230 | 237-294 | 293-365 |
| 6.0 | 120-90 | 40-49 | 57-70 | 86-105 | 121-149 | 162-200 | 207-256 | 257-316 |
| 9.0 | 120-90 | 37-45 | 53-65 | 80-97 | 113-138 | 151-184 | 194-236 | 240-292 |
| 12.0 | 120-90 | 35-43 | 50-61 | 75-91 | 106-129 | 141-173 | 181-221 | 224-274 |
| 15.0 | 120-90 | 22-37 | 32-53 | 48-79 | 68-112 | 91-150 | 116-192 | 144-238 |
| 18.0+ | 120-90 | 9-11 | 13-15 | 20-23 | 28-33 | 37-44 | 48-56 | 59-70 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 16-18 | 19-21 | 23-26 | 27-30 | 31-34 | 34-39 | 38-43 |
| 6.0 | 120-90 | 14-16 | 17-19 | 20-23 | 24-27 | 28-31 | 31-34 | 34-38 |
| 9.0 | 120-90 | 14-15 | 16-18 | 20-22 | 23-25 | 26-29 | 20-32 | 32-36 |
| 12.0 | 120-90 | 13-14 | 15-17 | 18-20 | 22-24 | 25-28 | 28-31 | 31-34 |
| 15.0 | 120-90 | 9-13 | 10-15 | 12-18 | 15-21 | 17-24 | 19-27 | 21-30 |
| 18.0+ | 120-90 | 4 | 5 | 6 | 7 | 8 | 9 | 9 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

TABLE 34:  FUEL MODEL 4―90% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 98-121 | 117-146 | 150-186 | 190-236 | 237-294 | 238-359 | 345-429 |
| 6.0 | 120-90 | 86-105 | 103-126 | 131-162 | 167-205 | 208-256 | 253-312 | 302-373 |
| 9.0 | 120-90 | 80-97 | 96-117 | 123-149 | 156-189 | 194-236 | 237-287 | 283-344 |
| 12.0 | 120-90 | 75-91 | 90-109 | 114-140 | 145-178 | 181-221 | 221-270 | 264-323 |
| 15.0 | 120-90 | 48-79 | 58-95 | 74-122 | 93-154 | 116-192 | 142-234 | 170-280 |
| 18.0+ | 120-90 | 20-23 | 24-28 | 30-36 | 38-45 | 48-56 | 58-69 | 70-82 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 23-26 | 25-28 | 28-31 | 31-35 | 34-39 | 38-42 | 41-46 |
| 6.0 | 120-90 | 20-23 | 22-25 | 25-28 | 28-31 | 31-34 | 34-38 | 37-41 |
| 9.0 | 120-90 | 20-22 | 21-23 | 24-26 | 26-29 | 29-32 | 32-35 | 35-38 |
| 12.0 | 120-90 | 18-20 | 20-22 | 23-25 | 25-28 | 28-31 | 30-34 | 33-37 |
| 15.0 | 120-90 | 12-18 | 14-205 | 15-22 | 17-25 | 19-27 | 20-30 | 22-33 |
| 18.0+ | 120-90 | 6 | 6 | 7 | 8 | 0 | 8-9 | 10-11 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

TABLE 35:  FUEL MODEL 5―0% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 1 | 7-10 | 16-23 | 28-39 | 42-58 | 56-78 | 72-100 |
| 6.0 | 120-90 | 1 | 4-8 | 9-20 | 16-34 | 24-50 | 32-67 | 42-87 |
| 9.0 | 120-90 | 1 | 2-5 | 6-13 | 10-22 | 14-32 | 19-44 | 20•-56 |
| 12.0 | 120-90 | 0 | 2-3 | 5-6 | 9-11 | 13-16 | •18-•22 | •18-•22 |
| 15.0 | 120-90 | 0 | 2 | 4-5 | 8-9 | 11-14 | •12-•15 | •12-•15 |
| 18.0+ | 120-90 | 0 | 1 | 3 | •4 | •4 | •4 | •4 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 1-2 | 3-4 | 5-6 | 7-8 | 8-10 | 9-11 | 10-12 |
| 6.0 | 120-90 | 1 | 2-4 | 3-6 | 4-7 | 5-8 | 6-10 | 6-11 |
| 9.0 | 120-90 | 1 | 1-2 | 2-4 | 2-5 | 3-6 | 3-7 | •3-7 |
| 12.0 | 120-90 | 1 | 1 | 2 | 2 | 3 | •3 | •3-•4 |
| 15.0 | 120-90 | 1 | 1 | 2 | 2 | 3 | •3 | •3 |
| 18.0+ | 120-90 | <1 | 1 | 1 | •1 | •1 | •1 | •1 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 36:  FUEL MODEL 5―30% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 4-5 | 10-14 | 19-27 | 31-43 | 44-62 | 59-82 | 75-104 |
| 6.0 | 120-90 | 2-5 | 6-12 | 11-23 | 18-37 | 26-53 | 34-71 | 43-90 |
| 9.0 | 120-90 | 1-3 | 3-8 | 7-15 | 10-24 | 15-35 | 20•-46 | •20-59 |
| 12.0 | 120-90 | 1-2 | 3-4 | 6-8 | 10-12 | 14-17 | 18•-22• | •18-•22 |
| 15.0 | 120-90 | 1 | 3 | 5-6 | 9-10 | •12-•15 | •12-•15 | •12-•15 |
| 18.0+ | 120-90 | 1 | 2 | 3-•4 | •4 | •4 | •4 | •4 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 3 | 4-5 | 6-7 | 7-8 | 8-10 | 9-11 | 10-13 |
| 6.0 | 120-90 | 2-3 | 2-4 | 3-6 | 4-7 | 5-9 | 6-10 | 6-11 |
| 9.0 | 120-90 | 1-2 | 2-3 | 2-4 | 3-5 | 3-6 | •3-7 | •3-8 |
| 12.0 | 120-90 | 1 | 1-2 | 2 | 3 | 3 | •3 | •3 |
| 15.0 | 120-90 | 1 | 1 | 2 | 2 | •3 | •3 | •3 |
| 18.0+ | 120-90 | 1 | 1 | •1 | •1 | •1 | •1 | •1 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 37:  FUEL MODEL 5―45% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 8-11 | 13-19 | 23-32 | 35-48 | 48-67 | 63-87 | 79-109 |
| 6.0 | 120-90 | 4-9 | 8-16 | 13-28 | 20-42 | 28-58 | 36-75 | 45-94 |
| 9.0 | 120-90 | 3-6 | 5-10 | 8-18 | 12-27 | 16-37 | •20-49 | •20-61 |
| 12.0 | 120-90 | 2-3 | 4-5 | 7-9 | 11-14 | 15-19 | •18-•22 | •18-•22 |
| 15.0 | 120-90 | 2-3 | 4 | 6-8 | 10-12 | •12-•15 | •12-•15 | •12-•15 |
| 18.0+ | 120-90 | 1 | 2-3 | •4 | •4 | •4 | •4 | •4 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 4 | 5 | 6-7 | 7-9 | 8-10 | 10-12 | 11-13 |
| 6.0 | 120-90 | 2-4 | 3-5 | 4-6 | 4-8 | 5-9 | 6-10 | 6-11 |
| 9.0 | 120-90 | 1-3 | 2-3 | 2-4 | 3-5 | 3-6 | •3-7 | •3-8 |
| 12.0 | 120-90 | 1 | 2 | 2 | 3 | 3 | •3 | •3 |
| 15.0 | 120-90 | 1 | 2 | 2 | 2 | •2 | •2 | •2 |
| 18.0+ | 120-90 | 1 | 1 | •1 | •1 | •1 | •1 | •1 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 38:  FUEL MODEL 5―60% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 13-18 | 19-26 | 28-39 | 40-55 | 53-74 | 68-94 | 84-117 |
| 6.0 | 120-90 | 7-15 | 11-22 | 16-34 | 23-48 | 31-64 | 39-81 | 48-101 |
| 9.0 | 120-90 | 4-10 | 6-14 | 10-22 | 13-31 | 18-41 | •20-53 | •20-65 |
| 12.0 | 120-90 | 4-5 | 6-7 | 9-11 | 13-16 | 17-21 | •18-•22 | •18-•22 |
| 15.0 | 120-90 | 3-4 | 5-6 | 8-9 | 11-13 | •12-•15 | •12-•15 | •12-•15 |
| 18.0+ | 120-90 | 2 | •4 | •4 | •4 | •4 | •4 | •4 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 5-6 | 5-7 | 7-10 | 8-10 | 9-11 | 10-12 | 11-13 |
| 6.0 | 120-90 | 3-5 | 3-6 | 4-7 | 5-8 | 5-10 | 6-11 | 7-12 |
| 9.0 | 120-90 | 2-3 | 2-4 | 2-5 | 3-6 | 3-6 | •3-7 | •3-8 |
| 12.0 | 120-90 | 2 | 2 | 2-3 | 3 | •4 | •4 | •4 |
| 15.0 | 120-90 | 1-2 | 2 | 2 | 2-3 | •3 | •3 | •3 |
| 18.0+ | 120-90 | 1 | 1 | •1 | •1 | •1 | •1 | •1 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 39:  FUEL MODEL 5―90% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 27-38 | 33-46 | 43-59 | 54-76 | 68-94 | 83-115 | 99-137 |
| 6.0 | 120-90 | 16-33 | 19-40 | 25-51 | 31-65 | 39-81 | 48-99 | 57-118 |
| 9.0 | 120-90 | 9-21 | 11-26 | 14-33 | 18-42 | •20-53 | •20-64 | •20-77 |
| 12.0 | 120-90 | 9-11 | 11-13 | 14-17 | 17-21 | •18-•22 | •18-•22 | •18-•22 |
| 15.0 | 120-90 | 7-9 | 9-11 | •12-•14 | •12-•15 | •12-•15 | •12-•15 | •12-•15 |
| 18.0+ | 120-90 | •4 | •4 | •4 | •4 | •4 | •4 | •4 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 7-8 | 7-9 | 8-10 | 9-11 | 10-12 | 11-13 | 12-14 |
| 6.0 | 120-90 | 4-7 | 4-8 | 5-9 | 5-10 | 6-11 | 6-12 | 7-13 |
| 9.0 | 120-90 | 2-5 | 3-5 | 3-6 | 3-6 | •3-7 | •3-8 | •3-9 |
| 12.0 | 120-90 | 2 | 2-3 | 3 | •4 | •4 | •4 | •4 |
| 15.0 | 120-90 | 2 | 2 | •3 | •3 | •3 | •3 | •3 |
| 18.0+ | 120-90 | •1 | •1 | •1 | •1 | •1 | •1 | •1 |
| 21.0 | 120-90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 2 | 15 | 33 | 56 | 81 | 109 | 138 |
| 6.0 | 2 | 11 | 25 | 43 | 62 | 83 | 105 |
| 9.0 | 1 | 9 | 21 | 35 | 52 | 69 | 88 |
| 12.0 | 1 | 8 | 19 | 31 | 45 | 61 | 77 |
| 15.0 | 1 | 7 | 17 | 28 | 41 | 55 | 69 |
| 18.0 | 1 | 6 | 15 | 24 | 35 | 47 | 60 |
| 21.0 | 1 | 6 | 11 | 19 | 28 | 37 | 47 |
|  | Flame Length/Feet |
| 3.0 | 1.9 | 4.5 | 6.5 | 8.3 | 9.8 | 11.3 | 12.6 |
| 6.0 | 1.6 | 3.7 | 5.4 | 6.8 | 8.1 | 9.2 | 10.3 |
| 9.0 | 1.4 | 3.2 | 4.7 | 6.0 | 7.1 | 8.2 | 9.1 |
| 12.0 | 1.3 | 3.0 | 4.4 | 5.6 | 6.6 | 7.6 | 8.5 |
| 15.0 | 1.2 | 2.8 | 4.1 | 5.2 | 6.2 | 7.1 | 7.9 |
| 18.0 | 1.1 | 2.6 | 3.8 | 4.8 | 5.7 | 6.5 | 7.2 |
| 21.0 | 0.9 | 2.1 | 3.1 | 3.9 | 4.7 | 5.3 | 6.0 |

TABLE 40:  FUEL MODEL 5―90% SLOPE

TABLE 41:  FUEL MODEL 6—45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 15 | 28 | 47 | 69 | 94 | 122 | 151 |
| 6.0 | 12 | 21 | 36 | 53 | 72 | 93 | 115 |
| 9.0 | 10 | 18 | 30 | 44 | 60 | 77 | 96 |
| 12.0 | 9 | 16 | 26 | 49 | 53 | 68 | 85 |
| 15.0 | 8 | 14 | 23 | 35 | 47 | 61 | 76 |
| 18.0 | 7 | 12 | 20 | 30 | 41 | 53 | 66 |
| 21.0 | 5 | 9 | 16 | 24 | 32 | 42 | 52 |
|  | Flame Length/Feet |
| 3.0 | 4.6 | 6.0 | 7.6 | 9.1 | 10.6 | 11.9 | 13.1 |
| 6.0 | 3.8 | 4.9 | 6.3 | 7.5 | 8.7 | 9.7 | 10.8 |
| 9.0 | 3.3 | 4.4 | 5.5 | 6.6 | 7.6 | 8.6 | 9.5 |
| 12.0 | 3.1 | 4.0 | 5.1 | 6.2 | 7.1 | 8.0 | 8.8 |
| 15.0 | 2.9 | 3.8 | 4.8 | 5.8 | 6.7 | 7.5 | 8.3 |
| 18.0 | 2.6 | 3.5 | 4.4 | 5.3 | 6.1 | 6.8 | 7.5 |
| 21.0 | 2.2 | 2.8 | 3.6 | 4.3 | 5.0 | 5.6 | 6.2 |

TABLE 42:  FUEL MODEL 6—60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 26 | 38 | 57 | 79 | 105 | 132 | 161 |
| 6.0 | 20 | 29 | 43 | 61 | 80 | 101 | 123 |
| 9.0 | 16 | 24 | 36 | 50 | 66 | 84 | 103 |
| 12.0 | 14 | 21 | 32 | 44 | 59 | 74 | 91 |
| 15.0 | 13 | 19 | 29 | 30 | 53 | 66 | 81 |
| 18.0 | 11 | 17 | 25 | 35 | 46 | 58 | 70 |
| 21.0 | 9 | 13 | 19 | 27 | 36 | 45 | 54• |
|  | Flame Length/Feet |
| 3.0 | 5.8 | 7.0 | 8.4 | 9.8 | 11.1 | 12.3 | 13.5 |
| 6.0 | 4.8 | 5.7 | 6.9 | 8.0 | 9.1 | 10.1 | 11.1 |
| 9.0 | 4.2 | 5.0 | 6.1 | 7.1 | 8.0 | 8.9 | 9.8 |
| 12.0 | 3.9 | 4.7 | 5.6 | 6.6 | 7.4 | 8.3 | 9.1 |
| 15.0 | 3.7 | 4.4 | 5.3 | 6.2 | 7.0 | 7.8 | 8.5 |
| 18.0 | 3.3 | 4.0 | 4.8 | 5.6 | 6.4 | 7.1 | 7.8 |
| 21.0 | 2.8 | 3.3 | 4.0 | 4.6 | 5.2 | 5.8 | 6.3• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 43:  FUEL MODEL 6—90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 55 | 67 | 86 | 109 | 134 | 161 | 191 |
| 6.0 | 42 | 51 | 66 | 83 | 102 | 123 | 146 |
| 9.0 | 35 | 43 | 55 | 69 | 85 | 103 | 121 |
| 12.0 | 31 | 38 | 48 | 61 | 75 | 90 | 107 |
| 15.0 | 28 | 34 | 43 | 55 | 67 | 81 | 96 |
| 18.0 | 24 | 29 | 38 | 47 | 58 | 70 | 83 |
| 21.0 | 19 | 23 | 29 | 37 | 46 | 54• | 54• |
|  | Flame Length/Feet |
| 3.0 | 8.2 | 9.0 | 10.1 | 11.3 | 12.4 | 13.5 | 14.6 |
| 6.0 | 6.8 | 7.4 | 8.3 | 9.2 | 10.2 | 11.1 | 12.0 |
| 9.0 | 6.0 | 6.6 | 7.3 | 8.2 | 9.0 | 9.8 | 10.6 |
| 12.0 | 5.5 | 6.1 | 6.8 | 7.6 | 8.3 | 9.1 | 9.8 |
| 15.0 | 5.2 | 5.7 | 6.4 | 7.1 | 7.8 | 8.5 | 9.2 |
| 18.0 | 4.7 | 5.2 | 5.8 | 6.5 | 7.1 | 7.8 | 8.4 |
| 21.0 | 3.9 | 4.3 | 4.8 | 5.3 | 5.9 | 6.5• | 6.3• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 44:  FUEL MODEL 7—0% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 1-2 | 10-11 | 23-26 | 38-44 | 55-64 | 74-85 | 94-109 |
| 6.0 | 120-90 | 1 | 9-10 | 20-23 | 33-38 | 48-55 | 64-73 | 81-93 |
| 9.0 | 120-90 | 1 | 8-9 | 17-20 | 29-33 | 42-48 | 56-65 | 72-82 |
| 12.0 | 120-90 | 1 | 7-8 | 16-18 | 26-30 | 38-44 | 51-59 | 65-74 |
| 15.0 | 120-90 | 1 | 6-7 | 15-17 | 24-28 | 35-40 | 47-54 | 60-69 |
| 18.0+ | 120-90 | 1 | 6-7 | 14-16 | 23-26 | 33-38 | 45-51 | 57-64 |
| 21.0 | 120-90 | 1 | 6 | 13-15 | 22-25 | 32-36 | 42-48 | 54-61 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 2 | 4 | 6 | 7-8 | 8-9 | 10 | 11-12 |
| 6.0 | 120-90 | 1 | 3-4 | 5 | 6-7 | 8 | 9 | 10 |
| 9.0 | 120-90 | 1 | 3 | 5 | 6 | 7 | 8 | 9 |
| 12.0 | 120-90 | 1 | 3 | 4-5 | 5-6 | 6-7 | 7-8 | 8-9 |
| 15.0 | 120-90 | 1 | 3 | 4 | 5-6 | 6-7 | 7 | 8 |
| 18.0+ | 120-90 | 1 | 3 | 4 | 5 | 6 | 7 | 8 |
| 21.0 | 120-90 | 1 | 3 | 4 | 5 | 6 | 7 | 7-8 |

TABLE 45:  FUEL MODEL 7—30% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 5-6 | 14-16 | 27-31 | 42-49 | 59-68 | 78-90 | 98-113 |
| 6.0 | 120-90 | 5 | 12-14 | 23-26 | 36-42 | 51-59 | 67-77 | 84-97 |
| 9.0 | 120-90 | 4-5 | 11-12 | 20-23 | 32-37 | 45-52 | 59-68 | 75-86 |
| 12.0 | 120-90 | 4 | 10-11 | 18-21 | 29-33 | 41-47 | 54-62 | 68-77 |
| 15.0 | 120-90 | 3-4 | 9-10 | 17-20 | 27-31 | 38-43 | 50-57 | 63-72 |
| 18.0+ | 120-90 | 3-4 | 8-9 | 16-18 | 25-29 | 36-41 | 47-53 | 59-67 |
| 21.0 | 120-90 | 3 | 8-9 | 15-17 | 24-27 | 34-38 | 45-50 | 56-63 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 3 | 4-5 | 6 | 7-8 | 9 | 10-11 | 11-12 |
| 6.0 | 120-90 | 3 | 4 | 5-6 | 7 | 8 | 9-10 | 10 |
| 9.0 | 120-90 | 2 | 4 | 5 | 6 | 7-8 | 8-9 | 9-10 |
| 12.0 | 120-90 | 2 | 4 | 5 | 6 | 7 | 8 | 9 |
| 15.0 | 120-90 | 2 | 3 | 4-5 | 5-6 | 6-7 | 7-8 | 8 |
| 18.0+ | 120-90 | 2 | 3 | 4 | 5-61 | 6 | 7 | 8 |
| 21.0 | 120-90 | 2 | 3 | 4 | 5 | 6 | 7 | 7-8 |

TABLE 46:  FUEL MODEL 7―45% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 10-12 | 19-22 | 32-37 | 47-54 | 64-74 | 83-96 | 103-119 |
| 6.0 | 120-90 | 9-10 | 16-19 | 27-31 | 40-47 | 55-64 | 71-82 | 89-102 |
| 9.0 | 120-90 | 8-9 | 16-14 | 24-28 | 36-41 | 49-56 | 63-72 | 78-90 |
| 12.0 | 120-90 | 7-8 | 13-15 | 22-25 | 33-37 | 44-51 | 57-66 | 71-81 |
| 15.0 | 120-90 | 7 | 12-14 | 20-23 | 30-34 | 41-47 | 53-61 | 66-75 |
| 18.0+ | 120-90 | 6-7 | 11-13 | 19-22 | 28-32 | 39-44 | 50-57 | 62-70 |
| 21.0 | 120-90 | 6-7 | 11-12 | 18-20 | 27-30 | 37-42 | 47-54 | 59-67 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 4 | 5-6 | 6-7 | 8 | 9-10 | 10-11 | 11-12 |
| 6.0 | 120-90 | 4 | 5 | 6 | 7-8 | 8-9 | 9-10 | 10-11 |
| 9.0 | 120-90 | 3 | 4 | 5-6 | 6-7 | 7-8 | 8-9 | 9-10 |
| 12.0 | 120-90 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| 15.0 | 120-90 | 3 | 4 | 5 | 6 | 7 | 7-8 | 8-9 |
| 18.0+ | 120-90 | 3 | 4 | 5 | 5-6 | 6-7 | 7-8 | 8 |
| 21.0 | 120-90 | 3 | 3-4 | 4-5 | 5-6 | 6 | 7 | 8 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 47:  FUEL MODEL 7―60% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 17-20 | 26-30 | 38-44 | 54-62 | 71-82 | 90-104 | 109-127 |
| 6.0 | 120-90 | 15-17 | 22-25 | 33-38 | 46-53 | 61-70 | 77-89 | 95-109 |
| 9.0 | 120-90 | 13-15 | 20-22 | 29-34 | 41-47 | 54-62 | 68-79 | 84-96 |
| 12.0 | 120-90 | 12-14 | 18-20 | 27-30 | 37-43 | 49-56 | 62-71 | 76-87 |
| 15.0 | 120-90 | 11-13 | 16-19 | 25-28 | 35-36 | 46-52 | 58-66 | 70-80 |
| 18.0+ | 120-90 | 10-12 | 15-18 | 23-26 | 32-37 | 43-49 | 54-61 | 66-75 |
| 21.0 | 120-90 | 10-11 | 15-17 | 22-25 | 31-35 | 41-46 | 51-58 | 63-71 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 5 | 6 | 7-8 | 8-9 | 10 | 11 | 12 |
| 6.0 | 120-90 | 4-5 | 5-6 | 6-7 | 7-8 | 8-9 | 9-10 | 10-11 |
| 9.0 | 120-90 | 4 | 5 | 6 | 7 | 8 | 9 | 9-10 |
| 12.0 | 120-90 | 4 | 4-5 | 5-6 | 6-7 | 7-8 | 8-9 | 9 |
| 15.0 | 120-90 | 4 | 4-5 | 5-6 | 6 | 7 | 8 | 8-9 |
| 18.0+ | 120-90 | 3-4 | 4 | 5 | 6 | 7 | 7-8 | 8-9 |
| 21.0 | 120-90 | 3-4 | 4 | 5 | 6 | 6-7 | 7-8 | 8 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 48:  FUEL MODEL 7―90% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 37-42 | 45-51 | 58-67 | 73-85 | 90-105 | 109-126 | 129-149 |
| 6.0 | 120-90 | 32-36 | 39-45 | 50-58 | 63-73 | 78-90 | 94-109 | 111-128 |
| 9.0 | 120-90 | 28-32 | 35-40 | 44-51 | 56-64 | 69-79 | 83-96 | 99-113 |
| 12.0 | 120-90 | 25-29 | 31-36 | 40-46 | 51-58 | 63-72 | 76-87 | 90-102 |
| 15.0 | 120-90 | 24-27 | 29-33 | 37-42 | 47-54 | 58-66 | 70-80 | 83-94 |
| 18.0+ | 120-90 | 22-25 | 27-31 | 35-40 | 44-50 | 55-62 | 66-75 | 78-89 |
| 21.0 | 120-90 | 21-24 | 26-29 | 33-38 | 42-48 | 52-59 | 63-71 | 74-84 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 7-8 | 8 | 9 | 10 | 11 | 12 | 12-13 |
| 6.0 | 120-90 | 6-7 | 7 | 8 | 9 | 9-10 | 10-11 | 11-12 |
| 9.0 | 120-90 | 6 | 6-7 | 7-8 | 8 | 9 | 9-10 | 10-11 |
| 12.0 | 120-90 | 5-6 | 6 | 6-7 | 7-8 | 8-9 | 9 | 10 |
| 15.0 | 120-90 | 5 | 6 | 6-7 | 7 | 8 | 8-9 | 9-10 |
| 18.0+ | 120-90 | 5 | 5-6 | 6 | 7 | 7-8 | 8 | 9 |
| 21.0 | 120-90 | 5 | 5-6 | 6 | 6-7 | 7-8 | 8 | 8-9 |
|  |  | • MEANS YOU HIT THE WIND LIMIT |

TABLE 49:  FUEL MODEL 8―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 0 | 1 | 2 | 3 | 5 | 7 | 8 |
| 6.0 | 0 | 1 | 2 | 3 | 4• | 5• | 5• |
| 9.0 | 0 | 1 | 1 | 2 | 3• | 3• | 3• |
| 12.0 | 0 | 0 | 1 | 2 | 3• | 3• | 3• |
| 15.0 | 0 | 0 | 1 | 2 | 2• | 2• | 2• |
| 18.0 | 0 | 0 | 1 | 1 | 2• | 2• | 2• |
| 21.0 | 0 | 0 | 1 | 1 | 2• | 2• | 2• |
|  | Flame Length/Feet |
| 3.0 | 0.5 | 0.8 | 1.2 | 1.5 | 1.8 | 2.1 | 2.2• |
| 6.0 | 0.4 | 0.7 | 1.0 | 1.2 | 1.5 | 1.6• | 1.6• |
| 9.0 | 0.4 | 0.6 | 0.8 | 1.1 | 1.3• | 1.3• | 1.3• |
| 12.0 | 0.3 | 0.5 | 0.8 | 1.0 | 1.2• | 1.2• | 1.2• |
| 15.0 | 0.3 | 0.5 | 0.7 | 0.9 | 1.1• | 1.1• | 1.1• |
| 18.0 | 0.3 | 0.5 | 0.7 | 0.9 | 1.0• | 1.0• | 1.0• |
| 21.0 | 0.3 | 0.4 | 0.6 | 0.8 | 0.9• | 0.9• | 0.9• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 50:  FUEL MODEL 8―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 1 | 1 | 2 | 4 | 5 | 7 | 8• |
| 6.0 | 1 | 1 | 2 | 3 | 4 | 5• | 5• |
| 9.0 | 0 | 1 | 1 | 2 | 3• | 3• | 3• |
| 12.0 | 0 | 1 | 1 | 2• | 3• | 3• | 3• |
| 15.0 | 0 | 1 | 1 | 2• | 2• | 2• | 2• |
| 18.0 | 0 | 1 | 1 | 2 | 2• | 2• | 2• |
| 21.0 | 0 | 0 | 1 | 1 | 2• | 2• | 2• |
|  | Flame Length/Feet |
| 3.0 | 0.7 | 1.0 | 1.3 | 1.6 | 1.9 | 2.1 | 2.2• |
| 6.0 | 0.6 | 0.8 | 1.0 | 1.3 | 1.5 | 1.6• | 1.6• |
| 9.0 | 0.5 | 0.7 | 0.9 | 1.1 | 1.3• | 1.3• | 1.3• |
| 12.0 | 0.5 | 0.6 | 0.8 | 1.0 | 1.2• | 1.2• | 1.2• |
| 15.0 | 0.4 | 0.6 | 0.8 | 1.0 | 1.1• | 1.1• | 1.1• |
| 18.0 | 0.4 | 0.6 | 0.7 | 0.9 | 1.0• | 1.0• | 1.0• |
| 21.0 | 0.4 | 0.5 | 0.7 | 0.8 | 0.9• | 0.9• | 0.9• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 51:  FUEL MODEL 8―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 1 | 2 | 3 | 4 | 6 | 8• | 8• |
| 6.0 | 1 | 1 | 2 | 3 | 5 | 5• | 5• |
| 9.0 | 1 | 1 | 2 | 3• | 3• | 3• | 3• |
| 12.0 | 1 | 1 | 2 | 2 | 3• | 3• | 3• |
| 15.0 | 1 | 1 | 1 | 2• | 2• | 2• | 2• |
| 18.0 | 1 | 1 | 1 | 2• | 2• | 2• | 2• |
| 21.0 | 0 | 1 | 1 | 2• | 2• | 2• | 2• |
|  | Flame Length/Feet |
| 3.0 | 0.9 | 1.1 | 1.4 | 1.7 | 1.9 | 2.2• | 2.2• |
| 6.0 | 0.8 | 0.9 | 1.1 | 1.4 | 1.6• | 1.6• | 1.6• |
| 9.0 | 0.7 | 0.8 | 1.0 | 1.2 | 1.3• | 1.3• | 1.3• |
| 12.0 | 0.6 | 0.7 | 0.9 | 1.1 | 1.2• | 1.2• | 1.2• |
| 15.0 | 0.6 | 0.7 | 0.9 | 1.0 | 1.1• | 1.1• | 1.1• |
| 18.0 | 0.5 | 0.6 | 0.8 | 1.0• | 1.0• | 1.0• | 1.0• |
| 21.0 | 0.5 | 0.6 | 0.7 | 0.9• | 0.9• | 0.9• | 0.9• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 52:  FUEL MODEL 8―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 2 | 3 | 4 | 5 | 7 | 8• | 8• |
| 6.0 | 1 | 2 | 3 | 4 | 5• | 5• | 5• |
| 9.0 | 1 | 2 | 2 | 3• | 3• | 3• | 3• |
| 12.0 | 1 | 1 | 2 | 3• | 3• | 3• | 3• |
| 15.0 | 1 | 1 | 2• | 2• | 2• | 2• | 2• |
| 18.0 | 1 | 1 | 2• | 2• | 2• | 2• | 2• |
| 21.0 | 1 | 1 | 1 | 2• | 2• | 2• | 2• |
|  | Flame Length/Feet |
| 3.0 | 1.2 | 1.3 | 1.5 | 1.8 | 2.1 | 2.2• | 2.2• |
| 6.0 | 0.9 | 1.1 | 1.3 | 1.5 | 1.6• | 1.6• | 1.6• |
| 9.0 | 0.8 | 0.9 | 1.1 | 1.3• | 1.3• | 1.3• | 1.3• |
| 12.0 | 0.7 | 0.8 | 1.0 | 1.2• | 1.2• | 1.2• | 1.2• |
| 15.0 | 0.7 | 0.8 | 0.9 | 1.1• | 1.1• | 1.1• | 1.1• |
| 18.0 | 0.7 | 0.8 | 0.9 | 1.0• | 1.0• | 1.0• | 1.0• |
| 21.0 | 0.6 | 0.7 | 0.8 | 0.9• | 0.9• | 0.9• | 0.9• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 53:  FUEL MODEL 8―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 4 | 5 | 6 | 7 | 8• | 8• | 8• |
| 6.0 | 3 | 3 | 4 | 5• | 5• | 5• | 5• |
| 9.0 | 2 | 3• | 3• | 3• | 3• | 3• | 3• |
| 12.0 | 2 | 2 | 3• | 3• | 3• | 3• | 3• |
| 15.0 | 2 | 2• | 2• | 2• | 2• | 2• | 2• |
| 18.0 | 2• | 2• | 2• | 2• | 2• | 2• | 2• |
| 21.0 | 1 | 2• | 2• | 2• | 2• | 2• | 2• |
|  | Flame Length/Feet |
| 3.0 | 1.6 | 1.7 | 1.9 | 2.1 | 2.2• | 2.2• | 2.2• |
| 6.0 | 1.3 | 1.4 | 1.5 | 1.6 | 1.6• | 1.6• | 1.6• |
| 9.0 | 1.1 | 1.2 | 1.3• | 1.3• | 1.3• | 1.3• | 1.3• |
| 12.0 | 1.0 | 1.1 | 1.2• | 1.2• | 1.2• | 1.2• | 1.2• |
| 15.0 | 1.0 | 1.0 | 1.1• | 1.1• | 1.1• | 1.1• | 1.1• |
| 18.0 | 0.9 | 1.0• | 1.0• | 1.0• | 1.0• | 1.0• | 1.0• |
| 21.0 | 0.9 | 0.9• | 0.9• | 0.9• | 0.9• | 0.9• | 0.9• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 54:  FUEL MODEL 9―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 1 | 3 | 8 | 16 | 25 | 36 | 49 |
| 6.0 | 1 | 2 | 6 | 12 | 19 | 27 | 37 |
| 9.0 | 1 | 2 | 5 | 10 | 15 | 22 | 30 |
| 12.0 | 1 | 2 | 4 | 8 | 13 | 19 | 26 |
| 15.0 | 1 | 2 | 4 | 7 | 12 | 17 | 23 |
| 18.0 | 0 | 1 | 3 | 6 | 10 | 14 | 19 |
| 21.0 | 0 | 1 | 2 | 4 | 7 | 10 | 13 |
|  | Flame Length/Feet |
| 3.0 | 1.3 | 2.1 | 3.2 | 4.2 | 5.2 | 6.2 | 7.1 |
| 6.0 | 1.0 | 1.6 | 2.5 | 3.4 | 4.2 | 4.9 | 5.7 |
| 9.0 | 0.9 | 1.4 | 2.2 | 2.9 | 3.6 | 4.3 | 5.0 |
| 12.0 | 0.8 | 1.3 | 2.0 | 2.7 | 3.4 | 4.0 | 4.6 |
| 15.0 | 0.8 | 1.2 | 1.9 | 2.5 | 3.1 | 3.7 | 4.3 |
| 18.0 | 0.7 | 1.1 | 1.7 | 2.2 | 2.7 | 3.3 | 3.7 |
| 21.0 | 0.5 | 0.8 | 1.2 | 1.6 | 2.0 | 2.4 | 2.7 |

TABLE 55:  FUEL MODEL 9―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 3 | 5 | 10 | 17 | 27 | 38 | 51 |
| 6.0 | 2 | 4 | 7 | 13 | 20 | 28 | 38 |
| 9.0 | 2 | 3 | 6 | 11 | 16 | 23 | 31 |
| 12.0 | 1 | 3 | 5 | 9 | 14 | 20 | 27 |
| 15.0 | 1 | 2 | 5 | 8 | 13 | 18 | 24 |
| 18.0 | 1 | 2 | 4 | 7 | 11 | 15 | 20 |
| 21.0 | 1 | 1 | 3 | 5 | 7 | 10 | 14 |
|  | Flame Length/Feet |
| 3.0 | 1.9 | 2.5 | 3.4 | 4.4 | 5.4 | 6.3 | 7.2 |
| 6.0 | 1.5 | 2.0 | 2.7 | 3.5 | 4.3 | 5.0 | 5.8 |
| 9.0 | 1.3 | 1.7 | 2.4 | 3.1 | 3.7 | 4.4 | 5.0 |
| 12.0 | 1.2 | 1.6 | 2.2 | 2.8 | 3.5 | 4.1 | 4.7 |
| 15.0 | 1.1 | 1.5 | 2.1 | 2.6 | 3.2 | 3.8 | 4.3 |
| 18.0 | 1.0 | 1.3 | 1.8 | 2.3 | 2.8 | 3.3 | 3.8 |
| 21.0 | 0.7 | 1.0 | 1.3 | 1.7 | 2.1 | 2.4 | 2.8 |

TABLE 56:  FUEL MODEL 9―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 5 | 7 | 12 | 19 | 29 | 40 | 53 |
| 6.0 | 4 | 5 | 9 | 14 | 21 | 30 | 39 |
| 9.0 | 3 | 4 | 7 | 12 | 17 | 24 | 32 |
| 12.0 | 3 | 4 | 6 | 10 | 15 | 21 | 28 |
| 15.0 | 2 | 3 | 6 | 9 | 14 | 19 | 25 |
| 18.0 | 2 | 3 | 5 | 8 | 11 | 16 | 21 |
| 21.0 | 1 | 2 | 3 | 5 | 8 | 11 | 14 |
|  | Flame Length/Feet |
| 3.0 | 2.4 | 2.9 | 3.7 | 4.6 | 5.6 | 6.5 | 7.4 |
| 6.0 | 1.9 | 2.3 | 3.0 | 3.7 | 4.4 | 5.2 | 5.9 |
| 9.0 | 1.7 | 2.0 | 2.6 | 3.2 | 3.9 | 4.5 | 5.1 |
| 12.0 | 1.6 | 1.9 | 2.4 | 3.0 | 3.6 | 4.2 | 4.7 |
| 15.0 | 1.5 | 1.7 | 2.2 | 2.8 | 3.3 | 3.9 | 4.4 |
| 18.0 | 1.3 | 1.5 | 2.0 | 2.4 | 2.9 | 3.74 | 3.9 |
| 21.0 | 0.9 | 1.1 | 1.4 | 1.8 | 2.2 | 2.5 | 2.8 |

TABLE 57:  FUEL MODEL 9―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 8 | 10 | 15 | 22 | 32 | 43 | 56 |
| 6.0 | 6 | 7 | 11 | 16 | 23 | 32 | 41 |
| 9.0 | 5 | 6 | 9 | 14 | 19 | 26 | 34 |
| 12.0 | 4 | 5 | 8 | 12 | 17 | 23 | 30 |
| 15.0 | 4 | 5 | 7 | 11 | 15 | 20 | 26 |
| 18.0 | 3 | 4 | 6 | 9 | 12 | 17 | 22 |
| 21.0 | 2 | 3 | 4 | 6 | 9 | 12 | 15 |
|  | Flame Length/Feet |
| 3.0 | 3.0 | 3.4 | 4.1 | 4.9 | 5.8 | 6.7 | 7.5 |
| 6.0 | 2.4 | 2.7 | 3.3 | 3.9 | 4.6 | 5.3 | 6.0 |
| 9.0 | 2.1 | 2.4 | 2.9 | 3.4 | 4.0 | 4.6 | 5.2 |
| 12.0 | 1.9 | 2.2 | 2.6 | 3.2 | 3.7 | 4.3 | 4.9 |
| 15.0 | 1.8 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 |
| 18.0 | 1.6 | 1.8 | 2.2 | 2.6 | 3.0 | 3.5 | 4.0 |
| 21.0 | 1.2 | 1.3 | 1.6 | 1.9 | 2.2 | 2.6 | 2.9 |

TABLE 58:  FUEL MODEL 9―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 16 | 18 | 23 | 30 | 40 | 51 | 64 |
| 6.0 | 12 | 13 | 17 | 22 | 29 | 38 | 47 |
| 9.0 | 10 | 11 | 14 | 18 | 24 | 31 | 39 |
| 12.0 | 8 | 10 | 12 | 16 | 21 | 27 | 34 |
| 15.0 | 7 | 9 | 11 | 14 | 19 | 24 | 30 |
| 18.0 | 6 | 7 | 9 | 12 | 16 | 20 | 25 |
| 21.0 | 4 | 5 | 6 | 8 | 11 | 14 | 17• |
|  | Flame Length/Feet |
| 3.0 | 4.2 | 4.5 | 5.0 | 5.7 | 6.5 | 7.2 | 8.0 |
| 6.0 | 3.4 | 3.6 | 4.0 | 4.5 | 5.1 | 5.8 | 6.4 |
| 9.0 | 2.9 | 3.1 | 3.5 | 4.0 | 4.5 | 5.0 | 5.6 |
| 12.0 | 2.7 | 2.9 | 3.2 | 3.7 | 4.2 | 4.7 | 5.2 |
| 15.0 | 2.5 | 2.7 | 3.0 | 3.4 | 3.9 | 4.3 | 4.8 |
| 18.0 | 2.2 | 2.3 | 2.6 | 3.0 | 3.4 | 3.8 | 4.2 |
| 21.0 | 1.6 | 1.7 | 1.9 | 2.2 | 2.5 | 2.8 | 3.0• |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 59:  FUEL MODEL 10―0% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 1 | 4 | 8 | 11-13 | 16-20 | 22-27 | 28-35 |
| 6.0 | 120-90 | 1 | 3 | 7 | 9-12 | 14-17 | 19-23 | 24-30 |
| 9.0 | 120-90 | 1 | 3 | 6 | 9-10 | 13-15 | 17-21 | 22-27 |
| 12.0 | 120-90 | 1 | 3 | 6 | 8-10 | 12-14 | 16-19 | 21-25 |
| 15.0 | 120-90 | 1 | 2 | 5 | 9 | 11-13 | 15-18 | 19-23 |
| 18.0+ | 120-90 | 1 | 2 | 5 | 8 | 10-12 | 14-16 | 18-21 |
| 21.0 | 120-90 | 0 | 2 | 4 | 6 | 8-10 | 11-13 | 14-17 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 2.0 | 3.5 | 5.0 | 6.4 | 7.7 | 8.9 | 10.0 |
| 6.0 | 120-90 | 1.7 | 3.1 | 4.5 | 5.6 | 6.8 | 7.8 | 8.9 |
| 9.0 | 120-90 | 1.6 | 2.9 | 4.2 | 5.3 | 6.2 | 7.2 | 8.2 |
| 12.0 | 120-90 | 1.5 | 2.7 | 4.0 | 5.1 | 6.0 | 6.9 | 7.8 |
| 15.0 | 120-90 | 1.5 | 2.6 | 3.8 | 4.8 | 5.7 | 6.6 | 7.5 |
| 18.0+ | 120-90 | 1.4 | 2.4 | 3.5 | 4.4 | 5.3 | 6.0 | 6.8 |
| 21.0 | 120-90 | 1.2 | 2.0 | 2.9 | 3.7 | 4.4 | 5.1 | 5.8 |

TABLE 60:  FUEL MODEL 10―30% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 3 | 5 | 8-10 | 12-15 | 18-21 | 23-29 | 30-36 |
| 6.0 | 120-90 | 2 | 4 | 8 | 11-13 | 15-18 | 20-24 | 26-31 |
| 9.0 | 120-90 | 2 | 4 | 7 | 10-12 | 14-17 | 18-22 | 23-28 |
| 12.0 | 120-90 | 2 | 3 | 6 | 9-11 | 13-15 | 17-20 | 22-26 |
| 15.0 | 120-90 | 2 | 3 | 6 | 8-10 | 12-14 | 16-19 | 20-24 |
| 18.0+ | 120-90 | 2 | 3 | 5 | 8 | 11-13 | 15-17 | 19-20 |
| 21.0 | 120-90 | 1 | 2 | 4 | 7 | 8-11 | 11-14 | 14-18 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 3.0 | 4.2 | 5.6 | 6.8 | 8.0 | 9.2 | 10.3 |
| 6.0 | 120-90 | 2.7 | 3.7 | 4.9 | 6.0 | 7.1 | 8.1 | 9.0 |
| 9.0 | 120-90 | 2.5 | 3.4 | 4.5 | 5.6 | 6.6 | 7.5 | 8.3 |
| 12.0 | 120-90 | 2.3 | 3.2 | 4.3 | 5.3 | 6.2 | 7.0 | 7.9 |
| 15.0 | 120-90 | 2.2 | 3.0 | 4.1 | 5.0 | 5.9 | 6.7 | 7.5 |
| 18.0+ | 120-90 | 2.1 | 2.8 | 3.8 | 4.7 | 5.5 | 6.2 | 7.0 |
| 21.0 | 120-90 | 1.7 | 2.4 | 3.2 | 3.9 | 4.6 | 5.3 | 5.9 |

TABLE 61:  FUEL MODEL 10―45% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 5 | 7 | 9-12 | 14-17 | 19-23 | 25-31 | 31-38 |
| 6.0 | 120-90 | 4 | 6 | 8-10 | 12-15 | 16-20 | 21-26 | 27-33 |
| 9.0 | 120-90 | 4 | 6 | 7-9 | 11-13 | 15-18 | 19-23 | 24-29 |
| 12.0 | 120-90 | 3 | 5 | 8 | 10-12 | 14-17 | 18-22 | 23-27 |
| 15.0 | 120-90 | 3 | 5 | 6-8 | 11 | 13-16 | 17-20 | 21-25 |
| 18.0+ | 120-90 | 3 | 4 | 7 | 10 | 13-14 | 16-18 | 20-23 |
| 21.0 | 120-90 | 2 | 4 | 6 | 7-9 | 9-12 | 12-15 | 15-19 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 3.9 | 4.8 | 6.0 | 7.2 | 8.3 | 9.3 | 10.4 |
| 6.0 | 120-90 | 3.4 | 4.2 | 5.3 | 6.3 | 7.3 | 8.3 | 9.1 |
| 9.0 | 120-90 | 3.2 | 3.9 | 4.9 | 5.8 | 6.8 | 7.6 | 8.4 |
| 12.0 | 120-90 | 3.0 | 3.7 | 4.6 | 5.5 | 6.4 | 7.2 | 8.0 |
| 15.0 | 120-90 | 2.9 | 3.6 | 4.4 | 5.3 | 6.1 | 6.9 | 7.6 |
| 18.0+ | 120-90 | 2.7 | 3.3 | 4.1 | 4.9 | 5.7 | 6.4 | 7.1 |
| 21.0 | 120-90 | 2.2 | 2.7 | 3.4 | 4.0 | 4.7 | 5.3 | 5.9 |

TABLE 62:  FUEL MODEL 10―60% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 7 | 8-10 | 12-14 | 16-20 | 21-26 | 27-33 | 34-41 |
| 6.0 | 120-90 | 6 | 8 | 10-12 | 14-17 | 18-22 | 23-28 | 29-35 |
| 9.0 | 120-90 | 6 | 6-8 | 9-11 | 13-15 | 17-20 | 21-26 | 26-32 |
| 12.0 | 120-90 | 5 | 7 | 10 | 12-14 | 16-19 | 20-24 | 24-29 |
| 15.0 | 120-90 | 5 | 7 | 9 | 11-13 | 15-17 | 19-22 | 23-27 |
| 18.0+ | 120-90 | 4 | 6 | 7-9 | 10-12 | 13-16 | 17-20 | 21-25 |
| 21.0 | 120-90 | 4 | 5 | 7 | 8-10 | 10-13 | 12-17 | 16-20 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 4.9 | 5.6 | 6.6 | 7.6 | 8.7 | 9.7 | 10.7 |
| 6.0 | 120-90 | 4.3 | 2.9 | 5.8 | 6.8 | 7.7 | 8.6 | 9.4 |
| 9.0 | 120-90 | 3.9 | 4.6 | 5.4 | 6.3 | 7.1 | 7.9 | 8.7 |
| 12.0 | 120-90 | 3.8 | 4.3 | 5.1 | 5.9 | 6.7 | 7.5 | 8.3 |
| 15.0 | 120-90 | 3.6 | 4.1 | 4.9 | 5.7 | 6.4 | 7.2 | 7.9 |
| 18.0+ | 120-90 | 3.3 | 3.8 | 4.5 | 5.2 | 6.0 | 6.7 | 7.3 |
| 21.0 | 120-90 | 2.7 | 3.2 | 3.8 | 4.4 | 5.0 | 5.5 | 6.1 |

TABLE 63:  FUEL MODEL 10―90% SLOPE

| Fuel Moisture % (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 120-90 | 13-15 | 15-18 | 18-22 | 23-28 | 28-34 | 34-41 | 40-49 |
| 6.0 | 120-90 | 11-13 | 13-15 | 16-19 | 20-24 | 24-29 | 29-35 | 34-42 |
| 9.0 | 120-90 | 10-12 | 11-14 | 14-17 | 18-21 | 22-26 | 26-32 | 31-38 |
| 12.0 | 120-90 | 9-11 | 11-13 | 13-16 | 17-21 | 20-24 | 25-29 | 29-35 |
| 15.0 | 120-90 | 10 | 10-12 | 12-15 | 16-18 | 19-23 | 23-27 | 27-32 |
| 18.0+ | 120-90 | 9 | 9-11 | 11-13 | 14-17 | 17-20 | 21-25 | 25-29 |
| 21.0 | 120-90 | 6-8 | 7-9 | 9-11 | 11-14 | 13-17 | 16-21 | 19-24 |
|  |  | Flame Length/Feet |
| 3.0 | 120-90 | 6.8 | 7.3 | 8.1 | 9.0 | 9.8 | 10.7 | 11.6 |
| 6.0 | 120-90 | 6.0 | 6.5 | 7.1 | 7.9 | 8.7 | 9.4 | 10.3 |
| 9.0 | 120-90 | 5.5 | 5.9 | 6.6 | 7.3 | 8.0 | 8.8 | 9.4 |
| 12.0 | 120-90 | 5.3 | 5.7 | 6.2 | 6.9 | 7.6 | 8.3 | 9.0 |
| 15.0 | 120-90 | 5.0 | 5.4 | 6.0 | 6.6 | 7.2 | 7.9 | 8.6 |
| 18.0+ | 120-90 | 4.6 | 5.0 | 5.5 | 6.1 | 6.7 | 7.3 | 7.9 |
| 21.0 | 120-90 | 3.9 | 4.1 | 4.6 | 5.1 | 5.6 | 6.1 | 6.6 |

TABLE 64:  FUEL MODEL 11―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 1 | 3 | 6 | 9 | 12 | 16 | 19 |
| 6.0 | 1 | 2 | 5 | 7 | 10 | 13 | 16 |
| 9.0 | 0 | 2 | 4 | 6 | 9 | 11 | 14 |
| 12.0 | 0 | 2 | 3 | 5 | 7 | 9 | 11 |
| 15.0 | 0 | 1 | 2 | 3 | 4 | •5 | •5 |
| 18.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 1.3 | 2.6 | 3.6 | 4.3 | 5.0 | 5.6 | 6.1 |
| 6.0 | 1.2 | 2.3 | 3.1 | 3.8 | 4.4 | 4.9 | 5.4 |
| 9.0 | 1.1 | 2.1 | 2.9 | 3.5 | 4.0 | 4.5 | 5.0 |
| 12.0 | 0.9 | 1.8 | 2.4 | 2.9 | 3.4 | 3.8 | 4.2 |
| 15.0 | 0.5 | 1.0 | 1.4 | 1.7 | 1.9 | 2.2 | •2.3 |
| 18.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | • MEANS YOU HIT THE WIND LIMIT. |

TABLE 65:  FUEL MODEL 11―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 2 | 4 | 7 | 10 | 13 | 17 | 20 |
| 6.0 | 1 | 3 | 6 | 8 | 11 | 14 | 17 |
| 9.0 | 1 | 3 | 5 | 7 | 10 | 12 | 15 |
| 12.0 | 1 | 2 | 4 | 6 | 8 | 10 | 12 |
| 15.0 | 1 | 1 | 2 | 3 | 4 | •5 | •5 |
| 18.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 2.1 | 3.0 | 3.8 | 4.6 | 5.2 | 5.8 | 6.3 |
| 6.0 | 1.8 | 2.7 | 3.4 | 4.0 | 4.6 | 5.1 | 5.5 |
| 9.0 | 1.7 | 2.4 | 3.1 | 3.7 | 4.2 | 4.7 | 5.1 |
| 12.0 | 1.4 | 2.1 | 2.6 | 3.1 | 3.5 | 3.9 | 4.3 |
| 15.0 | 0.8 | 1.2 | 1.5 | 1.8 | 2.0 | 2.2 | •2.3 |
| 18.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 66:  FUEL MODEL 11―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 3 | 6 | 8 | 11 | 15 | 18 | 22 |
| 6.0 | 3 | 5 | 7 | 9 | 12 | 15 | 18 |
| 9.0 | 2 | 4 | 6 | 8 | 11 | 13 | 16 |
| 12.0 | 2 | 3 | 5 | 7 | 8 | 10 | 12 |
| 15.0 | 1 | 2 | 3 | 3 | 4 | •5 | •5 |
| 18.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 2.7 | 3.5 | 4.2 | 4.8 | 5.4 | 6.0 | 6.5 |
| 6.0 | 2.4 | 3.0 | 3.7 | 4.2 | 4.8 | 5.2 | 5.7 |
| 9.0 | 2.2 | 2.8 | 3.4 | 3.9 | 4.4 | 4.8 | 5.2 |
| 12.0 | 1.8 | 2.4 | 2.9 | 3.3 | 3.7 | 4.1 | 4.4 |
| 15.0 | 1.0 | 1.3 | 1.6 | 1.9 | 2.1 | •2.3 | •2.3 |
| 18.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 67:  FUEL MODEL 11―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 5 | 7 | 10 | 13- | 17 | 20 | 24 |
| 6.0 | 4 | 6 | 9 | 11- | 14 | 17 | 19 |
| 9.0 | 4 | 5 | 7 | 10 | 12 | 14 | 17 |
| 12.0 | 3 | 4 | 6 | 8 | 10 | 11 | 13 |
| 15.0 | 2 | 2 | 3 | 4 | •5 | •5 | •5 |
| 18.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 3.3 | 4.0 | 4.6 | 5.2 | 5.7 | 6.3 | 6.7 |
| 6.0 | 2.9 | 3.5 | 4.0 | 4.6 | 5.0 | 5.5 | 5.9 |
| 9.0 | 2.7 | 3.2 | 3.7 | 4.2 | 4.7 | 5.1 | 5.5 |
| 12.0 | 2.3 | 3.7 | 3.1 | 3.5 | 3.9 | 4.3 | 4.6 |
| 15.0 | 1.3 | 1.5 | 1.8 | 2.0 | 2.2 | •2.3 | •2.3 |
| 18.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 68:  FUEL MODEL 11―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 11 | 13 | 16 | 19 | 22 | 26 | 29 |
| 6.0 | 9 | 11 | 13 | 16 | 18 | 21 | 24 |
| 9.0 | 8 | 9 | 11 | 14 | 16 | 18 | 21 |
| 12.0 | 6 | 7 | 9 | 11 | 13 | 15 | 17 |
| 15.0 | 3 | 4 | •5 | •5 | •5 | •5 | •5 |
| 18.0+ | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | Flame Length/Feet |
| 3.0 | 4.7 | 5.1 | 5.6 | 6.1 | 6.6 | 7.0 | 7.4 |
| 6.0 | 4.1 | 4.5 | 4.9 | 5.4 | 5.8 | 6.1 | 6.5 |
| 9.0 | 3.8 | 4.1 | 4.5 | 4.9 | 5.3 | 5.7 | 6.0 |
| 12.0 | 3.2 | 3.5 | 3.8 | 4.2 | 4.5 | 4.8 | 5.1 |
| 15.0 | 1.8 | 2.0 | 2.2 | •2.3 | •2.3 | 2.3• | •2.3 |
| 18.0+ | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
|  | •MEANS YOU HIT THE WIND LIMIT. |

TABLE 69:  FUEL MODEL 12―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 2 | 7 | 13 | 20 | 27 | 34 | 42 |
| 6.0 | 1 | 6 | 11 | 16 | 22 | 27 | 33 |
| 9.0 | 1 | 5 | 9 | 14 | 19 | 24 | 29 |
| 12.0 | 1 | 4 | 8 | 12 | 17 | 21 | 26 |
| 15.0 | 1 | 4 | 7 | 11 | 15 | 19 | 23 |
| 18.0 | 1 | 3 | 6 | 8 | 11 | 15 | 18 |
| 21.0 | 0 | 2 | 3 | 5 | 7 | 9 | 11 |
|  | Flame Length/Feet |
| 3.0 | 3.3 | 6.3 | 8.5 | 10.3 | 11.8 | 13.2 | 14.4 |
| 6.0 | 2.8 | 5.4 | 7.3 | 8.8 | 10.1 | 11.3 | 12.4 |
| 9.0 | 2.6 | 5.0 | 6.7 | 8.1 | 9.3 | 10.3 | 11.3 |
| 12.0 | 2.4 | 4.7 | 6.3 | 7.6 | 8.7 | 9.7 | 10.6 |
| 15.0 | 2.2 | 4.3 | 5.7 | 6.9 | 7.9 | 8.9 | 9.7 |
| 18.0 | 1.9 | 3.5 | 4.7 | 5.7 | 6.6 | 7.4 | 8.1 |
| 21.0 | 1.2 | 2.3 | 3.1 | 3.7 | 4.2 | 4.7 | 5.2 |

TABLE 70:  FUEL MODEL 12―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 4 | 9 | 16 | 22 | 29 | 37 | 44 |
| 6.0 | 3 | 8 | 13 | 18 | 24 | 29 | 35 |
| 9.0 | 3 | 7 | 11 | 16 | 21 | 26 | 31 |
| 12.0 | 3 | 6 | 10 | 14 | 18 | 23 | 27 |
| 15.0 | 2 | 5 | 9 | 12 | 16 | 20 | 24 |
| 18.0 | 2 | 4 | 7 | 10 | 13 | 16 | 19 |
| 21.0 | 1 | 2 | 4 | 8 | 8 | 9 | 11 |
|  | Flame Length/Feet |
| 3.0 | 5.1 | 7.3 | 9.2 | 10.9 | 12.3 | 13.6 | 14.8 |
| 6.0 | 4.3 | 6.3 | 7.9 | 9.3 | 10.6 | 11.7 | 12.7 |
| 9.0 | 4.0 | 5.7 | 7.2 | 8.5 | 9.7 | 10.7 | 11.6 |
| 12.0 | 3.7 | 5.4 | 6.8 | 8.0 | 9.1 | 10.0 | 10.9 |
| 15.0 | 3.4 | 4.9 | 6.2 | 7.3 | 8.3 | 9.2 | 10.1 |
| 18.0 | 2.8 | 4.1 | 5.2 | 6.1 | 6.9 | 7.6 | 8.3 |
| 21.0 | 1.8 | 2.6 | 3.3 | 3.9 | 4.4 | 4.9 | 5.3 |

TABLE 71:  FUEL MODEL 12―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 7 | 13 | 19 | 26 | 33 | 40 | 47 |
| 6.0 | 6 | 10 | 15 | 21 | 26 | 32 | 38 |
| 9.0 | 5 | 9 | 13 | 18 | 23 | 28 | 33 |
| 12.0 | 5 | 8 | 12 | 16 | 20 | 25 | 29 |
| 15.0 | 4 | 7 | 10 | 14 | 18 | 22 | 26 |
| 18.0 | 3 | 5 | 8 | 11 | 14 | 17 | 20 |
| 21.0 | 2 | 3 | 5 | 7 | 8 | 10 | 12 |
|  | Flame Length/Feet |
| 3.0 | 6.5 | 8.3 | 10.0 | 11.5 | 12.9 | 14.1 | 15.3 |
| 6.0 | 5.6 | 7.2 | 8.6 | 9.9 | 11.1 | 12.1 | 13.1 |
| 9.0 | 5.1 | 6.6 | 7.9 | 9.1 | 10.0 | 11.1 | 12.0 |
| 12.0 | 4.8 | 6.2 | 7.4 | 8.5 | 9.5 | 10.4 | 11.3 |
| 15.0 | 4.4 | 5.6 | 6.8 | 7.8 | 8.7 | 9.5 | 10.3 |
| 18.0 | 3.6 | 4.7 | 5.6 | 6.4 | 7.2 | 7.9 | 8.5 |
| 21.0 | 2.3 | 3.0 | 3.6 | 4.1 | 4.6 | 5.1 | 5.5 |

TABLE 72:  FUEL MODEL 12―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 12 | 17 | 23 | 30 | 37 | 44 | 52 |
| 6.0 | 10 | 14 | 19 | 24 | 30 | 36 | 42 |
| 9.0 | 8 | 12 | 16 | 21 | 26 | 31 | 36 |
| 12.0 | 7 | 11 | 15 | 19 | 23 | 28 | 32 |
| 15.0 | 6 | 9 | 13 | 16 | 20 | 24 | 28 |
| 18.0 | 5 | 7 | 10 | 13 | 16 | 19 | 22 |
| 21.0 | 3 | 4 | 6 | 8 | 9 | 11 | 13 |
|  | Flame Length/Feet |
| 3.0 | 8.1 | 9.5 | 11.1 | 12.4 | 13.7 | 14.9 | 16.0 |
| 6.0 | 7.0 | 8.2 | 9.5 | 10.7 | 11.7 | 12.7 | 13.7 |
| 9.0 | 6.4 | 7.5 | 8.7 | 9.8 | 10.7 | 11.7 | 12.5 |
| 12.0 | 6.0 | 7.1 | 8.2 | 9.2 | 10.1 | 10.9 | 11.8 |
| 15.0 | 5.5 | 6.5 | 7.4 | 8.4 | 9.2 | 10.0 | 10.7 |
| 18.0 | 4.5 | 5.4 | 6.2 | 6.9 | 7.6 | 8.3 | 8.9 |
| 21.0 | 2.9 | 3.4 | 4.0 | 4.5 | 4.9 | 5.3 | 5.7 |

TABEL 73:  FUEL MODEL 12―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 25 | 30 | 36 | 43 | 50 | 57 | 64 |
| 6.0 | 20 | 24 | 29 | 34 | 40 | 46 | 52 |
| 9.0 | 17 | 21 | 25 | 30 | 35 | 40 | 45 |
| 12.0 | 15 | 19 | 23 | 27 | 31 | 36 | 40 |
| 15.0 | 13 | 16 | 20 | 23 | 27 | 31 | 35 |
| 18.0 | 11 | 13 | 15 | 18 | 21 | 24 | 28 |
| 21.0 | 6 | 8 | 9 | 11 | 13 | 15 | 17 |
|  | Flame Length/Feet |
| 3.0 | 11.3 | 12.4 | 13.5 | 14.6 | 15.7 | 16.7 | 17.7 |
| 6.0 | 9.7 | 10.6 | 11.6 | 12.5 | 13.4 | 14.3 | 15.1 |
| 9.0 | 8.9 | 9.7 | 10.6 | 11.5 | 12.3 | 13.1 | 13.9 |
| 12.0 | 8.4 | 9.1 | 10.0 | 10.8 | 11.6 | 12.3 | 13.0 |
| 15.0 | 7.6 | 8.3 | 9.1 | 9.8 | 10.5 | 11.2 | 11.9 |
| 18.0 | 6.3 | 6.9 | 7.5 | 8.2 | 8.8 | 9.3 | 9.9 |
| 21.0 | 4.1 | 4.5 | 4.9 | 5.3 | 5.6 | 6.0 | 6.3 |

TABLE 74:  FUEL MODEL 13―0% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 2 | 9 | 16 | 24 | 33 | 42 | 51 |
| 6.0 | 2 | 7 | 13 | 19 | 26 | 33 | 40 |
| 9.0 | 2 | 6 | 11 | 16 | 22 | 28 | 34 |
| 12.0 | 1 | 5 | 10 | 14 | 20 | 25 | 30 |
| 15.0 | 1 | 5 | 9 | 13 | 18 | 22 | 27 |
| 18.0 | 1 | 4 | 8 | 12 | 16 | 20 | 24 |
| 21.0 | 1 | 3 | 6 | 9 | 13 | 17 | 21 |
|  | Flame Length/Feet |
| 3.0 | 4.6 | 8.4 | 11.2 | 13.5 | 15.5 | 17.3 | 18.9 |
| 6.0 | 3.9 | 7.1 | 9.5 | 11.5 | 13.2 | 14.7 | 16.1 |
| 9.0 | 3.5 | 6.4 | 8.5 | 10.3 | 11.8 | 13.2 | 14.4 |
| 12.0 | 3.2 | 5.9 | 7.9 | 9.6 | 11.0 | 12.3 | 13.4 |
| 15.0 | 3.1 | 5.6 | 7.5 | 9.0 | 10.4 | 11.6 | 12.7 |
| 18.0 | 2.9 | 5.2 | 7.0 | 8.5 | 9.7 | 10.8 | 11.9 |
| 21.0 | 2.6 | 4.7 | 6.3 | 7.6 | 8.7 | 9.7 | 10.6 |

TABLE 75:  FUEL MODEL 13―30% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 6 | 12 | 19 | 27 | 36 | 45 | 54 |
| 6.0 | 4 | 9 | 15 | 22 | 29 | 36 | 43 |
| 9.0 | 4 | 8 | 13 | 18 | 24 | 30 | 36 |
| 12.0 | 3 | 7 | 12 | 16 | 21 | 27 | 32 |
| 15.0 | 3 | 6 | 10 | 15 | 19 | 24 | 29 |
| 18.0 | 3 | 6 | 9 | 13 | 17 | 22 | 26 |
| 21.0 | 2 | 5 | 8 | 11 | 15 | 19 | 22 |
|  | Flame Length/Feet |
| 3.0 | 6.8 | 9.7 | 12.2 | 14.3 | 16.2 | 17.9 | 19.5 |
| 6.0 | 5.8 | 8.2 | 10.3 | 12.1 | 13.7 | 15.2 | 16.5 |
| 9.0 | 5.2 | 7.4 | 9.2 | 10.9 | 12.3 | 13.6 | 14.8 |
| 12.0 | 4.8 | 6.9 | 8.6 | 10.1 | 11.5 | 12.7 | 13.8 |
| 15.0 | 4.6 | 6.5 | 8.2 | 9.6 | 10.8 | 12.0 | 13.1 |
| 18.0 | 4.3 | 6.1 | 7.6 | 9.0 | 10.1 | 11.2 | 12.2 |
| 21.0 | 3.8 | 5.4 | 6.8 | 8.0 | 9.1 | 10.0 | 10.9 |

TABLE 76:  FUEL MODEL 13―45% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 10 | 16 | 23 | 31 | 40 | 49 | 58 |
| 6.0 | 8 | 13 | 19 | 25 | 32 | 39 | 46 |
| 9.0 | 6 | 11 | 16 | 21 | 27 | 33 | 39 |
| 12.0 | 6 | 9 | 14 | 19 | 24 | 29 | 35 |
| 15.0 | 5 | 9 | 13 | 17 | 22 | 26 | 31 |
| 18.0 | 5 | 8 | 11 | 15 | 19 | 24 | 28 |
| 21.0 | 4 | 7 | 10 | 13 | 17 | 20 | 24 |
|  | Flame Length/Feet |
| 3.0 | 8.8 | 11.1 | 13.3 | 15.2 | 17.0 | 18.6 | 20.1 |
| 6.0 | 7.5 | 9.4 | 11.3 | 12.9 | 14.4 | 15.8 | 17.1 |
| 9.0 | 6.7 | 8.4 | 10.1 | 11.6 | 12.9 | 14.2 | 15.3 |
| 12.0 | 6.2 | 7.9 | 9.4 | 10.8 | 10.8 | 13.2 | 14.3 |
| 15.0 | 5.9 | 7.4 | 8.9 | 10.2 | 11.4 | 12.5 | 13.5 |
| 18.0 | 5.5 | 6.9 | 8.3 | 9.5 | 10.6 | 11.7 | 12.6 |
| 21.0 | 4.9 | 6.2 | 7.4 | 8.5 | 9.5 | 10.4 | 11.3 |

TABLE 77:  FUEL MODEL 13―60% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 15 | 21 | 29 | 37 | 46 | 54 | 63 |
| 6.0 | 12 | 17 | 23 | 29 | 36 | 43 | 50 |
| 9.0 | 10 | 14 | 19 | 25 | 31 | 37 | 43 |
| 12.0 | 9 | 13 | 17 | 22 | 27 | 32 | 38 |
| 15.0 | 8 | 12 | 16 | 20 | 25 | 29 | 34 |
| 18.0 | 7 | 10 | 14 | 18 | 22 | 26 | 31 |
| 21.0 | 6 | 9 | 12 | 15 | 19 | 23 | 26 |
|  | Flame Length/Feet |
| 3.0 | 10.9 | 12.8 | 14.7 | 16.4 | 18.1 | 19.6 | 21.0 |
| 6.0 | 9.2 | 10.8 | 12.4 | 13.9 | 15.3 | 16.6 | 17.8 |
| 9.0 | 8.3 | 9.7 | 11.1 | 12.5 | 13.7 | 14.9 | 16.0 |
| 12.0 | 7.7 | 9.0 | 10.4 | 11.6 | 12.8 | 13.9 | 14.9 |
| 15.0 | 7.3 | 8.5 | 9.8 | 11.0 | 12.1 | 13.1 | 14.1 |
| 18.0 | 6.8 | 8.0 | 9.2 | 10.3 | 11.3 | 12.3 | 13.2 |
| 21.0 | 6.1 | 7.1 | 8.2 | 9.2 | 10.1 | 11.0 | 11.8 |

TABLE 78:  FUEL MODEL 13―90% SLOPE

| Fuel Moisture (1-Hour) | Midflame Wind, mi/h |
| --- | --- |
|  | 0. | 2. | 4. | 6. | 8. | 10. | 12. |
|  | Rate of Spread/Chains per Hour |
| 3.0 | 31 | 37 | 45 | 53 | 62 | 70 | 79 |
| 6.0 | 25 | 30 | 36 | 42 | 49 | 56 | 63 |
| 9.0 | 21 | 25 | 30 | 36 | 41 | 47 | 53 |
| 12.0 | 19 | 22 | 27 | 32 | 37 | 42 | 47 |
| 15.0 | 17 | 20 | 24 | 29 | 33 | 38 | 43 |
| 18.0 | 115 | 18 | 22 | 26 | 30 | 34 | 38 |
| 21.0 | 13 | 16 | 19 | 22 | 26 | 29 | 33 |
|  | Flame Length/Feet |
| 3.0 | 15.2 | 16.5 | 17.9 | 9.4 | 20.7 | 22.1 | 23.3 |
| 6.0 | 12.9 | 14.0 | 15.2 | 16.4 | 17.6 | 18.7 | 19.8 |
| 9.0 | 11.5 | 12.5 | 13.6 | 14.7 | 15.8 | 16.8 | 17.7 |
| 12.0 | 10.7 | 11.7 | 12.7 | 13.7 | 14.7 | 15.6 | 16.5 |
| 15.0 | 10.2 | 11.1 | 12.0 | 13.0 | 13.9 | 14.8 | 15.6 |
| 18.0 | 9.5 | 10.3 | 11.2 | 12.1 | 13.0 | 13.8 | 14.6 |
| 21.0 | 8.5 | 9.2 | 10.1 | 10.9 | 11.6 | 12.4 | 13.1 |

# Text boxes

TABLE 1:  Description of Fuel Models

TABLE 2:  Reference Fuel Moisture, Day (0800-1959)

TABLE 3:  Dead Fuel Moisture Content Corrections, Day

(0800-1959)

May, June, July

TABLE 5: Fine Dead Fuel Moisture Content Corrections, Day

(0800-1759)

November, December, January

B-21

DIAGRAM 1-20-Foot Windspeed Adjusted to Midflame

Windspeed Based on Overstory

=

x 100 = % Slope

TABLE 4: Dead Fuel Moisture Content Corrections, Day

(0800-1759)

February, March, April, August, September, October

February, March, April,

August, September, October

B-25

B-26

B-27

B-28