PEEM Engineering Meeting Minutes 12/06/04

Attendees: A. Demello, A. MacDowell, T. Miller, R. Low, P.McKean, D. Munson, F. Ottens, M.Fahmie, F.Ottens and N. Kelez

Vessel/Shielding – P.McKean reported he was 2/3 complete with detailing the mu-metal shields. He estimated he would be complete in another week. A.MacDowell noted that the 90 degree ccd is only crudely drawn in the current 3D model. N.Kelez stated he would finalize the location and thus confirm that the current mu-metal and vacuum chamber details are correct.

Electron Optics – Projector lens electrodes were inspected by Ed Wong and R.Low using various techniques. They are not perfect. R.Low to make up a comparison table so that we can see where we are. A.Demello working on the lens supports. A.MacDowell looking into the witchcraft of finish for the electron lenses.

Electrical – Last weeks Electrical meeting (12/1/04) decided on the tray layout. The trays would be laid from the 5 bay overhead racks to the beamline racks, then upstream before branching off with ladder trays at ~ 45 deg over the upstream side of the Peem3 instrument. Today it was decided that there will be 2 ladder trays (6" and 18") to separate signal and power, the trays to be supported from the overhead mezzanine. A.MacDowell to supply rack layout to F.Ottens.

Manipulator/Sample Transfer – T.Miller reported that the sample prototype is under fabrication - parts arrive next week.

General – D.Munson to get another motor quote from Minarik for the 5 stage motors and 2 aperture motors. A Design review of the Microscope vessel, support and magnetic shielding before going out for fabrication will be held this Wednesday. AM and NK to coordinate presentation.