| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| COMMITTEE 4 | Addendum 2 to Document 16-E |
|  | 2 November 2007 |
|  | Original: Russian |
| Regional Commonwealth in the field of Communications |
| COMMON Proposal for the work of the Conference |
| Agenda item 1.4 |
| Assessment of the possible impact of IMT identification in the band 470-862 MHz on the digital terrestrial broadcasting service and other primary services |

In the RCC countries, the band 470-862 MHz is currently intensively used for the broadcasting and other primary services. In the broadcasting service, moreover, the transition from analogue to digital broadcasting is being carried out in accordance with the digital frequency Plan of the Geneva-06 Agreement, and this will result in the need for additional frequency channel usage and create a situation of near full usage of the entire frequency band 470-862 MHz.

Studies on the impact on the Geneva-06 Plan of a primary allocation to the mobile service in the band 470-862 MHz and on the possibility of identifying harmonized sub-bands for IMT mobile systems have not yet been completed. This being the case, a breach of electromagnetic compatibility could occur between IMT and existing systems in that band.

The RCC countries are therefore of the view that any decision on identification of the band 470-862 MHz or parts thereof must be based on detailed technical and regulatory studies, particularly studies of electromagnetic compatibility between IMT systems and the radio facilities of the terrestrial broadcasting service and of other primary services. Such studies are already being carried out in ITU-R, in regional organizations and at the national level, although not all of the issues are as yet being covered.

The RCC countries have analysed the possible impact of identifying the band 470-862 MHz or parts thereof on the Geneva-06 digital Plan, as well as the difficulties that could arise on account of the need to protect the radio facilities of other primary services used in the RCC countries.

Table 1 and Figures 1 to 3 show the change in the number of available frequency allotments and reduction in the number of coverages in the Geneva-06 digital Plan for different identification scenarios in the band in question for IMT. Broadcasting service losses within the radio-frequency spectrum may be from 10 to 40 per cent (see Table 1), resulting in a reduction in the number of coverages in the Geneva-06 digital Plan on average from 7-8 to 3-4 (see Figures 1 to 3). This will present the RCC countries with considerable difficulties for the future development of the broadcasting service, particularly when it comes to expanding the number of programmes transmitted and introducing HDTV.

Table 2 and Figures 4 to 6 show the number of frequency assignments to the fixed service and aeronautical radionavigation service in the band 470-862 MHz requiring protection in the RCC countries under the Geneva-06 Agreement. As will be seen from the said table and figures, the considerable number of assignments indicated and significant requirements in terms of their protection will result in substantial difficulties when it comes to introducing IMT systems in neighbouring countries for all 470-862 MHz identification scenarios for IMT.

RCC/16A2/1

On the basis of  their analysis, the RCC administrations do not support allocation of the band 470-862 MHz to the mobile service and its identification at WRC-07, but support the need to conduct additional studies in the period leading up to the next competent conference.

Table 1

Number of frequency allotments in the Geneva-06 digital Plan in different parts of the band 470-862 MHz (RCC countries)

| Adm | 806-862 MHz (56 MHz, 14%) | 790-862 MHz (72 MHz, 18%) | 725-862 MHz (137 MHz, 35%) | 698-862 MHz (164 MHz, 42%) | 470-862 MHz (392 MHz, 100%) |
| --- | --- | --- | --- | --- | --- |
|  | Number of allotments | % of total number of allotments in the band 470-862 MHz | Number of allotments | % of total number of allotments in the band 470-862 MHz | Number of allotments | % of total number of allotments in the band 470-862 MHz | Number of allotments | % of total number of allotments in the band 470-862 MHz | Number of allotments | % of total number of allotments in the band 470-862 MHz |
| ARM | 29 | 13.9 | 29 | 13.9 | 59 | 28.2 | 70 | 33.5 | 209 | 100.0 |
| AZE | 37 | 9.9 | 58 | 15.5 | 126 | 33.6 | 141 | 37.6 | 375 | 100.0 |
| BLR | 19 | 9.3 | 26 | 12.7 | 61 | 29.8 | 72 | 35.1 | 205 | 100.0 |
| GEO | 8 | 5.1 | 16 | 10.3 | 42 | 26.9 | 49 | 31.4 | 156 | 100.0 |
| KAZ | 223 | 13.3 | 303 | 18.1 | 622 | 37.2 | 723 | 43.2 | 1 674 | 100.0 |
| KGZ | 25 | 9.3 | 35 | 13.0 | 86 | 32.0 | 107 | 39.8 | 269 | 100.0 |
| MDA | 10 | 17.9 | 12 | 21.4 | 18 | 32.1 | 23 | 41.1 | 56 | 100.0 |
| RUS | 747 | 12.8 | 984 | 16.9 | 2 056 | 35.3 | 2 421 | 41.5 | 5 829 | 100.0 |
| TJK | 43 | 11.4 | 62 | 16.4 | 132 | 35.0 | 159 | 42.2 | 377 | 100.0 |
| TKM | 41 | 15.2 | 52 | 19.3 | 103 | 38.3 | 116 | 43.1 | 269 | 100.0 |
| UKR | 94 | 14.8 | 123 | 19.3 | 248 | 39.0 | 282 | 44.3 | 636 | 100.0 |
| UZB | 44 | 6.5 | 73 | 10.8 | 201 | 29.8 | 251 | 37.2 | 675 | 100.0 |
| AVG |  | 11.6 |  | 15.6 |  | 33.1 |  | 39.2 |  | 100.0 |
| Min |  | 5.1 |  | 10.3 |  | 26.9 |  | 31.4 |  | 100.0 |
| Max |  | 17.9 |  | 21.4 |  | 39.0 |  | 44.3 |  | 100.0 |

Figure 1

Number of coverages in the band 470-862 MHz under the Geneva-06 digital Plan 
(in RCC countries, in the case of NOC in RR Article 5)

Figure 2

Number of coverages in the band 470-806 MHz under the Geneva-06 digital Plan 
(in RCC countries, in the case of 806-862 MHz band identification for IMT)

Figure 3

Number of coverages in the band 470-698 MHz under the Geneva-06 digital Plan 
(in RCC countries, in the case of 698-862 MHz band identification for IMT)

Table 2

Number of assignments to FS and ARNS in the band 470-862 MHz in accordance with the Geneva-06 Agreement (RCC countries)

| Adm | Number of assignments |
| --- | --- |
|  | 806-862 MHz | 790-862 MHz | 725-862 MHz | 698-862 MHz | 470-862 MHz |
| ARM |  |  |  |  |  |
| AZE | 0 | 0 | 0 | 0 | 3 |
| BLR |  |  |  |  |  |
| GEO | 6 | 6 | 7 | 7 | 7 |
| KAZ | 9 | 9 | 18 | 18 | 18 |
| KGZ | 5 | 6 | 10 | 10 | 10 |
| MDA |  |  |  |  |  |
| RUS | 1 042 | 1 177 | 1 330 | 1 331 | 1 420 |
| TJK | 2 | 2 | 2 | 2 | 2 |
| TKM |  |  |  |  |  |
| UKR |  |  |  |  |  |
| UZB | 7 | 7 | 21 | 21 | 27 |
| Total | 1 071 | 1 207 | 1 388 | 1 389 | 1 487 |

Figure 4

Service area of FS and ARNS assignments in the band 698/725-862 MHz

Figure 5

Service area of FS and ARNS assignments in the band 790-862 MHz 
(RCC countries, Geneva-06 Agreement)

Figure 6

Service area of FS and ARNS assignments in the band 806-862 MHz 
(RCC countries, Geneva-06 Agreement)

_______________

# Text boxes

RCC countries

Min: 4 coverages

Average: 7-8 coverages

Number of coverages

9

8

7

6

5

4

3

2

1

10

RCC countries

Min: 2 coverages

Average: 4-5 coverages

6

5

4

3

2

1

9

8

7

10

Number of coverages

RCC countries

Min: 1 coverage

Average: 3-4 coverages

8

7

6

5

4

3

2

1

10

Number of coverages

9

Max coordination distance with ARNS 
(420 km)

HNG

SVK

BUL

UZB

TJK

KGZ

EST

BLR

NOR

S

FIN

RUS

ROU

CHN

KAZ

TKM

TUR

IRN

AZE

ARM

GEO

MDA

POL

UKR

LTU

LVA

Max coordination distance with ARNS 
(420 km)

NOR

EST

BLR

S

FIN

RUS

ROU

BUL

SVK

HNG

TJK

KGZ

KAZ

UZB

TKM

TUR

AZE

ARM

GEO

MDA

POL

UKR

LTU

LVA

CHN

IRN

POL

Max coordination distance with ARNS 
(420 km)

NOR

GEO

MDA

UKR

LTU

LVA

BLR

S

FIN

RUS

EST

ROU

BUL

SVK

HNG

TJK

KGZ

KAZ

UZB

TKM

TUR

AZE

ARM