# Multi-story Cropping

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 379

### MULTI-STORY CROPPING

Multi-story cropping means that existing or planted stands of trees or shrubs are managed as an overstory with an understory of woody and/or nonwoody plants that are grown for a variety of products.

### PRACTICE INFORMATION

The purpose of multi-story cropping is to:

Improve crop diversity by growing mixed but compatible crops having different heights on the same area

Improve soil quality by increasing utilization and cycling of nutrients and maintaining or increasing soil organic matter

Increase net carbon storage in plant biomass and soil

This practice applies on all lands where trees, shrubs, and woody or nonwoody crops can be grown in combination. This practice does not apply on land that is grazed.

Multi-story cropping can provide a way to cultivate high-value specialty crops under the protection of a forest canopy. Meanwhile, timber stand improvement can result in a higher value timber crop as a long-term economic strategy.

### COMMON ASSOCIATED PRACTICES

Multi-story cropping is commonly applied as part of a Conservation Management System with practices such as:

Forest Stand Improvement (666)

Tree/Shrub Establishment (612)

Tree/Shrub Pruning (660)

Tree/Shrub Site Preparation (490)

Access Control (472)

For further information, refer to the practice standard in the local Field Office Technical Guide and associated practice specifications and job sheets.

# Text boxes

I.10 (+/-) Potential income

Associated practice or activity

LEGEND

C. Cumulative effect

I. Indirect effect

D. Direct effect

#. Created by practice

(+) increase; (-) decrease

pathway

Multi-Story Cropping (379)

7/2008

C.4 (+) Environmental quality

Notes:  Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect of the resource, not whether the effect is beneficial or adverse.

* When traditional cropland is converted to multi-story cropping

D.10 (-) Micro- climate extremes*

I.9 (-) Traditional crop production

I.8 (+) Tree and understory production

C.5 (+) Air quality

I.6 (-) Pesticide drift

I.7 (-) Wind-borne sediment and sediment-attached pollutants

D.9 (-) Wind velocity*

Initial setting: Cropland or unmanaged forest with potential for growing trees or shrubs that may or may not be dissected by streams. Field concerns are water and wind erosion and lack of diverse tree and understory products and habitat

D.12 (+) Diversified landowner income; contractor income

4. Harvested wood fiber (manufactured wood products) and other tree/understory-related products

O&M - periodic tree and understory product removal while maintaining erosion control

I.1 (-) Later wood fiber growth rate

D.1 (+) Initial wood fiber growth rate

C.3 (+) Aquatic health for humans, domestic and wild animals

Start

D.11 (-) Traditional cropland area*

C.6 (+) Recreation business and support infrastructure

I.4 (+) Stream fauna, e.g., fish, invertebrates

I.5 (+) Forest wildlife

I.3 (-) Stream water temperature

D.8 (+) Aesthetics

D.7 (+) Arboreal, understory habitat; detritus and large woody debris*

D.6 (+) Shade*

C.7 (+) Tree and understory product business and support infrastructure

C.1 (-) Atmospheric CO2 and greenhouse effect

C.8 (+) Income and income stability (individuals and community)

C.2 (+) Quality of receiving waters

D.2 (+) Carbon storage

I.2 (+) Denitrification of soil nitrates

D.5 (-) Sheet, rill, streambank erosion and sedimentation*

D.3 (+) Infiltration of precipitation and soil storage*

D.4 (+) Uptake of soil nutrients and trapping of water-borne sediment

2. Woody plant root systems, litter, and soil OM

1. Wood fiber in established plants

3. Canopy cover and vertical vegetative structure from established plants

Multi-Story Cropping (379)