Memorandum

To: 		Lynn Dail, U.S Environmental Protection Agency

From:		Chris Sarsony, e2M

Through:	John Crenshaw, Eastern Research Group

Date:		April 12, 2007

Re:	Development of the 2002 Degreasing Database from the 2002 NEI Database

1.0	Summary

The cost and risk analyses for the proposed halogenated solvent cleaning residual risk NESHAP were based on a 1999 degreasing database developed primarily from the 1999 NEI database.  After the proposal was developed a final version of the 2002 NEI database was released.  In response to public comment and to ensure that the latest available information was utilized, a new 2002 degreasing database was developed from the final version of the 2002 NEI Database (Final Version 2, Dated 10-23-06) and used as the basis for the final rule.

The 2002 degreasing database was developed by querying the 2002 NEI database based on the following criteria:

- Halogenated HAP Emissions (PCE, TCE, MC, TCA, CT, and Methyl Chloroform),

- Degreasing Source Classification Codes (SCC),

- Keywords in Process and Unit Descriptions, and

- Facility Name and location.

Tables 1a and 1b summarize the 2002 degreasing database and compare it to the 1999 database that was developed prior to proposal.  Based on the comparison of the 1999 and the 2002 degreasing databases it can be seen that the population of degreasers decreased by about 8% and the emissions of halogenated solvents from degreasers decreased by about 31% overall.  However, given the uncertainties associated with the development of emission inventories, neither the 1999 nor the 2002 NEI inventory should be considered as correct in an absolute sense or as suggesting temporal trends in degreasing machine populations or emissions.  Rather, we consider them to be “snapshots” of the true long-term inventory of emissions for this source category, each carrying its own degree of uncertainty.

Section 2.0 of the memorandum describes in detail how the 2002 degreasing database was developed.

Table 1a – Comparison of the 1999 Degreasing Database to the 2002 Degreasing Database

| Category | 1999 Degreasing Database | 2002 Degreasing Database | Percent Change |
| --- | --- | --- | --- |
| Number of Records | 2,110 | 1,946 | -8% |
| Number of Units | 1,874 | 1,725 | -8% |
| Number of Facilities | 1,093 | 1,080 | -1% |

Table 1b – Comparison of the 1999 and 2002 Degreasing Databases

| Halogenated HAP Emissions | 1999 Database (tons/yr) | 2002 Database (tons/yr) | Percent Change |
| --- | --- | --- | --- |
| PCE (CAS# 127184) | 1,297 | 889 | -31% |
| Carbon Tetrachloride. (CAS# 56235) | NR | 0 | NA |
| Chloroform (CAS# 67663) | NR | 5 | NA |
| TCA (CAS# 71556) | 3,704 | 2,300 | -38% |
| MC (CAS# 75092) | 1,384 | 567 | -59% |
| TCE (CAS# 79016) | 3,054 | 2,760 | -10% |
| TOTAL | 9,439 | 6,521 | -31% |

2.0	Steps in the Development of the 2002 Degreasing Database

The 2002 degreasing database was derived from the 2002 NEI database in a logical step-wise fashion.  Each of these steps is described in this section and corresponds to a specific component of the database as it is shown in the Access file.  In the final step the different components of the database, i.e., steps 1 to 8, were put together to form the complete 2002 degreasing database summarized in Table 1.

STEP 1 – Halogenated HAP

The Pollutant Code field of the 2002 NEI database was queried to obtain emissions data for the halogenated solvents listed in Table 2.  The resulting data from the query on the halogenated solvents contained 31,091 tons of emissions in 88,059 records (includes 17,469 facilities and 26,770 units).  Since only halogenated solvent emissions are of interest, these 88,059 records were used as the starting database for all subsequent queries when developing the 2002 degreasing database.

Table 2 – Halogenated Solvent Pollutant Codes and Emissions from 2002 NEI

| Pollutant Code (CAS #) | Pollutant | Emissions Reported in 2002 NEI Database (tons/year) |
| --- | --- | --- |
| 127184 | Tetrachloroethylene (PCE) | 5,289 |
| 56235 | Carbon Tetrachloride | 356 |
| 67663 | Chloroform | 1,095 |
| 71556 | Methyl Chloroform (TCA) | 9,197 |
| 75092 | Methylene Chloride (MC) | 9,793 |
| 79016 | Trichloroethylene (TCE) | 5,361 |
|  | TOTAL | 31,091 |

STEP 2 - Degreasing Source Classification Codes (SCC)

Not all units emitting halogenated HAP are degreasing units; therefore, SCC data were used to identify degreaser units within the 88,059 records of halogenated HAP data.  Specifically, the SCC field of the halogenated HAP data was queried for the 31 SCC codes shown in Table 3.  The query for these 31 SCC resulted in the identification of 1,648 records of degreasing data.  These data represent 973 facilities and 1,482 emission units.  The halogenated HAP emissions from these units are summarized in Table 4.

Table 3 – List of Degreasing Source Classification Codes Included in

Initial SCC Query

| Degreasing Category | SCC | SCC6_DESC | SCC8_DESC |
| --- | --- | --- | --- |
| Open-Top Vapor | 40100202 | Degreasing | 1,1,1-Trichloroethane (Methyl Chloroform): Open-top Vapor Degreasing |
| Open-Top Vapor | 40100203 | Degreasing | Perchloroethylene: Open-top Vapor Degreasing |
| Open-Top Vapor | 40100204 | Degreasing | Methylene Chloride: Open-top Vapor Degreasing |
| Open-Top Vapor | 40100205 | Degreasing | Trichloroethylene: Open-top Vapor Degreasing |
| Open-Top Vapor | 40100215 | Degreasing | Entire Unit: Open-top Vapor Degreasing |
| Open-Top Vapor | 40100297 | Degreasing | Other Not Classified: Open-top Vapor Degreasing |
| Open-Top Vapor | 40100299 | Degreasing | Other Not Classified: Open-top Vapor Degreasing |
| Conveyorized Vapor | 40100222 | Degreasing | 1,1,1-Trichloroethane (Methyl Chloroform):Conveyorized Vapor Degreaser |
| Conveyorized Vapor | 40100223 | Degreasing | Perchloroethylene: Conveyorized Vapor Degreasing |
| Conveyorized Vapor | 40100224 | Degreasing | Methylene Chloride: Conveyorized Vapor Degreasing |
| Conveyorized Vapor | 40100225 | Degreasing | Trichloroethylene: Conveyorized Vapor Degreasing |
| Conveyorized Vapor | 40100235 | Degreasing | Entire Unit: with Vaporized Solvent: Conveyorized Vapor Degreasing |
| Conveyorized Vapor | 40100236 | Degreasing | Entire Unit: with Non-boiling Solvent: Conveyorized Vapor Degreasing |
| Conveyorized Vapor | 40100298 | Degreasing | Other Not Classified: Conveyorized Vapor Degreasing |
| Cold Solvent Cleaning | 40100302 | Cold Solvent Cleaning/Stripping | Methylene Chloride |
| Cold Solvent Cleaning | 40100304 | Cold Solvent Cleaning/Stripping | Perchloroethylene |
| Cold Solvent Cleaning | 40100305 | Cold Solvent Cleaning/Stripping | 1,1,1-Trichloroethane (Methyl Chloroform) |
| Cold Solvent Cleaning | 40100306 | Cold Solvent Cleaning/Stripping | Trichloroethylene |
| Cold Solvent Cleaning | 40100335 | Cold Solvent Cleaning/Stripping | Entire Unit |
| Cold Solvent Cleaning | 40100336 | Cold Solvent Cleaning/Stripping | Degreaser: Entire Unit |
| Cold Solvent Cleaning | 40100398 | Cold Solvent Cleaning/Stripping | Other Not Classified |
| Cold Solvent Cleaning | 40100399 | Cold Solvent Cleaning/Stripping | Other Not Classified |
| General Degreasing | 40100216 | Degreasing | Degreaser: Entire Unit |
| General Degreasing | 40100217 | Degreasing | Entire Unit |
| General Degreasing | 40100252 | Degreasing | 1,1,1-Trichloroethane (Methyl Chloroform): General Degreasing Units |
| General Degreasing | 40100253 | Degreasing | Perchloroethylene: General Degreasing Units |
| General Degreasing | 40100254 | Degreasing | Methylene Chloride: General Degreasing Units |
| General Degreasing | 40100255 | Degreasing | Trichloroethylene: General Degreasing Units |
| General Degreasing | 40100259 | Degreasing | 1,1,1-Trichloroethane (Methyl Chloroform): General Degreasing Units |
| General Degreasing | 40100295 | Degreasing | Other Not Classified: General Degreasing Units |
| General Degreasing | 40100296 | Degreasing | Other Not Classified: General Degreasing Units |

Table 4 – Halogenated Solvent Emissions from 31 Degreasing SCC in 2002 NEI

| Pollutant Code (CAS No.) | Pollutant | Emissions Reported in 2002 NEI Database (tons/year) |
| --- | --- | --- |
| 127184 | Tetrachloroethylene (PCE) | 811 |
| 56235 | Carbon Tetrachloride | 0 |
| 67663 | Chloroform | 2.7 |
| 71556 | Methyl Chloroform (TCA) | 2,232 |
| 75092 | Methylene Chloride (MC) | 373 |
| 79016 | Trichloroethylene (TCE) | 2,297 |
|  | TOTAL | 5,716 |

STEP 3 - Keyword searches on process and unit descriptors

To identify additional degreasing units the Unit Description and Process Description fields were searched for the following keywords: "*degreas*", "*clean*", "*web*",  "*wash*", and "*cold*".  However, the version of the 2002 NEI Database that was available (Final Version 2, Dated 10-23-06), did not contain the unit description and process description fields.  Therefore, the keyword query was conducted on an earlier version of the 2002 NEI database (5-31-06 version).  Once the facilities were identified in this earlier version the facility registry identifier was used to identify the facilities in the 10-23-06 version of the 2002 NEI Database.

A review of the Unit Descriptions and Process Descriptions showed that degreasing as well as non-degreasing units were captured.  Non-degreasing units included dry cleaning units, web printing, wipe cleaning, etc.  After removing the non-degreasing units from the keyword search there were 160 records remaining.  The 160 records represented 83 facilities and 134 units.  The halogenated HAP emissions from these units are summarized in Table 5.

Table 5 – Halogenated Solvent Emissions from Facilities Identified on the

Basis of Keywords

| Pollutant Code (CAS No.) | Pollutant | Emissions Reported in 2002 NEI Database (tons/year) |
| --- | --- | --- |
| 127184 | Tetrachloroethylene (PCE) | 64 |
| 56235 | Carbon Tetrachloride | 0 |
| 67663 | Chloroform | 0 |
| 71556 | Methyl Chloroform (TCA) | 34 |
| 75092 | Methylene Chloride (MC) | 36 |
| 79016 | Trichloroethylene (TCE) | 311 |
|  | TOTAL | 445 |

STEP 4 – Combination of Step 2 and 3

The data identified in Steps 2 and 3 were combined resulting in 1,808 records, 1,036 unique facilities, and 1,616 unique units.

STEP 5 – Web Cleaning Machines

The data compiled in Step 4 were checked to ensure that all known facilities (as identified primarily from comment letters on the 1994 NESHAP) performing web cleaning were captured.  Table 6 shows each web cleaning facility and the result of the 2002 NEI search.  Of the ten web cleaning facilities 6 were captured in the SCC and keyword searches.  Two facilities were not captured based on SCC or keyword, but were found in 2002 NEI using a facility name search.  The data for these two facilities were added to the degreasing database (3 units, 57.9 tons of Methylene Chloride, 17.1 tons of Trichloroethylene).  The American Safety Razor facility in Verona, VA and the LTV-Copperweld facility in Fayetteville, TN were not found in the 2002 NEI database.

Table 6 – Results of 2002 NEI Search for Facilities Performing Web Cleaning

| Facility Name | City | State | Results of 2002 NEI Search |
| --- | --- | --- | --- |
| Alcoa Inc. | Riverdale | IA | Captured based on keywords. |
| American Safety Razor Inc. | Verona | VA | Not captured and could not be found in the 2002 NEI. |
| American Safety Razor Knoxville Div. | Knoxville | TN | Captured based on SCC. |
| Arcos Div Hoskins Mf/Mt Carmel Plt | Mt Carmel | PA | Captured based on SCC. |
| Johnson & Johnston Associates | Hampstead | NH | Not captured by SCC or keyword, but was found in 2002 NEI by name. Brought data for this facility into Step 5. |
| Olin Corp. Somers Thin Strip Brass Group | Waterbury | CT | Not captured by SCC or keyword, but was found in 2002 NEI by name. Brought data for this facility into Step 5. |
| LTV-Copperweld Fayetteville Div. | Fayetteville | TN | Not Captured and could not be found in the 2002 NEI. |
| Consolidated Film Industries | Hollywood | CA | Captured on the basis of SCC. |
| Technicolor Inc | North Hollywood | CA | Captured on the basis of SCC. |
| Deluxe Labs | Hollywood | CA | Captured on the basis of SCC. |

STEP 6 - Searches on Additional SCC Codes Identified in Keyword Searches and from Other Known Degreasing Facilities

To identify additional degreasing units a closer look was taken at identifying additional SCC that could be used to further develop the database.  The following approaches were used to identify additional SCC.

- We looked at the top 50 (on the basis of magnitude of emissions) SCC codes emitting halogenated HAP as reported in the 2002 NEI database (Appendix Table A1).

- We looked at the SCC for the units identified based on the keyword search of process descriptors and unit descriptors (Appendix Table A2).

- We looked at the SCC for units at web facilities and other facilities identified through public comments.

- A search of the full list of SCC codes was conducted based on keywords, such as, “cleaning” and “degreasing.”  Several additional SCC were identified.

- We evaluated adding SCC 49099999 (Petroleum and Solvent Evaporation, Organic Solvent Evaporation, Miscellaneous Volatile Organic Compounds, Process and Solvent to be identified in Comments) which is a generic SCC.  In the 2002 NEI there are 126 records with a total of 222 tons of halogenated HAP emissions that are designated with SCC 49099999.  Of the 222 tons, 109 tons (49%) were already identified as degreasing units.  Based on the unit and process descriptions we determined that another 67 tons (30%) are definitely not degreasing units.  For the remaining 47 tons (21%) there is not enough data to determine whether they are degreasers or not.  Therefore, these units were not added to the degreasing database.

Table 7 shows the additional SCC that were used to search the 2002 NEI Database to identify degreasers.  As a result of the search for additional SCC 119 records, representing 91 units and 55 facilities, were identified.  The halogenated HAP emissions from these facilities are shown in Table 8.

Table 7 – Additional SCC Identified

| SCC | SCC Description |
| --- | --- |
| 30105108 | Industrial Processes | Chemical Man. | Animal Adhesives | Degreasing |
| 40201402 | Pet. and Solvent Evap. | Surface Coating Ops. | Large Appliances | Cleaning/Pretreatment |
| 40201502 | Pet. and Solvent Evap. | Surface Coating Ops. | Magnet Wire Surface Coating | Cleaning/Pretreatment |
| 40201602 | Pet. and Solvent Evap. | Surface Coating Ops. | Automobiles and Light Trucks | Cleaning/Pretreatment |
| 40201702 | Pet. and Solvent Evap. | Surface Coating Ops. | Metal Can Coating | Cleaning/Pretreatment |
| 40201802 | Pet. and Solvent Evap. | Surface Coating Ops. | Metal Coil Coating | Cleaning/Pretreatment |
| 40202002 | Pet. and Solvent Evap. | Surface Coating Ops. | Metal Furniture Operations | Cleaning/Pretreatment |
| 40202202 | Pet. and Solvent Evap. | Surface Coating Ops. | Plastic Parts | Cleaning/Pretreatment |
| 40202302 | Pet. and Solvent Evap. | Surface Coating Ops. | Large Ships | Cleaning/Pretreatment |
| 40202402 | Pet. and Solvent Evap. | Surface Coating Ops. | Large Aircraft | Cleaning/Pretreatment |
| 40202502 | Pet. and Solvent Evap. | Surface Coating Ops. | Miscellaneous Metal Parts | Cleaning/Pretreatment |
| 40202602 | Pet. and Solvent Evap. | Surface Coating Ops. | Steel Drums | Cleaning/Pretreatment |
| 31303502 | Industrial Processes | Electrical Equipment | Manufacturing - General Processes | Cleaning |
| 31306501 | Industrial Processes | Electrical Equipment | Semiconductor Manufacturing | Cleaning Processes: Wet Chemical: Specify Aqueous Solution |
| 40100201 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Stoddard (Petroleum Solvent): Open-top Vapor Degreasing |
| 40100206 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Toluene: Open-top Vapor Degreasing |
| 40100207 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Trichlorotrifluoroethane (Freon): Open-top Vapor Degreasing |
| 40100208 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Chlorosolve: Open-top Vapor Degreasing |
| 40100209 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Butyl Acetate: Open-top Vapor Degreasing |
| 40100221 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Stoddard (Petroleum Solvent): Conveyorized Vapor Degreasing |
| 40100251 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Stoddard (Petroleum Solvent): General Degreasing Units |
| 40100256 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Toluene: General Degreasing Units |
| 40100257 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Trichlorotrifluoroethane (Freon): General Degreasing Units |
| 40100258 | Pet. and Solvent Evap. | Organic Solvent Evap. | Degreasing | Trichlorofluoromethane: General Degreasing Units |
| 40100301 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Methanol |
| 40100303 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Stoddard (Petroleum Solvent) |
| 40100307 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Isopropyl Alcohol |
| 40100308 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Methyl Ethyl Ketone |
| 40100309 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Freon |
| 40100310 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Acetone |
| 40100311 | Pet. and Solvent Evap. | Organic Solvent Evap. | Cold Solvent Cleaning/Stripping | Glycol Ethers |
| 31612002 | Industrial Processes | Photographic Film Man. | Support Activities - Cleaning Operations | General Cleaning Operations |
| 31612003 | Industrial Processes | Photographic Film Man. | Support Activities - Cleaning Operations | Parts Cleaning Operations |

Table 8 – Halogenated Solvent Emissions from Facilities Identified on the

Basis of Additional SCC

| Pollutant Code (CAS No.) | Pollutant | Emissions Reported in 2002 NEI Database (tons/year) |
| --- | --- | --- |
| 127184 | Tetrachloroethylene (PCE) | 14.0 |
| 56235 | Carbon Tetrachloride | 0 |
| 67663 | Chloroform | 1.9 |
| 71556 | Methyl Chloroform (TCA) | 34.5 |
| 75092 | Methylene Chloride (MC) | 29.6 |
| 79016 | Trichloroethylene (TCE) | 47.8 |
|  | TOTAL | 127.8 |

STEP 7 – Check for Commenters

The degreasing database was checked to ensure that all of the facilities conducting degreasing that submitted public comments were captured.  In addition, we checked to make sure that the magnitude of emissions captured in NEI for these facilities was comparable to the emissions values cited in the comment letters.  Table 9 shows the facilities that were evaluated as part of this analysis.  This analysis resulted in the addition of 6 records representing 6 units.  The emissions that were added to the database are shown in Table 10.

Table 9 – Evaluation of Emissions Captured for Facility for which Public Comments were Received

| Facility | Findings |
| --- | --- |
| Superior Tube, PA | Some units in already. Added 3 additional units that were coded with a generic SCC. |
| Accellent, PA | Already in. |
| Plymouth Tube, MD | Already in. |
| Salem Tube, PA | Already in. |
| Anniston Army Depot, AL | Some units in already. Added 1 unit that was coded with a generic SCC. |
| Summerill Tube, PA | Already in. |
| American Airlines, CA, MO and OK | Already in. |
| DOE Kansas City Plant, MO | Already in. |
| Stewart Stamping, NY | Some units in already. Added 2 units that were coded with a different SCC. The emission unit ID field indicates that these are in-line cleaning machines. |
| Delta Airlines, GA | Not found |
| Wolverine Tube, TN | Already in under Tube Forming Inc. |
| Spirit Aerosystems, KS and OK | Not found |
| PPG | Found in 2002 NEI but additional Information is required. PPG did not specify a plant location for their degreasing activities. Five PPG facilities were found with halogenated solvent emissions. |
| Kodak, NY | Found 44 units at this location with halogenated HAP emissions of 434 tons. These were not added to the degreasing database because the Kodak comment letter indicates that they only have a small R&D cleaner at that location. Therefore, the 44 units must be something other than degreasers. |

Table 10– Halogenated Solvent Emissions from Facilities that

Provided Public Comments

| Pollutant Code | Pollutant | Emissions Reported in 2002 NEI Database (tons/year) |
| --- | --- | --- |
| 127184 | Tetrachloroethylene (PCE) | 0 |
| 56235 | Carbon Tetrachloride | 0 |
| 67663 | Chloroform | 0 |
| 71556 | Methyl Chloroform (TCA) | 0 |
| 75092 | Methylene Chloride (MC) | 70.0 |
| 79016 | Trichloroethylene (TCE) | 16.4 |
|  | TOTAL | 86.4 |

STEP 8 – Search for 96 Facilities from the Preliminary Risk Test and Compilation of Steps

The degreasing database developed to this point was checked to determine whether the 96 degreasing facilities from the preliminary risk test were included.  The preliminary risk test facilities were originally identified from compliance reports submitted to the States in 1998.  Therefore, this data is from a different source than NEI and is somewhat outdated.

The results of our search for the 96 preliminary risk test facilities are as follows (See Table A3):

- 28 facilities were already captured by our 2002 degreasing database.

- 7 facilities were found in 2002 NEI with halogenated HAP emissions.  These 7 facilities represent 10 records, 10 units, with 71.8 tons of TCE emissions.  These data were added to the degreasing database and are shown in Table 11.

- 12 facilities were found in 2002 NEI but did not have halogenated HAP emissions reported.

- 49 facilities were not found in the 2002 NEI.  In addition, we checked the Toxics Release Inventory for these facilities and none were found to have reported halogenated HAP emissions for 2002.  Therefore, we assumed that these facilities were not conducting halogenated solvent cleaning any longer.

Table 11 – Data added for Facilities that were Originally Identified

in the Preliminary Risk Test

| Facility Name | Pollutant Code Desc | Emissions (TPY) |
| --- | --- | --- |
| Indium Corp. of America | Trichloroethylene | 0.75 |
| Indium Corp. of America | Trichloroethylene | 1.5635 |
| Keywell L.L.C. Vac Air Div. | Trichloroethylene | 3.516 |
| Keywell L.L.C. Vac Air Div. | Trichloroethylene | 2.9785 |
| Carter Spray Finishing Corp. | Trichloroethylene | 3.0115 |
| Carter Spray Finishing Corp. | Trichloroethylene | 1.292 |
| CMW, INC. | Trichloroethylene | 7.554 |
| Gilpin Ironworks Inc. | Trichloroethylene | 29.268 |
| Raybestos | Trichloroethylene | 14.0825 |
| Art Brass Plating Inc. | Trichloroethylene | 7.8325 |
|  | TOTAL | 71.8485 |

Table 12 summarizes the records, units, facilities, and halogenated HAP emissions contained in the 2002 degreasing database by Step and Total.  The 1,080 facilities contained in the degreasing database were used as the basis for the cost and risk analyses conducted for the final rule.

Table 12 – Summary of 2002 Degreasing Database by Step and Total

| Category | Step 2 – SCC | Step 3 – Keywords | Step 5 – Web | Step 6 – Additional SCC | Step 7 - Commenters | Step 8 - Risk Test | Total 2002 Degreasing Database |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Number of Records | 1,648 | 160 | 3 | 119 | 6 | 10 | 1,946 |
| Number of Units (a) | 1,482 | 134 | 3 | 91 | 6 | 10 | 1,725 |
| Number of Facilities (a) | 973 | 83 | 2 | 55 | 0 | 7 | 1,080 |
| PCE Emissions (tons/year) (CAS# 127184) | 811 | 64 | 0 | 14.0 | 0 | 0 | 889 |
| Carbon Tet. Emissions (tons/year) (CAS# 56235) | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Chloroform Emissions (tons/year) (CAS# 67663) | 2.7 | 0 | 0 | 1.9 | 0 | 0 | 4.6 |
| TCA Emissions (tons/year) (CAS# 71556) | 2,232 | 34 | 0 | 34.5 | 0 | 0 | 2,300.5 |
| MC Emissions (tons/year) (CAS# 75092) | 373 | 36 | 57.9 | 29.6 | 70.0 | 0 | 566.5 |
| TCE Emissions (tons/year) (CAS# 79016) | 2,297 | 311 | 17.1 | 47.8 | 16.4 | 71.8 | 2,761.1 |
| TOTAL | 5,715.7 | 445.0 | 75.0 | 127.8 | 86.4 | 71.8 | 6,521.7 |

(a) – The total represents the number of unique units.  Different records for the same unit or facility could have been added during the different steps.  Therefore,  the total of the units or facilities for all the steps does not equal the number of unique units or facilities.

Appendix

| Table A1 - Top 50 SCC Emitting Halogenated HAP - All Sources |
| --- |
| Halogenated HAP Emissions(TPY) | SCC | SCC Description |
| 4129.51 | 39999999 | Industrial Processes | Miscellaneous Manufacturing Industries | Miscellaneous Industrial Processes | See Comment ** |
| 3471.13 |  | BLANK |  |  |  |
| 2774.70 | 50100402 | Waste Disposal | Solid Waste Disposal - Government | Landfill Dump | Fugitive Emissions |
| 1227.16 | 40100205 | Already Captured |  |  |  |
| 1170.03 | 40100103 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Dry Cleaning | Perchloroethylene |
| 1053.90 | 30800801 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Plastic Foam Products | Expansion Process via Steam |
| 860.22 | 40200110 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Paint: Solvent-base |
| 802.05 | 30180001 | Industrial Processes | Chemical Manufacturing | General Processes | Fugitive Leaks |
| 787.45 | 40100202 | Already Captured |  |  |  |
| 779.54 | 40100305 | Already Captured |  |  |  |
| 515.42 | 40200101 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Paint: Solvent-base |
| 509.34 | 40100113 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Dry Cleaning | Perchloroethylene |
| 456.34 | 40100252 | Already Captured |  |  |  |
| 454.18 | 40100203 | Already Captured |  |  |  |
| 438.08 | 40100255 | Already Captured |  |  |  |
| 416.19 | 30199999 | Industrial Processes | Chemical Manufacturing | Other Not Classified | Specify in Comments Field |
| 375.24 | 31616003 | Industrial Processes | Photographic Film Manufacturing | Support Activities - Other Operations | Miscellaneous Manufacturing Operations |
| 362.00 | 30101870 | Industrial Processes | Chemical Manufacturing | Plastics Production | Reactor (Polyether Resins) |
| 313.75 | 30101880 | Industrial Processes | Chemical Manufacturing | Plastics Production | Reactor (Polyurethane) |
| 280.84 | 30700114 | Industrial Processes | Pulp and Paper and Wood Products | Sulfate (Kraft) Pulping | Bleaching Reactors |
| 277.66 | 30700199 | Industrial Processes | Pulp and Paper and Wood Products | Sulfate (Kraft) Pulping | Other Not Classified |
| 263.62 | 40100306 | Already Captured |  |  |  |
| 245.45 | 40100225 | Already Captured |  |  |  |
| 238.04 | 40288822 | Petroleum and Solvent Evaporation | Surface Coating Operations | Fugitive Emissions | Coating |
| 229.77 | 40202501 | Petroleum and Solvent Evaporation | Surface Coating Operations | Miscellaneous Metal Parts | Coating Operation |
| 222.30 | 49099999 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Miscellaneous Volatile Organic Compound Evaporation | Identify the Process and Solvent in Comments |
| 219.62 | 40200701 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Adhesive Application |
| 218.97 | 40200710 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Adhesive: General |
| 215.56 | 30101899 | Industrial Processes | Chemical Manufacturing | Plastics Production | Others Not Specified |
| 186.79 | 40100101 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Dry Cleaning | Perchloroethylene |
| 178.37 | 30106099 | Industrial Processes | Chemical Manufacturing | Pharmaceutical Preparations | Other Not Classified |
| 170.57 | 40100398 | Already Captured |  |  |  |
| 166.59 | 40100253 | Already Captured |  |  |  |
| 165.47 | 30112599 | Industrial Processes | Chemical Manufacturing | Chlorine Derivatives | Other Not Classified |
| 163.78 | 40201901 | Petroleum and Solvent Evaporation | Surface Coating Operations | Wood Furniture Surface Coating | Coating Operation |
| 158.97 | 40200810 | Petroleum and Solvent Evaporation | Surface Coating Operations | Coating Oven - General | General |
| 140.00 | 30101882 | Industrial Processes | Chemical Manufacturing | Plastics Production | Blowing Agent: Methylene Chloride (Polyurethane) |
| 138.02 | 30800799 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Fiberglass Resin Products | Other Not Classified |
| 137.71 | 30800703 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Fiberglass Resin Products | Solvent Consumption |
| 131.59 | 40100399 | Already Captured |  |  |  |
| 129.88 | 30800199 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Tire Manufacture | Other Not Classified |
| 124.41 | 40299998 | Petroleum and Solvent Evaporation | Surface Coating Operations | Miscellaneous | Specify in Comments Field |
| 122.11 | 40500412 | Petroleum and Solvent Evaporation | Dry Cleaning | Petroleum Solvent - Industrial | Stoddard |
| 115.28 | 30800699 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Other Fabricated Plastics | Other Not Classified |
| 114.33 | 30182002 | Industrial Processes | Chemical Manufacturing | Wastewater Treatment | Wastewater Treatment |
| 112.35 | 30999999 | Industrial Processes | Fabricated Metal Products | Other Not Classified | Other Not Classified |
| 106.34 | 41000102 | Petroleum and Solvent Evaporation | Printing/Publishing | General | Lithographic: 2752 |
| 102.00 | 40200410 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Lacquer |
| 96.71 | 40100304 | Already Captured |  |  |  |
| 91.83 | 40188898 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Fugitive Emissions | Specify in Comments Field |
| 26,161.18 | Total |  |  |  |  |
| 84% | Percent of Total Hal. HAP |  |  |  |

| Table A2 - SCC for the Units Identified Based on Process or Unit Keyword |
| --- |
| SCC | Records | Emissions (TPY) | SCC Description |
| 10500106 | 1 | 0.00 | External Combustion Boilers | Space Heaters | Industrial | Natural Gas |
| 30106008 | 2 | 0.02 | Industrial Processes | Chemical Manufacturing | Pharmaceutical Preparations | Exhaust Systems |
| 30119799 | 1 | 0.84 | Industrial Processes | Chemical Manufacturing | Butylene, Ethylene, Propylene, Olefin Production | Other Not Classified |
| 30125880 | 1 | 0.08 | Industrial Processes | Chemical Manufacturing | Benzene/Toluene/Aromatics/Xylenes | Aromatics: Fugitive Emissions |
| 30188801 | 2 | 0.00 | Industrial Processes | Chemical Manufacturing | Fugitive Emissions | Specify in Comments Field |
| 30200704 | 1 | 2.34 | Industrial Processes | Food and Agriculture | Grain Millings | Milo Cleaning |
| 30400199 | 2 | 52.92 | Industrial Processes | Secondary Metal Production | Aluminum | Other Not Classified |
| 30700199 | 1 | 0.00 | Industrial Processes | Pulp and Paper and Wood Products | Sulfate (Kraft) Pulping | Other Not Classified |
| 30800199 | 1 | 0.03 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Tire Manufacture | Other Not Classified |
| 30800703 | 2 | 0.90 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Fiberglass Resin Products | Solvent Consumption |
| 30899999 | 1 | 0.30 | Industrial Processes | Rubber and Miscellaneous Plastics Products | Other Not Specified | Other Not Classified |
| 30900198 | 1 | 14.10 | Industrial Processes | Fabricated Metal Products | General Processes | Other Not Classified |
| 30901098 | 2 | 0.14 | Industrial Processes | Fabricated Metal Products | Electroplating Operations | Other Not Classified |
| 30999999 | 2 | 66.46 | Industrial Processes | Fabricated Metal Products | Other Not Classified | Other Not Classified |
| 31303502 | 1 | 0.11 | Industrial Processes | Electrical Equipment | Manufacturing - General Processes | Cleaning |
| 31306501 | 17 | 0.15 | Industrial Processes | Electrical Equipment | Semiconductor Manufacturing | Cleaning Processes: Wet Chemical: Specify Aqueous Solution |
| 31306599 | 5 | 1.17 | Industrial Processes | Electrical Equipment | Semiconductor Manufacturing | Miscellaneous Operations: General: Specify Material |
| 31503001 | 2 | 0.23 | Industrial Processes | Photo Equip/Health Care/Labs/Air Condit/SwimPools | Laboratories | Bench Scale Reagents: Research |
| 33000399 | 1 | 0.00 | Industrial Processes | Textile Products | Carpet Operations | Other Not Classified |
| 39999993 | 2 | 13.58 | Industrial Processes | Miscellaneous Manufacturing Industries | Miscellaneous Industrial Processes | Other Not Classified |
| 39999994 | 6 | 11.45 | Industrial Processes | Miscellaneous Manufacturing Industries | Miscellaneous Industrial Processes | Other Not Classified |
| 39999995 | 1 | 5.02 | Industrial Processes | Miscellaneous Manufacturing Industries | Miscellaneous Industrial Processes | Other Not Classified |
| 39999997 | 2 | 46.37 | Industrial Processes | Miscellaneous Manufacturing Industries | Miscellaneous Industrial Processes | Other Not Classified |
| 39999999 | 3 | 1.61 | Industrial Processes | Miscellaneous Manufacturing Industries | Miscellaneous Industrial Processes | See Comment ** |
| 40100201 | 2 | 6.45 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Degreasing | Stoddard (Petroleum Solvent): Open-top Vapor Degreasing |
| 40100207 | 15 | 13.33 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Degreasing | Trichlorotrifluoroethane (Freon): Open-top Vapor Degreasing |
| 40100251 | 4 | 2.90 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Degreasing | Stoddard (Petroleum Solvent): General Degreasing Units |
| 40100257 | 7 | 2.09 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Degreasing | Trichlorotrifluoroethane (Freon): General Degreasing Units |
| 40100301 | 1 | 0.00 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Cold Solvent Cleaning/Stripping | Methanol |
| 40100303 | 3 | 0.01 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Cold Solvent Cleaning/Stripping | Stoddard (Petroleum Solvent) |
| 40100309 | 6 | 1.25 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Cold Solvent Cleaning/Stripping | Freon |
| 40188801 | 9 | 0.46 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Fugitive Emissions | Specify in Comments Field |
| 40188898 | 6 | 5.30 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Fugitive Emissions | Specify in Comments Field |
| 40200101 | 1 | 1.71 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Paint: Solvent-base |
| 40200110 | 6 | 1.62 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Paint: Solvent-base |
| 40200201 | 1 | 0.70 | Petroleum and Solvent Evaporation | Surface Coating Operations | Surface Coating Application - General | Paint: Water-base |
| 40200901 | 19 | 2.43 | Petroleum and Solvent Evaporation | Surface Coating Operations | Thinning Solvents - General | General: Specify in Comments |
| 40200912 | 4 | 0.75 | Petroleum and Solvent Evaporation | Surface Coating Operations | Thinning Solvents - General | Isopropyl Alcohol |
| 40200920 | 28 | 11.04 | Petroleum and Solvent Evaporation | Surface Coating Operations | Thinning Solvents - General | Mineral Spirits |
| 40200929 | 1 | 6.89 | Petroleum and Solvent Evaporation | Surface Coating Operations | Thinning Solvents - General | 1,1,1-Trichloroethane (Methyl Chloroform) |
| 40200931 | 2 | 1.28 | Petroleum and Solvent Evaporation | Surface Coating Operations | Thinning Solvents - General | Perchloroethylene |
| 40200998 | 5 | 13.75 | Petroleum and Solvent Evaporation | Surface Coating Operations | Thinning Solvents - General | General: Specify in Comments |
| 40202405 | 1 | 0.04 | Petroleum and Solvent Evaporation | Surface Coating Operations | Large Aircraft | Equipment Cleanup |
| 40202501 | 1 | 3.42 | Petroleum and Solvent Evaporation | Surface Coating Operations | Miscellaneous Metal Parts | Coating Operation |
| 40202502 | 3 | 25.09 | Petroleum and Solvent Evaporation | Surface Coating Operations | Miscellaneous Metal Parts | Cleaning/Pretreatment |
| 40202701 | 1 | 0.01 | Petroleum and Solvent Evaporation | Surface Coating Operations | Glass Mirrors | Mirror Backing: Coating Operation |
| 402888 | 2 | 0.00 | Petroleum and Solvent Evaporation | Surface Coating Operations | Fugitive Emissions |  |
| 40299999 | 1 | 0.03 | Petroleum and Solvent Evaporation | Surface Coating Operations | Miscellaneous | See Comment ** |
| 40400151 | 1 | 0.03 | Petroleum and Solvent Evaporation | Petroleum Liquids Storage (non-Refinery) | Bulk Terminals | Valves, Flanges, and Pumps |
| 40500514 | 2 | 10.33 | Petroleum and Solvent Evaporation | Printing/Publishing | General | Gravure: Cleanup Solvent |
| 40500601 | 1 | 0.56 | Petroleum and Solvent Evaporation | Printing/Publishing | General | Ink Mixing |
| 40799997 | 1 | 0.84 | Petroleum and Solvent Evaporation | Organic Chemical Storage | Miscellaneous | Specify in Comments |
| 40799998 | 2 | 0.01 | Petroleum and Solvent Evaporation | Organic Chemical Storage | Miscellaneous | Specify in Comments |
| 49000105 | 1 | 26.49 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Solvent Extraction Process | Trichloroethylene |
| 49000206 | 1 | 0.00 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Waste Solvent Recovery Operations | Fugitive Leaks |
| 49099998 | 7 | 8.85 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Miscellaneous Volatile Organic Compound Evaporation | Identify the Process and Solvent in Comments |
| 49099999 | 11 | 92.57 | Petroleum and Solvent Evaporation | Organic Solvent Evaporation | Miscellaneous Volatile Organic Compound Evaporation | Identify the Process and Solvent in Comments |
| BLANK | 3 | 37.37 |  |  |  |  |
|  | 219 | 495.42 |  |  |  |  |

Highlighted SCC are those we included in the database search criteria.

| Table A3 - 96 Risk Test Facilities |
| --- |
| Facility | COMPANY | ADDRESS1 | CITY | ST | In 10-23 version of 2002 Database? | EnviroFacts/TRI Information |
| 2-1 | Auburn Technology | 100 Orchard Street | Auburn | NY | Not in 2002 NEI. | Also called bombardier transportation and Alco Power. TRI shows years 1999 to 2004, but no emissions reported. No action. |
| 3-1 | B.G. Sulzle | 1 Needle Lane | North Syracuse | NY | Not in 2002 NEI. | TRI shows years 1987 to 1998. Latest reported halogenated emissions are for 1998 - 5.16 tons of TCE. No action. |
| 4-1 | Brainerd | 115 N. Washington Street | East Rochester | NY | Not in 2002 NEI. | Also called Dispatch Industries. TRI shows years 1987 to 1997, no emissions shown for 1997, 1996 shows copper only. Latest reported halogenated emissions are for 1995 - 7.48 tons of TCE. No action. |
| 6-1 | Carter Spray Finishing | 257 Driggs Ave | Brooklyn | NY | Found in Hal. HAP data. Need to pull in. | N/A |
| 8-1 | Dover Findings | 10 Jefferson Avenue | Saint James | NY | Not in 2002 NEI. | No TRI data. No action. |
| 12-1 | Gary-Syracuse | 901 East Genesee Street | Chittenango | NY | Not in 2002 NEI. | Name is "Gray Syracuse" or "Esco Turbine Technologies". TRI shows years 1987 to 2004, with emissions of other pollutants shown as recent as 2004. Latest reported halogenated emissions are for 1995 - 9.125 tons TCA. No action. |
| 14-1 | Hitemco Div. Of Barson Composites | 160 Sweet Hollow Road | Old Bethpage | NY | Not in 2002 NEI. | TRI shows years 1996 to 2004. Air emissions are shown only for Copper. No action. |
| 16-1 | Indium Corp of America | 1676 Lincoln Avenue | Utica | NY | Found in Hal. HAP data. Need to pull in. | N/A |
| 19-1 | Keywell LLC | 300 Falconer Road | Frewsburg | NY | Found in Hal. HAP data. Need to pull in. | N/A |
| 22-1 | Lighting Services Inc | 2 Kay Fries Drive | Stony Point | NY | Not in 2002 NEI. | TRI shows years 1988 to 1997. Latest Hal HAP emissions are for 1997 - 9.13 tons TCE. No action. |
| 31-2 | DOD - Tinker AFB | 7701 Arnold Street | Tinker AFB | OK | Already in Degreasing Database. | N/A |
| 31-3 | DOD - Kelly AFB | 307 Tinker Drive | Kelly AFB | TX | Not in 2002 NEI. | TRI shows years 1994 to 1999. Latest reported halogenated emissions are for 1999 - 6.5 tons PCE. No action. |
| 31-5 | DOD - Puget Sound Naval Shipyard | 1400 Farragut Avenue | Bremerton | WA | Already in Degreasing Database. | N/A |
| 36-1 | Central Moloney | 2400 West 6th Avenue | Pine Bluff | AK | In 2002 NEI but no halogenated HAP. | N/A |
| 37-1 | Greenville Tube | 5 Montgomery Street (South Montgomery Street?) | Clarksville | AR | In 2002 NEI but no halogenated HAP. | N/A |
| 38-1 | DOE - Sandia NL | Technical Area I | Albuquerque | NM | Already in Degreasing Database. | N/A |
| 39-1 | American Airlines | 3800 N. Mingo Road | Tulsa | OK | Already in Degreasing Database. | N/A |
| 40-4 | Boeing Defense | 20403 68th Avenue S | Kent | WA | In 2002 NEI but no halogenated HAP. | N/A |
| 42-1 | Nordam Repair Div. | 11200 E. Pine Street | Tulsa | OK | Already in Degreasing Database. | N/A |
| 44-1 | Dallas Airmotive (Forest Park Facility) | 6114 Forest Park | Dallas | TX | Already in Degreasing Database. | N/A |
| 45-1 | Dallas Semiconductor | 4335 South Beltwood Parkway | Dallas | TX | Maybe: A facility by this name was found at a different address; no hal. HAP | N/A |
| 49-1 | J&S Plating and Repair | 1318 County Road 655 | Farmersville | TX | Not in 2002 NEI. | No TRI data. No action. |
| 53-1 | Northrop Gruman | 9314 W. Jefferson Blvd | Dallas | TX | Not in 2002 NEI. | Also called "US Navy Weapons Ind Res Plt" and "Vought Aircraft Inds. Inc". TRI data shows 0.125 tons of PCE emissions in 2002 - 0.125 tons. Manually enter 0.125 tons of PCE for 2002. |
| 54-1 | Parkview Metal Products | 400 Barnes Drive | San Marcos | TX | Already in Degreasing Database. | N/A |
| 56-1 | R.E. Dye Manufacturing | 207 W. Williams | Breckenridge | TX | Not in 2002 NEI. | No TRI data. No action. |
| 57-2 | Texas Aero engine Service (Aircraft Engine Overhaul) | 2180 Eagle Parkway | Forth Worth | TX | Already in Degreasing Database. | N/A |
| 59-1 | U.S. Brass | 2117 Interstate 20 | Abilene | TX | Not in 2002 NEI. | TRI data shows 1987 to 2000. Shows TCE emissions of 1.7 tons in 2000. |
| 60-1 | Victor Equipment | 3501 Maple Street | Abilene | TX | Not in 2002 NEI. | TRI data shows 1987 to 2001. TRI data shows 5.491 tons of TCE emissions for 2001. |
| 61-1 | Wolverine Tube - Tube Forming, Inc. | 2021 Beltline Road West | Carrollton | TX | Already in Degreasing Database. | N/A |
| 73-1 | Stennis space center | Hancock County |  | MS | Not in 2002 NEI. | Also called the U.S. NASA Stennis Space Center. TRI data is shown for 1987 to 2003. There are no halogenated HAP emissions shown after 1993. No action. |
| 75-1 | A.O. SMITH/UPPCO | 302 NORTH 6TH | MONTICELLO | IN | Not in 2002 NEI. | TRI data is shown for 1996 to 2003. No halogenated HAP emissions are reported for any year. No action. |
| 78-1 | AUSPRO MFG. CO. | 21671 BECK DR. | ELKHART | IN | Not in 2002 NEI. | No TRI data. No action. |
| 79-1 | BRIDON AMERICAN CORP. | COUNTY RD 200 SOUTH | OAKLAND CITY | IN | Already in Degreasing Database. | N/A |
| 80-1 | CALFLEX | 835 S. MARR ROAD | COLUMBUS | IN | Not in 2002 NEI. | Also called Caltherm Corp. No TRI data. No action. |
| 81-1 | CMW, INC. | 70 S. GRAY ST. | INDIANAPOLIS | IN | Found in Hal. HAP data. Need to pull in. | N/A |
| 82-1 | COMMERCIAL PLATING CO., INC. | 1142 E. BATES ST. | INDIANAPOLIS | IN | Not in 2002 NEI. | No TRI data. No action. |
| 83-1 | CORE TECH | 542 EAST CR 200 N | WARSAW | IN | Not in 2002 NEI. | No TRI data. No action. |
| 84-1 | CRADDOCK FINISHING CORP. | 1400 W. ILLINOIS | EVANSVILLE | IN | Already in Degreasing Database. | N/A |
| 85-1 | CRAFTSMAN COATING, CO. | 1226 LINCOLN AVE. | EVANSVILLE | IN | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 86-1 | DELCO ELECTRONICS CORP. | 2001 E. LINCOLN RD. | KOKOMO | IN | Already in Degreasing Database. | N/A |
| 86-2 | DELPHI DELCO ELECTRONICS SYSTEMS | 2100 E. LINCOLN RD. | KOKOMO | IN | Already in Degreasing Database. | N/A |
| 87-1 | DOUGLASS ELECTRIC MOTOR REPAIR | 368 JEFFERSON | PERU | IN | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 88-1 | ELECTRIC MOTORS & SPECIALTIES, INC. | 701 W. KING ST. | GARRETT | IN | Not in 2002 NEI. | No TRI data. No action. |
| 90-1 | ELKHART PRODUCTS | 700 RAINBOW RD. | GENEVA | IN | Not in 2002 NEI. | TRI data shown for 1987 to 2004. No halogenated HAP emissions reported after 1998. No action. |
| 91-1 | ELLIOTT COMPANY OF INDIANAPOLIS | 9200 ZIONSVILLE RD. | INDIANAPOLIS | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 92-1 | ELSA CORPORATION | 1240 STATE RD. 37 | ELWOOD | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 93-1 | F&F SCREW MACHINE PRODUCTS, INC. | 2709 WHIPPLE | ELKHART | IN | Not in 2002 NEI. | No TRI data. No action. |
| 94-1 | FEDERAL-MOGUL, CORP. | 451 COUNTY LINE RD. | MOORESVILLE | IN | Not in 2002 NEI. | TRI data shows data from 1987 to 1999. No halogenated HAP emissions are shown. No action. |
| 95-1 | FORD ELECTRONICS & REFRIGERATION (Visteon Systems, LLC) | 4747 WESTERN AVENUE | CONNERSVILLE | IN | Already in Degreasing Database. | N/A |
| 97-1 | GILPIN IRONWORKS | 1819 PATTERSON ST. | DECATUR | IN | Found in Hal. HAP data. Need to pull in. | N/A |
| 98-1 | HAND INDUSTRIES, INC. | 315 HAND AVENUE | WARSAW | IN | Not in 2002 NEI. | TRI data shown for 1987 to 1994. 5.5 tons of TCE emissions is shown for 1994. No action. |
| 99-1 | HANSEN CORPORATION | 901 S. FIRST | PRINCETON | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 100-1 | HITACHI CABLE INDIANA, INC. | 5300 GRANTLINE RD. | NEW ALBANY | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 101-1 | HOOSIER TIRE AND RUBBER | 1420 STANLEY | PLYMOUTH | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 102-1 | HORNER ELECTRIC INC. | 1521 E. WASHINGTON ST. | INDIANAPOLIS | IN | Not in 2002 NEI. | TRI data shown for 1990 to 2000. 20 tons of TCE emissions shown for 2000. |
| 104-1 | IDX, INC. | 4700 N. 600 WEST | MCCORDSVILLE | IN | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 105-1 | INDIANA METAL COATINGS, INC. | 7945 S. INTERNATIONAL DR. | COLUMBUS | IN | Already in Degreasing Database. | N/A |
| 106-1 | JASPER ENGINE EXCHANGE, INC. | 815 WERNSING RD. | JASPER | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 107-1 | K AND I HARD CHROME, INC. | 1900 E. MAIN ST. | NEW ALBANY | IN | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 108-1 | K.C.L. CORP. | 701 HODELL ST. | SHELBYVILLE | IN | Not in 2002 NEI. | Also called Pliant Corp. No TRI data. No action. |
| 109-1 | KECO ENGINEERED COATINGS, INC. | 1030 S. KEALING AVE. | INDIANAPOLIS | IN | Not in 2002 NEI. | No TRI data. No action. |
| 110-1 | KEN-KOAT, INC. | 1605 RIVERFORK DR. E. | HUNTINGTON | IN | Already in Degreasing Database. | N/A |
| 111-1 | K-T CORP | 5150 EAST 65th ST. | SHELBYVILLE | IN | Not in 2002 NEI. | TRI data for 1990 to 2001. 9.74 tons of PCE emissions reported for 2001. |
| 112-1 | LINCOLN FOODSERVICE PRODUCTS | 1111 N. HADLEY ROAD | FORT WAYNE | IN | Already in Degreasing Database. | N/A |
| 113-1 | MACHINE-RITE PRODUCTS | 1775 U.S.20 E | LAGRANGE | IN | Not in 2002 NEI. | Also called Atwood Mobile Products. No TRI data. No action. |
| 114-1 | MCDOWELL ENTERPRISES, INC. | 2010 SUPERIOR ST. | ELKHART | IN | Not in 2002 NEI. | TRI data reported for 1987 to 1997. 10 tons of TCE emissions reported for 1997. No action. |
| 115-1 | MID STATES RUBBER | 1230 SOUTH RACE STREET | PRINCETON | IN | In 2002 NEI but no halogenated HAP. | N/A |
| 116-1 | MONARCH SPECIALTY SYSTEMS, INC. | 713 W. LAFEVER ST | OSSIAN | IN | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 117-1 | OAK-RITE MFG. CORP. | 701 CARR RD. P.O. 380 | PLAINFIELD | IN | Not in 2002 NEI. | No TRI data. No action. |
| 118-1 | PETTIFOR'S, INC. | 732 LOS ANGELES AVE. | ELKHART | IN | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 119-1 | PRECISIONEERING, INC. | 707 LEESBURG RD. | FT. WAYNE | IN | Not in 2002 NEI. | Also called ESOX Tool Inc. No TRI data. No action. |
| 121-1 | RAYBESTOS PRODUCTS, CO. | 1204 DARLINGTON AVE. | CRAWFORDSVILLE | IN | Found in Hal. HAP data. Need to pull in. | N/A |
| 122-1 | REDI STRIP OF NEW ALBANY, INC. | 4160 CAPITAL DRIVE | NEW ALBANY | IN | Not in 2002 NEI. | Also called The Woodstripper. No TRI data. No action. |
| 123-1 | REMOTE CONTROLS, INC. | 512 S. MERRIFIELD | MISHAWAKA | IN | Already in Degreasing Database. | N/A |
| 124-1 | SOUTH BEND CONTROLS, INC. | 1237 NORTH SIDE BLVD. | SOUTH BEND | IN | Not in 2002 NEI. | TRI data reported for 1987 to 1998. 5.178 tons of TCE emissions reported for 1998. No action. |
| 125-1 | THE SELMER COMPANY/VINCENT BACH DIV. | 500 INDUSTRIAL PKWY. | ELKHART | IN | Already in Degreasing Database. | N/A |
| 129-1 | Caddock | 17271 North Umpqua Hwy | Roseburg | OR | Not in 2002 NEI. | No TRI data. No action. |
| 130-1 | Color Tech Division of ASKO | 1405 NW 46th | Seattle | OR | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 133-1 | Electro-Chem Metal Finishing | 4849 SE 26th Avenue | Portland | OR | Not in 2002 NEI. | TRI data reported for 1987 to 1995. 5.482 tons of TCE reported for 1994. No action. |
| 141-1 | Portland Public School | 716 N. Marine Drive | Portland | OR | Not in 2002 NEI. | Also called "Multnomah co SD 1 PPS Transp S". No TRI data. No action. |
| 144-1 | Tektronix | Howard Vollum Park | Beaverton | OR | Already in Degreasing Database. | N/A |
| 145-1 | Vispro | 13465 SW Karl Braun Drive | Beaverton | OR | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 147-1 | Art Brass Plating, Inc. | 5516 3rd Avenue South | Seattle | WA | Found in Hal. HAP data. Need to pull in. | N/A |
| 148-1 | Battelle | 520 Third Street | Richland | WA | Not in 2002 NEI. | Not found in EnviroFacts. No action. |
| 150-1 | Exotic Metals Forming Co. | 5411 S. 226th Street | Kent | WA | Not in 2002 NEI. | TRI data reported for 1987 to 2004. No halogenated HAP emissions listed. No action. |
| 151-1 | HTB, Inc. | 22615 83rd Avenue South | Kent | WA | Not in 2002 NEI. | Also called Tubetronics. No TRI data. No action. |
| 152-1 | Johnson Matthey | 15128 E. Euclid | Spokane | WA | Already in Degreasing Database. | N/A |
| 153-1 | LE Wilson, Inc | 404 Pioneer Avenue | Cashmere | WA | Not in 2002 NEI. | No TRI data. No action. |
| 154-1 | MANCO Mfg | 1411 NW 50th | Seattle | WA | Not in 2002 NEI. | TRI data reported for 1987 to 1990. 7.69 tons of TCA emissions reported in 1990. No action. |
| 164-1 | Alcoa | 4879 State Street | Riverdale | IA | Already in Degreasing Database. | N/A |
| 165-1 | American Safety Razor Inc. (VA) | 1 Razor Blade Lane, Route 612 | Verona | VA | In 2002 NEI but no halogenated HAP. | N/A |
| 165-2 | American Safety Razor Inc. (TN) | 2820 Media Drive, Forks of River | Knoxville | TN | Already in Degreasing Database. | N/A |
| 166-1 | Arcos Alloys | 1 Arcos Drive | Mt. Carmel | PA | Already in Degreasing Database. | N/A |
| 167-1 | Johnson and Johnston (a.k.a. Gould Electronics) | 130 Route 111 | Hampstead | NH | Already in Degreasing Database. | N/A |
| 169-1 | Olin Corp. (Somers Thin Strip, Olin Brass) | 215 Piedmont Street | Waterbury | CT | Already in Degreasing Database. | N/A |
| 170-1 | Stewart Stamping Corp. (Stewart EFI) | 630 Central Park Ave. | Yonkers | NY | Already in Degreasing Database. | N/A |