JRG-87

ITU-R JRG 1A-1C-8B

5th Meeting – London – 23rd - 27th April 2007

Spectrum measurements of various radars

(Switzerland)

# Introduction

In order to support the work of the Joint Rapporteur Group 1A-1C-8B, OFCOM Switzerland decided to perform some measurements of radar sideband and spurious emissions. As the time left for this project was rather short it was decided to measure radar equipment of well-known operators such as the Swiss air traffic control operator Skyguide and a heritage weather radar operated by the Swiss Federal Institute of Technology. The aim of this report is to provide more results of radar spectra in order to support JRG 1A-1C-8B in its efforts towards a revision of ITU-R Rec. SM.1541-2.

# Radar Equipment measured

The following radars were investigated:

- Air navigation monopulse secondary surveillance radar at 1030 MHz in the region of Zurich airport.

- Air navigation primary surveillance radar at 2720 MHz in the region of Zurich airport.

- Airport surface movement radars at 9175 MHz and 9420 MHz in the region of Zurich airport.

- Weather radar at 5628 MHz of the Swiss Federal Institute of Technology in Zurich.

The specifications of the different radars investigated are detailed in Table 1. It should be noted that the weather radar at 5628 MHz was tested with two different pulse lengths, thus corresponding to two different spectrum masks. As it is operated with a BP filter added to the original design, the spectrum both prior to and after the filter was measured.

# Measurement setup and procedure

The block diagram of the measurement setup is depicted in Fig. 1.

It should be noted that:

- All measurements were done at monitor points. This can clearly be a disadvantage if this point is prior to a combining filter such as in the 9 GHz radars. On the other hand it is the only way of measuring in a densely loaded area such as an airport. A proper way would be to take into account the filter specs, but they were not available and measurement was not possible.

- A single notch filter operating in the bands 2.7 GHz and 5.5 GHz was available. It was used wherever possible. As a result of the insertion of this notch a dynamic range of greater than 90 dB was achieved.

- Care was taken to use the spectrum analyzer under optimum conditions; therefore an external attenuator with 1 dB steps was inserted at the input.

- The spectrum was measured in at least 3 overlapping subranges (lower part, centre part, upper part) in order to have maximum dynamic range without overloading the analyzer. The three subranges were recombined in Excel to obtain the full spectrum.  In this way it was possible to improve the dynamic range by approx. 10 dB without creating an overload situation to the analyzer. It was found that an overload situation can be safely avoided if the analyzer is used with 3 dB headroom to the point where overload is indicated. Even if there is only a slight overload to the instrument, the spectrum cannot be recombined in Excel without creating a sharp step at the combining frequency. In this way we have a sensitive indicator to ensure proper measurements.

- The tolerance curves were calculated strictly according to Rec. SM.1541-2 based on pulse length and rise- and fall-time, i.e. the assigned frequency was calculated using the pulse length only as well as using rise- respectively fall-time and pulse length. From the two resulting bandwidths the smaller was chosen.

# Results

The measured spectra of the radar systems are displayed in Fig. 2 to 8.

## MSSR 1030 MHz (Fig. 2)

This radar has a spectrum that easily meets the spec given by the 20 dB/decade mask and also the planned future spec based on the 40 dB/decade mask from the design objective. From all systems tested this is the only one easily meeting current and future specs.

## Primary surveillance radar 2720 MHz (Fig. 3)

This radar system represents the biggest surprise of all system measured. Despite of the fact that it is a solid state design it fails to meet even current specs. The reason for this fact is unknown, but it clearly shows that every radar system can be an interference source.

## Surface movement radars 9175 and 9420 MHz (Fig. 4 & 5)

These radar systems operate with a common antenna so they need a combining filter that, if implemented as band pass design, will further improve the spectrum shaping. However the roll-off is rather smooth, specially in the light of the fact that this radar is a magnetron-based design.

## Weather radar 5628 MHz (Fig. 6 to 8)

This weather radar is a heritage system which is the only remaining in Switzerland with this design. The spectrum generated by the radar itself is rather wide (Fig. 6) and the limits of SM.1541-2 could not be met. Therefore a band pass filter was added which efficiently limits the spurious response when the system was commissioned. The filter response can be clearly seen in the output spectrum measured (Fig. 7 & 8). With the filter inserted even a 40 dB/decade slope can almost be met. This clearly shows the potential of filters.

# Conclusions

## Conformity with current Rec. ITU-R SM.1541-2

- As can be seen in the different figures, conformity with the current Rec. SM.1541-2 cannot be guaranteed under all circumstances. The radar system exceeding the most the current spec is the primary surveillance radar at 2720 MHz with the solid state design and not as could be expected a magnetron based system. This shows that every radar system has the potential to violate the limits.

- The reason why the specs are so much violated can only be guessed. The system was originally combined with a second radar to the same antenna. Of course a combining filter was inserted in order to separate the 2 systems. This filter was removed with the second radar “because it was not needed any more”. We assume that with this filter inserted the specs would be met.

- As a consequence of the measured results the question arises of what should be done from the regulator side to ensure conformity to the limits, whether based on current or revised specs. It is obvious that the radar operator is mainly interested in proper system operation and far less in respecting specs. So the regulator should clearly become more active to ensure and enforce internationally agreed specs.

- Since the system that is clearly out of specs is used all over Europe the question arises if this is the only one that fails to meet the limits or if all similar systems show the same spectrum characteristics.

## Use of filters in radar systems

- Use of filters in radar systems is standard since a long time. Often 2 systems with adjacent frequencies are combined to the same antenna, requiring combining filters. So from a technical point of view, there will be no problems inserting filters into the antenna path in most cases.

- Radar systems measured here are high quality systems that require quite some investment. Adding a filter for improving specs does not pose an undue load on the radar industry or on the standard users.

## Defence environment

- In a military environment, filters are in use already for radar systems. A system recently measured in Switzerland easily meets the current Rec. SM.1541-2 with 20 dB/decade slope as well as a planned slope of 40 dB/decade.

- It can be assumed that in a modern battlefield area many different radar systems will have to operate in parallel in ever changing configurations. In such environment it is essential that every system has a strictly limited bandwidth in order not to interfere with others. Moreover the defence part of the radar operators can only profit from more stringent specs as it will experience generally less interference from civilian sources as well.

Table 1: Radar Systems Measured

| Parameter | Radar 1 | Radar 2 | Radar 3 | Radar 4 | Radar 5a | Radar 5b |
| --- | --- | --- | --- | --- | --- | --- |
| Purpose | Air navigation | Air navigation | Surface movement radar | Weather radar |
|  | Monopulse secondary surveillance radar | Primary surveillance radar | Surface movement radar |  |
| Radar manufacturer | Raytheon | Raytheon | Terma | Enterprise Electronics Corp. USA |
| Reference | MSSR | ASR-10SS Mk2 | Scanter 2001 | WR100-5 |
| Frequency | 1030 MHz | 2720 MHz | 9175 MHz | 9420 MHz | 5628 MHz |
| Output device | Solid state | Solid state | Magnetron | Magnetron | Magnetron |
| Peak Power | 1 kW | 16 kW | 20 kW | 20 kW | 250 kW |
| Pulse length | 750 ns | 1.6 µs | 60 ns | 54 ns | 580 ns | 3.0 µs |
| Rise time Fall time | 88 ns 60 ns | 200 ns 2.6 ns | 4.3 ns 16.8 ns | 5.7 ns 15 ns | 36 ns 457 ns | 29 ns 567 ns |
| PRF | 150 Hz | 770 Hz | 8000 Hz | 8000 Hz | 1180 Hz | 250 Hz |
| 40 dB Bandwidth | 29.8 MHz | 40 MHz | 474 MHz | 432 MHz | 42.7 MHz | 19.4 MHz |
| Compliant with SM.1541-2? | yes | no | yes | yes | yes | yes |
| Compliant with 40 dB/decade spec.? | yes | no | yes | no | no | no |
| Spectrum | Fig. 2 | Fig. 3 | Fig. 4 | Fig. 5 | Fig. 6; Fig. 7 | Fig. 8 |

Fig. 1: Block Diagram Test Setup

# Text boxes

Diode Detector

DSO

Agilent 80404B

4 GHz / 40 GSa/s

Attenuator fix

20 dB / 50W

Step attenuator

0 - 70 dB

0 - 11dB

direct

Spectrum

Analyzer

R/S FSQ

20Hz to 26GHz

Notch Filter

2.7 / 5.6 GHz

Coupler

Radar System

Antenna