POLAR Spacecraft Status As of: Weds, 28 Dec 05, 14:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:56=AN STIP data only | NOAA-14J AM: 20:57=AN STIP data only | NOAA-15K AM: 17:57=AN GAC data only | NOAA-16L PM: 14:54=AN GAC&LAC data | NOAA-17M AM: 22:24=AN GAC&LAC data | NOAA-18N PM 13:54=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU-1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ Very low N2 gas | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate ROLL Rgmode=PASSIVE Gyro-1 Off 10/24/05 Gyro-3 Off 6/10/04 Gyro chans XA-ZB TOAR 454 Pitch wheel bias change 16 Dec | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 TOAR 451 Possible hydrazine leak TOAR 455 NULS/Gas enabled 16 Dec at 18:00 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Momentum shift transition started 1 Nov ended 18 Nov. |
| RXO All clocks except N12 to have updates 31 Dec | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/3/03) #2 has 3 chans inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 ON 16Dec 137.50mhz | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ Swap planned 4Jan |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 omni=rcp Power Drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/05 Full Sun Sun Angle 20 up to 22 in early Jan Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -50 Batts 1&3V/T=6/9 Batt2 VT=7/9 Since 11/22/05 Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Degraded shunts SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 15 Topped out Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 45 uptrend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Variable Status upgraded to Yellow 20 Dec Frequent scan motor current surge Occasional imagery bar codes Channels 2&4 APT | Nominal Rare major scan motor surges. Last Incident 11/18/04 Channel 3B only | Variable All time low scan motor currents No bar codes since 12 Oct. TCE24 OFF 4/14/04 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal 7/12/05 FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 CLOSED Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment. | Operational Status downgraded to Yellow 15 Aug 05 LW channel 1-12 noise TOAR 448 Problem isolated to loose LWIR lens |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 Investigating change in motor current trend. Spin state anomaly 16 Dec TOAR 456 |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU8 off TOAR 449 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 as of 27 Sept | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous TED shutdown 24 Sept | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active 7 deg increase in N2 Thruster #2 temp on 13 Dec no other coinciding |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	There were no changes to N12 during the past reporting period.

NOAA-14:	With the exception of a single quick surge on Christmas Day, the N14 AVHRR scan motor has remained nominal

during the past week (it was recently upgraded in status to YELLOW) as has the N14 Power subsystem (illustration 1).

No further planning was conducted on the N14 MSU “tilt test” during the past week.

NOAA-15:	The N15 payload suite was nominal last week with the AMSU’s starting a thermal downtrend and AMSU-B showing

some minor scan motor current instabilities.  In addition, the AVHRR continued to show continued slow and minor improvements in scan motor current values, retreating from some recent “multi year” high values while the HIRS remained solidly nominal (illustration 2).  Finally, the N15 ADACS subsystem was also nominal and stable during the past week (illustration 3).

NOAA-16:	The N16 AVHRR scan motor current fell to its lowest values ever during the past week but then began to exhibit some

instabilities albeit within nominal values while the HIRS filter motor current continued to operate at or near all time high values and high-low ranges (illustration 4).  The N16 ADACS also remained “nominal” relative to the constraints of it now very limited capability (illustration 5).

NOAA-17:	The operational N17 AMSU’s were stable and nominal during the past week while the N17 AVHRR was nominal but

slightly less stable, displaying an operating range very similar to that exhibited by the N16 AVHRR last week (minor “surges” well within nominal values (illustration 6).  The N17 ADACS was also nominal and stable during the past week with no new “perturbations” to report (illustrations 7 & 8 ) and the auto gas unloading threshold for pitch momentum remained at <-40 or >+40 ft lbs (somewhat close to its current value which is averaging around +38).

NOAA-18:	The N18 HIRS period monitor appeared to “tighten” during the past day with no other components showing any out of

family operational changes (illustration 9)  Meanwhile, MHS experienced no further perturbations either during the past week (illustration 10) and the EMOSS team submitted a new TOAR (456) because of the 16 Dec problem (see last weeks report).  Otherwise N18 was nominal during the past week (illustration 11 depicts ADACS performance values).

.

Plans are currently being generated that will change the APT data stream on N18 to VTX-1 (137.10 MHz).  This is scheduled to take place on 4 Jan.

MISC:	On 1 Jan all POES spacecraft will experience a “leap second” that will increase their command clock by 1000 mSecs (1 full

second).  To compensate for this change as well as drift that has occurred through the year, EMOSS will be changing all spacecraft command clocks EXCEPT N12 on 31 Dec at 23:59z.  Of the spacecraft that will have a clock update all of them except N15 will have 1500 mSecs (1.5 seconds) subtracted.  For N15 only 500 MSecs (0.5 sec) will be subtracted.  For more information on this operation see the clock matrix (illustration 22) at the end of this report.

Illustration 1:  NOAA-14 AVHRR (upper right) & Power Balance Health Analysis

(Both as good as they have been all year.  AVHRR status upgraded to Yellow.)

Illustration 2:  N15 Payload Health Analysis

(Some small improvement in the AVHRR scan motor, some minor degradation in the AMSU-B otherwise nominal and stable.)

Illustration 3:  N15 ADACS Health Analysis

(Nominal and stable)

HIRS								AVHRR

Illustration 4:  N16 HIRS and AVHRR Health Analysis

(Generally nominal and stable but not perfectly so…)

Illustration 5:  N16 ADACS Health Analysis

(About as nominal and stable as an anomalous unstable subsystem can be…)

Illustration 6:  N17 Payload Health Analysis

(Nominal and stable, note how the N17 AVHRR scan motor current on the upper left, demonstrates a similar pattern as that of the N16 AVHRR, 2 pages earlier)

Illustration 7:  N17 ADACS Health Analysis

(No perturbations since 8 Dec.  K.O.W.)

Illustration 8:  N17 ADACS Health Analysis (cont)

(Z-momentum continues to be stable near the threshold where gas unloading would occur.  Hydrazine pressure was unchanged from the previous report.)

Illustration 9:  N18 HIRS Health Analysis

(Nominal and stable, note the improvement on the period monitor, upper right, since yesterday.)

ILLUSTRATION 10:  N18 Payload Health Analysis

(Nominal and stable during the past week.  TOAR submitted on MHS anomaly of 16 Dec.)

ILLUSTRATION 11:  N18 ADACS Health Analysis

(Nominal and stable.)

LEAP SECOND TIP CLOCK CORRECTIONS FOR 31 Dec 05 at 23:59z

|  | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| TIP Clock Error as of 12/14/05 | -430 msec | +294 msec | -362 msec | +367 msec | +198 msec | +155 msec |
| Uncompensated Daily Error Rate | -0.8 ms/day | +0.57 ms/day | -0.92 ms/day | +1.05 ms/day | +0.53 ms/day | +1.35ms/day |
| Estimated TIP Clock Error on 12/31/05 | -445 msec | +301 msec | -382 msec | +388 msec | +206 msec | +180 msec |
| Estimated TIP Clock Error on 01/01/06 | +556 msec | +1302 msec. | +617 msec. | +1389 msec. | +1207 msec. | +1182 msec. |
| Recommended TIP Clock Correction | NO CORRECTION | -1500 msec via SCT | -500 msec via SCT | -1500 msec via SCT | -1500 msec via SCT | -1500 msec via SCT |
| ETCUP Data Words | N/A | FFFF D000 | FFFF F000 | FFFF D000 | FFFF D000 | FFFF D000 |
| TIP Clock Error after Leap Second and Correction | +556 msec | -198 msec | +117 msec | -111 msec | -293 msec | -318 msec |

ETCUP commands to be executed from stored command table @ 2005/365/23:59:00 for control OBP, for non control OBP the command will be in the schedule at any convenient time on Dec. 31(no non control command for NOAA-14).