# Building Services Standard Solutions: a proposal to the International Alliance for Interoperability

##### B. Medjdoub*, P. Richens* and N. Barnard**

* The Martin Centre, University of Cambridge

** Oscar Faber

This document contains the attribute descriptions of the building services standard components defined by the Link MCNS project “Building Services Standard Solutions implemented in CAD”. These are being forwarded to the IAI for consideration  for incorporation into the IFCs, The attributes were defined on the basis of what was required for selection, sizing and location of plant for the purposes of the project .

Project partners. 	The Martin Centre University of Cambridge, Oscar Faber, BSRIA, Taylor Woodrow Construction Ltd, The SCI, Sainsburys, Carrier, Hamworthy Heating Ltd, Woods, Pullen Pumps Ltd, Waterloo, Delta, Biddle Air Systems Ltd, Bentley Systems Ltd, CADAC, IES Facet.

Project abstract. This two year project was funded by EPSRC and DETR under the LINK Meeting Client Needs through Standardisation programme in UK. Standardisation is widely recognised as a key element in reducing design time, cutting construction costs and ensuring efficient building solutions. This research focuses on the rules and parameters required to define standard plant room layouts, ceiling voids, risers and main distribution systems. The rules define a set of standard solutions which have been implemented in CAD.

In this project, we have used the object-based CAD programming to handle the selection, sizing, layout and (potentially) pipe-routing for heating and ventilating plant rooms. Our approach combines automation and interactivity. From a simple specification of the plant room geometry (an orthogonal polygon with known obstructions, openings and external walls), and the heating load in kW, our software proceeds through a number of steps. First the number and size of standard modular boilers, pumps etc is determined from the heat load. Then a compatible optimising 3D variational solution is generated, using Constraint Logic Programming. To do this we firstly enumerate a satisfactory topological solution, and then refine it to form a compatible geometrical solution. The final step generates pipe routes, using optimisation techniques to minimise the length of pipes and the number of bends.

The solutions generated by our prototype have been tested against conventional solutions in a benchmarking exercise. Advantages have been underlined and suggestions for further development have been made.

The solution obtained can be modified or improved by the designer, for which we have interactivity. Modifying the topology of the solution or the geometry of the plant room is done directly through the graphic interface, e.g. modifying a boiler position is done by dragging; the system automatically updates the 3D model including the pipe-routing while maintaining all the design rules.

This application is developed in JMDL (Java Modeling Language) as embedded in MicroStation/J, and ECLiPSe the constraint logic programming system. We used JNI (Java Native Interface) as the programming interface between ECLiPSe and JMDL. We used MicroStation/J to hold the object model and for 3D rendering.

# Boiler

| Attributes | Type | Example |
| --- | --- | --- |
| Description Manufacturer Model Ref Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) Output (kW) Gas input rate (m3/h) Minimum gas inlet pressure (mbar) Maximum gas inlet pressure (mbar) Gas setting pressure (mbar) Water content (l) Water flow rate (l/s) Minimum Water flow rate (l/s) Pressure drop (kPa) Maximum water pressure (bar) Minimum water pressure (bar) Flue gas volume (m3/h) Flue gas temperature ((C) Gas connection size (mm) Gas connection location x Gas connection location y Gas connection location z Gas connection direction x Gas connection direction y Gas connection direction z LPHW inlet connection size (mm) LPHW inlet connection location x LPHW inlet connection location y LPHW inlet connection location z LPHW inlet connection direction x LPHW inlet connection direction y LPHW inlet connection direction z LPHW outlet connection size (mm) LPHW outlet connection location x LPHW outlet connection location y LPHW outlet connection location z LPHW outlet connection direction x LPHW outlet connection direction y LPHW outlet connection direction z Flue connection size (mm) Flue connection location x Flue connection location y Flue connection location z Flue connection direction x Flue connection direction y Flue connection direction z Electrical connection size (mm) Electrical connection location x Electrical connection location y Electrical connection location z Electrical connection direction x Electrical connection direction y Electrical connection direction z Running Current (Amps) Starting Current (Amps) Phases Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Double Double Double Double Double Integer Double Double Double Double Double Double Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Double Double Double Double | Hamworthy P50 Hamworthy Purewell P50 532 950 872 150 50 610 460 0 0 600 2100 50 5.92 17.5 25 12.5 30 1.08 0.54 1 6 0.42 78.8 200 20 131 1000 569 0 1 0 50 31 1185 269 0 1 0 50 328.5 1050 573 0 1 0 206 266 684 872 0 0 1 5 0 0 0 0 0 0 6 6 1 50 |

# Pump

| Attributes | Type | Example |
| --- | --- | --- |
| Description Manufacturer Model Ref Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) Power (kW) Water Flow Rate (l/s) Pressure Drop (kPa) LPHW inlet connection size (mm) LPHW inlet connection location x LPHW inlet connection location y LPHW inlet connection location z LPHW inlet connection direction x LPHW inlet connection direction y LPHW inlet connection direction z LPHW outlet connection size (mm) LPHW outlet connection location x LPHW outlet connection location y LPHW outlet connection location z LPHW outlet connection direction x LPHW outlet connection direction y LPHW outlet connection direction z Electrical connection size (mm) Electrical connection location x Electrical connection location y Electrical connection location z Electrical connection direction x Electrical connection direction y Electrical connection direction z Running Current (Amps) Starting Current (Amps) Phases Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Double Double Double Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Double Double Double Double | Pullen belt-driven Pullen Serie C50L-2c 550 650 1000 0 0 600 600 0 0 600 2100 50 100 60 50 275 50 1500 0 0 1 50 50 210 1500 0 0 1 5 0 0 0 0 0 0 90 90 3 20 |

# Pressurisation unit

| Attributes | Type | Example |
| --- | --- | --- |
| Description Manufacturer Model Ref Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) System Volume (l) System Temperature ((C) Vessel Volume (l) Fill Pressure (bar) Static head (bar) Antifreeze percentage (%) Maximum Temperature ((C) Mains supply connection size (mm) Mains supply location x Mains supply location y Mains supply location z Mains supply direction x Mains supply direction y Mains supply direction z System fill connection size (mm) System fill connection location x System fill connection location y System fill connection location z System fill connection direction x System fill connection direction y System fill connection direction z Electrical connection size (mm) Electrical connection location x Electrical connection location y Electrical connection location z Electrical connection direction x Electrical connection direction y Electrical connection direction z Motor Size (kW) Running Current (Amps) Starting Current (Amps) Phases Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Double Integer Double Double Double Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Double Double Double Double Double | Pressurisation Unit Pullen Pulpress 2000 FD50 725 615 1740 600 0 600 300 0 0 600 2100 80 82 50 5.5 1.5 20 100 15 -100 400 1550 0 -1 0 15 -25 500 1650 0 -1 0 5 0 0 0 0 0 1 0.37 3.2 3.2 1 105 |

# Panel board

| Attributes | Type | Example |
| --- | --- | --- |
| Description Manufacturer Model Ref. Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) Incomer size (No) Outgoing ways (No) Incoming cable tray connection size (mm) Incoming cable tray connection location x Incoming cable tray connection location y Incoming cable tray connection location z Incoming cable tray connection direction x Incoming cable tray connection direction y Incoming cable tray connection direction z Outgoing cable tray connection size (mm) Outgoing cable tray connection location x Outgoing cable tray connection location y Outgoing cable tray connection location z Outgoing cable tray connection direction x Outgoing cable tray connection direction y Outgoing cable tray connection direction z Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Double Double Double Integer Integer Integer Integer Double Double Double Integer Integer Integer Double | Panel board Bill BT206 400 150 770 400 400 400 0 1200 1100 600 2100 200 6 225 200 75 0 0 1 0 300 200 75 770 0 1 0 60 |

# Fan

| Attributes | Type | Example |
| --- | --- | --- |
| Description Manufacturer Model Ref. Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) Power (kW) Air Flow Rate (m3/s) Pressure drop (Pa) Sound power (dBA) Outlet connection size (mm) Outlet connection location x Outlet connection location y Outlet connection location z Outlet connection direction x Outlet connection direction y Outlet connection direction z Electrical connection size (mm) Electrical connection location x Electrical connection location y Electrical connection location z Electrical connection direction x Electrical connection direction y Electrical connection direction z Running Current (Amps) Starting Current (Amps) Phases Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Double Double Double Double Integer Double Double Integer Integer Integer Integer Integer Double Double Double Integer Integer Integer Double Double Double Double | Fan Woods 180 1130 1200 1200 0 0 600 0 0 0 600 2100 50 5 1500 80 50 328.5 950 269 0 1 0 1 328.5 950 269 0 1 0 6 6 1 100 |

# Fan coil unit

| Attributes | Type | String |
| --- | --- | --- |
| Description Manufacturer Model Ref. Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) Outlet duct connection size (mm) Outlet duct connection location x Outlet duct connection location y Outlet duct connection location z Outlet duct connection direction x Outlet duct connection direction y Outlet duct connection direction z Outlet duct spigot number Outlet duct spigot pitch Inlet duct connection size (mm) Inlet duct connection location x Inlet duct connection location y Inlet duct connection location z Inlet duct connection direction x Inlet duct connection direction y Inlet duct connection direction z Inlet duct spigot number Inlet duct spigot pitch Cooling output (kW) Cooling coil water content (l) Cooling coil water flow rate (l/s) Cooling coil pressure drop (bar) Maximum CHW pressure (bar) CHW inlet connection size (mm) CHW inlet connection location x CHW inlet connection location y CHW inlet connection location z CHW inlet connection direction x CHW inlet connection direction y CHW inlet connection direction z CHW outlet connection size (mm) CHW outlet connection location x CHW outlet connection location y CHW outlet connection location z CHW outlet connection direction x CHW outlet connection direction y CHW outlet connection direction z Condensate connection size (mm) Condensate connection location x Condensate connection location y Condensate connection location z Condensate connection direction x Condensate connection direction y Condensate connection direction z Heating output (kW) Heating coil water content (l) Heating coil water flow rate (l/s) Heating coil pressure drop (kPa) Maximum LPHW pressure (bar) LPHW inlet connection size (mm) LPHW inlet connection location x LPHW inlet connection location y LPHW inlet connection location z LPHW inlet connection direction x LPHW inlet connection direction y LPHW inlet connection direction z LPHW outlet connection size (mm) LPHW outlet connection location x LPHW outlet connection location y LPHW outlet connection location z LPHW outlet connection direction x LPHW outlet connection direction y LPHW outlet connection direction z Filter EU rating Fan power (kW) Air Flow Rate (m3/s) Fan pressure drop (Pa) Sound power (dBA) Electrical connection size (mm) Electrical connection location x Electrical connection location y Electrical connection location z Electrical connection direction x Electrical connection direction y Electrical connection direction z Running Current (Amps) Starting Current (Amps) Phases Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Double Double Double Double Integer Integer Integer Integer Double Double Double Double Double Integer Integer Integer Integer Double Double Double Double Double Double Double Double Double Double Integer Integer Integer Double Double Double Double Integer Integer Integer Double Double Double Double Integer Integer Integer Double Double Double Double Double Double Double Double Double Integer Integer Integer Double Double Double Double Integer Integer Integer Double Double Double Double Double Double Double Double Double Integer Integer Integer Double Double Double Double | Fan coil unit Biddle A1 1100 915 250 200 200 200 200 100 100 800 500 200 1200 457.5 125 1 0 0 3 305 200 -100 457.5 125 -1 0 0 3 305 2.5 5 0.1 4.94 6 15 771 1205 93 0 1 0 15 799 1310 121 0 1 0 15 770 915 0 0 1 0 5 5 0.1 3.32 6 15 684 995 93 0 1 0 15 712 1100 121 0 1 0 3 0.1 0.2 1500 35 1 779.5 915 240 0 1 0 0.5 1.5 1 100 |

# Diffuser

| Attributes | Type | Example |
| --- | --- | --- |
| Description Manufacturer Model Ref. Width (mm) Depth (mm) Height (mm) Maintenance space left (mm) Maintenance space right (mm) Maintenance space front (mm) Maintenance space back (mm) Maintenance space above (mm) Maintenance space below (mm) Access width (mm) Access height (mm) Duct connection Type Duct Diameter Duct connection location x Duct connection location y Duct connection location z Duct connection direction x Duct connection direction y Duct connection direction z Effective Area (m2/s) Air Flow Rate (m3/s) Pressure Drop (kPa) Noise Criteria (dB) Weight (kg) | STRING STRING STRING Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer Integer STRING Integer Integer Integer Integer Integer Integer Integer Double Double Double Double Double | Diffuser Trox 300 300 300 112 0 0 0 0 0 0 100 100 Round 150 150 150 112 0 0 1 0.0175 0.046 0.014 25 5 |

# Footnotes

The Engineering and Physical Sciences Research Council.

Department of the Environment, Transport and the Regions.

The LINK scheme is the UK Government's principal mechanism for promoting partnership in pre-competitive research between industry and the research base.

Microstation/J is a trademark of Bentley Systems.

ECLiPSe is a trademark of IC-PARC at Imperial College, London.

JNI is a trademark of Sun Microsystems, Inc.