POLAR Spacecraft Status As of: Tues, 25 Jul 06, 22:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:59=AN STIP data only | NOAA-14J AM: 21:10=AN STIP data only | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 2 Since 19 Jul 06 | 2 (since 4/3/03) #2 has 3 chans inop | 2 (drifting?) since 4/18/05 | 1 Analog telem drifting Swap considered | 1 Analog telem drift? |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 ON 137.50 MHZ Turned on 21 Jul at 21:00z | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ Swapped 20 Jul 06 |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 Omni=rcp Power Drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff -60 since 6/28/06 Eclipse season waning ends 12Aug Sun Angle 34 trend down to 9 in Oct Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded SA CANT=37 degs PSSS trigger =18.5 | Array Off -50 Since 22Nov05 Batts 1&3V/T=6/9 Batt2 VT=7/9 SSU off 5 May to reduced load Eclipse all year Sun angle at 58 steady trend Batts 1-3= LRC Degraded shunts SA CANT=22 degs | Array Off -45 Since 1/25/01 Eclipse season waning ends 1 Aug Sun Angle 31 downtrend to 5 in mid-Oct Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 51 Down trend to 33 in late Oct Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 71 steady trend Batts 1-3=LRC Batts 1-3 V/T=4/8 SA CANT=22 BVR Phase Control autonomous swap 3/29=TOAR 457 |
| AVHRR | Nominal | Nominal Since 18 Feb 06 Occasional scan motor current surge Channels 2&4 APT | Nominal Channel 3B only Recent minor scan motor instabilities | Nominal since mid Oct 05 TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Frequent scan motor current minisurges | Nominal Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 Degraded Chan-3 since 4/30/05 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON/Inop Turned On 4/30/05 for power balance Filter Wheel OFF | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 CLOSED Recent momentary FW synch dropouts Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment. | Operational LW Chans degraded 25 June LW channel 1-12 noise TOAR 448 Loose LWIR lens. Inconsistent, LW often erratic. |
| MHS/MIU |  |  |  |  |  | Nominal Flywheel current increase 23 Jun big surge 25 Jun, 8 Jul and again on 17 Jul Space View=0 Rare Turbo anomalies over SAA |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems EOL test planned |  |  |  |  |
| SSU |  | OFF/Nominal Turned off 5 May for power balance |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR |  | Nominal All time high component temps | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | ON/Nominal Autonomous reset 8 Jun, back to nominal 10 June Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 15:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 16:00z | Nominal Elec-CH-HVPS=1 27 June 17:00z Prot-CH-HVPS=0 |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops | Nominal Anode mode since 6 July 13:30z Electronics turnoff taken out of STESM safestate table |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft thermal in uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active TCE3H displaying invalid readings TOAR 458 submitted |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	N12 power balance remained stable and nominal during the past week as the N12 eclipse season continued waning

(illustration 1).  The solar array offset configuration of -60 degrees will have to be re-considered by mid-August at the latest because of the risk of autonomous switching to YGC attitude control mode that may result once the sun angle on the spacecraft falls below 20 degs (predicted for 3 Sept).

NOAA-14:	The TIP on N14 was swapped (to side-2 from side-1) on 19 July in order to determine the true value of the nitrogen

low Pressure on account of TIP side-1 drift.

NOAA-15:	The N15 payload suite was nominal and stable through out the past week (illustration 7) while continuing their thermal

uptrend’s.  The N15 power subsystem also performed nominally as its eclipse season continued to wind down (illustration 8).  Engineers anticipate that the season should be completely over during the first week of August with no reconfigurations recommended in response.  The ADACS was also generally nominal during the past week notwithstanding some minor perturbations (i.e. a large yaw update of .29 on 19 July) that generally returned to nominal.

In addition, the Z-wheel completed its transition from a positive speed bias to one that is again all negative again) on 22 July.  At this time, it appears that it has reached equilibrium between -500 and -800 RPM.  The reason for the transition shifts remains unknown but now that the wheel no longer passes through 0 RPM, attitude precision, especially along the Z-axis, should be improved (illustrations 9 and 10).

On 21 July the VTX (APT data) RF conflict between N12 and N15 ended at which time the N15 VTX-1 transmitter was again commanded on.  Since that time the system has been performing nominally (illustration 11).

NOAA-16:	The N16 payload suite was relatively nominal and stable during the past week (illustration 12 and 13).  Conversely, the

only operational gyro remaining on N16 (gyro-2) showed some minor instabilities last week including a spin motor current jump that was the 4th highest value observed since gyro-1 failed last October.  This increase however was very short lived and the value has sustained itself within its nominal range for the past 4-5 days.  Otherwise the ADACS subsystem performed in a stable and nominal manner (illustrations 14 and 15).

NOAA-17:	The N17 AMSU’s (A2 and B) were nominal during the past week while the HIRS filter motor and AVHRR scan motor were relatively unchanged from previous weeks (i.e. nominal but slightly less stable than desired.  See illustrations 16 and 17).  The N17 ADACS was generally nominal last week as well (illustration 18) although the gyro-1 spin motor current did register a small drop in its equilibrium value during the past several days, a drop that coincided with an

increase in IMU TCA voltage (illustration 19.)  This situation is not considered cause for concern except for the generic concerns regarding all KLM gyros.

Discussions continue regarding a TIP swap on N17 some time before the end of summer.  N17 TIP drift has been substantial and is now at a level reached by both N15 and N16 at the time of their own TIP swaps.

NOAA-18:	The N18 AVHRR and AMSU’s were nominal and stable last week (illustration 20) while the HIRS was basically unchanged from previous weeks with nominal hardware performance and degraded long wave channel quality (illustration 21).  The MHS flywheel continued to show less than optimum performance although a large current surge of the type seen in the past several weeks was not specifically observed (although such an event might have occurred but was “masked” by ABE noise.)   The N18 ADACS was nominal and stable last week with some minor perturbations observed during periods of sun-moon incursions on the earth sensor (illustrations 22 and 23).

On 20 July, enginees oversaw the switch of N18’s APT channel back to #2 (137.9125 MHz, from #1 137.1 MHz).  Since that time the transmitter has been performing nominally (illustration 24).

NOTES: Illustrations 1-6, 8-10, 15-16, 18-19, 22-24 have been omitted for web hosting.

Illustration 7:  N15 Payloads Analysis

(Generally nominal and stable last week.)

ILLUSTRATION 11:  N15 VTX Analysis

(RF conflict with N12 is over, VTX-APT data again nominally transmitting from N15.)

HIRS							AVHRR

ILLUSTRATION 12:  N16 AVHRR & HIRS Health Analysis

(Nominal and stable last week.)

ILLUSTRATION 13:  N16 AMSU’s Health Analysis

(Nominal and stable last week.)

HIRS								AVHRR

ILLUSTRATION 16:  N17 AVHRR & HIRS Health Analysis

(Generally nominal and stable last week although AVHRR mini surges continue [lower right plot].)

ILLUSTRATION 17:  N17 AMSU’s Health Analysis

(Generally nominal and stable last week.  AMSU-A1 is non-operational.)

ILLUSTRATION 20:  N18 Primary Payload Analysis

(Nominal and stable last week.)

ILLUSTRATION 21:  N18 HIRS & MHS Health Analysis

(HIRS continues to experience nominal hardware performance and less than nominal long wave channel quality [upper left plot.  The MHS flywheel continues to show historically less stable behavior [lower right plot] while ABE spikes continue to make analysis more difficult for Engineers.)