International is recalling 1,200 MY 2006 and 2007 IC RESB (PB305) school buses.  A joint at the rear of the bus where the davenport is attached to the floor does not meet the joint strength requirements of federal motor vehicle safety standard no. 221, school bus body joint strength.  IC will notify owners and will add a retaining bar along the front of the davenport free of charge.  The recall is expected to begin on August 18, 2006.  06V-228