DEPARTMENT OF HOUSING AND URBAN DEVELOPMENT 	STRUCTURAL ENGINEERING

## Housing - Federal Housing Commissioner 	BULLETIN NO.

# TO: 	DIRECTORS, SINGLE FAMILY HOCs 	ISSUE DATE

# DIRECTORS, MULTIFAMILY HUBs

#### REVIEW DATE

##### SUBJECT: 	1.	 Item Description

- Name and address

of Manufacturer

This Structural Engineering Bulletin (SEB) should be filed with other SEBs and related Bulletins on materials or products as required by prescribed procedures.

1.	General:

This Bulletin sets forth specific requirements under the Technical Suitability of Products Program for determining the eligibility of housing to be constructed under HUD mortgage insurance, or other HUD housing programs.

2.	Scope:

This Bulletin applies only to the structural features of this method of construction.  Final determination of eligibility is made by the appropriate HUD Field Office. Other factors considered by the Field Office will be valuation, location, architectural planning and appeal, mechanical equipment, thermal characteristics, and market acceptance.  Consideration is also necessary to determine whether a specific property will qualify under the specific HUD program, when constructed according to the method outlined in this Bulletin, and where the structure is to be located.

-2-

In geographical areas subject to hurricanes, earthquakes, or other severe conditions affecting dwelling structures, the HUD Field Office or Homeownership Center shall require additional safeguards in proposed designs, when necessary.

3.	Minimum Property Standards (MPS):

Compliance with HUD MPS will be determined by the HUD Field Office or Homeownership Center on the same basis as submissions involving conventional construction, except for the special features described in this Bulletin.

4.	Inspection:

Field compliance inspections covering conventional items of construction and any special features covered in this Bulletin shall be made in accordance with prescribed procedures.

The appropriate HUD Field Office or Homeownership Center shall furnish a copy of a HUD field inspection report to Headquarters, FHA Standards, Office of Manufactured Housing Programs, when there is:

- Evidence of noncompliance with portions of the system of construction described in this Bulletin.

- Faulty shop fabrication, including significant surface defects.

- Damage to shop fabricated items or materials due to improper transportation, storage, handling or assembly.

- Unsatisfactory field workmanship or performance of the product or system.

- Any significant degradation or deterioration of the product or evidence of lack of durability or performance.

Periodic plant inspections will be made by HUD Field Office, Homeownership Center, State Agency personnel, or a HUD designated representative in accordance with their prescribed procedures.  Factory inspection reports shall be submitted to HUD Headquarters, upon request.

-3-

5.	Certification:

The manufacturer named in this Bulletin shall furnish the builder with a written certification stating that the product has been manufactured in compliance with the HUD Minimum Property Standards (MPS), except as modified by this Bulletin.  The Builder shall endorse the certification with a statement that the product has been erected in compliance with the HUD MPS except as modified by this Bulletin, and that the manufacturer's certification does not relieve the Builder, in any way, of responsibility under the terms of the Builder's Warranty required by the National Housing Act, or under any provisions applicable to any other housing program.  This certification shall be furnished to the HUD Field Office upon completion of the property.

OUTLINE DESCRIPTION, CATEGORY II CONSTRUCTION

GENERAL:

The NASCOR III wall system is a prefabricated wall panel intended for use as an above grade exterior load-bearing wall.  The primary components of the wall system are wood I-studs and expanded polystyrene (EPS) insulation infill panels, with factory installed single solid sawn lumber top and bottom plates.

All materials and methods of installation shall be in accordance with HUD Minimum Property Standards (MPS), Use of Materials Bulletins (UM), and Materials Releases (MR), except as may be specifically noted herein. Plumbing, heating and electrical systems are field installed and connected.

This Bulletin is based upon a structural review of the prefabricated wall panels of NASCOR Ltd., but may be considered applicable to all structurally similar units of this company.  Foundation design, dwelling design, and nonstructural items (such as architectural, plumbing, heating and electrical features) are not covered by this Bulletin.

SPECIFICATIONS:

Form HUD-92005, “Description of Materials” specifying only the structurally related items (Nos. 1 to 12, 14, 26, and 27), as originally submitted for determination of technical suitability, describes the materials that shall be used in construction of housing units under this system of construction. Form HUD-92005, furnished with each application for use under HUD housing programs, shall include as a minimum the same structural materials.

-4-

DRAWINGS:

The following drawing(s) by NASCOR Ltd. shall be considered an integral part of this Bulletin:

Drawing No.		Date	Description

Figure 1			July 2001	Nascor III Wall System

Figure 2			July 2001	Cross-Section of Nascor III Columns

Figure 3			July 2001	Nascor Infill Panel and Spline

The Builder shall submit construction drawing(s) to the HUD Field Office or Homeownership Center with each application under HUD housing programs, which shall include the same or similar structural features as shown on the drawings listed above.  Copies of these listed drawings shall also be furnished to the HUD Field Office or Homeownership Center by the Builder upon request.

SPECIAL  CONSTRUCTION  FEATURES:

NASCOR III wall system, nominal 8 to 16 feet high and 8 to 16 feet wide, are furnished in this method of construction. System consists of: (1) wood I-studs, (2) expanded polystyrene (EPS) insulation infill panels, (3) lumber top and bottom plates, and (4) fasteners.

- NASCOR III I-studs are prefabricated wood I-studs with structural wood flanges and a 3/8 inch thick oriented strand board (OSB) web. The I-studs are available in depths of 5-1/2 and 7-1/4 inches.

- Insulation infill panels shall be 5-1/2 or 7-1/4 inch thick by 92-13/16 inch high, Type 1, expanded polystyrene (EPS) produced from beads provided by BASF Corporation or Huntsman Chemical Corporation. The density is 1.0 pcf. The widths of the panels are 9-1/2, 13-1/2, and 21-1/2 inches for I-stud spacings of 12, 16, and 24 inches on center respectively. Each end of the panel is profiled to accept an EPS spline. The interior face of each panel has a 1 inch wide by 1-3/4 inch deep channel located 24 inches from the bottom of the panel. This channel, referred to as the electrical keyway aligns the 1-1/2 in. diameter opening in the I-studs to provide a continuous path through which electrical wiring can be installed. Foam insulation shall be separated from all inhabited and finished spaces by a thermal barrier that will stay in place after 15 minutes of fire exposure.

-5-

- Each fabricated wall panel is joined together by fasteners and a top and bottom plate. The plates consist of nominal 2 x 6 or 2 x 8 inch dimension lumber, depending on the thickness of the wall panel. Where the bottom of the plate is to be supported on a concrete or masonary fondation the lumber shall be naturally durable or pressure treated.

- Fasteners connecting the wood components of the wall system shall comply with Table 8 of this report. The fasteners used to connect the naturally durable or pressure treated bottom plate to the I-studs shall be hot-dipped zinc coated glavanized, stainless steel, silicon bronze, or copper.

DESIGN AND CONSTRUCTION REQUIREMENTS:

Design Loads: The method described in this Bulletin is based on a  Basic Wind Speed range of 70 - 110 mph and Exposure B, C, and D in accordance with ASCE 7-88.

The Builder shall submit structural calculations to the local HUD Office or Homeownership Center for wall assemblies which are to include openings in the system.

The Builder shall submit structural calculations to the local HUD Office or Homeownership Center if housing units are to be located in geographical areas where these conditions are exceeded.

| Table 1 – WOOD MEMBER DESCRIPTIONS |
| --- |
| Component | Size | Length | Species & Grade 1, 2 |
| Cripple & corner studs | 2x6 (R-20) 2x8 (R-30) | 92-5/8 in. Greater than 92-5/8 in. Up to 192 in. | Spruce-pine-fir stud grade Spruce-pine-fir No. 1 or 2 |
| Top & bottom plates, sills | 2x6 (R-20) 2x8 (R-30) | Varies | Spruce-pine-fir No. 1 or 2 |
| I-studs | 2x3 | 92-5/8 in. to 192 in. | Spruce-pine-fir No. 1 or 2 |
| Lintels | 2x10 or 2x12 | Varies | Spruce-pine fir No. 1 or 2 Douglas-fir-larch No. 1 or 2 |
| Notes: 1. Lumber is graded under standards recognized by the American Lumber Standards Committee (ALSC) or equivalent. 2. Lumber for I-stud column flanges is one-piece or finger jointed and meets requirements of NLGA Special Products Standard 1 (SPS-1). |

-6-

| Table 2 – Nascor R20 & R30 Column Design Properties |
| --- |
| Allowable Moment (ft-lbs) | Stiffness (x106 lbs-in.2) | Compressive Strength (psi) |
| 897 | 32.5 | 1150 |
| Notes: 1. Structural design properties for R20 and R30 columns are to be the same, and are based upon R20 capacities. |

| Table 3 – Nascor R20 Column Section Properties |
| --- |
| Area (in.2) | Moment of Inertia (in.4) | Section Modulus (in.3) |
| 7.50 | 23.214 | 8.44 |
| Notes: 1. Section properties are noted ignoring the web and the notch in the flange. 2. Structural design properties for R20 and R30 columns are to be the same, and are based upon R20 capacities. |

-7-

| Table 4 Total Allowable Gravity Load (plf) for R20 and R30 Columns for Exposure Class B |
| --- |
| Height (ft) | Spacing (in.) | BASIC WIND SPEED (mph) = (V) |
|  |  | 70 | 75 | 80 | 85 | 90 | 100 | 110 |
| 6 6 6 | 12 16 24 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 |
| 7 7 7 | 12 16 24 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4550 |
| 8 8 8 | 12 16 24 | 8289 6216 4031 | 8289 6216 4031 | 8289 6216 4031 | 8289 6216 3985 | 8289 6216 3903 | 8289 6055 3738 | 8193 5860 3564 |
| 9 9 9 | 12 16 24 | 7159 5171 3214 | 7159 5171 3214 | 7159 5171 3214 | 7098 5117 3165 | 6994 5021 3083 | 6781 4829 2914 | 6562 4628 2738 |
| 10 10 10 | 12 16 24 | 5832 4178 2555 | 5832 4178 2555 | 5832 4178 2555 | 5771 4124 2508 | 5668 4031 2427 | 5485 3841 2262 | 5241 3645 2089 |
| 11 11 11 | 12 16 24 | 4774 3391 2039 | 4774 3391 2039 | 4774 3391 2039 | 4715 3338 1993 | 4615 3248 1915 | 4412 3066 1755 | 4615 2877 1587 |
| 12 12 12 | 12 16 24 | 3937 2772 1635 | 3937 2772 1635 | 3937 2772 1635 | 3882 2721 1591 | 3786 2636 1516 | 3592 2460 1361 | 3392 2279 1197 |
| 13 13 13 | 12 16 24 | 3273 2282 1317 | 3273 2282 1317 | 3273 2282 1317 | 3220 2234 1275 | 3128 2151 1202 | 2943 1983 1051 | 2752 1808 -- |
| 14 14 14 | 12 16 24 | 2741 1890 1064 | 2741 1890 1064 | 2741 1890 1064 | 2690 1844 1023 | 2603 1766 952 | 2425 1603 -- | 2241 1433 -- |
| 15 15 15 | 12 16 24 | 2311 1574 860 | 2311 1574 860 | 2311 1574 860 | 2262 1530 -- | 2178 1454 -- | 2007 1296 -- | 1829 -- -- |
| Notes: 1. The total allowable gravity loads given in the table are per lineal foot of wall (plf). 2. A wind importance factor (I) of 1.00 was used in determining the wind load. 3. Design wind loads were determined in accordance with the main windforce resisting system. 4. Dashed entries correspond to designs which do not meet the L/240 deflection limit and/or exceed the allowable bending moment. |

-8-

| Table 5 Total Allowable Gravity Load (plf) for R20 and R30 Columns for Exposure Class C |
| --- |
| Height (ft) | Spacing (in.) | BASIC WIND SPEED (mph) = (V) |
|  |  | 70 | 75 | 80 | 85 | 90 | 100 | 110 |
| 6 6 6 | 12 16 24 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4636 |
| 7 7 7 | 12 16 24 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4576 | 9152 6864 4484 | 9152 6720 4371 | 9152 6836 4134 | 9152 6563 3883 |
| 8 8 8 | 12 16 24 | 8289 6170 3840 | 8289 6044 3727 | 8250 5913 3612 | 8106 5780 3492 | 7956 5643 3370 | 7647 5358 3114 | 7326 5061 2846 |
| 9 9 9 | 12 16 24 | 6912 4949 3018 | 6768 4817 2903 | 6621 4673 2786 | 6472 4547 2666 | 6318 4408 2543 | 6003 4120 2284 | 5677 3820 2011 |
| 10 10 10 | 12 16 24 | 5587 3957 2363 | 5445 3829 2251 | 5300 3698 2136 | 5153 3566 2018 | 5003 3428 1896 | 4695 3146 1640 | 4375 2852 1364 |
| 11 11 11 | 12 16 24 | 4537 3179 1854 | 4400 3055 1745 | 4261 2928 1633 | 4119 2800 1518 | 3975 2668 1398 | 3676 2393 1142 | 3366 2103 -- |
| 12 12 12 | 12 16 24 | 3711 2568 1457 | 3580 2449 1351 | 3446 2328 1242 | 3310 2204 1129 | 3172 2075 -- | 2883 1807 -- | 2582 -- -- |
| 13 13 13 | 12 16 24 | 3057 2087 1144 | 2932 1973 1042 | 2804 1856 -- | 2673 1735 -- | 2539 1610 -- | 2260 -- -- | 1965 -- -- |
| 14 14 14 | 12 16 24 | 2535 1703 896 | 2414 1593 -- | 2291 1479 -- | 2165 1361 -- | 2036 -- -- | -- -- -- | -- -- -- |
| 15 15 15 | 12 16 24 | 2112 1393 -- | 1997 1286 -- | 1878 -- -- | 1756 -- -- | -- -- -- | -- -- -- | -- -- -- |
| Notes: The total allowable gravity loads given in the table are per lineal foot of wall (plf). A wind importance factor (I) of 1.00 was used in determining the wind load. Design wind loads were determined in accordance with the main windforce resisting system Dashed entries correspond to designs which do not meet the L/240 deflection limit and/or exceed the allowable bending moment. |

-9-

| Table 6 Total Allowable Gravity Load (plf) for R20 and R30 Columns for Exposure Class D |
| --- |
| Height (ft) | Spacing (in.) | BASIC WIND SPEED (mph) = (V) |
|  |  | 70 | 75 | 80 | 85 | 90 | 100 | 110 |
| 6 6 6 | 12 16 24 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4936 | 9872 7404 4904 | 9872 7404 4635 |
| 7 7 7 | 12 16 24 | 9152 6864 4569 | 9152 6864 4440 | 9152 6864 4308 | 9152 6864 4170 | 9152 6720 4027 | 9101 6394 3727 | 8734 6048 3883 |
| 8 8 8 | 12 16 24 | 8218 5883 3584 | 8047 5726 3445 | 7873 5566 3301 | 7694 5400 3153 | 7510 5231 3000 | 7129 4879 2679 | 6730 4508 2335 |
| 9 9 9 | 12 16 24 | 6587 4652 2759 | 6412 4493 2618 | 6233 4330 2473 | 6050 4163 2323 | 5863 3992 2168 | 5478 3636 1840 | 5076 3260 1482 |
| 10 10 10 | 12 16 24 | 5266 3668 2110 | 5095 3512 1971 | 4920 3353 1828 | 4740 3188 1679 | 4558 3020 1523 | 4180 2669 1189 | 3783 2294 -- |
| 11 11 11 | 12 16 24 | 4229 2900 1607 | 4063 2749 1471 | 3894 2594 1330 | 3721 2434 1181 | 3544 2270 -- | 3176 1922 -- | 2786 -- -- |
| 12 12 12 | 12 16 24 | 3415 2300 1217 | 3256 2154 1083 | 3094 2004 -- | 2926 1847 -- | 2755 1686 -- | 2395 -- -- | -- -- -- |
| 13 13 13 | 12 16 24 | 2774 1828 -- | 2621 1687 -- | 2464 1540 -- | 2302 -- -- | 2135 -- -- | -- -- -- | -- -- -- |
| 14 14 14 | 12 16 24 | 2535 1453 -- | 2115 -- -- | 1962 -- -- | 1804 -- -- | -- -- -- | -- -- -- | -- -- -- |
| 15 15 15 | 12 16 24 | 1850 -- -- | 1706 -- -- | -- -- -- | -- -- -- | -- -- -- | -- -- -- | -- -- -- |
| Notes: The total allowable gravity loads given in the table are per lineal foot of wall (plf). A wind importance factor (I) of 1.00 was used in determining the wind load. Design wind loads were determined in accordance with the main windforce resisting system. Dashed entries correspond to designs which do not meet the L/240 deflection limit and/or exceed the allowable bending moment. |

-10-

| Table 7 – Maximum Allowable Shear Values (plf) for Wood Structural Panel Shear Walls with Framing of Nascor III Columns |
| --- |
| Column Spacing | Fastening | Sheathing | Allowable Shear |
| 24 in. on center | 2-1/2 in. common nails spaced at 3 in. on center at panel perimeter and 12 in. on center at intermediate supports | 5/16 in. thick OSB | 250 |
| 24 in. on center | 1-5/8 in. gypsum board screws at 4 in. on center | 1/2 in. thick vertical gypsum wallboard | 125 |
| 24 in. on center | 1-5/8 in. gypsum board screws at 7 in. on center | 1/2 in. thick vertical gypsum wallboard | 100 |

Table 8 - Fasteneing Schedule

| Connection | Fastener |
| --- | --- |
| Top plate to I-stud (end screw) | 2 - 3 in. long wood screw |
| I-stud to bottom plate (end screw) | 2 - 3 in. long wood screw |
| Cripples to lintel (end screw) | 2 - 3 in. long wood screw |
| Doubled lintel (face nail) | 5 in. long spiral nail - 2 rows @ 16 in. o.c. |
| Top plate to lintel (face screw) | 3 in. long wood screw @ 16 in. o.c. |
| Sill plates to cripples (toe screw) | 2 - 3 in. long wood screw @ each end |
| I-stud to end post (face screw) | 3 in. long wood screw @ 24 in. o.c. |
| Corner connection (toe nail) | 3-1/4 in. long common wire nails @ 16 in. o.c. |

Figure 1

NASCOR III WALL SYSTEM

-11-

Figure 2

CROSS-SECTION OF

NASCOR III COLUMNS

Figure 3

NASCOR INFILL PANEL AND SPLINE

-12-

MANUFACTURING PLANT(S):

Wall panels covered under this Bulletin will be produced in the following plant:

NASCOR Ltd.

1212 34th Avenue

Calgary, Alberta, Canada  T2G1V7

Ph. 403-243-8919

The appropriate HUD Field Office or Homeownership Center in whose jurisdiction the manufacturing plant is located, or HUD designated representative will inspect this plant in accordance with prescribed procedures.

QUALITY CONTROL:

The appropriate HUD Field Office or Homeownership Center in whose jurisdiction the manufacturing plant is located, or the State Agency (in Category III states) shall review and approve plant fabrication procedures and quality control program, to ensure compliance with approved plans and specifications.  The quality control program shall include field erection or supervision by NASCOR Ltd.

RECORD OF PROPERTIES:

The manufacturer shall provide HUD a list of the first ten properties in which the component or system described in this Bulletin is used.  The list shall include the complete address, or description of location, and approximate date of installation or erection.  Failure of the manufacturer to provide HUD with the above information may result in cancellation of this Bulletin.

NOTICE OF CHANGES:

The manufacturer shall inform HUD in advance of changes in production facilities, transportation, field erection procedures, design, or materials used in this product.  Further, the manufacturer must inform HUD of any revision to corporate structure, change of address or change in name or affiliation of the prime manufacturer.  Failure of the manufacturer to notify HUD of any of the above changes may result in cancellation of this Bulletin.

-13-

EVALUATION:

This SEB is valid for a period of three years from the date of initial issuance or most recent renewal or revision, whichever is later.  The holder of this SEB shall apply for a renewal or revision 90 days prior to the Review Date printed on this SEB.  Submittals for renewal or revision shall be sent to:

U. S. Department of Housing and Urban Development

FHA Standards, Office of Manufactured Housing Programs

451 Seventh Street, SW, Room 9168

Washington, DC  20410-8000

Additionally, the appropriate User Fee shall be sent to:

U. S. Department of Housing and Urban Development

Miscellaneous Income – Technical Suitability of Products Fees

Bank of America

P. O. Box 198762

Atlanta, GA  30384-8762

The holder of this SEB may apply for revision at any time prior to the Review Date.  Minor revisions may be in the form a supplement.

If the Department determines that a proposed renewal or supplement constitutes a revision, the appropriate User Fee for a revision will need to be submitted in accordance with Code of Federal Regulations 24 CFR 200.934, "User Fee System for the Technical Suitability of Products Program", and current User Fee Schedule.

CANCELLATION:

Failure to apply for a renewal or revision shall constitute a basis for cancellation of the SEB. HUD will notify the manufacturer that the SEB may be canceled when:

- conditions under which the document was issued have changed so as to affect production of, or to compromise the integrity of the accepted material, product, or system,

- the manufacturer has changed its organizational form without notifying  HUD, or

- the manufacturer has not complied with responsibilities it assumed as a condition of HUD's acceptance.

-14-

However, before cancellation, HUD will give the manufacturer a written notice of the specific reasons for cancellation, and the opportunity to present views on why the SEB should not be canceled. No refund of fees will be made on a canceled document.

****************************************************************************

This Structural Engineering Bulletin is issued solely for the captioned firm and is not transferable to any person or successor entity.

****************************************************************************

# Text boxes

NASCOR Ltd.

1212 34th Avenue

Calgary, Alberta, Canada T2G1V7

NASCOR III Wall System

April 11, 2009

April 11, 2006

(Supersedes issue dated

January 14, 2002)

1129 Rev. 1

The technical description, requirements and limitations expressed herein do not constitute an endorsement or approval by the Department of housing and Urban Development (HUD) of the subject matter, and any statement or representation, however made, indicating approval or endorsement by HUD is unauthorized and false, and will be considered a violation of the United States Criminal Code, 18 U.S.C. 709.

NOTICE: THIS BULLETIN APPLIES TO DWELLING UNITS BUILT UNDER HUD HOUSING PROGRAMS. NON-HUD-INSURED UNITS MAY OR MAY NOT BE IN CONFORMINTY WITH THE REQUIREMENTS OF THE HUD MINIMUM PROPERTY STANDARDS.

Any reproduction of this Bulletin must be in its entirety and any use of all or any part of this Bulletin in sales promotion or advertising is prohibited.