NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 03/13/2006, 12/20/2006

LOCATION: Fort Payne (Highway 35)

STREAM: Big Wills Creek

BASIN: Coosa                            HSA: HUN

REFERENCES:

USGS Description of gaging station, prepared 05/24/2005.

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level	TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: BGWA1

NWS INDEX NUMBER:

USGS NUMBER:

MAP OF GAGE LOCATION

LATITUDE: 34 26 17  		SOURCE:

LONGITUDE: 85 46 02

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                     HSA: HUN          NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:                  VERTICAL DATUM:

LEVELING AGENCY AND DATE:                        CHECKBAR:

RATING AGENCY:

BENCHMARK     DESCRIPTION                                                                   GAGE ZERO      DATUM

----------------------------------------------------------------------------------------    ---------     -------

RM1           HIGHWAY TABLET LOCATED ON LEFT DOWNSTREAM WINGWALL.                                          31.554

RM2           SQUARE LOCATED ON LEFT DOWNSTREAM FOOTING AT WINGWELL.                                       27.187

RM3           SQUARE LOCATED ON LEFT UPSTREAM WINGWALL.                                                    28.459

RP1           TOP OF RIGHTSIDE OF WIRE WEIGHT BRACKET.                                                     32.011

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                     HSA: HUN          NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID: 02400680                TYPE OF TELEMETRY:

OWNER: USGS                                OWNER:

REPORT TIME: 00:59                        PHONE NUMBER:

INTERVAL: 60                               INTERVAL:

PAYOR/COST OF LINE:  / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- -----------------------------------------------

crest       USGS        USGS        10/03/2002

pres trans  USGS        USGS        10/03/2002

wireweight  USGS        USGS        10/03/2002

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                          HSA: HUN           NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

crest                     USGS        10/03/2002

pres trans                USGS        10/03/2002

wireweight                USGS        10/03/2002

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                          HSA: HUN           NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 11.00    ACTION STAGE: 10.00     BANKFULL STAGE:

FLOOD FLOW:           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ------------------------------------------

02/22/2003 17:45   12.16                                       flow is normally around 5.0 feet

05/06/2003 12:00   14.19

02/06/2004 11:00    9.75

09/17/2004 06:00   13.43

12/10/2004 03:00   11.13

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                    HSA: HUN           NWS FORM E-19 PAGE 5: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                   HSA: HUN            NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH:            DRAINAGE AREA: 55.4       POOL STAGE:

STREAM BED: Straight at approach, but curves slightly to the right ds.

REACH: Approximately 2 miles upstream to 1/2 mile downstream.

REGULATION: None.

DIVERSION: None.

WINTER: None.

TOPOGRAPHY: Valley at base of Sand Mountain.

REMARKS:

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                     HSA: HUN          NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  ----------------------------------------------------------------------------------------------------

10.00  THE RIVER REACHES BANKFULL NEAR THE GAGE SITE.

11.00  THE RIVER SPILLS OVER THE BANKS INTO A WIDE FLOOD PLAIN NEAR THE GAGE SITE.

13.00  FLOOD WATERS BEGIN TO APPROACH ROADS AND BUSINESSES NORTH OF INTERSTATE 59 IN FORT PAYNE.

20.00  WIDESPREAD FLOODING IS OCCURRING ON THE NORTH SIDE OF FORT PAYNE. NUMEROUS ROADS AND BUSINESSES ARE

FLOODED BY SEVERAL FEET OF WATER. THE HOSPITAL IS CUT OFF FROM HIGHWAY 35 BY FLOOD WATERS.

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                       HSA: HUN        NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  25-|

|-----|

|-----|

|-----|

|-----|

|  23-|

|-----|

|-----|

|-----|

|-----|

|  21-|

|-----|

|-----|

20.00 - WIDESPREAD FLOODING IS OCCURRING ON THE NORTH SIDE OF FORT PAYNE. NUMEROUS ROADS AND    |-----|

BUSINESSES ARE FLOODED BY SEVERAL FEET OF WATER. THE HOSPITAL IS CUT OFF FROM           |-----|

HIGHWAY 35 BY FLOOD WATERS.                                                             |  19-|

|-----|

|-----|

|-----|

|-----|

|  17-|

|-----|

|-----|

|-----|

|-----|

|  15-|

|-----|

|-----|

|-----|   14.19  05/06/2003

|-----|   13.43  09/17/2004

|  13-|

13.00 - FLOOD WATERS BEGIN TO APPROACH ROADS AND BUSINESSES NORTH OF INTERSTATE 59 IN FORT      |-----|

PAYNE.                                                                                  |-----|

|-----|   12.16  02/22/2003

|-----|

|  11-|   11.13  12/10/2004

11.00 - THE RIVER SPILLS OVER THE BANKS INTO A WIDE FLOOD PLAIN NEAR THE GAGE SITE.             |-----|

|-----|

10.00 - THE RIVER REACHES BANKFULL NEAR THE GAGE SITE.                                          |-----|

|-----|    9.75  02/06/2004

|   9-|

|-----|

|-----|

|-----|

|-----|

|   7-|

|-----|

|-----|

|-----|

|-----|

|   5-|

REACH: Approximately 2 miles upstream to 1/2 mile downstream.                          	ELEVATION ZERO:     nan

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                      HSA: HUN         NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

1  Susan Battles

DeKalb County EMA

2  Jason Elliott

NWS Huntsville

LOCATION: Big Wills Creek NEAR Fort Payne (Highway 35), AL          Revised, Printed Dates: 03/13/2006, 12/20/2006

ID: BGWA1                                       HSA: HUN       NWS FORM E-19 PAGE 10: CONTACTS

photo at gage site