International is recalling 2 MY 2005-2006 5600I and 5900I trucks built with a 8X6 wheel configuration (Tridems) fail to comply with the requirements of Federal Motor Vehicle Safety Standard No. 121, 'Air Brake Systems.'  The as-built air brake component size and configuration are inadequate for the extended wheelbases causing the mid-rear and rear-rear axle brake apply timing to be noncompliant with the standard. The longer brake apply time may result in extended stopping distances, which could result in a crash.  Dealers will change the air hosing (to 3/4" diameter) from the air tank; air hosing (to 3/4") from the abs-modulator valves to service brake quick release valves; and the service brake quick release valves will be upgraded with larger ports to accommodate higher air flow free of charge.  The recall is expected to begin on February 10, 2006.  05V-569