CQC ACCESSIBILITY INSPECTION REPORT

CONTRACT NO._________________________   REPORT NO. _____________	SHEET _____ OF _________

Note:  This report covers only the most common accessibility requirements. This form can be expanded as needed for elements not shown. Inspect for compliance with all requirements of the ABAAS.

| CQC Inspector: | Date: |
| --- | --- |
| Parking and Passenger Loading Zones: Attach grading plan with running and cross slope readings noted. Yes No Accessible parking spaces and access aisles running slope and cross slope is 1:48 (2%) or less. Yes No Car spaces are at least 96 inches wide and van spaces 132 inches wide, and have an adjacent access aisle. Yes No Access aisles are 60 inches wide min. and adjoin an accessible route. Yes No Curb ramps meet slope requirements for ramps and have 36 inch minimum landing length at top of ramp. Yes No Curb ramp flared side slopes are 1:10 (10%) or less. Inspection Results: Corrective Actions Needed/Taken: |

SHEET _____ OF _________

Walking surfaces and Accessible Route: The accessible route is defined as the pedestrian route from the accessible parking and passenger loading zones to all accessible facilities and features. Attach grading plan with accessible route highlighted and running and cross slope readings noted. Yes No Floor and ground surfaces are stable, firm, and slip resistant as defined by ADAABAAG Advisory 302.1 Yes No Running slope of all walking surfaces on the accessible route is 1:20 (5%) or less. Yes No Cross slope of walking surfaces is 1:48 (2%) or less. Yes No Clear widths of walking surfaces are 36 inches minimum. Yes No Elongated openings in floor or ground surfaces are 1/2 inch wide or less. Yes No Elongated openings are perpendicular to direction of travel. Yes No Accessible route surface changes are 1/2 inch or less with 1/4 inch maximum vertical change. Yes No Floor drains and grates on accessible route meet all above requirements Inspection Results: Corrective Actions Needed/Taken:

Ramps: Ramps are defined as walking surfaces on the accessible route that are steeper than 1:20 (5%) but less than 1:12 (8.33%). Attach grading plan with running and cross slope readings noted. Yes No Running slope is 1:12 (8.33%) or less. Measured at 2-foot intervals. Yes No Cross slope is 1:48 (2%) or less. Measured at 2-foot intervals. Yes No Clear width is 36 inches minimum, clear width between handrails is 36 inches minimum. Yes No Rise for any ramp run is 30 inches maximum. Yes No Ramps have landings at the top and the bottom of each ramp run. Yes No Landing clear length is 60 inches minimum, running slope and cross slope of landing is 1:48 (2%) or less. Yes No Ramps with a rise greater than 6 inches have handrails. Yes No Ramps and landings have edge protection on both sides that prevents passage of a 4 inch diameter sphere. Inspection Results: Corrective Actions Needed/Taken:

SHEET _____ OF _________

4. Handrails: Yes No Top of handrail is 34 inches minimum and 38 inches maximum vertically above walking surfaces. Yes No Handrails extend 12 inches minimum beyond the top and bottom of ramp runs. Yes No Handrails extend horizontally 12 inches minimum at top of stairs. Yes No Handrails extend at slope of the stair flight at bottom of stairs minimum one tread depth beyond last riser. Yes No Handrail clearance is 1 ½ inches clear minimum to walls and above horizontal attachments. Inspection Results: Corrective Actions Needed/Taken:

5. Drinking fountains (Two spout heights required for each drinking fountain): Yes No Spout outlet is 36 inches maximum above the finish floor or ground for wheelchair accessible spout. Yes No Spout outlet for standing persons is 38 inches minimum and 43 inches maximum above the finish floor. Yes No Drinking fountain is recessed or has 27 inches maximum space from floor to bottom of fountain. Inspection Results: Corrective Actions Needed/Taken:

SHEET _____ OF _________

6. Toilet Compartments: Attach floor plan with as-constructed dimensions noted. Yes No Wheelchair accessible compartment is 60 inches wide min., and 59 inches deep minimum. Yes No Ambulatory stall is 60 inches deep min. width of 35 inches min. and 37 inches max, toilet is centered in stall. Yes No Accessible compartment has 32 inch wide door opening minimum with door opening outward, or adequate clear space for door opening inward. Yes No Seat height is 17 inches minimum and 19 inches maximum measured to the top of the seat. Yes No Urinal rim is 17 inches maximum above the finish floor and 13 1/2 inches deep minimum. Yes No Urinal has a clear floor space of 30 inches wide by 48 inches long minimum. Yes No Side wall grab bar is 42 inches long minimum, located 12 inches maximum from the rear wall. Yes No Rear wall grab bar is 36” long min. extends from toilet centerline 12” min. one side, 24” min. other side. Yes No Grab bar height is 33 inches minimum and 36 inches maximum. Yes No Toilet paper dispensers are 7 inches min. and 9 inches max. in front of the toilet to centerline of the dispenser. Yes No Toilet paper dispenser outlet is 15 inches minimum and 48 inches maximum above the finish floor. Yes No Centerline of the wheelchair stall toilet is 16 inches min. to 18 inches max. from the side wall. Yes No Sinks and counters are 34 inches max. above the finish floor with 27 inches min. knee space. Sink drain pipes are insulated, or concealed. Inspection Results: Corrective Actions Needed/Taken:

7. Service Counters, Dining and Work Surfaces: (Service counters are parallel or forward approach) Yes No Parallel Approach. Counter is 36 inches long min. and 36 inches high max. Yes No Forward Approach. Counter surface is 30 inches long min. and 36 inches high max, knee space under counter. Yes No Tops of dining and work surfaces are 28 inches minimum and 34 inches maximum above the finish floor. Inspection Results: Corrective Actions Needed/Taken:

SHEET _____ OF _________

| 8. Doors: Yes No Door openings on accessible routes provide a clear width of 32 inches minimum. Yes No Door closers move door from open position of 90 degrees to 12 degrees from the latch is 5 seconds min. Yes No Spring hinge doors close from open position of 70 degrees to closed position in 1.5 seconds minimum. Yes No Fire doors have the minimum opening force allowable by the appropriate administrative authority. Yes No Interior hinged doors have an opening force of 5 pounds maximum. Inspection Results: Corrective Actions Needed/Taken: |
| --- |
| 9. Signs: Yes No Parking space signs are 60 inches minimum above finish ground surface measured to the bottom of the sign. Yes No Van parking space sign includes the designation "van accessible". Yes No Tactile characters on signs are 48 inches minimum and 60 inches maximum above the finish floor. Yes No Sign is located alongside the door at the latch side. Yes No Sign is located with a clear floor space of 18 inches by 18 inches minimum. Inspection Results: Corrective Actions Needed/Taken: |
| CERTIFICATION: I certify that the above inspection report is complete and correct and that this inspection is in compliance with the contract documents. |
|  | Signature of Inspector |