The Storage Resource Manager

Web Services

Operational Interface Specification

Version 2.2

8 June 2006

| Collaboration Web: | http://sdm.lbl.gov/srm-wg |
| --- | --- |
| Document Location: | http://sdm.lbl.gov/srm-wg/doc/SRM.v2.2.ws.op.pdf |

| Editors: |
| --- |
| Alex Sim | Lawrence Berkeley National Laboratory |

| Contributors: |
| --- |
| Timur Perelmutov Don Petravick | Fermi National Accelerator Laboratory (FNAL), USA |
| Junmin Gu Arie Shoshani | Lawrence Berkeley National Laboratory (LBNL), USA |
| Olof Barring Jean-Philippe Baud Shaun De Witt | LHC Computing Project (LCG, CERN), Switzerland |
| Jens Jensen Owen Synge | Rutherford Appleton Laboratory (RAL), England |
| Michael Haddox-Schatz Bryan Hess Andy Kowalski Chip Watson | Thomas Jefferson National Accelerator Facility (TJNAF), USA |

Copyright Notice

© Copyright Lawrence Berkeley National Laboratory (LBNL), Fermi National Accelerator Laboratory (FNAL), Jefferson National Accelerator Facility (JLAB), Rutherford Appleton Laboratory (RAL) and European Organization for Nuclear Research (CERN) 2000, 2001, 2002, 2003, 2004, 2005, 2006. All Rights Reserved.

Permission to copy and display this “The Storage Resource Manager Interface Specification” (“this paper"), in any medium without fee or royalty is hereby granted, provided that you include the following on ALL copies of this paper, or portions thereof that

you make:

1. A link or URL to this paper at this location.

2. This Copyright Notice as shown in this paper.

THIS PAPER IS PROVIDED "AS IS," AND Lawrence Berkeley National Laboratory, Fermi National Accelerator Laboratory, Jefferson National Accelerator Facility, Rutherford Appleton Laboratory and European Organization for Nuclear Research (COLLECTIVELY, THE “COLLABORATION”) MAKE NO REPRESENTATIONS OR WARRANTIES, EXPRESS OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, WARRANTIES OF  MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT OR TITLE; THAT THE CONTENTS OF THIS PAPER ARE SUITABLE FOR ANY PURPOSE; NOR THAT THE IMPLEMENTATION OF SUCH CONTENTS WILL NOT INFRINGE ANY THIRD PARTY PATENTS, COPYRIGHTS, TRADEMARKS OR OTHER RIGHTS.

THE COLLABORATION WILL NOT BE LIABLE FOR ANY DIRECT, INDIRECT, SPECIAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF OR RELATING TO ANY USE OR DISTRIBUTION OF THIS PAPER.

The names and trademarks of the Collaboration may NOT be used in any manner, including advertising or publicity pertaining to this paper or its contents, without specific, written prior permission. Title to copyright in this paper will at all times remain with the Collaboration.

No other rights are granted by implication, estoppel or otherwise.

PORTIONS OF THIS PAPER WERE PREPARED AS AN ACCOUNT OF WORK FUNDED BY U.S. Department of Energy AT UNIVERSITY OF CALIFORNIA'S LAWRENCE BERKELEY NATIONAL LABORATORY. NEITHER THE AUTHORS, NOR THE UNITED STATES GOVERNMENT OR ANY AGENCY THEREOF, NOR THE UNIVERSITY OF CALIFORNIA, NOR ANY OF THEIR EMPLOYEES OR OFFICERS, NOR ANY OTHER COPYRIGHT HOLDERS OR CONTRIBUTORS, MAKES ANY WARRANTY, EXPRESS OR IMPLIED, OR ASSUMES ANY LEGAL LIABILITY OR RESPONSIBILITY FOR THE ACCURACY, COMPLETENESS, OR USEFULNESS OF ANY INFORMATION, APPARATUS, PRODUCT, OR PROCESS DISCLOSED, OR REPRESENTS THAT ITS USE WOULD NOT INFRINGE PRIVATELY OWNED RIGHTS. REFERENCE HEREIN TO ANY SPECIFIC COMMERCIAL PRODUCT, PROCESS, OR SERVICE BY TRADE NAME, TRADEMARK, MANUFACTURER, OR OTHERWISE, DOES NOT NECESSARILY CONSTITUTE OR IMPLY ITS ENDORSEMENT, RECOMMENDATION, THE UNITED STATES GOVERNMENT OR ANY AGENCY THEREOF OR ANY OTHER COPYRIGHT HOLDERS OR CONTRIBUTORS. THE VIEW AND OPINIONS OF AUTHORS EXPRESSED HEREIN DO NOT NECESSARILY STATE OR REFLECT THOSE OF THE UNITED STATES GOVERNMENT OR ANY AGENCY THEREOF, OR THE ENTITY BY WHICH AN AUTHOR MAY BE EMPLOYED.

This paper preparation has been partially supported  by the Office of Energy Research, Office of Computational and Technology Research, Division of Mathematical, Information, and Computational Sciences, of the U.S. Department of Energy under Contract No. DE-AC03-76SF00098.

The U.S. Government retains for itself, and others acting on its behalf, a paid-up, nonexclusive, irrevocable worldwide license in said article to reproduce, prepare derivative works, distribute copies to the public, and perform publicly and display publicly, by or on behalf of the Government.

Table of Contents

Introduction	6

1. Common Types	9

1.1. Simple Types	9

1.2. Complex Types	12

2. Space Management Functions – Message Types and Operations	18

2.1. srmReserveSpace	18

2.2. srmStatusOfReserveSpaceRequest	20

2.3. srmReleaseSpace	22

2.4. srmUpdateSpace	23

2.5. srmGetSpaceMetaData	24

2.6. srmChangeSpaceForFiles	25

2.7. srmStatusOfChangeSpaceForFilesRequest	28

2.8. srmExtendFileLifeTimeInSpace	30

2.9. srmPurgeFromSpace	31

2.10. srmGetSpaceToken	33

3. Permission Functions – Message Types and Operations	35

3.1. srmSetPermission	35

3.2. srmCheckPermission	36

4. Directory Functions – Message Types and Operations	38

4.1. srmMkdir	38

4.2. srmRmdir	39

4.3. srmRm	39

4.4. srmLs	41

4.5. srmStatusOfLsRequest	43

4.6. srmMv	44

5. Data Transfer Functions – Message Types and Operations	46

5.1. srmPrepareToGet	46

5.2. srmStatusOfGetRequest	49

5.3. srmBringOnline	51

5.4. srmStatusOfBringOnlineRequest	54

5.5. srmPrepareToPut	57

5.6. srmStatusOfPutRequest	59

5.7. srmCopy	62

5.8. srmStatusOfCopyRequest	65

5.9. srmReleaseFiles	68

5.10. srmPutDone	70

5.11. srmAbortRequest	71

5.12. srmAbortFiles	72

5.13. srmSuspendRequest	73

5.14. srmResumeRequest	74

5.15. srmGetRequestSummary	75

5.16. srmExtendFileLifeTime	76

5.17. srmGetRequestTokens	78

6. Discovery Functions – Message Types and Operations	80

6.1. srmGetTransferProtocols	80

6.2. srmPing	80

7. Appendix	82

7.1. Status Code Specification	82

7.2. SRM WSDL discovery method	83

# Introduction

This document contains the interface specification of SRM 2.2.  It incorporates the functionality of SRM 2.0 and SRM 2.1, but is much expanded to include additional functionality, especially in the area of dynamic storage space reservation and directory functionality in client-acquired storage spaces.

This document reflects the discussions and conclusions of a 2-day meeting in May 2006, as well as email correspondence and conference calls.  The purpose of this activity is to further define the functionality and standardize the interface of Storage Resource Managers (SRMs) – a Grid middleware component.

The document is organized in four sections.  The first, called “Defined Structures” contain all the type definitions used to define the functions (or methods).  The next 5 sections contain the specification of “Space Management Functions”, “Permission Functions”, “Directory Functions”, “Data Transfer Functions” and “Discovery Functions”.  All the “Discovery Functions” are newly added functions.

It is advisable to read the document SRM.v2.2.changes.doc posted at http://sdm.lbl.gov/srm-wg before reading this specification.

Each function from the functional interface specification is mapped into a separate WS portType request-response operation. The request-response operation is message exchange between the client and the endpoint, in which the request message is received by the endpoint and the endpoint sends back the response message. In the WSDL1.1 the message either an enumeration of its parts, or is of some complex type. If message is an enumeration, then each part is required and we can not express their options. If message is an instance of a complex type, then all the flexibility of the XML Schema can be applied to the definition of this type. So, express the options of some of the SRM function arguments in functional interface specification, we use the approach of defining a separate type for each request and the response message. Unfortunately,  some wsdl toolkit (at least it is true in case of Apache Axis and gSoap), this leads to the generation of the stubs with one input argument of request  message  type and one output argument of response message type. These are not limitations of the WSDL, but of the particular wsdl stab generation toolkits.

For notes and comments for each function, please refer to the functional specification (see http://sdm.lbl.gov/srm-wg/doc/SRM.spec.v2.2.html).

Understandings and Agreements

- By “https” we mean http protocol with GSI authentication. It may be represented as “httpg”. At this time, any implementation of http with GSI authentication could be used. It is advisable that the implementation is compatible with Globus Toolkit 3.2 or later versions.

- We use GSI proxy from the underlying https protocol to authenticate the caller.

- Primitive types used below are consistent with XML build-in schema types: i.e.

  - long is 64bit: (+/-) 9223372036854775807

  - int is 32 bit: (+/-) 2147483647

  - short is 16 bit: (+/-) 32767

  - unsignedLong ranges (inclusive): 0 to18446744073709551615

  - unsignedInt ranges (inclusive): 0 to 4294967295

  - unsignedShort ranges (inclusive): 0 to 65535

- The definition of the type “anyURI” is compliant with the XML standard. See http://www.w3.org/TR/xmlschema-2/#anyURI.   It is defined as: "The lexical space of anyURI is finite-length character sequences which, when the algorithm defined in Section 5.4 of [XML Linking Language] is applied to them, result in strings which are legal URIs according to [RFC 2396], as amended by [RFC 2732]".

- In “localSURLInfo”, we mean local to the SRM that is processing the request.

- storageSystemInfo is added in the arguments of functions srmPrepareToGet() srmPrepareToPut() and srmCopy(). This is to simplify the case when all files sent to the request share the same storageSystemInfo. If storageSystemInfo is provided at the request level and the file level, SRM will use the one provided at the file level.

- authorizationID : from the SASL RFC 2222
During the authentication protocol exchange, the mechanism performs authentication, transmits an authorization identity (frequently known as a userid) from the client to server…. The transmitted authorization identity may be different than the identity in the client’s authentication credentials. This permits agents such as proxy servers to authenticate using their own credentials, yet request the access privileges of the identity for which they are proxying. With any mechanism, transmitting an authorization identity of the empty string directs the server to derive an authorization identity from the client’s authentication credentials.

- For SOAP inter-operability, we recommend Apache Axis for Java ( see http://ws.apache.org/axis/) or gSOAP for C/C++ from FSU (see http://www.cs.fsu.edu/~engelen/soap.html).

- Regarding file sharing by the SRM, it is a local implementation decision.  An SRM can choose to share files by proving multiple users access to the same physical file, or by copying a file into another user’s space.  Either way, if an SRM chooses to share a file (that is, to avoid reading a file over again from the source site) the SRM should check with the source site whether the user has a read/write permission. Only if permission is granted, the file can be shared.

- The word “pinning” is limited to the “copies” or “states” of SURLs and the Transfer URLs (TURLs).

- For each function, status codes are defined with basic meanings for the function. Only those status codes are valid for the function. Specific cases are not stated for each status code. If other status codes need to be defined for a specific function, send an email to the collaboration to discuss the usage.

# Common Types

We define the SRM WSDL namespace as following:

targetNamespace="http://srm.lbl.gov/StorageResourceManager"

xmlns:impl="http://srm.lbl.gov/StorageResourceManager"

wsdl:portType name="ISRM"

wsdl:binding name="srmSoapBinding" type="impl:ISRM"

wsdlsoap:binding style="rpc" transport="http://schemas.xmlsoap.org/soap/http"

wsdl:service name="SRMService"

wsdl:port name="srm" binding="impl:srmSoapBinding"

Notation:

- Underlined attributes are REQUIRED and non-nillable.

- Brackets [] are to show an arrayType.

- Min and Max are to show the number of occurrences of elements in a sequence. This can be interpreted as nillable.

## Simple Types

| name | type |
| --- | --- |
| TFileStorageType | xsd:string enum {Volatile, Durable, Permanent} |
| TFileType | xsd:string enum {File, Directory, Link} |
| TRetentionPolicy | xsd:string enum {REPLICA , OUTPUT , CUSTODIAL} |
| TAccessLatency | xsd:string enum {ONLINE, NEARLINE} |
| TPermissionMode | xsd:string enum {NONE, X, W, WX, R, RX, RW, RWX} |
| TPermissionType | xsd:string enum {ADD, REMOVE, CHANGE} |
| TRequestType | xsd:string enum {PREPARE_TO_GET, PREPARE_TO_PUT, COPY, BRING_ONLINE, RESERVE_SPACE, UPDATE_SPACE, CHANGE_SPACE_FOR_FILES. LS } |
| TOverwriteMode | xsd:string enum {Never, Always, WhenFilesAreDifferent} |
| TFileLocality | xsd:string enum { ONLINE, NEARLINE, ONLINE_AND_NEARLINE, LOST, NONE, UNAVAILABLE } |

TRetentionPolicy

  - Quality of Retention (Storage Class) is a kind of Quality of Service. It refers to the probability that the storage system lose a file. Numeric probabilities are self-assigned.

    - Replica quality has the highest probability of loss, but is appropriate for data that can be replaced because other copies can be accessed in a timely fashion.

    - Output quality is an intermediate level and refers to the data which can be replaced by lengthy or effort-full processes.

    - Custodial quality provides low probability of loss.

  - The type will be used to describe retention policy assigned to the files in the storage system, at the moments when the files are written into the desired destination in the storage system. It will be used as a property of space allocated through the space reservation function. Once the retention policy is assigned to a space, the files put in the reserved space will automatically be assigned the retention policy of the space. The assigned retention policy on the file can be found thought the TMetaDataPathDetail structure returned by the srmLs function.

TAccessLatency

- Files may be Online, Nearline or Offline. These terms are used to describe how latency to access a file is improvable. Latency is improved by storage systems replicating a file such that its access latency is online.

  - The ONLINE cache of a storage system is the part of the storage system which provides file with online latencies.

  - ONLINE has the lowest latency possible. No further latency improvements are applied to online files.

  - NEARLINE file can have their latency improved to online latency automatically by staging the file to online cache.

  - For completeness, we also describe OFFLINE here.

  - OFFLINE files need a human to be involved to achieve online latency.

  - For the SRM we only keep ONLINE and NEARLINE.

- The type will be used to describe a space property that access latency can be requested at the time of space reservation. The content of the space, files may have the same or “lesser” access latency as the space.

TFileLocality

  - Files may be located online, nearline or both. This indicates if the file is online or not, or if the file reached to nearline or not. It also indicates if there are online and nearline copies of the file.

    - The ONLINE indicates that there is a file on online cache of a storage system which is the part of the storage system, and the file may be accessed with online latencies.

    - The NEARLINE indicates that the file is located on nearline storage system, and the file may be accessed with nearline latencies.

    - The ONLINE_AND_NEARLINE indicates that the file is located on online cache of a storage system as well as on nearline storage system.

    - The LOST indicates when the file is lost because of the permanent hardware failure.

    - The NONE value shall be used if the file is empty (zero size).

    - The UNAVAILABLE indicates that the file is unavailable due to the temporary hardware failure.

  - The type will be used to describe a file property that indicates the current location or status in the storage system.

| name | type |
| --- | --- |
| TAccessPattern | xsd:string enum { TransferMode, ProcessingMode } |
| TConnectionType | xsd:string enum { WAN, LAN } |
| TStatusCode | xsd:string enum { SRM_SUCCESS, SRM_FAILURE, SRM_AUTHENTICATION_FAILURE, SRM_AUTHORIZATION_FAILURE, SRM_INVALID_REQUEST, SRM_INVALID_PATH, SRM_FILE_LIFETIME_EXPIRED, SRM_SPACE_LIFETIME_EXPIRED, SRM_EXCEED_ALLOCATION, SRM_NO_USER_SPACE, SRM_NO_FREE_SPACE, SRM_DUPLICATION_ERROR, SRM_NON_EMPTY_DIRECTORY, SRM_TOO_MANY_RESULTS, SRM_INTERNAL_ERROR, SRM_FATAL_INTERNAL_ERROR, SRM_NOT_SUPPORTED, SRM_REQUEST_QUEUED, SRM_REQUEST_INPROGRESS, SRM_REQUEST_SUSPENDED, SRM_ABORTED, SRM_RELEASED, SRM_FILE_PINNED, SRM_FILE_IN_CACHE, SRM_SPACE_AVAILABLE, SRM_LOWER_SPACE_GRANTED, SRM_DONE, SRM_PARTIAL_SUCCESS, SRM_REQUEST_TIMED_OUT, SRM_LAST_COPY, SRM_FILE_BUSY, SRM_FILE_LOST, SRM_FILE_UNAVAILABLE, SRM_CUSTOM_STATUS } |

TAccessPattern

  - TAccessPattern will be passed as an input parameter to the srmPrepareToGet and srmBringOnline functions. It will make a hint from the client to SRM how the Transfer URL (TURL) produced by SRM is going to be used. If the parameter value is “ProcessingMode”, the system may expect that client application will perform some processing of the partially read data, followed by more partial reads and a frequent use of the protocol specific “seek” operation. This will allow optimizations by allocating files on disks with small buffer sizes. If the value is “TransferMode” the file will be read at the highest speed allowed by the connection between the server and a client.

TConnectionType

  - TConnectionType indicates if the client is connected though a local or wide area network. SRM may optimize the access parameters to achieve maximum throughput for the connection type. This will be passed as an input to the srmPrepareToGet, srmPrepareToPut and srmBringOnline functions.

## Complex Types

| name | type | Min | Max |
| --- | --- | --- | --- |
| TRetentionPolicyInfo | TRetentionPolicy retentionPolicy TAccessLatency accessLatency | 1 0 | 1 1 |
| TRequestToken | xsd:string | 1 | 1 |
| ArrayOfTRequestToken | TRequestToken [] | 1 | 1 |
| TSpaceToken | xsd:string | 1 | 1 |
| ArrayOfTSpaceToken | TSpaceToken [] | 1 | 1 |
| TUserID | xsd:string | 1 | 1 |
| TGroupID | xsd:string | 1 | 1 |
| TOwnerPermission | TPermissionMode | 1 | 1 |
| TUserPermission | TUserID userID TPermissionMode mode | 1 1 | 1 1 |
| ArrayOfTUserPermission | TUserPermission [] |  |  |
| TGroupPermission | TGroupID groupID TPermissionMode mode | 1 1 | 1 1 |
| ArrayOfTGroupPermission | TGroupPermission [] |  |  |
| TOtherPermission | TPermissionMode | 1 | 1 |
| TCheckSumType | xsd:string | 1 | 1 |
| TCheckSumValue | xsd:string | 1 | 1 |
| TSizeInBytes | xsd:unsignedLong |  |  |
| ArrayOfTSizeInBytes | TSizeInBytes [] |  |  |
| ArrayOfString | xsd:string [] |  |  |

TRequestToken

- The TRequestToken assigned by SRM is unique and immutable (non-reusable).  For example, if the date:time is part of the requestToken it will be immutable.

TUserPermission

- TUserID may represent the associated client’s Distinguished Name (DN) instead of unix style login name.  VOMS role may be included.

TGroupPermission

  - TGroupID may represent the associated client’s Distinguished Name (DN) instead of unix style login name. VOMS role may be included.

TSizeInBytes

  - xsd:unsignedLong — Unsigned integer of 64 bits

| name | type | Min | Max |
| --- | --- | --- | --- |
| TUTCTime | xsd:dateTime | 1 | 1 |
| TLifeTimeInSeconds | xsd:unsignedLong |  |  |
| TSURL | xsd:anyURI | 1 | 1 |
| TTURL | xsd:anyURI | 1 | 1 |
| TReturnStatus | TStatusCode statusCode xsd:string explanation | 1 0 | 1 1 |
| TSURLReturnStatus | TSURL surl TReturnStatus status | 1 1 | 1 1 |
| ArrayOfTSURLReturnStatus | TSURLReturnStatus [] |  |  |
| TMetaDataPathDetail | xsd:string surl TReturnStatus status TSizeInBytes size TOwnerPermission ownerPermission ArrayOfTUserPermission arrayOfUserPermissions ArrayOfTGroupPermission arrayOfGroupPermissions TOtherPermission otherPermission TUTCTime createdAtTime TUTCTime lastModificationTime TUserID owner TFileStorageType fileStorageType TRetentionPolicyInfo retentionPolicyInfo TFileLocality fileLocality ArrayOfTSpaceToken arrayOfSpaceTokens TFileType type TLifeTimeInSeconds lifetimeAssigned TLifeTimeInSeconds lifetimeLeft TCheckSumType checkSumType TCheckSumValue checkSumValue ArrayOfTMetaDataPathDetail arrayOfSubPaths | 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 |
| ArrayOfTMetaDataPathDetail | TMetaDataPathDetail [] |  |  |
| TMetaDataSpace | TSpaceToken spaceToken TReturnStatus status TRetentionPolicyInfo retentionPolicyInfo TUserID owner TSizeInBytes totalSize TSizeInBytes guaranteedSize TSizeInBytes unusedSize TLifeTimeInSeconds lifetimeAssigned TLifeTimeInSeconds lifetimeLeft | 1 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 |
| ArrayOfTMetaDataSpace | TMetaDataSpace[] | 1 | 1 |

TUTCTime

  - Formerly TGMTTime in v2.1

  - date and time in Coordinated Universal Time (UTC, formerly GMT) with no local time extention.

  - Format is same as in XML dateTime type, except no local time extension is allowed. E.g. 1999-05-31T13:20:00 is ok (for 1999 May 31st, 13:20PM, UTC) but 1999-05-31T13:20:00-5:00 is not.

TLifeTimeInSeconds

  - xsd:unsignedLong — Unsigned integer of 64 bits

  - “0” (zero) will indicate the “infinite” lifetime.

TMetaDataPathDetail

  - The TMetaDataPathDetail describes the properties of a file. It is used as an output parameter in srmLs.

  - retentionPolicyInfo indicates the assigned retention policy.

  - fileLocality indicates where the file is located currently in the system.

  - arrayOfSpaceTokens as an array of TSpaceToken indicates where the file is currently located for the client. Only space tokens that the client has authorized to access to read the file must be returned.

TMetaDataSpace

  - TMetaDataSpace is used to describe properties of a space, and is used as an output parameter in srmGetSpaceMetaData.

  - retentionPolicyInfo indicates the information about retention policy and access latency that the space is assigned. retentionPolicyInfo is requested and assigned at the time of space reservation through srmReserveSpace and srmStatusOfReserveSpaceRequest.

  - TMetaDataSpace refers to a single space with retention policy.  It does not include the extra space needed to hold the directory structures, if there is any.

| name | type | Min | Max |
| --- | --- | --- | --- |
| TDirOption | xsd:boolean isSourceADirectory xsd:boolean allLevelRecursive xsd:int numOfLevels | 1 0 0 | 1 1 1 |
| TExtraInfo | xsd:string key xsd:string value | 1 0 | 1 1 |
| ArrayOfTExtraInfo | TExtraInfo [] |  |  |
| ArrayOfTSURL | TSURL [] |  |  |
| TSURLInfo | TSURL SURL ArrayOfTExtraInfo storageSystemInfo | 1 0 | 1 1 |
| ArrayOfTSURLInfo | TSURLInfo [] |  |  |
| TTransferParameters | TAccessPattern accessPattern TConnectionType connectionType, ArrayOfString arrayOfClientNetworks ArrayOfString arrayOfTransferProtocols | 0 0 0 1 | 1 1 1 1 |
| TGetFileRequest | TSURL sourceSURL TDirOption dirOption | 1 0 | 1 1 |
| ArrayOfTGetFileRequest | TGetFileRequest [] |  |  |
| TPutFileRequest | TSURL targetSURL TSizeInBytes expectedFileSize | 0 0 | 1 1 |
| ArrayOfTPutFileRequest | TPutFileRequest [] |  |  |
| TCopyFileRequest | TSURLInfo sourceSURLInfo TSURLInfo targetSURLInfo TDirOption dirOption | 1 1 0 | 1 1 1 |
| ArrayOfTCopyFileRequest | TCopyFileRequest [] |  |  |

TExtraInfo

  - TExtraInfo is used where additional information is needed, such as for additional information for transfer protocols of TURLs in srmPing, srmGetTransferProtocols, srmStatusOfGetRequest, and srmStatusOfPutRequest.  For example, when it is used for additional information for transfer protocols, the keys may specify access speed, available number of parallelism, and other transfer protocol properties.

  - It is also used where additional information to the underlying storage system is needed, such as for additional information, but not limited to, for storage device, storage login ID, storage login authorization. Formerly, it was TStorageSystemInfo.

TTransferParameters

  - TTransferParameters is used where arrayOfTransferProtocols was used previously in SRM v2.1.

  - TGetFileRequest includes TAccessPattern which may conflict with the characteristics of the online disk of the target space associated with target space token if provided. In this case, TAccessPattern must be ignored

  - File transfer protocols are specified in a preferred order on all SRM transfer functions.

  - arrayOfClientNetworks is a hint of the client IPs that SRM/dCache can use for optimization of its internal storage systems based on the client’s accessible IP addresses.

TPutFileRequest

  - If the optional targetSURL is provided, then the reference SURL is generated by the SRM. Specific SRM implementation may require targetSURL as an input parameter.

| name | type | Min | Max |
| --- | --- | --- | --- |
| TGetRequestFileStatus | TSURL sourceSURL TReturnStatus status TSizeInBytes fileSize TLifeTimeInSeconds estimatedWaitTime TLifeTimeInSeconds remainingPinTime TTURL transferURL ArrayOfTExtraInfo transferProtocolInfo | 1 1 0 0 0 0 0 | 1 1 1 1 1 1 1 |
| ArrayOfTGetRequestFileStatus | TGetRequestFileStatus [] |  |  |
| TBringOnlineRequestFileStatus | TSURL sourceSURL TReturnStatus status TSizeInBytes fileSize TLifeTimeInSeconds estimatedWaitTime TLifeTimeInSeconds remainingPinTime | 1 1 0 0 0 | 1 1 1 1 1 |
| ArrayOfTBringOnlineRequestFileStatus | TBringOnlineRequestFileStatus [] |  |  |
| TPutRequestFileStatus | TSURL SURL TReturnStatus status TSizeInBytes fileSize TLifeTimeInSeconds estimatedWaitTime TLifeTimeInSeconds remainingPinLifetime TLifeTimeInSeconds remainingFileLifetime TTURL transferURL ArrayOfTExtraInfo transferProtocolInfo | 1 1 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 |
| ArrayOfTPutRequestFileStatus | TPutRequestFileStatus [] |  |  |
| TCopyRequestFileStatus | TSURL sourceSURL TSURL targetSURL TReturnStatus status TSizeInBytes fileSize TLifeTimeInSeconds estimatedWaitTime TLifeTimeInSeconds remainingFileLifetime | 1 1 1 0 0 0 | 1 1 1 1 1 1 |
| ArrayOfTCopyRequestFileStatus | TCopyRequestFileStatus [] |  |  |
| TRequestStat | TStatusCode statusCode int numOfFiles | 1 1 | 1 1 |
| ArrayOfTRequestStat | TRequestStat [] |  |  |
| TRequestSummary | TRequestToken requestToken TReturnStatus status TRequestType requestType xsd:int totalNumFilesInRequest ArrayOfTRequestStat arrayOfRequestStats xsd:boolean isSuspended | 1 1 0 0 0 0 | 1 11 1 1 1 |
| ArrayOfTRequestSummary | TRequestSummary [] |  |  |
| TSURLPermissionReturn | TSURL surl TReturnStatus status TPermissionType permission | 1 1 0 | 1 1 1 |
| ArrayOfTSURLPermissionReturn | TSURLPermissionReturn [] |  |  |
| TRequestTokenReturn | TRequestToken requestToken TUTCTime createdAtTime | 1 0 | 1 1 |
| ArrayOfTRequestTokenReturn | TRequestTokenReturn [] |  |  |
| TSupportedTransferProtocol | xsd:string transferProtocol ArrayOfTExtraInfo attributes | 10 | 1 1 |
| ArrayOfTSupportedTransferProtocol | TSupportedTransferProtocol [] |  |  |

TRequestSummary

  - Int  totalNumFilesInRequest

Output parameter reporting the total number of files in the request

  - Boolean isSuspended

Output parameter reporting if the request has been suspended or not

TSupportedTransferProtocol

  - transferProtocol (required): Supported transfer protocol. For example, gsiftp, http.

  - attributes: Informational hints for the paired transfer protocol, such how many number of parallel streams can be used, desired buffer size, etc.

# Space Management Functions – Message Types and Operations

summary:

srmReserveSpace

srmStatusOfReserveSpaceRequest

srmReleaseSpace

srmUpdateSpace

srmGetSpaceMetaData

srmChangeSpaceForFiles

srmStatusOfChangeSpaceForFilesRequest

srmExtendFileLifeTimeInSpace

srmPurgeFromSpace

srmGetSpaceToken

## srmReserveSpace

This function is used to reserve a space in advance for the upcoming requests to get some guarantee on the file management. Asynchronous space reservation may be necessary for some SRMs to serve many concurrent requests.

| Input | srmReserveSpaceRequest |
| --- | --- |
| Output | srmReserveSpaceResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmReserveSpaceRequest | TUserID authorizationID xsd:string userSpaceTokenDescription TRetentionPolicyInfo retentionPolicyInfo TSizeInBytes desiredSizeOfTotalSpace TSizeInBytes desiredSizeOfGuaranteedSpace TLifeTimeInSeconds desiredLifetimeOfReservedSpace ArrayOfTSizeInBytes arrayOfExpectedFileSizes ArrayOfTExtraInfo storageSystemInfo TTransferParameters transferParametersHint | 0 0 1 0 1 0 0 0 0 | 1 1 1 1 1 1 1 1 1 |
| srmReserveSpaceResponse | TReturnStatus returnStatus TRequestToken requestToken TLifeTimeInSeconds estimatedProcessingTime TRetentionPolicyInfo retentionPolicyInfo TSizeInBytes sizeOfTotalReservedSpace TSizeInBytes sizeOfGuaranteedReservedSpace TLifeTimeInSeconds lifetimeOfReservedSpace TSpaceToken, spaceToken | 1 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 |

### Notes on the Behavior

- If the input parameter desiredLifetimeOfReservedSpace is not provided, the lifetime of the reserved space is set to “infinite” by default.

- If the input parameter retentionPolicyInfo cannot be satisfied by the SRM server, SRM_INVALID_REQUEST must be returned.

- Asynchronous space reservation may be necessary for some SRMs to serve many concurrent requests. In such case, request token must be returned, and space token must not be assigned and returned until space reservation is completed, to prevent the usage of the space token in other interfaces before the space reservation is completed. If the space reservation can be done immediately, request token must not be returned.

- When asynchronous space reservation is necessary, the returned status code should be SRM_REQUEST_QUEUED.

- Input parameter arrayOfExpectedFileSize is a hint that SRM server can use to reserve consecutive storage sizes for the request. At the time of space reservation, if space accounting is done only at the level of the total size, this hint would not help. In such case, the expected file size at the time of srmPrepareToPut will describe how much consecutive storage size is needed for the file. However, some SRMs may get benefits from these hints to make a decision to allocate some blocks in some specific devices.

- Optional input parameter storageSystemInfo is needed in case the underlying storage system requires additional security information.

- SRM may return its default space size and lifetime if not requested by the client. SRM may return SRM_INVALID_REQUEST if SRM does not support default space sizes.

- If input parameter desiredSizeOfTotalSpace is not specified, the SRM will return its default space size.

- Output parameter estimateProcessingTime is used to indicate the estimation time to complete the space reservation request, when known.

- Output parameter sizeOfTotalReservedSpace is in best effort bases. For guaranteed space size, sizeOfGuaranteedReservedSpace should be checked. These two numbers may match, depending on the storage systems.

- Output parameter spaceToken is a reference handle of the reserved space.

### Return Status Code

SRM_SUCCESS

- successful request completion. Space is reserved successfully as the client requested.

SRM_ REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned, and space token must not be assigned and returned.

SRM_LOWER_SPACE_GRANGED

- successful request completion, but lower space size is allocated than what the client requested

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to reserve space

SRM_INVALID_REQUEST

- the input parameter retentionPolicyInfo cannot be satisfied by the SRM server.

- If space size or lifetime is not requested by the client, and SRM does not support default values for space size or lifetime.

- input parameters do not conform the SRM server. For example, client requested negative desiredLifetimeOfReservedSpace and SRM server cannot honor the number.

SRM_NO_USER_SPACE

- SRM server does not have enough user space for the client for client to request to reserve.

SRM_NO_FREE_SPACE

- SRM server does not have enough free space for client to request to reserve.

SRM_EXCEED_ALLOCATION

- SRM server does not have enough space for the client to fulfill the request because the client request needs more than the allocated space  quota for the client.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

## srmStatusOfReserveSpaceRequest

This function is used to check the status of the previous request to srmReserveSpace, when asynchronous space reservation was necessary with the SRM. Request token must have been provided in response to the srmReserveSpace.

| Input | srmStatusOfReserveSpaceRequestRequest |
| --- | --- |
| Output | srmStatusOfReserveSpaceRequestResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfReserveSpaceRequestRequest | TUserID authorizationID TRequestToken requestToken | 0 1 | 1 1 |
| srmStatusOfReserveSpaceRequestResponse | TReturnStatus returnStatus TLifeTimeInSeconds estimatedProcessingTime TRetentionPolicyInfo retentionPolicyInfo TSizeInBytes sizeOfTotalReservedSpace TSizeInBytes sizeOfGuaranteedReservedSpace TLifeTimeInSeconds lifetimeOfReservedSpace TSpaceToken, spaceToken | 1 0 0 0 0 0 0 | 1 1 1 1 1 1 1 |

### Notes on the Behavior

- If the space reservation is not completed yet, estimateProcessingTime is returned when known. The returned status code in such case should be SRM_REQUEST_QUEUED.

- See notes for srmReserveSpace for descriptions for output parameters.

### Return Status Code

SRM_REQUEST_QUEUED

- successful request submission and the request is still on the queue to be served.

SRM_REQUEST_INPROGRESS

- the request is being processed.

SRM_LOWER_SPACE_GRANGED

- successful request completion, but lower space size is allocated than what the client requested

SRM_SUCCESS

- successful request completion. Space is reserved successfully as the client requested.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to reserve space

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

SRM_EXCEED_ALLOCATION

- SRM server does not have enough space for the client to fulfill the request because the client request needs more than the allocated space for the client.

SRM_NO_USER_SPACE

- SRM server does not have enough user space for the client for the client for client to request to reserve.

SRM_NO_FREE_SPACE

- SRM server does not have enough free space for the client for client to request to reserve.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

## srmReleaseSpace

srmReleaseSpace() releases an occupied space.

| Input | srmReleaseSpaceRequest |
| --- | --- |
| Output | srmReleaseSpaceResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmReleaseSpaceRequest | TUserID authorizationID TSpaceToken spaceToken ArrayOfTExtraInfo storageSystemInfo xsd:boolean forceFileRelease | 0 1 0 0 | 1 1 1 1 |
| srmReleaseSpaceResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- forceFileRelease is false by default.  This means that the space will not be released if it has files that are still pinned in the space.  To release the space regardless of the files it contains and their status forceFileRelease must be specified to be true.

- When space is releasable and forceFileRelease is true, all the files in the space are released, even in durable or permanent space.

- srmReleaseSpace may not complete right away because of the lifetime of files in the space.  When space is released, the files in that space are treated according to their types: If file storage types are permanent, keep them until further operation such as srmRm is issued by the client. If file storage types are durable, perform necessary actions at the end of their lifetime. If file storage types are volatile, release those files at the end of their lifetime.

### Return Status Code

SRM_SUCCESS

- successful request completion. Space is successfully released.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to release the space that is associated with the spaceToken

SRM_INVALID_REQUEST

- spaceToken does not refer to an existing known space in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- forceFileRelease is not supported

- function is not supported

SRM_FAILURE

- space still contains pinned files.

- space associated with space is already released.

- any other request failure. Explanation needs to be filled for details.

## srmUpdateSpace

srmUpdateSpace is to resize the space and/or extend the lifetime of a space. Asynchronous operation may be necessary for some SRMs to serve many concurrent requests.

| Input | srmUpdateSpaceRequest |
| --- | --- |
| Output | srmUpdateSpaceResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmUpdateSpaceRequest | TUserID authorizationID TSpaceToken spaceToken TSizeInBytes newSizeOfTotalSpaceDesired TSizeInBytes newSizeOfGuaranteedSpaceDesired TLifeTimeInSeconds newLifeTime ArrayOfTExtraInfo storageSystemInfo | 0 1 0 0 0 0 | 1 1 1 1 1 1 |
| srmUpdateSpaceResponse | TReturnStatus returnStatus TRequestToken requestToken TSizeInBytes sizeOfTotalSpace TSizeInBytes sizeOfGuaranteedSpace TLifeTimeInSeconds lifetimeGranted | 1 0 0 0 0 | 1 1 1 1 1 |

### Notes on the Behavior

- If neither size nor lifetime is provided in the input parameters, then the request will be failed.

- newSize is the new actual size of the space.

- newLifetime is the new lifetime requested regardless of the previous lifetime, and has to be positive.  It might even be shorter than the remaining lifetime at the time of the call. It is relative to the calling time. Lifetime will be set from the calling time for the specified period.

### Return Status Code

SRM_SUCCESS

- successful request completion. Space is successfully updated as the client requested.

SRM_ REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned.

SRM_LOWER_SPACE_GRANGED

- successful request completion, but lower space size is allocated than what the client requested

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to update the space that is associated with the spaceToken

SRM_SPACE_LIFETIME_EXPIRED

- lifetime of the space that is associated with the spaceToken is already expired.

SRM_INVALID_REQUEST

- spaceToken does not refer to an existing known space in the SRM server.

- input parameter size or time is not provided.

SRM_EXCEED_ALLOCATION

- SRM server does not have enough space for the client to fulfill the request because the client request has more than the allocated space for the client.

SRM_NO_USER_SPACE

- SRM server does not have enough space for the client to fulfill the request

SRM_NO_FREE_SPACE

- SRM server does not have enough free space to fulfill the request

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- New requested size is less than currently used space.

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported

## srmStatusOfUpdateSpaceRequest

This function is used to check the status of the previous request to srmUpdateSpace, when asynchronous space update was necessary with the SRM. Request token must have been provided in response to the srmUpdateSpace.

### Parameters

In:	TUserID			authorizationID,

TRequestToken		requestToken

Out:	TReturnStatus			returnStatus,

TSizeInBytes			sizeOfTotalSpace, 	// best effort

TSizeInBytes			sizeOfGuaranteedSpace,		TLifeTimeInSeconds		lifetimeGranted

### Notes on the Behavior

- Output parameters for sew sizes are the new actual sizes of the space.

- Output parameter, lifetimeGranted is the new lifetime granted regardless of the previous lifetime.  It might even be shorter than the previous lifetime. It is relative to the calling time.

### Return Status Code

SRM_REQUEST_QUEUED

- successful request submission and the request is still on the queue to be served.

SRM_REQUEST_INPROGRESS

- the request is being processed.

SRM_SUCCESS

- successful request completion. Space is successfully updated as the client requested.

SRM_LOWER_SPACE_GRANGED

- successful request completion, but lower space size is allocated than what the client requested

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to update the space that is associated with the spaceToken

SRM_SPACE_LIFETIME_EXPIRED

- lifetime of the space that is associated with the spaceToken is already expired.

SRM_INVALID_REQUEST

- spaceToken does not refer to an existing known space in the SRM server.

- input parameter size or time is not provided.

SRM_EXCEED_ALLOCATION

- SRM server does not have enough space for the client to fulfill the request because the client request has more than the allocated space for the client.

SRM_NO_USER_SPACE

- SRM server does not have enough space for the client to fulfill the request

SRM_NO_FREE_SPACE

- SRM server does not have enough free space to fulfill the request

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- New requested size is less than currently used space.

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported

## srmGetSpaceMetaData

This function is used to get information of a space.  Space token must be provided, and space tokens are returned upon a completion of a space reservation through srmReserveSpace or srmStatusOfReserveSpaceRequest.

| Input | srmGetSpaceMetaDataRequest |
| --- | --- |
| Output | srmGetSpaceMetaDataResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmGetSpaceMetaDataRequest | TUserID authorizationID ArrayOfTSpaceToken arrayOfSpaceTokens | 0 1 | 1 1 |
| srmGetSpaceMetaDataResponse | TReturnStatus returnStatus ArrayOfTMetaDataSpace arrayOfSpaceDetails | 1 0 | 1 1 |

### Return Status Code

For request level return Status,

SRM_SUCCESS

- successful request completion. Information of all requested spaces are returned successfully.

SRM_PARTIAL_SUCCESS

- Request is completed. Information of some requested spaces are returned successfully, and some are failed to be returned.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request space information

SRM_TOO_MANY_RESULTS

- Request produced too many results that SRM server cannot handle.

SRM_INVALID_REQUEST

- arrayOfSpaceToken is empty.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

For space level return Status,

SRM_SUCCESS

- successful request completion for the spaceToken. Space information is successfully returned.

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request information on the space that is associated with the spaceToken

SRM_INVALID_REQUEST

- spaceToken does not refer to an existing known space in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- The life time on the space that is associated with the spaceToken has expired

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmChangeSpaceForFiles

This function is used to change the space property of files to another space property by specifying target space tokens.  All files specified by SURLs will have a new space token. SURLs must not be changed. New space token may be acquired from srmReserveSpace.  Asynchronous operation may be necessary for some SRMs, and in such case, request token is returned for later status inquiry. There is no default behavior when target space token is not provided. In such case, the request will be rejected, and the return status must be SRM_INVALID_REQUEST.

| Input | srmChangeSpaceForFilesRequest |
| --- | --- |
| Output | srmChangeSpaceForFilesResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmChangeSpaceForFilesRequest | TUserID authorizationID ArrayOfTSURLInfo arrayOfSURLs TSpaceToken targetSpaceToken | 0 1 1 | 1 1 1 |
| srmChangeSpaceForFilesResponse | TReturnStatus returnStatus TRequestToken requestToken TLifeTimeInSeconds estimatedProcessingTime ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 0 0 | 1 1 1 1 |

### Notes on the Behavior

- When space transition is completed successfully, SRM_SUCCESS must be returned for each SURL.

- For any forbidden transition by the SRM implementation, SRM_INVALID_SPACE_TRANSITION must be returned.

- Asynchronous operation may be necessary for some SRMs to serve many concurrent requests. In such case, request token must be returned. If the request can be completed immediately, request token must not be returned.

- When asynchronous operation is necessary, the returned status code should be SRM_REQUEST_QUEUED, and arrayOfFileStatuses may not be filled and returned.

- All files specified in arrayOfSURLs will be moved to the space associated with targetSpaceToken.

- When target space token is used, space allocation for a new space token must be done explicitly by the client before using this function.

- If a directory path is provided, then the effect is recursive for all files in the directory.

- Space de-allocation may be necessary in some cases, and it must be done by the client explicitly after this operation completes. The status can be checked by srmStatusOfChangeSpaceForFilesRequest.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All file requests are successfully completed. All SURLs have new targetSpaceToken.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURL requests have new targetSpaceToken, and some SURL requests are failed to have new targetSpaceToken. Details are on the files status.

SRM_ REQUEST_QUEUED

- request is submitted and accepted. requestToken must be returned.

- The status can be checked by srmStatusOfChangeSpaceForFilesRequest.

SRM_ REQUEST_INPROGRESS

- The request is being processed. Some files are still queued, and some files are completed in space transition.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to change the file types

SRM_INVALID_REQUEST

- SURL is empty.

- targetSpaceToken is empty.

- targetSpaceToken does not refer to an existing space in the SRM server.

- targetSpaceToken refers to a forbidden transition by the SRM implementation.

SRM_SPACE_LIFETIME_EXPIRED

- target space that is associated with targetSpaceToken has an expired lifetime.

SRM_EXCEED_ALLOCATION

- target space that is associated with targetSpaceToken is not enough to hold SURLs.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. The SURL has a new targetSpaceToken.

SRM_ REQUEST_QUEUED

- file request is on the queue.

SRM_ REQUEST_INPROGRESS

- file request is being processed.

SRM_INVALID_PATH

- SURL does not refer to an existing file

SRM_AUTHORIZATION_FAILURE

- client is not authorized to change the space for the file that is associated with the SURL

SRM_INVALID_REQUEST

- targetSpaceToken refers to a forbidden transition for the particular SURL by the SRM implementation.

SRM_EXCEED_ALLOCATION

- target space that is associated with targetSpaceToken is not enough to hold SURL.

SRM_FILE_LOST

- the requested file with the SURL is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- The requested file with the SURL is being used by other clients.

SRM_FILE_UNAVAILABLE

- the requested file with the SURL is temporarily unavailable.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmStatusOfChangeSpaceForFilesRequest

This function is used to check the status of the previous request to srmChangeSpaceForFiles, when asynchronous operation was necessary in the SRM. Request token must have been provided in response to the srmChangeSpaceForFiles.

| Input | srmStatusOfChangeSpaceForFilesRequestRequest |
| --- | --- |
| Output | srmStatusOfChangeSpaceForFilesRequestResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfChangeSpaceForFilesRequestRequest | TUserID authorizationID TRequestToken requestToken | 0 1 | 1 1 |
| srmStatusOfChangeSpaceForFilesRequestResponse | TReturnStatus returnStatus TLifeTimeInSeconds estimatedProcessingTime ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- When space transition is completed successfully, SRM_SUCCESS must be returned for each SURL.

- If changing space is not completed, estimateProcessingTime is returned when known.

- If all files are still in the queue and none of the files are completed in changing space, the returned status code should be SRM_REQUEST_QUEUED.

- If some files are queued, and some files are completed in changing space, SRM_REQUEST_INPROGRESS must be returned as the return status code. Each file should have its own status code.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All file requests are successfully completed. All SURLs have new targetSpaceToken.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURL requests have new targetSpaceToken, and some SURL requests are failed to have new targetSpaceToken. Details are on the files status.

SRM_ REQUEST_QUEUED

- Request submission was successful and the entire request is still on the queue.

SRM_ REQUEST_INPROGRESS

- Some files are still queued, and some files are completed in space transition.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to change the file types

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

- targetSpaceToken refers to a forbidden transition by the SRM implementation.

SRM_SPACE_LIFETIME_EXPIRED

- target space that is associated with targetSpaceToken has an expired lifetime.

SRM_EXCEED_ALLOCATION

- target space that is associated with targetSpaceToken is not enough to hold SURLs.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. The SURL has a new targetSpaceToken.

SRM_ REQUEST_QUEUED

- file request is on the queue.

SRM_ REQUEST_INPROGRESS

- file request is being processed.

SRM_INVALID_PATH

- SURL does not refer to an existing file request

SRM_AUTHORIZATION_FAILURE

- client is not authorized to change the space for the file that is associated with the SURL

SRM_INVALID_REQUEST

- targetSpaceToken refers to a forbidden transition for the particular SURL by the SRM implementation.

SRM_EXCEED_ALLOCATION

- target space that is associated with targetSpaceToken is not enough to hold SURL.

SRM_FILE_LOST

- the requested file with the SURL is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- The requested file with the SURL is being used by other clients.

SRM_FILE_UNAVAILABLE

- the requested file with the SURL is temporarily unavailable.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmExtendFileLifeTimeInSpace

This function is used to extend lifetime of the files (SURLs) in a space.

| Input | srmExtendFileLifeTimeInSpaceRequest |
| --- | --- |
| Output | srmExtendFileLifeTimeInSpaceResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmExtendFileLifeTimeInSpaceRequest | TUserID authorizationID TSpaceToken spaceToken ArrayOfTSURL arrayOfSURLs TLifeTimeInSeconds newLifeTime | 0 1 0 0 | 1 1 1 1 |
| srmExtendFileLifeTimeInSpaceResponse | TReturnStatus returnStatus TLifeTimeInSeconds newTimeExtended ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 00 | 1 1 1 |

### Notes on the Behavior

- When spaceToken is provided, the lifetime of the file copy of the SURLs in the space associated with the space token will be extended.

- newLifeTime is relative to the calling time. Lifetime will be set from the calling time for the specified period.

- The new file lifetime, newTimeExtended must not exceed the remaining lifetime of the space.

- The number of lifetime extensions maybe limited by SRM according to its policies.

- If original lifetime is longer than the requested one, then the requested one will be assigned.

- If newLifeTime is not specified, the SRM can use its default to assign the newLifeTime.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs have a new extended lifetime.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURLs have a new extended lifetime, and some SURLS have failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to extend lifetime of files in the space specified by the space token.

SRM_INVALID_REQUEST

- spaceToken is empty.

- spaceToken does not refer to an existing known space in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. The SURL has a new extended lifetime.

SRM_INVALID_PATH

- SURL does not refer to an existing file request

- SURL does not refer to an existing file request that is associated with the space token

SRM_AUTHORIZATION_FAILURE

- client is not authorized to extend the lifetime for the file that is associated with the SURL

SRM_FILE_LOST

- the requested file is permanently lost.

SRM_FILE_UNAVAILABLE

- the requested file is temporarily unavailable.

SRM_FILE_LIFETIME_EXPIRED

- the requested file is expired already.

## srmPurgeFromSpace

This function is used when removing files from the given space is needed. Difference from srmReleaseFiles and srmAbortFiles is that srmPurgeFromSpace is not associated with a request. This function must not remove the SURLs, but only the "copies" or "states" of the SURLs.  srmRm must be used to remove SURLs.

| Input | srmPurgeFromSpaceRequest |
| --- | --- |
| Output | srmPurgeFromSpaceResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmPurgeFromSpaceRequest | TUserID authorizationID ArrayOfTSURLInfo arrayOfSURLs TSpaceToken spaceToken | 0 1 1 | 1 1 1 |
| srmPurgeFromSpaceResponse | TReturnStatus returnStatus ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 | 1 1 |

### Notes on the Behavior

- If the specified SURL is the only remaining copy of the file in the storage system, SRM_LAST_COPY must be returned. To remove the last copy of the SURL, srmRm may be used.

- The method shall only succeed if there are no outstanding pins or requests for the specified files. Otherwise, SRM_FILE_BUSY must be returned.

- When input parameter spaceToken is provided, SRM will remove only the “copies” (or “state”) of the SURLs associated with the space token.

- It has the effect of a release on the “copy” (or “state”) of the file before being removed.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs are purged from the space specified by the spaceToken.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURLs are successfully purged from the space specified by the spaceToken, and some SURLs are failed to be purged from the space specified by the spaceToken. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to clean up the space that is associated with spaceToken

SRM_INVALID_REQUEST

- arrayOfSURLs is empty.

- spaceToken is empty.

- spaceToken does not refer to an existing known space in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

For file level return Status,

SRM_SUCCESS

- successful request completion for the SURL. SURL is purged from the space specified by the spaceToken.

SRM_INVALID_PATH

- SURL does not refer to an existing file

- SURL does not refer to an existing file that is associated with the space token

SRM_AUTHORIZATION_FAILURE

- Client is not authorized to purge SURL in the space that is associated with spaceToken

SRM_FILE_LOST

- the request file is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- The requested file is used by other clients.

SRM_FILE_UNAVAILABLE

- the requested file is temporarily unavailable.

SRM_LAST_COPY

- the requested file is the last copy and will not be purged from the space. srmRm must be used to remove the last copy.

## srmGetSpaceToken

srmGetSpaceToken() returns space tokens for currently allocated spaces.

| Input | srmGetSpaceTokenRequest |
| --- | --- |
| Output | srmGetSpaceTokenResponse |

| name | type | Min | Max |
| --- | --- | --- | --- |
| srmGetSpaceTokenRequest | xsd:string userSpaceTokenDescription TUserID authorizationID | 0 0 | 1 1 |
| srmGetSpaceTokenResponse | TReturnStatus returnStatus ArrayOfTSpaceToken arrayOfSpaceTokens | 1 0 | 1 1 |

### Notes on the Behavior

- If userSpaceTokenDescription is null, returns all space tokens this user owns.

- If the user assigned the same name to multiple space reservations, he may get back multiple space tokens.

### Return Status Code

SRM_SUCCESS

- All requests are successfully completed. Space tokens are returned successfully.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request spaceTokens associated with the userSpaceDescription

SRM_INVALID_REQUEST

- userSpaceDescription does not refer to an existing space description.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

# Permission Functions – Message Types and Operations

summary:

srmSetPermission

srmCheckPermission

## srmSetPermission

srmSetPermission is to set permission on local SURL.

| Input | srmSetPermissionRequest |
| --- | --- |
| Output | srmSetPermissionResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmSetPermissionRequest | TUserID authorizationID TSURLInfo SURL TPermissionType permissionType TOwnerPermission ownerPermission ArrayOfTUserPermission arrayOfUserPermissions ArrayOfTGroupPermission arrayOfGroupPermissions TOtherPermission otherPermission | 0 1 0 0 0 0 0 | 1 1 1 1 1 1 1 |
| srmSetPermissionResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- Applies to both dir and file.

- Support for srmSetPermission is optional.

- User permissions are provided in order to support dynamic user-level permission assignment similar to Access Control Lists (ACLs).

- Permissions can be assigned to set of users and sets of groups, but only a single owner.

- In this version, SRMs do not provide any group operations (setup, modify, remove, etc.)

- Groups are assumed to be set up before srmSetPermission is used.

- If TPermissionType is ADD or CHANGE, and TPermissionMode is null, then it is assumed that TPermissionMode is READ only.

- If TPermissionType is REMOVE, then the TPermissionMode is ignored

### Return Status Code

SRM_SUCCESS

- successful request completion. SURL has a new permission.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to set permissions

- client is not authorized to set permissions on the SURL

SRM_INVALID_PATH

- SURL does not refer to an existing known path

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

## srmCheckPermission

srmCheckPermission is used to check the client permissions on the SURLs. It only checks for the client for authorization on the SURLs.

| Input | srmCheckPermissionRequest |
| --- | --- |
| Output | srmCheckPermissionResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmCheckPermissionRequest | ArrayOfTSURLInfo arrayOfSURLs TUserID authorizationID xsd:boolean checkLocalOnly | 1 0 0 | 1 1 1 |
| srmCheckPermissionResponse | TReturnStatus returnStatus ArrayOfTSURLPermissionReturn arrayOfPermissions | 1 0 | 1 1 |

### Notes on the Behavior

- When checkLocalOnly is true, then SRM will only check files in its local cache. Otherwise, if a file is not in its local cache, then SRM will go to the SURL to check the user permission.

- If checkLocalOnly  is false, SRM can choose to always check the SURL for user permission of each file. It is also ok if SRM choose to check its local cache first, if a file exists and the user has permission, return that permission. Otherwise, check the SURL and return permission.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. Permissions on SURLs are checked and returned.

SRM_PARTIAL_SUCCESS

- All requests are completed. Permissions of some SURLs are successfully checked and returned, but some permission of some SURLs are failed to be checked. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request permission information

SRM_INVALID_REQUEST

- arrayOfSURL is empty.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

- a particular type of an input parameter (checkLocalOnly = false) is not supported in the SRM server

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. Permissions on SURL are checked and returned.

SRM_INVALID_PATH

- SURL does not refer to an existing known path

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request permission information on the SURL

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

# Directory Functions – Message Types and Operations

summary:

srmMkdir

srmRmdir

srmRm

srmLs

srmStatusOfLsRequest

srmMv

## srmMkdir

srmMkdir creates a directory in a local SRM space.

| Input | srmMkdirRequest |
| --- | --- |
| Output | srmMkdirResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmMkdirRequest | TUserID authorizationID TSURLInfo directoryPath | 0 1 | 1 1 |
| srmMkdirResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- Consistent with unix, recursive creation of directories is not supported.

- directoryPath can include paths, as long as all directory hierarchy exists.

### Return Status Code

SRM_SUCCESS

- All requests are successfully completed. directoryPath is created.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to create a directory

- client is not authorized to create a directory as diretoryPath

SRM_INVALID_PATH

- directoryPath does not refer to a valid path

- component of directoryPath does not refer to an existing path

SRM_DUPLICATION_ERROR

- directoryPath exists already

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

## srmRmdir

srmRmdir removes an empty directory in a local SRM space.

| Input | srmRmdirRequest |
| --- | --- |
| Output | srmRmdirRespnose |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmRmdirRequest | TUserID authorizationID TSURLInfo directoryPath xsd:boolean recursive | 0 1 0 | 1 1 1 |
| srmRmdirRespnose | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- It applies to directory only.

- recursive is false by default.

- To distinguish from srmRm(), this function is for directories only

### Return Status Code

SRM_SUCCESS

- All requests are successfully completed. directoryPath is removed.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to remove a directory

- client is not authorized to remove a directory as directoryPath

SRM_INVALID_PATH

- directoryPath does not refer to a valid path

SRM_NON_EMPTY_DIRECTORY

- directoryPath is not empty

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

- input parameter recursive is not supported in the SRM server

## srmRm

This function will remove SURLs (the name space entries) in the storage system. Difference from srmPurgeFromSpace is that srmPurgeFromSpace removes only previously requested “copies” (or “state”) of the SURL in a particular space, and srmPurgeFromSpace shall not remove SURLs or the name space entries.  If any files are not released yet, this function will release them before removing SURLs.

| Input | srmRmRequest |
| --- | --- |
| Output | srmRmResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmRmRequest | TUserID authorizationID ArrayOfTSURLInfo arrayOfSURLs | 0 1 | 1 1 |
| srmRmResponse | TReturnStatus returnStatus ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 | 1 1 |

### Notes on the Behavior

- Applies to files only.

- To distinguish from srmRmdir(), this function applies to files only

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs are removed.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURLs are successfully removed, and some SURLs are failed to be removed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to remove any files

SRM_INVALID_REQUEST

- arrayOfSURLs is empty.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. SURL is removed.

SRM_INVALID_PATH

- SURL does not refer to an existing known file path

SRM_AUTHORIZATION_FAILURE

- client is not authorized to remove SURL

SRM_FILE_LOST

- the request file is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- SURL is being used by other clients

SRM_FILE_UNAVAILABLE

- the request file is temporarily unavailable.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmLs

srmLs() returns a list of files with a basic information. This operation may be asynchronous, and in such case, requestToken must be returned.

| Input | srmLsRequest |
| --- | --- |
| Output | srmLsResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmLsRequest | TUserID authorizationID ArrayOfTSURL arrayOfSURLs ArrayOfTExtraInfo storageSystemInfo TFileStorageType fileStorageType xsd:boolean fullDetailedList xsd:boolean allLevelRecursive xsd:int numOfLevels xsd:int offset xsd:int count | 0 1 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 |
| srmLsResponse | TReturnStatus returnStatus TRequestToken requestToken ArrayOfTMetaDataPathDetail details | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- Applies to both directory and file

- fullDetailedList is false by default.

  - For directories, only path is required to be returned.

  - For files, path and size are required to be returned.

- If fullDetailedList is true, the full details are returned.

  - For directories, path and userPermission are required to be returned.

  - For files, path, size, userPermission, lastModificationTime, file type, and lifetimeLeft are required to be returned, similar to unix command ls –l.

- If allLevelRecursive is true then file lists of all level below current will be provided as well.

- If allLevelRecursive is "true" it dominates, i.e. ignore numOfLevels.  If allLevelRecursive is "false" or missing, then do numOfLevels.  If numOfLevels is "0" (zero) or missing, assume a single level.  If both allLevelRecursive and numOfLevels are missing, assume a single level.

- If numOfLevels is 0, then information about directory itself is returned.

- If numOfLevels is 1, then information about files in the directory is returned.

- When listing for a particular type specified by “fileStorageType”, only the files with that type will be in the output.

- Empty directories will be returned.

- We recommend width first in the listing.

- We recommend that list of directories come before list of files in the return array (details).

- For non-existing file or directory, SRM_INVALID_PATH must be returned.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs are checked and the information for all SURLs is returned successfully.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURL request is successfully completed, and some SURL request is failed. Details are on the files status.

SRM_REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request information

SRM_TOO_MANY_RESULTS

- srmLs request has generated too many results that SRM cannot handle. In most cases, it needs to be narrowed down with offset and count by the client.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_INVALID_REQUEST

- Negative values for numOfLevels, offset and count are provided.

SRM_NOT_SUPPORTED

- Requested fileStorageType is not supported in SRM

- Filtering fileStorageType is not supported in SRM

- Directory operation (directory SURL, allLevelRecursive and numOfLevels) is not supported in SRM

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. The information for the SURL is checked and returned successfully.

SRM_FILE_IN_CACHE

- lifetime on SURL has expired, but the file is still in the cache.

SRM_INVALID_PATH

- SURL does not refer to an existing known file path.

SRM_AUTHORIZATION_FAILURE

- client is not authorized to receive the information of the SURL or to access the directory or sub-directories

## srmStatusOfLsRequest

srmStatusOfLsRequest() returns a list of files with a basic information. This is an  asynchronous operation of srmLs.

| Input | srmStatusOfLsRequestRequest |
| --- | --- |
| Output | srmStatusOfLsRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfLsRequestRequest | TUserID authorizationID TRequestToken requestToken xsd:int offset xsd:int count | 0 1 0 0 | 1 1 1 1 |
| srmStatusOfLsRequestResponse | TReturnStatus returnStatus ArrayOfTMetaDataPathDetail details | 1 0 | 1 1 |

### Notes on the Behavior

- Empty directories will be returned.

- We recommend width first in the listing.

- We recommend that list of directories come before list of files in the return array (details).

- For non-existing file or directory, SRM_INVALID_PATH must be returned.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs are checked and the information for all SURLs is returned successfully.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURL request is successfully completed, and some SURL request is failed. Details are on the files status.

SRM_REQUEST_QUEUED

- successful request submission and all files request is still on the queue.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request information

SRM_TOO_MANY_RESULTS

- srmLs request has generated too many results that SRM cannot handle. In most cases, it needs to be narrowed down with offset and count by the client.

SRM_INVALID_REQUEST

- Negative values for offset and count are provided.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- Requested fileStorageType is not supported in SRM

- Filtering fileStorageType is not supported in SRM

- Directory operation (directory SURL, allLevelRecursive and numOfLevels) is not supported in SRM

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. The information for the SURL is checked and returned successfully.

SRM_FILE_IN_CACHE

- lifetime on SURL has expired, but the file is still in the cache.

SRM_INVALID_PATH

- SURL does not refer to an existing known file path

SRM_AUTHORIZATION_FAILURE

- client is not authorized to receive the information of the SURL or to access the directory or sub-directories

## srmMv

srmMv is to move a file from one local path to another local path.

| Input | srmMvRequest |
| --- | --- |
| Output | srmMvResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmMvRequest | TUserID authorizationID TSURLInfo fromSURL TSURLInfo toSURL | 0 1 1 | 1 1 1 |
| srmMvResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- Applies to both directory and file.

- Authorization checks need to be performed on both fromSURL and toSURL.

### Return Status Code

SRM_SUCCESS

- All requests are successfully completed. SURL is moved successfully from one local path to another local path.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to move fromSURL.

- Client is not authorized to move a file into toSURL

SRM_INVALID_PATH

- fromSURL does not refer to an existing known path

- toSURL does not refer to a valid path

SRM_DUPLICATION_ERROR

- toSURL exists already.

SRM_FILE_LOST

- the requested file is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- The requested file is being used by other clients.

SRM_FILE_UNAVAILABLE

- the requested file is temporarily unavailable.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

# Data Transfer Functions – Message Types and Operations

summary:

srmPrepareToGet

srmStatusOfGetRequest

srmPrepareToPut

srmStatusOfPutRequest

srmCopy

srmStatusOfCopyRequest

srmBringOnline

srmStatusOfBringOnlineRequest

srmReleaseFiles

srmPutDone

srmAbortRequest

srmAbortFiles

srmSuspendRequest

srmResumeRequest

srmGetRequestSummary

srmExtendFileLifeTime

srmGetRequestTokens

## srmPrepareToGet

This function is used to bring files online upon the client’s request and assign TURL so that client can access the file. Lifetime (pinning expiration time) is assigned on the TURL. When specified target space token which must be referred to an online space, the files will be prepared using the space associated with the space token.  It is an asynchronous operation, and request token must be returned if request is valid and accepted. The status must be checked through srmStatusOfGetRequest with the returned request token.

| Input | srmPrepareToGetRequest |
| --- | --- |
| Output | srmPrepareToGetResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmPrepareToGetRequest | TUserID authorizationID ArrayOfTGetFileRequest arrayOfFileRequests xsd:string userRequestDescription ArrayOfTExtraInfo storageSystemInfo TFileStorageType desiredFileStorageType TLifeTimeInSeconds desiredTotalRequestTime TLifeTimeInSeconds desiredPinLifetime TSpaceToken targetSpaceToken TRetentionPolicyInfo targetFileRetentionPolicyInfo TTransferParameters transferParametersHint | 0 1 0 0 0 0 0 0 0 0 | 1 1 1 11 1 1 1 1 1 |
| srmPrepareToGetResponse | TReturnStatus returnStatus TRequestToken requestToken TLifeTimeInSeconds remainingTotalRequestTime | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- The default value of “lifetime” for Volatile or Durable files will be the lifetime left in the space of the corresponding file type. The default value of “fileStorageType” is Volatile.

- If input parameter TSpaceToken is provided, then the target space token must refer to online space. All requested files will be prepared into the target space.

- Input parameter targetFileRetentionPolicyInfo of TRetentionPolicyInfo is to specify the desired retention policy information on the file when the file is prepared online.

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly. Otherwise, the request may be rejected with SRM_INVALID_REQUEST.

- Access latency must be ONLINE always.

- Input parameter TAccessPattern is provided at the request-level, and all files will have the same access pattern.

- TAccessPattern may conflict with the type of the target space associated with target space token, when both provided. In this case, TAccessPattern in the input parameter TTransferParameters must be ignored.

- The userRequestDescription is a user designated name for the request.  It can be used in the srmGetRequestID function to get back the system assigned request tokens.

- Only pull mode is supported for file transfers that client must pull the files from the TURL within the expiration time (remainingPinTime).

- Input parameter desiredPinLifetime is for a client preferred lifetime (expiration time) on the prepared TURL.

- If request is accepted, SRM assigns the requestToken for asynchronous status checking. In such case, the returned status code should be SRM_REQUEST_QUEUED.

- totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- The invocation of srmReleaseFile() is expected for finished files later on.

- The returned request token should be valid until all files in the request are released or removed.

### Return Status Code

SRM_SUCCESS

- successful request submission and acceptance. Request token must be returned.

SRM_REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- arrayOfFileRequest is empty

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly.

- Access latency is something other than ONLINE.

- targetSpaceToken does not refer to an existing known space in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free. When client does not specify the targetSpaceToken, SRM uses a default space. The default space is not sufficient to accommodate the request.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- Directory operation is not supported in the SRM server.

- Recursive directory operation is not supported in the SRM server.

- None of the file transfer protocols are supported in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmStatusOfGetRequest

This function is used to check the status of the previously requested srmPrepareToGet. Request token from srmPrepareToGet must be provided.

| Input | srmStatusOfGetRequestRequest |
| --- | --- |
| Output | srmStatusOfGetRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfGetRequestRequest | TRequestToken requestToken TUserID authorizationID ArrayOfTSURL arrayOfSourceSURLs | 1 0 0 | 1 1 1 |
| srmStatusOfGetRequestResponse | TReturnStatus returnStatus ArrayOfTGetRequestFileStatus arrayOfFileStatuses TLifeTimeInSeconds remainingTotalRequestTime | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- The default value of “lifetime” for Volatile or Durable files will be the lifetime left in the space of the corresponding file type. The default value of “fileStorageType” is Volatile.

- If arrayOfSourceSURLs is not provided, SRM must return status for all file requests in the request that is associated with the request token.

- When the file is ready and TURL is prepared, the return status code should be SRM_FILE_PINNED.

- When the file is ready for the client, the file is implicitly pinned in the cache and lifetime will be enforced.

- If any of the request files is temporarily unavailable, SRM_FILE_UNAVAILABLE must be returned for the file.

- If any of the request files is permanently lost, SRM_FILE_LOST must be returned for the file.

- The file request must fail with an error SRM_FILE_BUSY if srmPrepareToGet requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- SRM must fail (SRM_FAILURE) only if all files in the request failed.

- totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

### Return Status Code

For request level return status,

SRM_SUCCESS

- all file requests are successfully completed. All SURLs are successfully pinned. For TURLs, file level status needs to be checked.

SRM_REQUEST_QUEUED

- successful request submission and all files request is still on the queue

SRM_REQUEST_INPROGRESS

- some files are completed, and some files are still on the queue

SRM_PARTIAL_SUCCESS

- All requests are completed. Some file request is successfully pinned, and some file request is failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- Directory operation is not supported in the SRM server.

- Recursive directory operation is not supported in the SRM server.

- None of the file transfer protocols are supported in the SRM server.

SRM_ABORTED

- The request has been aborted.

SRM_REQUEST_TIMED_OUT

- Total request time is over and the request is suspended.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_FILE_PINNED

- successful request completion for the SURL. SURL is successfully pinned, and TURL is available for access.

SRM_REQUEST_QUEUED

- file request is still on the queue.

SRM_REQUEST_INPROGRESS

- file request is being served.

SRM_ABORTED

- The requested file has been aborted.

SRM_RELEASED

- The requested file has been released.

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out.

SRM_FILE_LOST

- the requested file is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

SRM_FILE_UNAVAILABLE

- the requested file is temporarily unavailable.

SRM_INVALID_PATH

- SURL does not refer to an existing known file request that is associated with the request token

SRM_AUTHORIZATION_FAILURE

- client is not authorized to retrieve the file that is associated with the SURL

SRM_FILE_IN_CACHE

- pin lifetime has expired, but the file is still in the cache.

SRM_FILE_LIFETIME_EXPIRED

- SURL is expired

- TURL is expired

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmBringOnline

This function is used to bring files online upon the client’s request so that client can make certain data readily available for future access. In hierarchical storage systems, it is expected to “stage” files to the top hierarchy and make sure that the files stay online for a certain period of time. When client specifies target space token which must be referred to an online space, the files will be brought online using the space associated with the space token.  It is an asynchronous operation, and request token must be returned if asynchronous operation is necessary in SRM. The status may be checked through srmStatusOfBringOnlineRequest with the returned request token.

This function is similar to srmPrepareToGet, but it does not return Transfer URL (TURL).

| Input | srmBringOnlineRequest |
| --- | --- |
| Output | srmBringOnlineResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmBringOnlineRequest | TUserID authorizationID ArrayOfTGetFileRequest arrayOfFileRequests xsd:string userRequestDescription ArrayOfTExtraInfo storageSystemInfo TFileStorageType desiredFileStorageType TLifeTimeInSeconds desiredTotalRequestTime TLifeTimeInSeconds desiredLifetime TSpaceToken targetSpaceToken TRetentionPolicyInfo targetFileRetentionPolicyInfo TTransferParameters transferParametersHint TLifeTimeInSeconds deferredStartTime | 0 1 0 0 0 0 0 0 0 0 0 | 1 1 1 1 11 1 1 1 1 1 |
| srmBringOnlineResponse | TReturnStatus returnStatus TRequestToken requestToken TLifeTimeInSeconds remainingTotalRequestTime TLifeTimeInSeconds remainingDeferredStartTime | 1 0 0 0 | 1 1 1 1 |

### Notes on the Behavior

- Input parameter deferredStartTime is to support CE-SE resource co-allocation and tape mounting efficiency. It means that client does not intent to use the files before that time. If SRM decides not to bring any files until deferredStartTime is reached, SRM_REQUEST_QUEUED must be returned.

- Output parameter remainingDeferredStartTime indicates how long the deferredStartTime is left, if supported.

- Input parameter targetFileRetentionPolicyInfo of TRetentionPolicyInfo is to specify the desired retention policy information on the file when the file is brought online.

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly. Otherwise, the request may be rejected, and SRM_INVALID_REQUEST will be returned.

- TAccessPattern may conflict with the type of the target space associated with target space token, when both provided. In this case, TAccessPattern in the input parameter TTransferParameters must be ignored.

- If the transfer protocol hints are not specified, default is assumed to be processing mode and LAN access for the site.

- Access latency must be ONLINE always.

- It is up to the SRM implementation to decide TConnectionType if not provided.

- The userRequestDescription is a user designated name for the request.  It can be used in the srmGetRequestID method to get back the system assigned request ID.

- Input parameter desiredLifetime is for a client preferred lifetime (expiration time) on the file “copies (or “states”) of the SURLs that will be “brought online” into the target space that is associated with the targetSpaceToken.

- This call may be an asynchronous (non-blocking) call, and SRM assigns the requestToken when the request is valid and accepted. The returned status code should be SRM_REQUEST_QUEUED. To get subsequent status and results, separate calls should be made through srmStatusOfBringOnline.

- The returned request token should be valid until all files in the request are released, removed or aborted.

- Input parameter totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

- When srmAbortRequest is requested for srmBringOnline request, the request gets aborted, but those files that are brought online will remain in the space where they are brought in, and are not removed.  Clients need to remove those files through srmPurgeFromSpace or srmRm.

### Return Status Code

SRM_SUCCESS

- successful request submission and acceptance. Request token must be returned.

SRM_REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- arrayOfFileRequest is empty

- Access latency refers to something other than ONLINE.

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly.

- targetSpaceToken does not refer to an existing known space in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- deferredStartTime is not supported in the SRM server.

- Directory operation is not supported in the SRM server.

- Recursive directory operation is not supported in the SRM server.

- None of the file transfer protocols are supported in the SRM server.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmStatusOfBringOnlineRequest

This function is used to check the status of the previous request to srmBringOnline, when asynchronous operation is necessary in the SRM. Request token must have been provided in response to the srmBringOnline.

| Input | srmStatusOfBringOnlineRequestRequest |
| --- | --- |
| Output | srmStatusOfBringOnlineRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfBringOnlineRequestRequest | TRequestToken requestToken TUserID authorizationID ArrayOfTSURL arrayOfSourceSURLs | 1 0 0 | 1 1 1 |
| srmStatusOfBringOnlineRequestResponse | TReturnStatus returnStatus ArrayOfTBringOnlineRequestFileStatus arrayOfFileStatuses TLifeTimeInSeconds remainingTotalRequestTime TLifeTimeInSeconds remainingDeferredStartTime | 1 0 0 0 | 1 1 1 1 |

### Notes on the Behavior

- If arrayOfSourceSURLs is not provided, returns status for all files in this request.

- When the file is ready online, the return status code should be SRM_FILE_IN_CACHE.

- Output parameter remainingDeferredStartTime indicates how long the deferredStartTime is left, if supported.

- When the file is ready for the client, the file is implicitly pinned in the cache and lifetime will be enforced.

- If any of the request files is temporarily unavailable, SRM_FILE_UNAVAILABLE must be returned for the file.

- If any of the request files is permanently lost, SRM_FILE_LOST must be returned for the file.

- The file request must fail with an error SRM_FILE_BUSY if srmBringOnline requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

- SRM must fail (SRM_FAILURE) only if all files in the request failed.

- Input parameter totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- If totalRequestTime is 0 (zero), SRM server just continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

- If SRM decides not to bring any files until input parameter deferredStartTime is reached, SRM_REQUEST_QUEUED must be returned.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs are successfully brought online.

SRM_REQUEST_QUEUED

- successful request submission and all files request is still on the queue

SRM_REQUEST_INPROGRESS

- some files are completed, and some files are not completed yet.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some files are successfully brought online, and some files are failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- deferredStartTime is not supported in the SRM server.

- Directory operation is not supported in the SRM server.

- Recursive directory operation is not supported in the SRM server.

- None of the file transfer protocols are supported in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free.

SRM_ABORTED

- The request has been aborted.

SRM_REQUEST_TIMED_OUT

- Total request time is over and the request is suspended.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. SURL is successfully brought online.

SRM_REQUEST_QUEUED

- file request is still on the queue.

SRM_REQUEST_INPROGRESS

- file request is being served.

SRM_FILE_IN_CACHE

- pin lifetime has expired, but the file is still in the cache.

SRM_AUTHORIZATION_FAILURE

- client is not authorized to retrieve the file that is associated with the SURL

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out.

SRM_ABORTED

- The requested file has been aborted.

SRM_RELEASED

- The requested file has been released.

SRM_FILE_LOST

- the requested file is permanently lost.

SRM_FILE_BUSY

- client requests for files which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

SRM_FILE_UNAVAILABLE

- the requested file is temporarily unavailable.

SRM_INVALID_PATH

- SURL does not refer to an existing known file request that is associated with the request token

SRM_FILE_LIFETIME_EXPIRED

- SURL is expired

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmPrepareToPut

This function is used to write files into the storage. Upon the client’s request, SRM prepares a TURL so that client can write data into the TURL. Lifetime (pinning expiration time) is assigned on the TURL. When a specified target space token is provided, the files will be located finally in the targeted space associated with the target space token.  It is an asynchronous operation, and request token must be returned if the request is valid and accepted to the SRM. The status may be checked through srmStatusOfPutRequest with the returned request token.

| Input | srmPrepareToPutRequest |
| --- | --- |
| Output | srmPrepareToPutResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmPrepareToPutRequest | TUserID authorizationID ArrayOfTPutFileRequest arrayOfFileRequests xsd:string userRequestDescription TOverwriteMode overwriteOption ArrayOfTExtraInfo storageSystemInfo TLifeTimeInSeconds desiredTotalRequestTime TLifeTimeInSeconds desiredPinLifetime TLifeTimeInSeconds desiredFileLifetime TFileStorageType desiredFileStorageType TSpaceToken targetSpaceToken TRetentionPolicyInfo targetFileRetentionPolicyInfo TTransferParameters transferParametersHint | 0 1 0 0 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 1 1 |
| srmPrepareToPutResponse | TReturnStatus returnStatus TRequestToken requestToken TLifeTimeInSeconds remainingTotalRequestTime | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- The default value of “lifetime” for Volatile or Durable files will be the lifetime left in the space of the corresponding file type. The default value of “fileStorageType” is Volatile.

- TURL returned by the srmPrepareToPut may not be used for read access with any protocol. An explicit srmPrepareToGet or srmBringOnline is required.

- TAccessPattern may conflict with the type of the target space associated with target space token, when both provided. In this case, TAccessPattern in the input parameter TTransferParameters must be ignored.

- Input parameter TSpaceToken is provided at the request-level, and all files in the request will end up in the space that is associated with the target space token if the space is enough for all files.

- Input parameter targetFileRetentionPolicyInfo of TRetentionPolicyInfo is to specify the desired retention policy information on the file when the file is written into the target storage system.

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly. Otherwise, the request may be rejected and SRM_INVALID_REQUEST must be returned.

- Only push mode is supported for file transfers that client must “push” the file to the prepared TURL.

- Input parameter targetSURL in the TPutFileRequest has to be local to SRM. If targetSURL is not specified, SRM will make a reference for the file request automatically and put it in the specified user space if provided. This reference SURL will be returned along with the “Transfer URL”.

- srmPutDone() is expected after each file is “put” into the prepared TURL.

- Input parameter desiredPinLifetime is the lifetime (expiration time) on the TURL when the Transfer URL is prepared. It does not refer to the lifetime of the SURL.

- Input parameter desiredFileLifetime is the lifetime of the SURL when the file is put into the storage system. It does not refer to the lifetime (expiration time) of the TURL.

- The lifetime of the SURL starts as soon as SRM receives the srmPutDone().  If srmPutDone() is not provided, then the files in that space are subject to removal when the lifetime on the TURL expires or the lifetime on the space expires.  The lifetime on the TURL can be found in the status of the file request as output parameter remainingPinTime in TPutRequestFileStatus.

- If request is accepted, SRM assigns the requestToken for asynchronous status checking. In such case, the returned status code should be SRM_REQUEST_QUEUED.

- Input parameter totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

### Return Status Code

SRM_SUCCESS

- successful request submission and acceptance. Request token must be returned.

SRM_REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly.

- targetSpaceToken does not refer to an existing known space in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- None of the file transfer protocols are supported in the SRM server.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmStatusOfPutRequest

This function is used to check the status of the previously requested srmPrepareToPut. Request token from srmPrepareToPut must be provided.

| Input | srmStatusOfPutRequestRequest |
| --- | --- |
| Output | srmStatusOfPutRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfPutRequestRequest | TRequestToken requestToken TUserID authorizationID ArrayOfTSURL arrayOfTargetSURLs | 1 0 0 | 1 1 1 |
| srmStatusOfPutRequestResponse | TReturnStatus returnStatus ArrayOfTPutRequestFileStatus arrayOfFileStatuses TLifeTimeInSeconds remainingTotalRequestTime | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- The default value of “lifetime” for Volatile or Durable files will be the lifetime left in the space of the corresponding file type. The default value of “fileStorageType” is Volatile.

- If arrayOfTargetSURLs is not provided, returns status for all the file requests in this request.

- When the space is ready for client to “put” data and TURL is prepared, the return status code should be SRM_SPACE_AVAILABLE.

- When the file space is ready for the client, the TURL is available in the cache and pin lifetime on the TURL will be enforced.

- If a targetSURL is provided with some directory structure, the directory structure must exist, and SRM will not create the directory structure for the targetSURL.  In such case, SRM_INVALID_PATH must be returned. srmMkdir may be used to create the directory structure.

- If the space for the requested files is full, and TURL cannot be returned, then SRM_EXCEED_ALLOCATION, SRM_NO_USER_SPACE, or SRM_NO_FREE_SPACE must be returned for the files.

- SRM must fail (SRM_FAILURE) only if all files in the request failed.

- Input parameter totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. For all SURLs, spaces are allocated, and TURLs are prepared.

SRM_REQUEST_QUEUED

- successful request submission and all files request is still on the queue

SRM_REQUEST_INPROGRESS

- some files are completed, and some files are still on the queue

SRM_PARTIAL_SUCCESS

- All requests are completed. For some file requests, the spaces are allocated and TURLs are prepared, but for some file requests, it is failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

- targetSpaceToken that client provided does not refer to an existing space in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free.

SRM_REQUEST_TIMED_OUT

- Total request time is over and the request is suspended.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- None of the file transfer protocols are supported in the SRM server.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_SPACE_AVAILABLE

- successful request completion for the “put” request. The space is allocated, and TURL is prepared.

SRM_REQUEST_QUEUED

- file request is still on the queue.

SRM_REQUEST_INPROGRESS

- file request is being served.

SRM_DONE

- Client’s file transfer into TURL is completed, and srmPutDone on the targetSURL is completed. The file is now in the cache and lifetime on the targetSURL is started.

SRM_FILE_IN_CACHE

- lifetime on SURL has expired, but the file is still in the cache.

SRM_INVALID_PATH

- targetSURL does not refer to a valid path.

SRM_DUPLICATION_ERROR

- targetSURL refers to an existing SURL without no overwriting option.

SRM_AUTHORIZATION_FAILURE

- client is not authorized to retrieve the file that is associated with the SURL

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out.

SRM_ABORTED

- The requested file has been aborted.

SRM_RELEASED

- The requested file has been released.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmCopy

This function is used to copy files from source storage sites into the target storage sites. The source storage site or the target storage site needs to be the SRM itself that the client makes the srmCopy request. If both source and target are local to the SRM, it performed a local copy. There are two cases for remote copies: 1. Target SRM is where client makes a srmCopy request (PULL case), 2. Source SRM is where client makes a srmCopy request (PUSH case).

- PULL case: Upon the client’s srmCopy request, the target SRM makes a space at the target storage, and makes a request srmPrepareToGet to the source SRM. When TURL is ready at the source SRM, the target SR M transfers the file from the source TURL into the prepared target storage. After the file transfer completes, srmReleaseFiles is issued to the source SRM.

- PUSH case: Upon the client’s srmCopy request, the source SRM prepares a file to be transferred out to the target SRM, and makes a request srmPrepareToPut to the target SRM. When TURL is ready at the target SRM, the source SRM transfers the file from the prepared source into the prepared target TURL. After the file transfer completes, srmPutDone is issued to the target SRM.

When specified target space token is provided, the files will be located finally in the targeted space associated with the space token.  It is an asynchronous operation, and request token must be returned. The status may be checked through srmStatusOfCopyRequest with the returned request token.

| Input | srmCopyRequest |
| --- | --- |
| Output | srmCopyResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmCopyRequest | TUserID authorizationID ArrayOfTCopyFileRequest arrayOfFileRequests xsd:string userRequestDescription TOverwriteMode overwriteOption TLifeTimeInSeconds desiredTotalRequestTime TLifeTimeInSeconds desiredTargetSURLLifetime TFileStorageType targetFileStorageType TSpaceToken targetSpaceToken TRetentionPolicyInfo targetFileRetentionPolicyInfo | 0 1 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 |
| srmCopyResponse | TReturnStatus returnStatus TRequestToken requestToken TLifeTimeInSeconds remainingTotalRequestTime | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- The default value of “lifetime” for Volatile or Durable files will be the lifetime left in the space of the corresponding file type. The default value of “fileType” is Volatile.

- When aborted, target SURLs need to be provided.

- Input parameter TSpaceToken is provided at the request-level, and all files in the request will end up in the space that is associated with the target space token.

- Input parameter targetFileRetentionPolicyInfo of TRetentionPolicyInfo is to specify the desired retention policy information on the file when the file is written into the target storage system.

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly. Otherwise, the request may be rejected, and SRM_INVALID_REQUEST must be returned.

- If request is accepted, SRM assigns the requestToken for asynchronous status checking. In such case, the returned status code should be SRM_REQUEST_QUEUED.

- Pull mode: copy from remote location to the SRM. (e.g. from remote to MSS.)

- Push mode: copy from the SRM to remote location.

- Always release files through srmReleaseFiles from the source after copy is done, if source is an SRM and PULL mode was performed.

- Always issue srmPutDone to the target after copy is done, if target is an SRM and PUSH mode was performed.

- Note there is no protocol negotiation with the client for this request.

- Input parameter desiredTotalRequestTime means: if all the file transfer for this request must be complete in this desiredTotalRequestTime. Otherwise, the request is returned as failed at the end of the desiredTotalRequestTime, and SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED. All completed files must not be removed, but status of the files must be returned to the client.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

- When both sourceSURL and targetSURL are local, local copy must be performed.

- Empty directories are copied as well.

- If a targetSURL is provided with some directory structure, the directory structure must exist, and SRM will not create the directory structure for the targetSURL.  In such case, SRM_INVALID_PATH must be returned. srmMkdir may be used to create the directory structure.

- If the sourceSURL and targetSURL are provided as directories (copying directories) when SRM implementation supports, then all sub directories will be copied over from the source to the target, and complete sub-directory structure will be created only if TDirOption indicates them.

### Return Status Code

SRM_SUCCESS

- successful request submission and acceptance. Request token must be returned.

SRM_REQUEST_QUEUED

- successful request submission and acceptance. Request token must be returned.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

- Client is not authorized to copy files into the space that client provided with targetSpaceToken or targetFileRetentionPolicyInfo

SRM_INVALID_REQUEST

- If both input parameters TSpaceToken and TRetentionPolicyInfo are provided, then their types must match exactly.

- targetSpaceToken does not refer to an existing known space in the SRM server.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- user space is not enough to hold all requested SURLs.

SRM_NO_FREE_SPACE

- SRM space is not enough to hold all requested SURLs for free.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- Directory operation is not supported in the SRM server.

- Recursive directory operation is not supported in the SRM server.

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

- function is not supported in the SRM server

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmStatusOfCopyRequest

This function is used to check the status of the previously requested srmCopy. Request token from srmCopy must be provided.

| Input | srmStatusOfCopyRequestRequest |
| --- | --- |
| Output | srmStatusOfCopyRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmStatusOfCopyRequestRequest | TRequestToken requestToken TUserID authorizationID ArrayOfTSURL arrayOfSourceSURLs ArrayOfTSURL arrayOfTargetSURLs | 1 0 0 0 | 1 1 1 1 |
| srmStatusOfCopyRequestResponse | TReturnStatus returnStatus ArrayOfTCopyRequestFileStatus arrayOfFileStatuses TLifeTimeInSeconds remainingTotalRequestTime | 1 0 0 | 1 1 1 |

### Notes on the Behavior

- If arrayOfSourceSURLs and/or arrayOfTargetSURLs are not provided, return status for all file requests in the request.

- If the target space for the requested files is full, then SRM_EXCEED_ALLOCATION, SRM_NO_USER_SPACE, or SRM_NO_FREE_SPACE must be returned.

- SRM must fail (SRM_FAILURE) only if all files in the request failed.

- totalRequestTime means: All the file transfer for this request must be complete within this totalRequestTime.  Otherwise, SRM_REQUEST_TIMED_OUT must be returned as the status code with individual file status of SRM_REQUEST_SUSPENDED.

- If totalRequestTime is 0 (zero), SRM server must continues the request until completed.

- Client may use srmResumeRequest() to resume the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- Client must use srmAbortRequest() to terminate the request in the status of SRM_REQUEST_TIMED_OUT because of the totalRequestTime.

- SRM server may terminate the timed-out request after a certain period of time.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All source SURLs are copied into the target destination successfully.

SRM_REQUEST_QUEUED

- successful request submission and all files request is still on the queue

SRM_REQUEST_INPROGRESS

- Some files are completed, and some files are still on the queue. Details are on the files status.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some file request is successfully copied into the target destination, and some file request is failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to submit the request

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

- targetSpaceToken does not refer to an existing known space in the SRM server.

SRM_TOO_MANY_RESULTS

- Request produced too many results that SRM server cannot handle, and arrayOfSourceURLs and arrayOfTargetURLs cannot fit the results to return.

SRM_REQUEST_TIMED_OUT

- Total request time is over and the request is suspended.

SRM_SPACE_LIFETIME_EXPIRED

- space associated with the targetSpaceToken is expired.

SRM_EXCEED_ALLOCATION

- space associated with the targetSpaceToken is not enough to hold all requested SURLs.

SRM_NO_USER_SPACE

- Insufficient space left in the space that is associated with spaceToken.

SRM_NO_FREE_SPACE

- When client does not specify the spaceToken, SRM uses a default space. The default space is insufficient to accommodate the request.

SRM_ABORTED

- The request has been aborted.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- SRM server does not support the given input parameters. For example, client requested bbftp for the only transfer protocol, but SRM cannot support that. Client requested desiredFileStorageType that is not supported by the SRM server.

- targetFileRetentionPolicyInfo does not refer to a supported retention policy in the SRM server.

- Overwrite option is not supported in the SRM server.

- Directory operation is not supported in the SRM server.

- Recursive directory operation is not supported in the SRM server.

- any input parameter is not supported in the SRM server

- a particular type of an input parameter is not supported in the SRM server

- function is not supported in the SRM server

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For file level return status,

SRM_DONE

- successful request completion for the file. The source SURL is copied into the target destination targetSURL successfully, and lifetime on the targetSURL is started.

SRM_REQUEST_QUEUED

- file request is still on the queue.

SRM_REQUEST_INPROGRESS

- file request is being served.

SRM_FILE_LOST

- the request file (sourceSURL) is permanently lost.

SRM_FILE_BUSY

- client requests for files at the source (sourceSURL) which there is an active srmPrepareToPut (no srmPutDone is not yet called) for.

SRM_FILE_UNAVAILABLE

- the request file (sourceSURL)  is temporarily unavailable.

SRM_FILE_IN_CACHE

- lifetime on targetSURL has expired, but the file is still in the cache.

SRM_INVALID_PATH

- sourceSUR does not exist

- targetSURL does not refer to a valid path.

SRM_DUPLICATION_ERROR

- targetSURL refers to an existing SURL without no overwriting option.

SRM_AUTHORIZATION_FAILURE

- Client is not authorized to copy files from sourceSURL

- Client is not authorized to copy files into targetSURL

- Client is not authorized to copy files into the space that client provided with targetSpaceToken or targetFileRetentionPolicyInfo

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out.

SRM_ABORTED

- The requested file has been aborted.

SRM_RELEASED

- The requested file has been released.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmReleaseFiles

This function is used to release pins on the previously requested “copies” (or “state”) of the SURL. This function normally follows srmPrepareToGet or srmBringOnline functions.

| Input | srmReleaseFilesRequest |
| --- | --- |
| Output | srmReleaseFilesResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmReleaseFilesRequest | TRequestToken requestToken TUserID authorizationID ArrayOfTSURL arrayOfSURLs xsd:boolean doRemove | 0 0 1 0 | 1 1 1 1 |
| srmReleaseFilesResponse | TReturnStatus returnStatus ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 | 1 1 |

### Notes on the Behavior

- doRemove by default is false. If remove is true, the pin on the file is released, the “copy” or “state” is removed and SRM may release the resource.

- Directory is okay for SURL. In such case, it will release all files recursively in the directory.

- If requestToken is not provided, then the SRM will release all the files specified by the SURLs owned by this user, regardless of the requestToken.

- If requestToken is not provided, then authorizationID is needed.  It may be inferred or provide in the call.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs are released successfully.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURLs are successfully released, and some SURLs are failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to release files

SRM_INVALID_REQUEST

- arrayOfSURLs is empty.

- requestToken does not refer to an existing known request of srmPrepareToGet or srmBringOnline in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

- input parameter doRemove is not supported in the SRM. srmRm must be used.

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. SURL is released successfully.

SRM_INVALID_PATH

- SURL does not refer to an existing file

SRM_AUTHORIZATION_FAILURE

- client is not authorized to release SURL

SRM_LAST_COPY

- SURL is the last copy when remove flag is on

SRM_FILE_LIFETIME_EXPIRED

- SURL is expired already.

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out.

SRM_ABORTED

- The requested file has been aborted.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmPutDone

srmPutDone() is used to notify the SRM that the client completed a file transfer to the TransferURL in the allocated space. This call should normally follow srmPrepareToPut.

| Input | srmPutDoneRequest |
| --- | --- |
| Output | srmPutDoneResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmPutDoneRequest | TRequestToken requestToken TUserID authorizationID ArrayOfTSURL arrayOfSURLs | 1 0 1 | 1 1 1 |
| srmPutDoneResponse | TReturnStatus returnStatus ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 | 1 1 |

### Notes on the Behavior

- Called by client after srmPrepareToPut() prepares the TURL and the client completes the file transfer into the prepared TURL.

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. TURLs contain data, and file lifetimes on the SURLs start.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some file requests are successfully completed, and some file requests are failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to call the request specified by the requestToken

SRM_INVALID_REQUEST

- arrayOfSURLs is empty.

- requestToken is empty.

- requestToken does not refer to an existing known request in the SRM server.

SRM_REQUEST_TIMED_OUT

- Total request time is over and the request is suspended.

SRM_ABORTED

- The request has been aborted.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

For file level return status,

SRM_DONE

- successful request completion of the “put done” for the targetSURL

SRM_INVALID_PATH

- SURL does not refer to an existing file request

SRM_AUTHORIZATION_FAILURE

- client is not authorized to call the request srmPutDone() on the SURL

SRM_FILE_LIFETIME_EXPIRED

- targetSURL has an expired TURL.

SRM_SPACE_LIFETIME_EXPIRED

- targetSURL has an expired space allocation.

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out.

SRM_ABORTED

- The requested SURL file has been aborted.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmAbortRequest

srmAbortRequest() allows clients to prematurely terminate asynchronous requests of any types. It may involve data transfer requests initiated by a call to srmPrepareToGet(), srmBringOnline(), srmPrepareToPut() or srmCopy(). The effect of srmAbortRequest() depends on the type of request. For data transfer request, the SRM will attempt a complete cleanup of running transfers and files in intermediate state.

| Input | srmAbortRequestRequest |
| --- | --- |
| Output | srmAbortRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmAbortRequestRequest | TRequestToken requestToken TUserID authorizationID | 1 0 | 1 1 |
| srmAbortRequestResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- Terminate all files in the request regardless of the file state. Remove files from the queue, and release cached files if a limited lifetime is associated with the file. Expired files are released.

- Those files that are brought online with unlimited lifetime will remain in the space where they are brought in. and are not removed. Clients need to remove explicitly through srmRm or srmPurgeFromSpace.

- Abort must be allowed to all requests with requestToken.

### Return Status Code

SRM_SUCCESS

- successful request completion. Request is aborted successfully.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to abort files in the request specified by the requestToken

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

## srmAbortFiles

srmAbortFiles() allows clients  to abort selective file requests from the asynchronous requests of any type.  It may include data transfer requests initiated by a call to srmPrepareToGet(), srmBringOnline(), srmPrepareToPut(), or srmCopy(). The effect of a srmAbortFiles() depends on the type of the request.

| Input | srmAbortFilesRequest |
| --- | --- |
| Output | srmAbortFilesResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmAbortFilesRequest | TRequestToken requestToken ArrayOfTSURL arrayOfSURLs TUserID authorizationID | 1 1 0 | 1 1 1 |
| srmAbortFilesResponse | TReturnStatus returnStatus ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 | 1 1 |

### Notes on the Behavior

- Abort all files in this call regardless of the state.

### Return Status Code

For request level return status,

SRM_SUCCESS

- successful request completion. All SURLs are aborted successfully.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some SURLs ares successfully aborted, and some SURLs are failed. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to abort files in the request specified by the requestToken

SRM_INVALID_REQUEST

- arrayOfSURLs is empty.

- requestToken is empty.

- requestToken does not refer to an existing known request in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. SURL is aborted successfully.

SRM_INVALID_PATH

- SURL does not refer to an existing file request that is associated with the request token

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmSuspendRequest

srmSuspendedRequest is to suspend a previously submitted active request.

| Input | srmSuspendRequestRequest |
| --- | --- |
| Output | srmSuspendRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmSuspendRequestRequest | TRequestToken requestToken TUserID authorizationID | 1 0 | 1 1 |
| srmSuspendRequestResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- Suspend all files in this request until srmResumeRequest is issued.

### Return Status Code

SRM_SUCCESS

- successful request completion. Request is suspended successfully.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to suspend the request specified by the requestToken

SRM_INVALID_REQUEST

- requestToken is empty.

- requestToken does not refer to an existing known request in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

## srmResumeRequest

srmResumeRequest is to resume previously suspended requests or timed-out request.

| Input | srmResumeRequestRequest |
| --- | --- |
| Output | srmResumeRequestResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmResumeRequestRequest | TRequestToken requestToken TUserID authorizationID | 1 0 | 1 1 |
| srmResumeRequestResponse | TReturnStatus returnStatus | 1 | 1 |

### Notes on the Behavior

- Resume the previously suspended request.

- Resume the previously timed-out request which is in the state of SRM_REQUEST_TIMED_OUT.

### Return Status Code

SRM_SUCCESS

- successful request completion. Request is resumed successfully.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to resume the request specified by the requestToken

SRM_INVALID_REQUEST

- requestToken is empty.

- requestToken does not refer to an existing known request in the SRM server.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM server

## srmGetRequestSummary

srmGetRequestSummary is to retrieve a summary of the previously submitted request.

| Input | srmGetRequestSummaryRequest |
| --- | --- |
| Output | srmGetRequestSummaryResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmGetRequestSummaryRequest | ArrayOfTRequestToken arrayOfRequestTokens TUserID authorizationID | 1 0 | 1 1 |
| srmGetRequestSummaryResponse | TReturnStatus returnStatus ArrayOfTRequestSummary arrayOfRequestSummaries | 1 0 | 1 1 |

### Return Status Code

For request interface level return status,

SRM_SUCCESS

- All requests are successfully completed. All requests summaries are checked and returned successfully. Details are on the request status.

SRM_PARTIAL_SUCCESS

- All requests are completed. Summaries of some requests are successfully checked and returned, but some requests summaries are failed. Details are on the request status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to get summary of the request specified by the requestToken

SRM_INVALID_REQUEST

- arrayOfRequestTokens is empty.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

For request level return status,

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

SRM_SUCCESS

- The request has been completed successfully.

SRM_REQUEST_QUEUED

- successful request submission and all files request is still on the queue

SRM_REQUEST_INPROGRESS

- some files are completed, and some files are still on the queue

SRM_REQUEST_TIMED_OUT

- Total request time is over and the request is suspended.

SRM_REQUEST_SUSPENDED

- The request has been suspended.

SRM_ABORTED

- The request has been aborted.

SRM_PARTIAL_SUCCESS

- All requests are completed. Some request is successfully completed, and some request is failed.

SRM_FAILURE

- The request is failed. Explanation needs to be filled for details.

## srmExtendFileLifeTime

srmExtendFileLifetime() allows clients to extend lifetime of existing SURLs of volatile and durable file storage types or pinning lifetime of TURLs. Those TURLs are of the results of srmPrepareToGet and srmPrepareToPut.

| Input | srmExtendFileLifeTimeRequest |
| --- | --- |
| Output | srmExtendFileLifeTimeResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmExtendFileLifeTimeRequest | TUserID authorizationID TRequestToken requestToken ArrayOfTSURL arrayOfSURLs TLifeTimeInSeconds newFileLifetime TLifeTimeInSeconds newPinLifetime | 0 0 0 0 0 | 1 1 1 1 1 |
| srmExtendFileLifeTimeResponse | TReturnStatus returnStatus TLifeTimeInSeconds newExtendedFileLifetime TLifeTimeInSeconds newExtendedPinLifetime ArrayOfTSURLReturnStatus arrayOfFileStatuses | 1 0 0 0 | 1 1 1 1 |

### Notes on the Behavior

- newPinLifetime and newFileLifetime are relative to the calling time. Lifetime will be set from the calling time for the specified period.

- If only requestToken is provided, and none of SURLs are not provided, lifetime of all SURLs belong to the request that is associated with requestToken will have a new lifetime.

- When extending pinning lifetime of TURLs with newPinLifetime, requestToken must be provided.

- When extending lifetime of SURLs with newFileLifetime, requestToken is optional.

- The number of lifetime extensions maybe limited by SRM according to its policies.

- If original lifetime is longer than the requested one, then the requested one will be assigned.

- If newPinLifetime or newFileLifetime is not specified, the SRM can use its default to assign the newPinLifetime or newFileLifetime.

- Lifetime cannot be extended on the released files, aborted files, expired files, and suspended files.

- Extending file lifetime on SURL is similar to srmExtendFileLifetimeInSpace

### Return Status Code

For request level return status,

SRM_SUCCESS

- All requests are successfully completed. All SURLs or TURLs associated with SURLs in the specified request have an extended lifetime. Details are on the files status.

SRM_PARTIAL_SUCCESS

- All requests are completed. Lifetimes on some SURLs or TURLs are successfully extended, and lifetimes on some SURLs or TURLs are failed to be extended. Details are on the files status.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to extend file lifetime

SRM_INVALID_REQUEST

- requestToken does not refer to an existing known request in the SRM server.

- requestToken is not provided, and extending pinning lifetime of TURLs associated with SURLs require requestToken.

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

For file level return status,

SRM_SUCCESS

- successful request completion for the SURL. SURL or TURL associated with the SURL in the request has an extended lifetime.

SRM_INVALID_PATH

- SURL does not refer to an existing file

- SURL does not refer to an existing file request that is associated with the request token

SRM_FILE_LIFETIME_EXPIRED

- Lifetime on SURL is expired already.

SRM_REQUEST_SUSPENDED

- The requested file has been suspended because the request has timed out or because the request is suspended.

SRM_ABORTED

- The requested file has been aborted.

SRM_RELEASED

- The requested file has been released.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmGetRequestTokens

srmGetRequestTokens retrieves request tokens for the client’s requests, given client provided request description. This is to accommodate lost request tokens. This can also be used for getting all request tokens.

| Input | srmGetRequestTokensRequest |
| --- | --- |
| Output | srmGetRequestTokensResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmGetRequestTokensRequest | xsd:string userRequestDescription TUserID authorizationID | 0 0 | 1 1 |
| srmGetRequestTokensResponse | TReturnStatus returnStatus ArrayOfTRequestTokenReturn arrayOfRequestTokens | 1 0 | 1 1 |

### Notes on the Behavior

- If userRequestDescription is null, returns all requests this user has.

- If the user assigned the same name to multiple requests, he may get back multiple request IDs each with the time the request was made.

### Return Status Code

SRM_SUCCESS

- successful request completion. Request tokens are returned successfully.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is notauthorized to get request tokens specified by the userRequestDescription

SRM_INVALID_REQUEST

- userRequestDescription does not refer to any existing known requests

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

# Discovery Functions – Message Types and Operations

summary:

srmGetTransferProtocols

srmPing

## srmGetTransferProtocols

This function is to discover what transfer protocols are supported by the SRM.

| Input | srmGetTransferProtocolsRequest |
| --- | --- |
| Output | srmGetTransferProtocolsResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmGetTransferProtocolsRequest | TUserID authorizationID | 0 | 1 |
| srmGetTransferProtocolsResponse | TReturnStatus returnStatus ArrayOfTSupportedTransferProtocol protocolInfo | 1 0 | 1 1 |

### Notes on the Behavior

- srmGetTransferProtocols() returns the supported file transfer protocols in the SRM with any additional information about the transfer protocol.

### Return Status Code

SRM_SUCCESS

- successful request completion. List of supported transfer protocols are returned successfully.

SRM_AUTHENTICATION_FAILURE

- SRM server failed to authenticate the client

SRM_AUTHORIZATION_FAILURE

- client is not authorized to request storage information

SRM_INTERNAL_ERROR

- SRM has an internal transient error, and client may try again.

SRM_NOT_SUPPORTED

- function is not supported in the SRM

SRM_FAILURE

- any other request failure. Explanation needs to be filled for details.

## srmPing

This function is used to check the state of the SRM. It works as an “are you alive” type of call.

| Input | srmPingRequest |
| --- | --- |
| Output | srmPingResponse |

| Name | type | Min | Max |
| --- | --- | --- | --- |
| srmPingRequest | TUserID authorizationID | 0 | 1 |
| srmPingResponse | xsd:string versionInfo ArrayOfTExtraInfo otherInfo | 1 0 | 1 1 |

### Notes on the Behavior

- srmPing() returns a string containing SRM v2.2 version number as a minimal “up and running” information.  For this particular SRM v2.2 version, it must be “v2.2”.  Other versions may have “v1.1”, “v3.0”, and so on.

- Any additional information about the SRM can be provided in the output parameter otherInfo.

# Appendix

## Status Code Specification

Note:

- Status codes represent errors, warnings and status.

- For each function, status codes are defined with basic meanings for the function. Only those status codes are valid for the function. Specific cases are not stated for each status code.

- If other status codes need to be defined for a specific function, send an email to the collaboration to discuss the usage

## SRM WSDL discovery method

May 1, 2003

A) SURL format:

srm://host[:port]/[soap_end_point_path?SFN=]site_file_name

where […] means optional, and letters in bold are fixed.

We note if the SURL contains the soap_end_point_path, then  it is not possible to change the soap endpoint without changing all the previously published SURLs.

Example SURLs:

Without soap_end_point_path:

srm://dm.lbl.gov:4001/ABC/file_x

with soap_end_point_path:

srm://dm.lbl.gov:4001/srm_servlet?SFN=ABC/file_x

B) Given that soap-end-point-path clause is provided, then the soap endpoint is:

https://host[:port]/soap_end_point_path

C)  If port is missing, the default port assumed is 8443, which is the port for https with GSI.

The discussion below assumes no endpoint in the SURL, and shows how the soap endpoints and wsdl can be found given an SURL

Issues:

- We wish to have a way of finding the SRM WSDL for multiple versions from the SURL.

- We wish to support clients that know what SRM version they want to use.  For example, a client that uses version 1.1, should be able to got the WSDL and/or the SOAP endpoint for it directly.

- We wish to have a default where an SRM version number is not mentioned.  The version returned in this case is whatever the SRM currently supports, or if multiple versions are supported, the SRM chooses what to return.

- We wish to allow a file accessed by a previous SRM version to be accessed by a future SRM version without having to change the SURL.  Furthermore, if the file can be accessed by either version simultaneously (that depend on the SRM implementation) that should be possible too.

- We wish to have a way for a client to find out which version the SRM supports and the endpoint without having to read the WSDL.  This is necessary in a changing world, where new version can be introduced.

- We wish to have a client that can use multiple SRM versions to find out which SRM version is supported by the SRM.  This is probably the most realistic scenario, since we cannot expect all SRMs to support the same version at any one time.

- We wish to have a client find out which SRM versions are supported for accessing a particular file, in case that files can be accessed by multiple SRM versions simultaneously.  This is related to point 3 above.

This is a long wish list, but the proposed solution is simple.  We assume that the WSDL will contain the version number.  First, we propose that every SRM WSDL starts with:

SRM version number--> (e.g. <!--SRM version 2.1.3-->)

Now, the solution is as follows:

Give an SURL: srm://host[:port]/path/file (e.g. srm://dm.lbl.gov:4001/ABC/file_x)

The following can be derived:

Case 1)

For clients that know what SRM versions they want to use:

https://host:port/srm/srm.version.wsdl

https://host:port/srm/srm.version.endpoint

For example, given the SURL above, and the client uses version 1.1, you derive:

https://dm.lbl.gov:4001/srm/srm.1.1.wsdl

https://dm.lbl.gov:4001/srm/srm.1.1.endpoint

Note: the endpoint returned can be any URI, e.g.: https://gizmo.lbl.gov:10001/srm/v1.0

or:  https://dm.lbl.gov:12345/servlet/srm.1.1)

Case 2)

For clients that don’t know the version, and want to use the default:

https://host:port/srm/srm.wsdl

https://host:port/srm/srm.endpoint

For the example above:

https://dm.lbl.gov:4001/srm/srm.wsdl

https://dm.lbl.gov:4001/srm/srm.endpoint

Case 3)

For clients that want to find out the SRM version and endpoint without getting the entire WSDL:

https://host:port/srm/srm.info

The srm.info file will contain:

<!--SRM version number-- --srmEndpoint-->

For example:

<!--SRM version 2.1.3-- -- https://gizmo.lbl.gov:10001/srm-->

Case 4)

For servers that support multiple srm version accessing the SAME file:

The same format as above repeating for each srm version.

For example:

<!--SRM version 1.1-- -- https://sdm.lbl.gov:5005/srm-->

<!--SRM version 2.1.3-- -- https://gizmo.lbl.gov:10001/srm-->

To summarize, the following is what should be supported for WSDL and endpoint discovery:

Given an SURL:

srm://host[:port]/site_file_name

The following can be derived:

a) https://host[:port]/srm/srm[.version].wsdl

b) https://host[:port]/srm/srm[.version].endpoint

c) https://host[:port]/srm/srm.info

Where the content have the format repeated as many time as there are supported versions:

<!--SRM version number-- --srmEndpoint-->

-------------------------------------------