# VEGETATIVE BARRIER

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service—Practice Code 601

### VEGETATIVE BARRIER

Vegetative barriers are permanent strips of stiff, dense vegetation along the general contour of slopes or across concentrated flow areas.

### PRACTICE INFORMATION

Vegetative barriers can be applied on all eroding areas including cropland, grazing land, forestland, farmsteads, mined land, and construction sites. The practice is used to reduce sheet and rill erosion, reduce ephemeral gully erosion, manage water flow, stabilize steep slopes, and trap sediment.

Vegetative barriers are most effective on slopes of less than 10 percent. Other site considerations include the need for suitable outlets below the barrier and the capacity to readily establish adapted perennial vegetation.

Vegetative barriers use tall, stiff, dense perennial vegetation in narrow buffers to slow runoff. As the flow hits the vegetative barrier and slows, sediment drops from the runoff, infiltration of runoff increases, and typically, the flow of runoff passing through the barrier is less concentrated.

### COMMON ASSOCIATED PRACTICES

Vegetative Barrier is commonly planned as part of a Conservation Management System with Conservation Crop Rotation (328), Residue Management practices, Contour Farming (330), and other conservation practices.

For further information, refer to the practice standard in the local Field Office Technical Guide and associated practice specifications and job sheets.

# Text boxes

Vegetative Barrier

7/2008

Note:  Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Mitigating practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

Start

LEGEND

I.10 (+) Soil quality

I.3 (+/-) Ground water quality

C.2 (+) Aquatic habitats

D.5 (-) Area for agricultural production

C.3 (+) Biodiversity

C.4 (+) Income and income stability (individuals and communities)

C.1 (+) Surface water quality

I.12 (+/-) Potential income

I.13 (+/-) Net return

I.9 (+) Improved productivity, health, and vigor

I.11 (+) Land productivity

I.8 (+) Wildlife food and cover

I.7 (-) Nutrient and organics in surface water runoff

Pest Management (595)

Nutrient Management (590)

I.2 (+) Potential for transport of dissolved pollutants to ground waters

I.1 (+) Infiltration of runoff water at the site

I.4 (-) Surface water runoff leaving the field

I.6 (-) Turbidity in surface water runoff

D.6 (+) Cost of installation and maintenance

D.3 (+) Permanent vegetative cover

D.4 (+) Stabilization of steep slopes

D.1 (-) Flow rate of surface runoff water

I.5 (-) Sheet and rill, ephemeral, and gully erosion

1.  Appropriate permanent vegetative cover established on the contour or across concentrated flow areas

D.2 (+) Sediments trapped within the vegetative barrier

Initial setting: All eroding areas including cropland, pastureland, rangeland, forestland, farmsteads, mined land, and construction sites requiring stabilization and water flow management

Vegetative Barrier (601)