| ––––––––••••••••–––––––– | UNITED STATES DEPARTMENT OF THE INTERIOR BUREAU OF LAND MANAGEMENT JOB HAZARD ANALYSIS | Date: | February 9, 2005 |  | X | New |  |  | Revised |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Page: | 1 | of | 14 |  | Reviewed by (AFMO): |
| Work Group: | Station Manager: | Qualifications, training, and/or experience required: |
| Firefighters |  | S-130, S-190, Work Capacity Test (Pack Test) |
| Personal Protective Equipment:: | Hard hat with chin strap, ear protection, goggles, nomex clothing, fire shelter, 8" leather boots with lug soles, and small first aid kit |
| BASIC JOB STEPS | POTENTIAL HAZARDS | SAFE JOB PROCEDURES |
| General Fire Suppression Applies to all suppression operations; not associated with any specific task |  |  |  |  |  |  | STANDARD FIRE ORDERS Fight fire aggressively but provide for safety first. Initiate all action based on current and expected fire behavior. Recognize current weather conditions and obtain forecasts. Ensure instructions are given and understood. Obtain current information on fire status. Remain in communication with crew members, your supervisor, and adjoining forces. Determine safety zones and escape routes. Establish lookouts in potentially hazardous situations. Retain control at all times. Stay alert, keep calm, think clearly, act decisively. |  |  |  |  |  |  |  |
|  |  | WATCH OUT SITUATIONS Fire not scouted and sized up. In country not seen in the daylight. Safety zones and escape routes not identified. Unfamiliar with weather and local factors influencing fire behavior. Uninformed on strategy, tactics, and hazards. Instructions and assignments not clear. No communication link with crew members/supervisors and adjoining forces. Constructing line without a safe anchor point. Building fireline downhill with fire below. Attempting frontal assault on fire. Unburned fuel between you and the fire. Cannot see main fire, and not in contact with anyone who can. On a hillside where rolling material can ignite fuel below. Weather getting hotter and drier. Wind increases and/or changes direction. Getting frequent spot fires across line. Terrain and fuels make escape to safety zones difficult. Taking a nap near the fireline. LCES Lookouts are posted and fire has been thoroughly scouted Communications with dispatch and firefighting personnel are adequate Escape Routes: escape routes are identified and understood by all firefighters Safety zones have been identified and understood by all firefighter |
|  | Entrapment | 1a. Observe STANDARD FIRE ORDERS, WATCH OUT SITUATIONS, AND LCES; train annually on these principles. 1b. Annual fire shelter deployment training. |
|  | 1-2 Snags, falling trees, debris rolling downhill | 2a. Post lookouts. 2b. Fall hazardous trees and snags or flag and direct traffic around hazardous trees. 2c. Alert crews continuously about rolling debris. |
|  | 1-3 Radiant heat, contact with burning debris | 3a. Use standard PPE. 3b. Work at a suitable distance from fire. 3c. No patches or decals are allowed on nomex, fireshirts, or tee-shirts. |
|  | 1-4 Poor visibility due to smoke or darkness | 4a. Refer to STANDARD FIRE ORDERS 4b. Scout terrain during daylight or acquire a good map & talk with someone familiar with the area. 4c. Consider fire spread potential and values and risk versus safety risks associated with suppression during darkness |
|  | 1-5 Inhalation (dust, smoke, carbon monoxide) | 5a. Use bandana or dust mask 5b. Avoidance to prolonged exposure; work upwind 5c. Training on CO and smoke hazards |
|  | 1-6 Fatigue | 6a. Limit shifts to 12 hours (when possible) 6b. Set a reasonable work pace 6c. Allow adequate rest breaks while on the fireline 6d. Provide showers and confortable eating areas 6e. Supply adequate nutrition and water 6f. Provide quite, shaded sleeping areas away from noise and dust. Sign & rope off sleeping areas 6g. Locate rest and recuperation sites away from running fire, falling trees & snags, rolling rocks, moving vehicles, heliports, helispots, etc. 6h. Alert personnel to local elements 6i. Standard First Aid Training 6j. Comply with established Work/Rest Guidelines (2:1 work/rest ratio, 1 day off in 14 days worked, 2 days off in 21 days worked) |
|  | 1-7 Snakes & Insects | 7a. Insects –use standard PPE –fasten pant cuffs to boot top –repellents –inspect body & clothing twice daily; pay special attention to crevices and creases Snakes –leave them alone –keep alert |
|  | 1-8 Poisonous Plants | 8a. Use standard PPE 8b. Change clothing that come in contact with poisonous plants 8c. Wash exposed skin 8d. Avoid smoke of burning poisonous plants 8e. Learn to identify poisonous plants |
|  | 1-9 Heat-related Illnesses – heat cramps – heat exhaustion – heat stroke | 9a. Reduce fatigue (#1-6) 9b. During period of continued extreme temperatures (90º +) crew members must be monitored closely for signs of “heat syndrome” – heat stroke, cramps, exhaustion 9c. Acclimatize crewmembers to hot weather activity gradually. Be especially careful the first 2 or 3 days 9d. Set a moderate work pace and gradually slow down as temperatures increase. Schedule the hardest work during the cooler morning & evening hours 9e. Keep plenty of water available & encourage crewmembers to drink it. Monitor canteens to ensure that crewmembers are getting their needed liquids. Thirst alone will not make a person drink enough water. Do not allow water for drinking to run out before you order more 9f. Crew members may want to eat less. High protein and other foods increase metabolic heat production and water loss 9g. Have table salt readily available during meals, but do not issue salt tablets 9h. Prevent sunburn 9i. Encourage crewmembers to keep their hardhats on in the sun. These hats provide a very effective air conditioning system 9j. Encourage crew members to bathe or wash thoroughly each day to keep their pores & hair clean. Dirty, clogged skin and matted hair slow down heat dissipation 9k. As the temperature increases, give crewmembers frequent rest period of at least 15 minutes. Encourage them to relax in cool locations if at all possible |
|  |  | 9l. No synthetic clothing should be worn (outer or under garments). T-shirts and other under garments should be 100% cotton |
|  | 1-10 Lightning & Thunderstorms | 10a. During a storm: Stay out of dry creek beds Put down all tools If you are in open country, sit or lie down Avoid grouping together Do not handle flammable materials in open containers Stay in your vehicle (unless it is metal-tracked). Take shelter in vehicles if possible When there is no shelter, avoid high objects such as lone trees. If only isolated trees are nearby, the best protection is to crouch in the open, keeping a distance of twice the height of the tree. Keep away from wire fences, telephone line, and electrically conductive elevated objects Avoid tops of ridges, hilltops, wide-open spaces, outcrops of rocks and sheds or shelters in exposed locations Get away from horses and stock Turn off generators & electrical equipment |
| Fire Vehicle Operation (general) | 2-1 Defective vehicle | 1a Conduct routine vehicle inspections 1b Ensure repairs are made on defective item |
|  | 2-2 Rollovers (high center of gravity) | 2a Avoid side hills |
|  | 2-3 Backing up (limited visibility) | 3a Use guide and/or get out and look 3b Avoid backing situations 3c Equip vehicles with back-up warning device |
| Fire Vehicle Operation (Fire Suppression) | 3-1 Fire related hazards | 1a. Operate engines in tandem 1b. Back in or turn around facing escape route 1c. Limit amount of hard line deployed (to allow for rapid movements of vehicle) 1d. Avoid frontal attack with engines 1e. Personnel will not ride outside cab of moving vehicle |
| Pump Operation (vehicle mounted) | 4-1 Burns | 1a. Use PPE 1b. Provide guards over muffler and exhaust pipe |
|  | 4-2 Slips and falls | 2a. Provide non-skid surface 2b. Clean up spills and fuels and retardants |
|  | 4-3 Noise | 3a. Use PPE |
|  | 4-4 Fueling | 4a. Move truck away from fire 4b. Turn engine off 4c. Allow engine to cool prior to fueling 4d. Use funnel or spout to avoid spills |
|  | 4-5 Hose reels | 5a. Use gloves 5b. Keep hands and loose clothing away from reel 5c. Avoid nozzle and couplings |
|  | 4-6 Retardant, wetting agents, and foam concentrates | 6a. Avoid contact with skin 6b. Use PPE 6c. Avoid spills 6d. Flush contacted skin with water |
| Pump Operation (portable pump) | 5-1 Slips and falls | 1a. Use extra caution working in wet areas |
|  | 5-2 Noise | 2a. Use PPE |
|  | 5-3 Broken hoses | 3a. Shut down and replace broken hoses asap |
|  | 5-4 Flying debris | 4a. Use PPE 4b. Avoid excessive nozzle pressure and keep nozzles a safe distance from the ground |
|  | 5-5 Lifting strains | 5a. Lift with two people 5b. Use proper lifting techniques |
|  | 5-6 Burns | 6a. Use PPE 6b. Use extra caution around muffler and exhaust pipe |
| Walking, Hiking, Climbing | 6-1 Night Travel | 1a. Use headlamp 1b. Keep 10-foot spacing between people 1c. Reduce rate of travel – slow down |
|  | 6-2 Carrying Equipment | 2a. Carry tool on downhill side 2b. Leave guards on tools 2c. Other equipment on pack frames 2d. Limit load to 40 or 50 pounds |
|  | 6-3 Walking, Working in burned-over area | 3a. Refer to GENERAL FIRE HAZARDS 3b. Watch for burned-out stump holes 3c. Flag or otherwise identify hazardous areas |
| Hand Tool Use – Shovel – Pulaski – Axe – McLeod – Combination Tool | 7-1 Blisters/slivers Foot and leg injuries Head injury Slips & falls | 1a. Check handles and tool heads for tightness and condition 1b. Use PPE 1c. Use tool guard when tool is not in use 1d. When not being used, place tool on ground in plain sight 1e. Take a comfortable stance with feet spread and well anchored 1f. Check for overhead hazards 1g. Maintain a 10-foot distance between personnel 1h. Identify tools needing repair 1i. Never throw tools 1j. Training (S-130) |
| Hand Tool Maintenance | 8-1 Cuts, Punctures | 1a. Use PPE 1b. File must have handle and guard 1c. Sharpen away from cutting edge |
| Chainsaws (Use & Maintenance) | 9-1 Cutting Hazards – Cuts (lacerations) – Eye and ear damage – Falling debris – Log kickbacks and barber chairs – Saw kickbacks | 1a. Use PPE 1b. Chaps and hearing protection 1c. Post lookout (swamper) 1d. Only trained personnel will operate chainsaws (S-212) 1e. Be alert for kickback when cutting material 2 inches in diameter 1f. Never cut limbs; stand to the side of the cut while bucking 1g. Always keep your weight well balanced on both feet when cutting. Prevent loss of balance by being ready to pull up on the saw as it cuts through the material 1h. Throttle up to full speed before letting the chain contact the wood 1i. Do not throttle down before the cut has been completed 1j. Never cut at partial throttle, as clutch will slip and burn 1k. Stop if saw become pinched or wedged 1l. As soon as cutting load is removed, release the throttle trigger 1m. Never cut above waist height or while over-reaching 1n. Move away from the saw if you lose control |
|  | 9-2 Refueling Hazards – Burns – Fire and explosion | 2a. Designate an area on mineral soil for storing fuel and oil 2b. Stop the saw when checking fuel or bar oil levels and when refueling 2c. Outdoors, refuel at least 50 feet from persons smoking or other potential sources of ignition 2d. Make sure saw is cool 2e. Fill tank on bare ground or other noncombustible surface 2f. Wipe spilled fuel off saw 2g. Never start the saw within 10 feet of the fueling area 2h. Avoid fuel spills on clothes |
|  | 9-3 Carrying Hazards – Cuts – Slips and falls | 3a. Stop saw before carrying 3b. Point bar forward when going downhill and the saw is at the side. Point the bar to the rear when going uphill and the saw is at the side 3c. Pack and guard bar and dogs when carrying saw on the shoulder |
|  | 9-4 Field Maintenance Hazards – Muffler burns – Cuts and abrasions | 4a. Use PPE 4b. Let saw cool 4c. Use handle and guard on files 4d. Use bar guard |
| Mop-up & Water Application | 10-1 Burns | 1a. Use PPE |
|  | 10-2 Sprains | 2a. Avoid stepping in holes or depressions 2b. Warn crew of such dangers |
|  | 10-3 Flying debris | 3a. Use PPE (especially, goggles) 3b. Avoid excessive nozzle pressure and keep nozzles a safe distance from the ground 3c. Use fog stream |
|  | 10-4 Carbon Monoxide concentrations of smoldering fuels | 4a. Limit work shifts in concentrations of smoldering fuels 4b. Take breaks and camp in areas which minimize exposure to Carbon Monoxide |
|  | 10-5 Snags | 5a. Flag hazardous trees 5b. Use lookouts 5c. Work in pairs |
|  | 10-6 Lackadaisical attitude | 6a. Be alert 6b. Keep the lookup, look down, look around attitude at all times |
| Dozer Operations | 11-1 Falling Debris | 1a. Do not work downhill of dozers 1b. Do not work within 100 feet of heavy equipment |
|  | 11-2 Being run over | 2a. Never approach moving heavy equipment 2b. Utilize a swamper – do not work heavy equipment alone 2c. Do not work within 100 feet of heavy equipment |
| Firing Operations | 12-1 Burns | 1a. Use PPE 1b. Avoid spills 1c. Change clothing that has had fuels spilled on it 1d. Proper training on firing operations (S-234) |
|  | 12-2 Explosions | 2a. Use proper fuel mixture 2b. Use safety cans for transporting fuel 2c. Proper grounding of larger containers |
|  | 12-3 Fumes/Inhalation | 3a. Mix fuels in adequately ventilated areas |
| Hazardous Materials |  |  |
| Retardant Use | 14-1 Impact from falling retardant and/or flying debris | 1a. Wear PPE 1b. Move out of drop area 1c. Stay clear of large old trees/snags and loose rocks/debris |
|  | 14-2 Slips & falls | 2a. Retardant is slick when wet . . . walk & drive slowly and carefully through these areas |
| Helicopter Bucket Drops | 15-1 Impact from water drops and/or flying debris | 1a. Wear PPE 1b. Move out of drop area 1c. Stay clear of large old trees/snags and loose rocks/debris |
| Fire Shelter Deployment | 16-1 Shelter in poor condition | 1a. Check shelter periodically for rips, tears and date |
|  | 16-2 Not knowing proper deployment procedures | 2a. Training |
|  | 16-3 Deployment in dense fuels | 3a. Clear area 3b. Deploy in light fuels 3c. Scout a safety zone |
|  | 16-4 Hesitation and timely deployment | 4a. Follow crew leader orders 4b. Drop all equipment and run to safety zone |
|  | 16-5 Lungs and airway threatened | 5a. Face down in dirt 5b. Hold shelter down with gloved hands and feet |
|  | 16-6 Bad positioning in shelter | 6a. Feet toward on-coming fire 6b. Hold shelter down with gloved hands and feet 6c. Get rid of line gear because of flammable material inside |
|  | 16-7 Exiting shelter prematurely | 7a. Communicate with crew 7b. Wait until supervisor lets you know it is safe to come out |
|  | 16-8 No gloves | 8a. Keep gloves on 8b. Have a spare pair readily available |
| Physical Fitness Training – Work Capacity Testing – Running – Weight Lifting – Sit-ups, Push-ups, Pull-ups |  |  |
| Urban Interface Fire Suppression | 18-1 Structural Watch-out Situations Wooden construction, shake roofs Poor access, narrow one-way roads Inadequate water supply Natural fuels 30 feet or closer to structures Extreme fire behavior Strong winds (25 mph plus) Evacuation of public = panic Structures located in chimneys, box or narrow canyons, on slopes 30% or more in continuous, flashy fuel types Bridge load limits | 1a Wear full PPE 1b. Keep at least 100 gallons of water reserve in engine tank for your protection. Never pass up an available water source when tank is less than full 1c. Have a dedicated protective line for your crew and engine 1d. Park engine in safe area, with front toward escape route. Do not block escape routes. Back into driveways, or narrow access roads 1e. Use 1½ inche lines when possible 1f. Post lookouts as needed 1g. Do not park in saddles or chimneys 1h. Do not enter a burning structure 1i. Observe and do not exceed bridge load limits 1j. Utilize law enforcement authorities to conduct evacuations and maintain traffic control 1k. Keep headlights and warning light on for increased visibility |
|  | 18-2 Power lines | 2a. Downed conductor on vehicle: do not leave vehicle until power company arrives 2b. Do not operate heavy equipment under power lines 2c. Do not use rights-of-way as a jump or cargo drop spot 2d. Do not drive with long antennas under power lines 2e. Do not fue vehicles under power lines 2f. Do not stand near power lines during retardant drops 2g. Do not park under power lines 2h. Do not apply straight stream to power line |