In Cooperation with the Edwards Aquifer Authority

Helicopter Electromagnetic and Magnetic Survey Data and Maps, Seco Creek Area, Medina and Uvalde Counties, Texas

By

Bruce D. Smith, David V. Smith, Patricia L. Hill, and Victor F. Labson

This report is preliminary and has not been reviewed for conformity with U.S. Geological Survey editorial standards or with North American Stratigraphic Code.

Any use of trade, product, or firm names is for descriptive purposes only and does not constitute endorsement by the U.S. Government.

Open-File Report 03-226

U.S. DEPARTMENT OF THE INTERIOR

U.S. GEOLOGICAL SURVEY

Table of Contents

Abstract..........................................................................................................................ii

Introduction....................................................................................................................1

Geologic Setting.............................................................................................................3

Hydrologic Setting..........................................................................................................6

Helicopter Geophysical Survey......................................................................................6

Apparent Resistivity Maps.................................................................................7

Digital Data.........................................................................................................9

Conclusions...................................................................................................................10

Appendix……………………………………………………………………………...12

Abstract

A helicopter electromagnetic and magnetic (HEM) survey was completed of a 209 square kilometer (81 square miles) area of the central Edwards aquifer. This open-file report is a release of the airborne geophysical data and a summary of the hydrologic application. The survey area was centered on the Valdina Farms sinkhole along the Seco Creek drainage in western Medina County, Texas. Flight lines were flown north south with three east west tie lines to aid in leveling the magnetic data. Additional lines were flown on each side of the Seco and Little Seco Creek drainages. A five kilometer (4 mile) extension of 15 lines was flown north of the main survey block centered on Seco Creek. This digital data release contains the flight line data, grids, and maps of the HEM survey data.

The Edwards aquifer in this area consists of three hydrologic zones: catchment, recharge, and confined. The Glen Rose Formation is exposed in the catchment area. The recharge zone is situated in the Balcones fault zone where the Devils River Group of the Edwards aquifer has been exposed by normal faults. The magnetic data is not discussed in depth here, but does have high amplitude closed anomalies caused by shallow igneous intrusives. The Woodard Cave Fault that separates the recharge and catchment zones is in places associated with a weak linear magnetic low.

The HEM data has been processed to produce apparent resistivities for each of the six EM coil pairs and frequencies. Maps of the apparent resistivity for the five horizontal coil pairs show that the catchment, recharge, and confined zones all have numerous linear features that are likely caused by structures, many of which have not been mapped. The distribution of high resistivity areas reflects the lithologic differences within the Trinity and Edwards aquifers.

Introduction

A successful high resolution airborne magnetic survey of the central Edwards and Trinity aquifers (Smith and Pratt, 2003; Smith and others, 2002) set the stage for additional applications of airborne geophysical surveys to hydrologic studies in the area. The U.S. Geological Survey (USGS), as part of a geological, geophysical, and hydrologic study of the Edwards aquifer, funded a helicopter electromagnetic and magnetic (HEM) survey to demonstrate the application to map subsurface features important in understanding and modeling the hydrology of the Edwards and associated aquifers. The Edwards Aquifer Authority funded additional flying to increase the survey area from 93 square kilometers (36 square miles) to 209 square kilometers (81 square miles).

Figure 1 Location of airborne geophysical surveys over the central Edwards Aquifer system.

The Seco Creek watershed was chosen for this detailed study (Figure 1) for a number of reasons:

1) the study area encompassed a typical stratigraphic section including the catchment, recharge, and confined areas,

2) the survey area covered a north-south section of the Balcones Fault Zone containing a variety of structural styles,

3) one of the most prominent recharge and diversion features, the Valdina               Farms Sinkhole, is located in the central part of the survey area, and

4) several USGS and Texas Bureau of Economic Geology (BEG) studies covered the area and are currently active.

The HEM survey used the RESOLVE© system flown by Fugro Airborne Surveys, which uses five horizontal coplanar coils and one vertical coaxial coil. The specific frequencies are given in Table 1. The system also includes in the bird (sensor housing) a total field magnetometer, differential kinematic GPS, and laser altimeter. The helicopter carries another differential GPS system, barometric and radar altimeters, and a video camera. Electromagnetic noise from power lines and natural sources (lightning) are also measured. The survey was flown with north-south flight lines and a nominal line spacing of 200 m with a sensor elevation of 30 m except as required for safety considerations and FAA regulations. The system was calibrated before and after the survey on the ground in the central part of the survey area away from power lines and other cultural noise. System calibration was also checked at the Fugro Airborne offices in Toronto when the system returned.   In addition four lines were flown along the Seco and Little Seco Creeks. These flight lines were flown to provide data directly along the drainages with consistent flight elevation and time (flight number).

Table 1 Frequencies and sensitivities for the HEM survey.

| COIL CONFIGURATION | FREQUENCY (Hz) | SENSITIVITY (ppm) |
| --- | --- | --- |
| Coplanar | 386 | 0.13 |
| Coplanar | 1514 | 0.12 |
| Coaxial | 3315 | 0.06 |
| Coplanar | 6122 | 0.24 |
| Coplanar | 25960 | 0.44 |
| Coplanar | 106400 | 0.44 |

Geologic Setting

Sedimentary rocks of the Seco Creek watershed are given in the stratigraphic section shown in Figure 2 and are described in detail by Maclay (1995) and Small and Clark (2000). The oldest, lower Cretaceous, rocks are the upper and lower members of the Glen Rose Limestone which is part of the Trinity Group. An evaporate unit is found at the base of the upper member. These units have a thickness greater than 150 m (500 ft). Mapping in the area by the Texas Bureau of Economic Geology (Murray and Collins, 2003) has not subdivided the Glen Rose Limestone. The Devils River is divided into upper and lower parts in this stratigraphic section (Figure 2) and are equivalent to the Segovia Formation (lower Devils River) and Fort Terrett Formation (upper Devils River) as described by Rose (1972). Small and Clark (2000) do not divide the Devils River in this area. The upper Devils River is more cavernous. The Georgetown formation at the top of the late Cretaceous section is rather impervious limestone and marl.

The upper Cretaceous consists of several formations (Figure 2) including (from oldest to youngest) the Del Rio Clay, Buda Limestone, Eagle Ford Group, Austin Group, Anachacho Limestone, and Escondido Formation. The Del Rio Clay is approximately 15 m (50 ft) thick. The Austin Group is massive chalk to marly flaggy limestone. The Eagle Ford is about 22 m (70 ft) and contains black shales. All of these units have a higher electrical conductivity than the more massive limestones of the Edwards and Trinity Groups. This high conductivity of the Del Rio Clay is used in electrical logs as a stratigraphic marker.

The Tertiary formations consist of the Midway and Wilcox Groups which together range in thickness from 200 to 500 feet thick. These units consist of shales, sandstones, siltstones, and some limestone. The Uvalde and Leona gravels overlay these units and are less than 100 feet thick.

The Balcones fault zone is the major structural feature of the study area. Uplift of the Edwards Plateau in the Miocene and subsidence of the Gulf of Mexico created a zone of normal faults. This zone is defined by a number of northeast trending faults (Figure 3) and is the southern end of the Edwards plateau. Some cross faults trend northwest to southeast. Most of the faults are normal with the downthrown side to the southeast toward the Gulf of Mexico. The Woodard Cave fault is the contact between the Trinity and Edwards Groups (Figure 3) in the Seco Creek area. It has a maximum displacement of about 600 feet. Many of the faults are more like fracture or shatter zones rather than sharp breaks. Some faults have gouge and small boulders.

Figure 2 Stratigraphic section for the Seco Creek area (Murray and Collins, 2003).

Figure 3. Geologic map (Murray and Collins, 2003) of the four 7.5 minute quadrangles in the upper Seco Creek Watershed. Lithologic units are given in Figure 2. North-South lines are the flight path for the HEM survey. Black lines are faults (dashed where inferred). Seco Creek occupies the yellow Quaternary areas in the central part of the survey area.

Hydrologic Setting

The Trinty Group in the northwest part of the survey area is termed the catchment zone since drainages cross this zone with presumed little recharge to the Edwards Aquifer. The Trinity Group is much less permeable than the Edwards Group but is locally cavernous. For example during normal flow, Seco Creek flow disappears in sink holes just north of the fault contact with the Edwards. There have been no studies of possible interconnection of recharge paths between the Trinity and Edwards in this area. However the relatively lower permeability due to shales and marls of the Trinity makes it a lower confining unit for the Edwards.

The Edwards Group exposed by the normal Balcones fault zone in the central part of the survey area (Figure 3) is termed the recharge zone. This part of the aquifer has a very high porosity and permeability typical of a karstic terrain developed since the Miocene uplift. Lithology, stratigraphy, diagensis, and selective dissolution (karstification) account for the effective porosity and permeability of the aquifer. Cave development is controlled by both lithology and structure.

In addition to the Trinity and Edwards aquifers, the Leona and Uvalde gravels constitute the other aquifers in the area. These aquifers have not been studied in the same detail as the Trinity and Edwards.

Faults in the area may act to increase the permeability by causing the development of fractures. Development of fault gouge may increase the clay content of the fault zones and effectively reduce the permeability. Clay zones could actually be aquitards impeding local groundwater flow.

Helicopter Geophysical Survey

Both electromagnetic and magnetic field measurements were made over the survey area. Smith and Pratt (2003) briefly discuss magnetic data for the survey area in the context of the larger high resolution aeromagnetic survey of the central Edwards Aquifer. The main conclusion at this stage of processing of the magnetic data is that a linear slight magnetic low can be correlated with parts of the main Woodard Cave fault. Additional processing of the magnetic data and ground follow up surveys are needed before any interpretation of this magnetic feature can be made. There appears to be no magnetic anomalies associated with the numerous other structures. A Cretaceous age intrusive is marked by a magnetic high in the northwest part of the survey (Figure 8 in Smith and Pratt, 2003). There are no indications of igneous dikes in this relatively high resolution magnetic survey. Data processing at this point has concentrated on the electromagnetic field measurements and is described below.

Apparent Resistivity Maps

Apparent resistivity is the resistivity of a homogeneous isotropic volume that would give the same electromagnetic signal as measured by the HEM system. Fugro Airborne as part of the contracted data processing has computed the apparent resistivity for each frequency. The computation is based on the pseudo-layer model (Fraser, 1978). Yin and Hodges (2003) discuss this method of apparent resistivity calculation and utilize it in an analysis of electrical anisotropy for this survey. Figure 4 shows apparent resistivity maps for the five horizontal coplanar coil frequencies (Table 1). The color scale has the same stretch between the highest and lowest measured apparent resistivity for each map. The highest apparent resistivity decreases an order of magnitude as frequency decreases 1.5 orders of magnitude (see figure caption), from 1300 to 150 ohm meters. The color scales have been used to emphasize comparative high and low resistivity areas within each map (at each frequency) rather than between maps. Note also that a resistivity color scale is used so that high resistivity (low conductivities) areas are in the warmer colors (reds) and areas of low resistivities (high conductivities) in the cooler colors (blues).

In general each map in Figure 4 shows progressively (from 4a to 4e) deeper sections of the earth. Smith and others (2003) discuss specific variations based on preliminary resistivity depth sections. Each part of the Edwards aquifer system is characterized by contrasting apparent resistivities. The lowest apparent resistivities are associated with the confining units in the southwest quadrant of the survey. The thick Del Rio Clay is source of the low resistivities. The electrically resistive Buda Limestone, stratigraphically above the clay, is found in higher elevations. Gravels along the drainages are also more resistive than many of the older confining layers.

The central northwest trending highest resistivities are from the exposed parts of the Devils River. The high resistivities at 100 and 25 kHz (Figure 4a and 4b) suggest a difference within the Devils River that correlates with the upper and lower divisions shown in Figure 4. The geophysical maps show more detail and precise locations than the geologic map. Lower apparent resistivities in the area of the lower Devils River at 400 Hz (northern part of the catchment zone) suggest that the more conductive upper Glen Rose influences these apparent resistivities.

Figure 4. Apparent resistivity maps for each horizontal coplanar coil pair. High resistivities (warm colors) for each frequency are (rounded up): a. 1300, b. 800, c. 500, d. 300, e. 150 ohm meters. The distance scale is 4 km or 2.5 miles (see also Plate 1).

Moderate resistivities in the northwest part of the survey area can be attributed to the Glen Rose Formation. The upper Glen Rose just north of the Woodard Cave fault maybe somewhat more conductive than the lower unit further to the north. The upper and lower Glen Rose appear to be in fault contact. There is an interesting but unexplained area of high resistivity in the upper Glen Rose along the northern part of Seco Creek (the northern extension of the central part of the survey area). The higher resistivity could be due to a more resistive limestone lithology at depth.

Linear apparent resistivity features correlate with known structures and suggest structures that have not been mapped. The narrow low resistivity trough in the southeast corner of the survey area (Figure 4) generally corresponds to a mapped graben (Figure 3) in the same area but can be much better defined from the geophysical maps since the graben structure is not exposed. The northeast trending structure that causes this graben, correlates with linear features in the confined zone to the west suggesting it extends further to the west than mapped. Other narrow zones in the confining units are suggestive of other similar structures that are covered. High resistivity linear features in the Edwards recharge area suggest structures along which there may be increased permeability due to fracturing or karstification.

Digital Data

Flight line data is given in an ASCII database in the directory linedata. The position is given in lattitude and longitude as well as UTM coordinates. The raw GPS positioning data for the survey is in NAD83 (zone 14N) but has been reprocessed to NAD27 (zone 14N) in the database. The header for each channel is given in the txt file in the directory. Each channel is described in the contractors report given in the appendix and the reports directory.

Grids of the magnetic field data and the apparent resistivities for the horizontal coplanar coil pairs are given in the grids directory. The apparent resistivities have been corrected for system drift and calibrations as described in the contractor’s report (appendix and reports directory). The grid cell size is 50 m. This is large in comparison to the measurement spacing along flight lines (about 3 m) because the spacing between flight lines is larger than the measurement interval. The grids are in grid exchange format (Grids\gxf_grid_documentation.pdf), a “standard” of the geophysical industry used in many map display programs.

The directory MapImages contains geotiff (UTM projected tif files) of the grids. Each file has an associated world file (tfw). In addition this directory contains AutoCad format files (extension dxf) of the flight lines. These files are georeferenced to the NAD27 projection. Plate 1 (pocket) shows plots of the map images.

Conclusions

The HEM survey of the Seco Creek area has mapped both the magnetic and electrical characteristics of geologic and hydrologic features from the near surface to depths on the order of 100 m. The magnetic survey data has not been discussed in detail here but does show some anomalies possibly associated with structures and a few high amplitude anomalies related to igneous intrusives. The HEM data has been processed to produce apparent resistivity maps. These maps show that the catchment, recharge, and confined zones all have numerous linear features that reflect exposed and covered structures. These structures are important in understanding and modeling the hydrology of each zone. There are areas of relatively high resistivity in the catchment and recharge zones that reflect lithologic differences perhaps related to stratigraphic changes.

References

Elliott, W.R. and Veni, G., 1994, The Caves and Karsts of Texas: National Speleological Society Convention Guidebook, 342 p.

Haung, H. and Fraser, D.C., 1996, The differential parameter method for multifrequency airborne resistivity mapping: Geophysics, vol. 61, p. 100-109.

Fraser, D.C., 1978, Resistivity Mapping with an Airborne Multicoil Electromagnetic System: Geophysics, vol. 43, p. 144-172.

Maclay, R.W., 1995, Geology and Hydrology of the Edwards Aquifer in the San Antonio Area, Texas: U.S. Geological Survey Water Resources Investigations Report 95-4186, 64p.

Murray, K.E. and Collins, E.W., 2003, GIS Compilation of Geologic Map Data for the Seco Creek Area, Medina County, Texas: U.S. Geological Survey, Open File Report, in preparation.

Small, T.A. and Clark, A.K., 2000, Geologic Framework and Hydrogeologic Characteristics of the Edwards Aquifer Outcrop, Medina County Texas: U.S. Geological Survey Water Resources Investigations Report 00-4195.

Smith, B.D., Irvine, R., Blome, C., Clark, A.K., and Smith, D.V., 2003, Preliminary Results, Helicopter Electromagnetic and Magnetic Survey of the Seco Creek Area, Medina and Uvalde Counties, Texas: Proceedings from the Symposium on the Application of Geophysics to Engineering and Environmental Problems, Environmental and Engineering Society, 15p.

Smith, D.V. and Pratt, D., 2003, Advanced Processing and Interpretation of the High Resolution Aeromagnetic Survey Data over the Central Edwards Aquifer, Texas: Proceedings from the Symposium on the Application of Geophysics to Engineering and Environmental Problems, Environmental and Engineering Society, 11p.

Smith, D.V., Smith, B.D., and Hill, P.L., 2002, Aeromagnetic Survey of Medina and Uvalde Counties, Texas: A Web Site for Distribution of Data, OFR-02-0049.

U. S. Geological Survey, 1999, Geologic Framework and Hydrologic Properties of the Seco Creek Watershed, Texas, Fact Sheet FS-104-98, 4 p.

Yin, C. and Hodges, G., Identification of Electrical Anisotropy from Helicopter EM Data, Proceedings from the Symposium on the Application of Geophysical methods Engineering and Environmental Problems, Environmental and Engineering Society, 12p.

Report # 6025

Logistics Report

Helicopter-borne

RESOLVE Electromagnetic and Magnetic

Geophysical Survey

Seco Creek, Texas

Prepared by:

Fugro Airborne Surveys

2270 Argentia Road

Mississauga (Toronto), Ontario, Canada  L5N 6A6

For:

the United States Geological Survey

October  2002

By: Michael J. Cain, P.Eng.

Fugro Airborne Surveys	Toronto, Canada

SUMMARY

This report describes the logistics and results of a RESOLVE EM and magnetic airborne geophysical survey carried out for the United States Geological Survey over the Seco Creek area, Texas.  Total coverage of the survey blocks amounted to 953 miles (1534 kilometres) over 2 survey blocks and several lines following the creeks through the survey area.  The survey was flown from May 21 to 27, 2002.

The purpose of the survey was to map the conductive and magnetic properties of Seco Creek and the surrounding area.  This was accomplished by using a RESOLVE multi-coil, multi-frequency electromagnetic system supplemented by a high sensitivity cesium magnetometer.  A GPS electronic navigation system ensured accurate positioning of the geophysical data.

The RESOLVE system comprises of five coplanar coil pairs and one coaxial coil pair with a frequency spread of 386 Hz to 106 400 Hz. This system provided optimum definition of the conductive properties of the Earth’s layering in the top 100 m.

TABLE OF CONTENTS

1.0	INTRODUCTION	1.1

2.0	SURVEY EQUIPMENT AND PROCEDURES	2.1

2.1	Electromagnetic System	2.1

2.2 	Magnetometer	2.4

2.3	Magnetic Base Station	2.4

2.4	Radar Altimeter	2.5

2.5	Analog Recorder	2.5

2.6	Digital Data Acquisition System	2.6

2.7	Video Flight Path Recording System	2.7

2.8	Navigation (Global Positioning System)	2.7

2.9	Field Workstation and Data Verification	2.9

3.0	PRODUCTS AND PROCESSING TECHNIQUES	3.1

3.1	Base Maps (optional)	3.1

3.2	Apparent Resistivity	3.2

3.3	EM Magnetite (optional)	3.3

3.4	Total Magnetic Field	3.4

3.5	Calculated Vertical Magnetic Gradient (optional)	3.4

3.6	Magnetic Derivatives (optional)	3.4

3.7	Multi-channel Stacked Profiles (optional)	3.5

3.8	Contour, Colour and Shadow Map Displays (optional)	3.6

3.9	Resistivity-depth Sections (optional)	3.6

4.0	CONCLUSIONS AND RECOMMENDATIONS	4.1

APPENDIX A  	LIST OF PERSONNEL

APPENDIX B	ARCHIVE DESCRIPTION

APPENDIX C	PROCESSING LOG

APPENDIX D	BACKGROUND INFORMATION

D.1	Resistivity Mapping

D.2	Reduction of Geologic Noise

D.3	Magnetics

APPENDIX E	FLIGHT LOGS

APPENDIX F	TESTS AND CALIBRATIONS

FIGURES

Figure 1.1	Seco Creek area, Texas.	1.3

TABLES

Table 1.1	Breakdown for the Seco Creek Survey	1.1

Table 2.1	The Analog Profiles, RESOLVE System	2.6

Table 3.1	Survey Products	3.2

# 1.0	INTRODUCTION

A RESOLVE electromagnetic and magnetic survey was flown for the United States Geological Survey over the Seco Creek area, Texas.  Details of the survey areas are shown in Table 1.1

| Block/Line | Line Spacing | Line Direction | Total distance |
| --- | --- | --- | --- |
| Block 1 | 200 metres 655 feet | 0( | 1370 km 851 miles |
| Block 2 (north extension) | 200 metres 655 feet | 0( | 54 km 33.6 miles |
| River lines | 200- 250 metres 655-820 feet | variable | 110 km 68.4 miles |
|  |  | TOTAL | 1534 km 953 miles |

Table 1.1	Breakdown for the Seco Creek Survey

Total coverage of the survey blocks amounted to 953 miles over 2 survey blocks and 2 river sections.  The survey was flown from May 21 to 27, 2002.  The blocks were flown in an azimuthal direction of 0°.  Three tie lines were flown over block 1 perpendicular to the flight lines.  Figure 1.1 displays the layout and location of the survey blocks.

Ancillary equipment consisted of a radar altimeter, a video camera, analog and digital recorders, and an electronic navigation system.  The instrumentation was installed in an Ecureuil AS350-B2 turbine helicopter (registration CF-ZTA) which was provided by Questral Helicopters Ltd.  The helicopter flew at an average airspeed of 70 mph (113 km/h) with an average EM sensor height of approximately 110 feet (33.5 metres).

Section 2 provides details on the survey equipment, the data channels, their respective sensitivities, and the navigation/flight path recovery procedure.

Figure 1.1	Seco Creek area, Texas.

# 2.0	SURVEY EQUIPMENT AND PROCEDURES

This section provides a brief description of the geophysical instruments, quality control and calibration procedures used to acquire the survey data.

##### 2.1	Electromagnetic System

Model:	RESOLVE

Type:		Towed bird, symmetric dipole configuration operated at a nominal survey altitude of 98 feet (30 metres).  Coil separation is 7.9 metres for 400 Hz, 1500 Hz, 6200 Hz, 25,000 Hz and 100,000 Hz and 9.0 metres for the 3300 Hz coil-pair.

Coil orientations/frequencies:	orientation	nominal		actual

coplanar		400 Hz	386 Hz

coplanar		1 500 Hz	1 514 Hz

coaxial		3 300 Hz	3 315 Hz

coplanar		6 200 Hz	6 122 Hz

coplanar		25 000 Hz	25 960 Hz

coplanar		100 000 Hz	106 400 Hz

Channels recorded:	6 in-phase channels

6 quadrature channels

2 monitor channels

Sensitivity:		0.13 ppm at 400 Hz CP

0.12 ppm at 1 500 Hz CP

0.06 ppm at 3 300 Hz CX

0.24 ppm at 6 200 Hz CP

0.44 ppm at 25 000 Hz CP

0.44 ppm at 100 000 Hz CP

Sample rate:		10 per second, equivalent to 1 sample every 3.5 m, at a survey speed of 125 km/h.

The electromagnetic system utilizes a multi-coil coaxial/coplanar technique to energize conductors in different directions.  The coaxial coil is vertical with its axis in the flight direction.  The coplanar coils are horizontal.  The secondary fields are sensed simultaneously by means of receiver coils which are maximally coupled to their respective transmitter coils.  The system yields an in-phase and a quadrature channel from each transmitter-receiver coil-pair.

Calibration of the system during the survey uses the Fugro AutoCal automatic, internal calibration process.  At the beginning and end of each flight, and at intervals during the flight, the system is flown up to high altitude to remove it from any “ground effect” (response from the earth). Any remaining signal from the receiver coils (base level) is measured as the zero level, and removed from the data collected until the time of the next calibration.  Following the zero level setting, internal calibration coils, for which the response phase and amplitude have been determined at the factory, are automatically triggered – one for each frequency.  The on-time of the coils is sufficient to determine an accurate response through any ambient noise.  The receiver response to each calibration coil “event” is compared to the expected response (from the factory calibration) for both phase angle and amplitude, and the applied phase and gain corrections adjusted to bring the data to the correct value.

In addition, the output of the transmitter coils are continuously monitored during the survey, and the applied gains adjusted to correct for any change in transmitter output (due to heating, etc.)

Because the internal calibration coils are calibrated at the factory (on a resistive halfspace) ground calibrations using external calibration coils on-site are not necessary for system calibration.  A check calibration may be carried out on-site to ensure all systems are working correctly.  All system calibrations will be carried out in the air, at sufficient altitude that there will be no measurable response from the ground.

The internal calibration coils are rigidly positioned and mounted in the system relative to the transmitter and receiver coils.  In addition, when the internal calibration coils are calibrated at the factory, a rigid jig is employed to ensure accurate response from the external coils.

Using real time Fast Fourier Transforms and the calibration procedures outlined above, the data will be processed in real time from measured total field at a high sampling rate to in-phase and quadrature values at 10 samples per second.

##### 2.2 	Magnetometer

Model:	Fugro AM102 processor with Geometrics G822 sensor

Type:		Optically pumped cesium vapour

Sensitivity:	0.01 nT

Sample rate:	10 per second

The magnetometer sensor is housed in the EM bird, 29 m below the helicopter.

##### 2.3	Magnetic Base Station

Model:	Fugro CF1

Type:		Digital recording proton precession

Sensitivity:	0.10 nT

Sample rate:	1 second intervals

The base station was located in a magnetically quiet area away from cultural interference.  The clock on the base station was synchronized with the airborne magnetometer to UTC time, permitting subsequent removal of the diurnal variation. The magnetic base station was located at approximately WGS84 latitude 29(21.87’N and longitude 99( 9.92’W.

##### 2.4	Radar Altimeter

Manufacturer:	Honeywell/Sperry

Model:	AA 330

Type:		Short pulse modulation, 4.3 GHz

Sensitivity:	0.3 m

The radar altimeter measures the vertical distance between the helicopter and the ground. This information is used in the processing algorithm that determines conductor depth.

##### 2.5	Analog Recorder

Manufacturer:	RMS Instruments

Type:		DGR33 dot-matrix graphics recorder

Resolution:	4x4 dots/mm

Speed:		1.5 mm/sec

The analog profiles are recorded on chart paper in the aircraft during the survey.  Table 2-1 lists the geophysical data channels and the vertical scale of each profile.

| Channel Name | Parameter | Scale units/mm |
| --- | --- | --- |
| 400I | coaxial in-phase (400 Hz) | 5 ppm |
| 400Q | coaxial quad (400 Hz) | 5 ppm |
| 1K5I | coplanar in-phase (1500 Hz) | 5 ppm |
| 1K5Q | coplanar quad (1500 Hz) | 5 ppm |
| 6K2I | coplanar in-phase (6200 Hz) | 10 ppm |
| 6K2Q | coplanar quad (6200 Hz) | 10 ppm |
| 1X8I | coaxial in-phase (3300 Hz) | 10 ppm |
| 1X8Q | coaxial quad (3300 Hz) | 10 ppm |
| 25KI | coplanar in-phase (25000 Hz) | 20 ppm |
| 25KQ | coplanar quad (25000 Hz) | 20 ppm |
| 100I | coplanar in-phase (100000 Hz) | 20 ppm |
| 100Q | coplanar quad (100000 Hz) | 20 ppm |
| ALTL | altimeter (laser) | 3 m |
| ALTR | altimeter (radar) | 3 m |
| MAGC | magnetics, coarse | 20 nT |
| MAGF | magnetics, fine | 2.0 nT |
| 2SP | coplanar spherics monitor |  |
| 2PL | coplanar power line monitor |  |
| 1KPA | altimeter (barometric) | 30 m |
| 2TDC | internal (console) temperature | 1º C |
| 3TDC | external temperature | 1º C |

Table 2.1	The Analog Profiles, RESOLVE System

##### 2.6	Digital Data Acquisition System

Manufacturer:	RMS Instruments

Model:			DGR 33

Recorder:		SanDisk 48-64 Mb flash cards

The data are stored on PCMCIA flash cards and are transferred to the field workstation PC at the survey base for verification, backup and preparation of in-field products.

##### 2.7	Video Flight Path Recording System

Type:	VHS Colour Video Camera (NTSC)

Model:	AG 2400/WVCD132

Fiducial numbers are recorded continuously and are displayed on the margin of each image. This procedure ensures accurate correlation of analog and digital data with respect to visible features on the ground.

##### 2.8	Navigation (Global Positioning System)

Airborne Receiver for Navigation

Model:		Ashtech Glonass GG24

Type:		SPS (L1 band), 24-channel, C/A code at 1575.42 MHz,

S code at 0.5625 MHz, Real-time differential.

Sensitivity: 	-132 dBm, 0.5 second update

Accuracy:  	Manufacturer’s stated accuracy is better than 10 metres

real-time

Airborne Receiver for Processing

Model:			Ashtech Z-Surveyor

Type:	Code and carrier tracking of L1 band, 12-channel,

dual-frequency C/A code at 1575.42 MHz, and L2 P-code

at 1227 MHz

Sensitivity:	0.5 second update

Accuracy:	Manufacturer’s stated accuracy for differential corrected

GPS is better than 1 metre

Base Station

Model:			Ashtech Z-Surveyor

Type:	Code and carrier tracking of L1 band, 12-channel,

dual-frequency C/A code at 1575.42 MHz, and L2 P-code

at 1227 MHz

Sensitivity:	0.5 second update

Accuracy:	Manufacturer’s stated accuracy for differential corrected

GPS is better than 1 metre

The Ashtech GG24 is a line of sight, satellite navigation system which utilizes time-coded signals from at least four of forty-eight available satellites.  Both Russian GLONASS and American NAVSTAR satellite constellations are used to calculate the position and to provide real time guidance to the helicopter.  The Ashtech system can be combined with a RACAL or similar GPS receiver which further improves the accuracy of the flying and subsequent flight path recovery to better than 5 metres.  The differential corrections, which are obtained from a network of virtual reference stations, are transmitted to the helicopter via a spot-beam satellite.  For flight path processing an Ashtech Z-surveyor was used as the mobile receiver and base station receiver.  The mobile and base station raw XYZ data are recorded, thereby permitting post-survey processing for theoretical accuracies of better than 5 metres.  The final navigation channels were produced from the Ashtech Z-Surveyor GPS unit which was located on the EM sensor.

The GPS base station was run for a period of at least 24 hours to obtained a master position for post processing.  For the Seco Creek survey the GPS station was located at latitude 29º 21' 53.5493”N, longitude 99º 09' 55.2231”W at an elevation of 277.5 metres a.m.s.l.  The GPS records data relative to the WGS84 ellipsoid, which is the basis of the revised North American Datum (NAD83).

##### 2.9	Field Workstation and Data Verification

A laptop computer is used at the survey base to verify data quality and completeness.  Flight data are transferred to the PC hard drive to permit the creation of a Geosoft database.  This process allows the geophysicist to display both the positional and geophysical data on a screen or printer.

# 3.0	PRODUCTS AND PROCESSING TECHNIQUES

##### 3.1	Base Maps

Base maps of the survey areas are produced from published topographic maps.  These provide a relatively accurate, distortion-free base which facilitates correlation of the navigation data to the UTM grid.  The original topographic maps are scanned to a digital format and combined with geophysical data for plotting the final maps.  All maps are created using the following parameters:

Projection Description:

Datum:	NAD27

Ellipsoid:	Clarke 1866

Projection:	UTM (Zone: 14)

Central Meridian:	99º West

False Northing:	0

False Easting:	500000

Scale Factor:	0.9996

WGS84 to Local Conversion:	Molodensky

X,Y,Z Datum Shifts:	8  -159  -175

Table 3.1	Survey Products

Digital Geosoft GDB archive format on CD-ROM (2 copies)

Digital grid archives in Geosoft GRD format on CD-ROM (2 copies)

Survey report (2 copies)

Analog chart records

Flight path videocassettes (VHS format)

Note:	Other products can be produced from existing survey data, if requested.

##### 3.2	Apparent Resistivity

The apparent resistivity in ohm-metres (ohm-m) can be generated from the in-phase and quadrature EM components for any of the frequencies, using a pseudo-layer half-space model.  Resistivity maps portray all the EM information for that frequency over the entire survey area.  This contrasts with discrete electromagnetic anomaly maps which provide information only over interpreted conductors.  The large dynamic range makes the resistivity parameter an excellent mapping tool.

The preliminary resistivity maps and images are carefully inspected to locate any lines or line segments which might require levelling adjustments.  Subtle changes between in-flight calibrations of the system can result in line to line differences, particularly in resistive (low signal amplitude) areas.  If required, manual levelling is carried out to eliminate or minimize resistivity differences which can be caused by changes in operating temperatures. These levelling adjustments are usually very subtle, and do not result in the degradation of anomalies from valid bedrock sources.

After the manual levelling process is complete, revised resistivity grids are created.  The resulting grids can be subjected to a microlevelling filter in order to smooth the data for contouring.  The coplanar resistivity parameter has a broad 'footprint' which requires very little filtering.

The apparent resistivities have been calculated for all five coplanar frequencies and the coaxial frequency using the pseudo-layer half-space model.  Digital data are contained on the CD-ROM archives.  Values are in ohm-m on all final products.

##### 3.3	EM Magnetite (optional)

The apparent percent magnetite by weight is computed wherever magnetite produces a negative in-phase EM response.  This calculation is more meaningful in resistive areas, and is not recommended for these survey areas due to the moderately conductive, non-magnetic background and sources of cultural interference.

##### 3.4	Total Magnetic Field

The aeromagnetic data are corrected for diurnal variation using the magnetic base station data.  Manual adjustments are applied to any lines that require levelling, as indicated by shadowed images of the gridded magnetic data or tie line/traverse line intercepts.  The IGRF gradient is removed from the corrected total field data.

##### 3.5	Calculated Vertical Magnetic Gradient (optional)

The diurnally corrected total magnetic field data are subjected to a processing algorithm which enhances the response of magnetic bodies in the upper 500 m and attenuates the response of deeper bodies.  The resulting vertical gradient map provides better definition and resolution of near-surface magnetic units.  It also identifies weak magnetic features which may not be evident on the total field map.  However, regional magnetic variations and changes in lithology may be better defined on the total magnetic field map.

##### 3.6	Magnetic Derivatives (optional)

The total magnetic field data can be subjected to a variety of filtering techniques to yield maps of the following:

- enhanced magnetics

- second vertical derivative

- reduction to the pole/equator

- magnetic susceptibility with reduction to the pole

- upward/downward continuations

- analytic signal

All of these filtering techniques improve the recognition of near-surface magnetic bodies, with the exception of upward continuation.  Any of these parameters can be produced on request.

##### 3.7	Multi-channel Stacked Profiles (optional)

Distance-based profiles of the digitally recorded geophysical data can be generated and plotted by computer.  These profiles also contain the calculated parameters that are used in the interpretation process.

##### 3.8	Contour, Colour and Shadow Map Displays

The geophysical data were interpolated onto a regular grid using a modified Akima spline technique.  The resulting grid is suitable for generating contour maps of excellent quality.  The grid cell size used was 50 metres or 1/4 of the line interval.

Colour maps are produced by interpolating the grid down to the pixel size.  The parameter is then incremented with respect to specific amplitude ranges to provide colour "contour" maps.

##### 3.9	Resistivity-depth Sections (optional)

The apparent resistivities for all frequencies can be displayed simultaneously as coloured resistivity-depth sections.  The sections can be plotted using the topographic elevation profile as the surface.  The digital terrain values, in metres a.m.s.l., are calculated from the GPS Z-value minus the aircraft radar altimeter.

Resistivity-depth sections can be generated in three formats:

- Sengpiel resistivity sections, where the apparent resistivity for each frequency is plotted at the depth of the centroid of the in-phase current flow; and,

(2)	Differential resistivity sections, where the differential resistivity is plotted at the differential depth.

(3)	Occam or Multi-layer inversion.

Both the Sengpiel and differential methods are derived from the pseudo-layer half-space model.  Both yield a coloured resistivity-depth section which attempts to portray a smoothed approximation of the true resistivity distribution with depth.  Resistivity-depth sections are most useful in conductive layered situations, but may be unreliable in areas of moderate to high resistivity where signal amplitudes are weak.  In areas where in-phase responses have been suppressed by the effects of magnetite, the computed resistivities shown on the sections may be unreliable.  The differential resistivity technique was developed by Dighem.  It is more sensitive than the Sengpiel section to changes in the earth's resistivity and it reaches deeper.

Both the Occam and Multi-layer Inversions compute the layered earth resistivity model which would best match the measured EM data.  The Occam inversion uses a series of thin, fixed layers (usually 20 x 5m and 10 x 10m layers) and computes resistivities to fit the EM data.  The multi-layer inversion computes the resistivity and thickness for each of a defined number of layers (typically 3-5 layers) to best fit the data.

# 4.0	CONCLUSIONS AND RECOMMENDATIONS

This report provides a description of the equipment, procedures and logistics of the survey.  The digital data included with this report display the magnetic and conductive properties of the survey area.

It is recommended that image processing of existing geophysical data be considered, in order to extract the maximum amount of information from the survey results.  Current software and imaging techniques often provide valuable information on structure and lithology, which may not be clearly evident on the contour and colour maps. These techniques can yield images which define subtle, but significant, structural details.

A complete assessment and evaluation of the survey data should be carried out by one or more qualified professionals who have access to, and can provide a meaningful compilation of, all available geophysical, geological and geochemical data.

Respectfully submitted,

FUGRO AIRBORNE SURVEYS

Michael J. Cain, P.Eng.

Geophysicist

# APPENDIX A

### LIST OF PERSONNEL

The following personnel were involved in the acquisition, processing, interpretation and presentation of data, of the RESOLVE airborne geophysical survey carried out for the United States Geological Survey over the Seco Creek area, Texas.

David Miles	Manager, Helicopter Operations

Emily Farquhar	Manager, Data Processing

Brett Robinson	Field Geophysicist

Will Marr	Geophysical Operator

Luke Kukovica	Pilot

Michael Cain	Project Geophysicist

Russell Imrie	Geophysical Data Processor

Lyn Vanderstarren 	Drafting Supervisor

Albina Tonello	Secretary/Expeditor

All personnel are employees of Fugro Airborne Surveys, except for the pilot who is an employee of Questral Helicopters.

# APPENDIX B

### ARCHIVE DESCRIPTION

This CD-ROM contains final data archives of an airborne survey conducted by Fugro Airborne Surveys on behalf of United States Geological Survey over the Seco Creek area, Texas. Total coverage of the survey blocks amounted to 953 miles (1534 kilometres) over 2 survey blocks and several lines following the creeks through the survey area.  The survey was flown from May 21 to 27, 2002.

Fugro Airborne Surveys Job #6025

The archives contain three directories.

- Line Data:	Geosoft GDB database with archive description.

- Grids:	Grids in Geosoft GRD format for the following parameters:

- Magnetic total field (IGRF corrected)

- 5 coplanar resistivities

3.	Report:	A digital copy of the operations report

Projection Description:

Datum:	NAD27

Ellipsoid:	Clarke 1866

Projection:	UTM (Zone: 14)

Central Meridian:	99º West

False Northing:	0

False Easting:	500000

Scale Factor:	0.9996

WGS84 to Local Conversion:	Molodensky

X,Y,Z Datum Shifts:	8  -159  -175

EM PARAMETERS

FREQUENCY

orientation	nominal		actual	COIL SPACING

-----------	-------		------	------------

coplanar		400 Hz		386 Hz	7.9 m

coplanar		1 500 Hz	1 514 Hz	7.9 m

coaxial		3 300 Hz	3 315 Hz	9.0 m

coplanar		6 200 Hz	6 122 Hz	7.9 m

coplanar		25 000 Hz	25 960 Hz	7.9 m

coplanar		100 000 Hz	106 400 Hz	7.9 m

DATABASE : 6025_Seco.GDB

====================================================

NUMBER OF DATABASE CHANNELS :      146

====================================================

1 - LINE             DBS-INC  0.10		LINE NUMBER

2 - FLIGHT           DBS-INC  0.10		FLIGHT NUMBER

3 - DATE             DBS-INC  0.10		FLIGHT DATE

4 - FID              DBS-INC  0.10		FIDUCIAL COUNTER

5 - UTC              DBS-INC  0.10		UTC TIME

6 - ALTBIRDM         DBS-INC  0.10		BIRD RADAR ALTIMETER (METRES)

7 - ALTBIRDR         DBS-INC  0.10		BIRD RADAR ALTIMETER RAW (METRES)

8 - ALTLASER         DBS-INC  0.10		BIRD LASER ALTIMETER PROCESSED (METRES)

9 - ALTRFT           DBS-INC  0.10		HELICOPTER RADAR ALTIMETER RAW (FEET)

10 - BALT             DBS-INC  0.10		BAROMETRIC ALTIMETER RAW (METRES)

11 - ALTBARO          DBS-INC  0.10		BAROMETRIC ALTIMETER PROCESSED (METRES)

12 - CPI100K          DBS-INC  0.10		COPLANAR INPHASE FULLY PROCESSED 100K HZ

13 - CPI1500          DBS-INC  0.10		COPLANAR INPHASE FULLY PROCESSED 1500 HZ

14 - CPI25K           DBS-INC  0.10		COPLANAR INPHASE FULLY PROCESSED 25K HZ

15 - CPI400           DBS-INC  0.10		COPLANAR INPHASE FULLY PROCESSED 400 HZ

16 - CPI6200          DBS-INC  0.10		COPLANAR INPHASE FULLY PROCESSED 6200 HZ

17 - CPIR100K         DBS-INC  0.10		COPLANAR INPHASE FILTERED 100K HZ

18 - CPIR1500         DBS-INC  0.10		COPLANAR INPHASE FILTERED 1500 HZ

19 - CPIR25K          DBS-INC  0.10		COPLANAR INPHASE FILTERED 25K HZ

20 - CPIR400          DBS-INC  0.10		COPLANAR INPHASE FILTERED 400 HZ

21 - CPIR6200         DBS-INC  0.10		COPLANAR INPHASE FILTERED 6200 HZ

22 - CPPL             DBS-INC  0.10		COPLANAR POWERLINE MONITOR

23 - CPPLR            DBS-INC  0.10		COPLANAR POWERLINE MONITOR RAW

24 - CPQ100K          DBS-INC  0.10		COPLANAR QUADRATURE FULLY PROCESSED 100K HZ

25 - CPQ1500          DBS-INC  0.10		COPLANAR QUADRATURE FULLY PROCESSED 1500 HZ

26 - CPQ25K           DBS-INC  0.10		COPLANAR QUADRATURE FULLY PROCESSED 25K HZ

27 - CPQ400           DBS-INC  0.10		COPLANAR QUADRATURE FULLY PROCESSED 400 HZ

28 - CPQ6200          DBS-INC  0.10		COPLANAR QUADRATURE FULLY PROCESSED 6200 Hz

29 - CPQR100K         DBS-INC  0.10		COPLANAR QUADRATURE FILTERED 100K HZ

30 - CPQR1500         DBS-INC  0.10		COPLANAR QUADRATURE FILTERED 1500 HZ

31 - CPQR25K          DBS-INC  0.10		COPLANAR QUADRATURE FILTERED 25K HZ

32 - CPQR400          DBS-INC  0.10		COPLANAR QUADRATURE FILTERED 400 HZ

33 - CPQR6200         DBS-INC  0.10		COPLANAR QUADRATURE FILTERED 6200 HZ

34 - CPSP             DBS-INC  0.10		COPLANAR SPHERICS MONITOR

35 - CPSPR            DBS-INC  0.10		COPLANAR SPHERICS MONITOR RAW

36 - CXI3300          DBS-INC  0.10		COAXIAL INPHASE FULLY PROCESSED 3300 HZ

37 - CXIR3300         DBS-INC  0.10		COAXIAL INPHASE FILTERED 3300 HZ

38 - CXPL             DBS-INC  0.10		COAXIAL POWERLINE MONITOR

39 - CXPLR            DBS-INC  0.10		COAXIAL POWERLINE MONITOR RAW

40 - CXQ3300          DBS-INC  0.10		COAXIAL QUADRATURE FULLY PROCESSED 3300 HZ

41 - CXQR3300         DBS-INC  0.10		COAXIAL QUADRATURE FILTERED 3300 HZ

42 - CXSP             DBS-INC  0.10		COAXIAL SPHERICS MONITOR

43 - CXSPR            DBS-INC  0.10		COAXIAL SPHERICS MONITOR RAW

44 - DTMB             DBS-INC  0.10		DIGITAL ELEVATION MODEL FROM BARO

45 - DTMBARO          DBS-INC  0.10		PROCESSED DIGITAL ELEVATION MODEL FROM BARO

46 - DTMGPSZ          DBS-INC  0.10		DIGITAL ELEVATION MODEL FROM GPSZ

47 - DTMZ             DBS-INC  0.10		PROCESSED DIGITAL ELEVATION MODEL FROM GPSZ

48 - DEP100K          DBS-INC  0.10		DEPTH 100K HZ FILTERED

49 - DEP1500          DBS-INC  0.10		DEPTH 1500HZ FILTERED

50 - DEP25K           DBS-INC  0.10		DEPTH 25K HZ FILTERED

51 - DEP3300          DBS-INC  0.10		DEPTH 3300 HZ FILTERED

52 - DEP400           DBS-INC  0.10		DEPTH 400 HZ FILTERED

53 - DEP6200          DBS-INC  0.10		DEPTH 6200 HZ FILTERED

54 - DEP100K_NF       DBS-INC  0.10		DEPTH 100K HZ NOT FILTERED

55 - DEP1500_NF       DBS-INC  0.10		DEPTH 1500HZ NOT FILTERED

56 - DEP25K_NF        DBS-INC  0.10		DEPTH 25K HZ NOT FILTERED

57 - DEP3300_NF       DBS-INC  0.10		DEPTH 3300 HZ NOT FILTERED

58 - DEP400_NF        DBS-INC  0.10		DEPTH 400 HZ NOT FILTERED

59 - DEP6200_NF       DBS-INC  0.10		DEPTH 6200 HZ NOT FILTERED

60 - DDEP100K         DBS-INC  0.10		DIFFERENTIAL DEPTH 100K HZ FILTERED

61 - DDEP1500         DBS-INC  0.10		DIFFERENTIAL DEPTH 1500HZ FILTERED

62 - DDEP25K          DBS-INC  0.10		DIFFERENTIAL DEPTH 25K HZ FILTERED

63 - DDEP400          DBS-INC  0.10		DIFFERENTIAL DEPTH 400 HZ FILTERED

64 - DDEP6200         DBS-INC  0.10		DIFFERENTIAL DEPTH 6200 HZ FILTERED

65 - DDEP100K_NF      DBS-INC  0.10		DIFFERENTIAL DEPTH 100K HZ NOT FILTERED

66 - DDEP1500_NF      DBS-INC  0.10		DIFFERENTIAL DEPTH 1500HZ NOT FILTERED

67 - DDEP25K_NF       DBS-INC  0.10		DIFFERENTIAL DEPTH 25K HZ NOT FILTERED

68 - DDEP400_NF       DBS-INC  0.10		DIFFERENTIAL DEPTH 400 HZ NOT FILTERED

69 - DDEP6200_NF      DBS-INC  0.10		DIFFERENTIAL DEPTH 6200 HZ NOT FILTERED

70 - CEN100K          DBS-INC  0.10		CENTROID DEPTH 100K HZ FILTERED

71 - CEN1500          DBS-INC  0.10		CENTROID DEPTH 1500HZ FILTERED

72 - CEN25K           DBS-INC  0.10		CENTROID DEPTH 25K HZ FILTERED

73 - CEN400           DBS-INC  0.10		CENTROID DEPTH 400 HZ FILTERED

74 - CEN6200          DBS-INC  0.10		CENTROID DEPTH 6200 HZ FILTERED

75 - CEN100K_NF       DBS-INC  0.10		CENTROID DEPTH 100K HZ NOT FILTERED

76 - CEN1500_NF       DBS-INC  0.10		CENTROID DEPTH 1500HZ NOT FILTERED

77 - CEN25K_NF        DBS-INC  0.10		CENTROID DEPTH 25K HZ NOT FILTERED

78 - CEN400_NF        DBS-INC  0.10		CENTROID DEPTH 400 HZ NOT FILTERED

79 - CEN6200_NF       DBS-INC  0.10		CENTROID DEPTH 6200 HZ NOT FILTERED

80 - DIURNAL          DBS-INC  0.10		DIURNAL CORRECTION APPLIED

81 - KPA1             DBS-INC  0.10		PRESSURE IN MBAR

82 - L100I            DBS-INC  0.10		BASE LEVELED INPHASE 100K HZ

83 - L100Q            DBS-INC  0.10		BASE LEVELED QUADRATURE 100K HZ

84 - L1K5I            DBS-INC  0.10		BASE LEVELED INPHASE 1500 HZ

85 - L1K5Q            DBS-INC  0.10		BASE LEVELED QUADRATURE 1500 HZ

86 - L1K7I            DBS-INC  0.10		BASE LEVELED INPHASE 3300 HZ

87 - L1K7Q            DBS-INC  0.10		BASE LEVELED QUADRATURE 3300 HZ

88 - L25KI            DBS-INC  0.10		BASE LEVELED INPHASE 25K HZ

89 - L25KQ            DBS-INC  0.10		BASE LEVELED QUADRATURE 25K HZ

90 - L400I            DBS-INC  0.10		BASE LEVELED INPHASE 400 HZ

91 - L400Q            DBS-INC  0.10		BASE LEVELED QUADRATURE 400 HZ

92 - L6K2I            DBS-INC  0.10		BASE LEVELED INPHASE 6200 HZ

93 - L6K2Q            DBS-INC  0.10		BASE LEVELED QUADRATURE 6200 HZ

94 - LAT_BIRD         DBS-INC  0.10		LATITUDE BIRD GPS WGS84 (NAD83)

95 - LAT_HELI         DBS-INC  0.10		LATITUDE HELI GPS WGS84 (NAD83)

96 - LAT4             DBS-INC  0.10		LATITUDE HELI GPS UNPROCESSED WGS84 (NAD83)

97 - LON_BIRD         DBS-INC  0.10		LONGITUDE BIRD GPS WGS84 (NAD83)

98 - LON_HELI         DBS-INC  0.10		LONGITUDE HELI GPS  WGS84 (NAD83)

99 - LON4             DBS-INC  0.10		LONGITUDE HELI GPS UNPROCESSED WGS84 (NAD83)

100 - LSR1             DBS-INC  0.10		RAW LASER ALTIMETER, NO CONVERSION FACTOR

101 - MAG              DBS-INC  0.10		FINAL TOTAL MAGNETIC FIELD IGRF REMOVED

102 - MAGD             DBS-INC  0.10		DIURNAL CORRECTED TOTAL MAGNETIC FIELD

103 - IGRF             DBS-INC  0.10		IGRF

104 - MAGSP            DBS-INC  0.10		TOTAL MAGNETIC FIELD DESPIKED

105 - MAGUR            DBS-INC  0.10		RAW TOTAL MAGNETIC FIELD

106 - RES100K          DBS-INC  0.10		RESISTIVITY 100K HZ FILTERED

107 - RES1500          DBS-INC  0.10		RESISTIVITY 1500 HZ FILTERED

108 - RES25K           DBS-INC  0.10		RESISTIVITY 25K HZ FILTERED

109 - RES3300          DBS-INC  0.10		RESISTIVITY 3300 HZ FILTERED

110 - RES400           DBS-INC  0.10		RESISTIVITY 400 HZ FILTERED

111 - RES6200          DBS-INC  0.10		RESISTIVITY 6200 HZ FILTERED

112 - RES100K_NF       DBS-INC  0.10		RESISTIVITY 100K HZ NOT FILTERED

113 - RES1500_NF       DBS-INC  0.10		RESISTIVITY 1500 HZ NOT FILTERED

114 - RES25K_NF        DBS-INC  0.10		RESISTIVITY 25K HZ NOT FILTERED

115 - RES3300_NF       DBS-INC  0.10		RESISTIVITY 3300 HZ NOT FILTERED

116 - RES400_NF        DBS-INC  0.10		RESISTIVITY 400 HZ NOT FILTERED

117 - RES6200_NF       DBS-INC  0.10		RESISTIVITY 6200 HZ NOT FILTERED

118 - DRES100K         DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 100K HZ FILTERED

119 - DRES1500         DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 1500 HZ FILTERED

120 - DRES25K          DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 25K HZ FILTERED

121 - DRES400          DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 400 HZ FILTERED

122 - DRES6200         DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 6200 HZ FILTERED

123 - DRES100K_NF      DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 100K HZ NOT FILTERED

124 - DRES1500_NF      DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 1500 HZ NOT FILTERED

125 - DRES25K_NF       DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 25K HZ NOT FILTERED

126 - DRES400_NF       DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 400 HZ NOT FILTERED

127 - DRES6200_NF      DBS-INC  0.10		DIFFERENTIAL RESISTIVITY 6200 HZ NOT FILTERED

128 - X                DBS-INC  0.10		FINAL BIRD UTM X CLARK 1866 (NAD27)

129 - X_HELI           DBS-INC  0.10		UTM X FROM HELI GPS CLARK 1866 (NAD27)

130 - Y                DBS-INC  0.10		FINAL UTM Y CLARK 1866 (NAD27)

131 - Y_HELI           DBS-INC  0.10		UTM X FROM HELI GPS CLARK 1866 (NAD27)

132 - Z_B              DBS-INC  0.10		FINAL Z

133 - Z_H              DBS-INC  0.10		Z FROM HELI GPS

134 - GPSZ4            DBS-INC  0.10		Z FROM HELI GPS RAW

135 - _100I            DBS-INC  0.10		RAW INPHASE 100K HZ

136 - _100Q            DBS-INC  0.10		RAW QUADRATURE 100K HZ

137 - _1K5I            DBS-INC  0.10		RAW INPHASE 1500 HZ

138 - _1K5Q            DBS-INC  0.10		RAW QUADRATURE 1500 HZ

139 - _1K7I            DBS-INC  0.10		RAW INPHASE 3300 HZ

140 - _1K7Q            DBS-INC  0.10		RAW QUADRATURE 3300 HZ

141 - _25KI            DBS-INC  0.10		RAW INPHASE 25K HZ

142 - _25KQ            DBS-INC  0.10		RAW QUADRATURE 25K HZ

143 - _400I            DBS-INC  0.10		RAW INPHASE 400 HZ

144 - _400Q            DBS-INC  0.10		RAW QUADRATURE 400 HZ

145 - _6K2I            DBS-INC  0.10		RAW INPHASE 6200 HZ

146 - _6K2Q            DBS-INC  0.10		RAW QUADRATURE 6200 HZ

========================================================================================

# APPENDIX C

### PROCESSING LOG

Electromagnetics Processing:

All steps performed on all EM channels unless otherwise stated.

- Due to a conversion error in the transfer of the raw helicopter data file to the field database, the coaxial 3300 Hz data required a multiplier of 2.  This factor was applied to the coaxial in-phase and quadrature channels prior to delivery of the final archives but would not have been applied to any of the preliminary data products.

- Filter raw EM channels 	11pt median followed by 11 pt Hanning
L400I  (  CPIR400, L400Q  (  CPQR400
L1K5I  (  CPIR1500, L1K5Q  (  CPQR1500
L1K7I  (  CXIR3300, L1K7Q  (  CXQR3300
L6K2I  (  CPIR6200, L6K2IQ  (  CPQR6200
L25KI  (  CPIR25K, L25KQ  (  CPQR25K
L100I  (  CPIR100K, L100Q  (  CPQR100K

- Apply manual leveling picks to filtered EM channels.

- Gain adjustment for 100 kHz and 25 kHz to correct known errors from EM calibration.  Gain increase of 18% and 13% applied to the inphase and quadrature of the 100 kHz and 25 kHz respectively.  These gain corrections would not have been applied to any preliminary data products.

- Calculate resistivity and depth channels with Fugro proprietary software using filtered and gained EM data.

- Calculate centroid depths (CEN*), differential resistivity (DRES*) and differential depths (DRES*).

- Filter output channels (RES*, DEP*, DRES*, DDEP*, CEN*).  21pt median 21pt Hanning.  All unfiltered channels are in the archive with the suffix _NF.

- See the archive CD-ROM or Appendix B for complete channel name description.

Magnetics Processing  (from Russell Imrie)

MAGSP is the raw channel MAGUR manually despiked using a fourth difference as a reference. All spikes occurred in areas where the mag was smoothly varying. This allowed the defaulted areas to be interpolated using an Akima spline. A 5 point hanning was used to smooth the transition from areas defaulted and splined to areas not defaulted. A lag of 11 scans (1.1 seconds) was applied to the mag.  DIURNAL data were examined for spikes and applied to produce the MAGDL channel. MAGDL and MAGL were gridded and compared to ensure no valid anomalies were being removed and that the grid was improved by the diurnal application.

IGRF was computed on a point by point basis using the final Z channel as height above sea level and a year 2000 table of coefficients. May 2002 was the calculation date. Tie line leveling was not used as the altitude and gradient misties were too great.

A grid based vertical gradient was calculated from the IGRF corrected mag. It was shadowed and inspected but revealed no leveling errors on either area.

Digital Elevation Model Processing (from Russell Imrie)

The barometric altimeter was converted to metres and filtered with an 11 point Hanning. It was profiled and inspected against the Z channel for spikes. Significant steps were removed and splined or DC shifted to match the character of the Z trace. The Z data were also inspected in this manner, compared to the filtered barometric altimeter trace for sharp changes. Corrections were made by defaulting and splining or by shifting data so the Z profile matched the character of the Baro.  Altbirdr has been filtered by Mike Cain to produce ALTBIRDM. ALTBIRDM had a couple of spikes that were removed and splined. ALTLASER was produced by Mike Cain and severe spikes were removed and splined using ALTBIRDM as a reference. Some of the ALTLASER data spikes covered areas where the ALTBIRDM showed rapid variation. These were not splined.

DTM's were calculated as follows:

DTMB - BALT-ALTBIRDM

DTMZ - Z-ALTBIRDM

These were contoured, inspected and compared. The tie line leveling corrections were applied to the BALTF channel to produce the final BALT channel.

# APPENDIX D

### BACKGROUND INFORMATION

##### D.1	Resistivity Mapping

Areas of widespread conductivity are commonly encountered during surveys.  These conductive zones may reflect alteration zones, shallow-dipping sulphide or graphite-rich units, saline pools or water tables, or conductive overburden.  In such areas, anomalies can be generated by decreases of only 5 m in survey altitude as well as by increases in conductivity.  The typical flight record in conductive areas is characterized by in-phase and quadrature channels which are continuously active.  Local EM peaks reflect either increases in conductivity of the earth or decreases in survey altitude.  For such conductive areas, apparent resistivity profiles and contour maps are necessary for the correct interpretation of the airborne data.  The advantage of the resistivity parameter is that anomalies caused by minor altitude changes are virtually eliminated, so the resistivity data reflect only those anomalies caused by conductivity changes.  The resistivity analysis also helps the interpreter to differentiate between conductive bedrock and conductive overburden.  For example, discrete conductors will generally appear as narrow lows on the contour map and broad conductors (e.g., overburden, tailings ponds leaks or saline water tables) will appear as wide lows.

The apparent resistivity is calculated using the pseudo-layer (or buried) half-space model defined by Fraser (1978).  This model consists of a resistive layer overlying a conductive half-space.  The depth channels give the apparent depth below surface of the conductive material.  The apparent depth is simply the apparent thickness of the overlying resistive layer. The apparent depth (or thickness) parameter will be positive when the upper layer is more resistive than the underlying material, in which case the apparent depth may be quite close to the true depth.

The apparent depth will be negative when the upper layer is more conductive than the underlying material, and will be zero when a homogeneous half-space exists.  The apparent depth parameter must be interpreted cautiously because it will contain any errors which may exist in the measured altitude of the EM bird (e.g., as caused by a dense tree cover).  The inputs to the conductivity algorithm are the in-phase and quadrature components of the coplanar coil-pair.  The outputs are the apparent conductivity of the conductive half-space (the source) and the sensor-source distance.  The flying height is not an input variable, and the output conductivity and sensor-source distance are independent of the flying height when the conductivity of the measured material is sufficient to yield significant in-phase as well as quadrature responses.  The apparent depth, discussed above, is simply the sensor-source distance minus the measured altitude or flying height.  Consequently, errors in the measured altitude will affect the apparent depth parameter but not the apparent conductivity parameter.

The apparent depth parameter is a useful indicator of simple layering in areas lacking a heavy tree cover.  The DIGHEM system has been flown for purposes of permafrost mapping, where positive apparent depths were used as a measure of permafrost thickness.  However, little quantitative use has been made of negative apparent depths because the absolute value of the negative depth is not a measure of the thickness of the conductive upper layer and, therefore, is not meaningful physically.  Qualitatively, a negative apparent depth estimate usually shows that the EM anomaly is caused by a conductive layer at surface.  Consequently, the apparent depth channel can be of significant help in distinguishing between overburden and bedrock conductors.

The DP channels, which give the apparent depth to the conductive material, also help to determine whether a conductive response arises from surficial material or from a conductive zone in the bedrock.  When these channels ride above the zero level on the digital profiles (i.e., depth is negative), it implies that the EM and conductivity profiles are responding primarily to a conductive upper layer, i.e., conductive overburden.  If the DP channels are below the zero level, it indicates that a resistive upper layer exists, and this usually implies the existence of a bedrock conductor.  If the low frequency DP channel is below the zero level and the high frequency DP is above, this suggests that a bedrock conductor occurs beneath conductive cover.

##### D.2	Reduction of Geologic Noise

Geologic noise refers to unwanted geophysical responses.  For purposes of airborne EM surveying, geologic noise refers to EM responses caused by conductive overburden and magnetic permeability.

Magnetite produces a form of geological noise on the in-phase channels of all EM systems.  Rocks containing less than 1 % magnetite can yield negative in-phase anomalies caused by magnetic permeability.  When magnetite is widely distributed throughout a survey area, the in-phase EM channels may continuously rise and fall, reflecting variations in the magnetite percentage, flying height, and overburden thickness.  This can lead to difficulties in recognizing deeply buried bedrock conductors, particularly if conductive overburden also exists.

##### D.3	Magnetics

Total field magnetics provides information on the magnetic properties of the earth materials in the survey area.  The information can be used to locate magnetic bodies of direct interest for exploration, and for structural and lithological mapping.

The total field magnetic response reflects the abundance of magnetic material, in the source.  Magnetite is the most common magnetic mineral.  Other minerals such as ilmenite, pyrrhotite, franklinite, chromite, hematite, arsenopyrite, limonite and pyrite are also magnetic, but to a lesser extent than magnetite on average.

In some geological environments, an EM anomaly with magnetic correlation has a greater likelihood of being produced by sulphides than one which is non-magnetic.  However, sulphide ore bodies may be non-magnetic (e.g., the Kidd Creek deposit near Timmins, Canada) as well as magnetic (e.g., the Mattabi deposit near Sturgeon Lake, Canada).

Iron ore deposits will be anomalously magnetic in comparison to surrounding rock due to the concentration of iron minerals such as magnetite, ilmenite and hematite.

Changes in magnetic susceptibility often allow rock units to be differentiated based on the total field magnetic response.  Geophysical classifications may differ from geological classifications if various magnetite levels exist within one general geological classification.  Geometric considerations of the source such as shape, dip and depth, inclination of the earth's field and remanent magnetization will complicate such an analysis.

In general, mafic lithologies contain more magnetite and are therefore more magnetic than many sediments which tend to be weakly magnetic.  Metamorphism and alteration can also increase or decrease the magnetization of a rock unit.

Textural differences on a total field magnetic contour, colour or shadow map, due to the frequency of activity of the magnetic parameter resulting from inhomogeneities in the distribution of magnetite within the rock, may define certain lithologies.  For example, near surface volcanics may display highly complex contour patterns with little line-to-line correlation.

Rock units may be differentiated based on the plan shapes of their total field magnetic responses.  Mafic intrusive plugs can appear as isolated "bulls-eye" anomalies.  Granitic intrusives appear as sub-circular zones, and may have contrasting rings due to contact metamorphism.  Generally, granitic terrain will lack a pronounced strike direction, although granite gneiss may display strike.

Linear north-south units are theoretically not well-defined on total field magnetic maps in equatorial regions due to the low inclination of the earth's magnetic field.  However, most stratigraphic units will have variations in composition along strike which will cause the units to appear as a series of alternating magnetic highs and lows.

Faults and shear zones may be characterized by alteration which causes destruction of magnetite (e.g., weathering) which produces a contrast with surrounding rock.  Structural breaks may be filled by magnetite-rich, fracture filling material as is the case with diabase dikes, or by non-magnetic felsic material.

Faulting can also be identified by patterns in the magnetic total field contours or colours.  Faults and dikes tend to appear as lineaments and often have strike lengths of several kilometres.  Offsets in narrow, magnetic, stratigraphic trends also delineate structure.  Sharp contrasts in magnetic lithologies may arise due to large displacements along strike-slip or dip-slip faults.

# APPENDIX E

FLIGHT LOGS

# APPENDIX F

TESTS AND CALIBRATIONS

EM Calibrations

# CALIBRATION OF THE DIGHEM DIGITAL (DSP) SYSTEM

The calibration method used in the digital DighemV has been developed as a significant improvement over the practices described by Fitterman (1998), which practices were originally developed through experimentation and consultation between Fugro and the United States Geological Survey.  The problems defined by Fitterman, including jig calibration and conductive ground response, are obviated by calibration at high altitude using internal, rigidly mounted, automatically triggered and measured calibration coils.

Calibration of the system during the survey will use the Fugro AutoCal™ automatic, internal calibration process.  At the beginning and end of each flight, and at intervals during the flight, the system will be flown up to high altitude to remove it from any “ground effect” (response from the earth). Any remaining signal from the receiver coils (base level) will be measured as the zero level, and removed from the data collected until the time of the next calibration.  Following the zero level setting, internal calibration coils, for which the response phase and amplitude have been determined at the factory, are automatically triggered – one for each frequency.  The on-time of the coils is sufficient to determine an accurate response through any ambient noise.  The receiver response to each calibration coil “event” is compared to the expected response (from the factory calibration) for both phase angle and amplitude, and the applied phase and gain corrections adjusted to bring the data to the correct value.

In addition, the output of the transmitter coils are continuously monitored during the survey, and the applied gains adjusted to correct for any change in transmitter output (due to heating, etc.)

Because the internal calibration coils are calibrated at the factory (on a resistive halfspace) ground calibrations using external calibration coils on-site are not necessary for system calibration.  A check calibration may be carried out on-site to ensure all systems are working correctly.  All system calibrations will be carried out in the air, at sufficient altitude that there will be no measurable response from the ground.

The internal calibration coils are rigidly positioned and mounted in the system relative to the transmitter and receiver coils.  In addition, when the internal calibration coils are calibrated at the factory, a rigid jig is employed to ensure accurate response from the external coils.

Using real time Fast Fourier Transforms and the calibration procedures outlined above, the data will be processed in real time from measured total field at a high sampling rate to in-phase and quadrature values at 10 samples per second.

# Greg Hodges, Chief Geophysicist  01/04/09

References:

Fitterman, D.V., (1998). Sources of calibration errors in helicopter EM data. Exploration Geophysics 29, 65-70.

External Calibration Results

| May 21, 2002 | Start calibrations. In Seco Creek survey area |  |  |
| --- | --- | --- | --- |
| FREQUENCY | CHANNEL | INTERNAL | EXTERNAL | PHASE |
|  |  | MEASURED | TARGET | MEASURED | TARGET |  |
| 400 | L400I | 207.0 | 200.0 | 208.0 | 200.4 | -233.0 |
|  | L400Q | 204.0 | 200.0 | 200.0 | 200.4 | -9.0 |
| 1500 | L1K5I | 185.0 | 183.0 | 199.0 | 204.2 | -175.0 |
|  | L1K5Q | 180.0 | 183.0 | 189.0 | 204.2 | 6.0 |
| 3300 | L1K7I | 93.0 | 94.0 | 88.0 | 99.9 | -259.0 |
|  | L1K7Q | 92.0 | 94.0 | 89.0 | 99.9 | -4.0 |
| 6200 | L6K2I | 830.0 | 822.0 | 186.0 | 207.5 | -414.0 |
|  | L6K2Q | 827.0 | 822.0 | 195.0 | 207.5 | -10.0 |
| 25000 | L25KI | 404.0 | 409.0 | 132.0 | 192.5 | -1695.0 |
|  | L25KQ | 398.0 | 409.0 | 155.0 | 192.5 | -76.0 |
| 100000 | L100I | 310.0 | 320.0 | 80.0 | 178.8 | -4430.0 |
|  | L100Q | 319.0 | 320.0 | 92.0 | 178.8 | -322.0 |
| May 27, 2002 | End calibrations. In Seco Creek survey area |  |  |
| FREQUENCY | CHANNEL | INTERNAL | EXTERNAL | PHASE |
|  |  | MEASURED | TARGET | MEASURED | TARGET |  |
| 400 | L400I | 206.0 | 200.0 | 210.0 | 200.4 | -225.0 |
|  | L400Q | 204.0 | 200.0 | 202.0 | 200.4 | -9.0 |
| 1500 | L1K5I | 182.0 | 183.0 | 199.0 | 204.2 | -261.0 |
|  | L1K5Q | 180.0 | 183.0 | 192.0 | 204.2 | 3.0 |
| 3300 | L1K7I | 92.0 | 94.0 | 87.0 | 99.9 | -273.0 |
|  | L1K7Q | 94.0 | 94.0 | 88.0 | 99.9 | -5.0 |
| 6200 | L6K2I | 824.0 | 822.0 | 187.0 | 207.5 | -439.0 |
|  | L6K2Q | 826.0 | 822.0 | 198.0 | 207.5 | -12.0 |
| 25000 | L25KI | 402.0 | 409.0 | 131.0 | 192.5 | -1661.0 |
|  | L25KQ | 402.0 | 409.0 | 156.0 | 192.5 | -60.0 |
| 100000 | L100I | 311.0 | 320.0 | * | 178.8 | -3724.0 |
|  | L100Q | 311.0 | 320.0 | * | 178.8 | -201.0 |
| * excessive noise could not determine data values |  |  |  |
| June 6, 2002 | Mountsberg calibration site, Milton, Ontario |  |  |
| FREQUENCY | CHANNEL | INTERNAL | EXTERNAL | PHASE |
|  |  | MEASURED | TARGET | MEASURED | TARGET |  |
| 400 | L400I | 203.0 | 200.0 | 209.2 | 200.4 | -238.0 |
|  | L400Q | 202.8 | 200.0 | 203.5 | 200.4 | -12.0 |
| 1500 | L1K5I | 182.2 | 183.0 | 200.0 | 204.2 | -250.0 |
|  | L1K5Q | 181.9 | 183.0 | 193.0 | 204.2 | 3.5 |
| 3300 | L1K7I | 94.5 | 94.0 | 88.0 | 99.9 | -222.0 |
|  | L1K7Q | 93.9 | 94.0 | 88.0 | 99.9 | -3.0 |
| 6200 | L6K2I | 825.0 | 822.0 | 189.3 | 207.5 | -456.0 |
|  | L6K2Q | 824.0 | 822.0 | 198.3 | 207.5 | -7.0 |
| 25000 | L25KI | 419.8 | 409.0 | 142.3 | 192.5 | -1950.0 |
|  | L25KQ | 407.4 | 409.0 | 156.7 | 192.5 | 3.0 |
| 100000 | L100I | 316.3 | 320.0 | 79.0 | 178.8 | -1479.0 |
|  | L100Q | 321.0 | 320.0 | 80.0 | 178.8 | 16.0 |

Notes:

- Differences in the “measured” and “target” values in the external calibrations are corrected using scaling factors in the DSP software.  The important numbers in the calibration tables above are the “measured” and “target” values in the internal calibrations.  These offsets can also be monitored during flight using digital data from the “turns” in the database.

- No changes were made during these calibrations.  The final calibration from Mountsberg on June 6 represents how the system was calibrated during the survey.

# Footnotes

Sengpiel, K.P., 1988, imate Inversion of Airborne EM Data from Multilayered Ground: Geophysical Prospecting 36, 446-459.

Huang, H. and Fraser, D.C., 1993, Differential Resistivity Method for Multi-frequency Airborne EM Sounding: presented at Intern. Airb. EM Workshop, Tucson, Ariz.

Constable et al, 1987, Occam’s inversion: a practical algorithm for generating smooth models from electromagnetic sounding data: Geophysics, 52, 289-300.

Huang H., and Palacky, G.J., 1991, Damped least-squares inversion of time domain airborne EM data based on singular value decomposition: Geophysical Prospecting, 39, 827-844.

Resistivity mapping with an airborne multicoil electromagnetic system:  Geophysics, v. 43, p.144-172