# FEDERAL AVIATION ADMINISTRATION

## AIRWORTHINESS DIRECTIVES

LARGE AIRCRAFT

BIWEEKLY 2002-15

This electronic copy may be printed and used in lieu of the FAA biweekly paper copy.

U.S. Department of Transportation

### Federal Aviation Administration

Regulatory Support Division

Delegation and Airworthiness Programs Branch, AIR-140

P. O. Box 26460

Oklahoma City, OK  73125-0460

FAX  405-954-4104

Biweekly 2002-01

| 2001-23-12 | R1 | SAAB Aircraft | SAAB SF340A Series and SAAB 340B Series |
| --- | --- | --- | --- |
| 2001-23-15 | C, S 01-05-05 | Boeing | 747 Series |
| 2001-24-25 | COR | McDonnell Douglas | DC-9-10, -20, -30, -40 Series; and C-9 |
| 2001-24-27 | C, S 96-02-05 | McDonnell Douglas | DC-9-10, -20, -30, -40, -50 Series; DC-9-81, -82, -83, -87 Series; MD-88; and C-9 Series |
| 2001-25-11 | S 01-15-12 & 99-17-16 | Pratt and Whitney | Engine: PW4050, PW4052, PW4056, PW4060, PW4060A, PW4060C, PW4062, PW4152, PW4156, PW4156A, PW4158, PW4160, PW4460, PW4462, and PW4650 |
| 2001-26-11 | S 00-24-26 | Rolls-Royce | Engine: RB211 Trent 875, RB211 Trent 877, RB211 Trent 884, RB211 Trent 892, and RB211 Trent 892B Series |
| 2001-26-12 | S 01-12-05 | Boeing | 747-100, 747-200, 747-300, and 747SR Series |
| 2001-26-14 | S 96-12-13 | Dornier Luftfahrt | 328-100 |
| 2001-26-15 |  | McDonnell Douglas | DC-9-81, -82, -83, -87; and MD-88 |
| 2001-26-16 |  | McDonnell Douglas | DC-9-81, -82, -83, -87 Series; and MD-88 |
| 2001-26-17 |  | Airbus Industrie | A330-202, -223, -243, -301, -321, -322, -323, -341, -342, and -343 Series |
| 2001-26-18 |  | Dornier Luftfahrt | 328-300 Series |
| 2001-26-19 |  | Boeing | 767 Series |
| 2001-26-20 |  | Airbus Industrie | A319, A320, and A321 Series |
| 2001-26-21 |  | Airbus Industrie | A319, A320, and A321 Series |
| 2001-26-22 |  | BAE Systems Limited | Avro 146-RJ Series |
| 2001-26-23 |  | Bombardier | DHC-8-102, -103, -106, -201, -202, -301, -311, and -315 |
| 2001-26-24 |  | McDonnell Douglas | DC-9-10, -20, -30, -40, -50 Series; and C-9 |
| 2001-26-51 | FR | Bombardier | CL-600-2B19 Series |
| 2002-01-03 |  | GE Aircraft | Engine: CT7-5A2, -5A3, -7A, and -7A1 |

Biweekly 2002-02

| 2002-01-01 |  | Boeing | 737-100, -200, -200C, -300, -400, and -500 Series |
| --- | --- | --- | --- |
| 2002-01-05 |  | British Aerospace | HP.137 Jetstream Mk.1, Jetstream Series 200, Jetstream Series 3101, and Jetstream Model 3201 |
| 2002-01-08 |  | Israel Aircraft Industries | Galaxy |
| 2002-01-12 |  | General Electric Company | Engine: GE90-76B, -77B, -85B, -90B, and -94B |
| 2002-01-14 | S 01-26-10 | Airbus Industrie | A319, A320, and A321 Series |

Biweekly 2002-03

| 2001-17-26 | R1 | Raytheon Aircraft | DH.125, HS.125, BH.125, and BAe.125 (U-125 and C-29A) Series, Hawker 800, Hawker 800 (U-125A), Hawker 800XP, Hawker 1000 |
| --- | --- | --- | --- |
| 2001-24-27 | COR S 96-02-05 | McDonnell Douglas | DC-9-10, -20, -30, -40, and -50 Series; DC-9-81, -82, -83, and -87 Series,; MD-88; and C-9 Series |
| 2001-25-04 | COR | Honeywell International Inc. | Engine: LTS101-600A-2 and LTS101-600A-3 Turboshaft; LTP101-600A-1A and LTP101-700A-1A Turboprop |
| 2002-01-04 |  | General Electric | Engine: CF6-80E1 |
| 2002-01-13 | S 96-21-06 | Boeing | 767 Series |
| 2002-01-15 |  | Boeing | 767-200, -300, and -300F Series |
| 2002-01-16 | S 86-24-11 & 86-25-04 | Fairchild Aircraft | SA26-AT, SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, SA227-TT |
| 2002-01-17 |  | Dornier Luftfahrt | 328-100 Series |
| 2002-01-18 |  | Airbus Industrie | A319, A320, and A321 Series |
| 2002-01-19 |  | Fokker | F.28 Mark 0070 and 0100 Series |
| 2002-01-20 |  | BAE Systems | BAe 146-200A Series |
| 2002-01-21 |  | BAE Systems | BAe-146 Series and Avro 146-RJ Series |
| 2002-01-22 |  | Short Brothers | SD3 Series |
| 2002-01-23 |  | Raytheon Aircraft | Beech 400, Beech 400A, Beech 400T Series, Beech 400T-1, Beech MU-300-10, Mitsubishi MU-300 |
| 2002-01-24 |  | McDonnell Douglas | DC-9-81, -82, , -83, and -87 Series, and MD-88 |
| 2002-01-25 |  | Bombardier | DHC-8-100, -200, and -300 Series |
| 2002-01-26 |  | Israel Aircraft | 1124 and 1124A Series, and 1125 Westwind Astra Series |
| 2002-01-27 | S 98-15-03 | General Electric Company | Engine: GE90-76B, -77B, -85B, and -90B Turbofan |
| 2002-01-28 |  | Dowty Aerospace | Propeller: R334/4-82-F/13 |

Biweekly 2002-03 cont'd…

| 2002-01-29 |  | Rolls-Royce | Engine: Tay 650-15 and 651-54 Turbofan |
| --- | --- | --- | --- |
| 2002-02-02 |  | Boeing | 707 and 720 Series |
| 2002-02-03 |  | BAE Systems | BAe 146 Series |
| 2002-02-09 |  | General Electric | Engine: CF6-45 and CF6-50 Series Turbofan |
| 2002-03-51 | E | Hamilton Sundstrand | Propeller: 568F-1 |

Biweekly 2002-04

| 2001-23-13 | COR | Boeing | 747 Series and 747SP Series |
| --- | --- | --- | --- |
| 2002-02-04 |  | Boeing | 757 Series |
| 2002-02-05 |  | Airbus Industrie | A300 B2 and A300 B4; A300 B4-600, B4-600R, F4-600R (collectively called A300-600), and A310 Series |
| 2002-02-06 |  | Airbus Industrie | A330-243, -341, -342, and -343 Series |
| 2002-02-07 |  | Airbus Industrie | A330 and A340 Series |
| 2002-02-08 |  | Boeing | 737-200, -200C, -300, and -500 Series |
| 2002-02-12 | S 2000-05-12 | Rolls-Royce plc. | Engine: RB211-524G2-19, RB211-524G2-T-19, RB211-524G3-19, RB211-524G3-T-19, RB211-524H2-19, RB211-524H2-T-19, RB211-524H-36, and RB211-524H-T-36 Turbofan |
| 2002-02-13 |  | CFM International | Engine: CFM56-5 Series Turbofan |
| 2002-03-02 | S 98-13-03 | British Aerospace | HP.137 Jetstream Mk.1, Jetstream Series 200, Jetstream Series 3101 |
| 2002-03-05 |  | McDonnell Douglas | DC-8 Series |
| 2002-03-06 | S 2001-07-10 | McDonnell Douglas | DC-9-81, -82, -83, and -87 Series, MD-88, and MD-90-30 Series |
| 2002-03-07 |  | BAE Systems | BAe 146 and Avro 146-RJ Series |
| 2002-03-08 | S 2000-12-02 | Pratt & Whitney | Engine: PW4050, PW4052, PW4056, PW4060, PW4060A, PW4060C, PW4062, PW4152, PW4156, PW4156A, PW4158, PW4160, PW4460, PW4462, PW4650, PW4164, PW4168, PW4168A, PW4074, PW4074D, PW4077, PW4077D, PW4084, PW4084D, PW4090, PW4090D, and PW4098 Turbofan |
| 2002-03-10 |  | BAE Systems | BAe 146 Series and Avro 146-RJ Series |
| 2002-03-11 | S 2000-11-27 | Airbus Industrie | A319, A320, and A321 Series |
| 2002-03-12 |  | Bombardier | DHC-8-400 Series |
| 2002-03-13 |  | Short Brothers | SD3-60, SD3-60 SHERPA, and SD3-SHERPA Series |
| 2002-03-14 |  | Bombardier | CL-600-2B19 Series |
| 2002-03-15 |  | Dornier Luftfahrt | 328-100 and 328-300 Series |
| 2002-04-01 | S 97-02-10 | McDonnell Douglas | DC-9, DC-9-80, and C-9 Series; MD-88 and MD-90 |
| 2002-04-02 |  | Airbus Industrie | A300 F4-605R |
| 2002-04-03 |  | Fokker | F27 Mark 050 Series |
| 2002-04-52 | E, S 2002-03-51 | Hamilton Sundstrand | Propeller: 568F-1 |

Biweekly 2002-05

| 2002-03-08 | COR S 2000-12-02 | Pratt & Whitney | Engine: PW4050, PW4052, PW4056, PW4060, PW4060A, PW4060C, PW4062, PW4152, PW4156, PW4156A, PW4158, PW4160, PW4460, PW4462, PW4650, PW4164, PW4168, PW4168A, PW4074, PW4074D, PW4077, PW4077D, PW4084, PW4084D, PW4090, PW4090-3, PW4090D, and PW4098 Turbofan |
| --- | --- | --- | --- |
| 2002-04-05 |  | Airbus | A300 B2-1C, A300 B2-203, A300 B2K-3C, and A300 B4 Series, A300 B4-600 Series, A300 B4-600R Series, A300 F4-605R, A310 Series |
| 2002-04-06 |  | Boeing | 727 Series |
| 2002-04-08 |  | Boeing | 737-600, -700, -700C, and -800 Series |
| 2002-04-09 |  | BAE Systems | BAe 146 and Avro 146-RJ Series |
| 2002-04-10 |  | Airbus | A319 Series and A320-200 Series |
| 2002-04-11 | S 2000-08-10 | General Electric | Engine: GE90-76B/ -77B/ -85B/ -90B/ -94B Series |
| 2002-05-01 | S 2001-12-23 | Boeing | 747-100, 747-200, 747-300, 747SP, and 747SR Series |
| 2002-05-02 | S 2000-03-03 R1 | General Electric | Engine: CF34-3A1 and -3B1 Series Turbofan |
| 2002-05-03 | S 2000-08-11 | General Electric | Engine: CF6-6, CF6-45, and CF6-50 Series Turbofan |
| 2002-05-51 | E, S2002-04-52 | Hamilton Sundstrand | Propeller: 568F-1 |

Biweekly 2002-06

| 2002-02-05 | COR | Airbus | A300 B2 and A300 B4; A300 B4-600, B4-600R, and F4-600R (collectively called A300-600); and Model A310 series |
| --- | --- | --- | --- |
| 2002-02-12 | COR, S 2000-05-12 | Rolls-Royce plc | Engine: RB211-524G2-19, RB211-524G2-T-19, RB211-524G3-19, RB211-524G3-T-19, RB211-524H2-19, RB211-524H2-T-19, RB211-524H-36, and RB211-524H-T-36 turbofan |
| 2002-02-13 | COR | CFM International | Engine: CFM56-5 series turbofan |
| 2002-05-07 |  | Boeing | 737-100, -200, -200C, -300, -400, and -500 Series |
| 2002-06-02 |  | Boeing | 747 Series |
| 2002-06-03 |  | Boeing | 737-600, -700, -700C and -800 Series |
| 2002-06-05 |  | Transport Category Airplanes Rockwell Collins | Appliance: Mode C 621A-3 Air Traffic Control (ATC) Transponder(s) |
| 2002-06-09 |  | Airbus | A300; A300 B4-600, B4-600R, and F4-600R (collectively called A300-600); and A310 Series |
| 2002-06-51 | E | Bombardier | CL-600-2C10 (Regional Jet Series 700 and 701) Series |
| 2002-06-53 | E | Airbus | A319, A320, and A321, A330 Series, A340 Series |

Biweekly 2002-07

| 2002-06-06 |  | Rockwell Collins | Appliance: TDR-94 and TDR-94D Mode S transponders |
| --- | --- | --- | --- |
| 2002-06-07 |  | General Electric Company | Engine: CF6-80E1 series turbofan |
| 2002-06-11 |  | McDonnell Douglas | MD-90-30 |
| 2002-06-12 |  | Dassault Aviation | Mystere-Falcon 50 Series |
| 2002-06-13 |  | McDonnell Douglas | MD-90-30 |
| 2002-06-14 |  | McDonnell Douglas | DC-10-10, -10F, -15, -30, -30F (KC-10A and KDC-10), -40, and -40F series; and MD-10-10F and MD-10-30F Series |
| 2002-06-15 |  | Boeing | 777-200 and -300 Series |
| 2002-06-16 |  | Boeing | 767-300 |
| 2002-06-51 | FR | Bombardier | CL-600-2C10 (Regional Jet Series 700 and 701) Series |
| 2002-07-02 |  | Israel Aircraft Industries, Ltd. | Galaxy airplanes and Model Gulfstream 200 Series |
| 2002-07-03 |  | Fokker Services B.V. | F.28 Series |

Biweekly 2002-08

| 2002-07-04 |  | Pratt & Whitney | Engine: JT9D-7R4D, -7R4D1, -7R4E, -7R4E1, -7R4E4, -7R4G2, and 7R4H1 Series Turbofan |
| --- | --- | --- | --- |
| 2002-07-05 |  | Airbus | A300 B2, A300 B4, A300 B4-600, A300 B4-600R Series, and A300 F4-605R |
| 2002-07-06 |  | McDonnell Douglas | DC-9-10, -20, -30, -40, and -50 Series, and C-9 |
| 2002-07-07 |  | Boeing | 777-200 Series |
| 2002-07-08 | S 97-22-07 | Boeing | 737-200, -200C, -300, -400, and -500 Series |
| 2002-07-09 | S 99-04-22 | Boeing | 727 Series |
| 2002-07-10 |  | Boeing | 737-200, -200C, -300, -400, and -500 Series |
| 2002-07-11 |  | Boeing | 737-200 and -200C |
| 2002-07-12 | S 2000-08-12 | General Electric | Engine: CF6-80A, CF6-80C2, and CF6-80E1 Series Turbofan |
| 2002-08-01 |  | Fairchild Aircraft | SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, and SA227-TT |
| 2002-08-02 | S 2001-20-14 | Fairchild Aircraft | SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, SA227-TT, and SA227-TT(300) |
| 2002-08-05 |  | Bombardier | DHC-8-400, -401, and -402 Series |
| 2002-08-06 |  | Boeing | 777-200, -300 Series |
| 2002-08-07 |  | Boeing | 767-200, -300, and -300F Series |
| 2002-08-51 | E | Airbus | A300 B2 and B4 Series |
| 2002-08-52 | E | Boeing | 737-600, -700, and -700C Series |

Biweekly 2002-09

| 2002-04-11 | COR, S 2000-08-10 | General Electric | Engine: GE90-76B/ -77B/ -85B/ -90B/ -94B Series Turbofan |
| --- | --- | --- | --- |
| 2002-06-01 | S 2000-10-16 | Airbus | A319, A320, and A321 Series |
| 2002-06-53 | FR | Airbus | A319, A320, A321, A330, and A340 Series |
| 2002-08-02 | COR, S 2001-20-14 | Fairchild Aircraft | SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, SA227-TT, and SA227-TT(300) |
| 2002-08-08 |  | Bombardier | CL-600-2B16 (CL-601-3R), and CL-600-2B16 (CL-604) Series |
| Biweekly 2002-09 continued |
| 2002-08-09 |  | McDonnell Douglas | DC-9-31 |
| 2002-08-10 |  | Boeing | 747 Series |
| 2002-08-11 | S 2000-01-13 | Pratt & Whitney | Engine: JT9D-3A, -7, -7A, -7H, -7AH, -7F, -7J, -20, -20J, -59A, -70A, -7Q, -7Q3, -7R4D, -7R4D1, -7R4E, -7R4E1, -7R4E4, -7R4G2, and -7R4H1 Series Turbofan |
| 2002-08-12 |  | Airbus | A330 and A340 Series |
| 2002-08-13 |  | Airbus | A319, A320, and A321 Series |
| 2002-08-14 |  | Airbus | A300 B2, B4, A300 B4-600, B4-600R, F4-600R (collectively called A300-600), and A310 Series |
| 2002-08-15 |  | Boeing | 767 Series |
| 2002-08-17 |  | McDonnell Douglas | DC-10-10, DC-10-10F, DC-10-15, DC-10-30, DC-10-30F, and DC-10-30F (KC10A and KDC-10) |
| 2002-08-18 |  | Embraer | EMB-135 and -145 Series |
| 2002-08-20 |  | Boeing | 737-600, -700, -700C, and -800 Series |
| 2002-08-21 | S 2001-17-04 | Embraer | EMB-135 and -145 Series |
| 2002-08-51 | FR | Airbus | A300 B2 and B4 Series |
| 2002-08-52 | FR | Boeing | 737-600, -700, -700C Series |
| 2002-09-01 |  | Pratt & Whitney | Engine: PW4090, PW4090-3, PW4074D, PW4077D, PW4090D, and PW4098 Turbofan |
| 2002-09-02 |  | Rolls-Royce, plc | Engine: Tay 650-15 and 651-54 Turbofan |
| 2002-09-05 |  | Bombardier | CL-600-2B19 Series |
| 2002-09-06 |  | McDonnell Douglas | DC-9-81 (MD-81), DC-9-82 (MD-82), DC-9-83 (MD-83), and MD-88 |
| 2002-09-07 |  | McDonnell Douglas | DC-9-81 (MD-81), DC-9-82 (MD-82), DC-9-83 (MD-83), and MD-88 |

Biweekly 2002-10

| 2002-07-09 | COR, S 99-04-22 | Boeing | 727 Series |
| --- | --- | --- | --- |
| 2002-09-10 |  | CFE Company | Engine: CFE738-1-1B Turbofan |
| 2002-10-01 |  | McDonnell Douglas | MD-90-30 |
| 2002-10-02 |  | Boeing | 757 Series |
| 2002-10-03 |  | McDonnell Douglas | DC-9-81 (MD-81), DC-9-82 (MD-82), DC-9-83 (MD-83), DC-9-87 (MD-87), MD-88, and Model MD-90-30 |
| 2002-10-04 |  | General Electric Company | Engine: CF6-80E1A2 |

Biweekly 2002-11

| 2002-08-06 | COR | Boeing | 777-200 and -300 Series |
| --- | --- | --- | --- |
| 2002-10-06 |  | Airbus | A319, A320, and A321 Series |
| 2002-10-07 |  | Pratt & Whitney | Engine: JT9D-59A, -70A, -7Q, and -7Q3 Turbofan |
| 2002-10-08 |  | General Electric | Engine: CF6-80E1 Series |
| 2002-10-09 |  | Gulfstream Aerospace | Galaxy and Gulfstream 200 |
| 2002-10-10 | S 93-08-12 | Boeing | 747 Series |
| 2002-10-11 | S 84-20-03 R1 | Boeing | 737-100, -200, -200C, -300, -400, and -500 series |
| 2002-10-12 |  | Boeing | 737-100, -200, -200C, -300, -400, and -500 Series |
| 2002-10-15 |  | Rolls-Royce plc | Engine: RB211 Trent 875, 877, 884, 892, 892B, and 895 Series Turbofan |

Biweekly 2002-12

| 2002-08-19 | S 2002-06-51 | Bombardier | CL-600-2C10 (Regional Jet Series 700 and 701) Series |
| --- | --- | --- | --- |
| 2002-11-04 | S 97-16-06 | Airbus | A300 B4-600, A300 B4-600R Series, and A300 F4-605R |
| 2002-11-06 | S 2000-19-08 | Boeing | 777 Series |
| 2002-11-08 |  | Rolls-Royce plc | Engine: RB211 Trent 875, 877, 884, 892, 892B, and 895 series Turbofan |
| 2002-11-11 |  | Boeing | 767-200, -300, and -300F Series |
| 2002-12-01 |  | BAe Systems | Jetstream 4101 |
| 2002-12-05 |  | Boeing | 767 Series |
| 2002-12-06 | S 2000-21-09 | Pratt & Whitney | Engine: PW2037, PW2040, PW2037M, PW2240, PW2337, PW2043, PW2643, and PW2143 series Turbofan |
| 2002-12-08 |  | Honeywell International | Engine: ALF502 and LF507 Series Turbofan |

Biweekly 2002-13

| 99-27-16 | R1 | CFE Company | Engine: CFE738-1-1B turbofan |
| --- | --- | --- | --- |
| 2002-05-02 | COR, S 2000-03-03 R1 | General Electric Company | Engine: CF34-3A1 and -3B1 series turbofan |
| 2002-12-04 |  | Boeing | 757-200, 757-200CB, 757-200PF, 767-200, 767-300, and 767-300F series |
| 2002-12-09 |  | Honeywell International Inc. | Engine: TPE331-11U, -12B, -12JR, -12UA, -12UAR, and -12UHR series turboprop |
| 2002-12-10 |  | McDonnell Douglas | MD-90-30 |
| 2002-12-11 |  | Bombardier, Inc. | DHC-8-100, -200 and –300 series |
| 2002-12-12 | S 99-16-04 | Bombardier, Inc. | CL-215-1A10 and CL-215-6B11 series |
| 2002-12-13 |  | Boeing | 727 series |
| 2002-12-15 | S 2001-20-13 | Pratt & Whitney | Engine: PW4052, PW4056, PW4060, PW4062, PW4152, PW4156A, PW4158, PW4460, and PW4462 turbofan |
| 2002-13-01 |  | McDonnell Douglas | MD-90-30 |
| 2002-13-03 | S 2000-12-01 | CFM International | Engine: CFM56-2, -2A, -2B, -3, -3B, -3C, -5, -5B, -5C, and -7B series turbofan |

Biweekly 2002-14

| 2002-09-02 | COR | Rolls-Royce, plc. | Engine: Tay 650-15 and 651-54 Turbofan |
| --- | --- | --- | --- |
| 2002-10-08 | COR | General Electric Company | Engine: CF6-80E1 series Turbofan |
| 2002-13-07 |  | Honeywell, Inc. | Appliance: Inertial Reference Unit (IRU) |
| 2002-13-09 | S 2000-21-07 | Pratt & Whitney | Engine: JT8D-200 series Turbofan |
| 2002-13-10 |  | McDonnell Douglas | DC-10-10, -10F, -15, -30, -30F, -30F (KC10A and KDC-10), -40, -40F, MD-10-10F, -30F, MD-11 and -11F |
| 2002-13-12 | S 2001-24-15 | McDonnell Douglas | DC-9-10, -30, -30F, and -40 series, and C-9 |
| 2002-14-02 |  | Boeing | 767-300 series |
| 2002-14-16 |  | McDonnell Douglas | 717-200 |

Biweekly 2002-15

| 2002-13-09 | COR S 2000-21-07 | Pratt & Whitney | Engine: JT8D-200 Series Turbofan |
| --- | --- | --- | --- |
| 2002-14-03 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-04 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-05 | S 99-26-03 C1 | McDonnell Douglas | MD-11 |
| 2002-14-06 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-07 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-08 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-09 | S 2000-03-15 | McDonnell Douglas | MD-11 and -11F |
| 2002-14-10 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-11 | S 2000-24-13 | McDonnell Douglas | MD-11 and -11F |
| 2002-14-12 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-13 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-14 |  | McDonnell Douglas | MD-11 and -11F |
| 2002-14-15 | S 2000-14-18 | McDonnell Douglas | MD-11 and -11F |
| 2002-14-19 |  | Rockwell Collins | Appliance: Air Data Computers (ADC) |
| 2002-14-20 | COR | Boeing | 737-600, -700, -800, and -900 Series |
| 2002-14-21 | S 99-03-08 | Boeing | 737-600, -700, and -800 Series |
| 2002-14-23 |  | Embraer | EMB-135 and -145 Series |
| 2002-14-24 |  | Cessna | 650 |
| 2002-14-25 | S 2002-08-18 | Embraer | EMB-135 and -145 Series |
| 2002-14-27 | S 94-25-03 | Fokker | F.28 Mark 0070, 0100, 1000, 2000, 3000, and 4000 Series |
| 2002-15-02 |  | Hamilton Sundstrand Power Sys. | Appliance: Auxiliary Power Units (APU's) |
| 2002-15-03 | S 2002-05-51 | Hamilton Sundstrand | Propellers: 568F-1 |

BW 2002-15

PRATT & WHITNEY

AIRWORTHINESS DIRECTIVE

ENGINE

LARGE AIRCRAFT

CORRECTION: [Federal Register: July 26, 2002 (Volume 67, Number 144); Page 48753; www.access.gpo.gov/su_docs/aces/aces140.html]

AD 2002-13-09  Pratt & Whitney: Amendment 39-12797. Docket No. 98ANE-43AD. Supersedes AD 2000-21-07, Amendment 39-11939.

Applicability: Pratt & Whitney (PW) JT8D-200 series turbofan engines, installed on but not limited to McDonnell Douglas MD-80 series airplanes.

Note 1: This airworthiness directive (AD) applies to each engine identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For engines that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless already done.

To prevent critical life-limited rotating engine part failure, which could result in an uncontained engine failure and damage to the airplane, do the following:

Inspections

(a) Within the next 30 days after the effective date of this AD, revise the Time Limits Section (TLS) of the JT8D-200 Turbofan Engine Manual, and for air carrier operations revise the approved continuous airworthiness maintenance program, by adding the following:

''Critical Life Limited Part Inspection

A. Inspection Requirements:

(1) This section contains the definitions for individual engine piece-parts and the inspection procedures, which are necessary, when these parts are removed from the engine.

(2) It is necessary to do the inspection procedures of the piece-parts in Paragraph B when:

(a) The part is removed from the engine and disassembled to the level specified in paragraph B and

(b) The part has accumulated more than 100 cycles since the last piece part inspection, provided that the part is not damaged or related to the cause of its removal from the engine.

(3) The inspections specified in this section do not replace or make unnecessary other recommended inspections for these parts or other parts.

B. Parts Requiring Inspection.

Note: Piece part is defined as any of the listed parts with all the blades removed.

| Description | Engine manual |
| --- | --- |
|  | Section | Inspection No. |
| Hub (Disk), 1st Stage Compressor: |  |  |
| Hub Detail—All P/N’s. | 72–33–31 | –02, –03 |
| Hub Assembly—All P/N’s. | 72–33–31 | –02, –03 |
| Disk, 13th Stage Compressor—All P/N’s. | 72–36–47 | –02 |
| HP Turbine, First Stage: |  |  |
| Rotor Assembly—All P/N’s. | 72–52–02 | –04 |
| Disk—All P/N’s | 72–52–02 | –03 |
| Disk, 2nd Stage Turbine—All P/N’s. | 72–53–16 | –02 |
| Disk, 3rd Stage Turbine—All P/N’s. | 72–53–17 | –02 |
| Disk, 4th Stage Turbine—All P/N’s. | 72–53–18 | –02’’ |

(b) Except as provided in paragraph (c) of this AD, and notwithstanding contrary provisions in section 43.16 of the Federal Aviation Regulations (14 CFR 43.16), these mandatory inspections must be performed using the TLS of the PW JT8D-200 Turbofan Engine Manual.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Engine Certification Office (ECO). Operators must submit their requests through an appropriate FAA Principal Maintenance Inspector (PMI), who may add comments and then send it to the ECO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the ECO.

Ferry Flights

(d) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be done.

Continuous Airworthiness Maintenance Program

(e) FAA-certificated air carriers that have an approved continuous airworthiness maintenance program in accordance with the record keeping requirement of Sec. 121.369(c) of the Federal Aviation Regulations (14 CFR 121.369(c)) must maintain records of the mandatory inspections that result from revising the TLS of the PW JT8D-200 Turbofan Engine Manual, and the air carrier's continuous airworthiness program. Alternatively, certificated air carriers may establish an approved system of record retention that provides a method for preservation and retrieval of the maintenance

records that include the inspections resulting from this AD, and include the policy and procedures for implementing this alternate method in the air carrier's maintenance manual required by Sec. 121.369(c) of the Federal Aviation Regulations (14 CFR 121.369(c)); however, the alternate system must be accepted by the appropriate PMI and require the maintenance records be maintained either indefinitely or until the work is repeated. Records of the piece-part inspections are not required under Sec. 121.380 (a)(2)(vi) of the Federal Aviation Regulations (14 CFR 121.380(a)(2)(vi)). All other operators must maintain the records of mandatory inspections required by the applicable regulations governing their operations.

Note 3: The requirements of this AD have been met when the engine manual changes are made and air carriers have modified their continuous airworthiness maintenance plans to reflect the requirements in the PW JT8D-200 Turbofan Engine Manual.

Effective Date

(f) This amendment becomes effective on December 30, 2002.

FOR FURTHER INFORMATION CONTACT: Christopher Spinney, Aerospace Engineer, Engine Certification Office, FAA, Engine and Propeller Directorate, 12 New England Executive Park, Burlington, MA; telephone (781) 238-7175; fax (781) 238-7199.

Issued in Burlington, Massachusetts, on June 18, 2002.

Jay J. Pardee,

Manager, Engine and Propeller Directorate, Aircraft Certification Service.

[FR Doc. 02-16535 Filed 7-2-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-03  McDonnell Douglas: Amendment 39-12803. Docket 2002-NM-168-AD.

Applicability: Model MD-11 and -11F airplanes listed as Group 1 or Group 2 airplanes in Boeing Alert Service Bulletin MD11-57A067, including Appendices A and B, dated July 10, 2002; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To detect and correct loose preload-indicating (PLI) washers or cracked or corroded nuts of the lower bolts of the inboard flap outboard hinge, which could result in separation of the inboard flap outboard hinge from the wing structure and consequent reduced controllability of the airplane, accomplish the following:

Inspection

(a) At the applicable time specified in paragraph (a)(1) or (a)(2) of this AD, do a detailed inspection (including removing sealant from the head and nut sides of both bolt assemblies) of the nuts and PLI washers of the lower bolts of the inboard flap outboard hinge to detect discrepancies (including loose PLI washers or cracked or corroded nuts, as applicable), in accordance with Boeing Alert Service Bulletin MD11-57A067, including Appendices A and B, dated July 10, 2002, except as required by paragraphs (b) and (c) of this AD. Before further flight thereafter, do applicable follow-on and corrective actions (including performing a magnetic particle inspection of the bolt to detect cracking and corrosion, replacing discrepant parts with new Inconel and/or alloy steel bolts and nuts and new PLI washers, and applying sealant, as applicable); and, within 600 flight cycles, replace discrepant bolts, nuts, and washers with new parts, as applicable; in accordance with the alert service bulletin.

(1) For Group 1 airplanes: Inspect within 30 days after the effective date of this AD.

(2) For Group 2 airplanes: Inspect within 60 days after the effective date of this AD.

Note 2: For the purposes of this AD, a detailed inspection is defined as: ''An intensive visual examination of a specific structural area, system, installation, or assembly to detect damage, failure, or irregularity. Available lighting is normally supplemented with a direct source of good lighting at intensity deemed appropriate by the inspector. Inspection aids such as mirror, magnifying lenses, etc., may be used. Surface cleaning and elaborate access procedures may be required.''

Exceptions to Paragraph (a) Requirements

(b) Where Boeing Alert Service Bulletin MD11-57A067, including Appendices A and B, dated July 10, 2002, specifies that testing for looseness of the PLI washers may be accomplished by the use of a wiggle tool, ''or equivalent'': Either the wiggle tool must be used, or the test must be accomplished in accordance with a method approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA.

(c) Where Boeing Alert Service Bulletin MD11-57A067, including Appendices A and B, dated July 10, 2002, specifies to contact Boeing for ''additional examination recommendations'': Before further flight, these actions, if accomplished, must be performed in accordance with a method approved by the Manager, Los Angeles ACO. For such a method to be approved by the Manager, Los Angeles ACO, as required by this paragraph, the Manager's approval letter must specifically refer to this AD.

Reporting Requirement

(d) At the applicable time specified in paragraph (d)(1) or (d)(2) of this AD: Send a report of the results (both positive and negative) of the inspection nuts and PLI washers of the lower bolts of the inboard flap outboard hinge to the Manager, Los Angeles ACO, FAA, 3960 Paramount Boulevard, Lakewood, CA 90712-4137, fax (562) 627-5210. The report must include the factory serial number of the airplane; inspection results for all four bolts; a description of any discrepancies found; the part numbers for the bolt, nut, and PLI washers; and the total number of landings and flight hours accumulated on the airplane. Information collection requirements contained in this AD have been approved by the Office of Management and Budget (OMB) under the provisions of the Paperwork Reduction Act of 1980 (44 U.S.C. 3501 et seq.) and have been assigned OMB Control Number 2120-0056.

(1) For airplanes on which the inspection is accomplished after the effective date of this AD: Submit the report within 10 days after performing the inspection required by paragraph (a) of this AD.

(2) For airplanes on which the inspection has been accomplished prior to the effective date of this AD: Submit the report within 10 days after the effective date of this AD.

Alternative Methods of Compliance

(e) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles ACO. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(f) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(g) Except as required by paragraphs (b) and (c) of this AD: The actions must be done in accordance with Boeing Alert Service Bulletin MD11-57A067, including Appendices A and B, dated July 10, 2002. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(h) This amendment becomes effective on August 2, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Ronald Atmur, Aerospace Engineer, Airframe Branch, ANM-120L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5224; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Editor/Writer; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 10, 2002.

Vi Lipski,

Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-18024 Filed 7-17-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-04  McDonnell Douglas: Amendment 39-12804. Docket 2001-NM-53-AD.

Applicability: Model MD-11 and -11F airplanes, as listed in Boeing Service Bulletin MD11-26-037, dated November 8, 2000; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent chafing and possible damage to the wiring of the Firex bottle discharge cartridge of the No. 2 engine, which could result in improper distribution of the fire extinguishing agent within the No. 2 engine in the event of a fire, accomplish the following:

General Visual Inspection

(a) Within 15 months after the effective date of this AD, do a general visual inspection of the wiring of the Firex bottle discharge cartridge of the No. 2 engine at station Y=2163.00 bulkhead for chafing on adjacent structure and damaged wiring, per Boeing Service Bulletin MD11-26-037, dated November 8, 2000.

Note 2: For the purposes of this AD, a general visual inspection is defined as: ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

Note 3: Where there are differences between the referenced service bulletin and the AD, the AD prevails.

Condition 1 (No Chafing or Damaged Wiring)

(1) If no chafing or damaged wiring is detected, no further action is required by this AD.

Condition 2 (Chafing with No Damaged Wiring)

(2) If any chafing with no damaged wiring is detected, before further flight, reposition wires, per the service bulletin.

Condition 3 (Chafing with Damaged Wiring)

(3) If any chafing with damaged wiring is detected, before further flight, repair damaged wires and reposition wires, per the service bulletin.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 4: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with Boeing Service Bulletin MD11-26-037, dated November 8, 2000. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17526 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-05  McDonnell Douglas: Amendment 39-12805. Docket 2001-NM-55-AD. Supersedes AD 99-26-03 C1, Amendment 39-11463.

Applicability: Model MD-11 airplanes, as listed in Boeing Service Bulletin MD11-24-184, dated February 22, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (d)(1) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent damage to the wire assembly terminal lugs and power feeder cables due to the accumulated effects over time from overheating of the power feeder cables on the No. 3 and 4 galley load control unit (GLCU), which could result in smoke and fire in the central accessory compartment, accomplish the following:

Restatement of Requirements of AD 99-26-03 C1

Repetitive Inspections and Replacement, If Necessary

(a) For airplanes listed in McDonnell Douglas Alert Service Bulletin MD11-24A160, Revision 01, dated November 11, 1999: Within 60 days after January 4, 2000 (the effective date of AD 99-26-03 C1, amendment 39-11463), perform a general visual inspection of the power feeder cables, terminal strip, fuseholder, and fuses of the GLCU within the No. 3 bay electrical power center to detect damage (i.e., discoloration of affected parts or loose attachments), in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A160, dated August 30, 1999; or Revision 01, dated November 11, 1999.

Note 2: For the purposes of this AD, a general visual inspection is defined as: ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in

the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

(1) If no damage is detected during any inspection required by this AD, repeat the general visual inspection thereafter at intervals not to exceed 600 flight hours.

(2) If any damage is detected during any inspection required by this AD, prior to further flight, replace the power feeder cables, fuseholder, and/or fuses, as applicable, in accordance with the service bulletin. Repeat the general visual inspection thereafter at intervals not to exceed 600 flight hours.

New Actions Required By This AD

Repetitive Inspections and Replacement, If Necessary

(b) For airplanes having serial numbers 547 and 554: Within 60 days after the effective date of this AD, do the actions required by paragraphs (a), (a)(1), and (a)(2) of this AD, as applicable.

Replacement

(c) Within 12 months after the effective date of this AD, replace the electrical wiring of the galley in the electrical power center in bays 1, 2, and 3 with larger gage cable assemblies, in accordance with Boeing Service Bulletin MD11-24-184, dated February 22, 2001. Accomplishment of the replacement constitutes terminating action for the repetitive inspection requirements of paragraphs (a) and (b) of this AD.

Alternative Methods of Compliance

(d)(1) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

(2) Alternative methods of compliance, approved previously in accordance with ADs 99-26-03 and 99-26-03 C1, both having amendment 39-11463, are approved as alternative methods of compliance with this AD.

Special Flight Permits

(e) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(f) The actions shall be done in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A160, dated August 30, 1999, or McDonnell Douglas Alert Service Bulletin MD11-24A160, Revision 01, dated November 11, 1999; and Boeing Service Bulletin MD11-24-184, dated February 22, 2001; as applicable.

(1) The incorporation by reference of Boeing Service Bulletin MD11-24-184, dated February 22, 2001, is approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51.

(2) The incorporation by reference of McDonnell Douglas Alert Service Bulletin MD11-24A160, dated August 30, 1999; and McDonnell Douglas Alert Service Bulletin MD11-24A160, Revision 01, dated November 11, 1999; was approved previously by the Director of the Federal Register as of January 4, 2000 (64 FR 71001, December 20, 1999).

(3) Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(g) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17527 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-06  McDonnell Douglas: Amendment 39-12806. Docket 2001-NM-59-AD.

Applicability: Model MD-11 and -11F airplanes, as listed in Boeing Service Bulletin MD11-24-197, dated May 16, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

Installation

(a) Within 18 months after the effective date of this AD, install protective sleeving on the right emergency wire assembly of the overhead switch panel, per Boeing Service Bulletin MD11-24-197, dated May 16, 2001.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The installation shall be done in accordance with Boeing Service Bulletin MD11-24-197, dated May 16, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17528 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-07  McDonnell Douglas: Amendment 39-12807. Docket 2001-NM-60-AD.

Applicability: Model MD-11 and -11F airplanes, as listed in Boeing Alert Service Bulletin MD11-24A036, Revision 01, dated May 21, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent chafing and compression of electrical wiring at the upper track mod blocks on the flight compartment floor beams in the avionics compartment beneath the Captain's and First Officer's seats, which could result in electrical arcing and consequent smoke and/or fire in the cockpit, accomplish the following:

Relocation of Mod Block Tracks

(a) Within 1 year after the effective date of this AD, relocate the mod block tracks on the flight compartment floor beams in the avionics compartment beneath the Captain's and First Officer's seats, per Boeing Alert Service Bulletin MD-1124A036, Revision 01, dated May 21, 2001.

Note 2: Accomplishment of the relocation per McDonnell Douglas Service Bulletin MD11-24-036, dated May 8, 1992, before the effective date of this AD, is considered acceptable for compliance with the requirements of this AD.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with Boeing Alert Service Bulletin MD11-24A036, Revision 01, dated May 21, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17534 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-08  McDonnell Douglas: Amendment 39-12808. Docket 2001-NM-61-AD.

Applicability: Model MD-11 and -11F airplanes, as listed in Boeing Alert Service Bulletin MD11-23A046, Revision 01, dated May 21, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent chafing of wiring in the avionics compartment, which could result in electrical arcing and consequent smoke and/or fire in the cockpit, accomplish the following:

(a) Within 1 year after the effective date of this AD, do a general visual inspection to detect discrepancies (i.e., chafing, improper routing or bundle support, missing tie wraps, improper clearance) of wire bundles in the avionics compartment in the vicinity of the pedestal extension area of the First Officer's seat, per the Accomplishment Instructions of Boeing Alert Service Bulletin MD11-23A046, Revision 01, dated May 21, 2001. If any discrepancy is detected, before further flight, perform the applicable corrective actions (i.e., repair, replacement of damaged wires with new wires, reroute wire bundle, and tie wrap bundle) per the Accomplishment Instructions of the service bulletin.

Note 2: For the purposes of this AD, a general visual inspection is defined as: ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

Note 3: Accomplishment of the inspections and corrective actions, if necessary, per McDonnell Douglas Service Bulletin MD11-23-046, dated March 17, 1995, before the effective date of this AD, is considered acceptable for compliance with the requirements of this AD.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 4: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with Boeing Alert Service Bulletin MD11-23A046, Revision 01, dated May 21, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17535 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-09  McDonnell Douglas: Amendment 39-12809. Docket 2001-NM-63-AD. Supersedes AD 2000-03-15, Amendment 39-11574.

Applicability: Model MD-11 and MD-11F airplanes, as listed in McDonnell Douglas Alert Service Bulletin MD11-24A150, dated March 25, 1999; and McDonnell Douglas Alert Service Bulletin MD11-24A178, Revision 01, dated December 17, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent electrical arcing caused by power feeder cable terminal lugs grounding against terminal strip support brackets, which could result in smoke and fire in the main cabin or avionics compartment, accomplish the following:

Restatement of Certain Requirements of AD 2000-03-15

Replacement of Terminal Strips and Supports

(a) For airplanes listed in the effectivity of McDonnell Douglas Alert Service Bulletin MD11-24A150, dated March 25, 1999, on which the modification specified in McDonnell Douglas Service Bulletin MD11-24-085, dated August 1, 1995, has not been accomplished: Within 1 year after March 23, 2000 (the effective date of AD 2000-03-15, amendment 39-11574), replace the existing terminal strips and supports above the main cabin at station Y=5-32.000 with new terminal strips and supports in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A150, dated March 25, 1999.

New Actions Required by This AD

Replacement, Inspection, and Corrective Action If Necessary

(b) For airplanes listed in the effectivity of McDonnell Douglas Alert Service Bulletin MD11-24A178, Revision 01, dated December 17, 2001: Within 18 months after the effective date of this AD, do the actions specified in paragraphs (b)(1) and (b)(2) of this AD per the service bulletin.

(1) Replace the applicable terminal strips in the avionics compartment with new terminal strips (including inspecting wires for damage, repairing any damaged wire, and removing the nameplate); and

(2) Perform a general visual inspection to detect arcing damage of the surrounding structure of the terminal strips and electrical cables in the avionics compartment. If any damage is detected, before further flight, repair or replace any damaged component with a new component, per the service bulletin; except if the type of structural material of the surrounding structure that has been affected is not covered in the Structural Repair Manual, repair per a method approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA.

Note 2: For the purposes of this AD, a general visual inspection is defined as ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or drop-light, and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

Note 3: Accomplishment of the replacement, inspection, and corrective action, before the effective date of this AD, per McDonnell Douglas Alert Service Bulletin MD11-24A178, dated May 14, 2001, is considered acceptable for compliance with the applicable actions specified in this amendment.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles ACO, FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 4: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(d) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(e) Except as provided by paragraph (b)(2) of this AD, the actions shall be done in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A150, dated March 25, 1999; and McDonnell Douglas Alert Service Bulletin MD11-24A178, Revision 01, dated December 17, 2001; as applicable.

(1) The incorporation by reference of McDonnell Douglas Alert Service Bulletin MD11-24A178, Revision 01, dated December 17, 2001, is approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51.

(2) The incorporation by reference of McDonnell Douglas Alert Service Bulletin MD11-24A150, dated March 25, 1999, was approved previously by the Director of the Federal Register as of March 23, 2000 (65 FR 8025, February 17, 2000).

(3) Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(f) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17536 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-10  McDonnell Douglas: Amendment 39-12810. Docket 2001-NM-64-AD.

Applicability: Model MD-11 and -11F airplanes, certificated in any category; equipped with United Technologies Pratt & Whitney Model PW4460 or PW4462 engines, engine buildup units having neutral quick engine change, cum units 4 through 240 inclusive and serial numbers 5166001 through 5213003 inclusive.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent arcing of the integrated drive generator (IDG) wire harness, which could result in smoke and/or fire in the area of the forward engine mount bolt retainer and/or fire detector responder, accomplish the following:

Replacement and Modification

(a) Within 1 year after the effective date of this AD, replace the wire harness support bracket of the IDG of the forward engine mounts with a new support bracket, and modify the angle of the bracket near the oil filter (i.e., cut and grind flanges, deburr edges, fusion weld flanges, and reidentify bracket), per Boeing Alert Service Bulletin MD11-71A086, Revision 01, dated May 21, 2001.

Note 2: Boeing Alert Service Bulletin MD11-71A086 references United Technologies Pratt & Whitney Service Bulletin PW4MD11 71-107, dated May 15, 1996, as an additional source of service information for accomplishing the proposed replacement and modification.

Spares

(b) As of the effective date of this AD, no United Technologies Pratt & Whitney Model PW4460 or PW4462 engines, engine buildup units having neutral quick engine change, cum units 4 through 240 inclusive and serial numbers 5166001 through 5213003 inclusive, shall be installed on any airplane unless the requirements of paragraph (a) of this AD have been done.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permit

(d) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(e) The replacement and modification shall be done in accordance with Boeing Alert Service Bulletin MD11-71A086, Revision 01, dated May 21, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(f) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17529 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-11  McDonnell Douglas: Amendment 39-12811. Docket 2001-NM-65-AD. Supersedes AD 2000-24-13, Amendment 39-12020.

Applicability: Model MD-11 and -11F airplanes, as listed in McDonnell Douglas Alert Service Bulletin MD11-24A138, Revision 01, dated June 5, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent arcing and heat damage to the attachment points of the main external and galley power receptacle ground wire, insulation blankets outboard and aft of the receptacle area, and adjacent power cables, which could result in smoke and fire in the forward cargo compartment, accomplish the following:

Replacement and Rerouting

(a) Within 12 months after January 8, 2001 (the effective date of AD 2000-24-13, amendment 39-12020), accomplish the actions specified in paragraph (a)(1) or (a)(2) of this AD, as applicable, in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A138, dated April 3, 2000, or Revision 01, dated June 5, 2001. As of the effective date of this AD, only Revision 01 of the service bulletin shall be used.

(1) For Group 1 airplanes listed in the original version of the service bulletin, excluding fuselage number 0456: Replace the ground support brackets with new brackets and reroute the ground cables of the galley external power and main external power.

(2) For Group 2 airplanes listed in the original version of the service bulletin and fuselage number 0456: Replace the ground support bracket and reroute the ground cables of the main external power.

Inspection and Corrective Actions, If Necessary

(b) Within 12 months after the effective date of this AD, accomplish the actions specified in paragraph (b)(1) or (b)(2) of this AD, as applicable, in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A138, Revision 01, dated June 5, 2001.

(1) For Group 3 airplanes listed in Revision 01 of the service bulletin: Do a general visual inspection of the ground cables of the main external power and galley external power for excessive length. If any cable length is excessive, before further flight, do applicable corrective actions (e.g., cut cable assembly to correct length and install a terminal on the cut end of the cable) per Condition 2 of Figure 3 of the service bulletin.

(2) For Group 4 airplanes listed in Revision 01 of the service bulletin: Do a general visual inspection of the ground cables of the main external power for excessive length. If any cable length is excessive, before further flight, do applicable corrective actions (e.g., cut cable assembly to correct length and install a terminal on the cut end of the cable) per Condition 2 of Figure 4 of the service bulletin.

Note 2: For the purposes of this AD, a general visual inspection is defined as: ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(d) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(e) The actions shall be done in accordance with McDonnell Douglas Alert Service Bulletin MD11-24A138, dated April 3, 2000, or McDonnell Douglas Alert Service Bulletin MD11-24A138, Revision 01, dated June 5, 2001; as applicable.

(1) This incorporation by reference of McDonnell Douglas Alert Service Bulletin MD11-24A138, Revision 01, dated June 5, 2001, is approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51.

(2) The incorporation by reference of McDonnell Douglas Alert Service Bulletin MD11-24A138, dated April 3, 2000, was approved previously by the Director of the Federal Register as of January 8, 2001 (65 FR 75616, December 4, 2000).

(3) Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(f) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17530 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-12  McDonnell Douglas: Amendment 39-12812. Docket 2001-NM-157-AD.

Applicability: Model MD-11 and -11F airplanes, as listed in Boeing Alert Service Bulletin MD11-28A058, Revision 01, dated March 29, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent chafing of the wiring in a cutout area in the wing fuel control panel due to improperly routed wiring, which could result in electrical arcing in an abnormal fuel vapor zone and consequent possible ignition of the fuel vapor, accomplish the following:

Inspection and Corrective Action, If Necessary

(a) Within 6 months after the effective date of this AD, do a general visual inspection of the wiring in the fuel control panel of the wings for chafing damage and for proper routing of the wiring, per Boeing Alert Service Bulletin MD11-28A058, Revision 01, dated March 29, 2001.

Note 2: For the purposes of this AD, a general visual inspection is defined as: ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

(1) Condition 1. If no chafing damage is found and if the wiring is NOT routed into the cutout area of the fuel control panel, no further work is required by this AD.

(2) Condition 2. If no chafing damage is found and if the wiring is routed into the cutout area of the fuel control panel, before further flight, revise the wire routing out of the cutout area in the fuel control panel, per the service bulletin.

(3) Condition 3. If any chafing damage is found and if the wiring is routed into the cutout area of the fuel control panel, before further flight, replace any damaged wire with a new wire, and revise the wire routing out of the cutout area in the fuel control panel, per the service bulletin.

Note 3: Accomplishment of the actions specified in McDonnell Douglas service Bulletin MD11-28-058, dated January 3, 1995, before the effective date of this AD, is considered acceptable for compliance with the requirements of this AD.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 4: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with Boeing Alert Service Bulletin MD11-28A058, Revision 01, dated March 29, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17531 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-13  McDonnell Douglas: Amendment 39-12813. Docket 2001-NM-158-AD.

Applicability: Model MD-11 and -11F airplanes, as listed in Boeing Alert Service Bulletin MD11-52A035, Revision 02, dated March 12, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent failure of the wire assemblies and damage of a ballast of a light fixture, and consequent smoke and/or fire in the forward cargo compartment, accomplish the following:

Installation of Clipnut and Bracket and Revision of Routing of Wiring

(a) Within 1 year after the effective date of this AD, install a clipnut and bracket and revise the routing of the wire assembly of the forward lower cargo door, per Boeing Alert Service Bulletin MD11-52A035, Revision 02, dated March 12, 2001.

Note 2: Accomplishment of the actions specified in McDonnell Douglas Service Bulletin MD11-52-035, Revision 01, dated March 9, 1998, before the effective date of this AD, is considered acceptable for compliance with the requirements of this AD.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with Boeing Alert Service Bulletin MD11-52A035, Revision 02, dated March 12, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17532 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-14  McDonnell Douglas: Amendment 39-12814. Docket 2001-NM-159-AD.

Applicability: Model MD-11 and -11F airplanes equipped with General Electric tail engine buildup units (EBU), as listed in Boeing Alert Service Bulletin MD11-24A095, Revision 01, dated March 16, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent chafing and arcing of the wire harness of the integrated drive generator (IDG) due to inadequate support, which could result in smoke and/or fire in the area of the forward engine mount, accomplish the following:

Installation of New Support Bracket

(a) Within 1 year after the effective date of this AD, install a new support bracket with a clamp and screw to support the wire harness of the IDG, per Boeing Alert Service Bulletin MD11-24A095, Revision 01, dated March 16, 2001.

Note 2: Accomplishment of the installation per McDonnell Douglas Service Bulletin MD11-24-095, dated January 29, 1996, before the effective date of this AD, is considered acceptable for compliance with the requirements of paragraph (a) of this AD.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The installation shall be done in accordance with Boeing Alert Service Bulletin MD11-24A095, Revision 01, dated March 16, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17533 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

MCDONNELL DOUGLAS

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-15  McDonnell Douglas: Amendment 39-12815. Docket 2002-NM-33-AD. Supersedes AD 2000-14-18, Amendment 39-11829.

Applicability: Model MD-11 and -11F airplanes, as listed in McDonnell Douglas Alert Service Bulletin MD11-25A227, Revision 01, dated October 31, 2001; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To ensure that the powered roller pans are positioned properly, accomplish the following:

(a) Within 18 months after the effective date of this AD, accomplish the actions specified in paragraphs (a)(1), (a)(2), and (a)(3) of this AD per McDonnell Douglas Alert Service Bulletin MD11-25A227, Revision 01, dated October 31, 2001.

Inspection

(1) Perform a general visual inspection of the powered drive unit power wires within three feet of each affected powered drive unit termination for mechanical damage. If any damaged wire is detected, before further flight, repair the damaged wire.

Note 2: For the purposes of this AD, a general visual inspection is defined as: "A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

Revise Wire Harnesses, Splice Wire, and Route and Install Parts

(2) Revise the wire harnesses, splice any additional length wire, and route and install parts.

Replacement

(3) Replace the floor panels with new and retained floor panels.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 3: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with McDonnell Douglas Alert Service Bulletin MD11-25A227, Revision 01, dated October 31, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Aircraft Group, Long Beach Division, 3855 Lakewood Boulevard, Long Beach, California 90846, Attention: Data and Service Management, Dept. C1-L5A (D800-0024). Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on August 5, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Brett Portwood, Aerospace Engineer, Systems and Equipment Branch, ANM-130L, FAA, Transport Airplane Directorate, Los Angeles Aircraft Certification Office, 3960 Paramount Boulevard, Lakewood, California 90712-4137; telephone (562) 627-5350; fax (562) 627-5210.

Other Information: Sandi Carli, Airworthiness Directive Technical Writer/Editor; telephone (425) 687-4243, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: sandi.carli@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 2, 2002.

Jeffrey E. Duven,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17525 Filed 7-18-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

ROCKWELL COLLINS, INC.

AIRWORTHINESS DIRECTIVE

APPLIANCE

LARGE AIRCRAFT

2002-14-19  Rockwell Collins, Inc.: Amendment 39-12819; Docket No. 2000-CE-14-AD.

(a) What airplanes are affected by this AD? This AD affects the following Rockwell Collins air data computers (ADC) that are installed in, but not limited to the airplanes that are listed below:

(1) Affected ADC's:

| Unit | Collins part no. (CPN) | Applicable to serial no. |
| --- | --- | --- |
| ADC–85 (Incorporating Rockwell Collins Service Bulletin No. 58) | 622–8051–002 622–8051–003 | All units. |
| ADC–85A (Incorporating Rockwell Collins Service Bulletin No. 58) | 822–0370–113 822–0370–123 822–0370–139 822–0370–404 822–0370–408 | All units. |
| ADC–850D (Incorporating Rockwell Collins Service Bulletin No. 58) ... | 822–0389–133 | All up to and including 3DGW (except for 1P6D, 22RC–22RF, and 23WK–3DGP). |
| ADC–850F | 822–1036–406 822–1036–418 | All Units. |

(2) List of airplanes where the affected ADC could be installed. This is not a comprehensive list and airplanes not on this list that have the ADC installed through field approval or other methods are still affected by this AD:

| Unit | Airplane model |
| --- | --- |
| ADC-85/ADC-85A | Astra AIA. |
|  | Chinese Y7 and Y8. |
|  | Czech LET-610. |
|  | DC-8. |
|  | Falcon 20F. |
|  | Piaggio P-180. |
|  | Raytheon B200, B300, C90A and 1900D. |
| ADC-850D | Lear 60. |
| ADC-850F | Falcon 20, 50, and 50EX. |

(b) Who must comply with this AD? Anyone who wishes to operate any airplane that uses one of the above referenced Rockwell Collins air data computers must comply with this AD.

(c) What problem does this AD address? The actions specified by this AD are intended to prevent an unwarranted display of the ADC flag when switching static air sources. This could cause the flight crew to react to this incorrect flight information and possibly result in an unsafe operating condition.

(d) What actions must I accomplish to address this problem? To address this problem, you must accomplish the following:

| Actions | Compliance | Procedures |
| --- | --- | --- |
| (1) Perform the following, unless already accomplished: (i) Remove any affected ADC from the airplanes. (ii) As applicable, replace or reprogram parts or circuit card assemblies on central processing unit (CPU) circuit cards. (iii) Test the ADC. (iv) Install the modified ADC in the airplanes. | Within the next 12 calendar months after August 23, 2002 (the effective date of this AD). | In accordance with Rockwell Collins Service Bulletin No. 62, Revision No. 2, ADC–85/85A/850C/850D/850E/850F–34–62), Revision No. 2, dated March 7, 2000, or Service Bulletin No. 62, dated October 25, 1999, as applicable, the applicable Collins Computer Component Maintenance Manual, and Collins Avionics Standard Shop Practices Instruction Manual. |
| (2) Do not install on any airplane one of the affected ADCs unless the modification and test required by paragraphs (d)(1)(ii) and (d)(1)(iii) of this AD are accomplished | As of August 23, 2002 (the Service date of this AD). | In accordance with Rockwell Collins Service Bulletin No. 62, Revision No. 2, ADC–85/85A/850C/850D/850E/850F–34–62, dated arch 7, 2000, or Service Bulletin No. 62, dated October 25, 1999, as applicable. |

Note 1: Rockwell Collins Operator Bulletin 99-7, dated August 1999, contains information about an operational placard to install until accomplishment of the actions of this AD. While not necessary to address the unsafe condition in this AD, FAA highly recommends that you incorporate this placard.

(e) Can I comply with this AD in any other way? You may use an alternative method of compliance or adjust the compliance time if:

(1) Your alternative method of compliance provides an equivalent level of safety; and

(2) The Manager, Wichita Aircraft Certification Office (ACO), approves your alternative. Submit your request through an FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Wichita ACO.

Note 2: This AD applies to each airplane identified in paragraph (a) of this AD, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if you have not eliminated the unsafe condition, specific actions you propose to address it.

(f) Where can I get information about any already-approved alternative methods of compliance? Contact Roger A. Souter, FAA, Wichita Aircraft Certification Office (ACO), 1801 Airport Road, Room 100, Wichita, Kansas 67209; telephone: (316) 946-4134; facsimile: (316) 946-4407, E-mail: Roger.Souter@faa.gov.

(g) What if I need to fly the airplane to another location to comply with this AD? The FAA can issue a special flight permit under sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate your airplane to a location where you can accomplish the requirements of this AD.

(h) Are any service bulletins incorporated into this AD by reference? Actions required by this AD must be done in accordance with Rockwell Collins Service Bulletin No. 62, Revision No. 2, ADC-85/85A/850C/850D/850E/850F-34-62, dated March 7, 2000, or Rockwell Collins Service Bulletin No. 62, ADC-85/85A/850C/850F-34-62, dated October 25, 1999. The Director of the Federal Register approved this incorporation by reference under 5 U.S.C. 552(a) and 1 CFR part 51. You may get copies from Rockwell Collins, Business and Regional Systems, 400 Collins Road Northeast, Cedar Rapids, Iowa 52498. You may view copies at the FAA, Central Region, Office of the Regional Counsel, 901 Locust, Room 506, Kansas City, Missouri, or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

(i) When does this amendment become effective ? This amendment becomes effective on August 23, 2002.

FOR FURTHER INFORMATION CONTACT: Roger A. Souter, FAA, Wichita Aircraft Certification Office (ACO), 1801 Airport Road, Room 100, Wichita, Kansas 67209; telephone: (316) 946-4134; facsimile: (316) 946-4407. E-mail address: Roger.Souter@faa.gov.

Issued in Kansas City, Missouri, on July 3, 2002.

Dorenda D. Baker,

Acting Manager, Small Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17306 Filed 7-12-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

BOEING

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

EDITORIAL CORRECTION published in Federal Register July 22, 2002, [Volume 67, Number 140); Page 47891; www.access.gpo.gov/su_docs/aces/aces140.html]

2002-14-20  Boeing: Amendment 39-12820. Docket 2002-NM-127-AD.

Applicability: Model 737-600, -700, -800, and -900 series airplanes; as listed in Boeing Alert Service Bulletin 737-24A1150, dated April 11, 2002; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (b) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent ice from blocking the pitot tube that provides airspeed data to the flightcrew, which could lead to the flightcrew receiving incorrect airspeed data, and result in loss of control of the airplane if the flightcrew fails to recognize that the data are incorrect, accomplish the following:

Measurement of Voltage and Corrective Actions

(a) Within 60 days after the effective date of this AD, measure the electrical voltage at the circuit breaker for the captain's pitot heater to determine if the pitot heater is connected to the correct power supply bus, per Boeing Alert Service Bulletin 737-24A1150, dated April 11, 2002.

(1) If the measurement is 100 to 122 volts alternating current (AC): No further action is required by this AD.

(2) If the measurement is not 100 to 122 volts AC: Before further flight, perform all actions associated with connecting the subject circuit breaker wire to the 115-volt AC standby power supply bus (including performing a test to ensure that the pitot heater system operates correctly, repeating the measurement of the electrical voltage at the circuit breaker for the captain's pitot heater, and troubleshooting and correcting the wire connections until the test and measurement are successful), per the service bulletin.

Alternative Methods of Compliance

(b) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Seattle Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Seattle ACO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Seattle ACO.

Special Flight Permits

(c) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(d) The actions shall be done in accordance with Boeing Alert Service Bulletin 737-24A1150, dated April 11, 2002. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Boeing Commercial Airplane Group, P.O. Box 3707, Seattle, Washington 98124-2207. Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(e) This amendment becomes effective on July 31, 2002.

FOR FURTHER INFORMATION CONTACT: Technical Information: Binh Tran, Aerospace Engineer, Systems and Equipment Branch, ANM-130S, FAA, Seattle Aircraft Certification Office, 1601 Lind Avenue, SW., Renton, Washington 98055-4056; telephone (425) 227-2890; fax (425) 227-1181.

Other Information: Judy Golder, Airworthiness Directive Technical Editor/Writer; telephone (425) 687-4241, fax (425) 227-1232. Questions or comments may also be sent via the Internet using the following address: judy.golder@faa.gov. Questions or comments sent via the Internet as attached electronic files must be formatted in Microsoft Word 97 for Windows or ASCII text.

Issued in Renton, Washington, on July 8, 2002.

Vi Lipski,

Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17548 Filed 7-15-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

BOEING

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-21  Boeing: Amendment 39-12821. Docket 2000-NM-367-AD. Supersedes AD 99-03-08, Amendment 39-11022.

Applicability: Model 737-600, -700, and -800 series airplanes, listed in Group I or II of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000; certificated in any category.

Note 1: This AD applies to Model 737-700 series airplanes in an increased-gross-weight configuration, as listed in the service bulletin referred to in the applicability statement of this AD.

Note 2: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (f)(1) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent major fuel leakage due to excessive wear of the quick-disconnect coupling on the fuel hose, fire in the engine nacelle, and consequent loss of thrust from the affected engine, which could result in reduced controllability of the airplane, accomplish the following:

Restatement of Requirements of AD 99-03-08

Repetitive Inspections and Corrective Actions

(a) For airplanes listed in Group I of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000: Within 7 days after February 19, 1999 (the effective date of AD 99-03-08, amendment 39-11022), perform a general visual inspection to detect discrepancies (i.e., fuel leakage, wear of the lock teeth, or missing lock pins on the coupling nut) of the quick-disconnect coupling on the fuel hose located at the fan case firewall, in accordance with Boeing Alert Service Bulletin 737-73A1011, dated November 25, 1998; or Revision 2, dated July 13, 2000.

(1) If no discrepancy is detected, repeat the inspection thereafter at intervals not to exceed 500 flight hours, until the installation required by paragraph (b) of this AD is accomplished.

(2) If any discrepancy is detected, prior to further flight, perform follow-on corrective actions, as applicable, in accordance with TABLE 1. of the Accomplishment Instructions of the alert service bulletin, and repeat the inspection thereafter at the time specified in TABLE 1. of the Accomplishment Instructions of the alert service bulletin.

Installation of Clamp Shell and Repetitive Inspections

(b) For airplanes listed in Group I of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000: Within 30 days after February 19, 1999, install an Aeroquip Clamp Shell, having part number (P/N) AE20074-165, on the quick-disconnect coupling on the fuel hose, which is located at the fan case firewall, in accordance with Boeing Alert Service Bulletin 737-73A1011, dated November 25, 1998; or Revision 2, dated July 13, 2000. Accomplishment of such installation terminates the repetitive inspection requirements of paragraphs (a)(1) and (a)(2) of this AD.

New Requirements of This AD

Note 3: For the purposes of this AD, a general visual inspection is defined as: ''A visual examination of an interior or exterior area, installation, or assembly to detect obvious damage, failure, or irregularity. This level of inspection is made from within touching distance unless otherwise specified. A mirror may be necessary to enhance visual access to all exposed surfaces in the inspection area. This level of inspection is made under normally available lighting conditions such as daylight, hangar lighting, flashlight, or droplight and may require removal or opening of access panels or doors. Stands, ladders, or platforms may be required to gain proximity to the area being checked.''

Note 4: Accomplishment of the requirements of paragraphs (a), (b), and (c) of this AD according to Boeing Alert Service Bulletin 737-73A1011, Revision 1, dated April 15, 1999, is acceptable for compliance with those paragraphs.

Repetitive Inspections

(c) For airplanes listed in Groups I and II of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000: Within 1,000 flight hours after installation of the clamp shell either per paragraph (b) of this AD (for Group I airplanes) or during production (for Group II airplanes), perform the inspection specified in paragraph (a) of this AD.

Note 5: The repetitive inspections required by paragraph (c) of this AD were previously required by paragraph (b) of AD 99-03-08.

(1) If no discrepancy is detected, repeat the inspection thereafter at intervals not to exceed 1,000 flight hours.

(2) If any discrepancy is detected, prior to further flight, perform follow-on corrective actions, as applicable, in accordance with Figures 1 and 3 of the Accomplishment Instructions of the alert service bulletin, as applicable, and repeat the inspection thereafter at the time specified in TABLE 1. of the Accomplishment Instructions of the alert service bulletin.

Replacement of Existing Parts

(d) For airplanes listed in Groups I and II of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000: Within 3 years after the effective date of this AD, remove the clamp shell installed per paragraph (b) of this AD (for Group I airplanes) or during production (for Group II airplanes), and replace the existing quick-disconnect fuel hose, coupling, and strut fitting with new, fixed-B-nut-type parts, in accordance with Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000. Such replacement terminates the repetitive inspections required by paragraphs (a)(1), (a)(2), and (c) of this AD, as applicable.

Spares

(e) After the effective date of this AD, no one may install a quick-disconnect fuel supply hose, coupling, or strut fitting with a part number listed in the ''Existing Part Number'' column of the table under paragraph 2.E. of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000, on any airplane.

Alternative Methods of Compliance

(f)(1) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Seattle Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Seattle ACO.

(2) Alternative methods of compliance, approved previously in accordance with AD 99-03-08, amendment 39-11022, are approved as alternative methods of compliance with paragraphs (a), (b), and (c) of this AD.

Note 6: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Seattle ACO.

Special Flight Permits

(g) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(h) The actions shall be done in accordance with Boeing Alert Service Bulletin 737-73A1011, dated November 25, 1998; or Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000.

(1) The incorporation by reference of Boeing Alert Service Bulletin 737-73A1011, Revision 2, dated July 13, 2000, is approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51.

(2) The incorporation by reference of Boeing Alert Service Bulletin 737-73A1011, dated November 25, 1998, was approved previously by the Director of the Federal Register as of February 19, 1999 (64 FR 5590, February 4, 1999).

(3) Copies may be obtained from Boeing Commercial Airplane Group, P.O. Box 3707, Seattle, Washington 98124-2207. Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(i) This amendment becomes effective on August 21, 2002.

FOR FURTHER INFORMATION CONTACT: Douglas Pegors, Aerospace Engineer, Propulsion Branch, ANM-140S, FAA, Seattle Aircraft Certification Office, 1601 Lind Avenue, SW., Renton, Washington 98055-4056; telephone (425) 227-1446; fax (425) 227-1181.

Issued in Renton, Washington, on July 8, 2002.

Vi Lipski,

Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-17550 Filed 7-16-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

EMPRESA BRASILEIRA DE AERONAUTICA S.A. (EMBRAER)

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-23  Empresa Brasileira de Aeronautica S.A. (EMBRAER): Amendment 39-12823. Docket 2002-NM-129-AD.

Applicability: Model EMB-135 and -145 series airplanes, certificated in any category; equipped with horizontal stabilizer actuator (HSA) assemblies having part numbers and serial numbers as listed in EMBRAER Service Bulletin 145-27-0088, dated February 1, 2002.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent a loose or disengaged clutch nut on the HSA clutch assembly, which could result in loss of pitch trim and consequent reduced controllability of the airplane, accomplish the following:

Detailed Inspection and Follow-On Actions

(a) Within 30 days after the effective date of this AD, perform a one-time detailed inspection of the HSA clutch assembly to verify that at least one locking tab on the key washer is bent into the locking groove of the clutch nut, per EMBRAER Service Bulletin 145-27-0088, dated February 1, 2002.

Note 2: For the purposes of this AD, a detailed inspection is defined as: ''An intensive visual examination of a specific structural area, system, installation, or assembly to detect damage, failure, or irregularity. Available lighting is normally supplemented with a direct source of good lighting at intensity deemed appropriate by the inspector. Inspection aids such as mirror, magnifying lenses, etc., may be used. Surface cleaning and elaborate access procedures may be required.''

Note 3: EMBRAER Service Bulletin 145-27-0088 refers to Parker Service Bulletin 362200-27-231, dated December 21, 2001, as the appropriate source of service information for accomplishment of the inspection described in paragraph (a) of this AD. A copy of the Parker service bulletin is contained within the EMBRAER service bulletin.

(1) If at least one locking tab is bent into the locking groove of the clutch nut: Before further flight, perform all applicable follow-on actions per the service bulletin. The follow-on actions include a detailed inspection for damage (e.g., nicks, tears, scarring) of the O-ring at the base of the HSA motor, replacement of the O-ring with a new O-ring if any damage is found, and a detailed inspection for damage (e.g., nicks, tears, scarring) of the sealing surface. If any damage is found on the sealing surface, before further flight, replace the HSA assembly with a serviceable assembly, per the service bulletin.

(2) If no locking tab is bent into the locking groove of the clutch nut: Before further flight, replace the HSA assembly with a serviceable HSA assembly, per the service bulletin.

Spares

(b) As of the effective date of this AD, no person may install on any airplane an HSA assembly with a part number and serial number included in the applicability statement of this AD, unless the HSA assembly has been inspected according to paragraph (a) of this AD and found to have at least one locking tab bent into the locking groove of the clutch nut.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Atlanta Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Atlanta ACO.

Note 4: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Atlanta ACO.

Special Flight Permits

(d) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(e) The actions shall be done in accordance with EMBRAER Service Bulletin 145-27-0088, dated February 1, 2002. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Empresa Brasileira de Aeronautica S.A. (EMBRAER), P.O. Box 343–CEP 12.225, Sao Jose dos Campos–SP, Brazil. Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; at the FAA, Atlanta Aircraft Certification Office, One Crown Center, 1895 Phoenix Boulevard, suite 450, Atlanta, Georgia; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Note 5: The subject of this AD is addressed in Brazilian airworthiness directive 2002-04-01, dated April 24, 2002.

Effective Date

(f) This amendment becomes effective on August 2, 2002.

FOR FURTHER INFORMATION CONTACT: Robert Capezzuto, Aerospace Engineer, Systems and Flight Test Branch, ACE-116A, FAA, Atlanta Aircraft Certification Office, One Crown Center, 1895 Phoenix Boulevard, suite 450, Atlanta, Georgia 30349; telephone (770) 703-6071; fax (770) 703-6097.

Issued in Renton, Washington, on July 11, 2002.

Lirio Liu-Nelson,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-18026 Filed 7-17-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

CESSNA AIRCRAFT COMPANY

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-24  Cessna Aircraft Company: Amendment 39-12824. Docket 2000-NM-388-AD.

Applicability: Model 650 airplanes, serial numbers -0001 through -0241 inclusive, and serial numbers -7001 through -7112 inclusive; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent inadvertent disengagement of the locking mechanism of the side brace mechanism assembly of the left or right main landing gear (MLG), which could lead to collapse of the respective MLG, and result in gear-up landing and possible injury to passengers and crew; accomplish the following:

One-Time Inspection

(a) Within 6 months after the effective date of this AD, do a one-time inspection of the side brace mechanism assemblies of the left and right MLGs to detect any incorrect part number (P/N) found installed, as specified in Cessna Service Bulletin SB650-32-47, including Cessna Service Bulletin Supplemental Data SB650-32-47, both dated August 14, 2000.

(1) If the correct part number is found installed on the left side brace mechanism assembly, P/N 6217076-201, and on the right side brace mechanism assembly, P/N 6217076-202, no further action is required by paragraph (a) of this AD.

Corrective Action

(2) If incorrect P/N 6217076-2, 6217076-4, or 6217076-9 is found installed on either the left or right side brace mechanism assembly: Prior to further flight, replace any incorrect left side brace mechanism assembly with a new, improved assembly, P/N 6217076-201; and replace any incorrect right side brace mechanism assembly with a new, improved assembly, P/N 6217076-202; per Cessna Service Bulletin SB650-32-47, including Cessna Service Bulletin Supplemental Data SB650-32-47, both dated August 14, 2000. After the replacement action, no further action is required by this AD.

Spares

(b) As of the effective date of this AD, no person shall install a left or right MLG side brace mechanism assembly, P/N 6217076-2, 6217076-4, or 6217076-9, on any airplane.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Wichita Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Wichita ACO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Wichita ACO.

Special Flight Permits

(d) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(e) The actions shall be done in accordance with Cessna Service Bulletin SB650-32-47, including Cessna Service Bulletin Supplemental Data SB650-32-47, both dated August 14, 2000. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Cessna Aircraft Co., P.O. Box 7706, Wichita, Kansas 67277. Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Wichita Aircraft Certification Office, 1801 Airport Road, Room 100, Mid-Continent Airport, Wichita, Kansas; or at the Office of the Federal Register, 800 North Capitol Street, NW., Suite 700, Washington, DC.

Effective Date

(f) This amendment becomes effective on August 26, 2002.

FOR FURTHER INFORMATION CONTACT: Robert P. Busto, Aerospace Engineer, Systems and Propulsion Branch, ACE-116W, FAA, Wichita Aircraft Certification Office, 1801 Airport Road, Room 100, Mid-Continent Airport, Wichita, Kansas 67209; telephone (316) 946-4157; fax (316) 946-4407.

Issued in Renton, Washington, on July 11, 2002.

Lorio Liu-Nelson,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-18199 Filed 7-19-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

EMPRESA BRASILEIRA DE AERONAUTICA S.A. (EMBRAER)

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002-14-25  Empresa Brasileira De Aeronautica S.A. (Embraer): amendment 39-128.25 Docket 2002-NM-131-AD. Supersedes AD 2002-08-18, Amendment 39-12730.

Applicability: Model EMB-135 and -145 series airplanes; certificated in any category; equipped with horizontal stabilizer actuators as listed in Embraer Service Bulletin 145-27-0082, Change No. 01, dated December 13, 2001.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (d)(1) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent loss of pitch trim command during the takeoff and climb phase of flight due to improper set point of the actuator clutches of the horizontal stabilizer, which could result in high pitch control forces and consequent reduced controllability of the airplane, accomplish the following:

Requirements of AD 2002-08-18, Amendment 39-12739

Repetitive Inspectors (Tests)/Replacement

(a) For airplanes subject to the requirements of AD 2002-08-18, within 800 flight hours after May 16, 2002 (the effective date of AD 2002-08-18): Do an inspection (test) of the actuator clutches of both the primary and backup pitch trim systems of the horizontal stabilizer for proper pitch trim indications per EMBRAER Service Bulletin 145-27-0082, dated September 18, 2001, or Change No. 01, dated December 13, 2001. Repeat the test after that every 2,000 flight hours.

(1) If either test indicates that the clutch is slipping (no PIT TRIM 1 INOP or PIT TRIM 2 INOP message appears, and the measured voltage during trim attempts is greater than 1 volt), before further flight, replace the applicable actuator with an improved actuator and before further flight, repeat the test.

(2) If both tests indicate that the clutch is acceptable (PIT TRIM 1 INOP or PIT TRIM 2 INOP message appears), repeat the test at the time specified in paragraph (a) of this AD.

New Requirements of This AD

(b) For airplanes other than those identified in paragraph (a) of this AD, within 800 flight hours after the effective date of this AD: Do an inspection (test) of the actuator clutches of both the primary and backup pitch trim systems of the horizontal stabilizer for proper pitch trim indications per EMBRAER Service Bulletin 145-27-0082, dated September 18, 2001, or Change No. 01, dated December 13, 2001. Repeat the test their that every 2,000 flight hours.

(1) If either test indicates that the clutch is slipping (no PIT TRIM 1 INOP or PIT TRIM 2 INOP message appears, and the measured voltage during trim attempts is greater than 1 volt), before further flight, replace the applicable actuator with an improved actuator per the service bulletin, and before further flight, repeat the test.

(2) If both tests indicate that the clutch is acceptable (PIT TRIM 1 INOP or PIT TRIM 2 INOP message appears), repeat the test at the time specified in paragraph (a) of this AD.

Spares

(c) As of the effective date of this AD, no person shall install an actuator having part number 362200-1007, -1009, -1011, or -1013 on any airplane, unless the actuator clutch is inspected as required by paragraph (a) of this AD.

Alternative Methods of Compliance

(d)(1) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Atlanta Aircraft Certification Office (ACO), FAA. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Atlanta ACO.

(2) Alternative methods of compliance, approved previously per AD 2002-08-18, amendment 39-12730, are approved as alternative methods of compliance with this AD.

Note 2: Information concerning the existing of approved alternative methods of compliance with this AD, if any, may be obtained from the Atlanta ACO.

Special Flight Permits

(e) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(f) Except as provided by paragraph (a)(1) of this AD, the actions shall be done in accordance with EMBRAER Service Bulletin 145-27-0082, dated September 18, 2001; or EMBRAER Service Bulletin 145-27-0082, Change No. 01, dated December 13, 2001.

(1) The incorporation by reference of EMBRAER Service Bulletin 145-27-0082, Change No. 01, dated December 13, 2001, is approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51.

(2) The incorporation by reference of EMBRAER Service Bulletin 145-27-0082, dated September 18, 2001, was approved previously by the Director of the Federal Register as of May 16, 2002 (67 FR 21567, May 1, 2002.)

(3) Copies may be obtained from Empresa Brasileira de Aeronautics S.A. (EMBRAER), P.O. Box 343-CEP 12.225, San Jose dos Campos–SP, Brazil. Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the FAA, Atlanta Aircraft Certification Office, One Crown Center, 1895 Phoenix Boulevard, suite 450, Atlanta, Georgia; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Note 3: The subject of this AD is addressed in Brazilian airworthiness directive 2001-10-02R2, dated May 6, 2002.

Effective Date

(g) This amendment becomes effective on August 8, 2002.

FOR FURTHER INFORMATION CONTACT: Robert Capezzuto, Aerospace Engineer, Systems and Flight Test Branch, ACE-116A, FAA, Atlanta Aircraft Certification Office, One Crown Center, 1895 Phoenix Boulevard, suite 450, Atlanta, Georgia 30349; telephone (770) 703-6071; fax (770) 703-6097.

Issued in Renton, Washington, on July 11, 2002.

Michael J. Kaszycki,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-18028 Filed 7-23-02; 8:45 am]

BILLING CODE 4910-13-M

BW 2002-15

FOKKER SERVICES B.V.

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002–14–27 Fokker Services B.V.: Amendment 39–12827. Docket 98–NM–224–AD. Supersedes AD 94–25–03, Amendment 39–9087.

Applicability: All Model F.28 Mark 0070, 0100, 1000, 2000, 3000, and 4000 series airplanes; certificated in any category.

Note 1: This AD applies to each airplane identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent takeoff with snow, ice, or frost on the critical surfaces of the airplane, which could result in reduced controllability of the airplane; accomplish the following:

Restatement of Requirements of AD 94–25–03, Amendment 39–9087

(a) Within 10 days after December 21, 1994 (the effective date of AD 94–25–03, amendment 39–9087), incorporate the following into the Limitations Section of the FAA-approved Airplane Flight Manual (AFM) (this may be accomplished by inserting a copy of this AD in the AFM):

“Wing De-Icing/Anti-Icing Prior To Takeoff

Caution

The Model F.28 series airplane has a wing design with no leading edge high lift devices, such as slats. Wings without leading edge high lift devices are particularly susceptible to loss of lift due to wing icing. Minute amounts of ice or other contamination (equivalent to medium grit sandpaper) on the leading edges or upper wing surfaces can cause significant reduction in the stall angle-of-attack. This can increase stall speed up to 30 knots. The increased stall speed can be well above the stall warning (stick shaker) activation speed.

Takeoff shall not be attempted unless the pilot-in-command has ensured that the aircraft surfaces are free of ice, frost, and snow accumulation, as required by §§ 91.527 and 121.629 of the Federal Aviation Regulations (FAR).

In addition, takeoff shall not be attempted when the Outside Air Temperature (OAT) is below 6 degrees C (Centigrade) [42 degrees F (Fahrenheit)]; and either the difference between the dew point temperature and OAT is less than 3 degrees C (5 degrees F), or visible moisture (rain, drizzle, sleet, snow, fog, etc.) is present, unless the operator complies with either Option 1 or Option 2 below:

Option 1

The leading edge and upper wing surfaces have been physically checked for ice/frost/snow and the flight crew verifies that a visual check and a physical (hands-on) check of the leading edge and upper wing surfaces has been accomplished and that the wing is clear of ice/frost/snow accumulation; or

Option 2

The following takeoff procedure is used:

Warning

The following technique cannot be used unless the pilot-in-command has ensured that the aircraft surfaces are free of ice, frost, and snow, as required by §§ 91.527 and 121.629 of the FAR.

- (All Marks, except Mark 0100 and Mark 0070) When using flight director for takeoff, select HDG mode and 10 degrees pitch attitude.

- Select the largest flap setting that is permissible for the takeoff weight/altitude/temperature conditions.

- (All Marks, except Mark 0100 and Mark 0070) Use rated takeoff thrust.

- (Mark 0100 and Mark 0070) Use takeoff/go-around (TOGA) thrust.

- Do not use flexible thrust.

- At VR rotate slowly (less than 3 degrees per second) to 10 degrees pitch attitude.

- When positively climbing, select gear UP.

- Do not exceed 10 degrees pitch until airspeed is above V2 + 20 KTS.

- When above V2 + 20 KTS, slowly increase the pitch attitude, keeping the speed above V2 + 20 KTS.

- Retract the flaps at or above VFR + 20 KTS.

Notes to Option 2

1. The available field length must be greater than or equal to 120 percent of the takeoff distance required by regulation for the actual gross weight. Also, the 20 percent increase in takeoff distance must be accounted for in the obstacle clearance analysis. Weight must be off-loaded, if necessary, to meet these conditions.

2. (Mark 0100 and Mark 0070) Do not follow the Flight Director pitch command during rotation for takeoff and initial climb, as this will result in exceeding the recommended maximum pitch angle of 10 degrees before reaching the speed of V2 + 20 KTS.

3. (Mark 0100 and Mark 0070) Do not engage the autopilot until leaving the Automated Flight Control and Augmentation System (AFCAS) takeoff (TO) mode.

4. For the case of an engine failure, refer to the applicable procedure in Section 4.17.01 Single Engine Operation of the F.28 Mark 0100 (Fokker 100) and F.28 Mark 0070 (Fokker 70) AFM, or Section 1.7.4 Operation Under Abnormal Conditions of the F.28 FHB, as applicable.

5. During takeoff, the first indication of wing contamination will probably be airframe buffet when the pitch angle is increased above 10 degrees, followed by wing drop and insufficient climb rate. Do not exceed 10 degrees pitch until airspeed is above V2 + 20 KTS.”

This action is required until the requirements of paragraph (c) of this AD are accomplished, or the actions specified in paragraphs (d) and (e) of this AD are accomplished.

Note 2: If an operator elects to implement in its fleet only one of the two options specified in this paragraph, the other OPTION does not have to be included in the Limitations Section of the AFM. However, the OPTION that is implemented must be incorporated in the AFM verbatim as it appears in this paragraph.

New Requirements of This AD

Modification

(b) Except as provided in paragraph (d) of this AD: Within 18 months after the effective date of this AD, modify the wing anti-ice system for operation on the ground as specified in paragraph (b)(1) or (b)(2) of this AD, as applicable.

(1) For Model F.28 Mark 0070 and 0100 series airplanes, modify in accordance with Fokker Service Bulletin SBF100–30–018, Revision 1, Appendix I, Appendix 1, dated August 14, 1999.

(2) For Model F.28 Mark 1000, 2000, 3000, and 4000 series airplanes, modify in accordance with Fokker Service Bulletin F28/30–031, Appendix I, Revision 1, dated May 4, 1998; and Fokker Proforma Service Bulletin F.28/30–032, including Appendix 1, dated December 1, 1999; as applicable.

Manual Change Notification (MCNO)

(c) Prior to further flight after accomplishing the modification required by paragraph (b) of this AD, remove the AFM revisions required by paragraph (a) of this AD, and incorporate the flight manual changes specified in Fokker MCNO F100–003, dated September 19, 1997 (for Fokker Model F.28 Mark 070 and 0100 series airplanes); and Fokker MCNO F28–003, dated September 5, 1997 (for Fokker Model F.28 Mark 1000, 2000, 3000, and 4000 series airplanes); as applicable. Accomplishment of the actions specified in paragraphs (b) and (c) of this AD constitute terminating action for the requirements of this AD.

Note 3: Incorporation of the leading edge thermal anti-ice modification and associated operating instructions does not relieve the requirement that airplane surfaces are free of ice, frost, and snow accumulation as required by §§ 91.527 and 121.629 of the Federal Aviation Regulations (14 CFR 91.527 and 121.629).

Acceptable Method of Compliance With the Requirements of Paragraphs (b) and (c) of This AD

(d) For Fokker Model F.28 Mark 0100 series airplanes on which a “Contaminant/Fluid Integrity Measuring System” (C/FIMS”) has been installed in accordance with Supplemental Type Certification ST291CH, as amended on August 20, 1998: Prior to further flight after accomplishment of STC ST291CH, as amended on August 20, 1998, remove the AFM revisions required by paragraph (a) of this AD, and incorporate the following into the Limitations Section of the FAA-approved AFM (This may be accomplished by inserting a copy of this AD in the AFM):

“Wing De-Icing/Anti-Icing Prior To Takeoff

Caution

The Model F.28 series airplane has a wing design with no leading edge high lift devices, such as slats. Wings without leading edge high lift devices are particularly susceptible to loss of lift due to wing icing. Minute amounts of ice or other contamination (equivalent to medium grit sandpaper) on the leading edges or upper wing surfaces can cause significant reduction in the stall angle-of-attack. This can increase stall speed up to 30 knots. The increased stall speed can be well above the stall warning (stick shaker) activation speed.

Takeoff shall not be attempted unless the pilot-in-command has ensured that the aircraft surfaces are free of ice, frost, and snow accumulation, as required by §§ 91.527 and 121.629 of the Federal Aviation Regulations (FAR).

In addition, takeoff shall not be attempted when the Outside Air Temperature (OAT) is below 6 degrees C (Centigrade) [42 degrees F (Fahrenheit)]; and either the difference between the dew point temperature and OAT is less than 3 degrees C (5 degrees F), or visible moisture (rain, drizzle, sleet, snow, fog, etc.) is present; unless the operator complies with Option 1, Option 2, or Option 3.

Option 1

(i) Operate the C/FIMS” in accordance with AFM Supplement AlliedSignal Aerospace Canada Document Number 6C–486, Revision 2, dated August 4, 1999.

(ii) C/FIMS” is an advisory system that must not be used as the primary means of determining whether the airplane should be initially deiced or anti-iced or used as the primary means of determining that the fluid has failed.

(iii) C/FIMS” may be used only for the time periods covered by the dicing/anti-icing holdover time tables. C/FIMS” may not be used when the holdover time tables have been exceeded; or

If the C/FIMSTM is not operational:

Option 2

The leading edge and upper wing surfaces have been physically checked for ice/frost/snow and the flight crew verifies that a visual check and a physical (hands-on) check of the leading edge and upper wing surfaces has been accomplished and that the wing is clear of ice/frost/snow accumulation; or

If the C/FIMSTM is not operational:

Option 3

The following takeoff procedure is used:

Warning

The following technique cannot be used unless the pilot-in-command has ensured that the aircraft surfaces are free of ice, frost, and snow, as required by §§ 91.527 and 121.629 of the FAR.

- Select the largest flap setting that is permissible for the takeoff weight/altitude/temperature conditions.

- Use takeoff/go-around (TOGA) thrust.

- Do not use flexible thrust.

- At VR rotate slowly (less than 3 degrees per second) to 10 degrees pitch attitude.

- When positively climbing, select gear UP.

Do not exceed 10 degrees pitch until airspeed is above V2 + 20 KTS.

- When above V2 + 20 KTS, slowly increase the pitch attitude, keeping the speed above V2 + 20 KTS.

- Retract the flaps at or above VFR + 20 KTS.

Notes to Option 3

1. The available field length must be greater than or equal to 120 percent of the takeoff distance required by regulation for the actual gross weight. Also, the 20 percent increase in takeoff distance must be accounted for in the obstacle clearance analysis. Weight must be off-loaded, if necessary, to meet these conditions.

2. Do not follow the Flight Director pitch command during rotation for takeoff and initial climb, as this will result in exceeding the recommended maximum pitch angle of 10 degrees before reaching the speed of V2 + 20 KTS.

3. Do not engage the autopilot until leaving the Automated Flight Control and Augmentation System (AFCAS) takeoff (TO) mode.

4. For the case of an engine failure, refer to the applicable procedure in Section 4.17.01 Single Engine Operation of the F.28 Mark 0100 (Fokker 100) AFM.

5. During takeoff, the first indication of wing contamination will probably be airframe buffet when the pitch angle is increased above 10 degrees, followed by wing drop and insufficient climb rate. Do not exceed 10 degrees pitch until airspeed is above V2 + 20 KTS.”

Accomplishment of the actions specified in this paragraph after the installation of STC ST291CH, as amended on August 20, 1998, constitute terminating action for the requirements of this AD.

Note 4: Operators should note that, while Option 1 specified in paragraph (d) of this AD must be incorporated into the Limitations Section of the AFM, operators may elect to incorporate either both or only one of the other two options specified in paragraph (d) of this AD. Only Option 1 and the elected option(s) need to be incorporated into the AFM. However, any option that is incorporated into the AFM must be identical to the option wording specified in paragraph (d) of this AD.

Note 5: Installation of the Contaminant/Fluid Integrity Measuring System (C/FIMS TM) in accordance with Supplemental Type Certification ST291CH, as amended on August 20, 1998, and accomplishment of the actions specified in paragraph (d) of this AD, do not relieve the requirement that airplane surfaces are free of ice, frost, and snow accumulation as required by §§ 91.527 and 121.629 of the Federal Aviation Regulations (14 CFR 91.527 and 121.629).

Alternative Methods of Compliance

(e) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, International Branch, ANM–116. Operators shall submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, International Branch, ANM–116.

Note 6: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the International Branch, ANM–116.

Special Flight Permits

(f) Special flight permits may be issued in accordance with §§ 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be accomplished.

Incorporation by Reference

(g) The actions required by paragraphs (b) and (c) of this AD shall be done in accordance with Fokker Service Bulletin SBF100–30–018, Appendix I, Revision 1, dated August 14, 1999; Fokker Service Bulletin F28/30–031, Appendix I, Revision 1, dated May 4, 1998; Fokker Proforma Service Bulletin F28/30–032, including Appendix 1, dated December 1, 1999; Fokker Manual Change Notification MCNO F100–003, dated September 19, 1997; and Fokker Manual Change Notification MCNO F28–003, dated September 5, 1997. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Fokker Services B.V., P.O. Box 231, 2150 AE Nieuw-Vennep, The Netherlands. Copies may be inspected at the FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(h) This amendment becomes effective on August 29, 2002.

FOR FURTHER INFORMATION CONTACT: Tom Rodriguez, Aerospace Engineer, International Branch, ANM–116, FAA, Transport Airplane Directorate, 1601 Lind Avenue, SW., Renton, Washington 98055–4056; telephone (425) 227–1137; fax (425) 227–1149.

Issued in Renton, Washington, on July 12, 2002.

Lirio Liu-Nelson,

Acting Manager, Transport Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02–18624 Filed 7–24–02; 8:45 am]

BILLING CODE 4910–13–U

BW 2002-15

HAMILTON SUNDSTRAND POWER SYSTEMS

AIRWORTHINESS DIRECTIVE

APPLIANCE

LARGE AIRCRAFT

2002-15-02  Hamilton Sundstrand Power Systems (formerly Sundstrand Power Systems, Turbomach, and Solar): Amendment 39-12830. Docket No. 2002-NE-01-AD.

Applicability

This airworthiness directive (AD) is applicable to Hamilton Sundstrand Power Systems (formerly Sundstrand Power Systems, Turbomach, and Solar) models T-62T-2C, T-62T-25, T-62T-29, and T-62T-39 auxiliary power units (APU's) that have compressor wheel part number (P/N) 100636-1 installed. These APU's are installed on, but not limited to, Fairchild FH-227, Dassault Falcon 20, Lockheed 1329 series (Jetstar), British Aerospace Jetstream 3101, Raytheon Aircraft HS125-600, -700, -800, and Sabreliner Corporation 60 and 80 airplanes, and Boeing Defense & Space Group 234 Series helicopters.

Note 1: This AD applies to each APU identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For APU's that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance

Compliance with this AD is required as indicated, unless already done.

To replace affected compressor wheels

P/N 100636-1, which if not replaced, could result in uncontained compressor wheel failure and damage to the airplane, do the following:

Cast Steel Compressor Wheel Replacement

(a) For compressor wheels, P/N 100636-1, made of cast steel, identifiable by a four-digit casting lot vendor identification number used as a prefix to the serial number, replace compressor wheels with compressor wheel P/N 4503164, 4504174, or M4504174 as follows:

(1) Replace cast steel compressor wheels with 2,350 or greater cycles-since-new (CSN) on the effective date of this AD within 250 cycles-in-service (CIS) after the effective date of this AD.

(2) Replace cast steel compressor wheels with less than 2,350 CSN on the effective date of this AD before accumulating 2,600 CSN.

Wrought Steel Compressor Wheel Replacement

(b) For compressor wheels, P/N 100636-1 made of wrought steel, identifiable by a serial number beginning with the letter W, replace compressor wheels with compressor wheel P/N 4503164, 4504174, or M4504174 as follows:

(1) Replace wrought steel compressor wheels with 3,600 or greater CSN on the effective date of this AD within 500 CIS after the effective date of this AD.

(2) Replace wrought steel compressor wheels with less than 3,600 CSN on the effective date of this AD before accumulating 4,100 CSN.

(c) Information on procedures for replacing compressor wheel P/N 100636-1 may be found in Hamilton Sundstrand Power Systems service bulletin No. SB-T-62T-49-148, Revision 1, dated December 20, 2001.

Reduced Life Limits

(d) This AD establishes new cyclic life limits for compressor wheels P/N 100636-1, of 2,600 CSN for cast steel compressor wheels and 4,100 CSN for wrought steel compressor wheels. Except as provided in paragraph (e) of this AD, no alternate life limits for these parts may be approved.

Alternative Methods of Compliance

(e) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Los Angeles Aircraft Certification Office (ACO). Operators must submit their request through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Los Angeles ACO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the Los Angeles ACO.

Special Flight Permits

(f) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the aircraft to a location where the requirements of this AD can be done.

Effective Date

(g) This amendment becomes effective on August 28, 2002.

FOR FURTHER INFORMATION CONTACT: Roger Pesuit, Aerospace Engineer, Los Angeles Aircraft Certification Office, FAA, Transport Airplane Directorate, 3960 Paramount Blvd., Lakewood, CA 90712-4137; telephone (562) 627-5251, fax (562) 627-5210.

Issued in Burlington, Massachusetts, on July 15, 2002.

Jay J. Pardee,

Manager, Engine and Propeller Directorate, Aircraft Certification Service.

[FR Doc. 02-18482 Filed 7-23-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-15

HAMILTON SUNDSTRAND CORPORATION

AIRWORTHINESS DIRECTIVE

LARGE AIRCRAFT

2002–15–03 Hamilton Sundstrand Corporation: Amendment 39–12831. Docket No. 2002–NE–02–AD. Supersedes AD 2002–05–51.

Applicability: This airworthiness directive (AD) is applicable to Hamilton Sundstrand Corporation (formerly Hamilton Standard Division) model 568F–1 propellers installed with blades, part numbers (P/N's) R815505–2 and R815505–3, that have a serial number (SN) of FR1698 or lower. These propellers are installed on, but not limited to, Aerospatiale ATR 42–400 and –500 and ATR 72 airplanes.

Note 1: This AD applies to each propeller identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For propellers that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (i) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance

Compliance with this AD is required as indicated, unless already done.

To prevent blade failure due to corrosion-induced fatigue, which could result in blade separation and possible loss of airplane control, do the following:

(a) For propeller blades P/N's R815505–2 and R815505–3, replace propeller blades SN FR265 or lower before further flight.

(b) Before further flight, replace propeller blades P/N's R815505–2 and R815505–3, that have a SN of FR1698 or lower, installed on ATR 72 and ATR 42–400 airplanes.

(c) After the effective date of this AD, do not install any propeller blade that was removed in accordance with paragraph (b) of this AD on any airplane.

(d) Replace propeller blades P/N's R815505–2 and R815505–3, that have a SN of FR1698 or lower, installed on ATR 42–500 airplanes, before December 31, 2002.

(e) After the effective date of this AD, do not install any propeller blades, P/N's R815505–2 and R815505–3, that have a SN of FR1698 or lower, on any airplane unless an ultrasonic shear wave inspection of the blade tulip is done in accordance with the Accomplishment Instructions of Hamilton Sundstrand ASB 568F–61–A35, Revision 2, dated March 21, 2002, before installation of the propeller blade.

(f) Procedures for removing the propeller blade and installing a serviceable blade can be found in Hamilton Sundstrand Maintenance Manual P5206.

(g) Within 50 FH since-last-inspection, for propeller blades, P/N's R815505–2 and R815505–3, that have a SN of FR1698 or lower, perform an ultrasonic shear wave inspection of the blade tulip in accordance with the Accomplishment Instructions of Hamilton Sundstrand ASB 568F–61–A35, Revision 2, dated March 21, 2002, and remove blades with unacceptable indications in accordance with the ASB.

(h) Thereafter, within 50 FH since-last-inspection, for propellers blades P/N's R815505–2 and R815505–3, that have a SN of FR1698 or lower, perform an ultrasonic shear wave inspection of the blade tulip in accordance with the Accomplishment Instructions of Hamilton Sundstrand ASB 568F–61–A35, Revision 2, dated March 21, 2002, and remove blades with unacceptable indications in accordance with the ASB.

Optional Terminating Action

(i) Replacement of propeller blades, P/N R815505–2, with propeller blades, P/N R81505R2; or propeller blades, P/N R815505–3, with propeller blades, P/N R815505R3, constitutes terminating action for the repetitive inspection requirements specified in paragraph (h) of this AD.

Alternative Methods of Compliance

(j) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Boston Aircraft Certification Office (ACO). Operators must submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Boston ACO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the Boston ACO.

Special Flight Permits

(k) Special limited flight permits may be issued in accordance with §§ 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) for a nonrevenue flight to a location where the requirements of this AD can be done.

Documents That Have Been Incorporated By Reference

(l) The actions required by this AD must be done in accordance with Hamilton Sundstrand Alert Service Bulletin No. 568F–61–A35, Revision 2, dated March 21, 2002. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Hamilton Sundstrand Propeller Technical Team,

One Hamilton Road, Mail Stop 1–3–AB43, Windsor Locks, CT 06096–1010, U.S.A.; Fax 1–860–654–5107. Copies may be inspected, by appointment, at the FAA, New England Region, Office of the Regional Counsel, 12 New England Executive Park, Burlington, MA; or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

Effective Date

(m) This amendment becomes effective August 9, 2002.

FOR FURTHER INFORMATION CONTACT: Frank Walsh, Aerospace Engineer, Boston Aircraft Certification Office, FAA, Engine and Propeller Directorate, 12 New England Executive Park, Burlington, MA 01803–5299; telephone (781) 238–7158; fax (781) 238–7170.

Issued in Burlington, Massachusetts, on July 15, 2002.

Jay J. Pardee,

Manager, Engine and Propeller Directorate, Aircraft Certification Service.

[FR Doc. 02–18481 Filed 7–24–02; 8:45 am]

BILLING CODE 4910–13–P