Docket No.  FAA-2007-27654

Notice No. 07-07

Activation of Ice Protection

Comment from BAE SYSTEMS Regional Aircraft

Please find below our comments in respect of  NPRM Docket No. FAA-2007-27654 No. 07-07.

The only suggestion for change is that the proposed wording for paragraphs (f), (g) and (h) it should be clarified that it is the 'airframe' ice protection systems that is being referred to.

Regards,

Mike Tuson

Airworthiness Manager,

BAE SYSTEMS Regional Aircraft.

Tel:   +44(0)1292 67 5078

Fax:  +44(0)1292 67 5703

From: Robertson, Neil K (UK Prestwick)

Sent: 11 July 2007 18:03

To: Scott, Alistair (UK Prestwick); Irvine, Colin (UK); Roberts, Ian R (UK Prestwick); Tuson, Michael (UK)

Subject: RE: Activation of Ice Protection - FAA NPRM

Gents,

I have reviewed the FAA proposed changes to the requirements of 25.1419, which introduce additional requirements to ensure the timely activation of airframe ice protection systems.  The requirements are intended to be for new aircraft designs only and so would not have any implications on the RA turboprop and jet types.

The deadline for comments is 25th July 2007.

The proposal is associated with NTSB safety recommendations following the ATR72 Roselawn and EMB120 Monroe accidents and the conclusions and recommendation of the ARAC Ice Protection Harmonisation Working Group following a review of icing related events.

Specifically, proposed § 25.1419(e) requires one of the following methods of icing detection and activation of the airframe IPS:

(1) A primary ice detection system that automatically activates or alerts the flightcrew to activate the airframe IPS;

or

(2) A definition of visual cues for recognition of the first sign of ice accretion on a specified surface combined with an advisory ice detection system that alerts the flightcrew to activate the airframe IPS;

or

(3) Identification of conditions conducive to airframe icing as defined by an appropriate static or total air temperature and visible moisture for use by the flightcrew to activate the airframe IPS.

Proposed § 25.1419(f) requires the activation method be applicable to all phases of flight unless it can be shown that the ice protection system need not be operated during specific phases of flight.

Proposed § 25.1419(h) requires that the procedures for operating the ice protection system be included in the Airplane Flight Manual.

I do not have any concerns with the proposal and the only minor comment would be that in the proposed wording for paragraphs (f), (g) and (h) it should be clarified that it is the 'airframe' ice protection systems that is being referred to.

Cheers,

Neil