This is the readme file for the atmospheric forcing data found in

forcing.r#, where the # refers to the revision number.  The format

and values will change during the course of the analysis as we

conduct post-cruise calibrations, improve the motion correction

algorithms, add more variables to the list, etc.  All of the data

collected during Leg II is provided so that investigators have

nearly continuous time series.  NOTE, however, that the data

includes values that are contaminated by flow distortion, rapid

changes in course, and heat island effects.  This is particularly

true for the wind data.  We have attempted to flag the worst data

using a status array that is given in the last column.  Currently,

the data is given a status of zero when the relative wind direction

is beyond +/- 90 degrees from head on, and when the standard

deviation of the ship's heading is greater than 30 degrees.  A few

(5 or so) anomalously high friction velocity values (u* > 1.2) are

also flagged.  Although a lot of the flagged data can be used in

your studies, please exercise caution when using data during these

periods.

Please email Jim Edson at jedson@whoi.edu if you discover data that

appears incorrect.

REVISION HISTORY

forcing.r1:  This file represents the initial posting on the data

on the GASEX ftp site.  Very few post-cruise calibrations have

been applied to the data, so it generally provides the raw

values collected aboard the R/V Ron Brown.  The data represents

30 minute averages at ten minute intervals, i.e., there is 20

minutes of overlap.

DATA FORMAT

1.  Yearday 1998 (decimal yearday)

2.  Latitude (degrees)

3.  Longitude (degrees)

4.  Ship heading (degrees)

5.  Wind speed at 18-m (m/s)

6.  Wind direction at 18-m (degrees).  Meteorological convention,

i.e., direction from.

7.  Air temperature at 17-m (degrees C)

8.  Sea temperature at 3 to 5-m depth (degrees C)

9.  Relative humidity at 17-m (%)

10.  Atmospheric Pressure (mb)

11.  Solar radiation (W/m^2)

12.  IR radiation (W/m^2)

13.  Friction velocity from direct covariance method (m/s)

14.  Friction velocity from bulk aerodynamic method (m/s)

15.  Sensible heat flux from bulk aerodynamic method (W/m^2)

16.  Latend heat flux from bulk aerodynamic method (W/m^2)

17.  Relative wind direction (degrees).  We use a right-handed

system with x pointed towards the bow and y to port.  For

example, a mean wind coming 10 degrees off the port would

yield a relative wind direction of 190 degrees.

18.  Standard deviation of ship's heading (degrees).

19.  Status Flag (1-good, 0-bad)