FIRE Conference Call

July 25, 2003

Meade, Schmidt, Kessel, Nelson, Strickler, Ulrickson

Agenda: Discuss status, issues and plans for Disruption Modeling, PFC/divertor and vacuum vessel work.

Kessel:

• Test disruption scenario (VDE without Cu cladding) - is available in a Public folder at directory /u/ftp/pub/kessel.fire2003; directions to access this are

ftp to ftp.pppl.gov

login with anonymous

password is your email address

cd to pub/kessel.fire2003

use get command to retrieve files

quit to exit

files are all labeled with dis_____

displas.dat ---global plasma parameters

discoil.dat---PF coil data

disjayp.dat---plasma filaments data

diswirt.dat---toroidal current related data for structures

diswirp.dat---poloidal current related data for structures

• Three cases (R = 2.14m, B = 10 T, Ip = 7.7 MA) will be developed for analysis

1. VDE with max dIp/dt according to 1998 ITER Specification

- with Cu clad included

- expected to be completed July 30

2. VDE with max halo current according to 1998 ITER Specification

- with Cu clad included

- expected to be completed Aug 5?

3. Radial disruption

- same structure model

- in 2 weeks

•  Clarify question about 2 inner PF coils versus 3 on Brown configuration drawing.

Ulrickson

• PC Opera is calculating trial disruption scenario

- this is without Cu clad to be consistent with TSC test disruption case

• Boeing is starting to work on divertor supports

- Mike has confirmed with Dan Driemeyer that he is incorporating Brad Nelson's configuration changes into the divertor design revision.

• Planning on running baffle cooling lines down every other angle port–Brown OK?

Nelson/Strickler

• scaling up vacuum vessel for disruption calculations – (describe method)

• will use TSC input in Eddy Cuff,

- eddy cuff will use gaps  as in Brown 2.14m model- clarify check with Tom

- eddy cuff will be compared with PC Opera for the Trial case?

• Heat Loads

- surface heat load is 0.5 MW/m2 average with a peaking factor of 2

- nuclear heating per Sawan for Pfusion = 150 MW

• Are we still on the right track with the inertial first wall?

- cheapest, big step up if actively cooled

- can we take more advantage of the cladding cooling? Later mod??

• Clarify parameters for H-mode and AT mode

Action: Meade to provide expanded table

Conference Call:   Next week 4pm Thursday (OK, if FESAC agenda doesn’t change)