$$713.00A

Section 713.—ROADSIDE IMPROVEMENT MATERIAL

Revised 8 May 2005

INCLUDE THE FOLLOWING FOR TOPSOIL

$$713.01A

713.01.  Add the following:

For furnished topsoil, submit a soil analysis report from the State University Agricultural Extension Service or other approved soil testing laboratory.  Include in the report the soil textural classification (percentage of sand, silt, clay and organic matter) and additive recommendations.

INCLUDE ONE OF THE FOLLOWING FOR STABILIZED SHOULDERS

$$713.01B

Furnish topsoil for aggregate-topsoil course from stockpiles conserved under Section 204, from stockpiles designated on the plans, or from Contractor sources.

$$713.01C

Furnish topsoil for aggregate-topsoil course from Contractor sources.

INCLUDE THE FOLLOWING ON NPS PROJECTS

$$713.02A

713.02. Add the following:

Use a maximum of 0.17 pounds (3 kilograms) of limestone per cubic foot (meter) of topsoil in order to adjust an acidic condition.

INCLUDE THE FOLLOWING FOR FERTILIZER FOR SEEDING

$$713.03A

713.03.  Add the following:

Furnish fertilizer containing the following minimum available nutrients, unless soil analysis indicates higher concentrations are required:

Total nitrogen					10 percent

Available phosphoric acid		10 percent

Water-soluble potash			10 percent

INCLUDE THE FOLLOWING ON NPS PROJECTS

$$713.05A

713.05.  Add the following after 713.05(h):

(i) Shredded Hardwood Mulch.  Furnish aged hardwood mulch, dark brown to black in color, with a particle size of less than 3 inches (75 millimeters or 80 per the FP96), a neutral pH, and free of sticks, stones, clay, or other matter which may injure plants.

$$713.06A

713.06(b).  Add the following:

The genus, species, and cultivar names shall agree with the nomenclature of the most current edition of “Hortus Third” by L.H. Bailey, Hortorium, Cornell University.

Provide durable tags, stating the date of installation, correct botanical name and size in weather-resistant ink or embossed letters.  Secure the tags to each tree, shrub, and other plant materials in a manner which will not restrict growth.  Leave the tags on all trees, shrubs, and other plant materials until final acceptance by the CO.

$$713.08A

713.08.  Add the following after 713.08(g):

(h) Tree protection.  Tree protection shall be a flexible PVC pipe 4 inches (10 centimeters) in diameter, 12 to 13 inches (30 to 32.5 centimeters or 35 per FP96) in height.

INCLUDE OF THE FOLLOWING, SELECT  THE TYPE OF SOD DESIGNATED IN 627.03

$$713.10A

713.10.  Add the following:

Cut Bermuda grass or Tall Fescue, Kentucky 31 sod to a depth equal to the growth of the roots, but not less than 1 inch (2.5 centimeters).

INCLUDE THE FOLLOWING FOR PESTICIDE

$$713.19A

Add the following after Subsection 713.18:

713.19.  Pesticide.  Pesticides to control armyworms are Bacillus Thuringiensis - Berliner, Bactospeine, Biotrol, BTB, BTV, Dipel, and Thuricide, as manufactured by Nutrilite Products, Inc., and Bioferm Corporation.