CRYSTALS

SPECIFICATIONS FOR SOLICITATION 1-057-RFJ.1251

1.     2 EA.       ZnGeP2 crystal, Size 8x8x25mm3, Face 8x8 Type I, 54 (+/-0.5) degree cut for 2.05 micron pumping, AR coating for 2.05 micron & 2.5-4.1 micron, (R<0.5%@2.05 micron, R<3%@2.5-4.1 micron, R<8%@4.1-9.5 micron Absorption coefficient (o-polarized) <0.10cm-1 at 2.05 micron, flatness: lambda/4@633nm, surface quality 20-10 s-d, Parallelism is better than 20 arc seconds, Damage threshold 2J/cm2.

2.   2 EA.        ZnGeP2 crystal, Size 12x12x22mm3, face 12x12. Make a mark on surface for optic axis. Please provide the crystal transmission measurement curve.