Deliverable 02.7.2.1.2

Comparison of DTF3 from RUC20 and RUC40

On the premise that the calibration and verification of DTF3 for RUC40 is acceptable, we have used its results to recalibrate and compare DTF3 from RUC20 and RUC40.

Diagnostic turbulence from DTF3 was computed for several cases from the daily RUC40 and RUC20 output. The area coverage of DTF5 has the tendency to increase with increased resolution (see Ed Szoke’s report). Similar behavior is also noticed for DTF3. One striking difference is that DTF3 from RUC20 diagnoses turbulence in different areas not present in the RUC40 patterns. Several cases, taken at random, were analyzed and all showed differences specially above 35,000 ft. These differences are attributed to the resolution used in RUC 20 which is higher than that of RUC40. It is reasonable to think that the higher the resolution the more short scale modes are exited in different areas that are not present in the RUC40 results. Figs. 1 and 2 show the DTF3 for a case on 21 August 2002 at 38,000 ft. Fig. 3 shows the DTF3 difference of RUC40 minus RUC20 for a horizontal cross section at 38,000. ft. Although the patterns do not show large areas for this case, they could be larger for more organized weather patterns like those experienced during the winter season. Figs. 4 and 5 show DFT3 for the same case but for 40,000 ft. Fig. 6 shows the difference between RUC20 and RUC40 at 40,000 ft elevation. In all cases analyzed (similar to the present case) the DTF3 amplitude increases with elevation and the differences are more remarcable.

The recalibration of DTF3 from RUC20 was performed by minimizing the difference between DTF3 from RUC20 and RUC40 after multiplying DTF3 from RUC20 by a factor (= 0.588) to reduce its amplitude. Because only a few cases were used, there was not a rigorous statistical analysis done. The recalibration becomes more difficult due the fact that the DTF3 patterns are different between the two models.

The recalibration factor of DTF3 from RUC10 (10-km grid spacing) is about 0.2 which demonstrate even further how the amplitude increase with model resolution. Also, the patterns from RUC10 show more differences than those when comparing RUC20 and RUC40 (not shown).

Fig. 1: DTF3 for 21 August 2002 from RUC20 valid at 1800 UTC and for 38,000 ft elevation.

Fig. 2: As for Fig. 1, except for DTF3 from RUC40.

Fig. 3: RUC20 minus RUC40 DTF3 for the case 21 August 2002 valid 1800 UTC and for 38,000 ft elevation.

Fig. 4: As in Fig. 1, except for 40,000 ft elevation.

Fig. 5: As in Fig.2, except for 40,000 ft elevation.

Fig. 6: As in Fig. 3, except for 40,000 ft elevation.