MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A06909 | In-Flight Anomaly Number -- | Contractor Report Number E-075-3 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title HELICOIL TANGS NOT BROKEN OFF TWO LEVEL SENSORS |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LO2 LEVEL SENSOR | PART# MC432-0205-0019 | SER/LOT# 0000101 | MANUFACTURER SIMMONDS |
| Test/Operation L - FLD | Prevailing Condtion N - INSPECTION | F / U UC | Fail Mode UC - UNSAT | Cause MAW - MFG-ASY-WORK |
| System ELECTRICAL | Defect CE - EXTRA | Material S - STRUCT | Work Contact L. CLANTON | Fail Date 06/30/1983 |
| Received at MSFC 07/22/1983 | Date Isolated -- | FMEA Reference 3.1.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom UC - UNSAT | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 01/16/1984 | Defer Date -- | Add Date -- | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design G. PLATT | Chief Engineer -- | S & MA D. NEWMAN | Project J. BREWER | Project MGR -- |
| Approval |
| Design G. PLATT | Chief Engineer -- | S & MA D. NEWMAN | Project J. BREWER | Project MGR -- |
| PAC Assignee M. GLASS | PAC Review Complete MG | MSFC Closure Date 04/26/1984 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: DURING NASA REVIEW OF LEVEL SENSORS AT MAF TWO (2) LEVEL SENSORS HAD EXPOSED HELICOIL WIRES, ONE SENSOR HAD (2) TANGS NOT BROKEN OFF WHILE OTHER SENSORS HAD (2) TANGS PROTRUDING OUTWARD |
| Contractor Investigation/Resolution CAUSE - VENDOR ERROR, WORKMANSHIP. 11/21/83 PRB STATUS - CLEARED BY (GNC) GOV'T NONCOMPLIANCE, MMC HAS CLOSEOUT INFO ON PQR ITEMS. 2/1/84 - REQUESTED BACK-UP SCAR & GOV. NONCOMPLIANCE. 2/8/84 - REC'D BACK-UP INFO. HOWEVER NO SCAR EXISTS. 2/15/84 - REQUESTED SCAR MENTIONED IN CAPS (E-075A). NO SCAR EXISTS THEREFORE, REQUESTED CAPS BE CORRECTED 3/1/84 - INQUIRED ABOUT STATUS OF REVISED CAPS. 3/27/84 - INQUIRED ABOUT STATUS OF REVISED CAPS. 4/2/84 - PER RAPI-FAX REQUESTED REVISED CAPS. 4/11/84 - REC'D REVISED CAPS (E-075B) WITH REVISED STATEMENT (PARA. 3 PG 10) SCAR DELETED. 4/12/84 RESOLUTION - DISCREPANT HELI-COIL, TANGS NOT REMOVED, RESULTED DUE TO VENDOR PERSONNEL ERROR MFG PROCEDURE REQ'D TANG REMOVAL. SENSORS FOR LWT-2 THRU LWT-7 WERE ACCEPTED FOR 'USE-AS-IS' PER GNC-ET-9-3. BASED ON FINDINGS OF DC&R E-83-025 & DC&R E-83-026, ONE SENSOR OUT OF 82 INSPECTED DID NOT HAVE THE TANG REMOVED. STRESS ANALY INDICATES THAT TANGS WILL NOT BECOME DISLODGED DURING PROPELLANT LOADING OR FLT, THEREFORE THIS IS NOT A CONTAMINATION ISSUE. RECURRENCE CONTROL - NONE REQ'D; VENDOR PROCEDURE IS ADEQUATE, PERSONNEL HAVE BEEN INSTRUCTED, CON- SEQUENTLY UNITS BEGINNING WITH LWT-8 SHOULD HAVE ALL TANGS REMOVED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A06909 | IFA# -- | Contractor RPT# E-075-3 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# MC432-0205-0019 | Asmnt Part Name L02 LEVEL SENSOR | Asmnt Serial/Lot# 101 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE UC - UNSAT |
| Asmnt FMEA 3.1.2.2 | Asmnt FM 2 | FMEA CSE A | FMEA SCSE 4 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |