MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A08605 | In-Flight Anomaly Number -- | Contractor Report Number S-066 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 DOME TANGS/CHORDS-MISALIGNMENT |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (3) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT-20 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 DOME | PART# 80914920900 | SER/LOT# N/A | MANUFACTURER MMC |
| Test/Operation M - MFG | Prevailing Condtion N - INSPECTION | F / U UC | Fail Mode UC - UNSAT | Cause MAT - MFG-ASY-EQUP |
| System STRUCTURAL | Defect MA - ME ADJ | Material S - STRUCT | Work Contact C. VOGEL | Fail Date 08/25/1984 |
| Received at MSFC 09/10/1984 | Date Isolated -- | FMEA Reference 1.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom UC - UNSAT | Time Cycle -- |
| Effectivity Text LWT-30 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 06/17/1985 | Defer Date -- | Add Date -- | R/C Codes 3 - F/TE -- -- |
| Assignee |
| Design J. WHITE | Chief Engineer -- | S & MA D. NEWMAN | Project M. PESSIN | Project MGR -- |
| Approval |
| Design J. NICHOLS | Chief Engineer -- | S & MA D. NEWMAN | Project M. PESSIN | Project MGR -- |
| PAC Assignee G. MILLER | PAC Review Complete GM | MSFC Closure Date 07/09/1985 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: A PRODUCTION PROBLEM EXISTS IN THE ALIGNMENT OF THE INNER TANGS WHICH ARE A PORTION OF THE DOME CHORDS. AN OFFSET BETWEEN THE TANGS OF ADJACENT CHORDS HAS BEEN SEEN AT THE DOME MECHANICAL ASSEMBLY LEVEL THIS HAS IN SOME CASES REQUIRED THE USE OF OPTICS FOR LEVELING THE DOME PRIOR TO MACHINING AND IN SOME CASES MRB DISPOSITION FOR MISALIGNED HOLES (REF. T-27929). THIS IS A PRODUCTION PROBLEM. THE PROBLEM OF INNER TANG ALIGNMENT BETWEEN CHORDS USUALLY RESULTS IN INCREASED PRODUCTION EFFORT BECAUSE OF THE NEED FOR OPTICS AT THE T02A7018 FIXTURE FOR LEVELING. IN SOME CASES SUCH AS LWT-20 (T-69670) HOLE ALIGNMENT RELATIVE TO PLANE AC RUNNING THRU THE TANG IS VIOLATED AND MRB REVIEW IS REQUIRED (STRESS ANALYSIS OF ALL CASES TO DATE HAS SHOWN AN ADEQUATE MS). PRIOR CORRECTIVE ACTION TAKEN IN MARCH 1984 RESULTED IN TCN 277 THAT CORRECTED THE HEIGHT OF THE PADS WHICH THE INNER TANGS REST ON IN THE 7018 FIXTURE. RECURRENCE OF LEVELING PROBLEMS WHEN MACHINING DOMES IN THIS FIXTURE HAS RESULTED IN RENEWAL OF INVESTIGATION INTO THIS PROBLEM. IT HAS BEEN NOTED THAT THE TANG ALIGNMENT REQUIREMENT OF .020" HAS BEEN VIOLATED IN SOME DOMES AND PRODUCTION PROCESSES AND HARDWARE SHALL BE INVESTIGATED |
| Contractor Investigation/Resolution R/A - TBD 6/6/85 PRB STATUS 4-16-85 MTG - READJUSTED TOOL T10A5002 ADJUSTED LOCATOR BLOCKS & COLOR CODED TO PREVENT MISIDENTIFICATION REPLACED TRIMMING SAW WITH ROUTER. ECD IS 6-15-85. 6/6/85 PRB STATUS - 5-16-85 MTG - PROBLEM APPEARS TO BE RESOLVED WITH USE OF NEW ROUTER MMC WILL EXPEDITE CLOSURE. 6/18/85 - A WAVY TRIM CUT ON THE 5002 TOOL WAS DETERMINED TO BE THE CAUSE OF THE MISALIGNMENT. RESOLUTION - THE 5002 QUARTER PANEL-CHORD TRIM & WELD FIXTURE WAS TRIMMING AN UNEVEN EDGE ON THE CHORD. THIS SUBSEQUENTLY CAUSED OFFSETS BETWEEN TANGS TO SHOW UP IN THE T02A7018 MECHANICAL ASSY FIXTURE. THE TRIM LINE WAS CORRECTED BY SEVERAL CHANGES. THE LOCATORS FOR POSITIONING THE CHORD WERE REALIGNED FOR EACH TYPE OF CHORD & COLOR CODED TO PREVENT ACCIDENTAL INTERCHANGING. THE CIR- CULAR SAW CUTTER, WHICH WAS ANGLED BY DESIGN FROM VERTICAL, WAS REPLACED WITH A ROUTER ORIENTED VERTICALLY. THE SAW BLADE COULD MISTRACK DUE TO THE HIGHER BENDING MOMENTS PLACED ON IT FROM THE WIDE BLADE. NO MARS TO DATE HAVE BEEN WRITTEN AT THE T02A7018 FOR THE ABOVE PROBLEM SINCE LWT-30, WHEN THESE CHANGES WERE MADE (6 UNITS CHECKED). RECOMMEND THIS PROBLEM REPORT BE CLOSED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A08605 | IFA# -- | Contractor RPT# S-066 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80904000000-020 | Asmnt Part Name LH2 TANK COMPLETE | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 3 | CAUSE CD MAT - MFG-ASY-EQUP | FAIL MODE UC - UNSAT |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |