Hurricane Ike Situation Report # 5

September 16, 2008 (10:00 AM EDT)

http://www.oe.netl.doe.gov/emergency_sit_rpt.aspx

Summary

Notes:

Total state customers are based on 2006 EIA Customer Data.

Note: due to a large number of service providers, including investor owned utilities and cooperatives, the number of customer outages reported may not be comprehensive.

Source:

Crude Oil and Natural Gas Production Data from Minerals Management Service.

Refinery Status confirmed by company or on company web site and through various trade press sources.

* % capacity out represents percent of production capacity in the Gulf of Mexico.

Highlights:

- As of 8:00 AM EDT September 16, there are an estimated 3,876,719 in the States most heavily impacted by Ike (see summary table above) plus an additional 12,024 in Illinois, West Virginia, and Missouri.  Largest outages remain in Texas where 2,202,334 customers are without power.

- On September 15, the U.S. Environmental Protection Agency issued a waiver for Texas permitting the use Federally-compliant ultra low sulfur diesel (ULSD) in lieu Texas Low-Emission Diesel (TxLED) through September 30, 2008.

- The Coast Guard Captain of the Port of Houston-Galveston has re-opened portions of the Gulf Intercoastal Waterway and Houston Channel to commercial vessel traffic, with some restrictions.  The following openings and restrictions are in effect: - The Houston Channel is open to outbound commercial vessels with a draft of 12-feet or less. The Gulf Intracoastal Waterway (GIWW) is open to from the Houston and Galveston area, west toward Corpus Christi, Texas.  The GIWW from Houston to Port Arthur, Texas is not passable from mile marker 238 to 350.  The Port of Freeport, Texas is still closed.  The waterways in the Port Arthur, Texas area are restricted to vessels with a draft of 16 feet or less.  The Port of Lake Charles, LA is closed.  There are many restrictions in effect in Louisiana waterways including the Lower Mississippi River.

- As of 1:45 AM EDT September 15, the LOOP resumed tanker offloadings.  The LOOP continues to make deliveries to customers from its Clovelly storage facility.

ESF 12 Actions:

- ESF-12 is working to facilitate restoration of critical assets in the affected area.  This includes coordination with DHS and the Ohio National Guard to use a Chinook helicopter for carrying heavy equipment needed to rebuild parts of the Entergy system. ESF-12 also is working closely with those conducting assessments of physical energy infrastructure in the field which will assist in developing restoration estimates.  On September 14, ESF-12 worked with DHS to facilitate air-based damage assessments of the CenterPoint and Entergy electric transmission systems.  ESF-12 responders participated in the flights to assist in these assessments.

- ESF-12 staff is enroute to the Region V Regional Response Coordination Center (RRCC) in Chicago, IL. ESF-12 is staffing the FEMA Region VI RRCC in Denton, TX, the FEMA Region VI Joint Field Office (JFO) in Austin, TX, the FEMA Region VI (JFO) in Baton Rouge, LA, and the National Response Coordination Center (NRCC) in Washington, DC.   In addition, a petroleum expert has been deployed to San Antonio, TX to serve as part of FEMA's National Incident Management Assistance Team (IMAT) and an electricity expert has been deployed to join the Region IV IMAT in Houston, TX.

Situation Report Detail

Petroleum & Gas Information

Source:   Minerals Management Service

- As of September 15, the Minerals Management Service (MMS) reports 6,942 million cubic feet per day (MMcf/d) of the Gulf’s natural gas production remains shut-in, equivalent to 93.8  percent of the Gulf production. MMS reports 1,298,309 barrels/day of the Gulf’s crude production remains shut-in, equivalent to 99.9 percent of the Gulf’s crude production. A total of 562 production platforms, or 78.4 percent of the Gulf’s 717 manned platforms, have been evacuated. Personnel from 82 rigs, representing 67.8 percent of those operating in the region, have been removed.

- On September 15, the head of Louisiana’s Department of Natural Resources reports that 33,975 barrels/day or 22 percent of the normal Louisiana oil production has been restored.  Operators in 17 parishes and in State offshore areas normally produce 155,767 barrels/day (the numbers are in addition to MMS reports of Federal offshore production).  Shut-in oil production is 85,730 barrel/day or 55 percent of the normal production and the status of 36,062 barrels/day is unknown.  The estimated amount of restored gas production is 548 MMcf/d or 33 percent of the daily gas production capacity, which is 1,642 MMcf/d.  The estimated amount of shut-in gas production is 703 MMcf/d and the status of the remaining 389 MMcf/d has not been confirmed.

- Major crude pipelines originating in Texas and Louisiana shut down operations in advance of Hurricane Ike, and many remain shut. Colonial pipeline reported at 7:30 PM EDT September 15, that the pipeline is receiving injects from storage facilities and refineries at Collins, MS, Baton Rouge, LA, Lake Charles, LA, and Pasadena, TX.  Portable generators have been installed in Beaumont where commercial power is at least a week away. (See table below.)

Source: Status of pipelines from Association of Oil Pipe Lines; Capacity data from company web sites.

- As of 9:00 AM EDT September 16, fourteen refineries in Texas and Louisiana are reported shut down due to Hurricane Ike.  These refineries located in Lake Charles/Port Arthur and Houston/Texas City, and have a total operable capacity of 3.6 million b/d.  (See table below.)

- Oil companies are installing generators at gas stations in the Houston and Beaumont area, especially along re-entry routes, where power is not reliable.  Shell reported deploying 19 generators as of September 15, and securing another ten generators for potential deployment later this week.  ExxonMobil and Chevron both report installing portable generators and making product deliveries at priority or strategic sites. Chevron also dispatched 20 tanker trucks from other areas of the country to Houston to expedite fuel distribution in the impacted area.

- ConocoPhillips reports that the Pasadena, TX, refined products distribution terminal reopened on the morning of September 15.  The Clifton Ridge Marine Terminal near Lake Charles, LA is also now open.

Note: 	The table does not include all refineries in the PADD III, Gulf Coast Region.

Storm column indicates hurricanes impacting refineries: G = Gustav; I = Ike, G+I = Both storms, and - = no impact.

Sources:  Confirmed by company or on company web site. Various trade press sources.

- The Independence Hub platform, located about 150 miles offshore LA in Mississippi Canyon reported gas flow of over 700 million cubic feet on September 15, which is an increase of approximately 100 million cubic feet from September 14, 2008.  This platform is the largest producing platform representing approximately 12% of the offshore Gulf of Mexico natural gas production and in July 2008, production from the Hub averaged over 800 MMcf/d.

- Damage assessments by natural gas pipeline operators are well underway.  Points that were in the path of Ike are for the most part reporting flood damage and lack of power. Some facilities still have standing water and it will likely take several weeks for repairs and clean up in order to restart these facilities.  If the standing water is sea water then expected even longer delays in restarting.   There have been reports of minor damage to off-shore facilities including pipeline breaches on several main and gathering lines.  It is too early to generate a detailed damage repair schedule, but as of now these repairs should not take more than a few weeks to complete weather permitting.

- As of 6:28 PM EDT September 15, the Enbridge Offshore pipeline systems remain under Force Majeure and remain shut-in until operation personnel can gain access to the facilities and conduct more thorough inspections.  See table below for more details.

- As of 9:00 PM EDT September 15, Tennessee Gas Pipeline (TGP) reports that all points upstream of the Grand Chenier and Sabine processing plants remain shut in.  Crosstex informed TGP that the Sabine plant experience storm surge and assessments are underway and the Bluewater plant is currently ready to process once upstream flow commences.  The Grand Chenier, owned by CDM Max reports to TGP that personnel are conducting damage assessments.  Lastly, Targa Resources, partial owner and operator of the Yscloskey plant in St. Bernard Parish, LA experienced additional water damage from Ike.  The plant has been reported shut down since Hurricane Gustav.

- As of 5:30 PM EDT September 15, Destin Pipeline Company has been notified by the Pascagoula Processing plant that volumes currently available on the Destin system are insufficient for commencing plant operations. This is considered a force majeure event by the plant for gas day September 15, 2008 and will remain in effect until further notice.  Note the Pascagoula plant is not depicted on the table as it was running at reduced levels when Ike made landfall.  The plant has an operating capacity of 1.5 Bcf/d

- There are 39 major natural gas processing plants in the path of Hurricane Ike with a total operating capacity of 17.6 billion cubic feet per day (Bcf/d).  As of 10:00 AM EDT, September 15, the Energy Information Administration (EIA) has confirmed that 23 plants remain shut down which includes those plants still impacted from Gustav, totaling an operating capacity of 11.29 Bcf/d (almost 65 percent of the capacity in Hurricane Ike’s path).  Thirteen of the 23 plants are located in LA.  In addition, EIA reports that 10 plants have resumed operations at reduced or normal levels totaling 4.26 Bcf/d operating capacity and 5 plants are capable to restart totaling 1.9 Bcf/d operating capacity once power is restored or upstream gas flow commences.

Note:  Storm column indicates hurricanes impacting processing plant:  G = Gustav; I = Ike, G+I = Both storms, and M = Maintenance

“N/A” (Not Available or Confirmed) identifies those plants that are in the path of Ike that have not yet been confirmed of their status.			1 The capacity represents the design capacity of the plants and does not represent the actual gas flow through these plants.

2 Confirmed plants capable to restart after electricity is restored or when upstream gas flow commences service.

Sources:  Confirmed by company or on company web site. Various trade press sources.

Electricity Updates:

| Louisiana: |  |
| --- | --- |
| As of: | 9/16/2008 6:30 AM EDT |  |

Total state and utility customers are based on 2006 EIA Customer Data; Electric Cooperative customer totals provided by Louisiana Public Service Commission.

Note: due to a large number of service providers, including investor owned utilities and cooperatives, the number of customer outages reported may not be comprehensive.

- As of 6:30 AM EDT September 16, there are 60,152 customers without power in Louisiana.  This is a decrease of 45,829 outages from Ike Situation Report No. 4.  Of remaining outages, 94,120 are due to Ike and 11,861 are due to Gustav.  Entergy has restored power to 938,374 customers who lost power due to Gustav and Ike.  Entergy reports that remaining Gustav damage to the transmission system includes 15 lines and seven substations out of service. SWEPCO reports as of 8 p.m. Monday, four transmission lines were out of service as a result of the storm.

| Texas: |  |
| --- | --- |
| As of: | 9/15/2008 8:00 PM EDT |  |

Total utility customers are based on field reports.

Note: due to a large number of service providers, including investor owned utilities and cooperatives, the number of customer outages reported may not be comprehensive.

- As of 8:00 PM EDT September 15, over 2.2 million people are reported without power in Texas.

- As of 9:00 PM September 15, CenterPoint reports the number of facilities out of service include: 90 transmission facilities; 126 equipment in substations; and 1,348 distribution circuits.  The number of facilities restored includes: 55 transmission facilities; 119 equipment in Substations; and 342 distribution circuits.

Additional State Reports:

- Ike caused major power outages in Arkansas and parts of the Midwest, Ohio Valley and Northeast.  Outages as of 8:30 AM EDT September 16:

  - Ohio -  1,046,100 outages, 19 percent of total customers

  - Kentucky – 355,900 outages, 16 percent of total customers

  - Indiana – 85,200 outages, 3 percent of total customers

  - New York – 33,700 outages, less than 1 percent of total customers

  - Arkansas – 33,433 outages, 2 percent of customers

  - Missouri - 8,400 outages, less than 1 percent of total customers

  - Illinois - 600 outages, less than 1 percent of total customers

  - Pennsylvania – 59,600, 1 percent of total customers

  - West Virginia – 3,024 less than 1 percent

Restoration Updates:

- As of 9:00 PM September 15, CenterPoint has restored power to over 583,000 customers. Centerpoint estimates that 50 to 75 percent of its customers will have power restored within seven to ten days; the reminder within three weeks, based on current assessments.  CenterPoint has 4,200 internal and contractor personnel and over 7,000 mutual assistance crews from over 25 states assisting in the restoration.

- CenterPoint reports that 7,000 mutual assistance personnel began to arrive September 14 to assist in restoration. Highlights of CenterPoint’s recent  restoration include:

  - The Department of Energy Bryan Mound facility, an important component of the United States Strategic Petroleum Reserve

  - Colonial Pipeline

  - 43 area hospitals

- In Texas, Entergy made initial transmission restoration to Beaumont-area substations on September 15.

- Entergy and CenterPoint worked together to restore an emergency tie between the two companies to the main water supply for the city of Houston.

- Entergy reports transmission outages caused by Ike include 278 of 312 substations and 183 of 187 transmission lines out of service in Texas.  Entergy’s Lewis Creek plant in Montgomery County, Texas, has shut down as a result of storm damage. It will be able to restart within a 16 hours after offsite power is restored. Restoration of transmission service to the Lewis Creek plant is being worked as a high priority. Lewis Creek will be able to restart within a few hours after offsite power is restored. The loss of generation from Entergy’s Sabine plant due to flooding from Hurricane Ike's storm surge resulted in a generation shortfall in the Western region of Entergy Texas, Inc.’s territory. Until damage to the plant can be assessed and restoration time can be estimated Entergy is balancing system load and generation.  Flood waters at Sabine have receded and safety assessment and environmental clean-up has begun.

- Entergy has offsite crews from 34 states.  Due to the large number of outages caused by Ike in over 10 states, availability of Entergy’s approximately 14,000 restoration crews could change as contract crews are recalled to other states.  As restoration is made in Arkansas and Louisiana, Entergy is shifting its crews to Texas.

- In Louisiana, Entergy restoration estimates by Parish are:

  - September 16  - East Feliciana

  - September 17 - Assumption, East Baton Rouge

  - September 18 - Jefferson (lower portion only, except Grand Isle), Plaquemines.

  - September 20 - Lafourche (except Fourchon).

  - September 24 - Ascension (Donaldsonville), Iberville, Lafourche (Fourchon), St. Martin.

  - September 27 - Terrebonne.

  - October 1 - Jefferson (Grand Isle).