DATE:			December 24, 2002	STUDY NUMBER:	03SN65-06

Requested By:	Rick Pendergrass

Due Date:		January 10, 2003

Purpose of Study:	Provide information for the FY03 Safety Net Cost Recovery Adjustment Clause considerations.  This study is similar to the 03SN65-05 study (intended to reflect operations in FY06) except updating the juvenile bypass spill at Lower Monumental (reduce spill due to RSW installation). Changes from 03SN65-05 are highlighted in grey.

This is a continuous study of the system operation under the 2000 NMFS and USFWS Biological Opinions. There are no spring flow augmentation targets for Priest Rapids, McNary or Lower Granite. Refill of reservoirs by June 30 takes precedence in all water years.

Directory of Study:		AER Step:

MODELA::DISK2:[NPR.FISHOPS.OY00.03SN65_04.AER]

LOGICAL: 00FSH_:[03SN65_04.AER]

OPER Step:

MODELA::DISK2:[NPR.FISHOPS.OY00.03SN65_06. OPER]

LOGICAL:  00FSH_:[03SN65_06.OPER]

#### Name of Regulator:	Jennie Tran

AER STEP

- This AER Step is used to determine the project minimum elevations (or maximum draft) using load equal to OY01 Firm Energy Load Carrying Capability (FELCC) and unlimited secondary market. Minimum elevations from the AER Step will be input into the Operational Step.

- This is a continuous study based on the OY01 PNCA data submittal. The study will begin on Aug. 1, 1928 and end on July 31, 1978, a 50-year study.

- Stream Flow: The 50 years of Modified Stream flows used are from “Modified Streamflows 1990 Level of Irrigation”, dated July 1993. They contain 1990 level irrigation depletion’s. Adjustments to these 1990 level modified stream flows are due to the Bureau of Reclamation’s updated Grand Coulee pumping schedule for the Columbia Basin Project. This pumping schedule is included in the BOR’s February 1, 2000 preliminary PNCA data submittal. No adjustments are made for NTSA storage and release. The inflows to Brownlee are adjusted by the BOR’s regulation of the Upper Snake projects to release 427 kaf (see Upper Snake).

- Plant Data: The OY01 plant data will be used with the following modifications: Packwood is a hydro independent plant in this study.

- Loads: All FELCC is taken from the OY01 Critical Period study run by the Northwest Power Pool (NWPP). The NWPP study has a one-year critical period (August 16, 1936 through March 31, 1937). Thus, only one year of FELCC values are used for all water conditions. This study reflects coordination between PNCA parties in meeting PNCA FELCC. Therefore, generation from projects owned by non-PNCA parties (Brownlee, Oxbow, Hells Canyon, and Canadian projects) is not used to meet PNCA FELCC in these studies. August, May, June, and July FELCC comes from the PNCA Final Regulation, which includes flow augmentation target flows at McNary and Lower Granite. FELCC plus Hydro-Independent generation from 1936-37 is the system total generation. Then, the system total generation will be reduced by 50 years of hydro-independent generation (PS_HI:HI9706_60YR_COOR.HYMOD) to produce 50 years of FELCC. There will be an unlimited secondary market.

- Unit Outages: The unit outages for non-federal projects were taken from the OY01 data submittal.  For federal projects the unit outages were based on the actual outages from 1999-2001, and these outages were adjusted to exclude unusual outages.

- Initial Contents: Storage reservoirs are initialized to full on 1 August 1928, with the following exceptions. Mica is initialized to the July target of 5752.1 ksfd (3456.2+2295.9 ksfd). Grand Coulee is initialized to 1285.0 feet (2408.4 ksfd). Brownlee is initialized to 2067.0 feet (422.4 ksfd). Libby is initialized to 2439 feet (2061.3 ksfd). John Day is initialized to 262.5 feet (127.7 ksfd). Corra Linn is initialized to 1743.32 feet (285.4 ksfd). Hungry Horse is initialized to 3560 feet (1548.5 ksfd). Dworshak is initialized to 1570.0 feet (753.0 ksfd). The lower Snake projects are initialized to their MOP elevations in July:  Ice Harbor 437.0 feet (193.4 ksfd), Lower Monumental 537.0 feet (180.5 ksfd), Little Goose 633.0 feet (260.5 ksfd), and Lower Granite 733.0 feet (225.0 ksfd).

- CRC Rule Curves: Critical Rule Curves (CRC) used are in accordance with PNCA 2001 adopted system critical rule curves. They are as follows: 1st year = OY01 CRC1; 2nd year = empty; 3rd year = empty; and 4th year = empty.

- Flood Control Rule Curves: Variable Flow (VARQ) flood control curves for Hungry Horse, Libby and Grand Coulee were provided by the Corps of Engineers to BPA on July 10, 2000.  On July 14, 2000 Bureau of Reclamation provided the new flood control (for Hungry Horse only) to replace the data from the COE.  The curves for Grand Coulee contained in the COE data set are adjusted for the amount of storage capability available below URC on April 30 each year for Mica, Arrow and Duncan to more closely reflect the methodology used in real-time operations.

- ECC Curves: VECC’s are calculated using OY01 Power Discharge Requirements (PDR’s), distribution factors and forecast errors which are used in PNCA planning. The ECC lower limit of 1225 feet (420.5 ksfd) in January-April 15, 1280 feet (2216.4 ksfd) April 30-May, 1290 feet in June-July at Coulee was used in calculating the VECC during periods in which the system is generating surplus energy. The Canadian AOP VECC’s are based on historical volumes and the Arrow Total method. The VECCs for the Federal projects are based on the Kuehl-Moffitt volume forecast (Kuehl-Moffitt Report dated July 1986).

Project Specific Data:

- Mica, Duncan and Arrow will be on their AOP02 operations including changes agreed to by the Entities as described in the DOP02. The Canadian Treaty projects are fixed to the 50-year DOP Treaty Storage Regulation run by BPA. Mica data logic in the Hydrosim program is turned off. Mica’s minimum storage content is reset to 0.0 ksfd so that drafting below 2295.9 ksfd (normal minimum content) can occur.

- Libby is operated to the draft limits of 2432.5 ft (1923.8 ksfd), 2425.5 ft (1781.8 ksfd), 2418.6 ft (1644.8 ksfd), and 2411.0 ft (1502.4 ksfd) in September through December to meet December URC of 2411.0 feet.  In January through mid-April, Libby is operated on minimum flow or VARQ flood control objectives as defined in the BiOP. It should be noted that Libby does violate URC for Corra Linn’s IJC operation. Sturgeon flow requirements are as follows:

| Libby is operated during May-July for Sturgeon./Bull trout in all years. The project draft limit for contributing to the McNary salmon flow augmentation target is 2439 ft (2061.3 ksfd) in August. Libby’s maximum outflow from mid-April through August is powerhouse hydraulic capacity without spill unless a higher outflow is required to maintain the required VARQ flood control space. |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

- Hungry Horse is operated in proportional draft mode September through December subject to draft limits of 3560 (1548.5 ksfd), 3555.7 (1496.8 ksfd), 3544 (1358.7 ksfd) and 3533 feet (1235.4 ksfd), respectively. In October through December it will not be operated above 3555.7 feet (1496.8 ksfd) to protect against winter floods. The reservoir storage-elevation relationship will reflect 3% bank storage. From January through March, Hungry Horse operates to the higher of IRC of 3520 ft (1098.4 ksfd) or Biological Rule Curve objectives but below a maximum content calculated to reduce the possibility of forced spill. The Biological rule curves are calculated using assumed inflows which are exceeded 75 percent of the time, perfect foreknowledge of the minimum outflow, and the requirement to be at flood control elevation on April 10. In April through June, Hungry Horse operates on or near flood control. On July 31, August 15 and August 31, Hungry Horse draft limit is 3560, 3550 and 3540.0 feet (1548.5, 1428.3 and 1313.2 ksfd) for McNary and Priest Rapids flow augmentation. Hungry Horse will be operated to support the Columbia Falls minimum flow of 3,500 cfs year round and maximum flow of 4,500 cfs October 15 through December 15. Hungry Horse maximum outflow from mid-April through August is powerhouse hydraulic capacity of 12,000 cfs and no spill is allowed unless required to maintain the required flood control space.  Hungry Horse will violate upper rule curve to keep its maximum outflow to 20 kcfs or below.  During the flow augmentation period, Hungry Horse will release no more water than necessary to meet the minimum flow requirements.  Maximum out flow at Horse is 6800 cfs from June through Labor Day except to contribute flow targets at Priest and McNary.

- Albeni Falls is operated in September – October to 2060.0 feet (465.7 ksfd) and 2056 feet (279.0 ksfd). In November - March, Albeni Falls is operated to 2055.0 feet (234.7 ksfd). In April 15, April 30, and May, Albeni Falls is operated to 2055.5 feet (256.9 ksfd), 2056 feet (279.0 ksfd), and 2057.0 feet (325.7 ksfd), respectively. In June through August, Albeni Falls is operated to full 2062.5 feet (582.4 ksfd) [per Dana Reedy 11/8/99, NWPP].

- Grand Coulee is operated to meet FELCC September through December subject to the draft limits of 1283 feet (2329.7 ksfd), 1280 feet (2216.4 ksfd), 1275 feet (2027.7 ksfd), and 1265 feet (1665.4 ksfd). In January through March, Coulee is operated to the higher of winter draft limits [1260 feet (1491.5 ksfd), 1250 feet (1159.1 ksfd), 1240 feet (843.9 ksfd), respectively] or the minimum storage values calculated.  The Biological Rule Curve reflects the expected April 10th URC and storage needed for the appropriate Vernita Bar minimum flow requirement. Grand Coulee is then operated above these minimum storage points. On April 15, Coulee is operated on flood control.  From April 30 through May, Grand Coulee may be drafted to the lower of flood control or 1280 feet to support Priest Rapids and McNary flow augmentation targets. In June - August, Grand Coulee draft limits are 1290 ft (2614.3 ksfd), 1285 feet (2408.2 ksfd), 1280 feet (2216.4 ksfd), and 1280 feet (2216.4 ksfd) respectively to support Priest Rapids and McNary flow augmentation targets. At-site minimum flow is equal to 30,000 cfs. Grand Coulee is subject to a draw down limit of 1.5 feet per day when Coulee is above 1260 feet, 1.3 feet per day when Coulee between 1260 and 1240 feet, and 1.0 feet per day when Coulee is below 1240 feet. During the flow augmentation period, Grand Coulee will release no more water than necessary to meet the minimum flow requirements.

- Vernita Bar minimum flows for December through May vary by water condition, with minimum flows established as the lesser of a) 68% of the largest of the October or November flow at Wanapum or b) 70,000 cfs. Values less than 70,000 cfs are rounded to the nearest 5,000-cfs. The minimum protection level flow at Vernita Bar will be 50,000 cfs.

- Priest Rapids: From April 10 to June 30 Priest Rapids has a flow augmentation target of 135000 cfs for Steelhead. The April 1 to April 9 the minimum flow for Priest Rapids is the same as the Vernita Bar minimum for each year.

- The Upper Snake reservoir operations adjustments to Brownlee inflows came from the BOR in May 1997. The operation tries to release 427 kaf in as many years as possible over the 50-year record during the May through August period.

- Brownlee will be on flood control from February through April. In May, the reservoir is operated to 2069 feet (436.3 ksfd). In June Brownlee is filled if necessary and maintained at elevation 2077 feet (491.7 ksfd). In July, August 1 and August 2, the reservoir is drafted to 2050 feet (320.4 ksfd), 2050 feet (320.4 ksfd) and 2045 feet (293.8 ksfd), respectively for flow augmentation that includes both IPCO contribution and shaping of Upper Snake water by the end of August. In September and October, the reservoir operates to 2045 feet and 2035 feet (242.0 ksfd), respectively in anticipation of providing a maximum discharge of 9,000 cfs from mid-October through November. Outflows up to 20,000 cfs are allowed in October (the average of 30,000 cfs in the first half and 9,000 cfs to 13,000 cfs in the second half of the month). No higher than 9,000 cfs is allowed in November. At the end of December and January, the reservoir is operated at 2070 feet (443.2 ksfd) and 2060 feet (379.5 ksfd), respectively.

- Dworshak is on minimum flow of 1300 cfs all periods or flood control objectives as defined in the BiOP, with the exception of April through August when it operates to meet Lower Granite flow augmentation targets. On April 15- August 31 Dworshak may draft to elevation 1520 feet (395.8 ksfd) to support Lower Granite flow augmentation targets. Note: Dworshak’s outflow is limited to 14,000 cfs during the flow augmentation period (April 3 through August 31) and is limited to 25,000 cfs in all other periods for downstream flood control. During the flow augmentation period, Dworshak will release no more water than necessary to meet the minimum flow requirements.

- The four lower Snake River projects (Lower Granite, Little Goose, Lower Monumental and Ice Harbor) and the four lower Columbia River projects (McNary, John Day, The Dalles and Bonneville) each are required to operate their turbines within 1% of peak efficiency during the period of March through November. This requirement is reflected in a hydro availability file, which limits the maximum generation capability of each project in each of the fourteen periods. No other hydro outages assumed.

- Generation at these eight projects (Lower Granite, Little Goose, Lower Monumental, Ice Harbor, McNary, John Day, The Dalles and Bonneville) is reduced further with the inclusion of Juvenile Bypass 2004 expected Fish Spill Plan. Juvenile Bypass Fish Spill at Federal projects (values less than one are percent of outflow and values greater than one are cfs), limited by Spill Caps, is as shown below. The spill caps represent completed modifications at spillways currently planned and which are used as hydroregulation modeling caps, not instantaneous. Lower Granite, Little Goose, Lower Monumental, Ice Harbor, McNary, John Day, The Dalles and Bonneville have a minimum turbine flow of 12000, 12000, 12000, 5500, 50000, 50000, 50000, and 30000-cfs respectively.

- Juvenile Bypass Spill and Dissolved Gas Caps:

There will be no Juvenile Bypass Spill requirement at Lower Granite, Little Goose, and Little Monumental if the regulated flow at Lower Granite is less than 85,000 cfs.

Lower Granite, Little Goose, and Lower Monumental will spill the amounts listed above, when the April through July volume forecast is greater than or equal to 17.5 MAF. Once spill has started, it will continue through June 20 even though subsequent forecasts may drop below 17.5 MAF.  Ice Harbor attempts to spill at the amounts listed above in all years.

- Lower Columbia fall spawning flow objectives (at Bonneville) are as follows: From November 1 through December 31 provide 125 kcfs.  The priority for releasing water from upstream reservoirs for this flow augmentation is Grand Coulee, Libby, and Hungry Horse.   The draft limits for Chum flow in Nov-Dec are: 3555.7 feet (1497.0 ksfd), and 3549.2 ft (1418.7 ksfd) respectively at Hungry Horse; 1275 ft (2027.7 ksfd) and 1265 feet ( 1665.4 ksfd) respectively at Coulee; 2418.6 ft (1644.8 ksfd), and 2411.0 ft (1502.4 ksfd) respectively at Libby.

- Use a sliding scale flow augmentation target of from 220,000 to 260,000-cfs at McNary based on The Dalles April 1, January through July volume runoff. A straight-line interpolation will be used for flow targets for volume forecasts between 85 and 105 Maf in the April 20 through June period. AP2 values are prorated at 4 days at 155,000 cfs and 11 days at from 220,000 to 260,000 cfs. Maximum and minimum targets are 260,000 cfs and 220,000 cfs, respectively. July and both halves of August flow targets are 200,000 cfs. The priority for releasing water from upstream reservoirs for flow augmentation is Grand Coulee, Libby and Hungry Horse.

- Lower Granite also has sliding scale flow augmentation targets. When the April 1 Lower Granite April through July runoff forecast is less than 16 Maf, then the April 3 through June 20 flow target is 85,000 cfs and the June 21 through August flow target is 50,000 cfs. When the April 1 Lower Granite April through July forecast is greater than 20 Maf, then the April 3 through June 20 target flow is 100,000 cfs. When the April 1 Lower Granite April through July forecast is greater than 28 Maf, then the June 21 through August target flow is 55,000 cfs. The spring flow targets are interpolated for forecasts between 16 and 20 Maf and the summer flow targets are interpolated for forecasts between 16 and 28 Maf.

- John Day is operated at 262.5 feet (127.8 ksfd) from mid-April through September. From October through mid-April, John Day operates to elevation 265 feet (191.0 ksfd).

- Lower Snake projects will be operated at MOP in accordance with the COE data submittal and the 1995 BiOp. As identified in the BiOp, the Corps will operate Little Goose, Lower Monumental, and Ice Harbor within one foot of minimum operating pool (MOP) during the period from approximately April 3 through August 31. Lower Granite will operate within one foot of MOP from approximately April 3 through November 15. MOP for Lower Granite, Little Goose, Lower Monumental and Ice Harbor is elevation 733 (225.0 ksfd), 633 (260.5 ksfd), 537 (180.5 ksfd) and 437 feet (193.4 ksfd), respectively. During the rest of the year Lower Granite, Little Goose, Lower Monumental and Ice Harbor will operate at elevation 738 (245.8 ksfd), 638 (285.1 ksfd), 540 (190.1 ksfd) and 440 feet (204.8 ksfd), respectively.

- Juvenile Bypass spills at non-Federal projects will be as described below and as was submitted for OY01 PNCA planning.

PROJECT SPILL FOR FISH IN

PERCENT OF REGULATED FLOW (%)

| PROJECTS: | Apr1 | Apr2 | May | Jun | Jul | Aug1 | Aug2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wells | 0.0 | 6.5 | 6.5 | 0.0 | 6.5 | 2.5 | 0.0 |  |
| Rocky Reach | 0.0 | 12.0 | 15.0 | 4.4 | 8.0 | 4.0 | 0.0 |  |
| Rock Island (cfs) | 4,800 | 19,300 | 23,000 | 23,000 | 23,000 | 19,300 | 4,800 |  |
| Wanapum | 0.0 | 50.0 | 50.0 | 42.5 | 35.0 | 35.0 | 35.0 |  |
| Priest Rapids | 0.0 | 75.0 | 75.0 | 60.0 | 45.0 | 45.0 | 45.0 |  |

- Kootenay Lake shall be operated as necessary, up to free flow, to maintain the lake level below the IJC rule curve and the calculated “allowable elevation at Queens Bay”. This is implemented using the 5 step method as developed by BPA and the Corps. After August 31, the lake level may be raised to elevation 1745.32 at the Queens Bay gage. This maximum elevation at Queens Bay is in effect through January 7. After January 7 the lake will be lowered to elevation 1744 on February 1, elevation 1742.4 on March 1, and 1739.32 on April 1. April through August 31, after the lake exceeds elevation 1739.32 feet at the Queens Bay gage, the lake shall be operated using the “allowable elevation” calculation to determine the Queens Bay maximum allowable elevation until the elevation at the Nelson gage drafts back to elevation 1743.32 feet.

OPER STEP

- All AER step criteria apply unless specifically amended below.

- Loads: The system is run to 2000 Coordinated system firm loads from BPA’s White Book. A secondary market of 9,000 aMW is used in every period, every year.

- Initial Contents: Brownlee is initialized to 2050.0 ft (320.4 ksfd) on August 1, 1928.

- Non-federal projects are run to the contents that resulted in the AER step.

- Lower Columbia fall spawning flow objectives (at Bonneville) are as follows: From November 1 through December 31 provide 125 kcfs  Grand Coulee, Libby, and Hungry Horse will release water (in that order) to meet the Lower Columbia fall spawning salmon flow objectives at Bonneville in November and December.  Each reservoir has been assigned a lower draft limit only in November and December so that each will draft no lower than the draft limit before the next priority reservoir is used.  The January-April 15 operation of the three reservoirs is to achieve the Biop April 10 URC objectives.   Hungry Horse, Grand Coulee, and Dworshak will be on minimum flow from April through June 30 in all water years (No spring flow targets required at Priest Rapid, Lower Granite, and McNary projects).  This operation is intended to maximize storage in the federal projects by June 30 to maximize the water available for summer flow augmentation.  These projects will release above minimum outflow only as needed to meet flood control requirements.  Grand Coulee will draft below flood control if required to meet the Vernita Bar flow requirement.

Project Specific Data:

- Mica, Duncan and Arrow will be on their AOP02 operations including changes agreed to by the Entities as described in the DOP02. The Canadian Treaty projects are fixed to the 50-year DOP Treaty Storage Regulation run by BPA. Mica data logic in the Hydrosim program is turned off. Mica’s minimum storage content is reset to 0.0 ksfd so that drafting below 2295.9 ksfd (normal minimum content) can occur.

- Libby: same as AER step.

- Hungry Horse is operated in September through December at 3560.0 feet (1548.5 ksfd), 3555.7 feet (1497.0 ksfd), 3555.7 feet (1497.0 ksfd), and 3549.2 ft (1418.7 ksfd) respectively, which are the VARQ flood control points. From January through March, Hungry Horse operates above its Biological Rule Curve objectives and below a maximum content calculated to reduce the possibility of forced spill. The Biological rule curves are calculated using assumed inflows that are exceeded 75 percent of the time, perfect foreknowledge of the minimum outflow, and the requirement to be at VARQ flood control elevation on April 10. On July 31, August 15 and August 31, Hungry Horse draft limits are 3550, 3542 and 3540 feet (1428.3, 1341.7, and 1313.2 ksfd) for McNary flow augmentation. When the July 1 April-August volume forecast at The Dalles is less than 80 MAF, the July flow augmentation draft limit is 3545 feet (1370.1 ksfd).  Hungry Horse is operated to support a Columbia Falls minimum flow of 3,500 cfs in September through December as well as a minimum project outflow of 900 cfs.  From January through August, the minimum flows at the project and at Columbia Falls are variable based on each month’s Hungry Horse April-August forecast.  The minimum flows are established using a straight-line interpolation between 400 and 900 cfs for the project and 3,200 and 3,500 cfs at Columbia Falls for volume forecasts between 1190 kAF and 1790 kAf.

- Albeni Falls is operated to 2051 feet (57.6 ksfd) during October through April.

- Grand Coulee’s operation during the September through December period is subject to draft limits of 1280, 1280, 1275 and 1265 feet (2216.4 ksfd, 2216.4 ksfd, 2027.7 ksfd, and 1665.4 ksfd) respectively. From January through March, Grand Coulee operates above its Biological Rule Curve. The Biological rule curves are calculated using assumed inflows that are exceeded 85 percent of the time, perfect foreknowledge of the minimum outflow, and the requirement to be at VARQ flood control elevation on April 10. When the July 1 April-August volume runoff at The Dalles is greater than 92 MAF, Grand Coulee is operated as low as 1285.0, 1280.0, and 1280.0 feet (2408.3, 2216.4, and 2216.4 ksfd) in July through August, respectively, to meet the McNary flow augmentation targets.  When the July 1 April-August volume runoff at The Dalles is 92 MAF or less, Grand Coulee is operated as low as 1285.0, 1278.0 and 1278.0 feet (2408.3, 2140.9 and 2140.9 ksfd) in July through August, respectively, to meet the McNary flow augmentation targets.  At-site minimum flow is 50,000 cfs for peaking purposes.

- Columbia Basin Irrigation Project Pumping (Banks Lake) will be reduced by the equivalent of 5 feet (65.5 ksfd) in August in years when it is needed to meet the McNary flow augmentation target of 200 kcfs.  Additional water is pumped in the following January-April period to return the Banks Lake elevation to its original level.

- In July through August, Dworshak may draft to elevation 1524, 1522 and 1520 feet (422.6, 409.2, and 395.8 ksfd) to support Lower Granite flow augmentation targets.

- Lower Granite has a sliding scale flow augmentation target for the summer. When the June 1 Lower Granite April through July runoff forecast is less than 16 Maf, the June 21 through August flow target is 50,000 cfs. When the June 1 Lower Granite April through July forecast is greater than 28 Maf, the June 21 through August target flow is 55,000 cfs. The summer flow targets are interpolated for forecasts between 16 and 28 Maf.

- Juvenile Bypass Spill and Dissolved Gas Caps (reduced spill at LMN due to RSW installation)

LWG, LGS and LMN spill the amounts listed above when the LWG Apr-Jul volume forecast is greater than or equal to 17.5 MAF.  A test of summer-time spill is in effect. Spill begins on April 3 and ends on August 31 at LWG, LGS and LMN in those years.

LWG spill is 18 kcfs through RSW, 24 hrs/day, April 3 – August 31;

LGS spill is at 120% TDG, 12 hrs/day, April 3 – August 31;

LMN spill is 18 kcfs through RSW, 24 hrs/day, April 3 – August 31;

IHR spill is 18 kcfs through RSW, 24 hrs/day, April 3 – August 31;

MCN spill is at 120% TDG, 12 hrs/day, April 10 – June 30;

JDA spill test of 60% vs. 30% of flow, alternating days, 12 hrs/day, April 10 – August 31;

TDA spill is at 40% of flow, 24 hrs/day, April 10 – August 31;

BON spill test of 120% TDG 24 hrs/day vs. 120% TDG for 12 hrs/day and 75 kcfs 12 hrs/day, alternating days, April 10 – August 31.