Any tank used to transport drip torch fuel or gasoline must be a DOT specification tank.  There are two companies that make tanks with a capacity of less than 119 gallons that are acceptable for the transport of drip torch fuel.  It is desirable to keep the tank capacity under 119 gallons so a CDL is not required.  The tank manufacturers are Custom Metalcraft and Transfer Flow.   The Transfer Flow tank is available in 50, 74, and 100 gallon capacities.  The part numbers are 080-01-09417, 080-01-09420, and 080-01-09416 or 080-01-09418 respectively.  The Custom Metalcraft is available in any capacity specified by the customer.  The Transfer Flow tank is less expensive than the Custom Metalcraft and takes up less room.  (see attached photos).  Any tank under 119 gallons must be labeled with the diamond shaped flammable liquid label.  The Transfer Flow tank must also be marked with the exemption number DOT-E 11911.  I'm not sure what type of pump you are looking for but as far as hand operated pumps are concerned the Fill-Rite Model FR112 and the Blackmer Model BRF210A meet Forest Service requirements (UL or FM approved with a conductive fuel hose).  As far as 12V DC pumps are concerned the Fill Rite Model FR1210C (15 gpm) or the FR4210 (20 gpm) should be acceptable because they are both UL listed and equipped with a conductive hose.  I should mention that to strictly follow DOT the pump can not be installed in the tank during transport.  We are currently working on this issue to determine the direction the Forest Service will take.

As far as the transportation of drip torches is concerned, the 440 pound rule applies to the weight of the fuel and the drip torch.  After weighing a few torches I would estimate that approximately 34 full drip torches could be carried and still remain under materials of trade.  There is some question as to whether or not non-dot specification drip torches can be transported with fuel in them however.  I just got off of the phone with the DOT help line ((800) 467-4922) where I was told that containers used to transport a mixture of diesel and gasoline must either meet OSHA requirements (be UL marked) or meet DOT requirements (UN marked).  Most drip torches do not meet either of these requirements.  The new drip torches that are being procured meet DOT specifications and will be marked UN3B somewhere on the container.

Transfer Flow tanks may be purchased from:

Transfer Flow Inc

1444 Fortress St

Chico, Ca 95973

(800) 442-0056

www.transferflow.com

The fuel pumps are available from:

Grainger (various locations)

www.grainger.com (Look under branch listings to find the Grainger nearest you)