Riparian Forest Buffer

Vermont Conservation Practice Job Sheet	391

Definition

A riparian forest buffer is an area of trees and shrubs located adjacent to streams, lakes, ponds, and wetlands.

Purpose

Riparian forest buffers of sufficient width intercept sediment, nutrients, pesticides, and other materials in surface runoff and reduce nutrients and other pollutants in shallow subsurface water flow. Woody vegetation in buffers provides food, cover and connectivity for wildlife, helps aquatic life by lowering water temperatures by shading the stream or waterbody, and slows out-of-bank flood flows. In addition, the vegetation closest to the stream or waterbody provides litter fall and large wood important to fish and other aquatic organisms as a nutrient source and structural components to increase channel roughness and habitat complexity. Also, the woody roots increase the resistance of streambanks and shorelines to erosion caused by high water flows or waves. Some tree and shrub species in a riparian forest buffer can be managed for timber, wood fiber, and horticultural products.

Where used

Buffers are located along or around permanent or intermittent streams, lakes, ponds, wetlands, and seeps in a variety of settings, such as cropland, rangeland, forest land, and urban areas.

Operation and maintenance

Replace dead and dying woody species in newly established plantings. Trees and shrubs in a riparian forest buffer can eventually become crowded slowing their growth and the growth, survival and composition of understory species. As the buffer matures, periodic harvesting of some of the overstory trees and shrubs becomes an important activity for maintaining plant health and buffer function. To maintain proper functioning of a planting, excessive water flows and erosion must be controlled upslope of the riparian forest buffer (filter strip, diversion, critical area planting, residue management). New plantings must be protected from grazing during establishment (prescribed grazing, use exclusion) period, as well as pests, including competing vegetation and animal pests (deer, beaver and mice).

Specifications

Site-specific requirements are listed on the specifications sheet. Additional provisions are entered on the job sketch sheet. Specifications are prepared in accordance with the VT NRCS Field Office Technical Guide. See practice standard Riparian Forest Buffer, code 391, Tree/Shrub Establishment, code 612, and Forest Site Preparation, code 490 where appropriate.

A riparian forest buffer includes zone 1, the forested area closest to the stream or waterbody, and zone 2, the forested area adjacent to and up gradient of zone 1. Zone 3 is established if periodic and excessive water flows, erosion, and sediment from upslope fields or tracts are anticipated. Zone 3 generally consists of herbaceous plants or grass and a diversion or terrace, if needed.

Riparian Forest Buffer – Job Sheet

| For: | Farm #: |
| --- | --- |
| Field(s): | Tract #: |
| Designed By: | Approved By: Signature: |
| Date: | Date: |

| Purpose (check all that apply) |
| --- |
| Create shade to lower water temps/improve aquatic habitat | Provide a harvestable crop of timber, fiber, forage, fruit, or other wood-tree related crops consistent with other purposes |
| Provide detritus/large woody debris for aquatic/terrestrial organisms | Provide protection against scour erosion within the floodplain |
| Create wildlife habitat and establish wildlife corridors | Restore natural riparian plant communities |
| Reduce excess sediment, organic material, nutrients, pesticides in surface runoff and excess nutrients/chemicals in shallow ground water flow | Moderate winter temperatures to reduce freezing of aquatic over-wintering habitats |
|  | Increase carbon storage |

| Layout |
| --- |
| Water body/course type and name, other: |
| Minimum buffer zone widths (ft) – specify left and right of stream [facing upstream/downstream (circle appropriate one)] for a two-side buffer; use left only for water bodies, such as lakes and ponds; include herbaceous species in zone 3 notes or refer to other jobs sheets. Refer to VT Standard 391 General Specifications, page 6 for appropriate buffer width determination. |
| Zone 1 (min. 15 feet) | Zone 2 (min. 20 feet) | Zone3 (min. 15 feet, when needed) |
| Left: Right: | Left Right: | Left: Right: |
| Notes: | Notes: | Notes: Refer to Filter Strip Job Sheet |
| Buffer zone length (ft): |
| Additional location and layout requirements: |

| Woody Plant Materials Information - Refer to Table 1 page 7, VT Standard 391 General Specifications for species to plant in riparian areas. For plants per acre and avg. spacing, refer to VT standard 391 General Specifications, page 5. |
| --- |
| Species/cultivars: | Plants/acre: | Kind of stock1: | Planting dates: | Avg. Spacing2: |
| Zone # 1 (minimum of two rows) |  |  |  |  |
| 1 |  |  |  | Ft X Ft |
| 2 |  |  |  | Ft X Ft |
| 3 |  |  |  | Ft X Ft |
| 4 |  |  |  | Ft X Ft |
| Zone # 2 |  |  |  |  |
| 1 |  |  |  | Ft X Ft |
| 2 |  |  |  | Ft X Ft |
| 3 |  |  |  | Ft X Ft |
| 4 |  |  |  | Ft X Ft |

1BAreroot, COntainer, CUtting; include size, caliper, height, and age as applicable. 2Spacing between plants to achieve plants/acre.

Riparian Forest Buffer – Job Sheet

Temporary Storage Instructions (Refer to VT Standard and Specification 612)

Planting stock that is dormant may be stored temporarily in a cooler or cool, moist, darkened area up to 3 days. For more than 3 days or for stock that is expected to begin growth before planting, dig a V-shaped trench (heeling-in-bed) sufficiently deep and bury seedlings so that all roots are covered by soil. Pack the soil firmly and water thoroughly. Additional requirements:

Site Preparation (Refer to VT Standard and Specification 490)

Remove debris and control competing vegetation to allow enough spots or sites for planting and planting equipment. The following method of site preparation is planned: ___Mechanical means such as plowing, disking or rototilling, ____Chemical control of vegetation, ___Hand scalping the area where trees are to be planted, ____Other: ____________________________ Additional requirements:

Planting Methods (Refer to VT Standard and Specification 612)

For container and bareroot stock, plant stock to a depth even with the root collar in holes deep and wide enough to fully extend the roots. Pack the soil firmly around each plant. Cuttings are inserted in moist soil with at least 2 to 3 buds showing above ground. Pest Management including weed control is required. Vegetation Mat-Size___________#___________ Tree Shelter-Size____________#_____________ Other ______________________ Additional requirements:

Operation and Maintenance

The buffer must be inspected periodically and protected from damage so proper function is maintained. Replace dead or dying tree/shrub stock to provide adequate plant densities as described in the 391 standard and continue control of competing vegetation to allow proper establishment for at least 3 years. Periodic harvesting of trees and shrubs in zone 2 may be necessary to maintain the health and vigor of mature stands. Keep large dead and dying trees for cavity nesting birds and a source of large wood in aquatic habitats. Additional requirements:

Questions regarding the planting or maintenance of the buffer planting should be directed to [name of technical specialist], at [phone number].

Riparian Forest Buffer – Job Sheet

If needed, an aerial view or a side view of the practice can be shown below. Other relevant information, complementary practices and measures, and additional specifications may be included.

Scale 1"=________ ft. (NA indicates sketch not to scale: grid size=1/2" by 1/2")

Additional Specifications and Notes:

The United States Department of Agriculture (USDA) prohibits discrimination in its programs on the basis of race, color, national origin, sex, religion, age, disability, political beliefs and marital or familial status.  (Not all prohibited bases apply to all programs.) Persons with disabilities who require alternative means for communication program information (Braille, large print, audiotape, etc.) should contact the USDA Office of Communications (202) 720-2791.

To file a complaint of discrimination write USDA, Director, Office of Civil Rights, Room 326-W, Whitten Building, 14th and Independence Avenue, SW, Washington, DC 20250-9410 or call (202) 720-5964 (voice or TDD). USDA is an equal opportunity provider and employer.