# U.S. Department of Energy

# Compliance Strategy

# for E.O. 13149

June 2001

Prepared by:

Office of Transportation Technologies

1000 Independence Ave, SW

Washington, D.C.  20585

# Contents

List of Tables	ii

Executive Summary	1

I.	Data Collection and Analysis	3

I-1	DOE Baseline Petroleum Fuel Use	3

I-2	DOE Fleet Characteristics	4

I-3	Basic Assumptions	6		I-4	Compliance Approach Analysis	6

(1)	  Biodiesel Blend Use	7

(2) AFV Acquisition and Alternative Fuel Use	7

(3) Acquisition of Higher Fuel Economy Vehicles	11

(4) Fleet Efficiency Improvements	13

II.	AFV Training Program	13

III.	Fleet Management Issues	14

IV.	Results of DOE Strategy	14

V.	Strategy Compliance Evaluation	15

VI.	Recognition and Awards	15

Attachments:  Individual DOE Fleet Location Analyses	17

BPA-Willamette	18

Brookhaven National Laboratory	19

Fermi National Accelerator Laboratory (Fermilab)	20

Idaho National Engineering and Environmental Laboratory	21

Lawrence Berkeley National Laboratory	22

Lawrence Livermore National Laboratory	23

Los Alamos National Laboratory	24

NETL Morgantown	25

NETL Pittsburgh	26

Nevada Test Site	27

National Renewable Energy Laboratory	28

Oak Ridge National Laboratory	29

Pantex	30

Richland-Hanford Site	31

Sandia National Laboratory-Kirtland	32

Savannah River Site	33

List of Tables

- Planned FY 2005 Petroleum Reduction by Strategic Approach	2

2.	Data Requirements	3

3.	DOE Fleetwide Petroleum Fuel Usage for FY 1999	4

4.	FY 1999 Fuel Use Breakdown for DOE	4

- Selected Fleet Locations for DOE-Wide Strategy	5

- Summary of B20 Use in DOE Strategy……………………	7

- Summary of AFV Fuel Savings	7

- Projected AFV Refueling Infrastructure Costs	10

- Summary of Higher Fuel Economy Savings	11

- The Acquisition of Higher Fuel Economy Vehicles at

Brookhaven National Laboratory	12

- Summary of Fleet Efficiency Fuel Savings	13

- DOE Compliance Strategy Results	16

# U.S. Department of Energy Compliance Strategy for E.O. 13149

Executive Summary

###### Executive Order (E.O.) 13149, Greening the Government through Federal Fleet and Transportation Efficiency, was signed by the President on April 21, 2000.   The order requires Federal agencies to reduce their vehicle petroleum consumption by 20 percent, relative to their FY 1999 baseline, through the use of alternative fuel in alternative fuel vehicles and improvements in fleet fuel efficiency.

One of the requirements of E.O. 13149 is for each agency to develop a comprehensive strategy that illustrates how it will achieve the petroleum reduction goals.  For the Department of Energy, the Office of Energy Efficiency and Renewable Energy was given lead responsibility for developing this compliance strategy.  The office’s efforts were coordinated with individual Department of Energy fleet managers to gain operational input and commitment to the strategy, which were viewed as key to its future success. The strategy also responds to other Departmental program initiatives having related petroleum reduction goals, such as the Energy Policy Act and the Secretary’s Pollution Prevention and Energy Efficiency Leadership Goals. Through discussions with and input from the key managers of these programs, the strategy ensures fleet compliance with the goals of the Energy Policy Act of 1992 and the Secretary’s Pollution Prevention and Energy Efficiency Leadership Goals, while at the same time meeting the requirements and objectives of the Executive Order.

The specific elements of the strategy include the use of biodiesel in vehicles with diesel engines, the use of other alternative fuels, the acquisition of light-duty vehicles with higher fuel economy, and improvements in the overall efficiency of fleet vehicle operations.  The approach taken in developing this strategy is consistent with the general guidance of The Federal Fleet Strategy Development Supplement. It entailed a review of the Department of Energy’s fleet composition and characteristics, identification of favorable individual fleet locations, and a “roll-up” of each individual location’s strategy to form an overall agency-wide strategy that meets the goals of E.O. 13149.

Table 1 summarizes the estimated petroleum use reduction that will be achieved by each element of the Department’s compliance strategy.  The quantities in the table are given in gasoline gallon equivalents.  Specific details on how each of these reductions will be achieved are provided in Section I-4 of this strategy.  As shown in Table 1, in fiscal year 2005 it is expected that the implementation of the strategy will achieve as much as 34 percent reduction in the agency’s on-road vehicle petroleum consumption by end of fiscal year 2005, which exceeds the 20 percent reduction goal of E.O. 13149.

Table 1. Planned FY 2005 Petroleum Reduction by Strategic Approach

| Reduction by Strategic Approach | Planned Total Petroleum Reduction in FY 2005 |
| --- | --- |
| Use of Biodiesel (GGE)* | Use of Alternative Fuels (GGE) | Fuel Economy/ Fleet Efficiency Improvements (GGE) | Total GGE | % Reduction |
| 473,745 | 1,222,511 | 276,977 | 1,973,233 | 33.8 |

# * GGE = Gasoline Gallons Equivalent

Fleet reporting, and tracking of compliance with the Department’s strategy and the E.O. 13149 in general, will be performed using the new Web-based database system, the Federal Automotive Statistical Tool.  The Department, in cooperation with the General Services Administration’s Office of Government-Wide Policy, developed the system based on the Vehicle Information Data System reporting mechanism that the Department’s fleets utilized in fiscal year 1999 to report their fuel consumption and alternative fuel vehicle activities. The new system is user-friendly and provides agency-wide roll-up features for effective management of fleet activities under E.O. 13149 and other programs. The system has been approved by the Field Management Council, and does not impose any new reporting requirements on Departmental fleets. Instead, it satisfies three Federal reporting requirements: E.O. 13149, the Energy Policy Act of 1992, and the General Services Administration’s SF-82 Agency Report of Motor Vehicle Data.

The Department has also assessed the cost impacts of the agency’s strategy on individual fleets. To offset the higher price of some types of alternative fuel vehicles compared to conventional vehicles, the Department of Energy established a “memorandum of understanding” with the General Services Administration that states that fleets that lease alternative fuel vehicles through the General Services Administration will pay the same monthly charge for alternative fuel vehicles as for leasing gasoline vehicles. The additional costs are recovered through a small monthly surcharge on all vehicles leased from the General Services Administration throughout the entire Department of Energy fleet. This means that all Departmental fleets that lease vehicles from the General Services Administration will share in the additional costs of alternative fuel vehicle acquisition rather than just the fleets using the vehicles. For vehicles leased from the General Services Administration, the monthly mileage fees cover the fuel costs and are the same regardless of vehicle fuel type. The Department is also working on securing funding (approximately $1.9 million) for covering the additional costs of installing on-site alternative fuel refueling stations at a number of the Department’s fleet locations.

The Department of Energy’s strategy is focused yet flexible, and has a high probability of success in achieving the required petroleum reduction goals. It is consistent with and supports the requirements of other Departmental programs aimed at achieving petroleum reductions, incorporates a Web-based tracking system for fleets, and addresses the cost impacts for individual fleets. It provides a compliance plan that is consistent with the needs of the agency’s fleets and the requirements of individual fleet locations, while ensuring the Department provides leadership among Federal agencies in reducing vehicle petroleum fuel consumption.

I.	Data Collection and Analysis

To develop a strategy for the Department of Energy (DOE) to comply with the petroleum use reduction goal of Executive Order (E.O.) 13149, the agency first conducted an extensive data collection effort.  Table 2 shows the types of data collected for each of the agency’s fleets and the sources used.  The data collected was then used to develop the baseline petroleum consumption, the baseline acquisitions’ average fuel economy, and a realistic strategy for achieving the goals of E.O. 13149.

# Table 2.  Data Requirements

| Data Requirement | Source |
| --- | --- |
| FY 1999 Petroleum Fuel Use (gallons) Total , non-road, and exempt vehicle fuel use | SF-82 report FEMP report |
| Fleet Composition and Characteristics FY 1999 inventory and new acquisitions (conventional and alternative fuel vehicles; light-, medium-, and heavy-duty; gasoline and diesel) FY 1999 new acquisition model breakdown FY2000 and FY2001 projected inventories and new acquisitions (conventional and alternative fuel vehicles; light-, medium-, and heavy-duty; gasoline and diesel) Number of exempt (security, military, etc.) vehicles purchased in FY1999 and their annual fuel consumption | SF-82 report FEMP report GSA Automotive Division GSA Fleet Division GSA Keeling Report, www.policyworks.gov/org/main/mt/homepage/mtv/KEELINGREPORT/MAINREPORT.htm Fleet manager interviews |
| Combined Fuel Economy Ratings by Light Duty Vehicle Category (subcompact, compact, etc.) | DOE/EPA Fleet Fuel Economy Guide, MY 1999 |

#### I-1.  DOE Baseline Petroleum Fuel Use

The DOE-wide fleet use of gasoline and diesel fuel was determined for fiscal year (FY) 1999, for both covered and non-covered vehicles.

A summary of the DOE-wide fuel use in FY 1999 is provided in Table 3. For FY 1999, the DOE fleet used about 7.3 million gasoline gallons equivalent (GGE) of petroleum fuel nationwide, with slightly more than half of this (on both a gallon and GGE basis) made up of gasoline. This data was based upon the Annual Report to Congress on Federal Government Energy Management and Conservation Programs for FY 1999, submitted by the Department of Energy’s Federal Energy Management Program (FEMP) and information provided to the General Services Administration (GSA) for the FY 1999 SF-82 report.

# Table 3.  DOE Fleetwide Petroleum Fuel Usage for FY 1999

| Fuel Type | Total DOE Petroleum Usage, FY 1999 (Gallons) | GGE Conversion Factor | Total DOE Petroleum Usage, FY 1999 (GGE) |
| --- | --- | --- | --- |
| Gasoline | 3,916,200 | 1.0 | 3,916,200 |
| Diesel Fuel | 3,014,000 | 1.147 | 3,457,058 |
| Total Petroleum Used |  |  | 7,373,258 |

The non-road and exempt vehicle fuel use was subtracted from the total fuel use figures to establish the Agency’s baseline. This fuel use baseline was then multiplied by 20 percent to determine the required reduction goal.  Based on this process, DOE’s overall compliance strategy must achieve a total of about 1.2 million GGE savings by FY 2005 when compared with FY 1999 fuel consumption figures, as shown in Table 4.

# Table 4. FY 1999 Fuel Use Breakdown for DOE

| Total DOE Fleet-wide Petroleum Use (GGE) | DOE Non-road Petroleum Use (GGE) | DOE Exempt Petroleum Use (GGE) | DOE Total Covered Petroleum Use (GGE) | Baseline DOE Petroleum 20% Reduction Goal (GGE) |
| --- | --- | --- | --- | --- |
| 7,373,258 | 1,087,099 | 452,146 | 5,834,002 | 1,166,800 |

## I-2.  DOE Fleet Characteristics

The DOE fleet is located in more than fifty individual sites across the country, including program and operational offices. Fleet sizes at these locations range from several thousand to less than a dozen.   Because of this complexity in the DOE fleet structure, the decision was made to develop a compliance strategy based on parameters of individual fleet locations rather than on an agency-wide basis.

To achieve the greatest impact from the location-based strategy, the primary focus was placed on sixteen locations having larger DOE fleet vehicles concentrations, with corresponding higher fuel consumption and the potential for more attractive economics associated with refueling infrastructure and vehicle maintenance support for alternative fuel vehicles (AFVs).  In 1999, the sixteen fleets were responsible for over 80 percent of the vehicle purchases and over 90 percent of the petroleum consumption of the total DOE fleet. These fleets were selected for implementing the strategy.  Table 5 summarizes the data on petroleum use and fleet inventory collected from these sixteen fleets.  Note that the majority of light duty vehicles operated by these fleets are leased through GSA.

# Table 5.  Selected Fleet Locations for DOE-Wide Strategy

| DOE Fleet Location | FY1999 Total Petroleum Use (GGE) | FY1999 Covered Petroleum Use (GGE) * | FY 1999 Fleet Inventory | Percent LDV GSA-Leased |
| --- | --- | --- | --- | --- |
|  |  |  | LDV** | MDV** | HDV** |  |
| BPA-Willamette | 193,596 | 193,596 | 400 | 464 | 176 | 100 |
| Brookhaven National Laboratory | 157,280 | 129,179 | 244 | 41 | 3 | 0 |
| Fermi National Accelerator Laboratory | 144,851 | 144,851 | 133 | 81 | 16 | 25 |
| Idaho National Engineering and Environmental Laboratory | 1,062,272 | 1,022,714 | 698 | 15 | 249 | 0 |
| Lawrence Berkeley National Laboratory | 111,682 | 110,584 | 191 | 56 | 39 | 100 |
| Lawrence Livermore National Laboratory | 506,337 | 462,255 | 808 | 51 | 54 | 100 |
| Los Alamos National Laboratory | 711,244 | 432,874 | 591 | 468 | 101 | 100 |
| National Renewable Energy Laboratory | 16,926 | 15,462 | 36 | 12 | 0 | 100 |
| NETL-Morgantown | 4,786 | 4,477 | 15 | 4 | 1 | 100 |
| NETL-Pittsburgh | 11,421 | 9,876 | 42 | 7 | 4 | 90 |
| Nevada Test Site | 1,708,950 | 1,289,307 | 1,040 | 170 | 257 | 100 |
| Oak Ridge National Laboratory | 667,132 | 420,293 | 1,741 | 220 | 216 | 25 |
| Pantex | 321,370 | 244,242 | 271 | 7 | 16 | 100 |
| Richland-Hanford Site | 631,286 | 593,413 | 551 | 823 | --- | 100 |
| SNL-Kirtland | 330,000 | 312,000 | 413 | 320 | 30 | 100 |
| Savannah River Site | 711,951 | 366,706 | 1,472 | --- | 87 | 100 |
| Total for Target Fleets | 7,291,083 | 5,751,828 | 8,646 | 2,739 | 1,249 | --- |

*      Covered = Total - Nonroad - Exempt

**     LDV= light-duty vehicles; MDV= medium-duty vehicles; HDV= heavy-duty vehicles

The remaining DOE fleet locations not identified in the strategy will be encouraged to reduce their petroleum use by amounts stated in the Executive Order, and will participate in the acquisition of higher fuel economy vehicles and AFVs.  In addition, all DOE fleet locations will be required to meet the objectives of other internal or external fuel and energy reduction initiatives.  One such initiative is the Pollution Prevention and Energy Efficiency (P2/E2) Leadership Goals effort established by the Secretary in November 1999.  The DOE P2/E2 Program established three goals related to transportation:

- Reduce the annual petroleum consumption of the overall DOE fleet by at least 20 percent by 2005 in comparison to 1999, including improving the fuel economy of new light duty vehicle acquisitions, and by other means.

- At least 75 percent of new light duty vehicle acquisitions are to be alternative fuel vehicles, in accordance with the requirements of the Energy Policy Act of 1992 (EPAct).

- Increase the usage rate of alternative fuel in DOE alternative fuel vehicles to 75 percent by 2005, and 90 percent by 2010, in areas where alternative fuel infrastructure is available.

This DOE strategy for compliance with E.O. 13149 is consistent with attaining each of these P2/E2 goals.

## I-3.  Basic Assumptions

A variety of assumptions were made in developing the DOE strategy, including the following:

- Biodiesel and E85 (a blend of 85 percent ethanol, 15 percent gasoline) fuel supplies are generally available or would become available in the near-term. Natural gas and electricity supplies are assumed to be currently available at each fleet location, unless otherwise known from discussions with fleet managers.

- Projected vehicle acquisition rates for FY 2001 are assumed to remain stable through FY 2005.

- Projected AFV acquisition rates for FY 2001 through FY 2005 are assumed to be 75 percent of new vehicle acquisitions for all fleet locations.

- The mix (among types of fuels) of future AFV acquisitions is based on interviews with individual fleet managers, as well as fleet AFV acquisitions for FY 1999 and FY 2000, and projections for FY 2001.

- Light duty vehicle turnover in DOE fleet locations is assumed to be five years, on average.

- Activities will be undertaken to ensure new AFVs use alternative fuel 75 percent and conventional fuel 25 percent of the time on an average annual basis.

- AFV refueling is assumed to follow an availability hierarchy: 1) using an existing on-site station, 2) using an existing public station, 3) constructing a new on-site station.

## I-4.  Compliance Approach Analysis

Previous DOE analyses indicated that simply purchasing AFVs and using biodiesel at current rates within the DOE fleet would not result in the required 20 percent reduction in petroleum use by FY 2005. Therefore, a more comprehensive strategy was developed for reaching the 20 percent reduction goal.

It was decided that the DOE compliance strategy would consist of four core elements:

- Biodiesel Blend (B20) Use

- AFV Acquisitions and Alternative Fuel Use

- Acquisition of Higher Fuel Economy Vehicles

- Fleet Efficiency Improvements.

These options were chosen for their significant potential for petroleum fuel savings for the DOE fleet. An analysis was performed for each element to determine its potential for reducing petroleum fuel use in the sixteen DOE fleets. Brief discussions of each of the four elements and their application in the strategy follow. (Each discussion begins with a table showing that element’s contribution to the overall strategy.)

### Biodiesel Blend Use

# Table 6. Summary of B20 Use in DOE Strategy

| Total DOE Covered Fuel Use in FY 99 (GGE) | 20% Fuel Reduction Goal (GGE) | Strategy Element 1: B20 Fuel Savings (GGE) | Percent of Agency Fuel Reduction Goal |
| --- | --- | --- | --- |
| 5,834,002 | 1,166,800 | 473,745 | 40.6 |

# Discussion of B20

As the first element of DOE’s strategy, B20 (a blend of 80 percent petroleum diesel with 20 percent biodiesel) fuel is proposed to be used in place of conventional diesel fuel at the sixteen fleet locations for both vehicular and non-road diesel equipment. This B20 strategy is estimated to result in an 18 percent GGE savings in annual diesel fuel usage at each fleet location, because every gallon of B20 used displaces about 18 percent of conventional diesel fuel when adjusted for energy content.  In terms of DOE’s overall fuel reduction goal, the use of B20 at the targeted fleet locations achieves about 40.6 percent of the total goal.

Estimated Cost Impacts of B20.  Since B20 can be used in any diesel-powered engine with no engine modifications or costs, both on-road and non-road vehicles and equipment can be operated on B20. B20 can also be stored in existing diesel storage tanks without significant modification or cost.  For fleet locations without existing on-site diesel storage and dispensing systems, such systems would have to be installed or existing diesel tanks switched to biodiesel storage.   B20 does cost slightly more per gallon (about $0.20 more per gallon on average) than conventional diesel fuel.  However, no additional cost will be incurred for GSA-leased vehicles since under the GSA contracts, DOE fleets will pay the same for B20 fuel as for conventional diesel fuel.  GSA may not under current fuel reimbursement agreements, established between the local GSA office and the DOE facility, reimburse the full cost of B20 to fleet.  The facility will need to implement a plan to successfully renegotiate the fuel cost issue with the local GSA office.

# AFV Acquisitions and Alternative Fuel Use

# Table 7.  Summary of AFV Fuel Savings

| Total DOE Covered Fuel Use in FY 99 (GGE) | 20% Fuel Reduction Goal (GGE) | Strategy Element 2: AFV Fuel Savings (GGE) | Percent of Agency Fuel Reduction Goal |
| --- | --- | --- | --- |
| 5,834,002 | 1,166,800 | 1,222,511 | 105* |

*This element alone exceeds the E.O. stated 20% goal

# Discussion of AFV Acquisitions and Alternative Fuel Use

AFV Acquisitions.  Future AFV acquisitions for each fleet location were first estimated. Agency-wide AFV acquisition rates for FY 2001 and later was set at 75 percent of total new vehicle acquisitions. This provides an aggressive AFV introduction rate through FY 2005 for the strategy. For those fleet locations covered by EPAct (eight of the sixteen are EPAct-covered fleets), the 75 percent AFV acquisition rate is compliant with EPAct requirements.

Estimated Cost Impacts of AFV Acquisitions.  The incremental costs of AFVs range from zero to several thousand dollars, depending on the AFV type.  However, a new DOE program, called the Fleet Surcharge Program, will help offset the incremental costs of future AFV acquisitions under this DOE strategy when vehicles are leased from the General Services Administration (GSA). The Fleet Surcharge Program, approved by the Deputy Secretary and instituted under an interagency agreement with the General Services Administration (GSA), will place a small surcharge on each DOE fleet vehicle leased from GSA beginning in FY 2001. This is critical since the majority of vehicles operated by DOE fleets are GSA-leased. The surcharge applies to all DOE fleet locations, not just those included in this strategy. In this way, all DOE fleets will share the cost burden of acquiring AFVs for the DOE fleet. The surcharge will be part of the overall monthly lease cost of the vehicles. Surcharge funds will be placed in a separate account for paying the incremental cost of AFVs acquired in FY 2001 and in the years to follow. Those fleets leasing AFVs will pay the same lease price as for conventional gasoline vehicles.

Alternative Fuel Use. While individual DOE fleets are encouraged to purchase dedicated vehicles, bi-fuel and flexible fuel vehicles will also be acceptable. However, the strategy requires that, on average, new AFVs use the alternative fuel for at least 75 percent of the time, consistent with the Department’s internal P2/E2 goals. Therefore, DOE fleets can purchase a mix of dedicated, bi-fuel, and flexible fuel vehicles as long as this AFV mix uses at least 75 percent alternative fuel annually. DOE fleet managers will be held responsible for meeting and maintaining the 75 percent alternative fuel use requirement by their AFV fleets.

AFV fleet fuel consumption in FY 2005 was calculated by first estimating the numbers of AFVs in service. Since a five-year light duty vehicle turnover is assumed, only those AFVs acquired in FY 2001 through FY 2005 would still be in service in FY 2005. The amount of petroleum fuel displaced by the AFVs was estimated by multiplying the numbers of AFVs by the annual per vehicle fuel consumption rate of the light duty gasoline vehicles being displaced and multiplied by 75 percent. In general, the annual per vehicle fuel consumption rate was calculated from the fleet’s FY 1999 gasoline usage and numbers of light duty gasoline vehicles. For some fleets, this meant first subtracting out estimated gasoline usage by medium and heavy-duty vehicles.  An example for the Lawrence Livermore fleet follows:

# Fleet Gasoline Usage in FY 1999 = 441,113 GGE

# Number of Light Duty Gasoline Vehicles in FY 1999 = 829

# Average Annual Light Duty Gasoline Vehicle Fuel Rate = 441,113/829 = 532 GGE/Vehicle

# Projected Numbers of New AFVs in Service in FY 2005 = 415

# Percentage of Alternative Fuel Use by AFVs = 75%

# Total Petroleum Fuel Displaced by AFVs in FY 2005 = 415*532*0.75 = 165,585 GGE

As summarized in table 7 above, a total of 1,222,511 GGE are saved with this approach, which is five percent higher than the overall fuel reduction goal of 1,166,800 GGE.

Estimated Cost Impacts of Alternative Fuel Use.  Recent national average retail cost figures for E85, liquefied petroleum gasoline (LPG), and compressed natural gas (CNG) are $1.99/GGE, $1.62/GGE and $0.89/GGE, respectively. Electricity on average nationally is about $0.03 to 0.07/kw-hr which equates to about 1 to 2 cents/mile. However, for vehicles leased through GSA, the monthly mileage fees charged by GSA cover the fuel costs and are the same regardless of vehicle fuel type.  Therefore, any higher costs or savings from use of alternative fuel are borne by GSA and not by the fleet leasing the AFV.

AFV refueling infrastructure.  The use of alternative fuel vehicles is the most effective means of reducing petroleum fuel use if they are operated on alternative fuels. Therefore, key factors in assigning particular types of AFVs to specific fleet locations will be the availability of on-site or public AFV refueling stations, and a commitment by vehicle operators to using alternative fuels a substantial part of the time in these vehicles. If alternative fuels are not available, provisions must be made for installing AFV refueling equipment. Because of the additional costs associated with using AFVs compared with conventional vehicles, careful consideration will be given for placing these vehicles in appropriate fleets.

Infrastructure requirements were assessed for serving the projected AFV populations at each fleet location. If an AFV refueling station already exists on-site at the fleet location, the future AFVs should refuel using that station. If an on-site station does not exist, but a public station is available, the projected AFVs should use the public station. And if neither an on-site nor a public station is available for a fleet location, a new AFV refueling station will be needed for this location, with the preference on a privately owned station as opposed to government owned. The status of on-site and public refueling stations was determined through fleet interviews and through the use of the DOE’s Alternative Fuel Data Center’s AFV refueling locator (www.afdc.doe.gov).

Estimated Cost Impacts of AFV Refueling Infrastructure. The projected costs of the new on-site stations were obtained from individual fleet managers for planned installations, or estimated based on installation costs reported in technical literature.  Costs represent required installations for serving the projected AFV fleet populations for FY 2005.  Table 8 provides an overall summary of estimated AFV infrastructure costs for the DOE fleet. Total AFV fleet refueling infrastructure costs were estimated at about $ 2.7 million.   It should be noted that $850,000 of these costs are already funded through a government/industry cost-shared project under the DOE’s AFV USER Program.  The DOE Office of Energy Efficiency and Renewable Energy (EERE) has identified funds in expired interagency agreements that will be de-obligated to cover the remaining infrastructure costs.

Some DOE fleets have been successful at negotiating the installation of an AFV refueling station with a local fuel provider at minimal extra cost to the fleet.  The fleets simply agreed to purchase a specific volume of alternative fuel from the station annually at an agreed fuel price. Also, ensuring that other Federal and non-Federal fleets in the area with AFVs commit to using the station will prevent any shortfalls of the agreed upon fuel use volume over the period of the contract.  One such fleet is Los Alamos National Laboratory, which recently had a local E85 fuel provider install a refueling station near the site at no cost to DOE.

# Table 8.  Projected AFV Refueling Infrastructure Costs

| DOE Fleet Location | Available On-Site or Public AFV Refueling? | AFV Refueling Infrastructure Costs ($) |
| --- | --- | --- |
|  |  | E85 | CNG | Electric |
| BPA-Willamette | No | 35,000 | 200,000 | --- |
| Brookhaven National Laboratory | No | --- | 480,000 | --- |
| Fermilab | Yes (CNG) | 75,000 | --- | --- |
| Idaho National Engineering and Environmental Laboratory | Yes (LCNG) | --- | --- | --- |
| Lawrence Berkeley National Laboratory | Yes (CNG) | 35,000 | --- | 110,000 |
| Lawrence Livermore National Laboratory (LLNL) | Yes (CNG)* | 50,000 | 850,000** | --- |
| Los Alamos National Laboratory | Yes (CNG, E85, Elect) | --- | --- | --- |
| National Renewable Energy Laboratory | Yes (CNG, E85, Elect) | --- | --- | --- |
| NETL-Morgantown | Yes (CNG slow) | --- | 125,000 | --- |
| NETL-Pittsburgh | Yes (CNG slow) | --- | 125,000 | --- |
| Nevada Test Site (NTS) | Yes (CNG)*** | 50,000 | 500,000 | --- |
| Oak Ridge National Laboratory | Yes (CNG) | 50,000 | --- | --- |
| Pantex | Yes (CNG) | 50,000 | --- | --- |
| Richland-Hanford Site | No | 35,000 | --- | --- |
| SNL-Kirtland | Yes (E85 & CNG) | --- | --- | --- |
| Savannah River Site | Yes (E85) | --- | --- | --- |
| Totals | --- | $355,000 | $2,280,000 | $110,000 |

# *	The existing CNG station at LLNL is a slow-fill station that no longer meets the needs of the fleet and is being replaced with a fast-fill station.

# ** LLNL has already received  funding under the DOE AFV USER Program to partially cover the costs of this station and the remaining costs are being borne by the fuel/station provider.

# ***A CNG public station is available in Las Vegas for the smaller portion of the NTS fleet, however infrastructure is needed at the test site to support the majority of the NTS fleet.

# Acquisition of Higher Fuel Economy Vehicles

Table 9. Summary of Higher Fuel Economy Savings

| Total DOE Covered Fuel Use in FY 99 (GGE) | 20% Fuel Reduction Goal (GGE) | Strategy Element 3: Higher FE Fuel Savings (GGE) | Percent of Agency Fuel Reduction Goal |
| --- | --- | --- | --- |
| 5,834,002 | 1,166,800 | 50,352 | 4.3 |

# Discussion of Higher Fuel Economy

Fuel savings due to increases in the new fleet vehicle average fuel economy were estimated based on the projected numbers of petroleum-fueled light duty vehicle purchases over the period of FY 2001 through FY 2005, and the annual per vehicle fuel consumption rates of these vehicles. Due to the importance of this strategy element, and to achieving some equity among DOE fleets in sharing the burden of this compliance strategy, it is planned that all DOE fleet locations will be required to meet the higher fuel economy schedule, not just the sixteen targeted locations.

It is anticipated that the DOE fleet would meet the increased average fuel economies of 1.0 mpg by FY 2002 and 3.0 mpg by FY 2005 compared with the FY 1999 baseline by pursuing the following schedule for fleet fuel economy increases in new acquisitions between 2001 and 2005:

- 0.5 mpg increase in FY 2001

- 1.0 mpg increase in FY 2002

- 2.0 mpg increase in FY 2003

- 2.5 mpg increase in FY 2004

- 3.0 mpg increase in FY 2005

For each DOE fleet location (since all fleets will participate in this element), FY 1999 baseline average fleet fuel economies were calculated for the vehicle types acquired in that year. For some fleet locations, the baseline fuel economies were calculated from the actual new model acquisitions in FY 1999 and the Department of Energy/Environmental Protection Agency’s Fleet Fuel Economy Guide. For most fleet locations, however, data was only available for vehicle class and size, not models.  As a result, baseline fuel economies were estimated for these vehicles.  These estimates were derived by first placing the light duty vehicle acquisitions into size categories, then obtaining the average fuel economies for those categories from the Department of Energy/Environmental Protection Agency’s Fleet Fuel Economy Guide. In all cases, fleet average fuel economies were calculated using the harmonic averaging method, as described in DOE’s guidance document for Federal agencies on E.O. 13149.

It is anticipated that the schedule for achieving the required fuel economy increase from 2001 through 2005 would be met by individual fleets acquiring vehicles with smaller engines and two-wheel versus four-wheel drives, as well as gasoline hybrid vehicles. However, it will be left to the individual fleets to decide the best means of achieving the fuel economy increases through their annual vehicle acquisition plans.

Table 10 presents data from the Lawrence Livermore fleet to derive the fuel savings achieved at this location by acquiring higher fuel economy vehicles. In this example, the annual per vehicle fuel consumption rates for the new light duty vehicles were calculated from the original per vehicle fuel consumption rate for FY 1999 (532 GGE for Lawrence Livermore), the increased fleet average fuel economy for the given fiscal year (e.g., 18.4 mpg in FY 2001), and the original FY 1999 fleet average fuel economy (17.9 mpg), as follows:

# Annual GGE for New LDV in FY 2001 = 532*17.9/18.4 = 518 GGE

As provided in Table 9, fuel savings associated with higher fuel economy vehicles are estimated to be 50,352 GGE, which equates to about 4.3 percent of the required DOE fuel reduction goal.

# Table 10. The Acquisition of Higher Fuel Economy Vehicles at Lawrence Livermore

|  | FY2001 | FY2002 | FY2003 | FY2004 | FY 2005 |
| --- | --- | --- | --- | --- | --- |
| New LDVs | 27 | 27 | 27 | 27 | 27 |
| Annual GGE/New LDV | 518 | 504 | 479 | 467 | 456 |
| Fuel Usage for New LDVs (GGE) | 13,976 | 13,606 | 12,921 | 12,604 | 12,303 |
| Fuel Usage for FY 1999 LDVs at 532GGE/LDV (GGE) | 14,364 | 14,364 | 14,364 | 14,364 | 14,364 |
| Fuel Saved (GGE) for New LDVs | 388 | 758 | 1,443 | 1,760 | 2,061 |
| Total Fuel Saved in FY2005 (GGE) |  | 6,410 |

Estimated Cost Impacts of Higher Fuel Economy.  The acquisition of conventional high fuel economy vehicles should provide no additional cost impact to DOE fleets.  In fact, higher fuel economy vehicles tend to be smaller vehicles with smaller displacement engines whose capital or lease costs are lower than vehicles with lower fuel economies.  In addition, the fuel savings realized by fleets due to higher fuel economy vehicle use would result in lower fleet fuel costs.

# Fleet Efficiency Improvements

Table 11. Summary of Fleet Efficiency Fuel Savings

| Total DOE Covered Fuel Use in FY 99 (GGE) | 20% Fuel Reduction Goal (GGE) | Strategy Element 4: Fleet Efficiency Fuel Savings (GGE) | Percent of Agency Fuel Reduction Goal |
| --- | --- | --- | --- |
| 5,834,002 | 1,166,800 | 226,626 | 19.4 |

Discussion of Fleet Efficiency Improvements

The strategy requires that each fleet location establish a fleet efficiency improvement plan that achieves a minimum 2 percent reduction in overall fleet petroleum fuel consumption relative to the baseline. For a small number of DOE fleets which have low petroleum reductions for the first three elements of the strategy, a minimum 10 to 15 percent reduction resulting from fleet efficiency improvements is suggested in order to achieve higher overall fuel reductions for those locations.  A fleet can also exceed the specific goals of the first three strategy elements, in lieu of meeting its fleet efficiency goals, as long as the same overall fuel reduction required by the DOE strategy is achieved.

The DOE strategy does not stipulate which types of efficiency improvement techniques must be instituted by individual fleets. Each fleet manager will assess his or her fleet’s efficiency in accomplishing its mission. Using compact sedans in preference to large sedans, rescheduling or combining routes to increase vehicle passenger capacities, and decreasing vehicle trips per day should all be considered in achieving a reduction in petroleum use. An added benefit of these improvements could be increased personnel productivity.

The projected DOE-wide fleet efficiency improvements resulted in 226,626 GGE of fuel savings. This is equal to about 19.4 percent of the total fuel reduction goal of 1,166,800 GGE, as indicated in Table 11.

Estimated Cost Impacts of Fleet Efficiency Improvements.  The implementation of fleet efficiency improvements among DOE’s fleets should provide a positive cost impact for their operations.  The resulting reductions in fleet fuel use, potential reductions in vehicle maintenance, and increases in personnel productivity should all serve to reduce overall fleet operational costs.

- AFV Training Program

Given the importance of AFV acquisition and utilization to the DOE compliance strategy, AFV training for fleet personnel will be a key component to its success.  Through an orchestrated training program, fleet personnel can become familiar with AFV technology and operation, safety issues, and proper refueling procedures.  Most alternative fuel providers offer this type of training as part of an initial fuel purchase contract or refueling station installation.  DOE EERE will assist fleets in negotiating AFV training as part of these contracts for their facilities.

- Fleet Management Issues

E.O. 13149 requires that Federal agencies ensure that all government-owned and government-operated vehicles, as well as contractor-operated vehicles under its jurisdiction, comply with goals and objectives of the executive order. This means that contractors must be made aware of and commit to the requirements of E.O. 13149 and this compliance strategy. DOE managers will need to modify contracts with contractors that operate vehicles to ensure compliance under this strategy. DOE’s Office of Management and Administration will soon issue guidance to DOE fleets on this issue.

The Department recognizes certain environmental issues that are addressed by E.O. 13149, as well as the earlier E.O. 13101 on “Greening the Government.”  These Executive Orders require the use of re-refined lubricating oils, with API certification meeting manufacturer’s performance standards, in Federal and contractor vehicles, as well as the use of retread tires and tires with recycled content when they are reasonably available and meet performance standards. As directed in the memorandum from Stephen J. Michelsen, Director of the Office of Resource Management, on April 18, 2001, DOE fleet shall use re-refined oil as outlined in these orders.  DOE also encourages the use of bio-based products as part of its compliance strategy.

# Results of DOE Strategy

The results expected from implementing the DOE strategy are provided in Table 12. (The analyses of individual fleet locations for developing the strategy results are provided as the Attachments to this document.) Estimated fuel savings are shown for each DOE fleet location. Under this strategy, the largest  petroleum use reductions will be achieved through the acquisition of AFVs and use of alternative fuel. The fleet location projected to have the largest total fleet petroleum reduction is the Nevada Test Site, with savings of about 532,900 GGE. All of the targeted fleets are projected to reduce their fleet fuel usage by more than the 20 percent goal. Overall, the strategy’s DOE-wide fleet fuel reduction of about 2.0 million GGE is equal to about a 34 percent decrease relative to the FY 1999 covered fuel baseline, well in excess of the 20 percent goal.

In addition, the DOE strategy achieves both performance measures established by E.O. 13149. The order requires the use of alternative fuels in AFVs the majority (greater than 50 percent) of the time, and requires the purchase of higher fuel economy petroleum fueled vehicles to achieve the 1.0 mpg increase in fleet average fuel economy by FY 2002, and the 3.0 mpg increase by FY 2005.

- Strategy Compliance Evaluation

DOE’s Office of Energy Efficiency and Renewable Energy (EERE), in conjunction with GSA’s Office of Government-wide Policy, has recently developed a Web-based reporting tool, called the Federal Automotive Statistical Tool (FAST) for evaluating E.O. 13149 compliance. FAST was based on the Vehicle Information Data System, or VIDS, which DOE fleets became familiar with during FY1999. Many of the data input screens of FAST are identical to those used in VIDS.  The Field Management Council has approved the use of the FAST system to collect data from Departmental fleets.  FAST can be accessed at the following website:

http://fastweb.inel.gov

The FAST system does not impose any new reporting requirements on DOE fleets.  Instead, it satisfies three Federal reporting requirements: E.O. 13149, EPACT, and GSA’s SF-82 Agency Report of Motor Vehicle Data.  This ability for fleets to report data for all three programs under FAST should greatly streamline the reporting process.  FAST will also provide a unique management tool for fleet managers for characterizing and assessing fleet activities. Compliance with this strategy will be reviewed each year through the use of FAST, and adjustments will be made as necessary to keep pace with evolving DOE fleet requirements. Compliance with using re-refined oil and retread tires will be evaluated based on sites’ annual RCRA/E.O. 13101 reports.

##### VI.  Recognition and Awards

As part of its strategy, special recognition or awards will be given for DOE personnel and/or fleets that exceed the strategy’s requirements or exhibit particularly noteworthy leadership in attaining its objectives and the goals of the Executive Order. The nature of this recognition has not yet been determined, but it will likely be similar to the GSA EPACT Award that provides $2,000 (after tax) to each of two awardees each year.  A ceremony will be held at DOE headquarters, potentially in October in conjunction with DOE’s P2/E2 awards, to recognize the awardees.  It is anticipated that representatives of the Secretary’s Office will present the awards.

# Table 12.  DOE Compliance Strategy Results

| PSO | Targeted DOE Location | FY 1999 Fleet Fuel Use | Baseline LDV FE (mpg) | FY 1999 Fleet Inventory | Required On-site AFV Infra Costs | DOE Strategy Fuel Savings in FY 2005 (GGE) | Total FY 2005 Savings |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Total Fuel Use (GGE) | Non-Road Fuel use (GGE) | Exempt Fuel Use (GGE) | Total Covered Fuel Use (GGE) |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  | Biodiesel | AFV Use | Fuel Economy/ Fleet Efficiency Improvements |  |
|  |  |  |  |  |  |  | LDV | M/HDV | AFV | Exempt Vehicles |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | GGE | % Reduction |
| BPA | BPA-Willamette | 193,596 | - | - | 193,596 | 16.7 | 400 | 640 | 41 | 0 | $235,000 | 29,172 | 14,400 | 8,760 | 52,331 | 27.0 |
| Defense Programs | Los Alamos | 711,244 | - | 278,371 | 432,874 | 16.5 | 591 | 569 | 244 | 263 | 0 | 32,877 | 72,075 | 10,637 | 115,589 | 26.7 |
|  | Nevada Test Site | 1,708,950 | 407,295 | 12,348 | 1,289,307 | 16.8 | 1,040 | 427 | 111 | 9 | $550,000 | 105,085 | 385,875 | 41,929 | 532,889 | 41.3 |
|  | Pantex | 321,370 | 77,128 | - | 244,242 | 16.8 | 271 | 23 | 63 | 0 | $50,000 | 20,165 | 98,280 | 9,282 | 127,727 | 52.3 |
|  | SNL-Kirtland | 330,000 | - | 18,000 | 312,000 | 16.5 | 413 | 350 | 84 | 24 | 0 | 11,394 | 71,160 | 9,389 | 91,943 | 29.5 |
|  | Lawrence Livermore | 506,337 | - | 44,082 | 462,255 | 17.9 | 808 | 105 | 121 | 30 | $900,000 | 11,780 | 165,585 | 15,655 | 193,020 | 41.8 |
| Energy Efficiency | NREL | 16,926 | - | 1,464 | 15,462 | - | 36 | 12 | 14 | 2 | 0 | 149 | 13,451 | 309 | 13,909 | 90.0 |
| Environmental Management | Idaho Eng. & Environ. Site | 1,062,272 | - | 39,558 | 1,022,714 | 16.4 | 698 | 264 | 125 | 57 | 0 | 119,991 | 67,665 | 23,466 | 211,102 | 20.6 |
|  | Richland-Hanford Site | 631,286 | - | 37,873 | 593,413 | 16.4 | 551 | 823 | 84 | 92 | $35,000 | 24,337 | 12,420 | 89,414 | 126,172 | 21.3 |
|  | Savannah River Site | 711,951 | 336,071 | 9,174 | 366,706 | 16.0 | 1,472 | 87 | 284 | 33 | 0 | 68,982 | 161,588 | 14,338 | 244,908 | 66.8 |
| Fossil Energy | NETL-Morgantown | 4,786 | - | 309 | 4,477 | 20.2 | 15 | 5 | 4 | 1 | $125,000 | 27 | 2,781 | 213 | 3,022 | 67.5 |
|  | NETL-Pittsburgh | 11,421 | - | 1,545 | 9,876 | 18.8 | 42 | 11 | 14 | 4 | $125,000 | 109 | 4,635 | 330 | 5,074 | 51.4 |
| Office of Science | Brookhaven | 157,280 | 19,766 | 8,335 | 129,179 | 17.5 | 244 | 44 | 9 | 38 | $480,000 | 3,570 | 22,106 | 3,488 | 29,164 | 22.6 |
|  | Fermilab | 144,851 | - | - | 144,851 | - | 133 | 97 | 19 | 0 | $50,000 | 6,477 | 71,700 | 2,897 | 81,074 | 56.0 |
|  | Lawrence Berkeley | 111,682 | - | 1,098 | 110,584 | 21.2 | 191 | 95 | 4 | 3 | $145,000 | 7,818 | 43,783 | 3,485 | 55,086 | 49.8 |
|  | Oak Ridge* | 667,132 | 246,839 | -** | 420,293 | 17.3 | 1,741 | 436 | 14 | 216*** | $50,000 | 31,811 | 15,008 | 42,583 | 89,401 | 21.3 |
| Total from targeted fleets | 7,291,083 | 1,087,099 | 452,156 | 5,751,828 | 16.7 | 8,646 | 3,988 | 1,235 | 772 | $2,745,000 | 473,745 | 1,222,511 | 276,155 | 1,972,411 | 34.3 |
| Totals from non-targeted fleets | 82,175 | - | - | 82,175 | - | - | - | - | - | 0 | - | - | 822 | 822 | 1.0 |
| Total DOE Fleetwide | 7,373,258 | 1,087,099 | 452,146 | 5,834,002 | 16.83 | - | - | - | - | $2,745,000 | 473,745 | 1,222,511 | 276,977 | 1,973,233 | 33.8 |
| Required 20% Fuel Use Reduction | 1,166,800 |  |

*    In addition to the Office of Science LPSO, some Oak Ridge National Laboratory operations fall under the Defense Programs and Environmental Management LPSOs.

**  Exempt fuel use included under non-road fuel use

*** Exempt vehicles include non-road vehicles

# Attachments

Individual DOE Fleet Location Analyses

BPA-WILLAMETTE

FUEL USE

TOTAL1999		1999 NON-ROAD		1999 EXEMPT		2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE	TOTAL GGE	GGE REDUCT

GASOL	 32,074 	 32,074 			0	0	 32,074

DIESEL	 140,821 	 161,522 					 161,522

TOTAL		 193,596 		 -   		 -   	 193,596 	 38,719

FLEET DATA -VIDS

1999			2000				2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY		NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	400	55	34	153		36	6	139	32	2

MDV	464			464				464

HDV	176			176				176

AFV	41

GASOL	DIESEL	EXEMPT

LDV	200	200	0		Assumed all LDV gasoline; all M/HDV diesel

MDV		464	0

HDV		176	0

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - VIDS

Vehicle Type				1999		Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions		City FE	Hwy FE	Combined FE

Ford	MINICOMPACT			0				0	0

Ford	SUBCOMPACT			0				0	0

COMPACT					20.3	28.5	23	0

MIDSIZE			1		19.7	29	23	0.043436023

LARGE					18	25	21	0

TWO-SEATER							0	0

SMALL P/U			4		16.1	20.2	18	0.225754874

LARGE P/U			12		14.3	19.1	16	0.744260975

SMALL VAN			1		15.5	20.7	17	0.057223001

LARGE VAN			3		14.2	19.1	16	0.186877811

Baseline Average FE		16.7

FY2002 FE Goal		17.7

FY2005 FE Goal		19.7

* Average fuel economy values estimated by category based on FY 1999 New GSA Leased Vehicles for DOE fleet								   and fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Willamette has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY 2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

140,821 	 143,567 		 29,172 			 29,172 	 29,172 	 29,172 	 29,172 	 29,172

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = ???

- Willamette not in MSA													- Non-AFV acquisition rates assumed same as FY2001											- Afv acquisition rates assumed 75% for FY2001 thru Fy2005											- All acquisitions assumed to be LDV												- LDV turnover assumed to be five years												- Mix of AFVs based on 1999 purchased (50% CNG; 50% E85)										- Avg annual LDV fuel use = 32074/200 =  160 GGE											- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000			2001		2002		2003		2004		2005

Total	AFV		Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	36	6		32	24	32	24	32	24	32	24	32	24

MDV

HDV

Total AF Use		AFV Refueling										Total AFVs in Service in FY2005	in FY 2005 (GGE)	Infra		FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	60		7200		250000

E85 FFV	60		7200		32500

Total	120		14400				2880	5760	8640	11520	14400

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 2672 mi/yr based on 160 gal/yr and avg 16.7  mpg

FY01	FY02	FY03		FY04	FY05

New LDV	8	8	8		8	8

gal/LDV	155	151	143		139	136

New gal used	1243	1208	1143		1113	1085

Gal saved in FY	893	928	993		1023	1051

Gal Saved Cum	893	1821	2814		3837	4888

Total gal saved in FY05 =			4888	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

193,596 		 3,872 				 774.38 	 1,548.77 	 2,323.15 	 3,097.53 	 3,871.91

OVERALL PETROL FUEL REDUCTIONS FOR BPA-WILLAMETTE STRATEGY

STRATEGY		FUEL SAVED

Element 		(GGE)

1		 29,172

2		14400

3		4888

4		 3,872

TOTAL		 52,331

BROOKHAVEN LAB

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 137,514 	 137,514 			8335	8335		 129,179

DIESEL	 17,233 	 19,766 	 17,233 	 19,766 				 -

TOTAL		 157,280 		 19,766 		 8,335 		 129,179 	 25,836

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	244	21	9	240	20	5	238	9	9

MDV	41

HDV	3

EXEMPT	38

AFV	9

FLEET FUEL ECONOMY (NEW ACQUISITIONS)

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Ford	MINICOMPACT			0			26	0

Ford	SUBCOMPACT			0			33	0

COMPACT				20.3	28.5	23	0

MIDSIZE				19.7	29	23	0

LARGE			2	18	25	21	0.097111111

TWO-SEATER						0	0

SMALL P/U			6	16.1	20.2	18	0.33863231

LARGE P/U				14.3	19.1	16	0

SMALL VAN				15.5	20.7	17	0

LARGE VAN			4	14.2	19.1	16	0.249170415

Baseline Average FE		17.5

FY2002 FE Goal		18.5

FY2005 FE Goal		20.5

* Average fuel economy values estimated by category based on FY 1999 New GSA Leased Vehicles for DOE fleet

and fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Brookhaven has MDV & HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

17,233 	 17,569 		 3,570 			 3,570 	 3,570 	 3,570 	 3,570 	 3,570

2. AFV ACQUISITIONS

- AFV Refueling access (< 15 miles) = LPG (private)

- Brookhaven is in MSA

- Non-AFV acquisition rates assumed same as FY2000; AFV acquisition at 75% per EPACT

- All acquisitions assumed to be LDV

- LDV turnover assumed to be five years

- Mix of AFVs based on 1999 purchased (50% CNG; 50% E85) and interview with fleet mgr

- Assume MD/HDV 7.0 mpg avg and 6566 mi/yr avg (DOE Databook for Federal fleets)

- Assume average annual LDV mileage of 5,500 mi/yr based on FY00 FAST data; avg fuel economy of 14 mpg based on fleet derived estimate

- Avg annual LDV fuel use = 5,500/14 = 393  GGE

- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	20	5	20	15	20	15	20	15	20	15	20	15

MDV

HDV

AFV Infra

Total AFVs in Service in FY2005  Total AF Fuel Use (GGE) in FY2005		Cost ($)		FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	75		22106 			480000	Quote from Fleet Manager							E85 FFV	0		0			0

Total	75		22106 			480000		4421	8842	13264	17685	22106

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 2000  travels 5,500  mi/yr  with avg 17.5 mpg

FY01	FY02	FY03	FY04	FY05

New LDV	5	5	5	5	5

gal/LDV	382	371	352	344	335

New gal used	1908	1857	1762	1718	1676

Gal saved in FY	57	108	203247289

Gal Saved Cum	57	165	368	615	904

Total gal saved in FY05 =			904	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%			FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

129,179 		 2,584 			 516.72 	 1,033.43 	 1,550.15 	 2,066.86 	 2,583.58

OVERALL PETROL FUEL REDUCTIONS FOR BROOKHAVEN STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 3,570

2		22106

3		904

4		 2,584

TOTAL		 29164

Fermilab

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 108,989 	 108,989 			0	0		 108,989

DIESEL	 31,266 	 35,862 						 35,862

TOTAL		 144,851 		 -   		 -   		 144,851 	 28,970

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	133	9	9	125	24	24	125	26	26

MDV	81			81	9	9	81	9	9

HDV	16			16			16

AFV	19

GASOL	DIESEL	EXEMPT

LDV	114	1	0

MDV	0	81

HDV	0	16

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - VIDS

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Ford	MINICOMPACT			0			26	0

Ford	SUBCOMPACT			0			33	0

COMPACT			0	20.3	28.5	23	0

MIDSIZE			0	19.7	29	23	0

LARGE			0	18	25	21	0

TWO-SEATER			0			0	0

SMALL P/U			0	16.1	20.2	18	0

LARGE P/U			0	14.3	19.1	16	0

SMALL VAN			0	15.5	20.7	17	0

LARGE VAN			0	14.2	19.1	16	0

Baseline Average FE		-

FY2002 FE Goal		#VALUE!

FY2005 FE Goal		#VALUE!

* Average fuel economy values estimated by category based on FY 1999 New GSA Leased Vehicles for DOE fleet

and fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- FERMI has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

31,266 	 31,876 		 6,477 			 6,477 	 6,477 	 6,477 	 6,477 	 6,477

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG on-site; LPG (private)

- FERMI is in MSA														- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition at 75% EPACT

- LDV turnover assumed to be five years

- Mix of AFV (100% E85); fleet stated do not want to use on-site CNG station; E85 in Illinois

- Avg annual LDV fuel use = 108989/(133-19) =   956 GGE

- FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	24	24	26	20	26	20	26	20	26	20	26	20

MDV

HDV

Total AF Fuel Use		AFV Infra

Total AFVs in Service in FY2005		in FY 2005 (GGE)		($)		FY01	FY02	FY03	FY04	FY05

E85 FFV	100			71700			50000

Total	100			71700					14340	28680	43020	57360	71700

3. Fuel Economy Increases

- Baseline FE is zero since did not buy any non-AFV LDVs in '1999'

FY01	FY02	FY03	FY04	FY05

New LDV	6	6	6	6	6

gal/LDV	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

New gal used	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

Gal saved in FY	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

Gal Saved Cumul

Total gal saved in FY05 =			0	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

144,851 		 2,897 				 579.40 	 1,158.81 	 1,738.21 	 2,317.62 	 2,897.02

OVERALL PETROL FUEL REDUCTIONS FOR FERMI STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 6,477

2		71700

3		0

4		 2,897

TOTAL		 81,074

IDAHO NAT'L LAB

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 397,889 	 397,889 			39558	39558		 358,331

DIESEL	 579,235 	 664,383 						 664,383

TOTAL		 1,062,272 		 -   		 39,558 		 1,022,714 	 204,543

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	698	61	47	698	41	25	700	35	20

MDV	15			15			15

HDV	249		1	249			249

AFV	125

GASOL	DIESEL	EXEMPT

LDV	573	3	57

MDV		15	(assumed all diesel)

HDV		249	(assumed all diesel)

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - VIDS

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Ford	MINICOMPACT			0			26	0

Ford	SUBCOMPACT			0			33	0

COMPACT				20.3	28.5	23	0

MIDSIZE				19.7	29	23	0

LARGE				18	25	21	0

TWO-SEATER						0	0

SMALL P/U				16.1	20.2	18	0

LARGE P/U			8	14.3	19.1	16	0.496173983

SMALL VAN			3	15.5	20.7	17	0.171669004

LARGE VAN			1	14.2	19.1	16	0.062292604

Baseline Average FE		16.4

FY2002 FE Goal		17.4

FY2005 FE Goal		19.4

* Average fuel economy values estimated by category based on FY 1999 New GSA Leased Vehicles for DOE fleet

and fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Idaho has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (Gal)	B20 USE (gal)		FUEL DISPL (GGE)

579,235 	 590,532 		 119,991 			 119,991 	 119,991 	 119,991 	 119,991 	 119,991

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (govt, private), LPG, Electric

- Idaho not in MSA

- Non-AFV acquisition rate assumed same as FY2001

AFV acquisition rate assumed 75%													- All acquisitions assumed to be LDV													- LDV turnover assumed to be five years													- Mix of AFVs purchased in FY99 (90% Bi-Fuel CNG; 10% E85)											- Avg annual LDV fuel use = 397889/(698-125) = 694 GGE												- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	41	25	35	26	35	26	35	26	35	26	35	26

MDV

HDV

Total AF Fuel Use			AFV Infra

Total AFVs in Service in FY2005	in FY 2005 (GGE)			($)		FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	130		67665			0	Existing LCNG station can handle						E85 FFV	0		0

Total	130		67665						13533	27066	40599	54132	67665

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase														- FY02 = 1.0 mpg increase														- FY03 = 2.0 mpg increase														- FY04 =2.5 mpg increase														- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 11413 mi/yr based on 694 gal/yr and avg 16.4 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		9	9	9	9	9

gal/LDV		674	655	619	603	587

New gal used		6065	5891	5572	5425	5285

Gal saved in FY	181	355	674	821	961

Gal Saved Cum	181	535	1210	2031	2992

Total gal saved in FY05 =			2992	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

1,022,714 		 20,454 				 4,090.85 	 8,181.71 	 12,272.56 	 16,363.42 	 20,454.27

OVERALL PETROL FUEL REDUCTIONS FOR IDAHO STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 119,991

2		67665

3		2992

4		 20,454

TOTAL		 211,102

LAWRENCE BERKLEY NAT'L LAB

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 68,393 	 68,393 			1098	1098		 67,295

DIESEL	 37,741 	 43,289 						 43,289

TOTAL		 111,682 		 -   		 1,098 		 110,584 	 22,117

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	191	46	2	194	44	22	194	38	20

MDV	56	4	0	56	2	0	56	6	0

HDV	39	0	0	39	1	0	39	2	0

AFV	4

GASOL	DIESEL	EXEMPT

LDV	187	0	3

MDV	0	56

HDV	0	39

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Astro			1	16	18	17	0.059375

Astro			3	16	19	17	0.174177632

Breeze			26	20	28	23	1.132857143

Cargo van			4	15	21	17	0.232380952

Contour			2	22	31	25	0.079032258

Ram 1500			1	16	21	18	0.055803571

Windstar			1	15	23	18	0.056231884

Baseline Average FE		21.23

FY2002 FE Goal		22.23

FY2005 FE Goal		24.23

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Law Berk has MDV & HDV fleet													- Assume diesel use remains constant through FY2005												- Assume total conversion to B20 by FY2005

FY 2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (Gal)	B20 USE (gal)		FUEL DISPL (GGE)

37,741 	 38,477 		 7,818 			 7,818 	 7,818 	 7,818 	 7,818 	 7,818

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (gov't), LPG (private, public)											- Lawrence Berk in MSA

- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition = 75% EPACT										- All acquisitions assumed to be LDV													- LDV turnover assumed to be five years													- Mix of AFVs based on 1999 purchased (33% Bi-Fuel CNG; 33% E85; 33% EV)										- Avg annual LDV fuel use = 68393/187 = 366 GGE												- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	44	22	38	29	38	29	38	29	38	29	38	29

MDV

HDV

Total AF Fuel Use		AFV Infra

Total AFVs in Service in FY2005	in FY 2005 (GGE)		($)		FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	48		13135			0

E85 FFV	48		13135			32500

EV	48		17513			112,000

Total	96		43783					8756.55	17513.1	26269.65	35026.2	43783

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 7765 mi/yr based on 366 gal/yr and avg 21.2 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		9	9	9	9	9

gal/LDV		357	349	334	327	320

New gal used		3216	3144	3008	2945	2884

Gal saved in FY	78	150	286	349	410

Gal Saved Cum	78	228	514	863	1273

Total gal saved in FY05 =			1273	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

110,584 		 2,212 				 442.34 	 884.67 	 1,327.01 	 1,769.34 	 2,211.68

OVERALL PETROL FUEL REDUCTIONS FOR LAWRENCE BERK STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 7,818

2		43783

3		1273

4		 2,212

TOTAL		 55,086

LAWRENCE LIV NAT'L LAB

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 441,113 	 441,113 	 -   		39574	39574		 401,539

DIESEL	 56,865 	 65,224 	 -   		 3,930 	 4,508 		 60,716

TOTAL		 506,337 		 -   		 44,082 		 462,255 	 92,451

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	808	98	83	592	118	96	592	110	48

MDV	51	7		51			51

HDV	54			54			54

AFV	121

GASOL	DIESEL	EXEMPT

LDV	808	0	21

MDV		51	2

HDV		54	7

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Ford	astro			4	16	19	17	0.232236842

breeze			6	20	28	23	0.261428571

crown vic			2	18	25	21	0.097111111

D1500			1	17	22	19	0.052807487

Durango			2	15	20	17	0.118333333

F250			9	13	18	15	0.605769231

Lumina			2	20	30	24	0.085

Ram 1500			1	16	21	18	0.055803571

Ranger			1	18	23	20	0.050120773

Tahoe			4	15	19	17	0.241403509

Taurus			1	19	27	22	0.045614035

Baseline Average FE		17.9

FY2002 FE Goal		18.9

FY2005 FE Goal		20.9

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

56,865 	 57,974 		 11,780 				5,890	 11,780 	20,615	 20,615

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (gov't), LPG (private, public)

- Lawrence in MSA

- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition = 75% EPACT										- All acquisitions assumed to be LDV													- LDV turnover assumed to be five years													- Mix of AFVs based on 1999 purchased (90% Bi-Fuel CNG; 10% E85)											- Avg annual LDV fuel use = 441113/(808+21) = 532 GGE												- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	118	96	110	83	110	83	110	83	110	83	110	83

MDV

HDV

Total AF Use			AFV Refueling

Total AFVs in Service in FY2005	(GGE) in FY05			Infra ($)			FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	374		149027			 $850,000 	Quote from Fleet Mgr; but funded under AFV User

E85 FFV	42		16559			 $50,000 	Estimated

Total	415		165585			 $900,000 			33117	66234	99351	132468	165585

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase														- FY04 =2.5 mpg increase														- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 9,514 mi/yr based on 532 gal/yr and avg 17.9 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		27	27	27	27	27

gal/LDV		518	504	479	467	456

New gal used		13976	13606	12921	12604	12303

Gal saved in FY	388	758	1443	1760	2061

Gal Saved Cum	388	1146	2589	4349	6410

Total gal saved in FY05 =			6410	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

462,255 		 9,245 				 1,849.02 	 3,698.04 	 5,547.07 	 7,396.09 	 9,245.11

OVERALL PETROL FUEL REDUCTIONS FOR LAWRENCE LIV STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 11,780

2		165585

3		6410

4		 9,245

TOTAL		 193,020

LOS ALAMOS NAT'L LAB

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 529,205 	 529,205 			209803	209803		 319,402

DIESEL	 158,709 	 182,039 			 59,780 	 68,568 		 113,472

TOTAL		 711,244 		 -   		 278,371 		 432,874 	 86,575

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	591	122	83	833	75	62	833	75	62

MDV	468	47	0	530	60	0	530	60	0

HDV	101	2	0	115	5	0	115	5	0

AFV	244

GASOL	DIESEL	EXEMPT

LDV	591	0	263

MDV	438	30

HDV	0	101

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

1500 Cargo			1	13	18	15	0.067307692

astro			3	16	19	17	0.174177632

breeze			3	20	28	23	0.130714286

cherokee			14	16	20	18	0.79625

D150			1	14	19	16	0.062969925

Dakota			3	15	20	17	0.1775

Durango			45	15	20	17	2.6625

Expedition			11	11	20	14	0.7975

F250			7	13	18	15	0.471153846

S10			3	17	21	19	0.161344538

Tahoe			13	15	19	17	0.784561404

Baseline Average FE		16.5

FY2002 FE Goal		17.5

FY2005 FE Goal		19.5

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- LANL has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

Fy2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

158,709 	 161,804 		 32,877 			 32,877 	 32,877 	 32,877 	 32,877 	 32,877

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (on-site), Electric (onsite); LPG (private, utility)

- LANL in MSA and Albuquerque is AFV User City

- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition = 75% EPACT

- All acquisitions assumed to be LDV

- LDV turnover assumed to be five years

- Mix of AFVs based on 1999 purchased (100% E85)

- Avg annual LDV fuel use = 310 GGE based on fleet ops data

- FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	75	62	75	62	75	62	75	62	75	62	75	62

MDV

HDV

Total AF Use			AFV Refueling

Total AFVs in Service in FY2005	(GGE) in FY05			Infra ($)		FY01	FY02	FY03	FY04	FY05

E85 FFV	310		72075			50000

Total	310		72075					14415	28830	43245	57660	72075

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 5115 mi/yr based on 310 gal/yr and avg 16.5 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		13	13	13	13	13

gal/LDV		300	292	276	269	262

New gal used		3901	3790	3586	3492	3402

Gal saved in FY	129	240	444	538	628

Gal Saved Cum	129	369	813	1352	1979

Total gal saved in FY05 =			1979	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

432,874 		 8,657 				 1,731.49 	 3,462.99 	 5,194.48 	 6,925.98 	 8,657.47

OVERALL PETROL FUEL REDUCTIONS FOR LOS ALAMOS STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 32,877

2		72075

3		1979

4		 8,657

TOTAL		 115,589

NETL MORGANTOWN

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

.	GASOL	 4,635 	 4,635 			 309 	309		 4,326

DIESEL	 132 	 151 			 -   	 -   		 151

TOTAL		 4,786 		 -   		 309 		 4,477 	 895

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	15			16	7	3	16	7	3

MDV	4			4	1	0	4	1	0

HDV	1			1	0	0	1	0	0

AFV	4

GASOL	DIESEL	EXEMPT

LDV	11	0	1	(Per vehicle fuel consumption assumed same as NETL-Pitt = 309 Gas; 132 diesel)

MDV	4	0	0

HDV	0	1

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - FAST Vehicle Data (2000)

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Van			1	13	18	15	0.067307692

0	16	19	17	0

Compact Sedan			3	20	28	23	0.130714286

0	16	20	18	0

0	14	19	16	0

0	15	20	17	0

0	15	20	17	0

0	11	20	14	0

0	13	18	15	0

0	17	21	19	0

0	15	19	17	0

Baseline Average FE		20.2

FY2002 FE Goal		21.2

FY2005 FE Goal		23.2

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- NETL PITT has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

Fy2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

132 	 135 		 27 			 27 	 27 	 27 	 27 	 27

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (on-site slow fill)

- Vehicle acquisition rates assumed to be 5/yr; AFV acquisition = 75% EPACT

- All acquisitions assumed to be LDV

- LDV turnover assumed to be three years													- Mix of AFVs based on 1999 purchased (100% CNG per fleet mgr)											- Avg annual LDV fuel use = 309 GGE based on FAST input for NETL-Pitt DOE-owned vehicles in FY2000									- FFVs assumed 75% CNG use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV			5	4	5	4	5	4	5	4	5	4

MDV

HDV

Total AF Use			AFV Refueling

Total AFVs in Service in FY2005	(GGE) in FY05			Infra ($)		FY01	FY02	FY03	FY04	FY05

CNG	12		2781			125000

Total	12		2781					556.2	1112.4	1668.6	2224.8	2781

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 6242 mi/yr based on 309 gal/yr and avg 20.2 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		1	1	1	1	1

gal/LDV		302	294	281	275	269

New gal used		302	294	281	275	269

Gal saved in FY	7	15	28	34	40

Gal Saved Cum	7	22	50	84	124

Total gal saved in FY05 =			124	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

4,477 		 90 				 18 	 36 	 54 	 72 	 90

OVERALL PETROL FUEL REDUCTIONS FOR LOS ALAMOS STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 27

2		2781

3		124

4		 90

TOTAL		 3,022

NETL PITTSBURGH

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 10,815 	 10,815 			 1,545 	1545		 9,270

DIESEL	 528 	 606 			 -   	 -   		 606

TOTAL		 11,421 		 -   		 1,545 		 9,876 	 1,975

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	42			39	5	2	39	5	2

MDV	7			5	1	0	5	1	0

HDV	4			5	0	0	5	0	0

AFV	14

GASOL	DIESEL	EXEMPT

LDV	28	0	4

MDV	7	0	1

HDV	0	4

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - FAST Vehicle Data (2000)

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

0	13	18	15	0

0	16	19	17	0

Compact Sedan			2	20	28	23	0.087142857

0	16	20	18	0

0	14	19	16	0

0	15	20	17	0

0	15	20	17	0

SUV				1	11	20	14	0.0725

0	13	18	15	0

0	17	21	19	0

0	15	19	17	0

Baseline Average FE		18.8

FY2002 FE Goal		19.8

FY2005 FE Goal		21.8

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- NETL PITT has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

Fy2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

528 	 538 		 109 			 109 	 109 	 109 	 109 	 109

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (on-site slow fill)

- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition = 75% EPACT										- All acquisitions assumed to be LDV

- LDV turnover assumed to be five years													- Mix of AFVs based on 1999 purchased (100% CNG per fleet mgr)											- Avg annual LDV fuel use = 309 GGE based on FAST input for DOE-owned vehicles in FY2000									- FFVs assumed 75% CNG use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	5	4	5	4	5	4	5	4	5	4	5	4

MDV

HDV

Total AF Use			AFV Refueling

Total AFVs in Service in FY2005	(GGE) in FY05			Infra ($)		FY01	FY02	FY03	FY04	FY05

CNG	20		4635			125000

Total	20		4635					927	1854	2781	3708	4635

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 5807 mi/yr based on 309 gal/yr and avg 18.8 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		1	1	1	1	1

gal/LDV		301	293	279	273	266

New gal used		301	293	279	273	266

Gal saved in FY	8	16	30	36	43

Gal Saved Cum	8	24	53	90	132

Total gal saved in FY05 =			132	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

9,876 		 198 				 40 	 79 	 119 	 158 	 198

OVERALL PETROL FUEL REDUCTIONS FOR LOS ALAMOS STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 109

2		4635

3		132

4		 198

TOTAL		 5,074

NEVADA TEST SITE

TOTAL FUEL USE - Fleet Sources

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 1,127,100 	 1,127,100 			12348	12348		 1,114,752

DIESEL	 507,280 	 581,850 	 355,096 	 407,295 		 -   		 174,555

TOTAL		 1,708,950 		 407,295 		 12,348 		 1,289,307 	 257,861

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	1040	100	20	981	232	91	880	100	20

MDV	170	0	0	169	0	0	0	0	0

HDV	257	0	0	256	1	0	200	0	0

AFV	111

GASOL	DIESEL	EXEMPT

LDV	657	0	9

MDV	105	2

HDV	48	210

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Plymouth	Breeze			5	20	28	23	0.217857143

Dodge	Caravan			1	16	20	18	0.056875

Jeep	Cherokee			26	16	20	18	1.47875

Ford	Contour			1	22	31	25	0.039516129

Dodge	Dakota			3	16	21	18	0.167410714

Dodge	Dakota			8	14	18	16	0.514285714

Ford	E150			2	14	17	15	0.131512605

Ford	Expedition			10	11	20	14	0.725

Ford	F250			4	13	18	15	0.269230769

Dodge	Ram 1500			5	16	21	18	0.279017857

Ford	Ranger			1	18	23	20	0.050120773

Chevy	Tahoe			4	15	19	17	0.241403509

Ford	Windstar			3	15	23	18	0.168695652

Baseline Average FE		16.82

FY2002 FE Goal		17.82

FY2005 FE Goal		19.82

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

507,280 	 517,173 		 105,085 			 105,085 	 105,085 	 105,085 	 105,085 	 105,085

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (onsite)											- Nevada Test Site is in the Las Vegas MSA according to the 1995 Census

- Non-AFV acquisition rates assumed same as FY2001												- AFV acquisition rates assumed to be 75% for FY 2001 thru Fy 2005											- LDV turnover assumed to be five years													- Mix of AFVs (80% CNG; 20% E85)													- According to fleet sources, 80% of gasoline is consumed by LDV											- Avg annual LDV fuel use = (1,127,100*0.8)/657 = 1372 GGE												- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	232	91	100	75	100	75	100	75	100	75	100	75

MDV

HDV

Total AF Use			AFV Refueling

Total AFVs in Service in FY2005	in FY 2005 (GGE)		Infra			FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	300		308700			479660	Existing CNG station serves 100 AFVs; still need more CNG for extra 300 veh

E85 FFV	75		77175			50000

Total	375		385875						77175	154350	231525	308700	385875

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 23086 mi/yr based on 1372 gal/yr and avg 16.82 mpg

FY01	FY02	FY03	FY04	FY05

New LDV	25	25	25	25	25

gal/LDV	1333	1295	1227	1195	1165

New gal used	33320	32385	30664	29871	29117

Gal saved in FY	980	1915	3636	4429	5183

Gal Saved Cum	980	2895	6531	10960	16143

Total gal saved in FY05 =			16143	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

1,289,307 		 25,786 				 5,157.23 	 10,314.46 	 15,471.68 	 20,628.91 	 25,786.14

OVERALL PETROL FUEL REDUCTIONS FOR NEVADA TEST SITE STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 105,085

2		385875

3		16143

4		 25,786

TOTAL		532889

NREL

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 16,100 	 16,100 			1464	1464		 14,636

DIESEL	 720 	 826 						 826

TOTAL		 16,926 		 -   		 1,464 		 15,462 	 3,092

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	36	9	8	36	6	5	37	9	9

MDV	12	1

HDV

Afv	14

GASOL	DIESEL	EXEMPT

LDV	22		2

MDV	0	12	(assume all diesel)

HDV	0	0

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - VIDS

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Ford	MINICOMPACT			0			26	0

Ford	SUBCOMPACT			0			33	0

COMPACT			0	20.3	28.5	23	0

MIDSIZE			0	19.7	29	23	0

LARGE			0	18	25	21	0

TWO-SEATER			0			0	0

SMALL P/U			0	16.1	20.2	18	0

LARGE P/U			0	14.3	19.1	16	0

SMALL VAN			0	15.5	20.7	17	0

LARGE VAN			0	14.2	19.1	16	0

Baseline Average FE		-

FY2002 FE Goal		#VALUE!

FY2005 FE Goal		#VALUE!

* Average fuel economy values estimated by category based on FY 1999 New GSA Leased Vehicles for DOE fleet

and fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- NREL has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

720 	 734 		 149 			 149 	 149 	 149 	 149 	 149

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (public); LPG (public); E85 (public)

- NREL is in MSA

- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition at 75% EPACT

- LDV turnover assumed to be five years

- Mix of AFVs (50% CNG; 30% Electric; 20% E85) based on Fy 1999 purchased

- Avg annual LDV fuel use = 16100/22 =   732 GGE

- CNG Bi-Fuel and FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	6	5	9	7	9	7	9	7	9	7	9	7

MDV

HDV

Total AFVs in Service in FY2005	Total AF Fuel Use (GGE) in FY2005		FY01	FY02	FY03	FY04	FY05

CNG Bi-Fuel	18		9608

Electric	11		7686

E85 FFV	7		3843

Total	25		13451				2690.1	5380.2	8070.3	10760.4	13451

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 6751 mi/yr based on 348 gal/yr and avg 19.4 mpg

FY01	FY02	FY03	FY04	FY05

New LDV	2	2	2	2	2

gal/LDV	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

New gal used	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

Gal saved in FY	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

Gal Saved Cum	#VALUE!	#VALUE!	#VALUE!	#VALUE!	#VALUE!

Total gal saved in FY05 =			0	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

15,462 		 309 				 61.85 	 123.69 	 185.54 	 247.39 	 309.24

OVERALL PETROL FUEL REDUCTIONS FOR FERMI STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 149

2		13451

3		0

4		 309

TOTAL		 13,909

OAK RIDGE NAT'L LAB

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL		 495,145 		 192,534 		0		 302,611

DIESEL		 171,987 		 54,305 				 117,682

TOTAL		 667,132 		 246,839 		 -   		 420,293 	 84,059

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	1741	39	17	1569	19	13	1514	30	12

MDV	220

HDV	216

AFV	14

GASOL	DIESEL	EXEMPT

LDV	1741	0	187

MDV		220	7	(assume all diesel)

HDV		216	22	(assume all diesel)

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - VIDS

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

Ford	MINICOMPACT			0			26	0

Ford	SUBCOMPACT			0			33	0

COMPACT			3	20.3	28.5	23	0.128649209

MIDSIZE				19.7	29	23	0

LARGE				18	25	21	0

TWO-SEATER						0	0

SMALL P/U			6	16.1	20.2	18	0.33863231

LARGE P/U			13	14.3	19.1	16	0.806282723

SMALL VAN				15.5	20.7	17	0

LARGE VAN				14.2	19.1	16	0

Baseline Average FE		17.3

FY2002 FE Goal		18.3

FY2005 FE Goal		20.3

* Average fuel economy values estimated by category based on FY 1999 New GSA Leased Vehicles for DOE fleet

and fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

153,560 	 156,555 		 31,811 			 31,811 	 31,811 	 31,811 	 31,811 	 31,811

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 20 miles) = CNG (govt), LPG (private)

- Oak Ridge in MSA

- Non-AFV acquisition rates assumed same as FY2001; AFV acquisition = 75% EPACT

- All acquisitions assumed to be LDV

- LDV turnover assumed to be five years

- Mix of AFVs based on 1999 purchased (100% E85)

- Avg annual LDV fuel use = 302611/1741 = 174 GGE

- FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	19	13	30	23	30	23	30	23	30	23	30	23

MDV

HDV

Total AF			AFV Infra

Total AFVs in Service in FY2005	Fuel Use (GGE) in FY 2005		($)		FY01	FY02	FY03	FY04	FY05

E85 FFV	115		15008			35000

Total	115		15008					3001.5	6003	9004.5	12006	15008

AFV Refueling

Infra		$

Biodiesel		0

E85		255000	(Two sites)

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase

- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 3010 mi/yr based on 174 gal/yr and avg 17.3  mpg

FY01	FY02	FY03	FY04	FY05

New LDV		7	7	7	7	7

gal/LDV		169	165	156	152	148

New gal used		1185	1153	1093	1066	1039

Gal saved in FY	33	65	125	152	179

Gal Saved Cum	33	98	222	375	554

Total gal saved in FY05 =			554	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 10%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

420,293 		 42,029 				 8,405.86 	 16,811.72 	 25,217.58 	 33,623.44 	 42,029.30

OVERALL PETROL FUEL REDUCTIONS FOR OAK RIDGE STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 31,811

2		15008

3		554

4		 42,029

TOTAL		 89,401

PANTEX

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 209,716 	 209,716 			0	0		 209,716

DIESEL	 97,344 	 111,654 						 111,654

TOTAL		 321,370 		 77,128 		 -   		 244,242 	 48,848

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	271	50	50	287	38	12	294	35	35

MDV	7	0	0	7	0	0	7	0	0

HDV	16	5	0	16	0	0	16	0	0

AFV	63

GASOL	DIESEL	EXEMPT

LDV	208	3	0

MDV	0	7

HDV	0	16

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

1500	1		5	13	18	15	0.336538462

1500	1			14	18	16	0

Countour	5		1	22	31	25	0.039516129

Crown Vic	1			18	25	21	0

Ram 1500	3		11	16	21	18	0.613839286

Tahoe	29		19	15	19	17	1.146666667

Baseline Average FE		16.8

FY2002 FE Goal		17.8

FY2005 FE Goal		19.8

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Pantex has HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

Fy2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

97,344 	 99,243 		 20,165 			 20,165 	 20,165 	 20,165 	 20,165 	 20,165

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (onsite); biodiesel (onsite)

- Pantex not in MSA

- Non-AFV acquisition rates assumed same as FY2001												 Afv acquisition rate assumed 75%													- All acquisitions assumed to be LDV													- LDV turnover assumed to be five years													- Problems with onsite CNG station; want to phase it out												- Mix of AFVs based on 1999 purchased (100% E85)												- Avg annual LDV fuel use = 209716/208 =  1008 GGE												- FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	38	12	35	26	35	26	35	26	35	26	35	26

MDV

HDV

AFV Infra

Total AFVs in Service in FY2005Total AF Fuel Use (GGE) in FY2005			($)		FY01	FY02	FY03	FY04	FY05

E85 FFV	130		98280				50000

Total	130		98280						19656	39312	58968	78624	98280

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase														- FY03 = 2.0 mpg increase														- FY04 =2.5 mpg increase														- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 16934 mi/yr based on 1008 gal/yr and avg 16.8 mpg

FY01	FY02	FY03	FY04	FY05

New LDV	9	9	9	9	9

gal/LDV	976	949	898	875	853

New gal used	8784	8538	8085	7876	7678

Gal saved in FY	288	534	987	1196	1394

Gal Saved Cum	288	821	1808	3003	4397

Total gal saved in FY05 =			4397	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

244,242 		 4,885 				 976.97 	 1,953.93 	 2,930.90 	 3,907.87 	 4,884.83

OVERALL PETROL FUEL REDUCTIONS FOR PANTEX STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 20,165

2		98280

3		4397

4		 4,885

TOTAL		 127,727

RICHLAND-HANFORD

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 499,704 	 499,704 			37873	37873		 461,831

DIESEL	 114,719 	 131,582 						 131,582

TOTAL		 631,286 		 -   		 37,873 		 593,413 	 118,683

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	551	7	7	820	10	10	820	7	7

MDV

HDV	823

AFV	84

GASOL	DIESEL	EXEMPT

LDV	551	0	92

MDV	0

HDV	663	160	Estimated

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

astro			1	15	19	17	0.060350877

cherokee			7	16	20	18	0.398125

durango			2	15	20	17	0.118333333

F250			8	13	18	15	0.538461538

S10			1	17	21	19	0.053781513

Tahoe			12	15	19	17	0.724210526

Windstar			1	15	23	18	0.056231884

Baseline Average FE		16.4

FY2002 FE Goal		17.4

FY2005 FE Goal		19.4

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Richland has MDV & HDV fleet

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

Fy2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

117,484 	 119,775 		 24,337 			 24,337 	 24,337 	 24,337 	 24,337 	 24,337

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = LPG (private)

- Richland not in MSA

- Non-AFV acquisition assumed same as FY2001												- Afv acquisition assumed 75%													- All acquisitions assumed to be LDV													- LDV turnover assumed to be five years													- Mix of AFVs based on 1999 purchased (100% E85)												- Avg annual LDV fuel use = 502801/(551+663) = 414 GGE												- FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	7	7	10	8	10	8	10	8	10	8	10	8

MDV

HDV

Afv Infra

Total AFVs in Service in FY2005Total AF Fuel Use (GGE) in FY2005			($)		FY01	FY02	FY03	FY04	FY05

E85 FFV	40		12420				35000

Total	40		12420						2484	4968	7452	9936	12420

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase														- FY03 = 2.0 mpg increase														- FY04 =2.5 mpg increase														- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 6790 mi/yr based on 414 gal/yr and avg 16.4 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		2	2	2	2	2

gal/LDV		401	390	369	359	350

New gal used		803	780	737	718	699

Gal saved in FY	25	48	91	110	129

Gal Saved Cum	25	73	164	274	402

Total gal saved in FY05 =			402	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall 15 percent reduction in covered fleet GGE

Covered		Assumed 15%				FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

593,413 		 89,011.94 				 17,802.39 	 35,604.77 	 53,407.16 	 71,209.55 	 89,011.94

OVERALL PETROL FUEL REDUCTIONS FOR RICHLAND-HANFORD STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 24,337

2		12420

3		402

4		 89,012

TOTAL		 126,172

SNL-KIRTLAND

TOTAL FUEL USE

1999		1999 NON-ROAD	1999 EXEMPT				2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		TOTAL GGE	GGE REDUCT

GASOL	 	 266,912 			18,000	18,000		 248,912

DIESEL	 55,003	 63,088						 63,088

TOTAL		 330,000 		 -   		 18,000 		 312,000 	 62,400

FLEET DATA -VIDS

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	413	52	11	414	124	68	414	43	7

MDV	320	31		320	26		320

HDV	30	14		30	4		30

AFV	84

GASOL	DIESEL	EXEMPT			VIDS-Gasol

LDV	386	27	24			0.935368043

MDV		320	(assume all diesel)

HDV	0	30

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

1500			1	13	18	15	0.067307692

1500			2	14	18	16	0.128571429

cherokee			2	16	20	18	0.11375

Contour			2	20	28	23	0.087142857

durango			2	15	20	17	0.118333333

F250			5	13	18	15	0.336538462

Ram 1500			2	16	21	18	0.111607143

suburban			2	14	16	15	0.134821429

tahoe			12	15	19	17	0.724210526

Windstar			1	15	23	18	0.056231884

Baseline Average FE		16.5

FY2002 FE Goal		17.5

FY2005 FE Goal		19.5

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

Fy2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

55,003 	 56,075 		 11,394 			 11,394 	 11,394 	 11,394 	 11,394 	 11,394

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = CNG (govt), LPG (private, utility), E85 (public)

- SNL in MSA and Albuquerque is AFV User City												- Non-AFV acquisition rates assumed same as FY2001												- AFV acquisition rates assumed 75% since AFV User City with 50% incremental cost paid										- All acquisitions assumed to be LDV													- LDV turnover assumed to be five years													- Mix of AFVs (50% CNG; 50% E85)													- Avg annual LDV fuel use = 228753/386 = 593 GGE												- Bi-fuel assumed to use CNG 75% of time; FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	124	68	43	32	43	32	43	32	43	32	43	32

MDV

HDV

AFV Infra

Total AFVs in Service in FY2005Total AF Fuel Use (GGE) in FY2005			($)		FY01	FY02	FY03	FY04	FY05

CNG bi-fuel	80		35580				New CNG station already funded

E85 FFV	80		35580				0

Total	160		71160						14232	28464	42696	56928	71160

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase														- FY04 =2.5 mpg increase														- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids

- LDV turnover assumed to be five years

- Assume average new LDV in 1999 travels 9780 mi/yr based on 593 gal/yr and avg 16.5 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		11	11	11	11	11

gal/LDV		575	559	529	515	501

New gal used		6327	6147	5814	5661	5516

Gal saved in FY	196	376	709	862	1007

Gal Saved Cum	196	572	1281	2142	3149

Total gal saved in FY05 =			3149	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%			FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

312,000 		 6,240 			 1,248	 2,496	 3,744 	 4,992 	 6,240

OVERALL PETROL FUEL REDUCTIONS FOR SNL-KIRTLAND STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		11,394

2		71,160

3		3,149

4		 6,240

TOTAL		 91,943

SAVANNAH RIVER

TOTAL FUEL USE

1999		1999 NON-ROAD		1999 EXEMPT			2005 GOAL

(GAL)	GGE	GAL	GGE	GAL	GGE		Covered GGE	GGE REDUCT

GASOL	 330,000 	 330,000 			9174	9174		 320,826

DIESEL	 333,000 	 381,951 	 293,000 	 336,071 		 -   		 45,880

TOTAL		 711,951 		 336,071 		 9,174 		 366,706 	 73,341

FLEET DATA -Fleet data

1999			2000			2001

INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV	INVENTORY	NEW TOTAL	NEW AFV

LDV	1472	210	169	1472	151	114	1472	206	101

MDV		48	0		96	0		93	0

HDV	87	2	0	87	3	0	87	3	0

AFV	284

GASOL	DIESEL	EXEMPT			Data

LDV	1188	0	33			Inventory #'s - from fleet

MDV						acquisition #'s - from VIDS

HDV		87

FLEET FUEL ECONOMY (NEW ACQUISITIONS) - GSA Leased Vehicle Data

Vehicle Type				1999	Fuel Economy Info

Make	Model	Cylinders	Drive	Acquisitions	City FE	Hwy FE	Combined FE

0	0	0	0	0

0			0	0

0			0	0

0			0	0

Ford	Windstar			4	15	23	18	0.224927536

Jeep	Cherokee			4	16	20	18	0.2275

Ford	F-250			9	13	18	15	0.605769231

Dodge	Dakota			4	16	21	18	0.223214286

Dodge	Ram 1500			8	16	21	18	0.446428571

Chevy	Suburban			16	14	16	15	1.078571429

Baseline Average FE		16.03

FY2002 FE Goal		17.03

FY2005 FE Goal		19.03

* Fuel economy values from DOE fleet fuel economy guide

STRATEGY

1. BIODIESEL USE

- Assume diesel use remains constant through FY2005

- Assume total conversion to B20 by FY2005

FY 2005	FY2005		EQUIV FY2005			FY01	FY02	FY03	FY04	FY05

Diesel (gal)	B20 USE (gal)		FUEL DISPL (GGE)

333,000 	 339,494 		 68,982 			 68,982 	 68,982 	 68,982 	 68,982 	 68,982

2. AFV ACQUISITIONS - VIDS

- AFV Refueling access (< 15 miles) = E85 (onsite); biodiesel (onsite); LPG (private)

- Savannah not in MSA

- Non-AFV acquisition rates assumed same as FY2001

- AFV aqusiition rate assumed to be 75% for FY 2001 -2005

- All acquisitions assumed to be LDV

- LDV turnover assumed to be five years

- Mix of AFVs based on 1999 purchased (100% E85) and current use of 61,000 E85

- Avg annual LDV fuel use = (330,000)/1188 = 278 GGE

- FFVs assumed 75% E85 use

2000		2001		2002		2003		2004		2005

Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV	Total	AFV

LDV	151	114	206	155	206	155	206	155	206	155	206	155

MDV

HDV

Total AF Fuel Use		AFV								Total AFVs in Service in FY2005	in FY 2005 (GGE)		Refueling Infra			FY01	FY02	FY03	FY04	FY05

E85 FFV	775		161588			None needed; use existing on-site

Total	775		161588						32317.5	64635	96952.5	129270	161588

3. Fuel Economy Increases

- Require gradually increasing FE consistent with FY02 and FY05 goals

- FY01 = 0.5 mpg increase

- FY02 = 1.0 mpg increase

- FY03 = 2.0 mpg increase

- FY04 =2.5 mpg increase														- FY05 = 3.0 mpg increase

- Achieve increased FE through better selection of vehicle types, use of hybrids										- LDV turnover assumed to be five years													- Assume average new LDV in 1999 travels 4456 mi/yr based on 278 gal/yr and avg 16.03 mpg

FY01	FY02	FY03	FY04	FY05

New LDV		51	51	51	51	51

gal/LDV		269	262	247	240	234

New gal used		13744	13341	12601	12261	11939

Gal saved in FY	434	837	1577	1917	2239

Gal Saved Cum	434	1271	2848	4765	7004

Total gal saved in FY05 =			7004	GGE

4. Fleet Efficiency Improvements

- Reduced vehicle trips

- Increased vehicle loads

- More use of higher FE

- Assume overall two percent reduction in LDV fleet GGE from baseline

Covered		Assumed 2%			FY01	FY02	FY03	FY04	FY05

Baseline GGE		Savings (GGE)

366,706 		 7,334 			 1,466.82 	 2,933.65 	 4,400.47 	 5,867.30 	 7,334.12

OVERALL PETROL FUEL REDUCTIONS FOR SAVANNAH STRATEGY

STRATEGY		FUEL SAVED

OPTION		(GGE)

1		 68,982

2		161588

3		7004

4		 7,334

TOTAL		 244,908

# Footnotes

U.S. Department of Energy, Office of Technology Utilization, The Federal Fleet Strategy Development Supplement, September 2000.

Executive Order 13149: Greening the Government through Federal Fleet and Transportation Efficiency, guidance Document for Federal Agencies, prepared by U.S. Department of Energy, Office of Technology Utilization, July 2000.