City of Santa Monica

Integrated Pest Management Program

### Conditions for Professional Service

Products Covered in the Following Excerpt:

Integrated Pest Management

EXCERPT:

# I.	General

## A.	Description of Program

This contract specification is part of a comprehensive Integrated Pest Management (IPM) Program for properties owned, occupied, leased or otherwise operated by the City of Santa Monica.   IPM is a process for achieving long term, environmentally sound pest management through the use of a wide variety of technical and management strategies.  Management techniques include structural modifications and procedural modifications that reduce food, water, harborage, access and environmental conditions that are favored by pests.  Management strategies include education, training and promotion of behavioral practices that are important in the IPM program.

The success of an IPM program relies on both verbal and written communication between the CONTRACTOR and city employees.  The city has designated appropriate individuals to take on the following roles and has created an IPM plan consistent with the City’s operations, facilities and needs:

IV.	Specific CONTRACTOR Service Requirements:

A.	Proposed Material and Equipment for Service

The CONTRACTOR shall provide the IPM Program Coordinator with current sample labels and Material Safety Data Sheets (MSDS) of all pesticide products to be used, and list and describe pesticide application equipment, rodent bait boxes, insect and rodent trapping devices, pest monitoring devices, pest surveillance and detection equipment, and any other pest management devices or equipment that may be used to provide service.  The description shall include brand names and other applicable information to clearly identify the products and their hazards.  Additionally, applicable labels and MSDS shall be provided to the Pest Manager at each site.

D.	Structural and Operational Changes

The CONTRACTOR shall recommend and describe site-specific solutions to pest management issues, including structural and operational changes, for observed sources of pest food, water, harborage and pest access at the time of inspection on the Quality Assurance Form.  If a more detailed report is necessary or if two consecutive reports asking for structural, operational or sanitation changes have gone unheeded by the Pest Manager, the CONTRACTOR shall file a supplemental report with the IPM Program Coordinator within five (5) working days of the third inspection.  The supplemental report shall summarize prior recommendations and formally request the assistance of the IPM Program Coordinator.

## VI.	Use of Pesticides

The  CONTRACTOR shall  be responsible for application of pesticides according to all label restrictions and instructions.  All pesticides used by the CONTRACTOR must be registered with the State of California.  Transport, handling, storage, use and disposal of all pesticides shall be in strict accordance with the pesticide product label and all applicable federal, state, county and City of Santa Monica laws and regulations as well as City policy.

The CONTRACTOR shall adhere to the following rules for pesticide use:

A.	Approved Products

The CONTRACTOR shall apply only those pesticide products that have been approved by the IPM Program Coordinator.

B.	Pesticide Storage

The CONTRACTOR shall not store any pesticide product on city premises without the approval of the IPM Program Coordinator.

C.	Application by Need

Pesticide application (with the exception of Insect Growth Regulators) shall be according to need and not by schedule.  As a general rule, application of pesticide in any interior or exterior area shall not occur unless visual inspection or monitoring devices indicate the presence of pests in that specific area and use of a pesticide is the most effective management technique for an IPM program.  Preventive pesticide treatments of areas are acceptable on a case-by-case basis where surveillance indicates a potential insect or rodent infestation.  Written approval MUST be granted by the IPM Program Coordinator prior to any preventive pesticide chemical application.

D.	Risk reduction

When pesticide use is necessary, the CONTRACTOR shall employ products and techniques that have been determined by the City, in consultation with other appropriate entities, to pose the least risk to people, workers and the environment.  Additionally, the most precise application technique and minimum quantity of pesticide necessary to achieve appropriate management shall be applied.

## VII.  Insect Management

A.  Emphasis on Non-Pesticide Methods:

The City prioritizes and the CONTRACTOR shall use non-pesticide methods of pest management wherever possible.  For example:

1.	Portable vacuums, rather than pesticide sprays, shall be used for initial clean-outs of cockroach infestations, for swarming insects (ants, termites and others) and for management of spiders in webs wherever appropriate.

- Trapping devices, rather than pesticide sprays, shall be used for fly management wherever appropriate.

- Other non-pesticide methods, as needed.

B.	Application of Insecticides to Cracks and Crevices

As a  general rule, the CONTRACTOR shall apply all insecticides as crack and crevice treatments only, defined in this contract as treatments in which the formulated insecticide is not visible to a bystander during or after the application process. The CONTRACTOR will seal cracks and crevices with caulk or other products approved by the IPM Program Coordinator and this will be considered part of routine pest management.

C.	Insecticide Bait Formulations

When pesticides must be used to manage cockroaches, ants and other insects, bait formulations shall be used whenever possible.

D.	Monitoring

Visual identification, sticky traps or other devices shall be used to guide and evaluate indoor insect management efforts whenever possible.

## VIII. Rodent Management

B.	Use of Rodenticides

In exceptional circumstances, when rodenticides are deemed essential for adequate management, the CONTRACTOR shall obtain approval of the IPM Program Coordinator prior to making any treatment.  As a general rule, rodenticide application outside buildings shall emphasize the direct treatment of rodent nesting sites and burrows wherever feasible.  In all other applications, bait formulations of rodenticides, regardless of packaging, shall be placed in EPA-approved tamper-resistant bait boxes.

C.	Use of Bait Boxes

Frequency of bait box servicing shall depend upon the level of rodent infestation and the needs of the City.  All bait boxes shall be maintained in accordance with EPA regulations, and with an emphasis on the safety for non-target organisms.  The CONTRACTOR shall adhere to the following five points:

1.	All bait boxes shall be placed out of the general view and in protected areas so as not to be affected by routine cleaning and other operations.

2.	The lids of all bait boxes shall be securely locked or fastened shut.

3.	All bait boxes shall be securely attached or anchored to the floor, ground, wall or other immovable surface so that the box cannot be picked up or moved.

4.	Bait shall always be placed in the baffle-protected feeding chamber of the box and never in the runway of the box.

5.	All bait boxes shall be labeled on the outside with the Contractor's business name, phone number, date, bait material and bait EPA registration number by the CONTRACTOR or his employee at the time of installation.  The labels shall be checked for readability at each servicing and the date of most recent servicing shall be written onto the label.