POLAR Spacecraft Status As of: Tues, 22 Nov, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:56=AN STIP data only | NOAA-14J AM: 20:57=AN STIP data only | NOAA-15K AM: 17:57=AN GAC data only | NOAA-16L PM: 14:54=AN GAC&LAC data | NOAA-17M AM: 22:24=AN GAC&LAC data | NOAA-18N PM 13:54=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU-1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ Investigating instability | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate ROLL Rgmode=PASSIVE Gyro-1 Off 10/24/05 Gyro-3 Off 6/10/04 Gyro chans X-Z only TOAR 454 RGyro roll estimate gains updated 11/17 | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation Probable collision on 20 Nov at 10:31z | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Momentum shift transition underway since 1 Nov 05. |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/3/03) #2 has 3 chans inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 2.66 Mbps reverse playback 18 Oct | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 OFF OFF 13Nov-13Dec | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 omni=rcp Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/05 Full Sun Sun Angle 13 start new uptrend to 22 in early Jan Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -50 Batts 1&3V/T=6/9 Batt2 VT=7/9 Since 11/22/05 Eclipse all year Sun angle 49 Steady trend Batts 1-3= LRC Degraded shunts SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 12 Uptrend to 15 in mid-Dec 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 41 Start new uptrend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Array 360 slew test on 21 & 22 Sept Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Erratic Frequent scan motor current surge Occasional imagery bar codes Channels 2&4 APT | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Variable No bar codes since 12 Oct. Status upgraded 10/18/05 TCE24 OFF 4/14/04 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal 7/12/05 FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 CLOSED Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | Operational Status downgraded to Yellow 15 Aug 05 LW channel 1-12 noise TOAR 448 LW Noise improved since 14 Oct |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU8 off TOAR 449 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 as of 27 Sept | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous TED shutdown 24 Sept | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Thermal downtrend ended 10 Oct | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	There were no changes to N12 during the past reporting period.

NOAA-14:	Recent N14 AVHRR imagery is mostly clean, although there are still instances of “bar codes”.  The scan motor

continues to experience very frequent scan motor current surges which affect synch delta and ultimately imagery.  However, AVHRR imagery is often nominal.  This higher than expected percentage of nominal N14 HRPT images can probably be attributed to the MIRP rephase enable operation that now occurs on N14 every orbit over the South Pole.  See illustration 1.

Power balance remains a significant concern on N14. At the present time, EMOSS power engineer is trying to balance the power situation by manipulating two mutually exclusive objectives.  The first and most important objective is to reduce shunt load stress which is best done by reducing power generation through solar array offset increases.  If shunt stress is not reduced, a bus over-voltage situation could result (as it once did in April of 2003) resulting in autonomous spacecraft safing routines (mode controller and boost regulator swaps) executing.  Conversely, reducing shunt stress tends to result in less than optimum battery charging and lower battery voltages which then increase the potential for a battery UNDERvoltage situation (load sheds) autonomously executing.  Unfortunately, the difference between one or the other of these two events occurring is approximately 75-100 watts, the amount of a single light bulb.   One 17 Nov, the V/T levels on all 3 N14 batteries were changed from 6/9, 7/8, 6/9 to 7/9, 8/9, 7/9.  Subsequent analysis revealed that this change was not sufficient at reducing shunt stress therefore, on 22 Nov at 13:50z the battery V/T curves were commanded back to their original 6/9, 7/8, 6/9 settings and the solar array offset was decreased to -50 degrees (from -45) in order to reduce power generation and reduce shunt loading.  Since the batteries were just making full charge at -45 degrees, the concern now is whether or not they will even reach full capacity at this new offset.  Analysis is as continuous as the 2-3 passes per day allow and additional reconfigurations can be anticipated.   See illustrations 2 and 3.

No further effort has gone into planning the MSU end of life “tilt test” on N14 that has been addressed in previous Weekly Reports although the power reconfiguration operations in recent days have fulfilled one perquisite for such a test.  That prerequisite is determining where the “edge” of power balance lies on N14.  Recent analysis has shown that under the present EPS configuration, the spacecraft is already on that edge.

NOAA-15:	N15 VTX-1 (APT data) remains off because of an RF conflict with N12 and will remain off until 13 Dec.  Otherwise, all N15 subsystems were nominal relative to recent performance during the past week.  See illustrations 4 and 5 for graphical depictions of selected payload and ADACS performance.

NOAA-16:	The N16 AVHRR scan motor current reached near nominal values during the past week and appeared to stabilize in

that range while synch delta has also markedly improved in the past week or two.  Imagery also appeared to be generally nominal with no bar codes or MIRP rephase frame losses during the entire week.  However, despite the scan motor improvement and stability, HRPT wave patterns still persist at times, possible because the scan motor current does often “breech” the transitional area between fully nominal and wave pattern values.  One other item of note on N16 AVHRR is that numerous components are at all time high temperatures.  This situation is partly by design because the AVHRR TCE (24) was turned off in order to warm the instrument somewhat.  It is now as warm as it has ever been although baseplate and scan motor temps remain several degrees below the threshold where TCE24 is supposed to be commanded back on (from the ground).  The EMOSS instrument engineer has been investigating this thermal situation and has been informed that it is not at this time a reason for concern.  See illustrations 6 and 7.

The N16 ADACS subsystem remains stable after the gyro 1 failure on 24 October while “cleanup operations”

continued.  As addressed in an Event Report (SER-05-P462) generated by EMOSS C&CS Engineer, “On 17 Nov 2005, the SOCC uplinked new gains for the reduced gyro roll estimation filter.  The gains were developed after reduced gyro performance was reviewed.  NOAA-16 has been in an Estimate Roll (Y) attitude algorithm since gyro 1 was turned off on Oct 24th, 2005.  The signal from the earth sensor was noisier than expected (as compared to NOAA-15’s reduced gyro testing of last year).  Filter performance using the initial gain set produced excessive noise in derived rate roll rate, causing the command Y-RWA torque signal to periodically saturate to the maximum value (see figure 1).  Attitude performance still met pointing specifications but there were questions about long term health of the attitude

control subsystem.  These new gains for the filter were created by LMSSC and uplinked to the control CPU and an improvement immediately resulted.  The new gains reduced the commanded torques significantly, lowering the average wheel motor currents and reducing the wheel bearing temperature fell by more than 4.5 degs C ( to 20 degrees).  N16 remains in the estimate roll reduced gyro algorithm, and is expected to remain so permanently.  The new filter gains improved roll attitude performance and will be analyzed to verify stability and long term health.   The filter was only installed on the control CPU in case of instability.  If the new gains threatened attitude performance, a switch of control to the backup CPU (which still had the old gain values) would have maintained spacecraft attitude.  Once performance has been analyzed and determined suitable to current operational health, the updated gains will also be uplinked to the backup CPU.”  See illustrations 8 and 9.

Otherwise N16 was generally nominal with the AMSU’s performing in a nominal and stable manner but the HIRS filter motor current again edging up to equal its all time high value (illustrations  10 & 11)

NOAA-17:	On 20 Nov, at 10:31Z, the N17 spacecraft apparently collided with some as yet undetermined space object.   This

conclusion was reached by engineering because at that time, numerous spacecraft attitude control component values (Rwheel speeds and motor currents,  calculated rates, attitude errors and momentums, etc.) along all 3 axis’ suddenly surged to extreme levels.  By degree of severity, this event affected Yaw the most, then Pitch while Roll was only (relatively) slightly impacted.  The severity of the yaw impact was so significant (Yaw error angles as high as +4 to as low as -6 degrees compared to a typical value of less than +/- 0.1)  that the X-wheel which controls Yaw surged 6 degrees C within a few minutes while its motor current pegged out at 3.5 amps.  Eventually, this wheel actually went non-linear for several seconds at 10:34:30z the first such occurrence on any N17 reaction wheel since launch.  At 10:42z a yaw unloading using Roll Yaw Coil #1 occurred.  However, spacecraft momentum at the conclusion of this unload remained so great that flight software intervened at 10:43z and autonomously swapped out RY Coil #1 for the backup RY Coil #2.  At 11:04z the next unload occurred while the spacecraft was being monitored over Barrow with the backup coil driving the operation and a miscompare flag on the Coil in use (among others) flagging the controllers of the problem.  At this point controllers notified engineering of the problem.  Engineers arrived at the SOCC but were unable to monitor any relevant data because no recorder dump had occurred at Barrow and N17 had just entered its daily blind.  At 14:45z, the spacecraft exited the blind and engineering was able to review data from the time in question.  By this time, the spacecraft attitude situation was back to near nominal.  Therefore, all that was left to accomplish was to switch back to the primary RY Coil and re-enabled RY Coil switching.  These commands were implemented at a Wallops pass at 16:30z.  Spacecraft attitude control has remained nominal ever since.  See illustrations 12-23.

An investigation has since ensued to determine the size of the object that struck the spacecraft as well as the impact location on the spacecraft as well as other relevant information.  It is known that the annual Leonid meteor shower peaked on 17 Nov and was ending the same day that N17 was struck although there is no definitive proof that this was a Leonid strike.  On 21 Nov, EMOSS engineers undertook a comprehensive analysis of the effect of this event on other subsystems and components on N17.  After generating and analyzing over 500 plots covering all N17 subsystems and most hardware components the teams conclusion is that other than attitude, which was significantly impacted but only for a very short duration, no other subsystem appeared to have been unduly influenced by this event.  The most salient effect during the time of this incident on N17 was primarily thermal, probably from the re-orientation of the spacecraft as it tried to regain nominal attitude as well as increased reaction wheel temperatures being conducted to nearby components.  Furthermore, almost all the thermal changes were relatively minor (no more than a couple of counts) and most returned back to previous equilibriums by the end of the day. Besides ADACS, the primary subsystem impacts from this event appeared to be COMM.  One noticeably change was the GRD AGC (which were noticeably although perhaps not significantly, lower during passes) and GRD temps which were slightly higher.  Another noticeable if not substantial change was STX-4 output power which was slightly lower after the event as were its temps.  There were also some minor influences on the power subsystem primarily because the changes in so many thermal profiles might have changed heater operational cycles (among other things).   The payloads suite, besides some thermal changes also appear to have not been impacted by this event in any way and no reports were received by EMOSS engineers regarding product problems.  The investigation is ongoing with a wide scope of involvement already underway.

NOAA-18:	In performing analysis on N18 EMOSS engineers detected that the Pitch torque coils had not been active in recent

days.  After looking further it was determined that the last time the pitch coil had performed an unload of the Z-(pitch) wheel was late on 1 Nov.  This was something not seen before on any POES spacecraft since before the year 2000.  Since that time, all other spacecraft (including N18 up until 1 Nov) have always unloaded pitch multiple times every day.  EMOSS ADACS engineer performed additional analysis and determined that the Z-wheel, over the course of the last couple of weeks, has transitioned from a negative speed to a positive speed, and, as it transitioned, it remained within non-unload values. (Note: Z-axis momentum has correspondingly shifted from positive to negative)  Engineers have seen this before (but not in a long time) and believes there are no negative implications to attitude control or spacecraft health although unsure of the reason for this shift.  Additional analysis is being performed and an Event Report will be generated on this situation (see illustration 24).  Otherwise N18 performed nominally during the past week.

Illustration 1:  NOAA-14 AVHRR Health Analysis

(The large current spikes continue affecting the scan motor. At times the value is nominally within the 150 mAmps range.  It just hasn’t been able to stabilize there.  Imagery is sometimes bar coded and sometimes nominal.  It is probable that most nominal images are a result of the MIRP rephases enable operations that are conducted once per orbit over the South Pole rather than once per day as was previously the case.

Illustration 2:  N14 Power Analysis part 1

(The VT change of 17 Nov appears to have not been effective at reducing shunt stress.  Depicted in this plot is the 12 hour period immediately following the VT change.)

Illustration 3:  N14 Power Analysis (part 2)

(It appears that the Array Move [SA] and VT change [VT] on 22 Nov may have improved the power balance situation.  Next week should tell the tale more thoroughly.)

Illustration 4:  N15 Payload Analysis

(Nominal and stable, just like last week.)

Illustration 5:  N15 ADACS Analysis

(Nominal and stable, relatively, just like last week.)

Illustration 6:  N16 AVHRR Analysis

(Scan motor current and synch delta looking good although thermal situation is at a new high for many components which is not considered a cause for concern at this time.)

Illustration 7:  N16 AVHRR Imagery Analysis

(No bar codes or MIRP rephase frame losses but wave patterns persist. )

Illustration 8:  N16 ADACS Analysis (part 1)

(Much improved since uplinking new gains for the reduced gyro roll estimation filter)

ILLUSTRATION 9:  N16 ADACS Analysis (part 2)

(Also improved since uplinking new gains for the reduced gyro roll estimation filter)

ILLUSTRATION 10:  N16 AMSU Health

(Everything generally stable and relatively nominal)

Illustration 11:  N16 HIRS Analysis

(Generally stable but filter motor current recently equaled an all time high.)

Illustration 12:  N17 ADACS Health Analysis

(The red X indicates the time when the spacecraft collision occurred which had no impact on these two values.)

Illustration 13:  N17 Collision Analysis In Perspective

(Pull back to show what a normal 10 days of history looks like.  X indicates where the collision occurred.)

Illustration 14:  N17 Collision Analysis

(Moving in closer to primarily show how everything returned back to normal within a day.)

Zoom in on the critical 16 minutes			Zoom in on the day in question

Illustration 15:  N17 ADACS Gyro Filtered Data & Torque Collision Analysis (zoom in and out)

(As the plots on the left show most of the problem had already begun to resolve itself by before the spacecraft even reached its next support at 11:03z.  Hence the absence of any limit flags during that support. )

Illustration 16:  N17 RWheels Health During Collision Day

(Everything returned quickly back to normal.)

Illustration 17:  N17 RWheels during the critical half hour before problem was discovered.

Zoom in on the critical 16 minutes			Zoom in on the day in question

Illustration 18:  N17 ADACS Error Angles and Calculated Rates Analysis (zoom in and out)

(As the plots on the left show most of the problem had already begun to resolve itself by before the spacecraft even reached its next support at 11:03z.  Hence the absence of any limit flags during that support. )

Illustration 19:  N17 ADACS Analysis on Collision Day

(Other than the Coil swap, not much impact.)

Illustration 20:  N17 CPU-B Telemetry Changes From Collision (part 1)

(No change since last week or month.)

Illustration 21:  N17 CPU-B Telemetry Changes From Collision (part 2)

(That’s all there was.)

Illustration 22:  N17 LAC Imagery Analysis Relative to Collision (before and slightly after)

(Looks no different)

Illustration 23:  N17 GAC & HRPT Imagery Analysis Relative to Collision

(GAC image contains the time period when the collision occurred.  No obvious problem.  HRPT is first image after the blind by which time attitude was basically nominal.)

Illustration 24:  N18 Transition to Positive Wheel Speeds and Negative Momentum

(Pitch-Z axis affected.  Pitch unloading in the top plot depicted by PTC coil current.)