CONSTRUCTION SPECIAL SPECIFICATION

SECTION 02935-S

SEEDING – NATIVE GRASS

Page

PART 1 - GENERAL	2

1.01	DESCRIPTION OF WORK	2

1.02	REFERENCES	2

1.03	SUBMITTALS	2

1.04	QUALITY ASSURANCE	3

1.05	DELIVERY, STORAGE AND HANDLING	4

1.06	JOB CONDITIONS	4

1.07	PROTECTION OF SEEDED AREAS	4

1.08	PLANTING SEASON	4

PART 2 - PRODUCTS	5

2.01 	MANUFACTURER’S	5

2.02 	SEED MATERIALS	5

2.03	TOPSOIL	6

2.04	FERTILIZERS	6

2.05	ENZYMATIC AGENT:	6

2.06	MULCH	7

2.07	STRAW MULCH	7

2.08	BINDER	7

2.09	ORGANIC AMENDMENT	8

2.10	WATER	8

2.11	TEMPORARY IRRIGATION SYSTEM	8

PART 3 - EXECUTION	8

3.01 	EXAMINATION	8

3.02	SOIL PREPARATION	8

3.03	FERTILIZATION AND ENZYME APPLICATION	10

3.04	SEED APPLICATION	10

3.05	HYDROMULCHING/TACKIFIER	11

3.06	STRAW MULCH	11

3.07	WATERING	12

3.08	ESTABLISHMENT OF TURF AND MAINTENANCE	12

3.09	INSPECTION	13

3.10	FINAL ACCEPTANCE	14

3.11	GUARANTEE	14

CONSTRUCTION SPECIAL SPECIFICATION

SECTION 2935-S

SEEDING – NATIVE GRASS

PART 1 - GENERAL

DESCRIPTION OF WORK

Sustainable site design promotes the use of native, well-adapted grass species that stabilize and bind the soil. This reduces maintenance and requires modest irrigation after initial establishment of a healthy stand of grass.  Maintenance is reduced and due to its low-growing habit frequent mowing isn’t necessary.

Conservation and protection of the natural resources at the site are important.  Any disturbance of natural resources occurring during planting operations should be kept to a minimum.

All native grass seed shall be certified by state of origin.  The certification authority for the state of New Mexico is the New Mexico Crop Improvement Association [505.646.4125]. Seeding establishment and maintenance of native grass and wildflower.

Furnish all labor, materials, and equipment necessary for preparation of seedbed, installation and establishment of seed, mulch, wildflower, and related work specified herein.

REFERENCES

    - The publications listed below form a part of this specification to the extent referenced. The publications are referred to in the text by basic designation only.

U.S. DEPARTMENT OF AGRICULTURE (USDA) AMS SEED ACT (1995) Federal.  See Act Regulations Part 201

AMERICAN SOCIETY FOR TESTING AND MATERIALS (ASTM)

ASTM D 4972 (1995a) pH of Soils

ASTM D 5268 (1992; R 1996) Topsoil used for Landscaping Purposes.

SUBMITTALS

    - Submit in accordance with the requirements of Section 01300:

Certification of Landscape Work

Certificates of inspection and manufacturer's or vendor's certified analysis for soil amendments, mulch blankets, fertilizer, and tackifier materials.

Vendor’s certification for each seed mixture required, stating botanical and common name, percentages or purity, germination, and weed seed percentages for each seed specie.  Seed bag tag and weights per bag with copies of invoices.

Proposed source of all native grass and shrub seed [wildflower], which shall indicate the location from which the seed was harvested.

B.	Planting Schedule, Landscape Work: Proposed planting/seeding schedule showing scheduled dates for each type of planting in each area of the site.  Coordinate with specified maintenance periods to provide maintenance from date of final acceptance.  Once the schedule is accepted, revise dates only with the SDR’s approval after documentation of delays.

- Maintenance Instructions, Landscape Work: Instructions shall be submitted recommending procedures for the maintenance of seeding work for one full year.  These instructions are provided as a guideline only to assist Sandia in establishing a maintenance program.

QUALITY ASSURANCE

A.	General

1.	Landscape Contractor: A single licensed firm specializing in all aspects of landscape work and has a minimum of 5 years of experience in performing seeding as specified.

Provide seed mixture in containers showing percentage of seed mix, year of production, net weight, date of packaging, and location of packaging. Containers shall be shipped with certificates of inspection as required by governmental authorities.

Furnish seed label in accordance with the requirements of the Federal and New Mexico statutes and regulations governing seed labeling: such resulting requirements include but are not limited to: Federal Seed Act and Amendments, rules and regulations established by the US Department of Agriculture, the New Mexico Seed Law, and all resulting regulations or restrictions established by the New Mexico State University or other authorized entity.

Ensure the seed mix and its application complies with the requirements of all other Federal and New Mexico statutes and regulations governing seeds, plants, and weeds:  these requirements include but are not limited to:  the Noxious Weed Control Act and all rules, regulations, or control measures.

Do not make substitutions for specified materials. If specified material is not available, submit proposal for use of substitute material.

B.	Analysis and Standards:

1.	Standard products shall be packed with manufacturer's certified analysis.

2.	For other materials, an analysis shall be performed by a recognized laboratory in accordance with methods established, wherever applicable or as further specified.

DELIVERY, STORAGE AND HANDLING

A.	Packaged Materials: Packaged materials shall be delivered in sealed containers showing the weight, analysis and name of manufacturer. Materials shall be protected from deterioration during delivery, and while stored at the site.

JOB CONDITIONS

A.	Seeding shall not be performed until finish grading, and structures in or adjacent to areas to be planted have been installed, and approved.

B.	Work within seasonal limitations for various seed species.  Refer to Section 3.04A.

C.	When detrimental conditions are encountered, notify the Sandia Delegated Representative before proceeding.

PROTECTION OF SEEDED AREAS

A.	Seeded areas shall be protected from damage, disturbance, or construction activity after planting operations are complete.

- Damage resulting from construction activities, erosion, gullies, washouts, or other causes shall be repaired by filling with topsoil, tamping, refertilizing, and reseeding by the Contractor at his expense, if such damage occurs prior to acceptance of the project.

- Protection and Maintenance of Native Seed in Irrigated Areas:  For areas where temporary irrigation is provided, protect and maintain native seed areas until uniform germination and growth is established.  At that time, the area will be accepted by the SDR if no void or bare areas greater than 25 square inches occur within the seeded area.  If these standards are not met the area shall be reseeded and maintained until final acceptance.  Remove tumbleweed, Russian Thistle and other nuisance, non-grassy weeds during the maintenance period.

PLANTING SEASON

A.	Native Grass Seed Mixture in Non-Irrigated Areas: Planting shall be done when conditions are favorable or as approved by the SDR.  Refer to Section 3.04.A.

B.	Native Grass and Wildflower Seed Mixture in Non-Irrigated Areas: Planting shall be done when conditions are favorable or as approved by the SDR.  Refer to Section 3.04.A.

PART 2 - PRODUCTS

2.01 	MANUFACTURER’S

A.	Native Grass and Wild Flowers – Plants of the Southwest (505) 344-8830, or approved equal.

B.	Natural Fertilizer and Soil Conditioner – Soil Food Inc., (505) 983-8075, or approved equal.

C.	Binder – Plants of the Southwest, (505) 344-8830, or approved equal.

2.02 	SEED MATERIALS

A.	Seed shall be fresh, clean, new-crop seed complying with the tolerance for purity and germination established by the Official Seed Analysts of North America.

1.	Native Grass and Wildflower Seed: High Desert Mix and Summer Green Lawn Blend.

  - Native Grass Seed: Mixture shall be composed of a 50/50 mix of Buffalo Grass and Blue Grama

  - Contractor shall furnish certification showing origin of all seed and pure live seed (PLS) purity times percent germination.  Each bag of seed shall be tagged and sealed by the seed dealer in accordance with the State Department of Agriculture or other local certification authority within the state of origin.  The label shall indicate analysis of seed and date of analysis, which shall not be more than 9 months prior to delivery date.  Seed may be premixed by the seed dealer and appropriate data indicated on the bag label for each variety.  Refer to 2.02.D for seed mixture and rate of application.

B.	Seed shall be domestic grown and shall be furnished in sealed standard containers, each of which carries the analysis label.

C.	Seed, which has become wet, musty or otherwise damaged in transit or storage will not be acceptable.

D.	The seeding rate of each seed type shall be as follows:

            - Wildflower Seed – High Desert Mix:  2 lbs. Per 6,400 sf.

            - Summer Green Lawn Blend – Blue Grama and Buffalo Grass:  2 lbs. Per 1,000 sf.

            - Buffalo Grass: 4 lbs. Per 1,000 sf.

2.03	TOPSOIL

A.	Topsoil shall be as defined in ASTM D 5268.

- Suitable topsoil includes selectively excavated material that is representative of soils in the local vicinity that produces growths of grass or other vegetation and is reasonably free from underlying subsoil, clay lumps, objectionable weeds, litter, brush, matted roots, toxic substances or any material that might be harmful to plant growth or be a hindrance to grading, planting or maintenance operations.

- Topsoil shall not contain more than five (5) percent by volume of stones, stumps, or other objects larger than one inch in any diameter.

- Imported topsoil shall comply with the following:

1. Composition (by volume)

Organic material – minimum of 2%.

Silt – minimum of 15%.

Sand – 15 to 50%.

Clay – 15 to 35%.

Foreign Materials – maximum of 1.0%.

- Soil pH shall be suitable for seed specified and be tested in accordance with ASTM D 4972.

- Transport imported topsoil directly from the source to final position unless approved by the Sandia Delegated Representative to be place in stockpiles.  If amendments are required, mix in an approved manner prior to placing on site.  If stockpiling is approved, the locations and amount of the stockpiles will be designated by the SDR.

  - FERTILIZERS

    - Fertilize native grass and wildflower areas after establishment when actively growing with a natural fertilizer/Soil Conditioner manufactured by Soil Food Inc., or approved equal.

  - ENZYMATIC AGENT:

BioMax or SuperBio, as available from Organic Technology Inc., (505) 291-1100, or an approved equivalent enzymatic agent.  Apply BioMax or SuperBio at a rate of 5 gallons per acre, diluted with 10 gallons or more of water.

  - MULCH

A.	Straw for vegetative mulch shall be harvested stalks of oats, wheat, barley or rye.

B.	65 percent of mulch by weight shall be 10 inches long or longer.

C.	Provide mulch material consisting of virgin wood fibers manufactured expressly from whole wood chips.  Process the chips in such a manner as to contain no growth or germination inhibiting factors.  Do not produce fiber from recycled material such as sawdust, paper, cardboard, or residue from pulp and paper plants. Mulch shall be free of noxious weed seed.

- Hydromulch:  Excel Fibermulch with binder as manufactured by American Excelsior Co.; 850 Avenue H East, P.O. Box 5067, Arlington, Texas, 76001, (817) 640-1555, local phone (505) 345-7806, or an approved equivalent mulch with binder.

- Combine mulch with a colloidal polysaccharide tackifier that has no growth or germination inhibiting factors and is nontoxic.  Apply the uniform mixture to the seeded area.

- Tackifier:  Exact-Tak tackifier as manufactured by American Excelsior Co.; 850 Avenue H East, P.O. Box 5067, Arlington, Texas, 76001, (817) 640-1555, local phone (505) 345-7806, or an approved equivalent tackifier for straw or hay mulch.

- Substitutions are allowed only under provisions of Section 1330, Submittal Procedures.

  - STRAW MULCH

A. 	Provide straw mulch that is perennial native or introduced grasses of fine stemmed varieties.  At least 65 percent of the herbage by weight of each bale of straw must be 10-inches in length or longer.  Hay with noxious seeds or plants will not be accepted.  Rotted, brittle or molded hay will not be accepted.  Marsh grass or prairie hay composed of native grass species to be seeded is acceptable.  Tall wheat grass, intermediate wheat grass, switch grass or orchard hay are acceptable if cut prior to seed formation.  Provide marsh grass composed of mid to tall native grasses (usually tough and wiry grass and grass-like plants found in the lowland areas within the Rocky Mountain Region).

  - BINDER

- A natural glue made form plant material that holds seed and mulch in place. Rate: 2 lbs. Per 1,000 sf.

  - ORGANIC AMENDMENT

OMNI as available from Western Organic Inc., (505) 877-8670.  Apply at a rate of 2-inch loose depth.

New Mexico Compost:	New Mexico Compost Products

Soilutions

Compost Site:  9008 Bates Road, SE

Albuquerque, New Mexico  87105

(505) 877-0220

Apply at a rate of 1-inch loose depth.

  - WATER

A.	Contractor shall provide suitable quality water to establish and maintain a vigorous growth of grass.

  - TEMPORARY IRRIGATION SYSTEM

    - The Contractor will provide a temporary irrigation system to establish a healthy stand of grass.

PART 3 - EXECUTION

3.01 	EXAMINATION

A.	Examine subgrade, verify elevations, as shown on drawings, repair deficiencies in need of correction.

B.	Notify the SDR of finished rough grading for approval before placing topsoil.  Acceptability of the grades shall be determined by the SDR prior to seedbed preparation.

  - SOIL PREPARATION

A. 	Seeded Areas:

1.	Undisturbed Topsoil:

a.	Prior to loosening topsoil, remove undesired vegetation and clear ground surface of all other materials that would hinder proper grading or tillage.

b.	Loosen topsoil of seeded areas to a minimum depth of 4 - 6 inches.  Uproot all competitive vegetation and work soil to a uniform surface free of clods and large stones 2-inches and larger in any dimension.

c.	Drag to a smooth even surface. Rake all areas to remove sticks and debris or other foreign matter that would interfere with seeding equipment. Grade to form all swales, pitch to catch basins streets, curbs, etc. to insure proper surface drainage.

    - Remove high areas and fill in depressions. Till soil to a homogenous mixture of the fine texture. Meet finished grades.  Till in organic amendment into the top 6" of the soil.

    - Tilling must be performed across the slope when practical and shall be performed in two directions whenever one is insufficient to adequately break up the soil.  Tilling shall not occur when the wind is over 10 mph and is causing a dust problem to adjoining areas.

    - Limit fine grading to areas, which can be promptly planted within a 24-hour period.

    - Seedbeds should be permitted to settle or should be firmed by rolling before seeding is made.

    - Prior to seeding, water all areas thoroughly for 4 weeks to the point of saturation to produce weed growth. Water at the rate of 2 cycles/day.  Apply "Roundup" herbicide to kill all growth, and proceed with seed installation after period recommended by herbicide manufacturer.

    - Do not work when the moisture content of the soil is unfavorable or the ground is otherwise in a non-tillable condition.

    - Do not till grounds that is already loose to a depth of 2-inches or more that has undergone regarding and fill.  Till newly cut slopes.

    - Repair any piping damaged during disking or seeding operations.

2.	Replace or New Topsoil:

a.	Prior to replacing topsoil, scarify subsoil to a minimum depth of 6 inches.  Soil clumps or clods shall not be larger than 3 inches in diameter. Remove all rocks larger than 1-1/2 inch diameter in size.

b.	Spread topsoil to a minimum depth of 4 inches.

c.	Drag to a smooth even surface. Grade to insure proper drainage.

d.	Grade lawn areas to a smooth, even surface with loose uniform texture.

e.	Limit fine grading to areas to be promptly planted.

Seedbeds should be permitted to settle or should be firmed by rolling before seeding.

  - FERTILIZATION AND ENZYME APPLICATION

- Apply fertilizer and enzymatic treatment of the type, formulation, and rate of application as designated uniformly to the prepared seedbed.  Delay application of fertilizer if seeding will not follow within a day.

- Prepare the seedbed again if the SDR determines that rain or some other factor has affected the prepared surfaces and may prevent seeding to the proper depth.

  - SEED APPLICATION

- Seeding shall be accomplished only between May 15th and September 15th unless specific permission in writing is issued by the SDR to allow seeding before or after these dates.

- Do not seed during windy weather, or when the topsoil is dry, saturated or frozen.

- Lightly roll surfaces and reshape to level humps and hollows.  Secure the SDR’s approval before seeding.

- Seed Application: Use approved seeder, distributing seed evenly over the entire area.  Rice hulls and other fillers shall be used to prevent uneven separation of lighter seed.

1.	Native Grass and Wildflower Area:

a.	Wildflower seed – High Desert Mix: 2 lbs. Per 6,400 sf area.

b.	Native Grass Area: Summer Green Lawn Blend – Blue Grama and Buffalo Grass: 2 lbs. Per 1,000 sf.

  - Native Grass Area:  Buffalo Grass: 2 lbs. Per 1,000 sf.

- Immediately following the seeding operation, the seedbed shall be lightly raked or chained to provide approximately ½-inch cover of soil over most of the seeds.

- Wet seeded areas slowly but thoroughly, and keep moist but not saturated at all times until the grass is up.

- Protect turf areas by erecting fences, barriers, and signs necessary to prevent trespass.

- Drill Seeding:

            - Refer to Contract Drawings for seed mix and rate.  Uniformly apply the prescribed mix and rate over the area to be seeded as follows:

  - Accomplish seeding operations, where practical, by drilling in a direction across the slope.  Plant seed approximately 1/2 – inch deep.  The distance between the drilled furrows must not exceed 4 – inches.  If the furrow openers on the drill exceed 4 – inches, drill the area twice to obtain a 4 – inch distance between furrows.  Seed with grass wheels, rate control attachment, seed boxes with agitators for trashy seed and separated boxes for small seed.

- Broadcast Seeding:

  - Where indicated on the Contract Drawings, or where it is not practical to accomplish seeding by drilling, mechanically broadcast the seed by use of hydro-mulch slurry blower or a rotary spreader or a seeder box with a gear feed mechanism.  If seeding is done with a slurry blower, use the highest pressure and smallest nozzle opening, which will accommodate the seed.

  - Immediately following the seeding operation, lightly rake the seedbed or loosen with a chain harrow to provide approximately 1/2-inch of soil cover over most of the seed.

  - HYDROMULCHING/TACKIFIER

- Immediately following the raking/chaining operation, apply hydro-mulch fibers with tackifier to seeded areas at the rate specified by the manufacturer.  Mix slurry in a tank with an agitator system and spray, under pressure, uniformly over seeded areas.

- Use both vertical and horizontal movements in the applicator to achieve an even application of the slurry material.  Keep all materials in uniform suspension throughout the mixing and suspension cycle when using hydraulic mulching equipment.

  - STRAW MULCH

A.	Immediately following the raking/chaining operation, add straw mulch to the seeded areas.

- Apply straw mulch at a minimum of 1.5 tons per acre of air dry material.  Spread the straw mulch uniformly over the area either by hand or with a mechanical mulch spreader.  When spread by hand, tear the bales of straw apart and fluff before spreading.  Do not mulch when velocity exceeds 10 mph.

- Wherever the use of crimping equipment is practical, place mulch in the manner noted above by anchoring it into the soil.  Use a heavy disc such as a mulch tiller, with flat serrated disc at least 1/4 – inch in thickness, having dull edges, and space no more than 9 – inches apart to anchor the mulch into the soil, with discs of sufficient diameter to prevent the frame of the equipment form dragging the mulch.  Anchor mulch a minimum depth of 2 – inches and across the slope where practical with no more than two passes of the anchoring equipment.

- If mulch areas cannot be anchored by crimping, provide hydro-mulch wood fibers with tackifier at the rate of 500 lbs. per acre. Mix slurry in a tank with an agitator system and spray, under pressure, uniformly over seeded areas. Keep all materials in uniform suspension throughout the mixing and suspension cycle when using hydraulic mulching equipment.  Mix 400 lbs. Of wood fiber with 100 lbs. of tackifier.

- Keep all materials in uniform suspension throughout the mixing and suspension cycle when using hydraulic mulching equipment.

  - WATERING

A.	Where irrigation watering is specified for seeded areas, watering of the seed will be the responsibility of the contractor.  Immediately upon completion of the mulching and binding operation, the seeded areas shall be watered, keeping the top 2 – inches of soil evenly moist until seed has uniformly germinated and grown to a height of   2 - inches.

B.	If a temporary sprinkler system is used, keep all pipe connections tight to avoid leakage and loss of water, and to prevent washing of erosion of growing areas.  Maintain sprinklers in proper working order during watering.

C.	Watering application shall be done in a manner which will provide uniform coverage but which will not cause erosion, movement or damage to the finished surface.

  - ESTABLISHMENT OF TURF AND MAINTENANCE

A.	General Maintenance:

1.	The Contractor shall maintain the seeded areas for not less than 60 days or until the final acceptance of the entire project.

2.	Turf establishment maintenance shall follow immediately, coincide with, and be continuous with the planting operation and after all planting is complete and accepted, or longer where necessary to establish acceptable stands of turf.

  - If required, maintain native grass seeded areas by watering operations with a temporary sprinkler system to maintain moisture in ground at least within two inches of surface.  Continue watering until grass stand is established to a minimum 2-inch height or for a minimum of 6 weeks.

  - Protect all areas against damage, including erosion and trespass, and provide proper safeguards. Maintain and keep all temporary barriers erected to prevent trespass.

  - Keep all walks and paved areas clean. Keep the site clear of debris resulting from landscape work or maintenance.

  - Repair all damaged seeded areas, and re-seed immediately upon discovery of damage or loss.

  - Check all barriers and temporary fencing daily, and repair or replace immediately as needed.

  - Keep native grass areas free of weeds until final acceptance by SDR.

B.	Watering

1.	Check temporary sprinkler system at each watering; adjust coverage to allow proper distribution.

2.	Newly planted areas shall be watered frequently to promote seed germination. Adjust sprinkler to prevent erosion or flooding.

3.	As turf develops, the frequency of watering shall be reduced.

C.	Mowing

1.	Buffalo grass is very low growing, frequent mowing is not necessary.  It is recommended to mow twice a year so that runners do not pile up on the surface.

2.	Do not mow native grass and wildflower area.

D.	Weed Control:

1.	Weed control shall be applied as necessary to minimize weed establishment.  Apply a broadleaf herbicide according to manufacturer's recommendations, cognizant of environmental and weather conditions. Only use on buffalo grass area. Do not use on native grass and wildflower area.

2.	Weed control shall not be applied without prior written notice as to the quantity and area to be covered. Weed control to be used shall be stored on the site and not used until it is inspected and approved by the SDR as to its conformance to quality requirements.  Any weed control applied without prior knowledge or observation by the SDR will be at Contractor's expense and considered as not applied.

E.	Fertilizing

1.	Fertilize with a natural fertilizer after establishment and when actively growing.

  - Fertilizer shall not be applied without prior written notice as to the quantity and area to be covered. Fertilizer to be used shall be stored on the site and not used until it is inspected and approved by the SDR as to its conformance to quality requirements. Any fertilizer applied without prior knowledge or observation by the SDR will be at Contractor's expense and considered as not applied.

  - INSPECTION

- The following inspection shall be the minimum required inspections to native grass after or during the course of construction.  Additional inspections shall be made at any time at the discretion of the SDR.

- Notify the SDR in writing 48 hours in advance of each required inspection.

- The sequence of required inspections shall not be changed from the sequence listed below.  Do not proceed with work of the next sequence without written approval of the work of the previous sequence.

  - Automatic irrigation system where required shall be installed, tested, and approved.

  - Each phase of soil preparation shall be inspected in process.

  - Finish grade shall be inspected.

  - Seed shall be inspected prior to seeding.

  - Seeding operations shall be monitored.

  - Seeded areas shall be inspected after completion.

  - Seeded areas shall be inspected at the end of the maintenance period.

  - FINAL ACCEPTANCE

- The Contractor shall maintain the seeded areas after seed installation until the final acceptance of the entire project and an establishment of an even, thick, vigorous strand of grass with no bare spots in seeded areas larger than 4-inch diameter.

- In the event that all other work required by the Contractor is completed before an acceptable grass cover is achieved or because of seasonal limitations, partial acceptance of the work will be made with final acceptance delayed until a satisfactory grass growth has been established.

- Final review for acceptance shall be made at the conclusion of the planting establishment period.  On such date, all project improvements and all corrective work shall have been completed.

- Written notice requesting review shall be submitted at least 10 days before the anticipated date.

- Prior to being considered ready for review, the Contractor shall have done a final weeding, and the job cleared of all debris.

  - GUARANTEE

- Guarantee all turf, native grass, and wildflowers to be in a healthy thriving condition until the end of the maintenance period.  The Contractor shall replace without cost to Sandia all seeded areas not acceptable.  Sandia will assume all maintenance responsibility upon the date final approval is given to the Contractor.

END OF SECTION