POLAR Spacecraft Status As of: Tues 24 April 07, 12:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:59=AN STIP data only No IPD processing | NOAA-14J AM: 21:10=AN STIP data only No IPD processing | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative Recursive SCT | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS | Nominal Mode Autonomous swap to YGC 30 Aug, commanded back to nominal 31 Aug RGmode=Monitor Gyro chans=XYZ | YGC Mode Autonomous swap 1 Dec Return to nominal TDB Very low N2 gas RYC switch 26 Feb 07, switched back on next pass | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB Pitch wheel bias 2400 Gyro2 safe macro | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB GAS Enabled Dec 05 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Z-momentum transition complete Pitch Torquer again active |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Macro rephased once per orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 Since 17 Apr 07 | 2 (since 4/3/03) 3 channels inop | 2 since 4/18/05 (analog drifting?) | 2 Swapped 9/20/06 | 1 Analog telem drifting |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B 4b low pressure | DTRs 1, 2B, 5B Safestate- 1B DTR 5A -INOP | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 4A Pressure leak | SSRs 1,2,3,4,5 Safestate=5B Current spikes |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 ON As of 27 Feb | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 Omni=rcp Power TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, eclipse states and sun angle) | ArrayOff +60 since 8/31/06 Full Sun Sun Angle 16 uptrend to 20 in early Jan 07 Shunt degraded SA CANT=37 degs PSSS trigger =18.5 | Array Off -50 Since 22Nov05 Eclipse all year Sun angle 55 steady Batts 1-3 LRC Degraded shunts SA CANT=22 degs PSS macro to safe SAD Motor switching enabled SAD side =A | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Uptrend to 18 early Jan 07 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 34 Steady trend SA CANT=22 degs Transitioning to full sun S/C in Sept 07 | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 66 Steady trend SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 63 uptrend to 65 on 1 Jan 07 SA CANT=22 BVR Phase Control auton swap 3/29/06 & 1/4/07 |
| AVHRR | Nominal HRPT and APT data only | Nominal HRPT data only Autonomous T/off 9/28 back on 9/30 Occasional SM current spikes. | Nominal Channel 3B only Occasional minor scan motor instabilities | Nominal Recent SM current increases TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Previous scan motor current mini surges | Nominal Channel 3B only Scan motor current drop 29 Aug 06 |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| `AMSU-A2 |  |  | Nominal | Nominal | Nominal | Nominal |
| AMSU-B |  |  | Operational Bias in All Chans. Degraded Chan-3 | Operational Space Position-3 Chan-8 degradation | Nominal | Replaced by MHS |
| HIRS | ON/Inop Turned On 4/30/05 for power balance Filter Wheel OFF | NOMINAL IPD no longer processing data Outgas heater turned ON 13 Nov 14:00z turned OFF 14 Nov 14:00z | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | NOMINAL New all time high filter motor current reached 9/17/06. Imagery occasionally exhibits high levels of radiometric noise | NOMINAL 1 Pixel cross-track misalignment. | Operational Filter Heat OFF. LW channel 1-12 noise TOAR 448 Loose LWIR lens. LW imagery erratic. |
| MHS/MIU |  |  |  |  |  | Nominal Fly Wheel Motor Current Spiking but not alarming since 27 Dec 06 Entered Motor Spin State on 27 March 07 |
| MSU | ON/Inop Turn on 12/7/06 16:53 for power balance | Operational AMDAHL Process shutdown permanently 10 Oct |  |  |  |  |
| SSU |  | OFF/Nominal Turned off 5 May for power balance |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal Autonomous turnoff 28 Sept Autonomous turnon on 30 Sept | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR |  | Nominal Autonomous turnoff 28 Sept Commanded back on 29 Sept | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | ON/Nominal Autonomous reset 8 Jun, back to nominal 10 June Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous Recursive SCT=no IFC capability | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 15:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 16:00z | Nominal Elec-CH-HVPS=1 27 June 17:00z Prot-CH-HVPS=0 |
| SBUV |  | ON No longer operational. Used for power balance only since AMDAHL Process shutdown 10 Oct 06 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops TOAR 463 sun glint IBSL test performed 12 Sept Grating motor investigation | Nominal Anode mode since 6 July 13:30z Electronics turnoff taken out of STESM safestate table TOAR 462 sun glint |
| SADPOS |  |  |  | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal Power survival safestate macro Implemented 28 Sept. Most TCE’s off. All TCE’s re-enabled 30 Sept 15:30z HIRS outgas heater turned on 13Nov, off 14Nov | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active HIRS filter heater turned OFF 9/28/06 |

COMMENTS/CHANGES:

NOAA-12:	There were relatively no changes to the NOAA-12 health situation during the past week.  NOAA-12 shunts continue to perform nominally.

N-12 NBAT2AT has started to trend up in temperature 4.5 to 5 degrees.  Sun angle is changing and NBAT2A has always been sensitive to sun angle.

N-12 bus voltage is showing signs of spikes in bus voltage below 28.5.  As the patch current gets closer to 240 mamps the shunts can not handle the excess power for the array.  N-12 will go into summer eclipse season in mid May.

NOAA-14:	There were relatively no changes to the NOAA-14 health situation during the past week.  NOAA14 continues to be in YGC mode.

A TIP swap from side 2 to 1 was performed at 14:10z on 17 April 2007 as part of End of Life testing.  Analysis shows that there was no change to TIP side 1. See Figures 1-4.

NOAA-15:	There were relatively no changes to the NOAA-15 health situation during the past week.

N15 AVHRR motor continues issuing increased current noise, as it is over the last three weeks.  Two plots are attached showing the 90-day trend, and the past 10 days. See Figure 5.

NOAA-16: 	There was relatively no change in the performance of the NOAA-16 payload subsystems during the past week and the rest of the spacecraft subsystems were also nominal during this time.

N-16 bus voltage continues to drift higher, just below 28.5 volts.  TIP drift.

NOAA-17: 	There was relatively no change in the performance of the NOAA-17 payload subsystems during the past week and the rest of the spacecraft subsystems were also nominal during this time.

NOAA-18:	The payload has operated nominal for the past week.  The EPS and ADACS subsystem has been performing nominally.

N-18 had a bus voltage spike of 30.81 volts on 15 April 2007 early in the day.  Looks like noisy telemetry during a CDA contact.  (N-17 had similar behavior and software is looking into how GAC data replaces CDA contact data in PACS for ABE use)  The bus current did not spike during this time and battery voltages were nominal.

The proposed HIRS/LRPT test has not occurred yet due to an increase in the noise of the HIRS.  The timing of the sequence is still up for debate.  But commanding sequence is it will be placed in cold cal, and the APT and beacon transmitters turned off, a wait of 120 seconds followed by the APT turn on, then the instruments and beacon will be returned to their original configuration.  This test is awaiting notifications of when to perform it.  The products are being regenerated based on the latest plan.

MetOp 2:	All NOAA instruments on MetOp were turned off on 20 April 2007 at ~11:30z.

Status as of 24 April 2007 at ~14:00z:  The NOAA instrument recovery activities have proceeded according to plan.  At the moment, we have the following instrument status:

- AVHRR in MEASURMENT mode Part 1 (Visible Channels ON), commanded during the 08:37 UTC Svalbard pass.  The patch is under control at 105K (it took approximately 2 orbits to reach this temperature).  Visible channel imagery on AVHRR looks good, based on the first orbit of data received in the EUMETSAT PPF.  The IR channels are still OFF, but since the patch is now under control, we hope to schedule the IR Channels ON during either the 13:47 UTC Svalbard pass or the 14:54 UTC Dongara pass (depending on MHS activities).  The day/night toggling has not been activated yet, but is scheduled for later this evening.  The instrument is currently operating in Day mode with Channel 3A selected.

- HIRS is in OFF mode (motors running and patch control ON), commanded during the 08:37 UTC Svalbard pass.  The HIRS patch has also reached its 95K set point, also within approximately 2 orbits.  Electronics are still OFF, but since the patch is now under control, we hope to schedule the Electronics ON (visible and IR channels ON) during either the 13:47 UTC Svalbard pass or the 14:54 UTC Dongara pass (depending on MHS activities).

- AMSU-A1 has been successfully commanded back to MEASUREMENT mode (Full Scan mode) during the 10:26 UTC Svalbard pass.  Everything ran nominally and the instrument is configured in its operational mode (PLLO-1 and Cold Cal Position 1 selected).  Motor currents came up as expected and are in family with previous results.

- AMSU-A2 has been successfully commanded back to MEASUREMENT mode (Full Scan mode) during the 12:07 UTC Svalbard pass.  Everything ran nominally and the instrument is configured in its operational mode (Cold Cal Position 1 selected). Motor currents came up as expected and are in family with previous results.

- SEM is still in OFF mode, but is scheduled for switch-on during the 13:47 UTC Svalbard pass.

- SARR is still in OFF mode, but is scheduled for switch-on during the 15:27 UTC Svalbard pass.  This pass allows observability over the Canadian LUT.

Figure1: TIP Swap

Figure42 TIP Swap

Figure3: TIP Swap

Figure4: TIP Swap

Figure5: MHS 90 Day Trend