Appendix D:  Initial ADS-B Surveillance Applications

ATC Surveillance. This application will use ADS-B surveillance information as a qualified surveillance source to provide ATC services throughout the NAS. ATC will use ADS-B surveillance information in the same manner as current cooperative surveillance system information is used, e.g., to assist aircraft with navigation, to separate aircraft, and to issue safety alerts and traffic advisories. ADS-B surveillance informationwill be used by ATC automation system functions, e.g., tracking and conflict alerting. Implementation areas include surface, terminal, en route, and oceanic domains.

Airport Surface Situational Awareness (ASSA). This application will reduce the potential for deviations, errors, and collisions through an increase in flight crew situational awareness while operating an aircraft on the airport movement area. Flight crews will use a cockpit display to increase awareness of other traffic on the airport movement area. Additionally, the display may be used to determine the position of ground vehicles, e.g., emergency vehicles and airport maintenance vehicles.

Final Approach Runway Occupancy Awareness (FAROA). This application will use a cockpit display to depict the runway environment and display traffic from the surface up to approximately 1,000 feet above ground level on final approach. It will be used by the flight crew to help determine runway occupancy, thereby reducing the likelihood of flight crew errors associated with runway occupancy and improving the capability of the flight crew to detect ATC errors.

Enhanced Visual Acquisition (EVAcq). This application uses a cockpit display to enhance out-of-the-window visual acquisition of air traffic. Flight crews will refer to the display during the instrument scan to supplement visual observations. The display can be used to either initially detect an aircraft or to receive further information on an aircraft that has been reported by ATC. The application will provide the flight crew with the relative range, altitude, and bearing of other aircraft.

Enhanced Visual Approach (EVApp). This application will enhance successive approaches for aircraft cleared to maintain visual separation from another aircraft on the approach. This will allow visual approach procedure operation arrival rates to be maintained, even during periods of reduced visibility or obstructions to vision (haze, fog, sunlight, etc). To achieve this, flight crews will be supported by a cockpit display of nearby traffic providing continually updated identity and position information of relevant traffic. Additional information such as range and speed will be provided to assist flight crews in monitoring their distance from the preceding aircraft. The display may also be used to monitor aircraft on approach to parallel runways.

Conflict Detection (CD). This application will provide alerting and relevant traffic information to help the flight crew identify conflicts with other aircraft based on current flight states and intentions. Aircraft equipped with a cockpit display will have the capability to display aircraft location and intent, and will alert pilots of developing conflicts. Also, the long surveillance range afforded by ADS-B will enable alerts to be issued in time to resolve conflicts with minimum disruption to the flight path. NOTE: This application is an ADS-B-enabled capability for properly equipped aircraft, and is not intended as a TCAS replacement.

This page intentionally blank

Appendix E:  Technical Team and Steering Committee Membership

Surveillance/Positioning Backup Strategy Technical Team

Member	Organization	Role

James Baird	FAA ATO-P	Team Lead

George Ligler	PMEI	Team Facilitator

Jonathan Hammer	MITRE/CAASD	Team Secretary

Shahan Stepanian	MCRI	Cost Analyst

Avani Pandya	MCRI	Cost Analyst

Jennifer Lamont	FAA ATO-E (CTR)	Safety Analyst

Mark McCoy	FAA ATO-E (CTR)	Safety Analyst

Ray McDonald	FAA ATO-E (CTR)	Radar, Multilateration SME

James Carroll	Volpe NTSC	eLoran SME

Jack Kraemer	Volpe NTSC	eLoran SME

Dan O’Laughlin	MITRE/CAASD	SATNAV SME

Robert Saffell	Rockwell-Collins	AT Avionics SME

Joel Wichgers	Rockwell-Collins	AT Avionics SME

Tom Mosher	Garmin	GA Avionics SME

Sally Frodge	FAA ATO-W	Navigation SME

David Olsen	FAA ATO-P	Navigation SME

Chris Moody	MITRE/CAASD	ADS-B SME

Gus Waters	FAA ATO-T	Air Traffic User/Eval

Paul Lipski	FAA AVS/AIR	Certification (Surv) User/Eval

Bruce DeCleene	FAA AVS/AIR	Certification (Nav) User/Eval

Bill Flathers	AOPA	GA User/Eval

George Wilson	Delta Airlines	AT User/Eval

Milton Clary	USAF/Pentagon	DoD (Nav) User/Eval

Robert Manning	USAF/Pentagon	DoD (Surv) User/Eval

William Thedford	USAF/Hanscom	DoD (Avionics) User/Eval

Wayne Buhrman	JHU APL	Independent Assessment

Other Participants

Ken Alexander	FAA AVS/AIR

Bradford Benjamin	FAA ATO-T

Jacob Dorsey	ATO-T

Leo Eldridge	FAA ATO-W

Mike Huffman	FAA ATO-T

Ken Kepchar	FAA ATO-P

Jim Linney	FAA ATO-T

John Marksteiner	FAA ATO-E

Gary Paull	MCRI

Robert Pomrink	FAA ATO-E (CTR)

Steve Ramdeen	FAA AVS/AIR

Steve VanTrees	FAA AVS/AIR

Pat Zelechoski	FAA AVS/AFS

Surveillance/Positioning Backup Strategy Steering Committee

Member	Organization

Vincent Capezzuto	FAA ATO-E

Rick Heinrich	Rockwell-Collins

Tony Broderick	Consultant

Mark Cato	ALPA

Scott Foose	RAA

Dave Hamrick	MITRE/CAASD

Randy Kenagy	AOPA

Dave Madison	FAA ATO-T

John McGraw	FAA AVS/AFS

Jay Merkle	JPDO

Dave Nakamura	Boeing

Dan Salvano	FAA ATO-W

Ken Speir	ADS-B WG, Chair

Roger Wall	FedEx

Dave Watrous	RTCA

This page intentionally blank

Appendix F:  Acronyms and Abbreviations

AC	Advisory Circular

ADS-B	Automatic Dependent Surveillance-Broadcast

ADS-R	Automatic Dependent Surveillance-Rebroadcast

AGL	Above Ground Level

ASDE	Airport Surface Detection Equipment

ASF	Additional Secondary Factor

ASR	Airport Surveillance Radar

ASSA	Airport Surface Situational Awareness

ASTERIX	All-Purpose Structured Eurocontrol Radar Information Exchange

AT	Air Transport

ATC	Air Traffic Control

ATCBI	Air Traffic Control Beacon Interrogator

ATMAC	Air Traffic Management Advisory Committee

CAIV	Cost as an Independent Variable

CD	Conflict Detection

CDTI	Cockpit Display of Traffic Information

CENRAP	Center Radar ARTS Presentation

CIP	Capital Investment Plan

CONOPS	Concept of Operations

CONUS	Continental United States

CRI	Cross rate interference

CSA	Comparative Safety Analysis

DME	Distance Measuring Equipment

DoD	Department of Defense

drms	Distance Root-Mean-Square

ECD	Envelope-to-Cycle Difference

E-field	Electric Field

eLoran	Enhanced Loran

ES	1090 MHz extended squitter

ESL	Economic Service Life

EVAcq	Enhanced Visual Acquisition

EVApp	Enhanced Visual Approach

F&E	Facilities and Engineering

FAA	Federal Aviation Administration

FAROA	Final Approach Runway Occupancy

FCC	Federal Communications Commission

FIS-B	Flight Information Service - Broadcast

FL	Flight Level

FMS 	Frequency Management System

fPR 	Final Program Requirements

ft	Foot/Feet

FY	Fiscal Year

GA 	General Aviation

GBAS	Ground-Based Augmentation System (satellite)

GLONASS	Global Navigation Satellite System (Russian)

GNSS	Global Navigation Satellite System

GPS	Global Positioning System

GRI	Group Repetition Rate

HAA	Height Above Airport

HAL	Horizontal Alert Limit

HDOP	Horizontal Dilution of Precision

HEA	Harbor Entrance Approach

H-field	Magnetic Field

HFOM	Horizontal Figure of Merit

ICAO	International Civil Aviation Organization

ID	Idnetification

IFR	Instrument Flight Rules

IRU	Inertial Reference Unit

JRC	Joint Resources Council

kHz	Kilohertz

kW	Kilowatt

LAN	Local Area Network

LDC	Loran Data Channel

LEMS	Loran Enhanced Monitoring System

LICOS	Loran Information, Control, and Operations System

Loran	Long Range Navigation

LSP	Link Specific Processing

MASPS	Minimum Aviation System Performance Standard

MHz	Megahertz

MLS	Microwave Landing System

MMR	Multi-Mode Receiver

Mode S	Mode Select

MOPS	Minimum Operational Performance Standard

MSL	Mean Sea Level

MW	Megawatt

NAC	Navigation Accuracy Category

NAS	National Airspace System

NIST	National Institute of Standards and Technology

nmi	Nautical Mile

NOTAM	Notice to Airmen

NPA	Non-Precision Approach

nsec	Nanosecond

NTIA	National Telecommunication and Information Administration

O&M	Operations and Maintenance

OEP	Operational Evolution Partnership

OMB	Office of Management and Budget

PARC	Performance-Based Aviation Rulemaking Committee

PHA	Preliminary Hazard Analysis

PSR	Primary Surveillance Radar

p-static	Precipitation Static

RAIL	Remote Automatic Integrated Loran

RAIM	Receiver Autonomous Integrity Monitor

RF	Radio Frequency

RFI	Radio Frequency Interference

RMS	Remote Monitoring Subsystem

RNAV	Area Navigation

RNP	Required Navigation Performance

RO	Receive Only

RT	Receive/Transmit

RTCA	RTCA

SATNAV	Satellite Navigation

SBAS	Satellite-Based Augmentation System

SBS	Surveillance and Broadcast Services

sec	Second(s)

SLEP	Service Life Extension Program

SNR	Signal-to-Noise Ratio

SoL	Safety of Life

SSR	Secondary Surveillance Radar

STARS	Standard Terminal Automation Replacement System

TCAS	Traffic Collision and Avoidance System

TCS	Transmitter Control Set

TD	Time Difference

TDOA	Time Difference of Arrival

TFE	Time and Frequency Equipment

TIS-B	Traffic Information Service - Broadcast

TOA	Time of Arrival

TOT	Time of Transmission

TSO	Technical Standard Order

UAT	Universal Access Transceiver

UPS	Uninterruptible Power Supply

USNO	U.S. Naval Observatory

UTC	Coordinated Universal Time

VFR	Visual Flight Rules

VOR	Very High Frequency Omnirange

WAAS	Wide Area Augmentation System

WBS	Work Breakdown Structure

WRC	World Radio Conference

Appendix G:  References

General

OMB Circular A-94, “Guidelines and Discount Rates for Benefit-Cost Analysis of Federal Programs, Office of Management and Budget (Revised),” January 18, 2006

“FAA Joint Resources Council Record of Decision,” JRC, September 9, 2005

“FAA Joint Resources Council Record of Decision,” JRC, June 7, 2006

“National Airspace System System Engineering Manual,” Version 3.0, ATO-P, September 30, 2004

NAS-SS-1000, “National Airspace System System Specification,” FAA, July 16, 1996

“Federal Aviation Administration Capital Investment Plan, 2006-2010,” FAA, February 2005

“Federal Aviation Administration Standard Work Breakdown Structure (WBS),” Version 4.1, FAA, April 2005

“Manual of Regulations and Procedures for Federal Radio Frequency Management,” NTIA, May 2006

Surveillance

“Surveillance and Broadcast Services Program Exhibit 300 Program Baseline,’ ATO-E, June 2006

“Final Program Requirements for Surveillance and Broadcast Services,” Version 1.0, ATO-E, May 9, 2006

“National Airspace System Surveillance and Broadcast Services Concept of Operations,” ATO-E, May 11, 2006

“Backup Strategy for ADS-B,” Draft, FAA/MITRE/Volpe, March 2006

DO-260A, “Minimum Operational Performance Standards for 1090 MHz Extended Squitter Automatic Dependent Surveillance-Broadcast (ADS-B) and Traffic Information Services-Broadcast (TIS-B),” Change 1, RTCA, June 27, 2006

DO-282A, “Minimum Operational Performance Standards for Universal Access Transceiver (UAT) Automatic Dependent Surveillance-Broadcast (ADS-B),” RTCA, July 29, 2004

DO-286A, “Minimum Aviation Systems Performance Standards (MASPS) for Traffic Information Services - Broadcast (TIS-B),” RTCA, April 7, 2005

DO-242A, “Minimum Aviation Systems Performance Standards for Automatic Dependent Surveillance-Broadcast (ADS-B),” RTCA, June 25, 2002

DO-289, “Minimum Aviation Systems Performance Standards for Aircraft Surveillance Applications (ASA),” RTCA, December 9, 2003

FAA-E-2942, “National Airspace System Subsystem Level Specification for Airport Surface Detection Equipment - Model X (ASDE-X),” Version 1.1, FAA, August 13, 2001

TM-2004-213447, “Deployment and Evaluation of Helicopter In-Flight Tracking System (HITS) Final Report,” NASA, December 2004

“En Route SSR Coverage,” MITRE/CAASD, November 15, 2006

NLR-CR-2004-472, “Wide Area Multilateration Report on EATMP TRS 131/04,” Version 1.1, National Airspace Laboratory for Eurocontrol, August 2005

Navigation

“Navigation and Landing Transition Strategy,” ASD-1 (now ATO-P), August 2002

DOT-VNTSC-RSPA-01-3.1, “2001 Federal Radionavigation Systems,” U.S. Department of Transportation, 2001

FAA Advisory Circular 90-100, “U.S. Terminal and En Route Area Navigation (RNAV) Operations,” FAA, January 7, 2005

FAA Advisory Circular 20-130A, “Airworthiness Approval of Navigation or Flight Management Systems Integrating Multiple Navigation Sensors,” FAA, June 14, 1995

DO-236B, “Minimum Aviation System Performance Standards: Required Navigation Performance for Area Navigation,” RTCA, October 23, 2003

“Loran’s Capability to Mitigate the Impact of a GPS Outage on GPS Position, Navigation, and Time Applications,” FAA, March 2004

“Modelling Loran-C Envelope-to-Cycle Differences in Mountainous Terrain,” P. Williams and D. Last, 32nd Annual International Loran Association Meeting, Boulder, CO, 2003

“Loran-C Accuracy Considerations: Terminal Area and En Route,” D. Diggle, Ohio U., and M. Narins, FAA, 35th Annual International Loran Association Meeting, Groton, CT, 2006

“LSU Timing Update,” LT K. Shmihluk, USCG Loran Support Unit, International Loran Association, October 2006

COMDTPUB P16562.6, “Loran-C User Handbook,” U.S. Coast Guard, 1992

“U.S. Space-Based Positioning, Navigation, and Timing Policy Fact Sheet,” National Space-Based Positioning, Navigation, and Timing (PNT) Executive Committee, December 15, 2004

“Global Positioning System Outage En Route Simulation,” ACB-330, April 2005

“GPS Backup for Positioning, Navigation and Timing, Transition Strategy for Navigation and Surveillance,” Aviation Management Associates for ATO-W, August 22, 2006

ICD-GPS-705, “NAVSTAR GPS Space Segment / User Segment L5 Interfaces,” NAVSTAR GPS Joint Program Office (DoD), December 2, 2002

“GPS Risk Assessment Study,” Johns Hopkins University Applied Physics Laboratory, January 29, 1999

“Vulnerability Assessment of the Transportation Infrastructure Relying on the Global Positioning System,” Final Report, Volpe National Transportation Systems Center, August 29, 2001

“Galileo Open Service Signal in Space (SIS) Interface Control Document (ICD),” Draft 0, Galileo Joint Undertaking (EU/ESA), 23 May 2006

“DME/DME En Route 0.6 NM (95%) Coverage at 18,000 and 24,000 feet MSL,” MITRE/CAASD, November 9, 2006

FAA Order 7470.1, “Distance Measuring Equipment (DME)/DME Infrastructure Evaluation for Area Navigation (RNAV) Routes and Procedures,” FAA, November 1, 2004

FAA Technical Standard Order TSO-C66c, “Distance Measuring Equipment (DME) Operating Within the Radio Frequency Range of 960-1215 Megahertz,” FAA, January 18, 1991

This page intentionally blank

Appendix H

Independent Assessment of the Surveillance/Positioning Backup Strategy

Alternatives Analysis for the Surveillance and Broadcast Services Program

by the

Johns Hopkins University Applied Physics Laboratory

As part of the Surveillance and Broadcast Services program, a preliminary hazard analysis was performed to identify potential risks to the ADS-B service.  One of the risks identified as a result of this analysis was the potential loss of ADS-B surveillance for multiple aircraft due to an interruption of the GPS L1 frequency.  A study was undertaken to recommend a backup strategy for mitigating the impact of a loss GPS to the ADS-B service.  As part of this study, an impartial, independent assessment was performed to provide assurance that the process used to select a particular mitigation strategy was properly executed and the resulting recommended strategy was appropriate given the conclusions reached by the technical team.

A technical team, made up of subject matter experts, representatives from key user groups and support analysts was formed to perform the study.  A steering committee formed by the RTCA Air Traffic Management Committee (ATMAC) provided direction and guidance to the technical team.  Representatives of the technical team periodically briefed the steering committee to provide status as well as receive direction and guidance.  During the course of the study, technical team members consulted additional subject matter experts as required, to ensure a complete and thorough analysis of all viable strategies that could potentially mitigate the identified risk.

The technical team followed the FAA trade study process as defined in the System Engineering Manual in a disciplined fashion to ensure an objective comparison of the potential alternatives to arrive at the most balanced technical solution(s).  The team worked cohesively as a group and was not influenced by outside interests.  All working assumptions developed by the team were vetted by the steering committee.

Evaluation criteria were developed to aid in scoring of the various strategies.  Weighting of the evaluation criteria was done by the steering committee and used in the scoring process.  Strategies were then formulated based on projected performance, availability of key technologies, current NAS evolution plans, and inputs from the Steering Committee.  The list of strategies was down-selected based on the technical team’s assessment of the viability of the strategy, resulting in a final list containing seven strategies that were coordinated with the Steering Committee for scoring purposes.

A sensitivity analysis was performed on each of the metrics to assess how the weighting of each metric impacted the overall score for each strategy.  This analysis provided confidence that small variations in the weighting factors did not significantly impact the overall ranking for the strategies.

The technical team report addresses the risk and provides a viable mitigation to the loss of the ADS-B service due to an interruption of GPS.  A review of the complete report is essential to assure the reader that a feasible mitigation strategy to the loss of GPS exists.  As with any recommendation, careful evaluation of the guidelines and assumptions is critical for full understanding of the conclusions reached.