# Optical System Design

March 5, 2004

### Requirement

Horizontal direction

=5 mm, =1 mrad, both adjustable

Vertical direction

=0.2 mm variable, <3 mrad.

### Light source

Nd:YAG, Continuum Powerlite Precision II 8030

Pulse repetition rate 30 Hz

Pulse width 6~8 ns

Pulse energy 650 mJ (fundamental, 1.06 m), 150 mJ (third harmonic, 355 nm)

Linewidth 0.003 cm-1 (90 MHz) with injection seeded.

=355 nm,

Assuming =0.1 mrad, =1.13 mm, =11.3 m.

### Design objectives

- Beam parameters (waist and divergence angle)

- Working distance from telescope to interaction region

- Pulse intensity at the window and lenses

### I. Pre-collimation with circular lens

Input beam parameters: =355 nm, =0.1 mrad, and z=100 m,

=1.13 mm, =11.3 m.

Pre-collimation lens parameters: f0=50 cm.

,

cm, =20.03 mrad,  cm,

=50.25 cm.

Beam size at the plane of zl=60 cm:

cm.

Beam size at the plane of zl=70 cm:

cm.

## II: Vertical beam design

Input beam parameters:

cm, =20.03 mrad,  cm, z=10 cm.

Target beam parameters:

=355 nm, =0.2 mm,  mrad, (we assume  mrad)

cm, =5.02 cm.

## Telescope design

(1) f1=-50 cm (concave cylindrical lens).

,

cm, =24.05 mrad,  cm,

cm.

(2) f2=12.5 cm (convex cylindrical lens), d=5 cm, z2=d-z1=13.367 cm.

,

cm, =1.67 mrad, = 4.06 cm,

=192.63 cm.

(3) To achieve beam size 2=0.4 mm, the distance from the telescope to the interaction region will be:

=181.35 cm.

Distance from the first cylindrical lens =186.35 cm.

Distance from the pre-stage lens  cm.

## III: Horizontal beam design

Input beam parameters:

cm, =20.03 mrad,  cm, z=20 cm.

Target beam parameters:

=355 nm, =5 mm, =1 mrad,

=0.0113 cm, =11.3 cm.

## Telescope design

(1) f1=-50 cm (concave cylindrical lens).

,

cm, =28.05 mrad,  cm,

cm.

(2) f2=22.5 cm (convex cylindrical lens), d=9 cm, z2=d-z1=23.3 cm.

,

=0.011 cm, =1.0 mrad, = 11.3 cm,

=655.1 cm.

(3) At cm,

cm.

Distance from the first cylindrical lens =176.35 cm.

IV: Optical pulse intensities at intersection planes

Assume (i) the telescopes are outside of the vacuum and (ii) the distance of the vacuum window to the light-particle interaction region is 50 cm.

(1) Pre-collimation Lens

Beam radius at the lens plane: wL0=1 cm,

Optical pulse intensity at the lens: .

(2) Vertical Telescope

Beam size at the first cylindrical lens:

,

Optical pulse intensity at the first cylindrical lens:

.

Beam size at the second cylindrical lens:

,

.

Optical pulse intensity at the first cylindrical lens:

.

(3) Horizontal Telescope

Beam size at the first cylindrical lens:

,

,

Optical pulse intensity at the first cylindrical lens:

.

Beam size at the second cylindrical lens:

,

.

Optical pulse intensity at the first cylindrical lens:

.

(4) Vacuum Window

Beam size at the vacuum window:

,

.

Optical pulse intensity at the vacuum window:

.