November 21, 1997

December 19, 1995

Contract # TW-0928AQ-1486A

SPECIALTANDARD SPECIFICATION

SECTION 09250-S

GYPSUM DRYWALL

Page

PART 1 - GENERAL

1.01 	Description Of Work

1.02 	Submittals

1.03 	Quality Assurance	33

1.04 	Delivery, Storage And Handling

1.05 	Project Conditions

PART 2 - PRODUCTS

2.01 	Manufacturers

2.02 	Steel Framing Components For Suspended And Furred Ceilings

2.03 	Steel Framing For Walls And Partitions

2.04 	Gypsum Board

2.05 	Trim Accessories

2.06 	Gypsum Board Joint Treatment Materials

2.07 	Miscellaneous Materials

PART 3 - EXECUTION

3.01 	General, Installation Of Steel Framing

3.02 	Installation Of Steel Framing For Suspended And Furred Ceilings

3.03 	Installation Of Steel Framing For Walls And Partitions

3.04 	Application And Finishing Of Gypsum Board

3.05 	Methods Of Gypsum Drywall Application

3.06 	Installation Of Drywall Trim Accessories

3.07 	Installation Of Miscellaneous Materials

3.08 	Finishing Of Drywall

3.09 	Surface Preparation And Primer

3.10 	Cleaning And Protection

3.11 	Flat Strapping Schedule	14

SPECIALTANDARD SPECIFICATION

SECTION 09250-S

GYPSUM DRYWALL

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	Extent of each type of gypsum drywall construction required is indicated on Contract documents.  This section includes the following types of gypsum board construction:

1.	Light-gauge, non-load bearing steel framing members.

2.	Gypsum board screw-attached to steel framing and furring members.

3.	Horizontal and vertical shaft wall systems.

B.	Related Sections:  Sound attenuation blankets are specified in Division 7, Section "Building Insulation.”

1.02	SUBMITTALS

A.	General:  Submit the following in accordance with provisions of conditions of Contract and Division 1, SSection  1300-S, “Descriptive Submittals.”

B.	Product Data:  Submit product information from manufacturers for each type of product specified.

C.	Corner Guards:  Submit floor plans showing proposed locations of corner guards.

Gypsum Drywall Bracing Plan:  Submit a plan showing proposed horizontal partition bracing for all floors and all walls terminating below elevated slabs.  Show member size, gauge and spacing in addition to location on floor plan.

Flat Strapping Coordination Plan:  Submit a plan showing proposed locations of flat strapping in walls.  Color code ¼” scale architectural floor plans to show laboratory walls and office walls that receive flat strapping, and mounting heights.

1.03	QUALITY ASSURANCE

A.	Fire-Resistance Rating:  Where gypsum drywall systems with fire-resistance ratings are indicated, provide materials and installations identical with applicable assemblies which have been tested and listed by UL.

B.	Manufacturer:  Obtain gypsum board products from a single manufacturer or from manufacturers recommended by the prime manufacturer of gypsum boards.

Manufacturers offering products which may be incorporated in the work are those who have been in business successfully for at least 5 years without record of product failure.

1.04	DELIVERY, STORAGE AND HANDLING

Deliver and store materials in manufacturer's original unopened packages, clearly marked with identifying information.  Protect materials as recommended by the manufacturer.

1.05	PROJECT CONDITIONS

A.	Environmental Conditions:  Establish and maintain environmental conditions for application and finishing of gypsum board to comply with ASTM C 840 and with gypsum board manufacturer's recommendations.

B.	Minimum Room Temperatures:  For attachment of gypsum board to framing, maintain not less than 40 degrees F.  For finishing of gypsum board, maintain not less than 50 degrees F for 48 hours prior to application, and continuously thereafter until drying is complete.

C.	Ventilation:  Ventilate building spaces to remove water not required for drying joint treatment materials.  Avoid drafts during dry, hot weather to prevent materials from drying too rapidly.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	Manufacturers:  Products made by the following manufacturers, provided they comply with requirements of Contract documents, arewill be among those considered acceptable.  However, it is the Contractor’s responsibility to provide only products compatible with adjacent materials in the assembly.

1.	Steel Framing and Furring:

Dale Industries, Inc.

Dietrich Industries, Inc.

National Gypsum Co.; Gold Bond Building Products Division

Unimast, Inc.

United States Gypsum Co.

2.	Grid Suspension System:

Armstrong World Industries, Inc.

Chicago Metallic Corp.

United States Gypsum Co.

Worthington Steel Company (formerly National Rolling Mills Co.)

3.	Gypsum Boards and Related Products:

Georgia Pacific Corp.

National Gypsum Co.; Gold Bond Building Products Division

United States Gypsum Co.

B.	Substitutions: only under provisions of Section 1600-S.

2.02	STEEL FRAMING COMPONENTS FOR SUSPENDED AND FURRED CEILINGS

A.	General:  Provide components which comply with ASTM C 754 for materials and sizes, unless otherwise indicated.

B.	Main Runners:  Hot or cold-rolled steel channels with rust inhibitive paint finish.

C.	Wire Ties:  ASTM A641, Class 1 zinc coating, soft temper, 0.062 inch (16 gage).

D.	Wire Hangers:  ASTM A641, Class 1 zinc coating, soft temper, 0.162 inch (8 gage).

E.	Hanger Anchorage Devices:  Screws, clips, bolts, cast-in-place concrete inserts or other devices applicable to the indicated method of structural anchorage for ceiling hangers.  Size devices for 3 times the calculated load supported, except size direct pull-out concrete inserts for 5 times the calculated loads.

CF.	Steel Rigid Furring Channels:  ASTM C 645, hat-shaped, depth of 7/8 inch; minimum 25 gauge thickness, unless otherwise indicated.

G.	Grid Suspension System:  ASTM C 645, manufacturer's standard grid suspension system composed of main beams and cross furring members which interlock to form a modular supporting network.

2.03	STEEL FRAMING FOR WALLS AND PARTITIONS

A.	Steel Studs and Runners:  ASTM C 645, galvanized, 25 gauge thickness unless otherwise indicated.  20 gauge at door jambs and for support of restroom fixtures.

1.	Depth of Section:  3-5/8 inch unless otherwise shown on drawings.  See wall types sheet 105634/A1.

2.	Runners:  Match studs; type recommended by stud manufacturer for floor and ceiling support of studs, and for vertical abutment of drywall work at other work.

3.	Flat Strap Bracing:  Provide 14 gauge x 6” wide flat strap bracing at heights of 4 feet, 5 feet and 7 feet above finished floor.  See wall types sheet 105634/A1 for walls to receive strap bracing.  identified in  Article 3.11 Flat Strapping Schedule.

B.	Steel Rigid Furring Channels:  ASTM C 645, hat-shaped, galvanized; minimum depth of 7/8 inch and minimum 25 gauge thickness, unless otherwise indicated.

C.	Steel C-H Studs (Shaft Wall Assemblies):  C-H shape, galvanized, depth of 2-1/2 inches and 4 inches as required, minimum 20 gauge, unless otherwise indicated.Z-Furring Members:  Manufacturer's standard zee-shaped furring members fabricated from hot-dip galvanized steel sheet complying with ASTM A 525, Coating Designation G60; minimum 25 gauge thickness, face flange of 1-1/4 inch, wall-attachment flange of 7/8 inch, and of depth required to fit insulation thickness indicated.

D.	Fasteners:  Type and size recommended by gypsum drywall manufacturer for the substrate and application indicated.

2.04	GYPSUM BOARD

A.	General:  Provide gypsum board of type, edge configuration, and thickness indicated, in maximum lengths available to minimize end-to-end butt joints.

B.	Gypsum Board:  ASTM C 36, and unless otherwise indicated:

1.	Type:  Regular.

2.	Edges:  Tapered.

3.	Thickness:  1/2 inch at ceilings.

4.	Thickness:  5/8 inch at walls.

C.	Fire-Resistive Board:  ASTM C 36, and unless otherwise indicated:

1.	Type:  Type ‘X.’

2.	Edges:  Tapered.

3.	Thickness:  5/8 inch at ceilings and walls.

D.	Gypsum Backing Board:  ASTM C 36 where indicated on Contract documents as base layer for multilayer application.  Unless otherwise indicated:

1.	Type:  Regular or Type ‘X’ for fire-resistance-rated assemblies.

2.	Edge:  Tapered.

3.	Thickness:  1/2 inch non-fire rated or 5/8 inch at fire rated applications.

E.	Water-Resistant Backing Board:  ASTM C 630, and use where indicated on drawings.  Unless otherwise indicated:

1.	Type:  Regular or Type "X" for fire-resistance-rated assemblies.

2.	Edge:  Tapered.

3.	Thickness:  5/8 inch.

F.	Gypsum Sheathing Board:  ASTM C 79, and unless otherwise indicated:

1.	Type:  Regular or Type ‘X.’

2.	Edges:  Square.

3.	Thickness:  1/2 inch at regular, 5/8 inch at fire rated applications.

2.05	TRIM ACCESSORIES

A.	Cornerbead and Edge Trim:  Provide cornerbeads, edge trim, and control joints which comply with ASTM C 1047 and requirements indicated below:

1.	Material:  Unless otherwise indicated, galvanized steel with either knurled and perforated or expanded flanges, and beaded for concealment of flanges in joint compound.

2.	Edge trim shapes indicated below by reference to designations of Figure 1 in ASTM C 1047:

a.	"L" Bead

b.	"U" Bead

c.	"LK" Bead

B.	Control Joint:  Provide one piece control joint formed with vee-shaped slot per Figure 1 in ASTM C 1047, with slot opening covered with removable strip.

2.06	GYPSUM BOARD JOINT TREATMENT MATERIALS

A.	General:  Provide materials complying with ASTM C 475, ASTM C 840 and type recommended by the manufacturer for the application indicated, except as otherwise indicated.

B.	Joint Tape:  Paper reinforcing.

C.	Ready-Mixed Taping Joint Compound:  Pre-mixed, non-asbestos, vinyl based compound formulated for tape application, fastener spotting, first fill coat on metal beads and trim and filling.

D.	Ready-Mixed Topping Joint Compound:  Pre-mixed, non-asbestos, vinyl based compound for second and third coats over taped joints, fastener spottings and the finish coat over metal beads and trim .

E.	Drywall Primer:  A flat latex based prime coat to equalize the texture and porosity differences between joint compound and drywall.

2.07	MISCELLANEOUS MATERIALS

A.	General:  Provide auxiliary materials for gypsum drywall construction which comply with referenced standards and the recommendations of the gypsum board manufacturer.

B.	Gypsum Board Screws:  ASTM C 1002.

C.	Acoustical Sealant:  Water base, non-drying, non-bleeding, non-staining type and permanently elastic.  Comply with requirements specified in Division 7, Section "Joint Sealants", and as recommended by the gypsum board manufacturer for application indicated.

D.	Powder Texturing Product:  Non-asbestos powder product, mixed with water for producing a satisfactory “spatter” spray texture.  Provide other textures as indicated in Contract documents.

E.	Corner Guards:  Provide surface-mounted corner guards on all corridor walls and other high impact areas as indicated on drawings.  Where corner guards are required on fire-resistive walls, provide surface or flush-mounted type that are UL listed.

1.	Corner guards shall consist of a continuous extruded aluminum retainer, top and bottom high impact nylon closer caps, and a vinyl/acrylic guard.

2.	Guard length shall be a minimum of 4'-0".

3.	Wall thickness of .110 inch and angle-shaped with 3 inch legs and 1/4 inch radius at corners and ends.

4.	Furnish guard in matte finish from manufacturer's standard color line.  Closure caps shall be of the same color as the guards.  Color to be selected from color selection charts provided by the manufacturer.

F.	Chair Rails:  Provide surface-mounted pre-finished vinyl/acrylic (unless material noted otherwise on drawings) chair rails on all conference room walls and as indicated on drawings.

1.	Chair rails shall consist of a continuous extruded aluminum retainer, end and corner transitions, and a vinyl/acrylic rail.

2.	Provide rails with a minimum overall height of 3-1/2 inches and overall depth of 7/8 inch.

3.	Color:  As chosen from manufacturer’s standard color charts at time of submittals.

PART 3 - EXECUTION

3.01	GENERAL, INSTALLATION OF STEEL FRAMING

A.	Steel Framing Installation Standard:  Install steel framing to comply with ASTM C 754 and with ASTM C 840 requirements that apply to framing installation.

B.	Install supplementary framing, blocking and bracing at terminations in the construction and for support of fixtures, equipment services, heavy trim, grab bars, toilet accessories, furnishings, and similar construction to comply with details indicated and with recommendations of gypsum board manufacturer.

C.	Isolate steel framing from building structure where edges of suspended ceilings abut building structure horizontally at ceiling perimeters, at penetration of structural elements, and where partition and wall framing abuts overhead structure.

D.	Do not bridge building expansion and control joints with steel framing or furring members.

3.02	INSTALLATION OF STEEL FRAMING FOR SUSPENDED AND FURRED CEILINGS

A.	Secure hangers to structural support by connecting directly to structure where possible, otherwise connect to inserts, clips or other anchorage devices or fasteners as indicated on drawings.

B.	Space main runners 4'-0" and hangers 4'-0" o.c. along runners, unless otherwise indicated.

C.	Installation Tolerances:  Install steel framing components for suspended ceilings so that cross furring members or grid suspension members are level to within 1/8 inch in 12'-0", measured lengthwise on each member and transversely between parallel members.

D.	Grid Suspension System:  Attach perimeter wall track or angle where grid suspension system meets vertical surfaces.  Mechanically join main beam and cross furring members to each other and butt-cut to fit into wall track.

E.	Attach perimeter wall track or  angle wherever support system meets vertical surfaces.

3.03	INSTALLATION OF STEEL FRAMING FOR WALLS AND PARTITIONS

A.	Install runners (tracks) at floors, ceilings and structural walls, and columns where gypsum drywall stud system abuts other work.

B.	Installation Tolerances:  Install each steel framing and furring member so that the fastening surface do not vary more than 1/8 inch from plane of faces of adjacent framing.

C.	Extend partition framing full height to structural supports or substrates above suspended ceilings,. except wWhere interior lab partitions are indicated to terminate at suspended ceilings below elevated slabs provide horizontal bracing to walls which terminate at elevated slabs.  Continue framing for doors and openings, and frame around ducts penetrating partitions above ceiling to provide support for gypsum board.

Size bracing to resist a lateral load of 5 psf acting normal to the partition wall.

D.	Space studs and wall furring at 16 inches o.c., except as otherwise indicated.  Attach studs to top and bottom tracks by button punch or screws, except that studs located adjacent to doors, windows, partition intersections or ends, and at corners shall be screwed to tracks.

E.	Frame door openings with vertical studs securely attached by screws at each jamb either directly to frames or to jamb anchor clips on door frame; install runner track sections (for jack studs) at head and secure to jamb studs.

F.	Frame openings other than door openings in same manner as required for door openings, and install framing below sills of openings to match framing required above door heads.

3.04	APPLICATION AND FINISHING OF GYPSUM BOARD

A.	Gypsum Board Application and Finishing Standard:  Install and finish gypsum board to comply with ASTM C 840.

B.	Install ceiling boards in the direction and manner which will minimize the number of end-butt joints, and which will avoid end joints in the central area of each ceiling.  Stagger end joints at least 12 inches.

C.	Install wall/partition boards vertically to avoid end-butt joints wherever possible.

D.	Install exposed gypsum board with face side out.  Do not install imperfect, damaged or damp boards.  Butt boards together for a light contact at edges and ends with not more than 1/16 inch open space between boards.  Do not force into place.

E.	Locate either edge or end joints over supports.  Position boards so that like edges abut, tapered edges against tapered edges and mill-cut or field-cut ends against mill-cut or field-cut ends.  Stagger vertical joints over different studs on opposite sides of partitions.

F.	Attach gypsum board to framing and blocking as required for additional support at openings and cutouts.

G.	Form control joints and expansion joints with space between edges of boards, prepared to receive trim accessories.

H.	Isolate perimeter of non-load bearing drywall partitions at structural abutments.  Provide 1/4 to 1/2 inch wide spaces and trim edges with “U”-bead trim where edges of drywall panels are exposed.  Seal joints between edges and abutting structural surfaces with acoustical sealant.  Do not fasten drywall directly to stud system runner tracks.

I.	Where sound attenuation drywall construction is indicated, seal the work at perimeters, control and expansion joints, openings, and penetrations with a continuous bead of acoustical sealant including a bead at both faces of partitions.  Comply with manufacturer's recommendations for location of beads and close off sound-flanking paths around or through the work.

J.	Space fasteners in each layer of gypsum board in accordance with manufacturer's recommendations, Uniform Building Code, and published U.L. or other published assemblies.

3.05	METHODS OF GYPSUM DRYWALL APPLICATION

A.	Single-Layer Application:  Install gypsum wallboard as follows:

1.	On ceilings, apply gypsum board prior to wall/partition board application to the greatest extent possible.

2.	On partitions/walls, apply gypsum board vertically (parallel to framing), unless otherwise indicated and provide sheet lengths which will minimize end joints.

3.	On Z-furring members, apply gypsum board vertically (parallel to framing) with no end joints.  Locate edge joints over furring members.

B.	Wall Tile Base:  Where drywall is base for thin-set ceramic tile and similar rigid applied wall finishes, install gypsum backing board.

At showers, tubs and similar "wet" areas, install water-resistant backing board.  Apply with un-cut long edge at bottom of work, and space 1/4 inch above fixture lips.  Seal ends, cut-edges, and penetrations of each piece with water-resistant compound before installation.

C.	Acoustical Tile Base:  Where drywall is base for adhesively-applied acoustical tile, install gypsum backing board.

Provide either V-joint type backing board, or tape and finish joints (2 coats unsanded).

DC.	Double-Layer Application:  Install gypsum backing board for base layer and gypsum board for face layer.

1.	On ceilings, apply base layer prior to application of base layer on walls/partitions; apply face layers in same sequence.  Offset joints between layers at least 10 inches.

2.	On partitions/walls apply base layer and face layers vertically (parallel to framing) with joints of base layer over supports, and with face layer joints offset at least 10 inches with base layer joints.

3.	On Z-furring members apply base layer vertically (parallel to framing), and face layer either vertically (parallel to framing) or horizontally (perpendicular to framing) with vertical joints offset at least one furring member.  Locate edge joints of base layer over furring members.

ED.	Single-Layer Fastening Methods:  Apply gypsum boards to supports with screws.

FE.	Double-Layer Fastening Methods:  Apply base layer of gypsum board and face layer to base layer by fastening both base layers and face layers separately to supports with screws.

3.06	INSTALLATION OF DRYWALL TRIM ACCESSORIES

A.	General:  Where feasible, use the same fasteners to anchor trim accessory flanges as required to fasten gypsum board to the supports.

B.	Install metal corner beads at external corners of drywall work.

C.	Install metal edge trim whenever edge of gypsum board would otherwise be exposed or semi-exposed.  Provide type with face flange to receive joint compound except where "U" bead (semi-finishing) type is indicated.

1.	Install "L" bead where work is tightly abutted to other construction.

2.	Install special "LK" bead where other work is kerfed to receive long leg of "L" bead trim.

3.	Install "U" bead where edge is exposed, revealed, gasketed, or sealant-filled (including expansion joints).

D.	Install "U" bead trim where indicated, and where exterior gypsum board edges are not covered by applied moldings.

E.	Install control joints at locations indicated, or if not indicated, at spacings and locations required by referenced gypsum board application and finish standard.

3.07	INSTALLATION OF MISCELLANEOUS MATERIALS

A.	Install each item in accordance with the manufacturer's directions and recommendations.  Use anchors and other fasteners supplied by the manufacturer which match the finish of the items.  Install all items plumb or level.

B.	Mount chair rails at 2'-6 1/2" above finished floor level.

3.08	FINISHING OF DRYWALL

A.	General:  Apply treatment at gypsum board joints (both directions), flanges of trim accessories, penetrations, fastener heads, surface defects, and elsewhere as required to prepare work for decoration.

1.	Prefill any open joints and rounded or beveled edges using type of compound recommended by the manufacturer.

2.	Apply joint tape over gypsum board joints, except those with trim accessories having flanges not requiring tape.  Do not apply joint tape to the base layer in a double layer application, except as required to meet specified fire-resistive assemblies, U.B.C., and elsewhere as noted on Contract documents.

3.	Finish interior gypsum board by applying joint compound in three coats (not including prefill of openings in base), and sand between coats and after last coat.

4.	Apply drywall primer to joints as recommended by primer manufacturer.

B.	Base for Acoustical Tile:  Where gypsum board is indicated as a base for adhesively-applied acoustical tile, install tape and 2-coat compound treatment, without sanding.

CB.	Water-Resistant Gypsum Board Base for Ceramic Tile:  Treat joints and fasteners to comply with directions of water-resistant joint compound manufacturer.

1.	In areas to be tiled, treat fastener heads with water-resistant joint compound.

a.	Fill tapered edges in gypsum panels with water-resistant joint compound, embed joint tape firmly, and wipe off excess compound.

b.	Follow immediately with a second coat of water-resistant joint compound over taping coat, being careful not to crown the joint.

c.	Fold and embed tape in all interior angles to form true angle.

2.	In areas not to be tiled, treat fastener heads and embed tape as indicated above, using water-resistant joint compound.  Finish with two coats of joint compound used for regular gypsum board work.

DC.	Fire-rated Gypsum Board:  Tape and bed all joints including all layers of multiple layer applications.

ED.	Surface Texturing:  All gypsum board surfaces exposed in finish areas shall be textured.  Finish areas are those specified to be painted and as scheduled on inthe drawings.  Room Finish Schedule Section 09000.

1.	Texture shall be a "spatter orange peel" spray application unless otherwise approved.

2.	Spray shall be applied to produce a uniform texture without starved spots or other evidence of thin application.

3.09	SURFACE PREPARATION AND PRIMER

Prepare and apply drywall primer to gypsum board and other surfaces prior to receiving texture finishes according to texture finish manufacturer’s instructions.  Apply primer only to surfaces that are clean, dry and smooth.

3.10	CLEANING AND PROTECTION

A.	Promptly remove any residual joint compound from adjacent surfaces not indicated to receive texture.

B.	Provide final protection and maintain conditions, in a manner acceptable to Installer, that ensure gypsum board assemblies are without damage or deterioration at the time of Substantial Completion.

Flat Strapping Schedule

Laboratory Walls:   Mount flat strapping on all four walls within laboratories and CFZ’s at the following heights:  15 inches, 57 inches and 81 inches above finished floor.

Office Walls:  Mount flat strapping on all four walls within offices and conference rooms at the following heights:  6 inches, 32 inches and 65 inches above finished floor

See wall type Sheet 105634/A1 for walls to receive strap bracing.

END OF SECTION