POLAR Spacecraft Status As of: Weds 19 Jan 05  16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1648=AN STIP data only | NOAA-14J AM: 2019=AN STIP data only | NOAA-15K AM: 1817=AN GAC data only | NOAA-16L PM: 1430=AN GAC&LAC data | NOAA-17M AM: 2224=AN GAC&LAC data | NOAA-N18 Planned PM Plan AN=14:00 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | NET 19Mar05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | Dress Rehearse #1 Completed 13Jan |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 | Dress Rehearse #2 10 Feb 05 |
| BUS VETO | NO | NO | NO | NO | NO |  |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | New ring laser gyro |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mS |  |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |  |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled |  |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 1 Analog telem drifting Swap considered | 1 Analog telem drifting |  |
| DTRs | 3A, 4, 5B Safestate 5B As of 8 Dec 04 | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B STIP only | 1,2,3,4 Safestate=1B DTR2-SSR | All solid state digital recorders |
| VTX (APT data) | #1 ON 137.50 MHZ Conflict with 15 | OFF Since 8/14/02 | OFF through 2/1/05 conflict with N12 | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #1=137.1 MHZ #2=137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |  |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP |  |
| POWER (Array offset, charge and eclipse states, sun angle) | ArrayOff +50 since 8/31/04 Full Sun Battery UVtrip 7/25 Sun Angle 21 steady trend Batts 1&2=LRC V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun Angle at 34 down trend to 32 Batts 1-3= LRC Batts 1&3V/T=8/11 Batt2 VT=9/11 VT and PSS changes planned Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 11 downtrend to 0 degs in lat Feb Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 54 Uptrend to 55 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 63 Down trend to 62 Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs |  |
| AVHRR | Nominal | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Nominal TCE24 OFF 4/14 Chan 3B only. | Nominal 3A-B switch enabled Scan Motor less stable than desired | New brushless scan motors |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop Significant noise present on chans 9-14 since 15 Jan 05 ATOVS products impacted | OFF/INOP Since 10/30/03 Survival heat on. |  |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal |  |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 Recent instabilities IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | VARIABLE FW mode=Hi Powr FW Heater OFF Frequent Filter Motor current “mini” surges Occasional major FM current surges, most recent 12/9/04 | DEGRADED Long wave channel degradation since 15 Dec 04 Occasional major FM surges, most recent 12/9/04 TOAR 441 submitted 11 Jan04 HIRS filter heater turned OFF 1/18/04 Plan switch to HIGH power 1/25/05 | NOMINAL 1 Pixel cross track misalignment . | HIRS-4 replacing HIRS-3 |
| MHS/MIU |  |  |  |  |  | Replaces AMSUB |
| MSU | ON / INOP Turned on 8/30/04 For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal |  |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode |  |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal |  |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |  |
| SBUV |  | Degraded Grating motor sticks Flex memory 3 (giant step) ops suspended indefinitely on 12/2/03 Reduced operations started 6/5/03 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode |  |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Autonomous implementation 10/14 | ON ENABLED |  |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat OFF TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 S/C in strong cooling trend | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 @19:10Z | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 |  |
|  | N12 | N14 | N15 | N16 | N17 | NOAA-N18 |

COMMENTS/CHANGES:

NOAA-12	There were no changes on N12 during the past reporting period.

NOAA-14:	The N14 power situation remained stable last week as the percentage of time that N14 spends in darkness each orbit trended slowly downward (illustration 1).  Plans are in place to change VT levels on all three batteries (Battery-1 from 8/11 to 7/11, Battery-2 from 9/11 to 8/11 and Battery-3 from 8/11 to 7/11) as well as reduce the power survival safestate trigger to 19.0 (from 19.4) volts with an implementation date expected to be sometime next week.  Carl Gliniak and Jon Woodward are POC’s.

NOAA-15: 	The N15 AMSU-B was generally stable last week as was the AVHRR including the scan motor currents and

temperatures (illustration 2) and synch delta values.  The HIRS was generally erratic with numerous “mini” filter motor current surges that stayed within typical ranges (illustration 3).  There were no reports of image degradation from any of these payloads during the past reporting period.

The VTX transmitters N15 is off (no APT data) and will remain so until 1 Feb 05 when its RF conflict with N12 ends.

The command clock offset on N15 is approaching 75 mSecs.  Therefore at the next opportunity, EMOSS will be adjusting this clock by 100 mSecs in order to keep this error within 1 AVHRR pixel.  Jim Sheprd is EMOSS POC and the date of implementation is still TBD.

NOAA-16	The N16 HIRS long wave channel degradation situation continued throughout the past reporting period.  During this

time, the HIRS filter heater remained on, per the Anomaly Teams recommendation.  The team reconvened on 18 Jan to discuss the HIRS responses to the heater turnon from 10 Jan.  Analysis focused on any observed improvement (tightening of the high vs. low range) in the period monitor while the heater was on.  This did not occur.  All engineering values, the period monitor and channel noise levels remained basically unchanged since the previous meeting (and previous weekly report) on 12 Jan.  In response the team determined that turning off the heater, letting the thermal situation stabilize for several days, then reconfiguring HIRS to high power mode (as N15 now operates) would be the next course of action.  Therefore, the heater was commanded off the same day (18 Jan) at 19:10Z (illustrations 4-7).  Current plans are to have the team reconvene at 10:30 eastern time on 25 Jan to finalize a GO/NO GO decision on HIRS high power mode.  As of this writing the consensus is that high power mode should be implemented.   If this consensus remains in place following the 25 Jan meeting, the operation will be performed that same day and the team will reconvene on 26 Jan at 13:30 to assess the HIRS response to this reconfiguration and determine any additional workarounds for this situation.  For those who would like to participate in the HIRS Anomaly Response team telecom, the number is,  Outside NOAA, 301-817-4220,   Inside NOAA dial 2000  Wait for a dial tone, followed by 2 short beeps,  Enter 1016*,  then  Enter 1234#  and you should be into the conference.

Early on 18 Jan 05, EMOSS engineers received a report from AMSU-A1 users that channels 9-14 were exhibiting a significant degradation because of increased noise, especially on Channel 9 (illustration 8).   By the end of 18 Jan, the noise had become so significant that the Met office had taken Chs. 10-11 out of operations out since their 6am run on 17 Jan adding to an already blacklisted Ch. 9.  Furthermore, also by the end of 18 Jan, Awdhesh K. Sharma had informed the user community “that NOAA/NESDIS ATOVS sounding products distribution has been ceased due to AMSU-A channels 9-14 increased noise and HIRS instrument noise. This has caused major impacts on the retrieved 850 mb and 500 mb temperature retrievals. We were generating the degraded quality products in the absence of HIRS data but now without AMSU-A channels 9-14 the sounding products do not qualify as operational quality products so the distribution of these products are terminated effective immediately. We will return to normal operation when the products will become useable.”  The problem was first noticed on 15 Jan and, while EMOSS engineering analysis has shown no change in the payloads operational profile that would explain this problem (illustration 9 & 10) there might be a correlation with the space environment because since 15 Jan (when the problem was first noticed) there has been significant solar activity.  As of this writing, there are no plans to workaround this problem except for continued monitoring of the payload and space environment in order to determine a possible correlation.  N16 AMSU-A1 is already categorized as YELLOW in status because of other problems with this payload.  See illustrations 11 & 12 for imagery depiction and analysis from the user’s perspective.

The N16 AVHRR was generally nominal during the past reporting period (illustration 13) although the scan motor current was slightly less stable and slightly more elevated than it has been in recent weeks.  However, imagery analysis shows no indication that this small change in operating profile has in any way impacted imagery and synch delta remains very favorable (illustration 14).   TCE24 remains off and rephase enable operations continue once per orbit over the South Pole with no actual MIRP rephasing occurring (and hence no frame losses) in the past 7 weeks.

The N16 TIP continues to show analog telemetry drift (as has been discussed in this report numerous times).  EMOSS engineers are starting to assess the necessity of swapping TIP sides on N16 (as it was done for N15 in April of 2003) sometime during the next several months (in conjunction with factory personnel being on site for N18 sims and operations).  No determination or implementation date has yet been made.  Jon Woodward and Will Chadwick are POC’s.

NOAA-17:	The N17 AVHRR was generally stable although the scan motor current continues to show slightly less stability than

desired (albeit nothing out of the range it has exhibited for the past several months; see illustration 15).  Conversely, the synch delta on N17 remains nominal (illustration 16) and there have been no reports of or imagery degradation reported to EMOSS nor has any been observed by EMOSS engineers.   EMOSS is continuing to monitor this payload very closely.  Sally House is POC.

For the first time on this mission, CPU-1 had a single event upset scrubbed in the “unknown” memory location (see CPU Errors graphic).  CPU-2 has had a number of such errors in the past and a TOAR had been outstanding on N17 for that situation.  No TOAR will be written on this situation as it is understood and no operational corrections are necessary.

NOAA-N:	EMOSS personnel supported the 13 Jan Dress Rehearsal.  All EMOSS launch team personnel participated.

EMOSS engineer Jim Sheperd placed an ephemeris load file on the Goddard computer IP# 128.183.208.98 for the Mar. 19, 2005 launch date.  It was placed in the Launch_Eph folder, with a file name of N18_078.EPH. The checksum is 4A0D. Load files for alternative launch dates have not yet been generated but should be by next week.

One interesting aspect of launch date for N18 is that the spacecraft separation will occur (for the first time) after the first ascending node.  Therefore, there may be a discrepancy in rev number count between the USAF and NOAA.  NASA launch managers are looking into this issue.

For a detailed calendar of events leading up to the 19  Mar launch go to the following web address:   https://www.qssmeds.com/~ddipaula/noaa-n_cal.htm.

Illustration 1:  N14 EPS Analysis

(Little difference from previous reports)

Illustration 2:  N15 AMSU-B and AVHRR Analysis

(Generally nominal, with better stability in AMSU-B than previous report)

Illustration 3:  N15 HIRS Health Analysis

(Nothing new here)

1=AVHRR Anomaly Starts,

2=TCE24 (AVHRR heater & louver) turned off

3=TCE24 turned on,

4=TCE24 turned off & first indications of degraded HIRS quality

5=Significant & sustained decrease in HIRS quality,

6=HIRS Heater turned on

7=HIRS Heater Turned OFF

Illustration 4:  N16 HIRS Situation Analysis

(Trend Data vs. incidents since before any problem existed)

Illustration 5:  N16 HIRS Health Analysis

(Heater turnoff appears to have adversely affected filter motor current)

Illustration 6:  N16 HIRS Health Analysis (cont)

(Heater turnon or turnoff appears to have not affected period monitor minimally if at all)

HIRS Imagery (All Channels) With Heater ON (18 Jan 11:50Z)

HIRS Imagery (All Channels) After Heater Turnoff (19 Jan 17:20Z)

Illustration 7:  N16 HIRS Imagery Analysis (PIDES), Heater ON vs. OFF

(Not much difference from this point of view)

ILLUSTRATION 8:  AMSU-A1 Imagery Analysis

(Note the degradation between the two images)

Illustration 9:  N16 AMSU-A1 Health Analysis

(No change in operational profile leading up to or following the first reported degradation on 15 Jan)

Illustration 10:  N16 AMSU-A1 Health Analysis (cont)

(Also no change in operational profile leading up to or following

the first reported degradation on 15 Jan)

User interpretation: The above image of the NOAA-16 AMSU-A1 ch # 9 and 10 along with the ATOVS retrieved temperature fields at 850 and 500 hPA.  As these images depict, this instrument is generating bad data (see arrows in lower left image) which is within the expected normal limits of performance.  Consideration is being given to leaving the operational NOAA-16 ATOVS A2 system running despite the fact that data collected for weekly coefficient updating will also be suspect and care should be exercised to exclude the affected time periods.

ILLUSTRATION 11:  AMSU-A1 Imagery Analysis (User Perspective)

User perspective: The above image shows the N16 AMSU-A ch # 9 together with the Superadiabatic Flag; the Superadiabatic Level and the Cloud Mask (currently in NOHIRS mode because of engineering testing). This image shows that at least for now, that if we do keep the N16 A2 system running operationally that all of the affected soundings will be flagged with the Superadiabatic Flags.  This instance together with the "bad backup oscillator" incident in Nov. '03 represents  the second documented case in which  AMSU-A has gone bad within the range of the expected normal measurements and the ATOVS system has generated bad products but managed to flag all of the

occurrences.

ILLUSTRATION 12:  AMSU-A1 Imagery Analysis (User Perspective, cont)

ILLUSTRATION 13:  N16 AVHRR Health Analysis

(Generally nominal although note the slight increases in recent days)

Illustration 4:  N15 AVHRR Synch Delta Analysis

(Steady and nominal)

Illustration 7:  N16 AVHRR Synch Delta & Imagery Analysis

(about as good as it gets)

ILLUSTRATION 14:  N16 AVHRR Imagery vs. Synch Delta Analysis

(Looking very good)

Illustration 8:  N17 AVHRR Analysis

(Generally steady, especially last week but still some less than desirable instability although within normal ranges)

ILLUSTRATION 15:  N17 AVHRR Health Analysis

(Looking about the same as usual)

ILLUSTRATION 16:  N17 AVHRR Synch Delta Analysis

(Looking good)

N17 CPU Single Event Upset Scrub Analysis

# Last week and Cumulative

CPU-1 Unknown location was:

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING January 14, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- |
| FRI. 01/07 | -637 msec | +103 msec | -058 msec | +019 msec | -005 msec |
| SAT. 01/08 | -633 msec | +103 msec | -058 msec | +019 msec | -002 msec |
| SUN. 01/09 | -622 msec | +109 msec | -058 msec | +019 msec | -002 msec |
| MON. 01/10 | -640 msec | +110 msec | -062 msec | +020 msec | -003 msec |
| TUE. 01/11 | N/A | +108 msec | -061 msec | +020 msec | -003 msec |
| WED. 01/12 | -639 msec | +105 msec | -062 msec | +020 msec | -003 msec |
| THU. 01/13 | N/A | +106 msec | -063 msec | +025 msec | -001 msec |

EMOSS POC for this chart Jim Sheperd

NOAA-12  	*Alternating +/- 500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily ETCUP is utilized to manage clock drift. Next +500 mS jump is expected on 1/30/05.

Daily ETCUP bias of +6.5 mSec started on 12/10/03.

NOAA-14:  	As of 1223/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

Subtracted 150 mSecs on 30 June

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –8 msec to compensate for drift.

Added 100 msec to spacecraft command clock on 31 Aug 04

NOAA-16:  	As of 12/23/03 the TIP clock is corrected daily by –5.5 msec to compensate for drift.

Subtracted 100 msec from spacecraft command clock on 31 Aug 04.

NOAA-17:  	As of 12/23/03 the TIP clock is corrected daily by –3 msec to compensate for drift.

Added 125 Msecs3 Feb 04.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads					301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS			 301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS (outgoing)	301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads (in training)			301-817-4026

William Chadwick EMOSS, POES Comm and DHS (in training)	301-817-4015