Users Manual for the Group for High Resolution Sea Surface Temperature (GHRSST-PP)

Draft V1.2

Revision schedule

| Reference: | GHRSST/17 |
| --- | --- |
| Issue: | Users Manual V0.1 |
| Date of issue: | Thursday,March 27, 2008 |
| Document type: | Reference document |
| Authors: | The GHRSST Science Team |
| Revision History: | March 27, 2008 Jorge Vazquez |
| Version 0.8 | April 21,2008 Jorge Vazquez |
| Version 1.0 | May 3. 2008 Jorge Vazquez, Chelle Gentemann, Helen Beggs |
| Version 1.2 | July 17, 2008 Jorge Vazquez |

1. General Introduction	4

2.0 Description of Data	4

2.1 SST Processing Levels and Overview	4

2.2 Where do I get data from?	5

2.3 Data Format and how do I read the data?	6

2.3.1 netCDF	6

2.3.2 How to read SST and confidence flags	6

2.3.3 How do I decide what product to use?	7

2.3.4 What software can I use to read the data	10

2.4 Complete GHRSST Data Formats	10

2.4.1 Level 2 Preprocessed (L2P)	10

2.4.2 Level 4 Analyzed Fields	17

2.4.3 GDSV2.0 L2, L3, and L4 File Naming Conventions	20

3. 0 Methods for Accessing Data	21

3.1 OPenDAP	21

3.2 FTP	21

3.3 HTTP	21

3.4 POET	21

4.0 Using Data (Confidence Flags and Ancillary Fields)	23

4.1 Description of how to use confidence flags and/or quality levels	23

4.1.2 MICROWAVE	23

4.1.3 MSG/SEVIRI SST	23

4.2 Confidence levels and SSES	24

4.3 Description of Ancillary Fields	24

5.0 Frequently Asked Questions	24

6.0 Getting information on GHRSST	24

6.1 Google	24

6.2 Wikipedia	25

6.3 Peer reviewed publications	25

6.4 Web of Science and Knowledge	25

6.5 User Contact Information	25

6.5.1 Jet Propulsion Laboratory	25

6.5.2 Bluelink	25

6.5.3 Long Term Stewardship and Reanalysis Facility (LTSRF)	25

7.0 APPENDICES	26

7.1 Example read software in IDL	26

7.2 The GHRSST Match-Up Database	36

7.2.1  Overview	36

7.2.2 Future plans	36

7.3 High Resolution Diagnostic Data Sets (HRDDS)	37

7.3.1 Overview	37

7.3.2 The HR-DDS portal	37

7.3.3 Time series analysis	38

7.3.4 CSV (comma separated value) pages	40

7.3.5 FTP and OPeNDAP access	40

7.3.6 Multivariate scatter plots	40

7.3.7 Quick look image	41

7.3.8 Spatial comparison page	42

7.3.9 Anomaly analysis page	43

7.3.10 Registered user services	44

7.3.11 MyDDSettes	45

7.3.12 Reporting bugs and suggesting changes	45

7.3.13 Accessibility options	45

7.3.14 HR-DDS file format	45

7.3.15 HR-DDS file name convention	46

7.3.16 FAQ	46

8.0 SST definitions	46

9.0 RDACs, GDAC, and the LTSRF	49

9. 1 RDACs	49

9. 2 GDAC	49

9. 3 LTSRF	49

10.0 netCDF Structure	50

10.1 Why use netCDF?	50

10.2  NetCDF and CF conventions	51

10.3 What's in a netCDF file?	51

10.4 Reading and writing netCDF	52

10.5 netCDF resources	52

11.0 MMR (Master Metadata Repository and search capability)	52

# 1. General Introduction

The Global Ocean Data Assimilation Experiment (GODAE) is an international collaboration for ocean forecasting activities, which in 2002 initiated a GODAE High Resolution SST Pilot Project (GHRSST-PP) to address an emerging need for accurate high-resolution sea surface temperature (SST) products derived from satellite data. High quality SST data is required by operational ocean and atmospheric forecasting systems to constrain the modelled upper ocean circulation thermal structure and for studies of the exchange of energy between the ocean and atmosphere.  However, individual satellites and their sensors are individually unable to provide global, high resolution coverage of the surface temperature of the world’s oceans, due to differing satellite orbits and sensor types.

The primary aim of the Global Ocean Data Assimilation Experiment (GODAE) High Resolution Sea Surface Temperature Pilot Project (GHRSST-PP) is to develop and operate an operational demonstration system that will deliver high-resolution (better than 10 km and ~6 hours), global coverage, SST data products for the diverse needs of GODAE and the wider scientific community. A new generation of SST data products is being derived and served to the user community by combining complementary satellite and in situ SST observations in near real-time. Significantly, GHRSST SST data products are global in scope, combining data received from multiple sensors and multiple satellite platforms. A full description of the GHRSST-PP project is given in the GHRSST-PP Development and Implementation Plan (GDIP) which can be obtained from the GHRSST-PP project web server located at http://www.ghrsst-pp.org.   For more details on how SST is defined within the GHRSST project see Appendix 9.5.

The rest of the Users Manual is organized such that detailed information can be found in the appendices.

# 2.0 Description of Data

## 2.1 SST Processing Levels and Overview

L2P data (Level 2 preprocessed data): - Geophysical variables derived from orbital source data at the same resolution and location as the source data (i.e., satellite projection with geographic information.).  Note that “L2” data may be spatially and temporally irregular, and further processing of the data is required to output data that is equally spaced temporally and spatially on a grid. (Reference:  http://goliath.ecnext.com/coms2/summary_0199-1538021_ITM)  Each SST data file is then reformatted to a common GDS pre-processed data format referred to in the GHRSST program as L2P (described in Appendix A1).  All GHRSST L2P data is in the netCDF format.

Each L2P data product contains original SST measurements together with confidence fields and an error estimate (called single sensor error statistics (SSES)). L2P data products consist of the original SST measurements (that are not re-gridded or modified) together with additional confidence and error estimates.  A separate L2P data product is produced for each sensor at each RDAC.

Each input SST data file is assessed pixel by pixel, using gross error checking rules. A configuration file is used to store all QC parameter limits and thresholds that will be revised as required.  Confidence data are extracted from native SST data streams if present and they are derived using auxiliary and reference data streams and sensor specific error statistics.

Sensor Specific Error Statistics (SSES) are assigned to each SST measurement based on Several different methodologies.

- GHRSST-PP L2P data products will serve the requirements of some operational ocean modelling groups in real-time.  However, many user applications and operational modelling groups request complete SST fields, free of gaps caused by clouds, rain or lack of data coverage, at regular intervals of between 6 and 24 hours.  To address these needs, a number of interplated SST products are also available.

L3 data (Level 3 data):– L3 data is L2 data that receives further processing and is equally mapped (gridded) to a projection of the Earth at various resolutions. Within GHRSST, Level 2 data are mapped on uniform space-time grid scales (Level 3).

L4P data:Each L4 data product is formatted to a common GDS L4 data format (Appendix A1) that contains the analysis at each grid cell together with quality control and error statistic information.  L4 data products are available in real-time to the GHRSST-PP user community. Results from analyses of lower level data (variables derived from multiple measurements). E.g., SST data sets generated from multiple-source satellite data using optimal interpolation. GHRSST L4 data are uniform, global, gap-free, high resolution SST products generated from multiple sensors and multiple satellites through the GDC process as described below:

There is currently no consensus within the GHRSST-PP science Team or indeed the international SST community that defines the optimal analysis procedure to use for the generation of high resolution SST data products based on multiple satellite data inputs.  There are several schemes that have been developed by operational agencies and research establishments (e.g., Reynolds and Smith) that could be used but in each case, the specific method must be adapted to the high resolution space scales that the GHRSST-PP is attempting to resolve. Significant developments have already produced viable results at the Japanese RDAC through the New Generation (NGSST) SST project and further developments are expected from other approaches at the EU RDAC (within the Medspiration project) and USA RDAC/GDAC (within the NOPP SST for GODAE project) in the next 12 months. A major goad of he project was to ensure that all GHRSST-PP data be in the same format. The standard chosen for the GHRSST-PP was netCDF.

## 2.2 Where do I get data from?

Near Real Users (NRT) users should acquire their data from the Global Data Analysis Centers (GDAC) (http://ghrsst.jpl.nasa.gov) where data are integrated, catalogued, and served to users for 30 days.  Users needing the full data set should get data from the Long Term Stewardship and Reanalysis Facility (LTSRF) (http://data.nodc.noaa.gov/cgi-bin/nph-dods/ghrsst/), where they are archived, documented, and served in perpetuity.  For more details on the relationships between the Regional Data Assembly Centers (RDACs), the GDAC, and the LTSRF see Appendix 9.6.

## 2.3 Data Format and how do I read the data?

### 2.3.1 netCDF

All GHRSST data are stored at netCDF data files that provide a convenient, standard, self-describing, platform independent format for data transport. NetCDF (network Common Data Form) is an interface for array-oriented data access and a freely-distributed collection of software libraries that provide implementations of the interface. The netCDF software was developed by Glenn Davis, Russ Rew, Steve Emmerson, John Caron, and Harvey Davies at the UNIDATA Program Center in Boulder, Colorado, and augmented by contributions from other netCDF users. The netCDF libraries define a machine-independent format for representing scientific data. Together, the interface, libraries, and format support the creation, access, and sharing of scientific data.  The British Atmospheric Data Centre (BADC) carries A short introduction to netCDF data. that provides an excellent introduction to netCDF at http://badc.nerc.ac.uk/help/formats/netcdf/index_cf.html.  The complete netCDF documentation can be found at the UNIDATA web site http://www.unidata.ucar.edu/packages/netcdf/index.html. For more detailed information see appendix.

### 2.3.2 How to read SST and confidence flags

In most cases users will simply want to read the SST value and apply the appropriate confidence flag. Confidence flags of 4-5 should be applied to extract the highest quality data.  Additionally a scale and offset needs to be applied to the SST integer value to convert to degrees Kelvin. The scale and offset and confidence flags can be directly read from the netCDF file.  Scale_factor and add_offset can be read directly from the netCDF file. Confidence flags can be read using the confidence_flag parameter in the netCDF file. To convert to SST then:

SST=sst*scale_factor+add_offset where SST is in degrees Kelvin.

The following table shows a summary of the netCDF attributes for the error characteristics, scale factor, offset, and confidence flags. For more detail and a complete list of all the L2P atrributes, including time information,  see the read software in appendix ?

#### 2.3.2.1 L2P data

Attribute Name					Description

| sst | Sea Surface Temperature as an integer |
| --- | --- |
| scale_factor | sst needs to be multiplied by this factor |
| add_offset | Needs to be added to sst*scale_factor |
| confidence_flags | Flag between 0-5 indicating the quality of the SST pixel. For highest quality choose 4-5 |
| SSES_standard_deviation_error | Standard deviation difference between the satellite SST value and in-situ data |
| SSES_bias_error | Mean difference between satellite SST value and in-situ data. |

#### 2.3.2.2 L4 data

| analysed_sst | Merged SST from different satellite sensors |
| --- | --- |
| analysis_error | Error estimates as result of optimal estmation. |

### 2.3.3 How do I decide what product to use?

The GHRSST project makes available several L2P and L4 products.  The following table lists, as of July 16, 2008 all the current products currently available through the GHRSST project. The table includes temporal coverage, spatial coverage, temporal resolution and spatial resolution to facilitate the users deciding what product best suits their needs.

Product [GHRSST product code] Instrument / Type Satellite / Orbit Data Source Agency Data producer [RDAC code] Resolut-ion Latitude range Longitude range Files per day Time Series L2P ATS_NR_2P AATSR / Infrared Envisat / Polar ESA EUR 1 km 90ºN -90ºS 180ºW - 180ºE 15 Mar 2005 -present SEVIRI_SST SEVIRI / Infrared MSG / Geostationary EUMETSAT EUR 0.1 deg 60ºN -60ºS 100ºW - 45ºE 8 (1 file per 3 hours) Feb 2005 -present AMSRE AMSRE / Microwave Aqua / Polar Remote Sensing Systems, Inc. EUR 25 km 90ºN -90ºS 180ºW - 180ºE 14 Feb 2005 – Feb 2007 AMSRE AMSRE / Microwave Aqua / Polar Remote Sensing Systems, Inc. REMSS 25 km 90ºN -90ºS 180ºW - 180ºE 14 (& 14 realtime files) * June 2002 -present AVHRR16_G AVHRR / Infrared NOAA-16 / Polar NAVOCEANO EUR 8.8 km 90ºN -90ºS 180ºW - 180ºE 14 Feb 2005 – Aug 2006 AVHRR16_L AVHRR / Infrared NOAA-16 / Polar NAVOCEANO EUR 2.2 km 90ºN -70ºS 100ºW - 45ºE 1-5 Feb 2005 – Oct 2005 AVHRR17_G AVHRR / Infrared NOAA-17 / Polar NAVOCEANO EUR 8.8 km 90ºN -90ºS 180ºW - 180ºE 14 Feb 2005 – Feb 2007 AVHRR17_L AVHRR / Infrared NOAA-17 / Polar NAVOCEANO EUR 2.2 km 90ºN -70ºS 100ºW - 45ºE ~1-5 Feb 2005 – Feb 2007 AVHRR17_G AVHRR / Infrared NOAA-17 / Polar NAVOCEANO NAVO 8.8 km 90ºN -90ºS 180ºW - 180ºE 14 Jun 2006 – present AVHRR17_L AVHRR / Infrared NOAA-17 / Polar NAVOCEANO NAVO 2.2 km N America west and east coasts and various other ~30 Jun 2006 – present

* AMSRE L2P “realtime” products (contain “_rt_” in filename) from Remote Sensing Systems (REMSS) can have partial orbits. A “-poX-“ will be found in the filename:

· "-po0-: the whole orbit

· -po1-: first section of orbit

· -po2-: second section of orbit

Product [GHRSST product code] Instrument / Type Satellite / Orbit Data Source Agency Data producer [RDAC code] Resolution Latitude range Longitude range Files per day Time Series L2P AVHRR18_G AVHRR / Infrared NOAA-18 / Polar NAVOCEANO NAVO 8.8 km 90ºN -90ºS 180ºW - 180ºE 14 Jan 2006 – present AVHRR18_L AVHRR / Infrared NOAA-18 / Polar NAVOCEANO NAVO 2.2 km N America west and east coasts and various other ~30 Jan 2006 – present AVHRRMTA_G AVHRR / Infrared Envisat / Polar ESA NAVO 9 km 90ºN -90ºS 180ºW - 180ºE 14 Sept 2007 – present NAR16_SST AVHRR / Infrared NOAA-16 / Polar NAVOCEANO EUR 2 km 78ºN -20ºS 45ºW - 45ºE 2 Feb 2005 – Nov 2005 NAR17_SST AVHRR / Infrared NOAA-17 / Polar NAVOCEANO EUR 2 km 78ºN -20ºS 45ºW - 45ºE 2 Feb 2005 – present NAR18_SST AVHRR / Infrared NOAA-18 / Polar NAVOCEANO EUR 2 km 78ºN -20ºS 45ºW - 45ºE 2 Nov 2005 – present MODIS_T MODIS / Infrared Terra / Polar NASA OBPG/RSMAS/JPL JPL 1 km 90ºN -90ºS 180ºW - 180ºE ~288 Oct 2006 - present MODIS_A MODIS / Infrared Aqua / Polar NASA OBPG/RSMAS/JPL JPL 1 km 90ºN -90ºS 180ºW - 180ºE ~288 Jul 2006 - present GOES11 GOES Imager / Infrared GOES-11 NOAA OSDPD 6 km 76ºN -50ºS 146E -59ºW ~48 Dec 2006 - present GOES12 GOES Imager / Infrared GOES-12 NOAA OSDPD 6 km 72ºN -55ºS 152W - 4ºE ~48 Dec 2006 - present TMI TMI / Microwave TRMM / Equatorial Remote Sensing Systems, Inc. EUR 25 km 38ºN -38ºS 180ºW - 180ºE ~16 Feb 2005 – Feb 2007 TMI TMI / Microwave TRMM / Equatorial Remote Sensing Systems, Inc. REMSS 25 km 38ºN -38ºS 180ºW - 180ºE 14 (& 14 realtime files) Jan 1998 – present

Product [GHRSST product code] Instrument / Type Satellite / Orbit Data Source Agency Data producer [RDAC code] Resolut-ion Latitude range Longitude range Files per day Time Series L3P/L2P_GRIDDED AMSRE AMSRE / Microwave Aqua / Polar Remote Sensing Systems, Inc. EUR 25 km 90ºN -90ºS 180ºW - 180ºE 1 (& 1 realtime file) Jun 2002 – present TMI TMI / Microwave TRMM / Equatorial Remote Sensing Systems, Inc. REMSS 25 km 38ºN -38ºS 180ºW - 180ºE 1 (& 1 realtimefile) Jan 1998 -present

Product [GHRSST product code] Region Source Data Producer Agency Data producer [RDAC code] Resolut-ion Latitude range Longitude range Files per day Time Series L4 ODYSSEA GLOB AVHRR, AMSRE, TMI, AATSR, SEVIRI, GOES CNES/Ifremere EUR 6 km 90ºN -90ºS 180ºW - 180ºE 1 Jan 2008 – present AVHRR_OI GLOB AVHRR, in situ (buoys, ships) NOAA NCDC 0.25 deg 90ºN -90ºS 180ºW - 180ºE 1 Jan 1985 -present AVHRR_AMSR_OI GLOB AVHRR, AMSRE, in situ NOAA NCDC 0.25 deg 90ºN -90ºS 180ºW - 180ºE 1 Jun 2002 – present OSTIA GLOB AVHRR, AMSRE, TMI, AATSR, SEVIRI, in situ UK Met Office UKMO 6 km 90ºN -90ºS 180ºW - 180ºE 1 Mar 2006 -present mw_ir_OI GLOB AMSRE, TMI, MODIS Remote Sensing Systems REMSS 6 km 90ºN -90ºS 180ºW - 180ºE 1 Aug 2005 – present ODYSSEA MED AVHRR, AMSRE, TMI, AATSR, SEVIRI CNES/Ifremer EUR 2 km 46.5ºN -30ºN 18.5ºW – 36.5ºE 1 Jan 2008 -present ODYSSEA GAL AVHRR, AMSRE, TMI, AATSR, SEVIRI CNES/Ifremere EUR 2 km 20ºN -20ºS 120ºW - 69ºE 1 Jan 2008 – present ODYSSEA NWE AVHRR, AMSRE, TMI, AATSR, SEVIRI CNES/Ifremer EUR 2 km 60ºN -43ºN 13ºW - 9ºE 1 Jan 2008 -present MED* MED AVHRR, AMSRE, TMI, AATSR, SEVIRI CNES/Ifremere EUR 2 km 45.99ºN -30.01ºN 5.99ºW – 36.49ºE 1 Jan 2005 – Jan 2008 DMI_OI NSEABLATIC AVHRR, AMSRE, AATSR, SEVIRI Danish Met Inst DMI 2 km 65.98ºN - 48.01ºS 9.99ºW - 30ºE 1 Jun 2007 -present

* L4 MED product originally produced from 2005 to 2008 has been superceded by the ODYSSEA product for this region since Jan 2008

ACRYNOMS

AATSR Advanced Along Track Scanning Radiometer

AMSRE Advanced Microwave Scanning Radiometer for EOS

AVHRR Advanced High Resolution Radiometer

CNES Centre National d’Etudes Spatiales

ESA European Space Agency

EUMETSAT European Organisation for the Exploitation of Meteorological Satellites

GOES Geostationary Orbiting Environmental Satellite

JPL Jet Propulsion Laboratory

MODIS Moderate Resolution Imaging Spectrometer

MSG Meteosat Second Generation

NAVOCEANO Naval Oceanographic Office

NASA National Aeronautics and Space Administration

NOAA National Oceanic and Atmospherics Administration

OBPG Ocean Biology Processing Group

RSMAS Rosenstiel School of Marine and Atmospheric Science

SEVIRI Spinning Enhanced Visible and Infrared Imager

TMI TRMM Microwave Imager

TRMM Tropical Rainfall Measuring Mission

RDAC codes

EUR European Medspiration Project

JPL NASA Jet Propulsion Laboratory

NAVO NAVOCEANO

NCDC NOAA National Climatic Data Center

OSDPD NOAA Office of Satellite Data Processing and Distribution

REMSS Remote Sensing Systems, Inc.

L4 Region Identifiers

GLOB: Global Ocean

MED Mediterranean Sea

NWE Northwest Europe (Atlantic)

GAL Galapagos Islands (Pacific)

NSEABALTIC North Sea and Baltic Sea

### 2.3.4 What software can I use to read the data

Read software is available in C and IDL. Such software can be used in designating appropriate flags, along with extraction parameters in latitude and longitude. For programs in C please see: ftp://podaac.jpl.nasa.gov/GHRSST/software/L2P/C. Software to read Level 4 data may be found under:  ftp://podaac.jpl.nasa.gov/GHRSST/software/L4/C.  For example software please see appendix?

## 2.4 Complete GHRSST Data Formats

### 2.4.1 Level 2 Preprocessed (L2P)

The L2P format in netCDF is the standard for all GHRSST non-gridded data.  This format includes all the single sensor statistics (SSES) see appendix 1, ancillary fields, confidence flags and other fields associated with the GHRSST data.  The structure, attributes, and parameters contained in the netCDF are shown below.

| Name | Definition | Description |
| --- | --- | --- |
| <Date Valid> | YYYYMMDD | Refers to the date for which this particular data set is valid for. |
| <L0 ID> | AVHRR18_L SEVIRI_SST MODIS_A ATS_NE_2P GOES12 GOES11 AMSRE TMI | Data set name |
| <Processing Centre Code> | NAVO EUR JPL OSDPD REMSS | Processing centre code |
| <SST filename> | Native to SST filename | Filename of input SST data file as given by data provider |
| <optional characteristic> | string | Free field to distinguish ambiguous cases (such as ascending/descending pass when contained into a single L2 file) |
| <processing model ID> | vnn (where nn is the GDS version number, e.g., 01 | Version number of the GDS system used to process the data file |
| <base format> | nc | Generic file format (nc=netCDF) |

The valid date component of the filename forms the first part of the string so that data can be easily sorted by date.  Examples of L2P files for MODIS, AATSR, SEVIRI, AVHRR, GOES TMI and AMSRE are shown below:

20080407-AVHRR18_L-NAVO-L2P-SST_s1620_e1631-v01.nc

20080407-SEVIRI_SST-EUR-L2P-sst3mlml_20080407_0400-v01.nc

20080407-MODIS_A-JPL-L2P-A2008098063500.L2_LAC_GHRSST-v01.nc

20080405-ATS_NR_2P-EUR-L2P-ATS_NR__2PNPDK20080405_122545_000060672067_00267_31884_7817.N1-v01.nc

20080404-GOES12-OSDPD-L2P-GOES12_South_2239Z-v01.nc

20080407-AMSRE-REMSS-L2P-amsr_l2b_rt_v05_r31531.dat-po0-v01.nc.

20080407-TMI-REMSS-L2P-tmi_L2b_rt_v04_059217.dat-v01.nc.gz

| Name | Description | Units |
| --- | --- | --- |
| lon | Longitude of pixel | Decimal Degrees |
| lat | Latitude of pixel | Decimal Degrees |
| time | Time of pixel observation | Seconds |
| sea_surface_temperature | Pixel SST values use attribute 'sea_surface_temperature:source = "..."' to specify the L2 product source | K |
| sst_dtime | Deviation in seconds from reference time defined as the time of the first L2P data record in this file stored in the netCDF global variable time. It is implicit that there will be a 0 value and sst_dtime is always positive. | second |
| SSES_bias_error | SSES Bias error based on confidence flags. ranges from -1 to 1 degree, precision 0.01 degree | K |
| SSES_standard_deviation_error | SSES standard deviation error based on confidence flags. Ranges from 0 to 1.5 K, precision 0.01 K | K |
| DT_analysis | Deviation from previous day (T-1) SSTfnd analysis. If no analysis is available, the reference mean SST climatology should be used defined as R9 in Table A3.3.1. Precision : 0.1 K | K |
| surface_solar_irradiance | Near contemporaneous SSI value. if 6 hourly irradiance : ranges from 0 to 500 Wm-2, precision 2 Wm-2 if 3 hourly irradiance : ranges from 0 to 1000 Wm-2, precision 4 Wm-2 if unique source (recommended), use attribute 'surface_solar_irradiance:source = "..."' | Wm-2 |
| wind_speed | Wind speed value. ranges from 0 to 50m/s. precision : 1 m/s. if unique source (recommended), use attribute 'wind_speed:source = "..."' | ms-1 |
| sea_ice_fraction | Fractional Sea Ice contamination flag. Ranges from 0 to 1, precision 0.01. if unique source (recommended), use attribute 'sea_ice_fraction:source = "..."' | Percent |
| aerosol_optical_depth | The Aeroptical depth due to extinction by the aerosol component of the atmosphere. Aerosol optical depths typically decrease with increasing wavelength and are much smaller for longwave radiation than for shortwave radiation. Values vary widely depending on atmospheric conditions, but are typically in the range 0.02–0.2 for visible radiation. See also turbidity. Aerosol optical depth. Aerosol optical depth. if unique source (recommended), use attribute 'aerosol_optical_depth:source = "..."' | Scaled value. |
| satellite_zenith_angle | -90 to +90 degrees | Degree |
| rejection_flag | Bit field: 0=SST out of range 1=Cosmetic value 2=IR_Cloudy 3=MW_rain 4=MW_ice 5=MW_wind 6=Land 7=spare | Flag |
| sources_of_wind_speed | Source of wind_speed value. Source codes must be detailed in the ‘sources_of_wind_speed: comment’ attribute. Must be used when several sources are mixed together to fill up this field. When a unique source is used, it can be replace by a variable attribute of wind_speed variable as detailed. | Code |
| sources_of_aod | Source of AOD data. Source codes must be detailed in the ‘sources_of_aod: comment’ attribute. Must be used when several sources are mixed together to fill up this field. When a unique source is used, it can be replace by a variable attribute of aerosol_optical_depth variable as detailed. | Code |
| sources_of sea_ice_fraction | Source of Fractional sea ice data. Source codes must be detailed in the ‘sources_of sea_ice_fraction: comment’ attribute. Must be used when several sources are mixed together to fill up this field. When a unique source is used, it can be replace by a variable attribute of sea_ice_fraction variable as detailed. | Code |
| sources_of_ssi | Source of SSI data. Source codes must be detailed in the ‘sources_of_ssi: comment’ attribute. Must be used when several sources are mixed together to fill up this field. When a unique source is used, it can be replace by a variable attribute of surface_solar_irradiance variable as detailed. | Code |
| wind_speed_dtime_from_sst | Time difference of wind_speed measurement from SST measurement | Scaled hours, 25=not known |
| aod_dtime_from_sst | Time difference of AOD measurement from SST measurement | Scaled hours, 25=not known |
| ssi_dtime_from_sst | Time difference of SSI measurement from SST measurement | Scaled hours, 25=not known |
| confidence_flag | b0 : 1=potential side lobe contamination; b1 : 1=relaxed rain contamination suspected; b2 : 1=TMI SST retrieved in SST < 285K b3 : 1=high wind speed retrieval b4 : 1=sea ice retrieval for MW data b5 : 1= sun glint suspected b6 : 1= L2 native bias and standard deviation; b7 : 1= L2 native confidence value " ; | 8 Flags |
| proximity_confidence | Proximity confidence value | Code |
| New additional fields may be added by L2P data providers if they are really relevant for users. However the new fields shall not increase L2P file size by more than 6 bytes. These New fields and there related properties (variable name, unit,…) must be approved by GHRSST-PO in order to keep the consistency of the various datasets (agreeing for instance on common standard names for the new variables,…). They shall also be documented at GHRSST-PO as an annex to the current GDS version. | Space to provide R&D fields that are in development for GDS-v2.0. E.g. MODIS could provide an estimate of Chlorphyll, to accompany the SST, diurnal variability work, sea ice experiments. 6-bytes are available in any coimbinatkion (i.e., 6x byte, 3 x short, 1 x long + 1 x int etc. These fields will be used to test new ideas for GDS-v2.0 and provide a limited amounmt of flexibility within the GDS for regional user requirements. Flexibility is provided through the netCDF API which allows fully self-describing fields. Use of this field implies documentation. The GHRSST-PO will publish the current use of this field by RDAC teams on the GHRSST-PP web site, The fields must be documented for the LTSRF system and re-analysis as well as a sanity check for the GHRSST-PP as a whole. As an ABSOLUTE MINIMUM, the attributes for this field should be completed including (a) title of field (b) structure of the field (bytes, floats, scale factors etc), (c) the field content (what is it, what are the units) (d) comment on how to use the field e.g. TITLE: DT_Diurnal STRUCTURE: 3 x short_int CONTENT: int#1: estimated deviation from L2P SST due to diurnal warming computed using Kantha Clayson model, uinits K, INT#2: standard deviation of DT_diurnal estimate, units K, INT#3: quality flag of DT_diurnal 0=bad, 1=acceptable,2=good, 3=excellent USAGE: Subtract DT_Diurnal from L2P SST to obtain an estimate of SSTfnd. DT_Diurnal has been computed for each satellite data stream separely. | Defined by RDAC |

Table 1: Description of L2P format array attributes

| Tag name | Format | Description |
| --- | --- | --- |
| Conventions | string | A text string identifying the netCDF convention followed. This attribute should be set to "CF-1.0" to indicate compatibility with the Climate and Forecast (CF) netCDF convention. |
| title | string | A descriptive title for the data set |
| DSD_entry_id | string | the DSD entry related to the data file, e.g. USA-RSS-AMSRE-MW-L2-SST |
| references | String | References that describe the data or the methods used to produce it. Include here the names of all GDS configuration files that have been used. |
| institution | string | GHRSST-PP data centre code (see Appendix A2 Table A2. 1) where the data were produced |
| contact | string | A free text string giving the primary contact for information about the data set |
| GDS_version_id | String | v1r1.4b (to be updated) |
| netcdf_version_id | String | 3.5 |
| creation_date | string,"yyyy-mm-dd" | Date the data file was created (UTC) |
| product_version | string | Release number of the datafile (File_Version in the MMR-FR, see A6.3.2) |
| history | string | List of the applications that have modified the original data |
| platform | string | Satellite identifier |
| sensor | string | Sensor identifier |
| spatial_resolution | string | Resolution of the product |
| start_time | string, “hh:mm:ss UTC” | Time of the first measurement in the data file |
| stop_time | string, “hh:mm:ss UTC” | Time of the last measurement in the data file |
| start_date | string,"yyyy-mm-dd UTC" | Start date of the data in universal time coordinated (UTC; ~ Greenwich Mean Time) |
| stop_date | string,"yyyy-mm-dd UTC" | End date of the data in universal time coordinated (UTC; ~ Greenwich Mean Time). |
| northernmost_latitude | Float | degrees north, range -90° to +90° |
| southernmost_latitude | Float | degrees north, range -90° to +90° |
| easternmost_longitude | Float | degrees east, range -180° to +180° |
| westernmost_longitude | Float | degrees east, range -180° to +180° |
| file_quality_index | integer | A code value : 0 : unknown quality 1: excellent (no known problems) 2 : suspect (occasional problems, e.g. after launch) 3 : extremely suspect (frequent problems, e.g.with known satellite problems) |
| source_data | string [1024] | Comma separated list of source data present in this file. SST sources followed by Auxillary sources. Source data identifiers are taken from Table A2.2. e.g., for an L2P file we might expect something like: ATS_NR__2P,SEVIRI_SSI,OSISAF_ICE,NESDIS_AOD,UKMO_WSP For an L4 product we may expect something like: ATS_NR__2P,AVHRR16_G,SEVIRI,AMSRE,SEVIRI_SSI,OSISAF_ICE,NESDIS_AOD,UKMO_WSP, AMSRE_ICE, AMSRE_WSP |
| comment | string | Miscellaneous information |

Table 2: Description of l2P format global attributes

| Tag name | Format | Description |
| --- | --- | --- |
| _FillValue | Depends on variable type | A value used to indicate array elements containing no valid data. This must be of the same type than the storage (packed) type; should be set as the minimum value for this type. Note that some netCDF readers are unable to cope with signed bytes and may, in these cases, report fill as 128 |
| units | string | Text description of the units, preferably S.I., and must be compatible with the Unidata UDUNITS package. For a given variable (e.g. wind speed), these must be the same for each dataset. |
| scale_factor | must be expressed in the unpacked data type (for instance float whereas the variable may be stored - or packed - as an array of short) | To be multiplied by the variable to recover the original value. Defined by RDAC |
| add_offset | must be expressed in the unpacked data type (for instance float whereas the variable may be stored - or packed - as an array of short) | To be added to the variable after multiplying by the scale factor to recover the original value. If only one of scale_factor or add_offset are needed, then both should be included anyway to avoid ambiguity, with scale_factor defaulting to 1.0 and add_offset defaulting to 0.0. Defined by RDAC |
| long_name | string | A long version of the variable name |
| valid_min | Same data type as variable | Minimum valid value for this variable once they are packed (in storage type). The fill value should be outside this valid range. Note that some netCDF readers are unable to cope with signed bytes and may, in these cases, report valid min as 129 |
| valid_max | Same data type as variable | Maximum valid value for this variable once they are packed (in storage type). The fill value should be outside this valid range. Note that some netCDF readers are unable to cope with signed bytes and may, in these cases, report valid min as 127 |
| standard_name | string | A standard and unique description of a physical quantity. For the complete list of standard name strings, see http://www.cgd.ucar.edu/cms/eaton/netcdf/standard_name.html. |
| source | string | Method of production of the original data or original provider |
| axis | string | Identifies latitude, longitude, vertical or time axis |
| positive | string | Indicates the real-world direction of a coordinate variable ("up" or "down"). E.g., a depth or atmospheric pressure coordinate would have this attribute set to "down". |
| coordinates | string | Identifies auxiliary coordinate variables, such as 2-D lat-lon coordinate arrays, label variables, and alternative coordinate variables. |
| grid_mapping | string | Identifies a variable that defines a grid mapping must be provided if data mapped following a projection. refer to CF convention for standard projection names. |
| comment | string | Miscellaneous information about the data or the methods used to produce it |

Table 3: Description of netCDF mandatory attributes

### 2.4.2 Level 4 Analyzed Fields

L4 analysed data products, L4 are derived from an analysis procedure based on L2P and other SST data products produced at regular (daily, six-hourly or other (e.g., APPW)) time periods. L4 data products are formatted as netCDF format data files and include ancillary data and error statistics for each grid-cell.  A six-byte experimental block is available for data providers to test new aspects of the file or information specific to the analysis system that will eventually transition into a GHRSST-PP standard L4 analysis field once tested.

L4 global/variable attributes and the coordinate variables are equivalent to L2P products format requirements (netCDF format, complying to CF-1.0 convention) as laid out in Appendix A1 (GDS data product format specification).

The GDS filename convention used for L4 data products has been designed to provide useful information in an easily readable format.  All L4 data product filenames are derived according to the following convention:

<Date Valid>-<Processing Centre Code>-L4<Product type>-<Area>-<Processing Model ID>-<FileVersion>.<base format>

which is defined in Table 2.

| Name | Definition | Description |
| --- | --- | --- |
| <Date Valid> | YYYYMMDD | Refers to the date for which this particular data set |
| <Processing Centre Code> | UKMO NAVO NCDC REMSS EUR | Processing centre code |
| <product type> | "LR"=low resolution, "HR"=high resolution or "UH"=ultra-high resolution followed by either fnd (for foundation SST), skin, subskin, blend (for blended SST) or 1m, 2m, .... , 10m (for SST at specific depth). UH<=5km, HR<=10km, LR>10km. | Resolution of analysed foundation SST (fnd) data |
| <Area> | GLOB MED NSEABALTIC NEW AUS | The area covered by the L4 product |
| <processing model ID> | vnn (where nn is the GDS version number, e.g., 01 | Version number of the GDS system used to process the data file |
| <FileVersion> | Fvxx.x (where xx.x is the release number of this file.g.fv11.3 | Release version for this L4 file |
| <Additonal Segregator> | Free text to distinguish between files with the same <Identifying Code> eg: OSTIA, ODYSSEA | This text is used since the other codes are often insufficient to uniquely identify a file. For example, in L2_GHRSST or L3_GHRSST (uncollated) products this is often the original file name or processing algorithm (note, underscores are used, not dashes). |
| <base format> | Nc | Generic file format (nc=netCDF) |

Table 4: L4 product filenames

Examples include;

20080406-UKMO-L4HRfnd-GLOB-v01-fv02-OSTIA.nc

20080407-NAVO-L4HR1m-GLOB-v01-fv01_0-K10_SST.nc

20080406-NCDC-L4LRblend-GLOB-v01-fv01_0-AVHRR_OI.nc

20061231-REMSS-L4HRfnd-GLOB-v01-fv01-mw_ir_OI.nc

20080113-EUR-L4UHFnd-MED-v01.nc

20080407-EUR-L4UHRfnd-MED-v01-fv01-ODYSSEA.nc

20080407-DMI-L4UHfnd-NSEABALTIC-v01-fv01-DMI_OI.nc

20040621-EUR-L4UHfnd-MED-v01-fv11.6.nc

20080331-ABOM-L4HRfnd-AUS-v01-fv01_0-RAMSSA_09km.nc

Refers to a data set valid on 21st June 2004 (20040621) generated at the European RDAC (EUR), the data is an estimate of the foundation SST at ultra-high resolution(L4UHfnd) covering the Mediterranean area (MED), it was generated using GDS version 1 (v01), it is release 11.6 of the file (implies considerable re-processing) and is formatted as a GHRSST-PP netCDF file (.nc)

| Code | Definition | Description |
| --- | --- | --- |
| GLOB | 90°S to 90°N and from 180°W - 180°E | Global coverer age data sets |
| MED | 30°N to 46°N and from 6°W to 36.5°E | Mediterranean sea area |
| EUR | 70°S to 90°N and from 100°W to 45°E | European RDAC area served by the ESA Medspiration project |
| AUS | 70S to 20N and from 60E to 170W. | BoM Australian regional analysis |

Table 5: Description of example  L4 product filename area code definitions

Table 6 describes the format of the L4 file variables associated with each grid cell.

| Name | Description | Units |
| --- | --- | --- |
| analysed_sst | SST from analysis system | K, scaled 2 byte int |
| analysis_error | Error standard deviation estimate output from the analysis system | K, scaled 2 byte int |
| mask | 0=grid cell is open water 1=land in grid 2=lake surface in grid cell, 3=ice in grid cell Bits [4-7] spare. | Flag [8bits] |
| sea_ice_fraction | Fractional Sea Ice area concentration. Optional when covered area never contains sea ice. | 0-1 scaled byte |
| sources_of sea_ice_fraction | Source of Fractional sea ice data should be same definition as for L2P. Should be replaced by a variable attribute of sea_ice_fraction when single source. | Code |
| Experimental field | Each grid cell has a 6 byte storage space available for RDACs and other users to incluse specific information. The policy for use of these fields is that they should make a useful contribution to the data sets and to GHRSST-PP. Ideally experimental fields should transition into full fields once stable and agreed by the GHRSS-PP Science Team. Use of these fields requires that a description of the content and specification is agreed with the GHRSST-PP Data Management Technical Advisory group and that CF-1.0 compliant attributes are included in the file. | 6 bytes (maximum) Defined by data providers. |

Table 5:  generic L4 SST Variables

The variable ‘analysed_sst’ will be included with the format requirements shown in Table A1.3.3.2.

Table A5 CDL description of analysed_sst variable

|  | Name | Description | Unit |
| --- | --- | --- | --- |
|  | analysed_sst | SST values from analysis systems | Kelvin |
| Comments |
| Code definitions for analysed_sst:type (see GHRSST-PP SST definitions in Section 2 of the GDS (Notations, conventions and definitions used by the GDS)): type Description skin Skin surface temperature subskin Subskin temperature foundation Foundation temperature depth_blended Temperature from a blended SST analysis valid over the surface ocean in a layer with unspecified depth 1m SST at 1m depth (SST1m) 2m SST at 2m depth (SST2m) 3m SST at 3m depth (SST3m) 4m SST at 4m depth (SST4m) 5m SST at 5m depth (SST5m) 6m SST at 6m depth (SST6m) 7m SST at 7m depth (SST7m) 8m SST at 8m depth (SST8m) 9m SST at 9m depth (SST9m) 10m SST at 10m depth (SST10m) |

### 2.4.3 GDSV2.0 L2, L3, and L4 File Naming Conventions

It is anticipated that GDSV2.0 will be implemented in the near future. Striving to achieve a more flexible naming convention that maintains consistency across data processing levels and better serves user needs, the GDS 2.0 will use a single form for all GHRSST files:

<Date Valid>-<RDAC>-L<X><OPTIONALCODE>_GHRSST-<Product Type>-<Identifying Code>-<Additional Segregator>-v<GDS Version>-fv<File Version>.nc

The variable components within braces ( “< >”) are defined in Table 1 below.

| Name | Definition | Description |
| --- | --- | --- |
| <Date Valid> | YYYYMMDD | Refers to the identifying date for this particular data set |
| <RDAC> | The RDAC where the file was created | Processing centre code, defined in a GDS Appendix |
| <X> | GHRSST Data Processing Level (X = 2, 3, or 4) | Refers to the data processing level, defined at the beginning of this proposal. |
| <OPTIONALCODE> | An optional, single-character | An optional one character long code. For example, if set to “P” for a Level 2 file, the name would now contain “L2P_GHRSST” instead of simply “L2_GHRSST” |
| <Product Type> | The type of SST data included in the file. | Conforms to the GHRSST definitions for SST, for example: SST1m, SSTfnd, SSTsubskin, SSTblend, SSTskin |
| <Identifying Code> | A unique code identifying the SST product set. | The unique “name” (within an RDAC) of the product line. (L2_GHRSST examples: AVHRR18_G, AMSRE; L3_GHRSST examples: NAR_AVHRR_METOP_A, GLOB_AVHRR_METOP_A; and L4_GHRSST examples: OSTIA, AVHRR_OI (note, underscores are used, not dashes) |
| <Additional Segregator> | Free text to distinguish between files with the same <Identifying Code> | This text is used since the other codes are often insufficient to uniquely identify a file. For example, in L2_GHRSST or L3_GHRSST (uncollated) products this is often the original file name or processing algorithm (note, underscores are used, not dashes). |
| <GDS Version> | nn.n | Version number of the GDS used to process the data file |
| <FileVersion> | xx.x | Version number for this file |

Table 6: GDS 2.0 File naming convention components

Changes in GDSv2.0 include the definitions of L2_GHRSST, L3_GHRSST, L4_GHRSST, as apposed to L2P, L3, and L4.

# 3. 0 Methods for Accessing Data

## 3.1 OPenDAP

Data is available through OPenDAP through http://dods.jpl.nasa.gov/ at the GDAC or  http://data.nodc.noaa.gov/cgi-bin/nph-dods/ghrsst/ at the LTSRF

## 3.2 FTP

All GHRSST Level 2 Preprocessed, Level 3 and Level 4 Preprocessed Products are available through a 30 day rolling archive at GDAC/PO.DAAC  through ftp://podaac.jpl.nasa.gov/pub/GHRSST. Also included is read software for all L2P and L4 products.  After 30 days data is available through the permanent archive at NODC at

ftp://data.nodc.noaa.gov/pub/data.nodc/ghrsst/

## 3.3 HTTP

Data may be retrieved directly for the first 30 days from the GDAC at http://ghrsst.jpl.nasa.gov. After 30 days data may be retrieved through the LTRSF at http://ghrsst.nodc.noaa.gov/

## 3.4 POET

Currently Level 4 data is available through the GDAC/PO.DAAC  Ocean Earth Science Information Partner Federation (ESIP) Tool (POET) (http://poet.jpl.nasa.gov). This tool allows for complete subsetting of all level 4 data in both the temporal and spatial domains. As of this writing level 4 data sets included in POET are:

OSTIA: Operational Sea Surface Temperature and Sea Ice Analysis

ODYSSEA: Global High Resolution Foundation Sea Surface Temperature Analysis

NODC AVHRR OI: National Oceanographic Data Center (NODC)  Advanced Very High Resolution Radiometer (AVHRR) Optimal Interpolation

NODC AVHRR + AMSRE OI: National Oceanographic Data Center (NODC) Advanced Very High Resolution Radiometer (AVHRR) and Advanced Microwave Scanning Radiometer-EOS (AMSRE) Optimal Interpolation

Remote Sensing Systems Blended AVHRR + Microwave product

It is anticipated that as GHRSST Level 4 data sets become available they will be integrated into the POET tool.   Future plans include the development of a L2P subsetting capability through the POET interface.  Other regional products in the Mediterranean and the Baltic Sea are available.

# 4.0 Using Data (Confidence Flags and Ancillary Fields)

## 4.1 Description of how to use confidence flags and/or quality levels

### 4.1.2 MICROWAVE

In the simplified user manual I would recommend that users simply use the total confidence value.  If MWCV is less than 3, then the data should be thrown out.  Advanced users can examine the actual confidence flags or rejection flags for additional information if they choose.

It might be useful if in the JPL software there was a special question asked of the user in the netcdf reading routines requesting confidence values to highlight the use of these confidence values.  Unprocessed data is given a higher value than Bad and Suspect data because if it hasn’t been flagged than it is good data.

Microwave Proximity confidence value (MWPCV) definitions.

| Value | Definition |
| --- | --- |
| 1 | Bad: Data has been rejected |
| 2 | Suspect: Data that may be contaminated, (any confidence flags thrown except DW) |
| 3 | Unprocessed: Data that have not been classified by confidence flags. This data should be fine. |
| 4 | Excellent: Data that we think are good |

Microwave confidence flags definitions.

| Bit | Definition |
| --- | --- |
| 0 | rain present within 50km and difference from yesterday’s OI SST greater than 0.6 K |
| 1 | rain present within 100km and difference from yesterday’s OI SST greater than 0.8 K |
| 2 | ice present within 150 km and difference from yesterday’s OI SST greater than 0.6 K |
| 3 | difference from yesterday’s OI SST greater than 5 K |
| 4 | STD and Mean calculated from yesterday’s OI SST from data within 250 km of pixel. SST at pixel required to be within 3*STD of mean |
| 5 | land present within 125 km and difference from yesterday’s OI SST greater than 0.6 K |
| 6 | diurnal warming calculated from model greater than 1 K |
| 7 | diurnal warming calculated from model greater than 0.3 K |

### 4.1.3 MSG/SEVIRI SST

Sensor description :

Meteosat Second Generation (MSG) is a series of spin stabilized geostationary satellites operated by EUMETSAT. Their subpoint nominal coordinates are  0N, 0E. MSG2 replaced MSG1 in May 2007. They carry the Spinning Enhanced Visible and Infrared Imager (SEVIRI) which has 2  visible channels at 0.6 and 0.8 mm , one near IR channel at 1.6 mm and 4 IR channels at 3.9, 8.7, 10.8 and 12 mm. The resolution ranges from 3km at subpoint to about 4.5 km at 40N 0E and 9 km at 60N 0E.The repeat cycle is 15minutes. For more details see Schmetz et al 2002.

SST processing:

SST processing is done by EUMETSAT through their Ocean and Sea Ice Satellite Application Facility (OSI SAF) at the Centre de Meteorologie Spatiale of Meteo-France (MF/CMS) in Lannion (France). They are then converted into L2P through the MEDSPIRATION chain also implemented at MF/CMS.

SST is calculated every hour at full satellite resolution; a confidence level is calculated for each pixel. They are remapped over a regular 0.1 degree resolution grid over the OSI SAF Atlantic domain (100W-45E, 60S-89.9N), then averaged over three hour periods centred on 0100, 0400, 0700… UTC. SEVIRI derived SST are subskin SST calculated via a split window algorithm and bias corrected against nighttime buoy measurements. A Saharan Dust Index is derived from the SEVIRI data and used to mask/correct the SST calculations (since April 2006).

For more details see Le Borgne et al., 2006. A detailed Product User Manual, validation results and reports are available through http://www.osi-saf.org.

Format and content :

The L2P products are full (GDS v1.5 compliant) L2P including SST, confidence levels and SSES with the following ancillary data: Sea Ice Fraction (OSI SAF), aerosol optical depth (NAAPS), wind speed (ECMWF), Surface Solar Irradiance (ECMWF or OSI SAF).

## 4.2 Confidence levels and SSES

The confidence levels are derived on a 5 level scale from 0 (unprocessed ) to 5 (excellent), as described in GDS v1.5. They reflect mainly a potential contamination by cloudiness. It is recommended not to use the level 2 (bad) data for quantitative use.

SSES are derived from the Match up Data Base (MDB) over a period of one year or longer and represents the error statistics (bias and standard deviation) corresponding to each confidence level. It is recommended to correct for the SSES bias before use. Note that the SSES always provides an error.

Contact:

Through the OSI SAF help desk system, see http://www.osi-saf.org

References:

Schmetz, J., P. Pili, S. Tjemkes, D. Just,, J. Kerkmann, S. Rota and A. Ratier,  2002, An introduction to Meteosat Second Generation, Bulletin of the American Meteorological Society, 977-992.

Le Borgne, P., G.Legendre and A. Marsouin, 2006, Proceedings of the 2006 EUMETSAT Meteorological Satellite data User’s Conference, Helsinki, Finland.

## 4.3 Description of Ancillary Fields

Each GHRSST L2P netCDF file contains ancillary fields, co-located in space and time to the L2P locations, that are known to affect the calculation of SSTs. These ancillary fields include, wind speed, surface-solar-irradiance, aerosols,  and sea ice fraction. These fields can then be used for flagging purposes or for statistical studies of the effects of these parameters on the calculation of SSTs. Ancillary fields are either filled in by the appropriate RDAC or at the GDAC. An additional field, the DT_analysis, compares the given day’s SST with a reference field or with the previous day’s fields.  All of these fields are available as attributes within the netCDF files.

# 5.0 Frequently Asked Questions

1. What is GHRSST? Group for High Resolution Sea Surface Temperature

2. What format is the data in? netCDF

3. How does GHRSST differ from previous SST data sets? Has complete error characterization, standard netCDF format for all products, the addition of ancillary fields.

# 6.0 Getting information on GHRSST

http://www.ghrsst-pp.org/ GHRSST project office

http://ghrsst.nodc.noaa.gov/ Long Term Stewardship and Reanalysis Facility

http://ghrsst.jpl.nasa.gov Global Data Assembly Center

## 6.1 Google

Doing a search on GHRSST immediately leads you to the GHRSST project page. Links from there go to GDAC, LTSRF and other GHRSST related projects.

## 6.2 Wikipedia

Doing a search through wikipedia using GHRSST leads you to a description of the project and it’s purpose.

## 6.3 Peer reviewed publications

## 6.4 Web of Science and Knowledge

http://apps.isiknowledge.com/

## 6.5 User Contact Information

### 6.5.1 Jet Propulsion Laboratory

JPL

Edward Armstrong

edward.m.armstrong@jpl.nasa.gov

Jorge Vazquez

jorge.vazquez@jpl.nasa.gov

Global Data Assembly Center

Physical Oceanography Distributed Active Archive Center

4800 Oak Grove Dr.

Pasadena, Ca. 91109

### 6.5.2 Bluelink

Helen Beggs

H.beggs@bom.gov.au

Ocean Satellite Observations Scientist,

Ocean Prediction Group,

Centre for Australian Weather and Climate Research,

Bureau of Meteorology,

700 Collins St, Melbourne Vic 3000 AUSTRALIA

<http://www.bom.gov.au/bluelink>

### 6.5.3 Long Term Stewardship and Reanalysis Facility (LTSRF)

Kenneth S. Casey, Ph.D.

Acting Technical Director

NOAA National Oceanographic Data Center

1315 East-West Highway

Silver Spring MD 20910

301-713-3272 ext 133

Kenneth.casey@noaa.gov

<http://www.nodc.noaa.gov/SatelliteData>http://www.nodc.noaa.gov/SatelliteData

# 7.0 APPENDICES

## 7.1 Example read software in IDL

;  Copyright 2005, by the California Institute of Technology.  ALL RIGHTS

;  RESERVED. United States Government Sponsorship acknowledged. Any commercial

;  use must be negotiated with the Office of Technology Transfer at the

;  California Institute of Technology.

; $Id: read_L2P.pro,v 1.4 2008/05/07 18:42:21 ghrsst_mmr Exp $

; read_L2P.pro  e. armstrong    Caltech/JPL/NASA

PRO read_L2P,     L2P_file, $,				; input

time, time_atts, $			; returned: reference time and attributes

lat, lat_atts, $			; latitude and attributes

lon, lon_atts, $  			; longitude and attributes

sst, sst_atts, $			; SST and attributes

sst_dtime, sst_dtime_atts, $		; deviation from reference time and attriubtes

sses_bias, sses_bias_atts, $		; SST bias error and attriubtes

sses_sd, sses_sd_atts, $		; SST standard dev. error and attributes

dt_analysis, dt_analysis_atts, $	; SST/analysis SST difference and attributes

ssi, ssi_atts, $			; surface solar irradiance and attributes

wind, wind_atts, $			; wind speed and attributes

aod, aod_atts, $ 			; aersol optical depth and attributes

seaice, seaice_atts, $		; sea ice fraction and attributes

ssi_source, ssi_source_atts, $	; source of ssi and attributes

wind_source, wind_source_atts, $	; soruce of wind speed and attributes

aod_source, aod_source_atts, $	; source of aod and attributes

seaice_source, seaice_source_atts, $	; source of sea ice and attributs

ssi_sst_dtime, ssi_sst_dtime_atts, $	; time difference between ssi and sst and attributes

wind_sst_dtime, wind_sst_dtime_atts,$ ; DT between wind and sst and attributes

aod_sst_dtime, aod_sst_dtime_atts, $	; DT between aod and sst and attributes

sat_zen_ang, sat_zen_ang_atts, $ 	; satellite zenith angle and attriubtes

reject_flag, reject_flag_atts, $	; rejection flag and attributes

conf_flag, conf_flag_atts, $		; confidence flag and attributes

proximity_conf, proximity_conf_atts,$ ; proximity confidence flag and attributes

global_atts				; global attributes

;---------------------------------------------------------------

; SYNOPSIS:

; Reads (and returns) all the arrays and attributes of a L2P file.

; USAGE:

; IDL> read_l2p, 'L2P_file.nc', .... and all the other args

;---------------------------------------------------------------

;--------------------------------

; Open the file and read the data

; arrays. The array attributes

; and global attributes are read

; into a structure.

;--------------------------------

print, ''

nid = ncdf_open( L2P_file, /nowrite )

; inquire about this file; returns structure

file_info = ncdf_inquire( nid )

; print out the dimensions of this file

for dimid=0, file_info.ndims -1 do begin

ncdf_diminq, nid, dimid, name, size

print, ' ---> dimension ' + name  + ' is: ', size

endfor

; ------------------------------------------------

; loop over each variable and extract its data and

; metadata

; ------------------------------------------------

for varid=0, file_info.nvars-1 do begin

; inquire about the variable; returns structure

var = ncdf_varinq( nid, varid )

print, '. . . reading variable ', var.name

case var.name of

'time': begin

id = ncdf_varid(nid, 'time')

ncdf_varget, nid, id, time

time_atts = get_array_attributes( nid, id )

break

end

'lat': begin

id = ncdf_varid(nid, 'lat')

ncdf_varget, nid, id, lat

lat_atts = get_array_attributes( nid, id )

break

end

'lon': begin

id = ncdf_varid(nid, 'lon')

ncdf_varget, nid, id, lon

lon_atts = get_array_attributes( nid, id )

break

end

'sea_surface_temperature': begin

id = ncdf_varid(nid, 'sea_surface_temperature')

ncdf_varget, nid, id, sst

sst_atts = get_array_attributes( nid, id )

break

end

'sst_dtime': begin

id = ncdf_varid(nid, 'sst_dtime')

ncdf_varget, nid, id, sst_dtime

sst_dtime_atts = get_array_attributes( nid, id )

break

end

'SSES_bias_error': begin

id = ncdf_varid(nid, 'SSES_bias_error')

ncdf_varget, nid, id, sses_bias

sses_bias_atts = get_array_attributes( nid, id )

break

end

'SSES_standard_deviation_error': begin

id = ncdf_varid(nid, 'SSES_standard_deviation_error')

ncdf_varget, nid, id, sses_sd

sses_sd_atts = get_array_attributes( nid, id )

break

end

'DT_analysis': begin

id = ncdf_varid(nid, 'DT_analysis')

ncdf_varget, nid, id, dt_analysis

dt_analysis_atts = get_array_attributes( nid, id )

break

end

'surface_solar_irradiance': begin

id = ncdf_varid(nid, 'surface_solar_irradiance')

ncdf_varget, nid, id, ssi

ssi_atts = get_array_attributes( nid, id )

break

end

'wind_speed': begin

id = ncdf_varid(nid, 'wind_speed')

ncdf_varget, nid, id, wind

wind_atts = get_array_attributes( nid, id )

break

end

'sea_ice_fraction': begin

id = ncdf_varid(nid, 'sea_ice_fraction')

ncdf_varget, nid, id, seaeice

seaice_atts = get_array_attributes( nid, id )

break

end

'aerosol_optical_depth': begin

id = ncdf_varid(nid, 'aerosol_optical_depth')

ncdf_varget, nid, id, aod

aod_atts = get_array_attributes( nid, id )

break

end

'satellite_zenith_angle': begin

id = ncdf_varid(nid, 'satellite_zenith_angle')

ncdf_varget, nid, id, sat_zen_ang

sat_zen_ang_atts = get_array_attributes( nid, id )

break

end

'sources_of_ssi': begin

id = ncdf_varid(nid, 'sources_of_ssi')

ncdf_varget, nid, id, ssi_source

ssi_source_atts = get_array_attributes( nid, id )

break

end

'sources_of_wind_speed': begin

id = ncdf_varid(nid, 'sources_of_wind_speed')

ncdf_varget, nid, id, wind_source

wind_source_atts = get_array_attributes( nid, id )

break

end

'sources_of_sea_ice_fraction': begin

id = ncdf_varid(nid, 'sources_of_sea_ice_fraction')

ncdf_varget, nid, id, seaice_source

seaice_source_atts = get_array_attributes( nid, id )

break

end

'sources_of_aod': begin

id = ncdf_varid(nid, 'sources_of_aod')

ncdf_varget, nid, id, aod_source

aod_source_atts = get_array_attributes( nid, id )

break

end

'ssi_dtime_from_sst': begin

id = ncdf_varid(nid, 'ssi_dtime_from_sst')

ncdf_varget, nid, id, ssi_sst_dtime

ssi_sst_dtime_atts = get_array_attributes( nid, id )

break

end

'wind_speed_dtime_from_sst': begin

id = ncdf_varid(nid, 'wind_speed_dtime_from_sst')

ncdf_varget, nid, id, wind_sst_dtime

wind_sst_dtime_atts = get_array_attributes( nid, id )

break

end

'aod_dtime_from_sst': begin

id = ncdf_varid(nid, 'aod_dtime_from_sst')

ncdf_varget, nid, id, aod_sst_dtime

aod_sst_dtime_atts = get_array_attributes( nid, id )

break

end

'rejection_flag': begin

id = ncdf_varid(nid, 'rejection_flag')

ncdf_varget, nid, id, reject_flag

reject_flag_atts = get_array_attributes( nid, id )

break

end

'confidence_flag': begin

id = ncdf_varid(nid, 'confidence_flag')

ncdf_varget, nid, id, conf_flag

conf_flag_atts = get_array_attributes( nid, id )

break

end

'proximity_confidence': begin

id = ncdf_varid(nid, 'proximity_confidence')

ncdf_varget, nid, id, proximity_conf

proximity_conf_atts = get_array_attributes( nid, id )

break

end

else: begin

print, ' unknown L2P variable: ', var.name

id = ncdf_varid(nid, var.name)

ncdf_varget, nid, id,  new_l2p_array

new_l2p_array_atts = get_array_attributes( nid, id )

end

endcase

endfor

; retrieve the global attributes

print, '. . . reading global attributes '

global_atts = get_global_attributes( nid, file_info )

; close the file

ncdf_close, nid

print,  '   --> done reading L2P <-- '

END

; ---------------------------------------------

; returns a structure of COARDS array attributes

; ---------------------------------------------

FUNCTION get_array_attributes, nid, array_id

; turn off error messages

ncdf_control, nid, /NOVERBOSE

; returned structure prototype for variable attributes

;array_atts = { long_name:'', units:'', FillValue:0L, add_offset:0.0, scale_factor:0.0, $

;		valid_min:0, valid_max:0, coordinates:'', source:'', comment:'', grid_mapping:'', $

;		standard_name:'', axis:'', positive:'' }

; first structure element

array_atts = create_struct('dummy', 'ignore'  )

; inquire about this variable; returns number of attributes

var_info = ncdf_varinq( nid, array_id )

; loop through the attributes and load into a structure

for att_id=0, var_info.natts - 1 do begin

att_name = ncdf_attname( nid, array_id, att_id )

;result = ncdf_attinq( nid, array_id, att_name )

case att_name of

'long_name': begin

ncdf_attget, nid, array_id, 'long_name', long_name

array_atts = create_struct( 'long_name', string(long_name), array_atts )

end

'units': begin

ncdf_attget, nid, array_id, 'units', units

array_atts = create_struct( 'units', string(units), array_atts )

end

'_FillValue': begin

ncdf_attget, nid, array_id, '_FillValue', FillValue

array_atts = create_struct('FillValue', FillValue, array_atts )

end

'missing_value': begin

ncdf_attget, nid, array_id, 'missing_value', FillValue

array_atts = create_struct('FillValue', FillValue, array_atts )

end

'add_offset': begin

ncdf_attget, nid, array_id, 'add_offset', add_offset

array_atts = create_struct('add_offset', add_offset, array_atts )

end

'scale_factor': begin

ncdf_attget, nid, array_id, 'scale_factor', scale_factor

array_atts = create_struct('scale_factor', scale_factor, array_atts )

end

'valid_min': begin

ncdf_attget, nid, array_id, 'valid_min', valid_min

array_atts = create_struct('valid_min', valid_min, array_atts )

end

'valid_max': begin

ncdf_attget, nid, array_id, 'valid_max', valid_max

array_atts = create_struct('valid_max', valid_max, array_atts )

end

'coordinates': begin

ncdf_attget, nid, array_id, 'coordinates', coordinates

array_atts = create_struct('coordinates', string(coordinates), array_atts )

end

'source': begin

ncdf_attget, nid, array_id, 'source', source

array_atts = create_struct('source', string(source), array_atts )

end

'comment': begin

ncdf_attget, nid, array_id, 'comment', comment

array_atts = create_struct('comment', string(comment), array_atts )

end

'grid_mapping': begin

ncdf_attget, nid, array_id, 'grid_mapping', grid_mapping

array_atts = create_struct('grid_mapping', string(grid_mapping), array_atts )

end

'axis': begin

ncdf_attget, nid, array_id, 'axis', axis

array_atts = create_struct('axis', string(axis), array_atts )

end

'standard_name': begin

ncdf_attget, nid, array_id, 'standard_name', standard_name

array_atts = create_struct('standard_name', string(standard_name), array_atts )

end

'positive': begin

ncdf_attget, nid, array_id, 'positive', positive

array_atts = create_struct('positive', string(positive), array_atts )

end

else: begin

print, ' unknown attribute: ',  att_name

end

endcase

endfor

return, array_atts

END

; ---------------------------------------------

; returns a structure of COARDS GLOBAL attributes

; ---------------------------------------------

FUNCTION get_global_attributes, nid, file_info

; returned structure prototype for GLOBAL attributes

global_atts = { global_attributes, Conventions:'', title:'', DSD_entry_id:'', references:'', institution:'', $

contact:'', GDS_version_id:'', netcdf_version_id:'', creation_date:'', $

product_version:'', history:'', platform:'', sensor:'', spatial_resolution:'', $

start_date:'', start_time:'', stop_date:'', stop_time:'', northernmost_latitude:0.0, $

southernmost_latitude:0.0, westernmost_longitude:0.0, easternmost_longitude:0.0, $

file_quality_index:0, comment:'' }

; loop through the global attributes and load into a structure

for gatt_id=0, file_info.ngatts - 1 do begin

gatt_name = ncdf_attname( nid, gatt_id, /GLOBAL )

case gatt_name of

'Conventions': begin

ncdf_attget, nid, 'Conventions', Conventions, /GLOBAL

global_atts.Conventions = string(Conventions)

end

'DSD_entry_id': begin

ncdf_attget, nid, 'DSD_entry_id', DSD_entry_id, /GLOBAL

global_atts.DSD_entry_id = string(DSD_entry_id)

end

'title': begin

ncdf_attget, nid, 'title', title, /GLOBAL

global_atts.title = string(title)

end

'references': begin

ncdf_attget, nid, 'references', references, /GLOBAL

global_atts.references = string(references)

end

'institution': begin

ncdf_attget, nid, 'institution', institution, /GLOBAL

global_atts.institution = string(institution)

end

'contact': begin

ncdf_attget, nid, 'contact', contact, /GLOBAL

global_atts.contact = string(contact)

end

'institution': begin

ncdf_attget, nid, 'institution', institution, /GLOBAL

global_atts.institution = string(institution)

end

'GDS_version_id': begin

ncdf_attget, nid, 'GDS_version_id', GDS_version_id, /GLOBAL

global_atts.GDS_version_id = string(GDS_version_id)

end

'netcdf_version_id': begin

ncdf_attget, nid, 'netcdf_version_id', netcdf_version_id, /GLOBAL

global_atts.netcdf_version_id = string(netcdf_version_id)

end

'creation_date': begin

ncdf_attget, nid, 'creation_date', creation_date, /GLOBAL

global_atts.creation_date = string(creation_date)

end

'product_version': begin

ncdf_attget, nid, 'product_version', product_version, /GLOBAL

global_atts.product_version = string(product_version)

end

'history': begin

ncdf_attget, nid, 'history', history, /GLOBAL

global_atts.history = string(history)

end

'platform': begin

ncdf_attget, nid, 'platform', platform, /GLOBAL

global_atts.platform = string(platform)

end

'sensor': begin

ncdf_attget, nid, 'sensor', sensor, /GLOBAL

global_atts.sensor = string(sensor)

end

'spatial_resolution': begin

ncdf_attget, nid, 'spatial_resolution', spatial_resolution, /GLOBAL

global_atts.spatial_resolution = string(spatial_resolution)

end

'start_date': begin

ncdf_attget, nid, 'start_date', start_date, /GLOBAL

global_atts.start_date = string(start_date)

end

'start_time': begin

ncdf_attget, nid, 'start_time', start_time, /GLOBAL

global_atts.start_time = string(start_time)

end

'stop_date': begin

ncdf_attget, nid, 'stop_date', stop_date, /GLOBAL

global_atts.stop_date = string(stop_date)

end

'stop_time': begin

ncdf_attget, nid, 'stop_time', stop_time, /GLOBAL

global_atts.stop_time = string(stop_time)

end

'northernmost_latitude': begin

ncdf_attget, nid, 'northernmost_latitude', northernmost_latitude, /GLOBAL

global_atts.northernmost_latitude = northernmost_latitude

end

'southernmost_latitude': begin

ncdf_attget, nid, 'southernmost_latitude', southernmost_latitude, /GLOBAL

global_atts.southernmost_latitude = southernmost_latitude

end

'westernmost_longitude': begin

ncdf_attget, nid, 'westernmost_longitude', westernmost_longitude, /GLOBAL

global_atts.westernmost_longitude = westernmost_longitude

end

'easternmost_longitude': begin

ncdf_attget, nid, 'easternmost_longitude', easternmost_longitude, /GLOBAL

global_atts.easternmost_longitude = easternmost_longitude

end

'file_quality_index': begin

ncdf_attget, nid, 'file_quality_index', file_quality_index, /GLOBAL

global_atts.file_quality_index = file_quality_index

end

'comment': begin

ncdf_attget, nid, 'comment', comment, /GLOBAL

global_atts.comment = string(comment)

end

else: begin

print, ' unknown attribute: ',  gatt_name

end

endcase

endfor

return, global_atts

END

;  Copyright 2005, by the California Institute of Technology.  ALL RIGHTS
;  RESERVED. United States Government Sponsorship acknowledged. Any commercial
;  use must be negotiated with the Office of Technology Transfer at the
;  California Institute of Technology.

; $Id: L2P_driver.pro,v 1.5 2008/05/07 18:51:26 ghrsst_mmr Exp $
; L2P_driver.pro	e. armstrong	Caltech/JPL/NASA

PRO L2P_driver, L2P_file

; ------------------------------------
; SYNOPSIS: 
; Calls read_L2P.pro to read
; the GHRSST L2P netCDF format. 
; All arrays and their attributes are
; read into memory.

; USAGE:
; IDL> .compile L2P_driver
; IDL> .compile read_L2P (may need to compile twice)
; IDL> L2P_driver, <L2P_file>
; ------------------------------------

if n_params() ne 1 then begin
    usage
    stop 
endif

print, ''
print, '      reading L2P file: ' + L2P_file 

; call the file reader
read_L2P,    L2P_file, $,				; only input
	     time, time_atts $				; returned: reference time and attributes
	     lat, lat_atts, $				; latitude and attributes
	     lon, lon_atts, $  				; longitude and attributes
	     sst, sst_atts, $				; SST and attributes
	     sst_dtime, sst_dtime_atts, $		; deviation from reference time and attriubtes 
	     sses_bias, sses_bias_atts, $		; SST bias error and attriubtes
	     sses_sd, sses_sd_atts, $			; SST standard dev. error and attributes
	     dt_analysis, dt_analysis_atts, $		; SST/analysis SST difference and attributes
	     ssi, ssi_atts, $				; surface solar irradiance and attributes
	     wind, wind_atts, $				; wind speed and attributes
	     aod, aod_atts, $ 				; aersol optical depth and attributes
	     seaice, seaice_atts, $			; sea ice fraction and attributes
	     ssi_source, ssi_source_atts, $		; source of ssi and attributes
	     wind_source, wind_source_atts, $		; soruce of wind speed and attributes
	     aod_source, aod_source_atts, $		; source of aod and attributes
	     seaice_source, seaice_source_atts, $	; source of sea ice and attributs
	     ssi_sst_dtime, ssi_sst_dtime_atts, $	; time difference between ssi and sst and attributes
	     wind_sst_dtime, wind_sst_dtime_atts,$ 	; DT between wind and sst and attributes
	     aod_sst_dtime, aod_sst_dtime_atts, $	; DT between aod and sst and attributes
	     sat_zen_ang, sat_zen_ang_atts, $ 		; satellite zenith angle and attributes
             reject_flag, reject_flag_atts, $		; rejection flag and attributes
	     conf_flag, conf_flag_atts, $		; confidence flag and attributes
	     proximity_conf, proximity_conf_atts,$ 	; proximity confidence flag and attributes
	     global_atts				; global attributes


; -------------------------------------
; Example of how to use the arrays and
; and metadata. 
; -------------------------------------

; find the missing values in the sst array 
missing_values = where( sst eq sst_atts.FillValue, count)

; scale the SST
sst = sst * sst_atts.scale_factor + sst_atts.add_offset

; set missing values to back to FillValue value
if count ne 0 then begin
    sst[missing_values] = sst_atts.FillValue 
endif

; print out a few things about this file
print, ''
print, ' some details of this file . . .  '
print, ' the northernmost latitude: ', global_atts.northernmost_latitude
print, ' the southernmost latitude: ', global_atts.southernmost_latitude
print, ' the easternmost longitude: ', global_atts.easternmost_longitude
print, ' the westernmost longitude: ', global_atts.westernmost_longitude
print, ''
print, '--> example for ', sst_atts.long_name
print, '--> units are: ', sst_atts.units 
print, '--> scale factor: ', sst_atts.scale_factor
print, '--> add offset: ', sst_atts.add_offset
print, '--> missing values are: ', sst_atts.FillValue 

lat_size = size(lat)  ; determine if 1d or 2d lat/lon array
if lat_size[0] eq 1 then begin
    print, '  AT latitude: ', lat[100]
    print, '  AND longitude: ', lon[100]
    print, '  SST is: ', sst[100]
endif else begin
    print, '  AT latitude: ', lat[100,100]
    print, '  AND longitude: ', lon[100,100]
    print, '  SST is: ', sst[100,100]
endelse

print, '  time of first observation is (sec):  ', time[0]


END

PRO usage
 print, " read L2P netCDF variables and metadata into memory"
 print, " USAGE: "
 print, " IDL> L2P_driver, <L2P_file>
 print, ''
END

## 7.2 The GHRSST Match-Up Database

### 7.2.1  Overview

The development of GHRSST-PP system has strengthened the need for the intercomparison of the available satellite sea surface temperature products and the estimation of the various sensor error statistics, especially when adressing issues such as sensor merging into analysis systems. In situ data have proved to be a reliable independant source to compare these products and sensors to each other. Satellite and in situ measurements coincident in time (typically less than 6 hours time difference) and space (typically less than 25 km distance) are refered as match-ups and can be extracted in real or near real-time on a systematic basis to perform continuous control of the sensors and retrieval algorithms.

To serve that purpose, a database (MDB) providing satellite to in situ match-ups was set up in the frame of ESA funded Medspiration project, relying within an integrated framework on Coriolis system (for the worlwide collection and provision of in situ sea temperature and salinity data from GTS, Argo,etc..., http://www.coriolis.eu.org) and Medspiration data archive (the european node to GHRSST-PP system, http://www.medspiration.org), both hosted at Ifremer, Brest, France. The strength of having a single source for in situ data is to ensure that all match-ups are consistent together since they have been processed in the same manner with the same in situ data, each of them with the same level of quality and following consistent control procedures; respective satellite sensor error statistics can then be estimated with better confidence.

The MDB service currently set up offers to users periodic match-up data files for each Medspiration GHRSST datasets in netCDF format, as well as an online extraction interface to perform more constrained queries (using time/space criteria, selecting the data sources to consider, using selection filters,..). It can be accessed at the following place :

http://www.medspiration.org/tools/mdb/

### 7.2.2 Future plans

The scope of the match-up database has been limited so far to the GHRSST products delivered by the European DAC (Medspiration project). Future plans mostly focus on extending this scope to all other data sources  (both satellite and in situ) and adding new high-level functionnalities to the service :

- processing and delivering match-ups for all other GHRSST datasets

- including new sources of in situ measurements (if not handled by Coriolis database), which may include for instance in situ radiometer data

- complementing the database with historical match-ups (provided by other existing MDBs such as for MODIS, AMSRE, TMI, METOP, AVHRR,....) or additional ancillary information (for better quality control or stratification of the MDB)

- implementing automatic procedures to trigger alarms when anomalies or drifting of the satellite sensors are detected by comparison with in situ data

- implementing automatic and independant computation of SSES and providing periodically updated values

For more information on MDB content, processign details or data format, please refer to the MDB user manual appendice.

## 7.3 High Resolution Diagnostic Data Sets (HRDDS)

### 7.3.1 Overview

The GHRSST-PP High Resolution Diagnostic Data Set is an online interactive archive and database system designed to allow fast and easy inter-comparison of all types of SST products.

The system features two main components. Firstly, a dedicated web portal, hosted at the National Oceanography Centre, Southampton (United Kingdom), that users may perform a host of interactive analysis through the HR-DDS database to which it is connected. Secondly, a large archive of GHRSST and other SST subsets that are made available via FTP and OPeNDAP.

The HR-DDS was initially constructed for the ESA funded MEDSPIRATION (http://www.medspiration.org) project, the European contribution to GHRSST. It has since been expanded to encompass the entire GHRSST project. It has received additional finding from the EU MERSEA (http://www.mersea.eu.org) project and also from the UK’s Met Office through the National Centre for Ocean Forecasting (NCOF http://www.ncof.co.uk).

The HR-DDS ingests nearly all GHRSST SST products and many additional SST products from outside the project. Every data file provided is analysed to find SST observations at all of approximately 250 HR-DDS sites. These HR-DDS sites are geographic regions typically 2( by 2( is size, located over regions of interesting oceanographic or atmospheric conditions, areas with known in situ observations or regions representative of typical oceanic conditions. Additionally, many site are located in Polar Regions to aid validation of SST products in the difficult conditions prevalent at those latitudes.

Every time an SST product contains an observation at one of these HR-DDS sites and new HR-DDS granule is produced. This is a subset of the original file with only the data for that location. This data is always interpolated onto a 0.01( by 0.01( degree regular grid through the nearest neighbour technique. Any absence of observation is maintained in the new grid. These files maintain the format of the source file, other that the grid specification as described.

Each of these granules is also analysed at creation to create a statistical representation of each field that is then entered into the HR-DDS database. These statistics include the mean, median, skew, kurtosis, standard deviation, maximum and minimum values for the field. The statistics are calculated for the entire field, and for a smaller 0.05( by 0.05( region known as the centre area (although this region is not exactly in the centre for each HR-DDS site – typically when that area my be land). All these statistics are then recomputed only for pixels of the highest quality level of each product. These statistics form a broadly representative sample of each HR-DDS granule and are very quick to analyse. At the time of writing the HR-DDS database contains over 300,000,000 statistics from over 2,000,000 HR-DDS granules.

### 7.3.2 The HR-DDS portal

The main feature of the HR-DDS system is the interactive web portal, which provides many features for the analysis of SST data. The portal is accessible at the URL http://www.hrdds.net.

The front page of the HR-DDS portal presents a global SST field, usually obtained from the previous days OSTIA analysis, a GHRSST L4 product. Superimposed on this image are approximately 250 rectangles. These represent the location of the HR-DDS sites, an example is shown in Figure 1.

Figure A7.1 The location of the HR-DDS sites. This image is taken from the HR-DDS web portal front page.  Red sites indicate the likely presence of in situ observations, white and yellow sites have been added by special request, purple sites indicate coasts or lakes. Blue sites have been added for the ocean colour communities.

The user may hold the mouse over any of these sites to see its exact location and name.  Users of the portal may now perform two tasks. They may select to zoom in to a region by clicking anywhere other than on an HR-DDS site, or they may choose to begin analysing the data at an HR-DDS site by clicking on that site.

There is a menu bar to the left of the website that is always available. This menu bar contains links to this user guide, ‘walkthrough’ demonstrations, descriptions of the data within the system, methods of downloading the data, user registration and configuration options and much more.

### 7.3.3 Time series analysis

Users may enter the time series analysis pages by clicking on any site on the front page. They are then presented with a dynamically generated graph showing the mean SST of every HR-DDS granule over that site for the last 14 days. An example of this type of image is given in Figure 2. A detailed and up to date legend is provided by the website.

Figure A7.2 An example time series produced by the HR-DDS website. This is an example for a site in the Western Approaches. A legend is available on the website, directly below this image. Colour represents an instrument type, and each shape represents a product type.

Above the plot are six small hyperlinks allowing the user to change the time frame of the image. Options are to move back or forward by on day, one month or one year. These are the only controls on the page that do not require the user to hit the ‘Select and Plot’ button at the bottom of the page

There are also many other controls the user may employ to modify the appearance of this plot and also control the data that is included in the plot. After modifying the value of these fields, the user must hit the ‘Select and Plot’ button at the bottom of the page to inform the website you have finished and wish to view the results. These are described bellow:

- Y-axis minimum. The user may enter any value into this box, which will define the lower limit of the Y-axis of the graph. Entering the word ‘auto’ will instruct the website to automatically select an appropriate minimum value. No units should be entered into this box, only numerical values or the word ‘auto’. To make the change user must hit the ‘Select and Plot’ button at the bottom of the page.

- Y-axis maximum. Same as Y-axis minimum except it controls the maximum value of the plot. Note: To reverse the Y-axis, simply enter the minimum value you wish into the maximum value box, and vice versa.

- Minimum valid data coverage. Enter into this box the minimum percentage of SST coverage you require of each granule in order to include it in the plot. For example, to restrict you analysis to data with a lower risk of cloud contamination, entre a higher value.

- Parameter type. This is the variable you wish to view on the Y-axis. The default parameter is sea surface temperature. At the time of writing nearly twenty other variables are available to plot, although no data source includes every parameter.

- Statistical operator. This defines the statistical value of each field you wish to plot, the default is mean. Therefore by default the mean sea surface temperature of each granule is shown in an unmodified plot.

- Coverage and quality. This option controls whether the statistic shown on the plot is derived from the centre area (0.05( by 0.05() or all the area (typically 2( by 2(), and whether the statistic is derived from all available observations or just high quality observations.

- Error estimation. Some statistics in the database have an associated error estimate (for example, the SSES_standard_deviation_error of the L2P format). By default these are represented as horizontal error bars on appropriate points. User may disable with feature by selecting no error estimation in this option list.

- Bias correction. Some statistics in the database have an associated error correction (for example, the SSES_bias_error of the L2P format). By default values are applied to appropriate points. User may disable with feature by selecting no bias correction in this option list.

- In situ observations. Recently the HR-DDS has included in situ observations of some parameters in the database. By default these are not displayed, however to view these observations you may select with in situ observations from this option list.

- Select your HRDDS site. This feature allows you to quickly view a plot with the same configuration by with data from a different HR-DDS site.

- Start date. This defines the date of the earliest data you wish to include. By default this will be set to 14 days before the current date.

- End date. This selects the date of the latest data you wish to include in the plot. By default it is the current date.

- Select and Plot. This activates any change you have made to the plot configuration.

Holding the mouse over any of the points on the plot will reveal more information about that point. The actual Y-axis value is included in this information along with a description of the sensor system and instrument used.

From here the user may either elect to produce a spatial inter-comparison of the data for a specific day, view an image of the field containing the data for which a statistic has been derived or produce a multivariate scatter plot.

To view an image of the data used to produce the point on the plot the user need only to click on that point. An image of the data is produced in real time form the HR-DDS granule used to generate the statistics.

Important note: The time series analysis pages show sea surface temperature in degrees Celcius without exception. The data within the HR-DDS granule will however usually be recorded in kelvin.

### 7.3.4 CSV (comma separated value) pages

From the time series analysis pages, a user may select to download the data from which the plot was generated by clicking on ‘Data Access’ in the left hand menu and then clicking on ‘CSV Data Access’. The user then view a page containing in CSV format the data used to generate the plot. This is useful as CSV data may easily be imported into scientific analysis applications.

For more simplistic analysis, a simple spreadsheet application will typically be able to read this data. When using a spreadsheet program with this data is important to remember that the first line of this data is a header.

The page contains some HTML so it is wise to copy the page from your web browser to a simple text editor instead of attempting to save the page from the browser itself. The CSV data contains the following columns (delimited, of course, by a comma):

- Source name.  This is the internal HR-DDS code for the dataset. These codes are identical to or closely resemble the GHRSST data code. The meaning of each is given in the product description section of the HR-DDS website.

- Value. This is the numerical value appearing on the Y-axis of the time series analysis page. Note. If the parameter you are viewing is sea surface temperature the value you download will be in Kelvin, not degrees Celsius as shown on the time series analysis plot. In fact all sea surface temperatures returned from the website will be given in degrees Celsius with the exception of the CSV data. This is due to various user requests.

- Observation start time. This is the observation time of the oldest observation in the HR-DDS granule from which the point was generated

- Observation end time. This is the observation time of the youngest observation in the HR-DDS granule form which the point was generated.

- Variable Name. The name of the parameter in the CSV data, for example sea surface temperature, or wind speed.

- Statistical Operator.  The statistical value of the field in the CSV data, for example the mean or the standard deviation.

- Quality Level. The coverage area and quality level of the data included in the analysis, denoted by the area first and then the quality level. For example area all describes data from the entire HR-DDS granule are at all quality levels.

- Type. The type of product, for example a swath satellite product or an analysis level 4 product.

### 7.3.5 FTP and OPeNDAP access

User may, form the any site on the page, enter the HR-DDS archive by clicking in ‘Data Access’ and then either ‘OPeNDAP Data Access’ or ‘FTP Data Access’.

Users within UK Universities and Natural Environment Research Council centres should be able to use the passive FTP mode. All other users will have to configure their FTP client to use the port FTP mode. Almost every FTP client will make this change automatically.

Users may also access the FTP archive from the command line by anonymous FTP by connecting to the server medserve.noc.soton.ac.uk. Most users (other than those at Natural Environment Research Council centres an institutions) will probably have to deactivate the FTP passive mode to use the site. Once logged in, the user must type ‘passive’ and enter it. The archive is divided into data and metadata directories. All HR-DDS granules are located within the data/hrdds/ directory of the server. Within this directory, all granules are organised by year, day of year and finally site code. The OPeNDAP archive is organised in exactly the same way.

All HR-DDS granules are compressed with the bzip2 compression utility.

### 7.3.6 Multivariate scatter plots

Users may, from the time series analysis page, select to produce a multivariate plot. This plot presents the same Y-axis as the time series plot, but wit the X-axis being replaced by another parameter. By default this parameter is wind speed.  The controls for this plot are very similar to the time series analysis plot, with the following additions, specifically for the X-axis.

- X-axis minimum. The user may enter any value into this box, which will define the lower limit of the X-axis of the graph. Entering the word ‘auto’ will instruct the website to automatically select an appropriate minimum value. No units should be entered into this box, only numerical values or the word ‘auto’. To make the change user must hit the ‘Select and Plot’ button at the bottom of the page.

- X-axis maximum. Same as X-axis minimum except it controls the maximum value of the plot. Note: To reverse the X-axis, simply enter the minimum value you wish into the maximum value box, and vice versa.

- Parameter type. This is the variable you wish to view on the Y-axis. The default parameter is sea surface temperature. At the time of writing nearly twenty other variables are available to plot, although no data source includes every parameter.

- Statistical operator. This defines the statistical value of each field you wish to plot, the default is mean. Therefore by default the mean sea surface temperature of each granule is shown in an unmodified plot.

- Coverage and quality. This option controls whether the statistic show on the plot is derived from the centre area (0.05( by 0.05() or all the area (typically 2( by 2(), and whether the statistic is derived from all available observations or just high quality observations.

An example of a multivariate scatter plot is show in Figure 3.

Figure A7.3 An example of a multivariate scatter plot produced by the HR-DDS website.

There are some important notes with regard to the multivariate scatter plots. Firstly, points are only displayed if the source HR-DDS granule contains both parameters being plotted. For example, as the OSTIA product contains only SST, it will not appear on the plot. Secondly, selecting different quality levels for each axis may not produce sensible results. This is not an error, it is simply a product of the fact that some ancillary products may not exist in different quality levels.

To active the multivariate scatter plot users must click on the synonymous link next the ‘Select and Plot’ button on the time series analysis page. Like the time series analysis page, users may also quickly choose to move forward or backwards in time by one day, one month or one year using the links above the image.

### 7.3.7 Quick look image

By clicking on any point in either a time series analysis plot or a multivariate scatter plot the user is presented with a quick look image. When activated form a time series analysis plot the users will observe the website fade into the background and a new virtual window appear containing the image requested. An example of this is shown in Figure 4.

Figure A7.4 Screenshot of a quick look image produced by clicking on a point in a time series analysis page.

The image is produced dynamically and in real time from the HR-DDS granule. The scale use is calculated form the maximum and minimum values of that parameter at that HR-DDS site for all products for the last seven days. White areas denote a missing value in the field, for example as caused by cloud, land, rain or some other event not allowing a value to exist.

The field show is the field being viewed on the time series analysis plot, or the Y-axis of the multivariate scatter plot. The quick look image also shows some information about the point in question. For example, the sensor and platform name (if there are inappropriate, a null value is displayed), the name of the original data provided, and a description of the type of sea surface temperature product from which the value derives.

Users may click on the left half of the image to view the chronologically previous image available for that parameter at the site. Similarly the may click on the right half of the image to view the chronologically next image. They may also click on the ‘CLOSE X’ button, or press the ‘esc’ key to return to the time series analysis or multivariate scatter plot page from which they came.

### 7.3.8 Spatial comparison page

From the quick look image of the time series analysis plot there is a link allowing users to enter the spatial comparison page. In this page the sea surface temperature of all the HR-DDS granules at that site for that data are show. The minimum coverage value is taken from the time series analysis page. An example of this is shown in Figure 5.

Figure A7.5 An example of a spatial comparison page.

The following controls are available on the spatial comparison page, all of which require the user to click on the ‘Select and Plot’ button in order to active:

- Maximum. This value controls the maximum value of the colour scale for all the images on the spatial comparison page. Entering the word ‘auto’ will require the HR-RRD website to select an appropriate value automatically.

- Minimum. This value controls the minimum value of the colour scale for all the images on the spatial comparison page. Entering the word ‘auto’ will require the HR-RRD website to select an appropriate value automatically.

- Minimum coverage percentage. The minimum percentage of area covered by the viewing parameter in order to be displayed on the page.

Additionally, before the array of images, there are links to move the data of the displayed either backward of forwards by one day, one month or one year.

Each image shows a colour scale and a title. The title indicated the GHRSST / HR-DDS code of the source data, and also the start time of the granule in UTC. By clicking on any of the images the user may view anther quick look image, or zoomed image of the field. From this quick look image there is a link to the anomaly analysis page for that image.

### 7.3.9 Anomaly analysis page

The anomaly analysis page shows a detailed comparison of the image selected to all the other data available at that site for that day. The image selected is the one that was clicked on in order to enter this page. The page consists of four columns of images as exemplified by

Figure 6 An Figure A7.6 Example of an anomaly analysis page.

The first (left) column shows the images that are being compared to the selected image. If the user holds the mouse over one of these images the mean and standard deviation of the observations in that image are shown as a popup. The user may also click on the image to reveal a zoomed quick look image, the user may click on the right side of this image to view the image to which this image will be compared to.

The second column shows the histogram of the differences between the image in the first column and the image selected form the spatial comparison page. This histogram is normalised on the Y-axis. Holding the mouse over the histogram will reveal the mean, standard deviation and mean to variance ratio of the differences of the two data sets. Clicking in the histogram will display a larger version of the histogram. The maximum and minimum difference the histogram shows is set to +3 and -3 respectively.

The third column shows the actual difference between the fields. The minimum and maximum difference is set to -1.5 and +1.5 respectively. The image shown is the data in the first column less the data selected from the spatial comparison page. Holding the mouse over the image will reveal the mean, standard deviation and mean to variance ratio of the differences of the two data sets. Clicking on the image will open a new quick look image virtual window. The user may click on the right hand side of that image to reverse the colour scale of the zoomed difference plot.

The forth (right) column shows the X Y scatter plot of the differences between the two datasets. Holding the mouse over the image will show the correlation coefficient of the two datasets.

You may choose to modify the minimum valid coverage percentage value for the anomaly analysis page by entering a different value into the appropriate box at the top of the page. To activate the change the user must click on the ‘Select and Plot’ button.

The user may download an image of the data to which all the other datasets are being compared by clicking on the link at the top of the page just under the minimum valid coverage percentage box.

### 7.3.10 Registered user services

Users may register for additional services by selecting ‘Users’ and then register from the menu on the left side of the web site. Follow the instructions on the page to register.

Registered users have access to many additional features on the HR-DDS website. The registered user homepage is similar to the normal front page of the HR-DDS website, but with a number of configurable options and additional links.

Below the site selection map are three links which link to the last time series analysis, spatial comparison page and anomaly analysis page viewed by the user. These links are automatically updated by the HR-DDS system every time a new page is viewed.

There are also several options for configuring the way plots are produced by the HR-DDS website. Users may define the following default parameters:

- To enable or disable the application of bias estimates on the time series analysis plots

- To enable or disable the display of vertical error bars on the time serried analysis plots

- The default coverage and quality levels shown on time series analysis plots.

- The number of days to plot in a time series analysis plot.

- The minimum valid data percentage required in order to include data from a particular HR-DDS granule.

To record these values the user must click on the ‘Change and Store’ button of their home page. All these configurable default parameters are overridden when a user changes them on an actual plot.

Users must register via the ‘Users’ and ‘Register’ tab of the left hand menu. Users should follow the up-to-date instructions on the web site in order to register correctly.

### 7.3.11 MyDDSettes

MyDDSettes are dynamically generated bookmarks stored on the HR-DDS server, which point to a time series analysis, multivariate scatter plot, spatial comparison page or anomaly analysis page. Registered users will be able to create these MyDDSettes by clinking on the link at the bottom of the page. Only logged in registered users will be able to view this link.

To create a MyDDSette, users click on this link are then enter a brief title and description of the page they are selecting to record.

These may be reviewed, accessed and deleted form the user’s home page on the HR-DDS website, bellow the plot configuration section. Selecting ‘Home’ and then ‘My HR-DDS’ from the menu on the right allows users to access this home page. Users must have previously logged by clicking on the  ‘Users’ and ‘Log in’ section of the left hand menu.

The MyDDSettes are listed with the following information:

- Title. The title given to the MyDDSette at the time of creation.

- Description. This is the description of the MyDDSettes given at the time of creation.

- Type. The type of data plot recorded in the MyDDSette, e.g. a time series analysis.

- Site code. The HR-DS code for the HR-DDS site that the MyDDSette referred to.

- Delete. Users may click on this link to remove the MyDDSette

### 7.3.12 Reporting bugs and suggesting changes

Users (who do not have to be registered) may report a bug or problem with any page by selecting ‘Help’ and then ‘Report Bug’ form the left hand menu. Users may enter a description of the problem but DO NOT have to report what page the error occurred on, that has already been recorded by the HR-DDS site.

Users may also suggest a change (or the addition of a feature) on any page by selecting ‘Help’ and ‘Suggest a change’ from the left hand menu on the website Users DO NOT need to not describe the page they are referring to, that has already been recorded by the HR-DDS system

### 7.3.13 Accessibility options

In accordance with European Law the HR-DDS website may be forced to use larger bolder fonts by the user, for reasons of impaired vision. This option is available form the ‘Help’ section of the left hand menu by clicking on the ‘Larger Text’ section.

### 7.3.14 HR-DDS file format

All HR-DDS granules are produced in netCDF format and are CF-1.0 compliant. When data are supplied that are not consistent with the GHRSST data specifications, the HR-DDS system converts these files into a pseudo GHRSST format. The output HR-DDS granule is extremely similar (or identical) to an HR-DDS granule form a GHRSST source.

See the GHRSST product user manual for an exact description of the GHTSST formats.

The HR-DDS granules are a subset of the data from which they were generated. As such they usually maintain the format of the original data file with the exception of the grid, which is always 0.01( by 0.01( in resolution and of a regular cylindrical projection.

GHRSST compliant L2P, L3P and L4 products (and their associated Core products) maintain almost the exact format of their original data, with the exception of changes in attributes due to the smaller geographical area of the data. The GHRSST example software used to read GRIDDED L2P files will be able to read HR-DDS granules.

Files that contain a small number of multiple time frames are split into separate HR-DDS granules. For example, the REMSS AMSRE L2PCore product contains one layer of data for ascending orbits and another layer for descending orbits. The HR-DDS system will produce two distinct HR-DDS granules at most sites in this instance, one for each layer. This is useful as the observations are typically 12 hours apart.

Files from the CORIOLIS in situ data set may have essentially one layer for each observation, in this case the HR-DDS system splits data up into 1 hour sections and produced an HR-DDS granule for each of these sections. This allows the diurnal signal to be recorded. Additionally, these data are converted into a pseudo L2PCore format by the HR-DDS system. Internally, the system regards them as AVHRR-GAC compliant data.

Non-compliant analysis datasets are converted into a pseudo GHRSST L4 format prior to processing. The output HR-DDS granule represents this change.

### 7.3.15 HR-DDS file name convention

The HR-DDS filename convention is as follows:

HRDDS-<data>T<time>Z-<product_code>-<RDAC>-<site_code>-<site_name>-<HRDDS_software_version>.nc.bz2

Where:

- <data> is a YYYYMMSS format data (e.g. 20010101 for 1st January 2001)

- <time> is a HHMMSS format time string (e.g. 060000 for 6AM – all times are in UTC)

- <product_code>  is the GHRSSR code for that product (e.g. SEVIRI_SST for data from the EUMETSAT SEVIRI instrument)

- <RDAC> is the GHRSST (or other) data provider (e.g. EUR for the MEDSPIRATION project)

- <site_code> is the code of the HR-DDS site (e.g. mfr002 for the Gulf of Lion MeteoFrance buoy site)

- <site_name> is the name of the HR-DDS site (e.g. UKMO_Celtic_Sea_62081, if at the end of the site name there is a 5 digit numerical code this may be interpreted as the WMO ID of an in situ observing station located at the centre of the HR-DDS site.)

- <HRDDS_software_version> is the version of the HR-DDS software used to generate the HR-DDS granule.

The following is an example of a valid HR-DDS granule name:

HRDDS-20080510T131900Z-NAR18_SST-EUR-ukm002-UKMO_Celtic_Sea_62081-v3.nc.bz2.

### 7.3.16 FAQ

1) Where can I get a more detailed description of data formats?

Answer: The HR-DDS data formats are compliant with the GHRSST format specification. See the documentation section of the GHRSST website for more information (http://www.ghrsst-pp.org)

2) What products are included in the HR-DDS?

Answer: A complete product description list is available at the HR-DDS website under the ‘Document’ section of the left hand menu

3) How can I suggest a data source or a site?

Answer: We can add a site in under a minute, and data will populate it instantly. Although at the moment we cannot guarantee when historical data will be added to the site. Email Dave Poulter at djsp@soton.ac.uk and suggest a site! To add a data source takes a bit more time, in the order of days, but feel free to email and request it!

4) Where can I get regular updates?

Answer: The HR-DDS provides regular updates via RSS, use your browser to subscribe form any page on the HR-DDS website.

# 8.0 SST definitions

As SST is not a simple measurement defined at one depth, the following definitions have been put together for the GHRSST project.

- The Interface SST (SSTint)

SSTint is a theoretical temperature at the precise air-sea interface. It represents the hypothetical temperature of the topmost layer of the ocean water and could be thought of as an even mix of water and air molecules. SSTint is of no practical use because it cannot be measured using current technology.

- The Skin SST (SSTskin)

SSTskin is defined as the radiometric skin temperature measured by an infrared radiometer operating in the 10-12 µm spectral waveband. As such, it represents the actual temperature of the water at a depth of approximately 10-20 µm. This definition is chosen for consistency with the majority of infrared satellite and ship mounted radiometer measurements. SSTskin measurements are subject to a large potential diurnal cycle including cool skin layer effects (especially at night under clear skies and low wind speed conditions) and warm layer effects in the daytime (not shown in Figure 1).  SSTskin will be similar to the red 1mm SSTdepth approximation shown in Figure 2.

Figure A8.1 Schematic diagram showing (a) idealised night-time vertical temperature deviations from SSTfnd and (b) idealised day-time vertical temperature deviations from SSTfnd in the upper ocean.

- The subskin SST (SSTsubskin)

SSTsubskin represents the temperature at the base of the thermal skin layer. The difference between SSTint and SSTsubskin is related to the net flux of heat through the thermal skin layer. For practical purposes, SSTsubskin can be well approximated to the measurement of surface temperature by a microwave radiometer operating in the 6-11 GHz frequency range, but the relationship is neither direct nor invariant to changing physical conditions or to the specific geometry of the microwave measurements. SSTskin will be similar to the red 1mm SSTdepth approximation shown in Figure 2.

- The sea temperature at depth (SSTdepth)

All measurements of water temperature beneath the SSTsubskin are obtained from a wide variety of sensors such as drifting buoys having single temperature sensors attached to their hull, moored buoys that sometimes include deep thermistor chains at depths ranging from a few meters to a few thousand meters, thermosalinograph (TSG) systems aboard ships recording at a fixed depth while the vessel is underway, Conductivity Temperature and Depth (CTD) systems providing detailed vertical profiles of the thermohaline structure used during hydrographic surveys and to considerable depths of several thousand meters and various expendable bathythermograph systems (XBT).  In all cases, these temperature observations are distinct from those obtained using remote sensing techniques and measurements at a given depth arguably should be referred to as ‘sea temperature’ (ST) qualified by a depth in meters rather than sea surface temperatures.  The situation is complicated further when one considers ocean model outputs for which the SST may be the mean SST over a layer of the ocean several tens of meters thick.

SSTdepth or SST(z) is the terminology adopted by GHRSST-PP to represent an in situ measurement near the surface of the ocean that is typically reported simply as SST or "bulk" SST. For example SST6m would refer to an SST measurement made at a depth of 6m.  Figure 2 demonstrated the need for introducing the new terminology in the upper 5m of the ocean surface as SSTdepth has magnitude and phase differences depending on the precise depth.  Without a clear statement of the precise depth at which the SST measurement was made, and the circumstances surrounding the measurement, such a sample lacks the information needed for comparison with, or validation of satellite-derived estimates of SST using other data sources.  The terminology has been introduced to encourage the reporting of depth (z) along with the temperature.

- The diurnal cycle/variation of SST (DV)

A diurnal cycle refers to changes in vertical and horizontal distribution of SST throughout a 24 hour period and thus includes warm stratified layers and cool skin effects.  Cool skin effects are typically more pronounced at night due to radiative cooling of the sea surface but may also occur during the day when the wind is light following a significant rainfall that may leave a cool freshwater layer on the surface of the ocean.

Warm layer effects are associated with environmental conditions characterised by low wind speed and strong insolation. A warm layer readily forms under such conditions effectively decoupling the surface layers (typically 0.1-3m deep) from the water beneath.

- The Foundation SST (SSTfnd)

The foundation SST, SSTfnd, is defined as the temperature of the water column free of diurnal temperature variability or equal to the SSTsubskin in the absence of any diurnal signal.  It is named to indicate that it is the foundation temperature from which the growth of the diurnal thermocline develops each day.  SSTfnd provides a connection with historical “bulk” SST measurements typically used as representative of the oceanic mixed layer temperature. This definition was adopted by GHRSST-PP at the Third GHRSST-PP Workshop (Donlon, 2003b) to provide a more precise, well-defined quantity than previous loosely defined “bulk” temperature quantities and consequently, a better representation of the mixed layer temperature.  The SSTfnd product provides an SST that is free of any diurnal variations (daytime warming or nocturnal cooling).  In general, SSTfnd will be similar to a night time minimum or pre-dawn value at depths of ~1-5 m, but some differences could exist.  Only in situ contact thermometry is able to measure SSTfnd.  SSTfnd cannot be directly measured using either microwave or infrared satellite instruments. Analysis procedures must be used to estimate the SSTfnd from radiometric measurements of SSTskin and SSTsubskin.

# 9.0 RDACs, GDAC, and the LTSRF

For distribution of the GHRSST –PP a distributed data system was setup in which the data processing operations that are necessary to generate and distribute high resolution SST data sets having global coverage are shared by an international group of Regional Data Assembly Centers (RDACs). RDACs ingest, quality control and merge existing satellite and in situ SST data sources that are then used together to generate quality-controlled SST data products to the same specification (called L2P products), in real-time.  The RDACs also may generate Level 3 (L3) and Level 4  (L4) products. RDAC data products are then assembled together at Global Data Analysis Centers (GDAC) where they are integrated, catalogued, and served to users for 30 days.  After 30 days, the data are all sent to the Long Term Stewardship and Reanalysis Facility (LTSRF), where they are archived, documented, and served in perpetuity. For a schematic showing the relationship between the RDACS, GDAC, and LTSRF, see Figure 3.

## 9. 1 RDACs

GHRSST-PP RDAC centers must implement data processing procedures that account for specific aspects of regional coverage input data products (e.g., geostationary imagers).  RDAC must also provide additional data products and services to satisfy regional user requirements (e.g., regionally specific analyzed data products or ultra-high resolution data products) that will require research and development of new analysis, quality control, and data provision procedures. GHRSST-PP global and regional coverage SST data products are now produced by GHRSST-PP RDACs in Australia, Japan, the USA and Europe.

## 9. 2 GDAC

RDAC SST Products are passed in near real-time to operational GHRSST-PP GDAC Global Data Assembly Centers (GDACs) where the RDAC products are integrated together and served to the global application community. GDACs play an essential role in quality control and data management.  See Figure A9.1 for the relationship between the RDACs and the GDAC.

## 9. 3 LTSRF

The  GHRSST Long Term Stewardship and Reanalysis Facility (LTSRF) is maintained at NOAA’s National Oceanographic Data Center (NODC), in Silver Spring, Maryland, USA.  The LTSRF receives all data produced by GHRSST and submitted to the GDAC. After 30 days, the data are sent from the GDAC to the NODC LTSRF, where final metadata records are completed and the data maintained in the

Figure A9.1: Shows the relationship between Regional Data Assembly Centers (RDACs), the Global Data Assembly Center (GDAC), and the Long Term Stewardship and Reanalysis Facility (LTSRF)

# 10.0 netCDF Structure

## 10.1 Why use netCDF?

The GHRSST-PP Science Team chose netCDF in preference to a custom binary format as this had already been adopted for the Data Sharing Pilot project within GODAE. While custom binary formats have the advantage of minimal size and fast I/O, they tend to suffer from documentation and portability problems. In contrast, netCDF files are self describing - meaning that software packages can directly read the data and determine its structure, the variable names and essential metadata such as the units. The self-describing aspect of netCDF file format means that the information needed to ensure accurate work by reducing the incidence of read errors is available with the data itself. netCDF files and be read and generated using a variety of different languages including Fortran, C/C++, JAVA or PERL. Most importantly, data visualisation and analysis packages (e.g. FERRET, IDL, MATLAB) can directly read netCDF files.  Although there is an initial learning curve for users new to netCDF, the high efficiency when reading netCDF files and ability to store and access multiple data means that ultimately more time for analysing data and addressing the application of GHRSST-PP data products rather than coding interfaces to a whole series of custom binary formats (as is currently the case).  Finally, netCDF is a preferred format for the Live Access Server (LAS) and OPeNDAP systems that provide easy on-line access to data and real-time data visualisation.

In summary, the advantages of netCDF files are:

- NetCDF is used extensively in the atmospheric and oceanic science communities.

- NetCDF is a portable self-describing binary data format.

- NetCDF is network-transparent, meaning that it can be accessed by computers that store integers, characters and floating-point numbers in different ways.

- NetCDF provides direct-access: a small subset of a large dataset may be accessed efficiently, without first reading through all the preceding data.

- NetCDF is appendable: data can be appended to a netCDF dataset along one dimension without copying the dataset or redefining its structure.

- NetCDF datasets can be read and written in a number of languages, these include C, C++, FORTRAN, IDL, Python, Perl, and Java.

- The different language implementations are freely available from the UNIDATA ftp area (ftp://ftp.unidata.ucar.edu/pub/netcdf/) or from other mirror sites (http://www.unidata.ucar.edu/packages/netcdf/mirrors.html) .

- Several graphics packages support netCDF input, making it very easy to display and analyse netCDF datasets. For instance FERRET (http://ferret.wrc.noaa.gov/Ferret/) and CDAT (http://esg.llnl.gov/cdat/) provide both command line and graphical user interfaces for displaying and analysing gridded data.

- NetCDF is completely and methodically documented in UNIDATA's NetCDF User's Guide (http://www.unidata.ucar.edu/packages/netcdf/guide.txn_toc.html) .

- Several groups have defined conventions	 (http://www.unidata.ucar.edu/packages/netcdf/conventions.html) for netCDF files, to enable the exchange of data. GHRSST-PP has adopted the Climate and Forecasting (CF) conventions (http://badc.nerc.ac.uk/help/formats/netcdf/index_cf.html) for netCDF data.

## 10.2  NetCDF and CF conventions

Climate and Forecast (CF) metadata conventions are guidelines and recommendations as to where to put information within a netCDF file, and they provide advice as to what type of information you might want to include. CF conventions allow the creator of the dataset to include information about the data and the dataset itself (metadata) in a structured way, which makes it easier for other users to retrieve the information. We have more information and some examples of CF conventions (http://badc.nerc.ac.uk/help/formats/netcdf/index_cf.html) as they are used in GHRSST-PP datasets. The global attributes describe the more general properties and origins of the dataset.

## 10.3 What's in a netCDF file?

A very simple example of a netCDF file with CF conventions applied is available at http://badc.nerc.ac.uk/help/formats/netcdf/nc_example.html . A netCDF dataset (the filename ends in .nc) is made up of three basic components:

- variables

- dimensions

- attributes

The variables store the actual data, the dimensions give the relevant dimension information for the variables, and the attributes provide auxiliary information about the variables or the dataset itself. You can study the example netCDF file and see more details of the components in a netCDF dataset. The global attributes can also be added to the netCDF file, following CF conventions.

## 10.4 Reading and writing netCDF

The popularity of netCDF stems from its portability and relative ease of use. Although it is a binary data format the netCDF distribution comes complete with the ncdump utility which produces an ASCII dump of the dataset and thereby provides a quick-look facility. You can also generate netCDF files from ASCII data files using the ncgen utility (see http://badc.nerc.ac.uk/help/formats/netcdf/nc_utilities.html#ncgen).  netCDF datasets are commonly written and read using library routines. The library routines are sensibly named and relatively consistently named across the different language implementations.

## 10.5 netCDF resources

- The main netCDF pages including downloads of netCDF code libraries and documentation and can be found at the UNIDATA site at	 http://my.unidata.ucar.edu/content/software/netcdf/index.html

- Useful help on installing netCDF libraries and utilities can be found at http://badc.nerc.ac.uk/help/formats/netcdf/nc_utilities.html

- A variety of low level example programs (IDL, C, FORTRAN) are available to read netCDF files at	 http://www-c4.ucsd.edu/~cids/software/visual.html.

- A large number of applications Software for Manipulating or Displaying NetCDF Data are available from	 http://www.unidata.ucar.edu/packages/netcdf/utilities.html

- A detailed FAQ for netCDF can be found at	 http://my.unidata.ucar.edu/content/software/netcdf/docs/faq.html

# 11.0 MMR (Master Metadata Repository and search capability)

Each data file or granule consists of two different data files, a satellite data  in netCDF, and a XML-based metadata file. The granule metadata record, known as the File Record (FR) contains XML tags that adhere broadly to the NASA Directory Interchange Format (DIF) format and describe relevant information such as time and geolocation. An additional XML metadata record known as the Data Set Descriptor (DSD) contains product summary information that is created once and updated on an as need basis. Together these metadata records reside in a relational database known as the Master Metadata Repository (MMR) that allows for search and discovery of all GHRSST products including those that do not immediately reside at the GDAC.  A search capability, based on the MMR has been developed and is accessible through the GDAC interface.  The MMR can be accessed from the GDAC at home page at http://ghrsst.jpl.nasa.gov