NEBRASKA CENTRAL RAILROAD COMPANY

SYSTEM SPECIAL INTRUCTIONS

EFFECTIVE AT 02:00, SUNDAY, APRIL 3, 2005

TABLE OF CONTENTS

| Personal Protective Equipment | page 4 |
| --- | --- |
| Rule of the Week | page 4 |
| FRA Track Classifications | page 4 |
| Temporary Changes to Timetable Instructions | page 4 |
| General Order Board, Bulletin Board, and Standard Clock Locations | page 4 |
| Communication with Operations Coordinator | page 5 |
| Position of Main Track Switches | page 5 |
| Reporting Trespassers or Unsafe Motorists | page 5 |
| Road Crossing Conditions | page 6 |
| Electrically Activated Highway Grade Crossing Signals – Indicator Lights | page 6 |
| Locomotive Horsepower Per Ton Requirements | page 6 |
| Remote Control Locomotive Operations | pages 7 & 8 |
| Engineer Certification | page 8 |
| NCRC Crews Operating on Foreign Railroad Properties | page 9 |
| Unit Grain Train Interchange | page 9 |
| Operating Between Stations | page 9 |
| Train Information Document | page 9 |
| Train Make-Up Requirements and Reporting Accuracy | page 10 |
| Handling Company Equipment | page 10 |
| Handling Excessive Height/Width Loads | page 10 |
| Proficiency Testing | page 11 |
| Operating at Restricted Speed | page 11 |
| Enroute Train Inspections | page 11 |
| Other Than Main Track | page 11 |
| Flag Protection | page 11 |
| Response to Red Flags, Fusees, or Torpedoes | page 11 |
| Securing Unattended Locomotives | page 11 |
| Sufficient Number of Handbrakes | page 12 |
| Locomotive Cab Signal testing | page 12 |
| Locomotive Fuel Readings | page 12 |
| Locomotive Fuel Conservation | page 12 |
| Locomotive Cold Weather Instructions | page 12 |
| Winter Operations: Train Handling | page 12 |
| Movements Over Frozen or Snow-Covered Road Crossings | page 13 |
| Heavy Rains / Flash Floods | page 13 |
| Tornado Warning | page 14 |
| RULES ADDITIONS/REVISIONS |  |
| 1.1.2 Alert & Attentive | page 15 |
| 1.1.3 Accidents, Injuries, and Defects | page 15 |
| 1.3.1 Rules, Regulations, and Instructions | page 15 |
| 1.3.2 General Orders | page 15 |
| 1.6.1 Motor Vehicle Driving records | page 15 |
| 5.8.1 Ringing Engine Bell | page 15 |
| 5.8.2 Sounding Whistle | page 15 |
| 6.21 Precautions Against Unusual Conditions | page 16 |
| 7.10 Movement Through Gates and Doorways | page 16 |
| 14.3 Operating with Track Warrants | page 16 |
| 14.4 Occupying Same Track Warrant Limits | page 16 |
| 14.5 Protecting Men or Equipment | page 16 |
| 14.7 Reporting Clear of Limits | page 16 |
| 15.1.1 Changing Address of Track Warrants or Track Bulletins | page 17 |
| 15.2.2 Protection of Non-Railroad Contractors | page 17 |
| 40.14 (Supplement) 14.7 Reporting Clear of Limits | page 17 |
| 42.17 Entering Remote Control Zone | page 17 |
| 81.5.4 Understanding Between Crew Members Before Fouling Track | page 18 |
| 81.7.1 Designated Riding Places | page 18 |
| 81.8.3 Impaired Clearances | page 18 |
| 81.11 Hand Brake | page 18 |
| 82.7 Operating Ground-Throw Switch | page 19 |
| MISC |  |
| Speed Table | page 20 |
| Mile Measurements | page 20 |
| Wind Chill Chart | page 21 |
| Heat Index Table | page 21 |
| NCRC, UPRR and BNSF Contact Numbers | page 22 |
| Emergency Contact Numbers | page 23 |

MISC. SPECIAL INSTRUCTIONS

Personal Protective Equipment

Rio Grande Pacific Corporation (RGPC) railroads have adopted the Union Pacific Railroad Safety Rules.  These include rules related to Personal Protective Equipment.  In addition, RPGC has implemented the following safety policy:

All employees, guests, and contractors who are performing railroad duties or who will be within four (4) feet of either rail of any track, are required to wear a brightly colored, highly reflective safety vest, on the outside of any other clothing.

Rule of the Week

All employees must review the requirements of the Rule of the Week.  Please direct any questions you may have to your immediate supervisor.  You should be prepared to discuss the requirements of the Rule of the Week with your supervisor and/or other Company officers.  Knowledge and application of the Rule of the Week will be included in proficiency testing procedures and safety observations.

FRA Track Classifications

All main tracks are classified as FRA Class II, except Palmer Subdivision main track  classified as FRA Class I.  All tracks other than main tracks on all subdivisions are classified as FRA EXCEPTED track.

Temporary Changes to Timetable Instructions

Information regarding changes to track conditions and other conditions affecting the movement of trains or employee safety will be issued by the appropriate Form B or Form C track bulletin.  Temporary speed restrictions will be issued by a Form A track bulletin or by track warrant.

General Order Board, Bulletin Board and Standard Clock Locations

West Columbus, Grand Island, Operations Coordinator’s Office (Norfolk), General Office (Norfolk)

Communication with Operations Coordinator

Employees are required to report to the Operations Coordinator’s office any information that may affect the overall operation of the railroad.  Communication is to include, but not limited to;

- Time of departure from initial station (time train or equipment departs from first station of TWC Authority), including the number of loads, empties, tonnage and length of train.

- Departure time from any station where train direction has changed.

- Any delays at initial station or enroute.

- Time clear of junctions, clear of main track, or any other reporting locations requested by the Operations Coordinator.

- Locomotive, company vehicle, or other equipment problems encountered.

- Before leaving trains, engines, or other equipment on the main track or on side tracks, employees must receive permission from the Operations Coordinator.

- Advance knowledge of any condition or work to be performed by any department that may affect the daily operation, must be provided as far ahead of time as possible, (M/W work for the next day, locomotives out of service, etc.).

Position of Main Track Switches

When departing from locations where main track switches have been hand operated, or when clearing the main track, the conductor or other responsible employee must communicate with the engineer, confirming that all main track switches have been restored to “normal” position (lined and locked for main track).  In instances where permission has been received to leave a main track switch open, that information must be provided.  Conductors or other responsible employee must complete a Main Track Switch Position Record form for each tour of duty and submit the completed report to the Operations Coordinator’s office.

MOW employees hand operating main track switches must communicate with the Operations Coordinator when switches have been restored to “normal” position and submit a completed Main Track Switch Position form at the end of their tour of duty.

Operations Coordinators will maintain a “Main Track Switch Position Record” in the Operations Coordinators office for all territories dispatched.

Reporting Trespassers or Unsafe Motorists

Whenever trespassers are observed on Company property or train movements encounter a near miss at a public or private road crossing, employees are required to report the incident to the proper authority immediately by the first available means of communication.

Initial notification is to be made to the Operations Coordinator on-duty.  The Operations Coordinator will make the proper notification to law enforcement personnel and Company managers, as well as establishing a written record of the incident.  When a Operations Coordinator is not on-duty, notification is to be made directly to law enforcement personnel and Company managers.

Road Crossing Conditions

All employees must continue to monitor the condition of all road crossings, particularly:

- Signage

- Crossing Surface

- Gates and Lights

- Impaired visibility due to vegetation, OTM, or equipment on the railroad right-of-way or adjacent track(s).

Immediately report any condition that does not comply with rules and/or standards.

Whenever any of the following conditions exists, a 10 MPH speed restriction will apply for all movements over the affected crossing:

- Vegetation on the right-of-way that obstructs the view of the crossing

- Vegetation that obstructs the view of the warning signs or signals on railroad property

- Material placed on the right-of-way that obstructs the view of the crossing

- Broken crossbuck posts

- Missing/damaged crossbuck signs, multi-track number plates, stop signs, yield signs, whistle posts

Note – Signs are considered damaged if they no longer fulfill their intended function.

Note – 10 MPH speed restriction applies until lead locomotive completely occupies crossing.

Note – When the crossing is protected by a properly equipped flagman, the 10 MPH speed restriction will not  apply.

All employees must immediately report malfunctioning automatic crossing warning devices to the Operations Coordinator and to the Signal Department Manager.

Electrically Activated Highway Grade Crossing Signals - Indicator Lights

When white light is visible it indicates power is on.  If white light is not lighted, signals are operating off standby batteries.  Continued operation on batteries can affect signal operation and cause an activation failure (dark signals).  Some locations have 2 additional indicator lights.  Yellow light will flash on and off when signals are operating.  Normally no red light is visible.  If red light is lighted, grade crossing  signals are not functional and no activation of the signals will occur.  If a grade crossing signal failure is observed, report failure immediately to the proper authority.

Locomotive Horsepower Per Ton Requirements

The following table indicates the minimum horsepower required per trailing ton for normal train operations.

| Subdivision | HPPT |
| --- | --- |
| Albion | .50 |
| Cedar Rapids | .50 |
| Norfolk | 1.00 |
| Ord | 1.00 |
| Palmer | .50 |
| Stromsburg | 1.00 |

Remote Control Locomotive Operations

Each employee operating remote control locomotives must be both a certified locomotive engineer and a certified remote control operator. The Railroad provides training for both certifications.

All such employees are required to be familiar with and keep in their possession while on duty, the booklet entitled: “Rules and Instructions for the Operation of Remote Control Locomotive Systems” (revised August 15, 2003).

All other employees must attend a familiarization session so that they understand their roles and responsibilities regarding the Remote Control Operation. Each such employee will also receive a copy of the rules and instruction booklet.

A Remote Control Zone has been established at the following location and is designated by signs posted at each end of the limits. The sign reads:

BEGIN REMOTE CONTROL ZONE:

Norfolk Subdivision:

| Limits | Name | Days of Active Operation | Hours of Active Operation |
| --- | --- | --- | --- |
| MP 47.4-MP 49.69, including all adjacent yard/industrial tracks. | Norfolk Remote Control Zone | Sunday through Saturday | When activated by a Form C Track Bulletin. |

A Remote Control Zone (RCZ) is defined as “any section of track, to include main line and/or yard or industry tracks, the limits of which are designated by General Order or Timetable and/or by posted signs on the right of way, in which a remote control system may operate according to rules established for that purpose.”

An “ACTIVE remote control zone (active RCZ) is a designated Remote Control Zone made active by Track Bulletin.  All employees or contractors who might have occasion to enter the ACTIVE RCZ must have a copy of the track bulletin in their possession.

During the hours and on the days specified above, no one may enter the remote control zone without first contacting the Remote Control Locomotive System-Employee in Charge (RCLS-EIC) – For each tour of duty on which two operator control units (OCU) are used by a single RCL crew, one RCO must be designated as the RCLS-EIC for purposes of controlling entrance of other trains, engines, employees, and contractors into the Remote Control Zone. The crewmembers will jointly determine the RCLS-EIC for that tour of duty and promptly notify the Operations Coordinator or other designated person (s).

If unable to contact the RCLS-EIC during the designated hours, personnel wishing to enter the RCZ must contact the Operations Coordinator on-duty to obtain the needed permission.

Other signage has been posted for information purposes.

At key locations along the right of way, this sign is posted as public information:

REMOTE CONTROL LOCOMOTIVES MAY BE IN USE

THERE MAY BE NO OPERATOR VISIBLE ON LOCOMOTIVE

The following sign has been posted at crossings used exclusively by employees and

contractors:

STOP

REMOTE CONTROL ZONE

PROCEED WITH CAUTION

Remote Control Locomotive Man Down Feature

During Remote Control Locomotive Operations whenever the radio message “NCRC operator down” is broadcast, all employees monitoring the radio frequency must take immediate action as follows;

- If the message is broadcast during a test of RCL equipment, the RCO performing the test must transmit a message identifying himself and that the message was the result of a test.

- When those employees monitoring the appropriate frequency do not hear a “test message” from the RCO, action must be taken to locate the RCO and provide assistance as needed.

Additions to “Rules and Instructions for the Operation of Remote Control Locomotive Systems”

- 1.11  Do not get on or off moving equipment while wearing the OCU.

- 1.12  Before coupling to or moving cars or engines, verify that the cars or engines are properly secured and can be coupled and moved safely.  Make couplings at a speed of not more than 4 MPH.  Always stretch the slack to ensure that all couplings are made before initiating the next movement.

- 2.3  Test locomotive brakes in accordance with UPRR Air Brake & Train Handling Rule 31.6.2.

- Motion Indicator:

  - Locomotive movement in either direction will cause a motion indicator light to be illuminated on the OCU display.

- Overspeed Protection:

  - When a speed greater than 7 MPH has been detected, the throttle is disabled (returns to idle) and the locomotive horn will begin to pulse.  Once the locomotive slows down to less than 6 MPH the system will return to normal operation.

If a speed of 9.5 MPH is detected an emergency brake application will occur.  The fault can be cleared by recovering an EMG penalty.

Engineer Recertification

All locomotive engineers must be recertified (licensed) every three (3) years.  Beginning September 1, 2003, licenses will be issued with an expiration date on the employee’s birthday, every third year.  All certified employees must keep their certificate current in order to avoid a possible interruption in service eligibility.

It is the individual employee’s responsibility to ensure that certification is kept current.

NCRC Crews Operating on Foreign Railroad Properties

NCRC trains will have two (2) crew members in the cab of the controlling locomotive while operating between stations.  When requesting authority to occupy the main track at any location the following instructions must be adhered to;

- Requests to occupy main track must be made via radio communication whenever possible.

- All requests to occupy main track must include the limits requested, such as “between MP ____ and MP ____”, main track number(s) and the type of move(s) to be made, such as “operating against the current of traffic”, or a “reverse movement”.

- At locations indicated in the Union Pacific Railroad, Council Bluffs Area, Timetable No. 2, where there is an exception to Rule 13.1.4, it is the responsibility of crew operating a “non-equipped” locomotive to inform the UPRR train dispatcher of that fact when making a request to occupy a main track.

Unit Grain Train Interchange

Procedures for delivery of loaded unit grain trains:

- Provide an accurate train list to NCRC Customer Service Department.

- Complete initial terminal air brake test certificate and place in the control compartment of the lead locomotive.

- Complete the lead locomotive cab signal test certificate and place in the control compartment of the lead locomotive.  *Cab signals must be sealed and the test certificate must reflect the correct seal number.

- EOT devices received from the UPRR on inbound trains are to remain with the train and are to be delivered back to interchange on the same train.  2-way EOT device must be armed and have a sufficiently charged battery.

- Notify UPRR Corridor Manager of any known condition that may delay the train after interchange.

- Provide a message in the control compartment of the lead locomotive for the UPRR crew, concerning hand brakes applied, crossings cut, inoperative locomotives, etc..

Operating Between Stations

Anytime a train crew consists of more than 2 crew members there are to be 2 crew members in the control compartment of the lead locomotive while operating between stations.  Locomotives operating with rear of the lead locomotive facing in the direction of movement must be turned at the first available location.

Train Information Document

A completed NCRC Train Information Document is to be placed in a conspicuous location, (in the “blue card” holder), in the control compartment of the lead unit on all trains and remain there until the train reaches its final destination.  For purposes of loaded unit grain trains interchanged to the UPRR, the Train Information Document must remain with the train.

When requested, crew members will provide a copy of their Train Information Document to the Operations Coordinator.

Train Make-Up Requirements & Reporting Accuracy

When empty cars, of any type are being moved in a train consisting of a solid block of  25 or more loaded cars, empty cars are to be handled in separate block(s) behind the solid block of 25 or more loaded cars.

Equipment tagged, stenciled, billed or shown on the train consist as “Rear End Only” must be placed within the rear five (5) cars of the train.

Two-axle scale test cars are to placed immediately ahead of the rear car in the train.  No more than one (1) two-axle scale test car may be moved in the train.

Conductors are responsible for reporting car consist/list accuracy.  Conductors must verify all cuts of cars handled during tour of duty.  Exceptions to the list (i.e., cars out of sequence, extra cars in the cut, cars on list but not physically in cut) must be immediately reported to the Customer Service Center for reconciliation.

When building or doubling a train up, the Conductor will be required to have a list in his possession for review.

When unable to accomplish assigned or scheduled work, the Conductor must notify

the Operations Coordinator on duty and include the reason why work was not completed.

Handling Company Equipment

Head Jordan Spreaders in the direction the train is moving, unless in work trains.  Inspect equipment carefully before moving, and frequently enroute.

- Operate with wings retracted, locked and secured with chain or cable.

- Handle on rear of train only.

- When necessary, only move in reverse direction to the first location machine can be turned, not exceeding 15 MPH.

Handling Excessive Height/Width Loads

- Mechanical personnel must inspect equipment for proper loading and securing prior to being placed in a train.

- Position dimensional loads, excess width shipments and unusual shipments that require close attention as close to the engine as possible, except equipment requiring handling on the rear end only.

- The conductor must notify other crew members of the presence of excessive height/width in their train before movement.

- Loads must not be kicked or humped or other cars kicked or humped against these type of loads during switching operations.

Proficiency Testing

The use of “Banner Testing” has been added to the type of Operating Rules Compliance Tests conducted on the NCRC.  These banners are bright orange in color with the words “STOP OBSTRUCTION AHEAD” printed on the face of the banner.  Additionally, two red flags are displayed on opposite corners on the top of the banner.  Banners will be displayed between the rails of the affected track with wording facing the approaching movement.  When encountered, the banner is to be taken as a stop signal, the same as a Red Board or Red Flag displayed between the rails, (movement must stop before any part of train or engine passes red signal).  Banner testing will only be used in situations where train movements are required to be made at restricted speed (after the explosion of torpedoes, where track warrant or track bulletin restricts movement to restricted speed, where normal operations are made at restricted speed in accordance with timetable instructions, yard limits, etc.).

Operating at Restricted Speed (rules 6.13, 6.27, & 8.7)

While operating at "restricted speed", engineers must approach all main track switches expecting to find switch improperly lined.  Conductors utilizing vehicles in conjunction with their duties must precede train movement, inspect all switches in advance of movement, report findings of switch inspections to engineer, and when possible, remain at the switch

location until entire movement has passed.

Enroute Train Inspections (rules 6.29.1 & 6.29.2)

When operating between stations, train crew members that are utilizing company vehicles are required to remain within radio range of the lead locomotive at all times and must make frequent inspections of  their train, reporting the results of the inspection to the engineer as soon as possible after the inspection is complete.

Other Than Main Track (rule 6.28)

Occupancy of and movements on any track other than main track are authorized by Rule 6.28.

Flag Protection (rule 6.19)

When flag protection is required, the minimum flagging distance is 1 mile.

Response to Red Flags, Fusees, or Torpedoes

In addition to complying with the applicable rules associated with “red flags” (rule 5.4.7), “fusees” (rule 5.6), or  “torpedoes” (rule 5.7), when red flags, fusees, or torpedoes are encountered, every effort must be made to notify other crew members and to establish radio communication with the Employee-In-Charge of the red flag, fusee, or torpedoes.  Delays associated with complying with red flags, fusees, or torpedoes must be properly reported to the Operations Coordinator.

Securing Unattended Locomotives (rule 32.1.3)

In addition to the procedures outlined by rule 32.1.3, the following instructions must be adhered to:  When operating conditions permit, locomotives left unattended must have the reverser removed and retained in the possession of the engineer.

Sufficient Number of Handbrakes

10% of total car count for train or standing cut of cars must have handbrakes applied with no less than five (5) cars or 100% if less than five (5) cars.  Exception:  if locomotive consist with two (2) or more locomotives is attached to a train or cut of cars, then five (5) handbrakes in addition to locomotive power is required.  If consist is later removed, then 10% standard applies to the remaining train or standing cut of cars.

Locomotive: Cab Signal Testing

Locomotive cab signal testing on a permanently installed “test loop” is to be performed rather than testing with a “self tester” whenever possible.

Locomotive:  Fuel Readings

At the time engineers take charge of their locomotive consist, they must report;

- Any locomotives with less than 1000 gallons of fuel

- Any locomotive with low oil levels.

Locomotive:  Fuel Conservation

When the air temperature is expected to be 40 degrees or higher, locomotives unattended or otherwise not in use (sitting idle), in excess of one (1) hour are to be shut down.  Anytime there are units in a locomotive consist that are not needed to maintain track speed engineers are required to shut down the excess locomotives.  Locomotives needed to maintain trainline air pressure are not to be shut down.  Locomotives that are known to have weak batteries or any condition that may prevent restarting, are not to be shut down, except at designated repair facilities, or as directed by Mechanical Department personnel.

Locomotive:  Cold Weather Instructions

When the air temperature is expected to be below 40 degrees, locomotives are to left idling.  When the air temperature is expected to fall below 10 degrees, locomotives are to be left running in throttle position #2.

If not practical to leave locomotives running, it is the locomotive engineer’s responsibility shut down locomotives and to ensure that locomotive cooling water systems are properly drained.

“Cold Weather Instructions” do not apply to locomotives equipped with “Hot-Start” equipment when those locomotives are at locations where “Hot-Start” equipment may be properly connected to a power source.

Winter Operations:  Train Handling

In blizzard, snow, or blowing snow conditions, or where heavy accumulation of snow is present, layers of ice can build up on brake shoes and may reduce brake efficiency.  Under those conditions, engineers should apply brakes earlier than usual.  Initial brake applications must be made sufficiently in advance to allow any accumulated ice and snow to melt from the brake shoes before braking is necessary.

Movements Over Frozen or Snow-Covered Road Crossings

When crews are required to make movements through road crossings that are frozen, ice packed, or snow covered, the following procedures must be followed:

- Stop must be made before going over crossing.

- A crew member must be on the ground at the crossing.

- Make movement at no more than two (2) MPH (walking speed), prepared to stop movement short of derailment, until lead locomotive or first car is completely through the crossing.

- Empty cars must never be used as the lead car.

- If movement cannot be made without derailing, a crew member must notify the Operations Coordinator.

Heavy Rains / Flash Floods

When advised of flash flood warnings on their territory, Operations Coordinator immediately contact all trains operating within or about to enter the warning area.  The dispatcher will instruct each train crew to comply with Rules 6.21, 6.21.1, and 6.21.2 to ensure the safety of train operations.  The Operations Coordinator will contact the appropriate Engineering personnel to perform special inspections of track and structures.

When instructed to comply with Rules 6.21, 6.21.1, and 6.21.2, each train crew must take all precautions necessary to ensure the safety of themselves and their train.  The train crew will maintain frequent communications with the Operations Coordinator and Engineering personnel to

advise of weather conditions and to receive further instructions

Tornado Warning

Tornado Warning Means:

A tornado has been sighted or verified by the National Weather Service or by persons associated with official weather spotters.

Employees are to follow the instructions as outlined below:

During a Tornado Warning, all train movements and yard activities must stop.  Any train enroute

will stop and employees will seek appropriate shelter.

Consistent with the safety of all involved, avoid stopping a train:

--  On high bridges,

--  Across railroad and highway crossings at grade, or

--  Anyplace where the presence of a train could be a hindrance.

After a Tornado Warning has been cleared and such information has reached the train crews, if the path of the tornado crossed the tracks at their location or in the immediate vicinity, crew members must:

-- Inspect their train before moving to find out if any damage or derailment has occurred to the

train, and

-- Inspect track structure for signs of damage from the tornado.

After inspecting the train and track, the train may proceed.

However, be prepared to stop when approaching bridges, culverts and other points likely to be  affected.  If unable to proceed safely, stop the movement and do not resume movement until safe to do so.  Advise the train dispatcher of such conditions by the first available means of communication. In case of communication failure, strictly follow standard operating procedures.

Rules – Additions / Revisions

General Code of Operating Rules

1.1.2 (Addition) – Alert and Attentive

Add last paragraph:  Employees are prohibited from using cellular telephones, whether Company owned or personal, under any of the following conditions:

- While at the operating controls of a moving locomotive.

- While driving a Company vehicle that is not equipped with “hands-free” type equipment.

- While operating other types of equipment or performing other types of duties where the use of a cellular telephone may distract the employee’s attention from the duties, and which subsequently could create an unsafe condition for themselves, other employees, or the general public.

- While working in or near flammable or combustible atmospheres, (such as gasoline vapors, welding gases, methane gas, grain dust), or areas marked by signs indicating “NO SMOKING or OPEN FLAMES.”

1.1.3 (Addition) – Accidents, Injuries, and Defects

Add last sentence:  All crew members, work group members, or other employees that have any knowledge of the incident must complete and submit a written incident report before going off duty.

1.3.1 (Addition) – Rules, Regulations, and Instructions

Add last sentence:  Employees are responsible for maintaining all books with the current rules and the latest revised pages in the proper page sequence.

1.3.2 (Addition) – General Orders

Add last sentence:  Employees must have a current copy of general orders they can refer to while on duty.

1.6.1 - Motor Vehicle Driving Records

Change first sentence to read:  All employees must report convictions for:

5.8.1 (Addition) - Ringing Engine Bell

Add to last paragraph:  Trains must ring locomotive bell when approaching private crossings at grade.

5.8.2 (Addition) - Sounding Whistle

Add to whistle signal (7):  Trains must sound locomotive whistle when approaching private

crossings at grade.

6.21 (Addition) - Precautions Against Unusual Conditions

Add sentence to second paragraph:  When weather conditions restrict visibility, make all

movements at restricted speed (rule 6.27).

7.10 (Addition) - Movement Through Gates or Doorways

Add last sentence:  Do not ride on the side of a car, engine, or other equipment when moving through gates, doorways, or similar openings.

14.3 (Addition) – Operating with Track Warrants

Add a second paragraph:  The use of “After-Arrival-Of” (box 7), track warrant instructions are prohibited, except when all movements are under the direction of a single designated employee, or when the dispatcher has ascertained that the train receiving “after-arrival-of” instructions is stopped at the location at which they will meet the opposing train.

14.4 (Addition) – Occupying Same Track Warrant Limits

Before entering the limits indicated on either line #11 or line #12, permission must be received from the dispatcher, or communication established with all other trains or men & equipment authorized to occupy the same limits and a thorough understanding reached concerning all movements to be made.

Trains holding track warrant authority with box #11 checked (operate at restricted speed, limits occupied by train), may proceed at normal speed on verbal authority from the dispatcher after other trains holding authority have reported clear of the limits, or after opposing movements holding work between authority have passed at a meeting point and movements are proceeding in opposite directions, or when all trains are proceeding in the same direction, the first train may operate at normal speed.

14.5 (Addition) – Protecting Men or Equipment

When men or equipment are performing any function other than track inspection or moving On-Track-Equipment between stations, protection within the working limits must be established by either a Form B track bulletin or Form C track bulletin.

Trains, Hy-Rail Vehicles or On-Track-Equipment must not enter the working limits until communication has been established with the Employee-In-Charge of either a Form B or Form C track bulletin.  The EIC may authorize Trains, Hy-Rail Vehicles and On-Track-Equipment to enter the working limits without receiving additional track warrant authority from the dispatcher.

14.7 (Addition) - Reporting Clear of Limits

Add second sentence to last paragraph:  In non-signaled territory, before reporting clear of the limits of a track warrant, the crew member releasing the track warrant must first advise the train dispatcher that main track switches have been restored to normal position.

15.1.1 (Addition) - Changing Address of Track Warrants or Track Bulletins

The train dispatcher may verbally change the engine identification on a track warrant, provided:  That all other employees holding authority (trains, M/W employees or On-Track-Equipment), in the affected territory are notified before the engine identification is changed, and, the date, limits of the track warrant, the direction of movement, or other instructions do not change.

15.2.2 - Protection of Non Railroad Contractors

When authorized non-railroad employees or non-railroad contractors are working within 25 feet of a main track or controlled siding protection will be provided as outlined below.

- When working within 10 feet of the track, protection will be provided by use of a track bulletin, track warrant, or other means of protection.

- When working between 10 and 25 feet of the track, trains will be notified of their presence by issuance of a Form C track bulletin that reads:

"Contractors are working at least 10 feet from the track at the following location:  (locations

identified at milepost or between mileposts)."

A watchman must ensure workers and equipment remain at least 10 feet from the track.

Railroad employees who observe work being performed within the boundaries of railroad right-of-way without notification as outlined above should report this information to the Operations Coordinator for further action.

Union Pacific Maintenance of Way Rules

40.14 – (Supplement) 14.7 Reporting Clear of Limits

Add new last paragraph reading:  In non-signaled territory, before reporting clear of the limits of a track warrant, advise the train dispatcher that main track switch(es), if used, have been restored to normal position.

42.17 - Entering Remote Control Zone

Change rule as follows:  Before entering a designated Remote Control Zone, employees must

determine whether the zone is activated.  Employees may receive this information from the remote control operator or from the supervisor in charge of yard movements.  When the Remote Control Zone is activated, track(s) within the zone must not be occupied with equipment or

fouled by equipment until the zone has been deactivated.  Switches may not be operated until either the zone has been deactivated or permission has been received from the Remote Control Operator.

Union Pacific Safety Rules

81.5.4 – Understanding Between Crew Members Before Fouling Track

If the equipment is coupled to an engine or other motive equipment, before an employee steps foul of the track:

- The employee must notify the engineer or operator by job briefing, agreed-upon hand signal, or radio communication (I.E.:  “Conductor Jones to NC 1234, going into the RED ZONE”).

- The engineer or operator must apply locomotive or train air brakes and center the reverser, then notify the employee by job briefing, agreed-upon hand signal, or radio communication (I.E.:  “NC 1234 to Conductor Jones, I understand. I’m set and centered”).  If the equipment is not equipped with a reverser, it must be placed in neutral or park with the brakes applied.

- If going between cars, the employee must inspect cars not coupled to the locomotive or motive equipment to ensure they will not move, applying hand brakes if necessary.  In bowl tracks and other yard tracks where cars are likely to roll together, separate cars at least 100 feet then apply sufficient hand brakes, but not less than two, on the unattached portion to prevent movement before going between cars to perform work on cars.

81.7.1 – Designated Riding Places

Change the 4th bullet to read:  Do not ride on the ends of moving cars except when necessary to operate hand brakes to stop or control the speed of cars cut off in motion.

81.8.3 - Impaired Clearances

Change entire rule to read:  Do not ride on the side of a moving car, engine, or other equipment under any of the following conditions:

- Next to a structure.

- Through gates or doorways.

- Into, out of, or within enclosed buildings.  Before entering enclosed buildings, an employee, if safe to do so, must precede the movement.  Further movements must only be made on that employee's signal.

In addition, do not position yourself or knowingly allow others to position themselves between a structure and moving cars(s), engine(s), or other equipment when clearance is minimal.

81.11 – Hand Brake

Add a paragraph following the second paragraph:  End mounted hand brake on cars without brake steps or crossover platforms must be operated from the ground, provided that the employee can safely reach the hand brake while keeping both feet firmly on the ground.  Cars without brake steps or crossover platforms are not to be “kicked, dropped, or otherwise let roll free under their own momentum”.

82.7 - Operating Ground-Throw Switch

Change rule title to read - Operating Lever-Action (Flop-Over) Switches

Change first sentence to read:  When operating a lever-action switch:

Change step 7 to read:  On switches where movement is completed in close proximity to the

ground, it is permissible to use one foot to complete the last 6 inches of movement, provided that good balance is maintained.  Place one foot near the end of the lever and step down until the lever arm is latched.

| SPEED TABLE |
| --- |
| Time Per Mile | Miles Per Hour | Time Per Mile | Miles Per Hour | Time Per Mile | Miles Per Hour |
| Min | Sec |  | Min | Sec |  | Min | Sec |  |
| - | 36 | 100 | - | 58 | 62.1 | 1 | 40 | 36.0 |
| - | 37 | 97.3 | - | 59 | 61.0 | 1 | 42 | 35.3 |
| - | 38 | 94.7 | 1 | - | 60.0 | 1 | 44 | 34.6 |
| - | 39 | 92.3 | 1 | 02 | 58.0 | 1 | 46 | 34.0 |
| - | 40 | 90.0 | 1 | 04 | 56.2 | 1 | 48 | 33.3 |
| - | 41 | 87.8 | 1 | 06 | 54.5 | 1 | 50 | 32.7 |
| - | 42 | 85.7 | 1 | 08 | 52.9 | 1 | 52 | 32.1 |
| - | 43 | 83.7 | 1 | 10 | 51.4 | 1 | 54 | 31.6 |
| - | 44 | 81.8 | 1 | 12 | 50.0 | 1 | 56 | 31.0 |
| - | 45 | 80.0 | 1 | 14 | 48.6 | 1 | 58 | 30.5 |
| - | 46 | 78.3 | 1 | 16 | 47.4 | 2 | - | 30.0 |
| - | 47 | 76.6 | 1 | 18 | 46.1 | 2 | 05 | 28.8 |
| - | 48 | 75.0 | 1 | 20 | 45.0 | 2 | 10 | 27.7 |
| - | 49 | 73.5 | 1 | 22 | 43.9 | 2 | 15 | 26.7 |
| - | 50 | 72.0 | 1 | 24 | 42.9 | 2 | 30 | 24.0 |
| - | 51 | 70.6 | 1 | 26 | 41.9 | 2 | 45 | 21.8 |
| - | 52 | 69.2 | 1 | 28 | 40.9 | 3 | - | 20.0 |
| - | 53 | 67.9 | 1 | 30 | 40.0 | 3 | 30 | 17.1 |
| - | 54 | 66.6 | 1 | 32 | 39.1 | 4 | - | 15.0 |
| - | 55 | 65.5 | 1 | 34 | 38.3 | 5 | - | 12.0 |
| - | 56 | 64.2 | 1 | 36 | 37.5 | 6 | - | 10.0 |
| - | 57 | 63.2 | 1 | 38 | 36.8 | 12 | - | 5.0 |

| FEET | TENTHS OF A MILE |
| --- | --- |
| 528 | .1 |
| 1,056 | .2 |
| 1,584 | .3 |
| 2,112 | .4 |
| 2,640 | .5 |
| 3,168 | .6 |
| 3,696 | .7 |
| 4,224 | .8 |
| 4,752 | .9 |
| 5,280 | 1.0 |

WIND CHILL CHART

| Wind | Temperature |
| --- | --- |
| In using the table below, values of wind chill below -10 are considered bitterly cold. Values of wind chill below -20 are extremely cold – human flesh will begin to freeze within one minute. |

|  | 35 | 30 | 25 | 20 | 15 | 10 | 5 | 0 | -5 | -10 | -15 | -20 | -25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5 | 32 | 27 | 22 | 16 | 11 | 6 | 0 | -5 | -10 | -15 | -21 | -26 | -31 |
| 10 | 22 | 16 | 10 | 3 | -3 | -9 | -15 | -22 | -27 | -34 | -40 | -46 | -52 |
| 15 | 16 | 9 | 2 | -5 | -11 | -18 | -25 | -31 | -38 | -45 | -51 | -58 | -65 |
| 20 | 12 | 4 | -3 | -10 | -17 | -24 | -31 | -39 | -46 | -53 | -60 | -67 | -74 |
| 25 | 8 | 1 | -7 | -15 | -22 | -29 | -36 | -44 | -51 | -59 | -66 | -74 | -81 |
| 30 | 6 | -2 | -10 | -18 | -25 | -33 | -41 | -49 | -56 | -64 | -71 | -79 | -86 |
| 35 | 4 | -4 | -12 | -20 | -27 | -35 | -43 | -52 | -58 | -67 | -74 | -82 | -92 |
| 40 | 3 | -5 | -13 | -21 | -29 | -37 | -45 | -53 | -60 | -69 | -76 | -84 | -92 |

Winds speeds above 40 MPH have little additional chilling affect.

HEAT INDEX TABLE

| Heat Index | Affects on Human Body |
| --- | --- |
| 130 or above | Heat stroke highly likely with continued exposure |
| 105 to 130 | Heat stroke likely with prolonged exposure |
| 90 to 105 | Heat stroke possible with prolonged exposure |

| Relative Humidity | Air Temperature |
| --- | --- |

|  | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 30 | 67 | 73 | 78 | 84 | 90 | 96 | 104 | 113 | 123 | 135 | 148 |
| 35 | 67 | 73 | 79 | 85 | 91 | 98 | 107 | 118 | 130 | 143 |  |
| 40 | 68 | 74 | 79 | 86 | 93 | 101 | 110 | 123 | 137 | 151 |  |
| 45 | 68 | 74 | 80 | 87 | 95 | 104 | 115 | 129 | 143 |  |  |
| 50 | 69 | 75 | 81 | 88 | 96 | 107 | 120 | 135 | 150 |  |  |
| 55 | 69 | 75 | 81 | 89 | 98 | 110 | 126 | 142 |  |  |  |
| 60 | 70 | 76 | 82 | 90 | 100 | 114 | 132 | 149 |  |  |  |
| 65 | 70 | 76 | 83 | 91 | 102 | 119 | 138 |  |  |  |  |
| 70 | 70 | 77 | 85 | 93 | 106 | 124 | 144 |  |  |  |  |
| 75 | 70 | 77 | 86 | 95 | 109 | 130 |  |  |  |  |  |
| 80 | 71 | 78 | 86 | 97 | 113 | 136 |  |  |  |  |  |
| 85 | 71 | 78 | 87 | 99 | 117 |  |  |  |  |  |  |
| 90 | 71 | 79 | 88 | 102 | 122 |  |  |  |  |  |  |
| 95 | 71 | 79 | 89 | 105 |  |  |  |  |  |  |  |
| 100 | 72 | 80 | 91 | 108 |  |  |  |  |  |  |  |

NCRC, UPRR, BNSF PHONE NUMBERS

| Name | Phone Number | Name | Phone Number |
| --- | --- | --- | --- |
| NCRC |  | UPRR |  |
| General Office | 402-371-9015 888-735-8634 | Omaha Cor. Mngr. | 402-636-7433 |
| Customer Service | 402-371-4153 800-990-2676 | NP Cor. Mngr. | 402-636-7439 |
| Operations Coordinators Office | 402-379-5824 | Grain Desk | 402-636-7501 |
| Signal Department Office | 402-379-0999 | Power Desk | 402-636-7186 |
| Columbus Office | 402-563-3595 800-347-9576 | Locomotive Trouble Desk | 402-636-7509 |
| Grand Island Shop | 308-382-8925 800-524-5558 | Disp. - Columbus Sub | 402-636-1733 |
| Ken Sidlinger V.P. - Operations RGPC | 402-750-4012 | Disp. - Kearney Sub | 402-636-1732 |
| Gary Hughes General Manager | 402-750-4048 | Columbus Office | 402-563-1800 |
| Donette Elston Director – Customer Service East | 402-750-4019 | Central City Office | 308-389-2237 |
| Barry Parsons OP Coordinator | 402-750-4060 | Grand Island Office | 308-389-2246 |
| Jeff Scholl OP Coordinator | 402-750-0663 | Kim Jungck – MTO Grand Island | 308-389-2269 |
| Tim Behrens OP Coordinator | 402-750-5093 | BNSF |  |
| Todd McKee Director – Signal Maintenance | 402-750-4089 | Dispatcher | 817-234-6044 |
| Ted Rydel Director – Track & Structures | 402-750-4086 | Division Office – Lincoln | 402-473-7736 |
| Ken Morriss Mechanical Manager | 402-750-4053 | Roadmaster | 402-430-8594 |
|  |  | Division Trainmaster | 402-694-2862 |
|  |  | Trainmaster | 402-461-7833 |
|  |  | Bellwood Sub Local Train Crew | 402-440-7299 |

EMERGENCY PHONE NUMBERS

| NAME | PHONE NUMBER | NAME | PHONE NUMBER |
| --- | --- | --- | --- |
| National Response Center (FRA/NTSB) | 800-424-0201 | CHEMTREX (Haz-Mat spills) | 800-424-9300 |
| Nebraska State Patrol | 800-525-5555 |  |  |
| County Sheriffs |  |  |  |
| Boone | 402-395-2144 |  |  |
| Butler | 402-367-7400 |  |  |
| Greeley | 308-428-2395 308-245-3236 |  |  |
| Hall | 308-385-5200 |  |  |
| Hamilton | 402-694-6936 |  |  |
| Howard | 308-754-5433 |  |  |
| Madison | 402-454-2100 |  |  |
| Merrick | 308-946-2345 |  |  |
| Nance | 308-536-2452 |  |  |
| Platte | 402-564-3229 |  |  |
| Polk | 402-747-2231 |  |  |
| Valley | 308-728-5771 |  |  |
| Cities / Towns |  | Cities / Towns |  |
| Albion | Police: 402-395-2154 Fire: 402-395-2345 | Humphrey | Police: 402-923-9342 Fire: 911 |
| Archer / Palmer | Police: 308-894-2100 Fire: 308-894-2100 | Madison | Police: 402-454-3333 Fire: 402-454-2135 |
| Belgrade / Fullerton | Police: 308-536-2452 Fire: 308-536-2452 | Monroe | Police: 402-564-3201 Fire: 402-495-2345 |
| Brainard | Police: 402-367-7400 Fire: 402-367-7400 | Norfolk | Police: 402-644-8700 Fire: 402-644-8740 |
| Cedar Rapids / Primrose | Police: 800-266-0935 Fire: 911 | North Loup / Ord | Police: 308-728-5771 Fire: 308-728-5771 |
| Central City | Police: 308-946-3063 Fire: 308-946-3000 | Polk | Police: 402-747-2231 Fire: 911 |
| Columbus | Police: 402-564-3201 Fire: 402-564-8127 | Platte Center | Police: 402-564-3229 Fire: 402-246-2926 |
| David City / Yanka | Police: 402-367-3530 Fire: 911 | Rising City | Police: 402-367-7400 Fire: 402-542-2430 |
| Elba / St. Libory / St. Paul | Police: 308-754-5433 Fire: 308-754-5254 | Shelby | Police: 402-747-2231 Fire: 402-747-2231 |
| Genoa | Police: 308-536-2452 Fire: 402-993-2200 | Spalding | Police: 308-942-3435 Fire: 308-497-2671 |
| Grand Island | Police: 308-385-5461 Fire: 911 | St. Edward | Police: 402-678-3466 Fire: 402-678-2222 |
| Hordville | Police: 402-694-6936 Fire: 402-757-3359 | Stromsburg | Police: 402-764-2100 Fire: 402-764-2100 |