Date:		November 23, 1999

To:		Distribution

From:		Jeannette Plante, Swales Aerospace

Subject:		Notes From Trip to BICC Nov 18 – 19 Regarding SSQ21654 Anomaly Investigation

When I joined the Boeing/ISS review team at BICC in Jackson, TN on Thursday, November 18th, they were starting the second half of a review of the build and traceability records for a predetermined six of cable.  During this time I continued to review the records which had been distributed by SEA and BICC regarding corresponding reel numbers, dates of manufacture and fiber lot numbers.

I photographed the “color line” which BICC uses to measure fiber OD and which respools the reels of fiber.  Dale Zevotek photographed the extrusion line for me (see attachment).

The group was given a demonstration of the operation of the “color line” during which I and Craig Mueller of Aerospace Corp., took electrostatic field measurements at different locations along the fiber’s path as it was re-spooled.  I used the 3M 709 Static Sensor.  Craig Meuller use the Pastic Systems 42720 Static Field Meter.

The machine was first operated at 20 m/min and measurements were taken and recorded.  The machine was then switch to operate at 50 m/min and again measurements were made.  Dale Zevotek reported to me that the tension on the fiber during this respooling was about 50g.  The data taken is shown in Table 1.  Through-out these measurements and measurements taken around the extrusion line, the minimum fields measured using the 3M meter were between +50V/inch and –50 V/inch.

Table 1.  Electrostatic Field Measurements Taken Around “Color Line”

| Location | Identifier on Figure 1 | Field During 20 m/min operation (V/inch) | Field During 50 m/min operation (V/inch) | Field During 20 m/min operation (V/inch) | Field During 50 m/min operation (V/inch) |
| --- | --- | --- | --- | --- | --- |
|  |  | 3M 709 Measurements | 42720 Measurements |
| Let-out reel | 1 | +40 | +25 | -200 | +640 |
| 1st pair of tension control wheels | 2 | +30 | +110 |  |  |
| Pre-ionizier wheel | 3 | -2000 | > -10,000 | +350 |  |
| Post-ionizer | 3a |  |  | -980 | -900 |
| Entrance into wheel/belt section | 4 | -140 | -1150 | -300 | -3500 |
| Exit out of wheel/belt section | 5 | -35 | -65 |  | 0 |
| Pre-OD detector | 6a |  |  |  | -500 |
| Post OD detector | 6 | -25 | -45 |  |  |
| Take-up reel | 7 | +85 | +50 | +50 | -300 |

Dale Zevotek arranged to have the extrusion line operating making a fiber-less buffer tube.  During this operation, the extrusion line was monitored in various spots for electrostatic field strength.  Figure 2 identifies the spots which correspond to the data in Table 2.

Table 2.  Electrostatic Field Measurements Taken Around the Extrusion Line

| Location | Identifier on Figure 2 | Field (V/inch) |
| --- | --- | --- |
| Let-out reel | A | -750 |
| Air space between quenching baths | B | -150 |
| Exit of second quenching bath | C | -10 |
| Length counter (wheel & belt) | D | * |
| Rubber belts – entry | E | -110 |
| Rubber belts – exit | F | -45 |
| Tension wheels – 1st | G | +2000 |
| Tension wheels – 2nd | H | +2250 |
| Tension wheels – 3rd | I | +75 |
| Ground chain | J | -100 |
| Metal feeder wheel | K | +305 |
| Take up reel (in path of de-ionizing fan) | L | -1500 |

* Did not capture numerical data but recollection is that it was near the

minimum/floor of 50V/inch.

The next day a telecon was then executed with those at BICC, Martin Seifert at Spectran and Henning Leidecker at GSFC.  Following this, the extrusion line was run again to show the jacketing operation (which is virtually the same as the buffering operation with the exception of the use of different tooling). I was not able to stay for the wrap-up due to my flight schedule.

Figure 1.  Color Line

Figure 2.  Extrusion Line

Distribution:

Boeing-HB:  D. Gill, J. White, H. Battaglia

Boeing-KSC:  E. Banks, C. Moore, D. Tambert

NASA ISS:  R. Prestridge, D.  Beverly

NASA GSFC:  H. Leidecker, J. Kolasinski

BICC:  D. Zevotek, D. Rothermel

Spectran.  M. Seifert

SEA:  A. Cantwell

Aerospace:  C. Meuller

Swales:  M. Ott