8-94-3 --COCKPIT OBSERVER SEAT SAFETY BELT LOCKING PROCEDURES.

a.  The L-1011 cockpit observer seat safety belt system differs from other aircraft in that the lapbelt portion has two spring-loaded reels which keep the belt ends retracted until the crewmember pulls or extends them for use.  The lapbelt is not an adjustable length belt as is commonly used on most other aircraft.  Once the safety belt system is fitted to the occupant, a locking lever located at the reel on each half of the lapbelt must be manually actuated in order to keep the lapbelt from extending further.  If the locking lever on each half of the lapbelt is not manually actuated (locked) the restraint system will not be capable of performing its intended function.  There is no inertia reel locking device on the shoulder harness of the L-1011 system.  The seats have a five-point restraining system with nonretracting shoulder harnesses and manual locks to keep the left and right sides of each half of the lapbelt assembly from extended from their takeup reels.  Therefore, on L-1011 aircraft with observer seat lapbelt locks installed, as well as on other aircraft equipped with a similar occupant restraining system, it is necessary to adjust seatbelts and shoulder harnesses tightly and to lock both sides of the lapbelts on cockpit observer seats before takeoff, landing, and during turbulence.  Flightcrews of aircraft equipped with the kind of occupant restraint system described in this ACOB should verbally inform occupants of observer seats of the proper operation of their seatbelts and shoulder harnesses and to visually confirm that the restraints are locked, if locks are provided, prior to takeoffs and landings and turbulence encounters during flight.

b.  Principal Inspectors who are assigned to air carriers that operate the L-1011 aircraft and other aircraft equipped with a similar cockpit observer seat occupant restraint system shall ensure that the following actions are accomplished:

(1)  Bring the contents of this ACOB to the attention of their operator.

(2)  Encourage their operator to instruct its flight crewmembers on the steps to follow in hooking-up, adjusting, and locking the safety belt and shoulder harness.

(3)  Direct their operator to develop and use procedures to ensure that cockpit observer seat occupants are given a proper briefing by a flight crewmember to include the steps to follow in hooking-up, adjusting, and locking the safety belt and shoulder harness.  In addition, the procedures must provide for a flight crewmember to visually confirm that the safety belt locks and shoulder harness locks, if installed, are locked prior to takeoffs and landings and when moderate to severe turbulence is encountered during flight.

(4)  Encourage the installation of a warning placard for seat occupants stating the need to lock safety belts and shoulder harnesses, if locks are installed.

c.  Each Flight Standards District Office (FSDO) manager will ensure that sufficient copies of this ACOB are reproduced and given to each inspector assigned responsibility for an operator or certificate holder affected by this ACOB.  The FSDO manager and supervisors are responsible for assuring that the action required by this ACOB is completed by each inspector assigned to their supervision within 120 days of receipt.

d.  Program Tracking and Reporting Subsystem (PTRS) Closeout.  When the action required by this ACOB is completed by the appropriate inspector, a PTRS record will be completed using PTRS activity code "1381" in section 1 of the PTRS data sheet and by adding "ACOB89403" to the "national use" field.  One PTRS record for each affected operator will be completed and appropriate comments written in the "comment text" section of the PTRS Data Sheet.  The comments must include the method used by the operator to comply with this ACOB.