SOME ADVANCED CONCEPTS IN DISCRETE

AERODYNAMIC SENSITIVITY ANALYSIS

Arthur C. Taylor III	*		Lawrence L. Green†

## Perry A. Newman†                  Michele M. Putko*

### Department of Mechanical Engineering*

# Old Dominion University

#### Norfolk, VA  23529

# Multidisciplinary Optimization Branch†

#### NASA Langley Research Center

# Hampton, VA  23681

http://fmad-www.larc.nasa.gov/mdob/MDOB

# THREE KEY IDEAS

# An Alternative Perspective on the Adjoint-Variable Method is Presented.

- A Highly-Efficient, Non-Iterative, ADIFOR-Assisted Method for Computing Second-Order Sensitivity Derivatives (SO SDs) is Presented and Verified.

- Significant Improvements in the Computational Efficiency of the Reverse-Mode Capability of ADIFOR 3.0 for First-Order Sensitivity Derivatives (FO SDs) are Achieved Through Incremental–Iterative Implementations.

# BASIC EQUATIONS

F = F(Q(b), X(b), b)

R = R(Q(b), X(b), b) = 0

F ( Aerodynamic Output Functions (Dimension: NOF)

b ( Aerodynamic Design Variables (Dimension: NDV)

Q ( Aerodynamic Field Variables

X ( Computational Grid

R ( Steady-State Discrete Nonlinear Flow Equations

# INDICIAL NOTATION

# FO SDs                                                                DIRECT METHOD (FORWARD-MODE)

# (NDV solutions for )

# FO SDs                                                             ADJOINT-VARIABLE METHOD             (REVERSE-MODE)

- Lagrange Multiplier Viewpoint (Conventional)

- Derivative (Chain Rule) Viewpoint

# ADJOINT-VARIABLE METHOD                      (CHAIN-RULE PERSPECTIVE)

# THE RELATIONSHIP

- The Adjoint -Variables (Lagrange-Multipliers) are Derivatives

- ADIFOR 3.0 Reverse-Mode computes them as such

# SO SDs

# INDICIAL NOTATION

# SO SDs                                                                 DIRECT METHOD  (FORWARD-MODE)

# NDV solutions for ,  followed by

(NDV2+NDV) / 2 solutions for

# NOTATIONAL COMPACTNESS

# DERIVATIVE COMPLEXITY

# DERIVATIVE COMPLEXITY

# EFFICIENT, NON-ITERATIVE METHOD

- NDV solutions for

- NOF solutions for

- Preferred if  (NDV2+NDV)/2  > NOF

# AIRFOIL EXAMPLE PROBLEM

- NACA 0012

- Euler Equations

- ( = 1.0(

- M( = 0.80

- Transonic flow

- Computational Grid, 129 x 33 points

- Upwind, Cell-Centered Finite-Volume Solver

(Continued >>>)

AIRFOIL EXAMPLE PROBLEM

- 3 Design Variables

g (geometric shape)

( (angle-of-attack)

M( (Freestream Mach. Number)

- 3 Output Functions

CL (Lift Coefficient)

CD (Drag Coefficient)

CM (Pitching-Moment Coefficient)

# FO SDs

# (Forward-Mode & Reverse-Mode)

|  | bj | Forward-Mode | Reverse-Mode |
| --- | --- | --- | --- |
|  | g | +0.1405406E+00 | +0.1405406E+00 |
|  | ( | -0.1087323E-01 | -0.1087323E-01 |
|  | M( | -0.4672729E-01 | -0.4672729E-01 |
|  | g | +0.1761807E+02 | +0.1761807E+02 |
|  | ( | +0.1158625E+01 | +0.1158625E+01 |
|  | M( | -0.2382580E+01 | -0.2382580E+01 |
|  | g | +0.3171492E+01 | +0.3171492E+01 |
|  | ( | +0.5955598E+01 | +0.5955598E+01 |
|  | M( | -0.1603002E+01 | -0.1603002E+01 |

- FO SDs from Hand-Differentiated Coding

- Results verified by Finite-Differences; Excellent Agreement

# SO SDs

# NON-ITERATIVE METHOD

|  | bj/bk | g | ( | M( |
| --- | --- | --- | --- | --- |
|  | g | +0.248807E+03 | +0.250402E+03 | +0.205825E+03 |
|  | ( | +0.250402E+03 | +0.184277E+05 | +0.160858E+05 |
|  | M( | +0.205825E+03 | +0.160858E+05 | +0.133087E+05 |
|  | g | +0.71777E+02 | +0.134379E+02 | +0.101304E+02 |
|  | ( | +0.134379E+02 | +0.959310E+03 | +0.804021E+03 |
|  | M( | +0.101304E+02 | +0.804021E+03 | +0.662088E+03 |
|  | g | -0.663590E+02 | -0.602441E+02 | -0.490399E+02 |
|  | ( | -0.6024415+02 | -0.449198E+04 | -0.386943+04 |
|  | M( | -0.490399E+02 | -0.386943E+04 | -0.320512E+04 |

- Results verified by Finite-Differences of FO SDs; Excellent Agreement

# Relative CPU Timings

# SO SDs, Non-Iterative Method

| Computational Procedure | % of Total |
| --- | --- |
| Nonlinear Flow | 5.4 |
| Forward-Mode FO SDs | 25.5 |
| Reverse-Mode FO SDs | 69.0 |
| SO SDs | 0.1 |
| Total | 100.0 |

# Intermediate Summary

# Non-Iterative SO SD Method

- First, one requires solution of both methods for FO SDs

- NDV forward-mode solutions for

- NOF reverse-mode solutions for (

- Selective forward-mode application of ADIFOR to strategic pieces of the same code used for the FO SDs for accurate construction of complicated SO derivative terms

- Thereafter, NOF x NDV2  “exact”  SO SDs  (i.e. the complete Hessian matrices) calculated essentially “for free”

# FO SDs                                                             REVERSE-MODE APPLICATIONS OF ADIFOR

# TABLE OF ACRONYMS

- HD – Hand Differentiated / Hand Coded

- AD – Automatic Differentiation (ADIFOR)

- II –  Incremental-Iterative Solution Algorithm

- BB – Black-Box Application of AD

- AV – Adjoint-Variable (Reverse-Mode) Differentiation

(Continued >>>>)

# FO SDs                                                                     TABLE OF ACRONYMS

| Forward-Mode Method | Reverse-Mode Method |
| --- | --- |
| HDII* | HDII-AV* |
| ADBB* | ADBB-AV* |
| ADII* | ADII-AV† |
| *Previous Studies |
| † Present Study |

INCREMENTAL-ITERATIVE APPLICATIONS  OF ADIFOR FOR CFD CODES

Computational Issues Associated With Present Reverse-Mode

Applications are Completely Analogous to Those Seen Previously

With Forward-Mode Applications

CRITICAL COMPUTATIONAL IDEA

Forward Mode: ADIFOR computes the post-multiplication of a large Jacobian Matrix times a vector very efficiently; in particular:

Reverse Mode: ADIFOR computes the pre-multiplication of a large Jacobian Matrix times a vector very efficiently; in particular:

# INCREMENTAL-ITERATIVE

# SOLUTION METHODS

Non-linear Flow

(N = 1, 2, 3, …)

FO SDs                                                                 Forward-Mode

Incremental–Iterative, Forward-Mode (HDII & ADII)

(M = 1, 2, 3,…)

Black-Box AD, Forward-Mode (ADBB)

(N = 1, 2, 3,…)

# FO SDs                                                                     Reverse-Mode

Incremental Iterative, Reverse-Mode (HDII-AV & ADII-AV)

(M = 1, 2, 3,…)

# RELATIVE CPU TIMING COMPARISON

| Reverse-Mode Method Tested | Relative Timing* |
| --- | --- |
| HDII-AV | 1.0 |
| ADBB-AV | 7.9 |
| ADII-AV | 4.7 |
| ADII-AV (with Single, Frozen Forward Pass) | 3.3** |
| *CPU Time/iteration/grid-point/differentiated output-function |
| **Work-In-Progress, Projected Timing |

- Results for Coarse Grid, 2D Internal Flow Example

- CFD Code Same as Previous Airfoil Example Problem

Accuracy: “Exact” Agreement among all methods tested, as expected; verified by Finite-Differences

# COMPUTER MEMORY

Disk Storage (ADIFOR Log Files)

ADBB-AV: Iterative Accumulation of  Log Files Unmanageably Large

ADII-AV: Log Files do  not accumulate; in contrast, they are fixed on  the first iteration and reused on all subsequent iterations

# RAM MEMORY

# Memory Increase – Original Flow Code x  NOF  Computed  Concurrently

# CONCLUSIONS                                                      (THREE KEY IDEAS)

# An Alternative Perspective on the Adjoint-Variable Method is Presented.

- A Highly-Efficient, Non-Iterative, ADIFOR-Assisted Method for Computing Second-Order Sensitivity Derivatives (SO SDs) is Presented and Verified.

- Significant Improvements in the Computational Efficiency of the Reverse-Mode Capability of ADIFOR 3.0 for First-Order Sensitivity Derivatives (FO SDs) are Achieved Through Incremental–Iterative Implementations.