Distribution: Initiated By: ATCBI-6 Program Office ATO-T

| NOTICE | U.S. DEPARTMENT OF TRANSPORTATION FEDERAL AVIATION ADMINISTRATION | N XXXX.XX |
| --- | --- | --- |
| July, 2005 |
| Cancellation Date: TBD |
| SUBJ: | AIR TRAFFIC CONTROL BEACON INTEROGATOR MODEL 6 SUPPLY SUPPORT PROCEDURES- Revision 1 |

1. PURPOSE. This notice announces the Air Traffic Control Beacon Interrogator Model 6 (ATCBI-6) site and depot interim maintenance procedures for the removal and replacement of Line Replaceable Units (LRU’s).

2. DISTRIBUTION. This notice is distributed to Division Level in the Air Traffic Organization, Terminal (ATO-T), FAA Academy, FAA Logistics Center, FAA Technical Center, and all ATCBI-6 sites, both DoD and FAA that are installed during the period of effectiveness of this notice.

3. OPERATIONAL APPROACH. The FAA is the lead acquisition agency for the ATCBI-6 and also provides the life-cycle coordination and support for all users of the system. Users include the FAA and the Air Force. The maintenance concept for the ATCBI-6 is a two level approach, site and depot. Site maintenance will be performed organically to the Line Replaceable Unit (LRU) level. Life–cycle depot level repair support will be provided by the contractor, Raytheon, on an interim basis until the organic depot capability is established at the Mike Monroney Aeronautical Center in Oklahoma City, OK.

a. Prior to Contractor Acceptance and Inspection (CAI) at any given site, Raytheon, (the Contractor) will control handling and repair of all ATCBI-6 LRU failures in accordance with their own internal operational procedures.

b. Initially and after CAI, the Prime Contractor will provide Interim Contractor Support (ICS) for all operational sites.

If, for any reason, FAA or Department of Defense (DOD) site personnel encounter problems concerning services with regard to these depot procedures please contact the following individuals via e-mail or by phone:

| Name/Code | Phone | E-Mail Address |
| --- | --- | --- |
| Mike Weiler/ATCBI-6 Sr. Engineer ATO-T | 202-385-8767 | Michael.Weiler@faa.gov |
| Raytheon Technical Services Company, LLC |
| Michael Walsh/Depot Operations | 757-852-2050 | Michael_J_Walsh@Raytheon.com |
| Bill Peters/Depot Operations | 757-852-2000 x2133 | William_A_Peters@Raytheon.com |
| Vidal De La Cruz, Jr. / Sr. Configuration Analyst | 781-238-2831 | Vidal_De_La_Cruz@Raytheon.com |
| Raytheon 24-Hour ATCBI-6 Help Line | 800-585-2585 |  |

4. SITE SPARES. Site spares are limited to items that are authorized to be removed and replaced by site level technicians, and normally consist of LRU’s and low-dollar expendable items.

a. Each FAA/DoD site will receive a set of site spares from Raytheon prior to CAI. LRU site configuration is available in the ATCBI-6 System Manual. (Hard copies and a CD-ROM version of this Manual have been delivered to each ATCBI-6 site.)

b. The Contractor’s Interim Depot will configure each site spare and replacement LRU with the appropriate approved software revision and firmware.

5. ATCBI-6 PROCEDURES FOR REPLACING A FAILED LRU.

a. Sites: FAA/DoD procedures are as follows:

(1) Fault-isolate to the LRU level and replace the failed LRU with a site spare, if available. Save packing material.

(2) FAA: Order replacement parts via the established Logistics and Inventory System (LIS) procedures

DoD: Order replacement parts via established MILSTRIP procedures.

NOTE: To insure material is received as required, please contact the FAA Customer Care Center at 405-954-3793 or 1-888-322-9824 if a Priority 1 order is placed after normal duty hours or on weekends.

(3) Upon receipt of the replacement LRU, package the failed LRU in the same shipping container return the failed LRU. The failed LRU must be returned within 5 working days.

(4) Return the failed LRU by any traceable means to the following address:

RAYTHEON COMPANY

ATCBI-6 PROGRAM

ATTN: MICHAEL WALSH

2555 ELLSMERE AVENUE

NORFOLK, VA 23513

FAX: 757-852-2114

(5) Report all maintenance activities in the Maintenance Management System (MMS) to the module level and record the module serial number in the module serial number field of the corrective maintenance log.

If difficulties are incurred during the replacement part ordering process, the following is a list of ATCBI-6 Points of Contact at the FAA Logistics Center in Oklahoma City, OK:

24-Hour Service-Customer Care Center: 405-954-3793 or 1-888-322-9824

Normal Duty Hours-Barbara Loving, Item Manager: 405-954-2146

Kim Hare, Provisioning: 405-954-9014

Lynn Garst, Engineer: 405-954-8083

John Bartels, Beacon/Weather Branch Chief: 405-954-1857

b. Raytheon.

Upon receipt of the web based notification, Raytheon will ship a replacement LRU directly to the designated address as provided by the site in accordance with the priority level guidance established in paragraph 6. Raytheon will ship the replacement LRU in a reusable shipping container and the site will be provided a FEDEX account number for return shipping of the failed LRU.

FIELD REPLACEABLE UNITS (FRUs). The parts lists contained within the system maintenance manuals are the most current and should be used when ordering replacement items. For a list of replaceable items stocked either as site spares or as depot spares, please go to:

http://www.aos.jccbi.gov/ATCBI-6/

- 6. STANDARD PROCESSING TIME. The codes listed in Table 1-1, Priority Table, were established by the FAA to expedite the processing of requisitions, based on the site’s required restoration time.

NOTE: To insure material is received as required, please contact the FAA Customer Care Center at 405-954-3793 or 1-888-322-9824 if a Priority 1 order is placed after normal duty hours or on week-ends.

| PRIORITY CODE | DEFINITION | RESPONSE |
| --- | --- | --- |
| 1 | Extreme Emergency. Req’d to restore ops as a result of facility outage or aircraft grounded. | Response/Procurement action within 24 hours |
| 2 | Emergency. Facility or aircraft is operating with substandard equipment and outage is imminent. No standby equipment available. | Response/Procurement action within 2 days |
| 5 | Routine. Routine equipment or stock replenishment | Response/Procurement action within 30 days. |

Table 1-1 Priority Table

- 7. SOFTWARE, FIRMWARE AND TECHNICAL DOCUMENTATION. Questions or comments concerning system software, firmware or ATCBI-6 Technical Documentation should be addressed to ATO-W, Secondary Radar Team, at the Program Support Facility located at the Mike Monroney Aeronautical Center, Oklahoma City, OK, at (405) 954-5181. ATCBI-6 Operational Site Technical Documentation includes the following manuals:

| Raytheon Equipment | Manual Title | Manual Reference |
| --- | --- | --- |
| MSSR SYSTEM FOR FAA ATCBI-6 | System Manual for MSSR System 806404/001 for FAA ATCBI-6 (2nd Edition) | SYM 808404/001 (2nd Edition) Issue 3 |
| Condor MSSR Interrogator | Equipment Manual for Condor MSSR Interrogator 808/136/006 (2nd Edition) | EQM 808136/006 (2nd Edition) Issue 3 |
| Site Monitor (PARROT) | Equipment Manual for Single Channel Site Monitor 808412/001 | EQM 808412/001 Issue 5 |
| OEM Equipment | Documentation Supplied | CD-ROM Folder Ref |
| System Interface Unit (SIU)-Sensis | Installation, Operation and Maintenance Manual for the ATCBI-6 SIU, Ref 730-005599, Version 6 | OEM Sensis (link to document) |
| GPS Precision Time Source-Rapco type 1804L17 | Equipment Manual for RAPCO Type 1804L17 GPS Precision Frequency Source, Issue 4 Feb 2002, plus supporting files | OEM Rapco (refer to folder) |
| UPS-MGE type Pulsar EX15 | User Manual for Pulsar EX7/EX10/EX15/EXB10/EXB15, plus supporting files | OEM MGE (refer to folder) |
| Product Improvement Manuals |
| Raytheon Equipment | Manual Title | Manual Reference |
| MSSR SYSTEM FOR FAA ATCBI-6 | System Manual for MSSR System 806404/001 for FAA ATCBI-6 (2nd Edition) | SYM 808404/001 (2nd Edition) Issue 4 |
| Condor MSSR Interrogator | Equipment Manual for Condor MSSR Interrogator 808/136/006 (2nd Edition) | EQM 808136/006 (2nd Edition) Issue 4 |
| Site Monitor (PARROT) | Equipment Manual for Single Channel Site Monitor 808412/001 | EQM 808412/001 Issue 5.1 |
| Raytheon Equipment | Manual Title | Manual Reference |
| MSSR SYSTEM FOR FAA ATCBI-6M | System Manual for MSSR System 808404/002 for FAA ATCBI-6(M) Document Ref. SYM 808404/002 | SYM 808404/001 Issue 5 |
| Condor MSSR Interrogator | Equipment Manual for CONDOR Mk2DS4 MSSR Interrogator 808136/013 Document Ref. EQM 808136/013 | EQM 808136/006 Issue 5 |
| Site Monitor (PARROT) | Equipment Manual for Single Channel Site Monitor 808412/001 Document Ref. EQM 808412/001 | EQM 808412/001 Issue 6 |