***** Paragraph Numbered Format ***** ******* Copyright 1988, ARCOM ******* ARCHITECTURAL COMPUTER SERVICES, INC.

November 21, 1997

Contract # TW-0928

SPECIAL SPECIFICATION

SECTION 10100-S

VISUAL DISPLAY BOARDS

Page

PART 1 - GENERAL

1.01	Summary	2

1.02	Submittals	2

PART 2 - PRODUCTS

2.01	Manufacturers	3

2.02	Manufactured Units	3

2.03	Accessories	3

PART 3 - EXECUTION

3.01	Installation	4

3.02	Adjust and Clean	4

3.03	Markerboard and Projection Screen Schedule	5

SPECIAL SPECIFICATION

SECTION 10100-S

VISUAL DISPLAY BOARDS

THIS SECTION USES THE TERM "ARCHITECT." CHANGE THIS TERM AS NECESSARY TO MATCH THE ACTUAL TERM USED TO IDENTIFY THE DESIGN PROFESSIONAL AS DEFINED IN THE GENERAL AND SUPPLEMENTARY CONDITIONS.

PART 1 - GENERAL

1.01		SUMMARY

A.	This Section includes porcelain enamel markerboards (for liquid chalk).

B.	Related Sections:

1.	Section 11132, Projection Screens.

2.	Section 09250, Gypsum Drywall for metal stud backing.

1.02		SUBMITTALS

A.	Submit in accordance with provisions of Section 01300-S.

B.	Product Data:  Provide product data for markerboards.  Include illustrations of typical trim members and dimensioned elevations.  Show anchors, grounds, reinforcement, accessories, layout, and installation details.

PART 2 - PRODUCTS

2.01		MANUFACTURERS

DELETE THIS ARTICLE IF OWNER-IMPOSED OR OTHER PROJECT REQUIREMENTS PROHIBIT MENTION OF MANUFACTURER'S NAMES.

A.	Manufacturer:  Subject to compliance with requirements, provide products of one of the following:

DELETE VISUAL DISPLAY BOARDS TYPES NOT INCLUDED IN THE PROJECT.  THE LIST OF MANUFACTURERS THAT FOLLOWS EACH PRODUCT CATEGORY IS AN EXAMPLE LIST ONLY, THAT GENERALLY INCLUDES COMPANIES WITH NATIONAL DISTRIBUTION.  REVISE LISTS TO SUIT PROJECT REQUIREMENTS.  SEE EVALUATIONS FOR FURTHER DISCUSSION AND THE NAMES OF ADDITIONAL COMPANIES.

1.	Porcelain Enamel Marker Boards:

MANUFACTURERS BELOW PRODUCE LIGHT-COLORED PORCELAIN ENAMEL MARKERBOARDS DESIGNED FOR USE WITH LIQUID MARKERS.  THEY MAY ALSO BE USED AS PROJECTION SCREENS.  AS WAS THE CASE WITH CHALKBOARDS, ONLY ALLIANCEWALL, CLARIDGE AND GREENSTEEL ARE PRIMARY MANUFACTURERS OF PORCELAIN ENAMEL FACE SHEETS FOR MARKERBOARDS.  THE OTHER COMPANIES MANUFACTURE THEIR MARKERBOARDS USING FACE SHEETS FROM ONE OF THESE THREE COMPANIES.

a.	Carolina Chalkboard Co.

b.	Claridge Products and Equipment, Inc.

c.	Greensteel, Inc.

B.	Substitutions: only under provisions of Section 1600-S.

2.02		MANUFACTURED UNITS

DELETE THE NEXT PARAGRAPH IF PORCELAIN ENAMEL CHALKBOARDS ARE NOT INCLUDED. AMPLIFY IF MARKERBOARDS ARE ALSO INCLUDED.  THIS PARAGRAPH CAN BE USED TO SPECIFY BOTH CHALKBOARDS AND MARKERBOARDS; THE MAJOR DIFFERENCE BETWEEN THE TWO IS IN THE COLOR AND MATTE OF THE COVER COAT FINISH.  SEE EVALUATION SHEETS FOR FURTHER DISCUSSION.

A.	Markerboards:  Provide LGS markerboards manufactured by Claridge Products and Equipment, Incorporated.

1.	Surface:  32LCS (white porcelain panel).

2.	Color:  White.

3.	Thickness:  24 gage.

4.	Nominal Size:  4' x 8' and 4' x 12'.

B.	Refer to Article 3.03 Markerboard  Schedule for location.

2.03		ACCESSORIES

REVIEW THIS ARTICLE THOROUGHLY.  DELETE UNNECESSARY ITEMS AND REVISE TO SUIT PROJECT.  WOOD TRIM, PRINCIPALLY RED OAK, IS AVAILABLE FROM CLARIDGE AND GREENSTEEL.

A.	Trim and Accessories:  Satin annodized aluminum frame, size and shape as indicated, to suit type of installation.  Provide straight, single-length units wherever possible; keep joints to a minimum.  Miter corners to a neat, hairline closure.

DELETE THE NEXT PARAGRAPH IF CONDITIONS REQUIRING ADDITIONAL SUPPORT DO NOT EXIST.

1.	Field-Applied Trim:  Provide the manufacturer's standard slip-on trim, to eliminate grounds.

2.	Chalktray:  Furnish manufacturer's standard continuous box-type aluminum chalktray with slanted front and cast aluminum end closures for each chalkboard.

IF THE PROJECT INCLUDES CHALKBOARDS, SELECT THE PARAGRAPH ABOVE OR BELOW.  VERIFY THAT THE CHALKTRAY TYPE SELECTED IS SUITABLE FOR THE ASSEMBLY METHOD AND TYPE OF MOUNTING.

3.	Map Rail:  Furnish map rail at the top of each unit.

PART 3 - EXECUTION

3.01		INSTALLATION

REVISE THE PARAGRAPHS BELOW AS NECESSARY TO SUIT PROJECT CIRCUMSTANCES.  NOTE:  SLATE CHALKBOARDS ARE PRIMARILY FIELD ASSEMBLED.

A.	Deliver factory-built chalkboard and tackboard units completely assembled in one piece without joints, wherever possible.  Where dimensions exceed panel size, provide 2 or more pieces of equal length as acceptable to the SDR.  When overall dimensions require delivery in separate units, prefit components at the factory, disassemble for delivery, and make final joints at the site.  Use splines at joints to maintain surface alignment.

B.	Install units in locations and at mounting heights indicated and in accordance with the manufacturer's instructions.  Keep perimeter lines straight, plumb, and level.  Provide grounds, clips, backing materials, adhesives, brackets, anchors, trim, and accessories necessary for a complete installation.

DELETE THE NEXT PARAGRAPH IF THERE ARE NO SLATE CHALKBOARDS.

C.	Coordinate job-site assembled units with grounds, trim, and accessories.  Join parts with a neat, precision fit.

3.02		ADJUST AND CLEAN

A.	Verify that accessories required for each unit have been properly installed and that operating units function properly.

B.	Clean units in accordance with the manufacturer's instructions. Break in chalkboards only as recommended by the manufacturer.

3.03		MARKERBOARD SCHEDULE

Location			Markerboard Size

Room 1001			8’ L by 4’ H

Room 1302			8’ L by 4’ H

Room 2001			8’ L by 4’ H

Room 2302			8’ L by 4’ H

Room 3302			8’ L by 4’ H

Room 1200C		8’ L by 4’ H

Room 1300D		8’ L by 4’ H

Room 2200C		8’ L by 4’ H

Room 2300D		8’ L by 4’ H

Room 3200D		8’ L by 4’ H

Room 3300D		8’ L by 4’ H

Mounting:  Mounting height and location as directed by the SDR.

END OF SECTION